| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING COLLEGE PARK, USA, 28 APRIL - 2 MAY 2014 |  | IPET-DRMM-II / Doc. 2.1 (2) (24. 4. 2014) ------------------------- ITEM 2.1 ENGLISH ONLY |
| --- | --- | --- |

GRIB

GRIB encoding of the beginning of overall time interval
in the past

Submitted by Manuel Werner, Sibylle Krebber (DWD)

_______________________________________________________________________

Summary and Purpose of Document

For some products to be encoded in GRIB the beginning of an overall time period lies before the reference time. It is not clear how to encode such products in GRIB. The proper way of encoding has to be discussed.

_______________________________________________________________________

ACTION PROPOSED

The team is invited to discuss the issue.

ANNEXES:

1.	Template 4.8

DISCUSSIONS

At DWD it is required to encode in GRIB a product which is obtained by a statistical process (accumulation) over a continuous time interval. GRIB Template 4.8 seems to be most appropriate for this purpose.

The product is generated at a point in time which is denoted as the reference time, encoded in Section 1, octets 13-19. The end of the time interval can be encoded using octets 35-41 in Template 4.8. However, the beginning of the time interval may not be individually defined.

Note 2 of Template 4.8 says: „The reference time in section 1 and the forecastTime together define the beginning of the overall time interval. “

The beginning of the time interval may lie in the past with respect to the reference time. In such a case, a negative value must be defined as forecastTime (octets 19-22 in Template 4.8), which is not permitted.

The question is how to deal with this deficiency.

PROPOSAL

To review and discuss Note (2) for templates with continuous or non-continuous time intervals.

Annex:

Product definition template 4.8 – average, accumulation and/or extreme values or other
	statistically processed values at a horizontal level or in a 	horizontal layer in a continuous or non-continuous time interval

Octet No.	Contents

10	Parameter category (see Code table 4.1)

11	Parameter number (see Code table 4.2)

12	Type of generating process (see Code table 4.3)

13	Background generating process identifier (defined by originating centre)

(continued)

(Product definition template 4.8 – continued)

Octet No.	Contents

14	Analysis or forecast generating process identifier (defined by originating centre)

15–16	Hours after reference time of data cut-off (see Note 1)

17	Minutes after reference time of data cut-off

18	Indicator of unit of time range (see Code table 4.4)

19–22	Forecast time in units defined by octet 18 (see Note 2)

23	Type of first fixed surface (see Code table 4.5)

24	Scale factor of first fixed surface

25–28	Scaled value of first fixed surface

29	Type of second fixed surface (see Code table 4.5)

30	Scale factor of second fixed surface

31–34	Scaled value of second fixed surface

35–36	Year

37	Month

38	Day            Time of end of overall time interval

39	Hour

40	Minute

41	Second

42	n – number of time range specifications describing the time intervals used to calculate the 
		statistically processed field

43–46	Total number of data values missing in statistical process

47–58   Specification of the outermost (or only) time range over which statistical 
			processing is done

47	Statistical process used to calculate the processed field from the field at each time incre-
		ment during the time range (see Code table 4.10)

48	Type of time increment between successive fields used in the statistical processing (see 
		Code table 4.11)

49	Indicator of unit of time for time range over which statistical processing is done (see Code 
		table 4.4)

50–53	Length of the time range over which statistical processing is done, in units defined by the 
		previous octet

54	Indicator of unit of time for the increment between the successive fields used (see Code 
		table 4.4)

55–58	Time increment between successive fields, in units defined by the previous octet (see Notes 3 
		and 4)

59–nn   These octets are included only if n > 1, where nn = 46 + 12 x n

59–70	As octets 47 to 58, next innermost step of processing

71–nn	Additional time range specifications, included in accordance with the value of n. Contents 
		as octets 47 to 58, repeated as necessary

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples. Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a raingauge.

(4)	The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 48, 60, 72, ...). For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast times.