| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING COLLEGE PARK, USA, 28 APRIL - 2 MAY 2014 |  | IPET-DRMM-II / Doc. 2.2 (4) (24. 4. 2014) ------------------------- ITEM 2.2 ENGLISH ONLY |
| --- | --- | --- |

GRIB

Update for distribution template

Submitted by Michael Baldauf, Sibylle Krebber (DWD)

_______________________________________________________________________

Summary and Purpose of Document

Last year a new template for distribution functions in GRIB was proposed and approved for validation. During the validation process it turns out that explanatory notes for the proposed template would be useful.

_______________________________________________________________________

ACTION PROPOSED

The meeting is invited to review the additional explanatory notes and to decide whether to include such notes to the Manual on Codes linked with the product definition template 4.57.

ANNEXES:

- Explanatory notes

- Product definition template 4.57

- Code table 4.240

DISCUSSIONS

Some product definition templates for GRIB in the Manual on Codes are incomprehensible at the first view. More information is needed for better understanding and proper use of the templates. Sometimes this lack of information could prevent users touse the templates and propose new ones instead.

Last year a new Product definition template 4.57 – “analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function” and a new Code table 4.240 – “Type of distribution function” were proposed.

The validation is ongoing and will be finished soon.

Admittedly, the proposed template for distribution functions 4.57 is a very specific one and not easily to understand for none specialists. Therefore, during the validation process, it turns out that explanatory notes for the proposed template would be useful.

This template was proposed in a very generic form to be able to use it for a huge amount of analogous proceedings.

PROPOSAL

Add explanatory notes as shown in the annex under Product definition template 4.57 - “analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function”

Annexes:

- Notes

- Proposed template in validation

| Product definition template 4.57 - analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function |
| --- |
| Octet No. | Contents |
| 10 | Parameter category (see Code table 4.1) |
| 11 | Parameter number (see Code table 4.2) |
| 12 – 13 | Atmospheric chemical constituent type (see Code table 4.230) |
| 14 – 15 | Number of mode (N) of distribution (see Note 2) |
| 16 – 17 | Mode number (l) |
| 18 – 19 | Type of distribution function (see Code table 4.240) |
| 20 | Number of following function parameters (Np), defined by type given in octet 18-19 (Type of distribution function) |
|  | Repeat the following 5 octets for the number of function parameters (n=1,Np), if Np > 0 |
| (21 + 5(n-1) | List of scale factor of fixed distribution function parameter (p1 – pNp)), defined by type of distribution in octet 18-19 |
| (22 + 5(n-1)) – (25 + 5(n-1)) | List of scaled value of fixed distribution function parameter (p1 – pNp)), defined by type of distribution in octet 18-19 |
| 21+5Np | Type of generating process (see Code table 4.3) |
| 22+5Np | Background generating process identifier (defined by originating centre) |
| 23+5Np | Analysis or forecast generating process identifier (defined by originating centre) |
| 24+5Np – 25+5Np | Hours of observational data cut-off after reference time (see Note 1) |
| 26+5Np | Minutes of observational data cut-off after reference time |
| 27+5Np | Indicator of unit of time range (see Code table 4.4) |
| 28+5Np – 31+5Np | Forecast time in units defined by octet 20 |
| 32+5Np | Type of first fixed surface (see Code table 4.5) |
| 33+5Np | Scale factor of first fixed surface |
| 34+5Np – 37+5Np | Scaled value of first fixed surface |
| 38+5Np | Type of second fixed surface (see Code table 4.5) |
| 39+5Np | Scale factor of second fixed surface |
| 40+5Np – 43+5Np | Scaled value of second fixed surface |

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	If Number of mode (N) > 1, then between x*N fields with mode number l=1,…,N define the distribution function. x is the number of variable parameters in the distribution function.

- New Code table and entries in validation

| Code table 4.0 – Product definition template number |
| --- |
| Code figure | Meaning |
| 57 | Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function |

| Code table 4.240 – Type of distribution function |
| --- |
| Code figure | Meaning |
| 0 | No specific distribution function given |
| 1 | Delta functions with spatially variable concentration and fixed diameters Dl (p1) in meter (see Note 1) |
| 2 | Delta functions with spatially variable concentration and fixed masses Ml (p1) in kg (see Note 2) |
| 3 | Gaussian (Normal) distribution with spatially variable concentration and fixed mean diameter Dl (p1) and variance σ (p2) (see Note 3) |
| 4 | Gaussian (Normal) distribution with spatially variable concentration, mean diameter and variance (see Note 4) |
| 5 | Log-normal distribution with spatially variable number density, mean diameter and variance (see Note 5) |
| 6 | Log-normal distribution with spatially variable number density, mean diameter and fixed variance σ (p1) (see Note 6) |
| 7 | Log-normal distribution with spatially variable number density and mass density and fixed variance σ (p1) and fixed particle density ρ (p2) (see Note 7) |
| 8 - 49151 | Reserved |
| 49152 – 65534 | Reserved for local use |
| 65535 | Missing |

Notes:

(1)	Bin-Model or delta function with N concentrations cl(r) in class (or mode) l. 
Concentration-density function:

where

N – number of modes in the distribution

δ  - delta-function

d  - diameter

Dl –diameter of mode l (p1)

(2)	Bin-Model or delta function with N concentrations cl(r) in class (or mode) l. 
Concentration-density function:

where 
N – number of modes in the distribution
δ  - delta-function
m  - mass
Ml –mass of mode l (p1)

(3)	N-modal concentration-density function consisting of Gaussian-functions:

where
N – number of modes in the distribution
d  - diameter
Dl –mean diameter of mode l (p1)
σl  - variance of mode l (p2)

with N fields of concentration cl(r).

(4)	N-modal concentration-density function consisting of Gaussian-functions:

with 3N fields of concentration cl(r), variance σl(r) and mean diameter Dl(r).

(5)	N-modal log-normal-distribution for the number density:
  
where 
d  - diameter

with 3N fields of number density nl(r), variance σl(r) and mean diameter Dl(r).

(6)	N-modal log-normal-distribution for the number density:
   
where
σl  - variance of mode l (p1)

with 2N fields of number density nl(r) and mean diameter Dl(r).

(7)	N-modal log-normal-distribution for the number density as in Note (6), but with a prescribed mass density ml(r), from which the diameter Dl(r) is calculated by:

where
σl  	- variance of mode l (p1)

ρp,l 	- particle density (p2)

with 2N fields of number density nl(r)  and mass density ml(r).