| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING College Park, MD, USA, 28 April – 2 May 2014 |  | IPET-DRMM-II / Doc. 3.2(1) (30. 4. 2014) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

Additional Common Code Table Entries and BUFR Table B Entries for Satellite Data

Submitted by Simon Elliott (EUMETSAT)

_______________________________________________________________________

Summary and Purpose of Document

This document proposes the addition of entries to Common Code Tables and a BUFR Table B Code Table which are required to allow the exchange of satellite data in BUFR.

_______________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the addition of Common Code Table entries and BUFR Table B Code Table entries for satellite data.

DISCUSSION

A recent meeting of the CGMS Task Force on Satellite Data and Codes concluded that a number of entries to Common Code Tables C-5 (Satellite Identifier), C-8 (Satellite Instruments) and C-12 (Sub-centres attached to centres in Table C-11) are needed to support the exchange of satellite data.  These are listed in the proposal below.

The Task Force also identified the need for three new entries in BUFR Code Table 0-02-020 (Satellite classification).  These are also listed in the proposal.

Proposal

The following additions to the Common Code Tables are proposed:

| Table | Proposed additions | Comment |
| --- | --- | --- |
| Common Code Table C-5 Satellite identifier | 061 Sentinel 3A 287 DMSP-19 288 GPM-core 516 FY-2F 517 FY-2G 522 FY-3C | These satellites are in orbit or planned for imminent launch |
| Common Code Table C-8 Satellite Instruments | 178 SRAL 179 OLCI 180 SLSTR | Sentinel-3 instruments |
|  | 518 DPR 519 GMI | GPM-core instruments |
|  | 953 MWHS-2 954 MWTS-2 955 HIRAS | FY-3-C instruments FY-3-D instrument |
| Common Code Table C-12 Sub-centres attached to centres in Table C-11 | Centre 191 French Polynesia Sub-centre : 01 Tahiti |  |
| BUFR Code Table 0-02-020 Satellite classification | 20 GPM-core 92 Sentinel-3 382 FY-3 |  |