| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING College Park, MD, USA, 28 April – 2 May 2014 |  | IPET-DRMM-II / Doc. 3.2 (4) (26. 3. 2014) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

New BUFR descriptors for OMPS total column data

Submitted by Jeff Ator (USA)

_______________________________________________________________________

Summary and Purpose of Document

This document proposes a new Table B descriptor for use with OMPS (ozone mapping and profiler suite) total column data.

_______________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the new descriptor for pre-operational status.

DISCUSSION

OMPS TC (ozone mapping and profiler suite total column) data is currently reported using the BUFR table D sequence 3-10-066, and several users have suggested that the datasets would be enhanced by providing the latitude and longitude corners of the total column observations.  Rather than modify the 3-10-066 sequence, our idea to address this concern was to precede the 3-10-066 sequence with this additional information in the BUFR data description, using one new Table B descriptor as described below.  This idea was first discussed and agreed within the CGMS Task Force for Satellite Winds and later submitted for review to the IPET-DRMM via email.  Since that time, sample data was provided and validated with the kind assistance of IBL, so we would now like to request pre-operational approval of the new Table B descriptor.

Proposal

New Table B descriptor:

| F X Y | Element name | BUFR Unit | BUFR Scale | BUFR Refval | BUFR Bits | CREX Unit | CREX Bytes | CREX Bytes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 08 087 | Corner position of observation | Code table | 0 | 0 | 3 | Code table | 1 | 4 |

| Code figure | DESCRIPTION |
| --- | --- |
| 0 | Upper left |
| 1 | Upper right |
| 2 | Lower right |
| 3 | Lower left |
| 4-6 | Reserved |
| 7 | Missing value |

The approval of this new descriptor would then allow the four latitude/longitude corners to be included in the data description for the total column ozone product as follows:

1-02-004
0-08-087
3-01-021

0-08-087 (set to "missing" to cancel)

3-10-066