| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING COLLEGE PARK, USA, 28 APRIL - 2 MAY 2014 |  | IPET-DRMM-II / Doc. 3.2 (6) (10. 4. 2014) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR and CREX

New BUFR elements for satellite data

Submitted by Enrico Fucile

_______________________________________________________________________

Summary and Purpose of Document

New elements are proposed to code new satellite

_______________________________________________________________________

ACTION PROPOSED

The team is requested to accept the proposed elements for validation

DISCUSSIONS

ECMWF is preparing to process data from the Global Precipitation Measurement (GMP) satellite and in particular from the GMI Microwave Imager instrument. In this context there is the need of defining new table B elements.

PROPOSAL

The following BUFR table B elements are proposed:

| F Y Z | Element Name | Units | Scale | Reference | Width | Description |
| --- | --- | --- | --- | --- | --- | --- |
| 0 05 062 | Spacecraft latitude | degrees | 5 | –9000000 | 25 | The geodetic latitude of the spacecraft at the Scan mid-Time |
| 0 06 041 | Spacecraft longitude | degrees | 5 | –18000000 | 26 | The geodetic longitude of the spacecraft at the Scan mid-Time |
| 0 40 027 | Spacecraft orientation | degrees | 2 | 0 | 16 | The positive angle of the spacecraft vector (v) from the satellite forward direction of motion, measured clockwise facing down |
| 0 40 028 | Sun-glint angle | degrees | 5 | 0 | 26 | The angle between the sun and the instrument view direction as reﬂected oﬀ the Earth’s surface |