| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING COLLEGE PARK, USA, 28 APRIL - 2 MAY 2014 |  | IPET-DRMM-II / Doc. 3.2 (8) (16. 4. 2014) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

REVISED BUFR SEQUENCE FOR SYNOPTIC REPORTS FROM SEA STATIONS SUITABLE FOR VOS OBSERVATION DATA

Submitted by JCOMM Representative, David Berry (United Kingdom)

_______________________________________________________________________

Summary and Purpose of Document

This document proposes a revised BUFR template for synoptic reports from sea stations suitable for VOS observation data.

This document also reports on the validation status of the JCOMM templates submitted to the first meeting of the IPET-DRMM.

_______________________________________________________________________

ACTION PROPOSED

The team is requested to review the revised BUFR template for synoptic reports from sea stations suitable for VOS observation data.

The team is also invited to note the validation status of the previously submitted JCOMM templates.

ANNEXES:

1.	SECURITY REQUIREMENTS FOR THE ENCRYPTION/DECRYPTION OF SHIP’S CALL SIGN

DISCUSSIONS

Background

At the first meeting of the IPET-DRMM  (IPET-DRMM-I, Tokyo, Japan, 1 – 5 July 2013) the JCOMM proposal for the encryption of Ship's callsigns within BUFR reports was accepted for validation. Whilst accepted for validation the new sequence, and associated elements, have not been validated due to concerns over the management of and security requirements for the encryption keys. A draft set of security requirements has been proposed by the UK Met Office. These have been approved for use on a trial basis by the JCOMM co-presidents (see Annex A) and endorsed by the 5th Meeting of the JCOMM Data Management Coordination Group (DMCG-5, Geneva, Switzerland, 29 – 31 January 2014).

In addition to the ENCODE proposal a number of other changes to the VOS template were proposed to IPET-DRMM-I. These were made to accommodate the requests of the JCOMM ship observation team for the inclusion of platform type and additional information on the types of humidity sensors used. In addition to these changes, a previous proposal to update the VOS BUFR template had been accepted for validation by the IPET-DRC.

This proposal seeks to combine those changes proposed at IPET-DRMM-I and previous IPET-DRC meetings. The current VOS template is given by sequence 3 08 009 (Table 1). The template approved by the IPET-DRC for validation combined the pressure, ice and marine data sequences into the a new ship “instantaneous“ sequence and made a number of elements optional through the use of delayed replication descriptors. This template is given in Table 2.

The new BUFR sequence, based on that given in Table 2, is given in the proposal section of this document. The new sequence takes into account previous recommendations and incorporates those proposed to IPET-DRMM-I. These are:

- The inclusion of sequence 3 01 018 (encrypted ship’s callsign and encryption method) at the start of the template

- The creation of a new sequence for marine air temperature and humidity, including the JCOMM requested metadata elements

- The use of delayed replication factors for optional sequences and those sequences that often contain missing data

- The inclusion of the pressure, ice and marine data in the “instantaneous” data sequence

- The inclusion of an optional sequence for the requested VOSClim elements

- The move of the “precipitation past 24 hours” sequence from the ship “instantaneous” data sequence to ship “period” data sequence

It should be noted that the metadata elements included in the proposed “extended ship temperature and humidity data” sequence differ slightly from those proposed at IPET-DRMM-I. New elements and associated code tables have been proposed specific to marine data to align the values with that information collected operationally and published quarterly in WMO Publication 47, the “International List of Selected, Supplementary and Auxiliary Ships”.

Table 1: BUFR sequence for synoptic reports from a sea station suitable for ship data (operational)

| Table reference | Table References | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 08 | 009 | 3 | 01 | 093 | Ship identification, movement, date/time, horizontal and vertical coordinates |  |
|  |  |  | 3 | 02 | 001 | Pressure and 3-hour pressure change |  |
|  |  |  | 3 | 02 | 054 | Ship “instantaneous” data |  |
|  |  |  | 0 | 08 | 002 | Vertical significance (surface observations) |  |
|  |  |  | 3 | 02 | 055 | Icing and ice |  |
|  |  |  | 3 | 02 | 057 | Ship marine data |  |
|  |  |  | 3 | 02 | 060 | Ship “period” data |  |

Table 2: Sequence for synoptic reports from sea stations suitable for VOS observation data (validation)

| Table reference | Table References | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 08 | 014 | 3 | 01 | 093 | Ship identification, movement, type, date/time, horizontal and vertical coordinates |  |
|  |  |  | 3 | 02 | 062 | Ship “instantaneous” data from VOS |  |
|  |  |  | 3 | 02 | 063 | Ship “period” data from VOS |  |

Validation of Marine Templates

During the past year, members of the JCOMM Task Team on Table Driven Codes have validated the templates listed in Table 3. Minor changes were required to the BUFR sequence for temperature and salinity profile data (3 15 007), with a number of metadata elements removed. The elements removed depended on BUFR descriptors not yet approved for validation. Post validation, one centre reported some issues with the nesting of delayed replication factors. These issues have since been resolved by that centre.

Following validation it has been proposed that descriptor 0 22 043 (sea / water temperature) be replaced by 0 22 049 (sea surface temperature) in the drifting buoy template (3 15 009). This is in effect only a change in name. The scale, reference value and data width are the same for both descriptors and the proposed change reflects a more accurate description of the observation being reported.

Table 3: List of marine templates validated and validating centres / organisations

| Template (Table D sequence) | Encoding Centre / Organisation (Software used) | Decoding Centre / Organisation (Software used) | Result |
| --- | --- | --- | --- |
| Temperature and salinity profile (3 15 007) | NOC (ECMWF BUFR library) | NOAA AOML (LIBECBUFR, AOML Custom Java App) | Validated, minor changes required |
| Temperature and salinity profile (3 15 007) | NOAA AOML (LIBECBUFR, Custom Java App) | NOC (ECMWF BUFR library) | Validated, minor changes required |
| Moored buoy (3 15 008) | NOC (ECMWF BUFR library) | UKMO (Custom UKMO software) NOC (NCEP BUFR library) | Validated |
| Moored buoy (3 15 008) | UKMO (Custom UKMO software) | NOC (ECMWF BUFR library) | Validated |
| Drifting buoy (3 15 009) | NOC (ECMWF BUFR library) | Pacific Gyre (ECMWF BUFR library) | Validated |
| Drifting buoy (3 15 009) | Pacific Gyre (Custom Pacific Gyre software) | NOC (NCEP BUFR library) | Validated |

PROPOSAL

Add new table B entries

New entries

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Units | Scale | Data width (characters) |
| 0 | 03 | YYY | Type of marine hygrometer | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 03 | YYY | Exposure of marine thermometer / hygrometer | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 | 03 | YYY | Type of marine thermometer | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 | 03 | YYY | Maximum height of deck cargo above summer load line | m | 0 | 0 | 6 | m | 0 | 2 |
| 0 | 03 | YYY | Departure of reference level (summer maximum load line) from actual sea level | m | 0 | -32 | 6 | m | 0 | 3 |
| 0 | 11 | YYY | Relative wind direction (in degrees off bow) | degree | 0 | 0 | 9 | degree | 0 | 3 |
| 0 | 11 | YYY | Relative wind speed | m/s | 1 | 0 | 12 | m/s | 1 | 4 |

Entries under validation

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Unit | Scale | Data width (characters) |
| 0 | 01 | 114 | Encrypted ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 352 | CCITT IA5 | 0 | 44 |
| 0 | 25 | 185 | Encryption method | Code table | 0 | 0 | 8 | Code table | 0 | 3 |
| 0 | 25 | 186 | Encryption key version | CCITT IA5 | 0 | 0 | 96 | CCITT IA5 | 0 | 12 |

Add new table D entries

New entries

Revised BUFR sequence (3 02 062) for the representation of ship “instantaneous” data.

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 062 | 3 | 02 | 001 | Pressure and 3-hour pressure change |  |
|  |  |  | 3 | 02 | YYY | Extended ship temperature and humidity data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 2 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 053 | Ship visibility data |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 004 | General cloud information |  |
|  |  |  | 3 | 02 | 005 | Cloud layer |  |
|  |  |  | 0 | 08 | 002 | Vertical significance (surface observations) | Set to missing (cancel) |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 055 | Icing and ice |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 056 | Sea / water temperature |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 021 | Waves |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 024 | Wind and swell waves |  |

Revised BUFR sequence (3 02 063) for the representation of Ship “period” data.

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 063 | 3 | 02 | 038 | Past and present weather |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 040 | Precipitation measurement |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 2 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 034 | Precipitation past 24 hours |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 058 | Extreme temperature data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | 064 | Ship wind data |  |

New BUFR sequence (3 02 YYY) for the representation of VOSClim data elements

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | YYY | 0 | 01 | 012 | Direction of motion of moving observing platform | Ship’s heading |
|  |  |  | 0 | 01 | 012 | Direction of motion of moving observing platform | Ship’s course over ground |
|  |  |  | 0 | 01 | 013 | Speed of motion of moving observing platform | Ship’s speed over ground |
|  |  |  | 0 | 03 | YYY | Maximum height of deck cargo above summer load line |  |
|  |  |  | 0 | 03 | YYY | Departure of reference level (summer maximum load line) from actual sea level |  |
|  |  |  | 0 | 11 | YYY | Relative wind direction (in degrees off bow) |  |
|  |  |  | 0 | 11 | YYY | Relative wind speed |  |

New BUFR sequence (3 02 YYY) for the representation of extended ship temperature and humidity data

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | X | YYY |  |  |
| 3 | 02 | YYY | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 0 | 03 | YYY | Type of marine thermometer |  |
|  |  |  | 0 | 03 | YYY | Exposure of marine thermometer / hygrometer |  |
|  |  |  | 0 | 12 | 101 | Temperature / air temperature |  |
|  |  |  | 0 | 02 | 039 | Method of wet-bulb temperature measurement |  |
|  |  |  | 0 | 03 | YYY | Type of marine hygrometer |  |
|  |  |  | 0 | 03 | YYY | Exposure of marine thermometer / hygrometer |  |
|  |  |  | 0 | 12 | 102 | Wet-bulb temperature |  |
|  |  |  | 0 | 12 | 103 | Dewpoint temperature |  |
|  |  |  | 0 | 13 | 003 | Relative humidity |  |
|  |  |  | 0 | 03 | YYY | Exposure of marine thermometer / hygrometer | Set to missing (cancel) |
|  |  |  | 0 | 03 | YYY | Type of marine thermometer | Set to missing (cancel) |
|  |  |  | 0 | 03 | YYY | Type of marine hygrometer | Set to missing (cancel) |

Revised BUFR sequence (3 08 014) for synoptic reports from sea stations suitable for VOS observation data.

| Table reference | Table References | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 08 | 014 | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 01 | 018 | Encrypted ship’s callsign and encryption method |  |
|  |  |  | 3 | 01 | 093 | Ship identification, movement, type, date/time, horizontal and vertical coordinates |  |
|  |  |  | 3 | 02 | 062 | Ship “instantaneous” data |  |
|  |  |  | 3 | 02 | 063 | Ship “period” data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 3 | 02 | YYY | VOSClim data |  |

Entries under validation

BUFR sequence 3 01 018 – encrypted ship's callsign and encryption method

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 01 | 018 | 0 | 01 | 114 | Encrypted ship or mobile land station identifier |  |
|  |  |  | 0 | 25 | 185 | Encryption method |  |
|  |  |  | 0 | 25 | 186 | Encryption key version |  |

BUFR sequence 3 02 064 – ship wind data

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
| 3 | 02 | 064 | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 0 | 02 | 002 | Type of instrumentation for wind measurement |  |
|  |  |  | 0 | 08 | 021 | Time significance | Set to 2, time averaged |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 001 | Wind direction |  |
|  |  |  | 0 | 11 | 002 | Wind speed |  |
|  |  |  | 0 | 08 | 021 | Time significance | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 000 | Short delayed replication factor |  |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 043 | Maximum wind gust direction |  |
|  |  |  | 0 | 11 | 041 | Maximum wind gust speed |  |

Amend Table D entry (amendment shown in red)

| Table reference | Table references | Element name | Notes |
| --- | --- | --- | --- |
| F XX YYY | F XX YYY |  |  |
| 3 15 009 | 0 01 087 | WMO marine observing platform extended identifier |  |
|  | 0 01 019 | Long station name |  |
|  | 0 02 149 | Type of data buoy |  |
|  | 0 08 021 | Time significance (set to 26, time of last known position) |  |
|  | 3 01 011 | Date |  |
|  | 3 01 012 | Time |  |
|  | 3 01 021 | Latitude and Longitude (high accuracy) |  |
|  | 2 08 016 | Change width of CCITT IA5 field (change to 16 characters) |  |
|  | 0 01 051 | Platform Transmitter ID number |  |
|  | 2 08 000 | Change data width (cancel previous value) |  |
|  | 0 02 148 | Data collection and / or location system |  |
|  | 0 01 012 | Direction of motion of moving observing platform |  |
|  | 0 01 014 | Speed of motion of moving observing platform |  |
|  | 0 33 022 | Quality of buoy satellite transmission |  |
|  | 0 33 023 | Quality of buoy location |  |
|  | 0 33 027 | Location quality class (range of radius of 66% confidence) |  |
|  | 0 25 026 | Battery voltage (large range) |  |
|  | 0 02 034 | Drogue type |  |
|  | 0 22 060 | Lagrangian drifter drogue status |  |
|  | 0 07 070 | Drogue depth |  |
|  | 0 02 190 | Lagrangian drifter submergence |  |
|  | 0 08 021 | Time significance (set to 25, nominal reporting time) |  |
|  | 3 01 011 | Date |  |
|  | 3 01 012 | Time |  |
|  | 0 02 005 | Precision of temperature observation |  |
|  | 0 22 049 | Sea surface temperature |  |
|  | 0 02 033 | Method of salinity / depth measurement |  |
|  | 0 22 059 | Sea-surface salinity |  |
|  | 0 08 029 | Surface type |  |
|  | 0 13 115 | Ice thickness |  |
|  | 1 03 000 | Replicate next 3 sequences |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 02 005 | Precision of temperature observation |  |
|  | 3 06 004 | Depth, temperature and salinity profile |  |  |
|  | 0 02 005 | Precision of temperature observation (set to missing to cancel previous value) |  |
|  | 0 10 004 | Pressure |  |
|  | 0 10 051 | Pressure reduced to mean sea level |  |
|  | 1 02 000 | Replicate next two descriptors |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 07 033 | Height of sensor above water surface |  |
|  | 0 12 101 | Temperature / air temperature |  |
|  | 1 01 000 | Replicate next sequence |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 06 042 | Wind measurement from drifting buoy |  |
|  | 1 01 000 | Repeat next sequence |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 06 039 | Sequence for representation of basic wave measurements |  |

Add new code tables

0 03 YYY

Type of marine hygrometer

| Code Figure | Meaning |
| --- | --- |
| 0 | Capacitance |
| 1 | Chilled mirror |
| 2 | Electric |
| 3 | Hair hygrometer |
| 4 | Hygristor |
| 5 | Psychrometer |
| 6 | Torsion |
| 7 | Other |
| 8 – 15 | Reserved |

0 03 YYY

Type of marine thermometer

| Code Figure | Meaning |
| --- | --- |
| 0 | Alcohol thermometer |
| 1 | Dry bulb mercury thermometer |
| 2 | Electric (resistance) thermometer |
| 3 – 7 | Reserved |

0 03 YYY

Exposure of marine thermometer / hygrometer

| Code Figure | Meaning |
| --- | --- |
| 0 | Aspirated (Assmann type) |
| 1 | Screen (non-ventilated, i.e. natural ventilation) |
| 2 | Screen (ventilated, i.e. assisted ventilation) |
| 3 | Ship's screen (property of the ship) |
| 4 | Ship's sling (property of the ship) |
| 5 | Unscreened |
| 6 | Whirling or sling psychrometer |
| 7 – 15 | Reserved |

Annexes (in needed), for example, BUFR/CREX templates

# Footnotes

http://www.jcomm.info/index.php?option=com_oe&task=viewEventRecord&eventID=1396

http://www.ecmwf.int/products/data/software/bufr.html

https://launchpad.net/libecbufr

http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/

Note that the test file had all spectral wave components present but set to 0.