| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING COLLEGE PARK, USA, 28 APRIL - 2 MAY 2014 |  | IPET-DRMM-II / Doc. 3.2 (9) (16. 4. 2014) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

PROPOSED BUFR SEQUENCE FOR REPORTING OBSERVATIONS FROM OFFSHORE PLATFORMS

Submitted by

JCOMM Representative, David Berry (United Kingdom)

Jon Turton (UK Met Office)

_______________________________________________________________________

Summary and Purpose of Document

This document proposes a new BUFR template for reporting observations from offshore platforms.

_______________________________________________________________________

ACTION PROPOSED

The team is requested to review the proposed BUFR template for reporting observations from offshore platforms.

ANNEXES:

1.	BUFR Template for reporting observations from offshore platforms.

DISCUSSIONS

The UK Met Office currently receives meteorological (and oceanographic) data from around 100 offshore oil and gas platforms around the UK. This is currently reported in FM-13. Data also exist from platforms in the German Bight, Baltic and Gulf of Mexico.

Either of the current BUFR templates for the Voluntary Observing Ships (VOS) and moored buoys could be used to represent this data, however this solution would be less than ideal and would not fully represent the data. As a result, a new BUFR sequence has been proposed by the UK Met Office (see Annex A).  This template largely used existing sequences and descriptors, with the exception of a sequence to identify the platform and a sequence currently under validation for wind speed data. One new descriptor is proposed for specifying the type of offshore platform.

PROPOSAL

Add new table B entries

New entries

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Units | Scale | Data width (characters) |
| 0 | 02 | YYY | Type of platform | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Add new table D entries

New entries

Sequence for platform identification, type, time and location of the observation report

| 3 01 AAA | 0 01 087 | WMO number (extended 7 digit identifier) |
| --- | --- | --- |
|  | 0 01 011 | Call sign (where allocated) |
|  | 0 01 015 | Platform name |
|  | 0 02 BBB | Type of offshore platform |
|  | 0 02 001 | Type of station |
|  | 3 01 011 | Year, month, day |
|  | 3 01 012 | Hour, minute |
|  | 3 01 021 | Latitude/longitude (high accuracy) |
|  | 0 07 030 | Height of station platform above mean sea level |
|  | 0 07 031 | Height of barometer above mean sea level |

Sequence for reporting observations from offshore platforms

| 3 08 XXX | 3 01 AAA | Sequence for representation of platform identification type, time and location of the observation report |
| --- | --- | --- |
|  | 3 02 001 | Sequence for pressure data |
|  | 3 02 052 | Sequence for temperature and humidity data |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 056 | Sequence for sea temperature data (optional) |
|  | 3 02 064 | Sequence for wind data* |
|  | 3 02 053 | Sequence for visibility data |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 004 | Sequence for cloud information (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 005 | Sequence for cloud layer information (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 038 | Sequence for present and past weather (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 06 039 | Sequence for representation of basic wave measurements (optional) |

*Note sequence 3 02 064 has previously been approved for validation and is also used in the sequence for synoptic reports from sea stations suitable for VOS data (see Document <link to other JCOMM proposal>).

Add new code tables

0 22 BBB

Type of offshore platform

| Code figure | Meaning |
| --- | --- |
| 0 | Fixed platform |
| 1 | Mobile offshore drill ship |
| 2 | Jack-up rig |
| 3 | Semi-submersible platform |
| 4 | FPSO (floating production storage and offloading unit) |
| 5 | Light vessel |
| 6 – 14 | Reserved |
| 15 | Missing value (or not known) |

Annex A – BUFR Template for reporting observations from offshore platforms

Items in red are new descriptors/sequences suggested for review and incorporation in the WMO Manual on Codes.

Template for reporting observations from offshore platforms

| 3 08 XXX | 3 01 AAA | Sequence for representation of platform identification type, time and location of the observation report |
| --- | --- | --- |
|  | 3 02 001 | Sequence for pressure data |
|  | 3 02 052 | Sequence for temperature and humidity data |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 056 | Sequence for sea temperature data (optional) |
|  | 3 02 064 | Sequence for wind data* |
|  | 3 02 053 | Sequence for visibility data |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 004 | Sequence for cloud information (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 005 | Sequence for cloud layer information (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 038 | Sequence for present and past weather (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 06 039 | Sequence for representation of basic wave measurements (optional) |

* Sequence 3 02 064 has been suggested as part of the proposed template for VOS Observations (3 08 014)

Sequences for platform identification, pressure, temperature, wind and visibility are mandatory. Sequences for sea temperature, cloud data, present/past weather and waves are optional and used only when the relevant data are measured or reported.

Description of sequences

Sequence for platform identification, type, time and location of the observation report

| 3 01 AAA |  | 0 01 087 | WMO number (extended 7 digit identifier) |
| --- | --- | --- | --- |
|  |  | 0 01 011 | Call sign (where allocated) |
|  |  | 0 01 015 | Platform name |
|  |  | 0 02 BBB | Type of offshore platform* |
|  |  | 0 02 001 | Type of station |
|  | 3 01 011 | 0 04 001 | Year |
|  |  | 0 04 002 | Month |
|  |  | 0 04 003 | Day |
|  | 3 01 012 | 0 04 004 | Hour |
|  |  | 0 04 005 | Minute |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) |
|  |  | 0 06 001 | Longitude (high accuracy) |
|  |  | 0 07 030 | Height of station platform above mean sea level |
|  |  | 0 07 031 | Height of barometer above mean sea level |

* suggest new code table to define platform type

Sequence for pressure data

| 3 02 001 |  | 0 10 004 | Pressure (as measured) |
| --- | --- | --- | --- |
|  |  | 0 10 051 | Pressure corrected to mean sea level |
|  |  | 0 10 061 | 3-hour pressure change* |
|  |  | 0 13 003 | Characteristic of pressure tendency* |

* would normally be omitted for hourly (or more frequent) reports

Sequence for temperature and humidity data

| 3 02 052 |  | 0 07 032 | Height of sensor above marine deck platform |
| --- | --- | --- | --- |
|  |  | 0 07 033 | Height of sensor above water surface |
|  |  | 0 12 101 | Temperature (dry bulb) |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement* |
|  |  | 0 12 102 | Wet bulb temperature* |
|  |  | 0 12 103 | Dew point temperature** |
|  |  | 0 13 003 | Relative humidity*** |

* for manual observations only otherwise code as missing

** this will normally be calculated

*** include only when measured otherwise code as missing

Sequence for sea temperature data

| 3 02 056 |  | 0 02 038 | Method of sea temperature measurement |
| --- | --- | --- | --- |
|  |  | 0 07 063 | Depth below sea water surface of sensor |
|  |  | 0 22 043 | Sea/water temperature |
|  |  | 0 07 063 | Depth below sea water surface of sensor (set to missing to cancel) |

Sequence for wind data*

| 3 02 064 |  | 0 07 032 | Height of sensor above marine deck platform |
| --- | --- | --- | --- |
|  |  | 0 07 033 | Height of sensor above water surface |
|  |  | 0 02 002 | Type of instrumentation for wind measurement |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |
|  |  | 0 11 001 | Wind direction |
|  |  | 0 11 002 | Wind speed |
|  |  | 0 08 021 | Time significance (= missing value) |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |
|  |  | 0 31 001 | Delayed descriptor replication factor (0 if no gust data, 1 otherwise) |
|  |  | 0 04 025 | Time period in minutes |
|  |  | 0 11 043 | Maximum wind gust direction |
|  |  | 0 11 041 | Maximum wind gust speed |

* sequence under validation

Sequence for visibility data

| 3 02 053 |  | 0 07 032 | Height of sensor above marine deck platform |
| --- | --- | --- | --- |
|  |  | 0 07 033 | Height of sensor above water surface |
|  |  | 0 20 001 | Horizontal visibility |

Sequences for cloud data

| 3 02 004 |  | 0 20 010 | Cloud cover (total) |
| --- | --- | --- | --- |
|  |  | 0 08 002 | Vertical significance |
|  |  | 0 20 011 | Cloud amount |
|  |  | 0 20 013 | Height of base of cloud |
|  |  | 0 20 012 | Cloud type (low clouds) |
|  |  | 0 20 012 | Cloud type (middle clouds) |
|  |  | 0 20 012 | Cloud type (high clouds) |
| 3 02 005 |  | 0 08 002 | Vertical significance |
|  |  | 0 20 011 | Cloud amount |
|  |  | 0 20 012 | Cloud type |
|  |  | 0 20 013 | Height of base of cloud |

Sequence for present and past weather data

| 3 02 058 |  | 0 20 003 | Present weather |
| --- | --- | --- | --- |
|  |  | 0 04 024 | Time period |
|  |  | 0 20 004 | Past weather (1) |
|  |  | 0 20 005 | Past weather (2) |

Sequence for basic wave data

| 3 06 039 |  | 0 22 078 | Duration of wave record |
| --- | --- | --- | --- |
|  |  | 0 22 070 | Significant wave height |
|  |  | 0 22 073 | Maximum wave height |
|  |  | 0 22 074 | Average wave period |
|  |  | 0 22 071 | Spectral peak wave period |
|  |  | 0 22 076 | Direction from which dominant waves are coming |
|  |  | 0 22 077 | Directional spread of dominant waves |

New code table 0 02 BBB for platform type

0 – fixed platform

1 – mobile offshore drill ship

2 – jack-up rig

3 – semi-submersible platform

4 – FPSO (floating production storage and offloading unit)

5 – light vessel

6-14 - reserved

15 – missing value (or not known).