| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- SECOND MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING College Park, MD, USA, 28 April – 2 May 2014 |  | IPET-DRMM-II / Doc. 9.1(1) (30. 4. 2014) ------------------------- ITEM 9.1 ENGLISH ONLY |
| --- | --- | --- |

Allocation of GTS Abbreviate Bulletin Headers for Satellite Data

Submitted by Simon Elliott (EUMETSAT)

_______________________________________________________________________

Summary and Purpose of Document

This document proposes the allocation of GTS abbreviated bulletin headers in the Manual on the GTS, WMO No, 386 Vol 1 to support the exchange of satellite data.

_______________________________________________________________________

ACTION PROPOSED

The meeting is requested to approve the allocation of the entries to the Manual on the GTS.

DISCUSSION

A recent meeting of the CGMS Task Force on Satellite Data and Codes concluded that there was a lack of clarity in the allocation of abbreviated bulletin headers to be used for the exchange of satellite data in the GTS.  The allocation of abbreviated bulletin headers is given in the Manual on the GTS, WMO No, 386 Vol 1. In order to capture the current practice and to clarify the future allocation of abbreviated bulletin headers, the Task Force has consolidated a list of designators for the data type designator A1.

Instruction 3 for the proper application of the data designators is as follows: “When the table does not contain a suitable designator for the data types, an alphabetic designator which is not assigned in the table should be introduced and the WMO Secretariat notified.”  This document constitutes the notification of the WMO Secretariat.

Proposal

The following additions to Table C6 of the Manual on the GTS (Data type designator A1 (when T1 = I or J)) are proposed:

| T1T2 | A1 | ii | Data type | TAC correspondence | Data category subcategory (Common Table C13) |
| --- | --- | --- | --- | --- | --- |
| IN | C |  | CrIS (selected channels) |  | 03/30 |
| IN | I |  | IRAS |  | 03/20 |
| IN | J |  | HIRAS |  | 03/30 |
| IN | K |  | MWHS/MWHS-2 |  | 03/40 |
| IN | Q |  | IASI (Principle component scores) |  | 03/7 |
| IN | S |  | ATMS |  | 03/40 |
| IN | T |  | MWTS/MWTS-2 |  | 03/40 |