- ANNEX TO PARAGRAPH 2.1.1 [FT2014-2/valid from 5 November 2014]

Add new bits and notes:

Flag table 3.4 – Scanning mode

Bit No.		Value				Meaning

5	0		Points within odd rows are not offset in i (x) direction

1		Points within odd rows are offset by Di/2 in i (x) direction

6	0		Points within even rows are not offset in i (x) direction

1		Points within even rows are offset by Di/2 in i (x) direction

7	0		Points are not offset in j (y) direction

1		Points are offset by Dj/2 in j (y) direction

8	0		Rows have Ni grid points and columns have Nj grid points

1		Rows have Ni grid points if points are not offset in i direction

Rows have Ni-1 grid points if points are offset by Di/2 in i direction

Columns have Nj grid points if points are not offset in j direction

Columns have Nj-1 grid points if points are offset by Dj/2 in j direction

Notes:

(4)	La1 and Lo1 define the first row, which is an odd row

(5)	Di and Dj are assumed to be positive, with the direction of i and j being given by bits 1 and 2

(6)	Bits 5 through 8 may be used to generate staggered grids, such as Arakawa grids (see Attachment, Volume I.2, Part B, Att. GRIB)

(7)	If any of bits 5, 6, 7 or 8 are set, Di and Dj are not optional

Add new Note (6) to GDT 3.0:

“In most cases, multiplying Ni (octets 31-34) by Nj (octets 35-38) yields the total number of points in the grid.  However, this may not be true if bit 8 of the scanning mode flags (octet 72) is set to 1.”

- ANNEX TO PARAGRAPH 2.2.1 [REVISED]

Add new entries:

Code table 4.2

| Product Discipline | Parameter Category | Parameter number | Parameter | Units |
| --- | --- | --- | --- | --- |
| 0 | 5 | 7 | Brightness temperature (See Note 1) | K |
| 2 | 0 | 38 | Soil volumetric ice content | m3 m–3 |
| 2 | 3 | 23 | Liquid water in snow pack | kg m–2 |
| 2 | 2 New category: Glaciers and inland ice | 1 | Glacier temperature | K |

Code Table 4.5

| Code Figure | Meaning | Unit |
| --- | --- | --- |
| 174 | Top surface of sea, lake or river ice | none |
| 175 | Top surface of sea, lake or river ice, under snow cover | none |
| 176 | Bottom surface (underside) of sea, lake or river ice | none |
| 177 | Deep soil (of indefinite depth) | none |
| 178 | Reserved |  |
| 179 | Inland or glacier ice (top surface) | none |
| 180 | Deep inland or glacier ice (of indefinite depth) | none |
| 181 | Grid tile land fraction as a model surface | none |
| 182 | Grid tile water fraction as a model surface | none |
| 183 | Grid tile sea, lake or river ice fraction as a model surface | none |
| 184 | Grid tile inland or glacier ice fraction as a model surface | none |

- ANNEX TO PARAGRAPH 2.2.2 [Validation]

Add a new template:

Product definition template 4.62 – Statistics over an ensemble reforecast, at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

Octet No.	Contents

10	Parameter category (see Code table 4.1)

11	Parameter number (see Code table 4.2)

12	Type of generating process (see Code table 4.3)

13	Background generating process identifier (defined by originating centre)

14	Forecast generating process identifier (defined by originating centre)

15	Indicator of unit of time range (see Code table 4.4)

16-19	Forecast time in units defined by octet 15 (see Note 1)

20	Type of first fixed surface (see Code table 4.5)

21	Scale factor of first fixed surface

22-25	Scaled value of first fixed surface

26	Type of second fixed surface (see Code table 4.5)

27	Scale factor of second fixed surface

28-31	Scaled value of second fixed surface

32	Type of ensemble forecast (see Code table 4.6)

33	Number of forecasts in ensemble

34	Number of years in the ensemble reforecast period (see Note 2)

35	First year of ensemble reforecast period

36	Last year of ensemble reforecast period

37	Total number of data values possible (or expected) in statistical process over the
 		ensemble reforecast

38-39	Total number of data values missing in statistical process over the ensemble
		reforecast

40	Statistical process used to calculate the processed field over the ensemble reforecast
		(see Code table 4.10)

41-42	Year of model version date (see Note 3)

43	Month of model version date

44	Day of model version date

45	Hour of model version date

46	Minute of model version date

47	Second of model version date

48	Month of end of overall time interval (see Note 5)

49	Day of end of overall time interval

50	Hour of end of overall time interval

51	Minute of end of overall time interval

52	Second of end of overall time interval

53	n - number of time range specifications describing the time intervals used

to calculate the statistically processed field

54-57	Total number of data values missing in statistical process

58-69	Specification of the outermost (or only) time range over which statistical

processing is done

58	Statistical process used to calculate the processed field from the field at

each time increment during the time range (see Code table 4.10)

59	Type of time increment between successive fields used in the statistical

processing (see Code table 4.11)

60	Indicator of unit of time for time range over which statistical processing is

done (see Code table 4.4)

61-64	Length of the time range over which statistical processing is done, in units

defined by the previous octet

65	Indicator of unit of time for the increment between the successive fields

used (see Code table 4.4)

66-69	Time increment between successive fields, in units defined by the previous

octet (see Note 3)

70-nn	These octets are included only if n>1, where nn=69 + 12 x n

70-81	As octets 58 to 69, next innermost step of processing

82-nn	Additional time range specifications, included in accordance with the value

of n. Contents as octets 58 to 69, repeated as necessary

Notes:

(1)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(2)	Octets 34-40 define a statistical process over both time and ensemble.

(3)	This is the date to identify the model version that is used to generate the reforecast.

(4)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples. Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge. The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 59, 71. 83 ...).  For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

- ANNEX TO PARAGRAPH 2.2.3 [FT2014-2/valid from 5 November 2014]

Add new entries:

Code table 4.2

Product discipline 0 – Meteorological products, parameter category 1: moisture

| Number | Parameter | Units | Description |
| --- | --- | --- | --- |
| 93 | Relative humidity with respect to water | % | The relative humidity with respect to water of moist air at pressure p and temperature T is the ratio in per cent of the vapour mole fraction xv to the vapour mole fraction xvw which the air would have if it were saturated with respect to water at the same pressure p and temperature T. |
| 94 | Relative humidity with respect to ice | % | The relative humidity with respect to ice of moist air at pressure p and temperature T is the ratio in per cent of the vapour mole fraction xv to the vapour mole fraction xvi which the air would have if it were saturated with respect to ice at the same pressure p and temperature T. |

Product discipline 0 – Meteorological products, parameter category 6: cloud

| Number | Parameter | Units | Description |
| --- | --- | --- | --- |
| 36 | Fraction of stratiform precipitation cover | Proportion | Horizontal fraction of the grid box covered by large-scale (stratiform) precipitation. |
| 37 | Fraction of convective precipitation cover | Proportion | Horizontal fraction of the grid box covered by convective precipitation. |

Add new entries:

Code table 4.201

Code table 4.201 – Precipitation type

Code figure 	Meaning

6	Wet snow

7	Mixture of rain and snow

8	Ice pellets

9	Graupel

10	Hail

- ANNEX TO PARAGRAPH 2.2.4 [COMBINED]

Add a new note:

Product definition template 4.57 - “analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function”

Add a new template (same as the previously proposed one):

Product definition template 4.57 - analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function

| Octet No. | Contents |
| --- | --- |
| 10 | Parameter category (see Code table 4.1) |
| 11 | Parameter number (see Code table 4.2) |
| 12–13 | Atmospheric chemical constituent type (see Code table 4.230) |
| 14–15 | Number of mode (N) of distribution (see Note 2) |
| 16–17 | Mode number (l) |
| 18–19 | Type of distribution function (see Code table 4.240) |
| 20 | Number of following function parameters (Np), defined by type given in octet 18-19 (Type of distribution function) |
|  | Repeat the following 5 octets for the number of function parameters (n=1,Np), if Np > 0 |
| (21+5(n-1) | List of scale factor of fixed distribution function parameter (p1–pNp)), defined by type of distribution in octet 18-19 |
| (22+5(n-1))– (25+5(n-1)) | List of scaled value of fixed distribution function parameter (p1–pNp)), defined by type of distribution in octet 18-19 |
| (21+5Np) | Type of generating process (see Code table 4.3) |
| (22+5Np) | Background generating process identifier (defined by originating centre) |
| (23+5Np) | Analysis or forecast generating process identifier (defined by originating centre) |
| (24+5Np)– (25+5Np) | Hours of observational data cut-off after reference time (see Note 1) |
| (26+5Np) | Minutes of observational data cut-off after reference time |
| (27+5Np) | Indicator of unit of time range (see Code table 4.4) |
| (28+5Np)– (31+5Np) | Forecast time in units defined by the previous octet |
| (32+5Np) | Type of first fixed surface (see Code table 4.5) |
| (33+5Np) | Scale factor of first fixed surface |
| (34+5Np)– (37+5Np) | Scaled value of first fixed surface |
| (38+5Np) | Type of second fixed surface (see Code table 4.5) |
| (39+5Np) | Scale factor of second fixed surface |
| (40+5Np)– (43+5Np) | Scaled value of second fixed surface |

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	If Number of mode (N) > 1, then between x*N fields with mode number l=1,…, N define the distribution function. x is the number of variable parameters in the distribution function.

Add new entries:

Code table 4.0 – Product definition template number

| Code figure | Meaning |
| --- | --- |
| 57 | Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function |

Code table 4.240 – Type of distribution function

| Code figure | Meaning |
| --- | --- |
| 0 | No specific distribution function given |
| 1 | Delta functions with spatially variable concentration and fixed diameters Dl (p1) in meter (see Note 1) |
| 2 | Delta functions with spatially variable concentration and fixed masses Ml (p1) in kg (see Note 2) |
| 3 | Gaussian (Normal) distribution with spatially variable concentration and fixed mean diameter Dl (p1) and variance σ (p2) (see Note 3) |
| 4 | Gaussian (Normal) distribution with spatially variable concentration, mean diameter and variance (see Note 4) |
| 5 | Log-normal distribution with spatially variable number density, mean diameter and variance (see Note 5) |
| 6 | Log-normal distribution with spatially variable number density, mean diameter and fixed variance σ (p1) (see Note 6) |
| 7 | Log-normal distribution with spatially variable number density and mass density and fixed variance σ (p1) and fixed particle density ρ (p2) (see Note 7) |
| 8-49151 | Reserved |
| 49152–65534 | Reserved for local use |
| 65535 | Missing |

Notes:

(1)	Bin-Model or delta function with N concentrations cl(r) in class (or mode) l. 
Concentration-density function:

where

N – number of modes in the distribution

δ – delta-function

d – diameter

Dl –diameter of mode l (p1)

(2)	Bin-Model or delta function with N concentrations cl(r) in class (or mode) l. 
Concentration-density function:

where 
N – number of modes in the distribution
δ – delta-function
m – mass
Ml –mass of mode l (p1)

(3)	N-modal concentration-density function consisting of Gaussian-functions:

where
N – number of modes in the distribution
d – diameter
Dl –mean diameter of mode l (p1)
σl – variance of mode l (p2)

with N fields of concentration cl(r).

(4)	N-modal concentration-density function consisting of Gaussian-functions:

with 3N fields of concentration cl(r), variance σl(r) and mean diameter Dl(r).

(5)	N-modal log-normal-distribution for the number density:

where 
d – diameter

with 3N fields of number density nl(r), variance σl(r) and mean diameter Dl(r).

(6)	N-modal log-normal-distribution for the number density:

where
σl – variance of mode l (p1)

with 2N fields of number density nl(r) and mean diameter Dl(r).

(7)	N-modal log-normal-distribution for the number density as in Note (6), but with a prescribed mass density ml(r), from which the diameter Dl(r) is calculated by:

where
σl – variance of mode l (p1)

ρp,l – particle density (p2)

with 2N fields of number density nl(r)  and mass density ml(r).

- ANNEX TO PARAGRAPH 2.2.5 [Validation]

Add new entries:

Code table 4.0

| Octet No. | Contents |
| --- | --- |
| 55 | Spatio-temporal changing tiles at a horizontal level or horizontal layer at a point in time |
| 56 | Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time for spatio-temporal changing tile parameters |

Add new templates:

Product definition template 4.55 – Spatio-temporal changing tiles at a horizontal level or horizontal layer at a point in time

| Octet No. | Contents |
| --- | --- |
| 10 | Parameter category (see Code table 4.1) |
| 11 | Parameter number (see Code table 4.2) |
| 12 | Tile classification (see Code table 4.242) |
| 13 | Number of used tiles (NUT) (see Notes 2 and 3) |
| 14 | Identification number of tile (ITN = {1,…, NUT}) (see Note 2) |
| 15 | Number of used tile attributes (NAT) for tile ITN (see Note 2) |
| 16 | Identification number of tile attribute (IAN = {1,…, NAT(ITN)}) (see Note 2) |
| 17 | Attribute of tile (see Code table 4.241) |
| 18 | Type of generating process (see Code table 4.3) |
| 19 | Background generating process identifier (defined by originating centre) |
| 20 | Analysis or forecast generating process identifier (defined by originating centre) |
| 21 – 22 | Hours of observational data cut-off after reference time (see Note) |
| 23 | Minutes of observational data cut-off after reference time |
| 24 | Indicator of unit of time range (see Code table 4.4) |
| 25 – 28 | Forecast time in units defined by octet 24 |
| 29 | Type of first fixed surface (see Code table 4.5) |
| 30 | Scale factor of first fixed surface |
| 31 – 34 | Scaled value of first fixed surface |
| 35 | Type of second fixed surface (see Code table 4.5) |
| 36 | Scale factor of second fixed surface |
| 37 – 40 | Scaled value of second fixed surface |

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The number of used Tiles (NUT) is the number of used different tiles, defining the cover structure of a point. As each of these tiles do have one or more different tile attributes NAT(ITN)  ( ITN=1,…,NUT), e.g. unmodified, snow-covered,…), there are  fields with identification numbers ( ITN, IAN )  with the following meaning:

1,1	First tile – first attribute (e.g. unmodified)

….	….

1,NAT(1)	First tile – NAT of first tile (last, e.g. snow-covered) attribute

2,1	Second tile – first attribute (e.g. unmodified)

….	….

2,NAT(2)	Second tile – NAT of second tile (last, e.g. snow-covered) attribute

.	.

.	.

NUT,1	NUT tile – first attribute (e.g. unmodified)

….	...

NUT,NAT(NUT)	NUT tile – NAT of last tile (last) attribute

A single tile index (ITN, IAN) with code value ITN (1,…,NUT) and attribute identification IAN (1,…,NAT(ITN)) is represented in the template. All partitions are linked by the normalisation formula stating that the sum of all partitions must be equal to a normalisation term (N=1 for fractions and N=100 for percentage) on each point of the grid.

To get the tile structure of each grid point, the fields “tile class” and “tile fraction” have to be provided.

Product definition template 4.56 – Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time for spatio-temporal changing tile parameters

| Octet No. | Contents |
| --- | --- |
| 10 | Parameter category (see Code table 4.1) |
| 11 | Parameter number (see Code table 4.2) |
| 12 | Tile classification (see Code table 4.242) |
| 13 | Number of used tiles (NUT) (see Notes 2 and 3) |
| 14 | Identification number of tile (ITN = {1,…, NUT}) (see Note 2) |
| 15 | Number of used tile attributes (NAT) for tile ITN (see Note 2) |
| 16 | Identification number of tile attribute (IAN = {1,…, NAT(ITN)}) (see Note 2) |
| 17 | Attribute of tile (see Code table 4.241) |
| 18 | Type of generating process (see Code table 4.3) |
| 19 | Background generating process identifier (defined by originating centre) |
| 20 | Analysis or forecast generating process identifier (defined by originating centre) |
| 21 – 22 | Hours of observational data cut-off after reference time (see Note) |
| 23 | Minutes of observational data cut-off after reference time |
| 24 | Indicator of unit of time range (see Code table 4.4) |
| 25 – 28 | Forecast time in units defined by octet 24 |
| 29 | Type of first fixed surface (see Code table 4.5) |
| 30 | Scale factor of first fixed surface |
| 31 – 34 | Scaled value of first fixed surface |
| 35 | Type of second fixed surface (see Code table 4.5) |
| 36 | Scale factor of second fixed surface |
| 37 – 40 | Scaled value of second fixed surface |
| 41 | Perturbation number |
| 42 | Number of forecasts in ensemble |

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	See note (2) under product definition template 4.55.

- ANNEX TO PARAGRAPH 2.2.6 [FT2014-2/valid from 5 November 2014]

Add new parameters:

Code table 4.2

Product discipline 2 - Land surface products, parameter category 0: vegetation/biomass

| Number | Parameter | Units |
| --- | --- | --- |
| 35 | tile class | Code table 4.243 |
| 36 | tile fraction | Proportion |
| 37 | tile percentage | % |

Add new code tables:

Code table 4.241 – Coverage attributes

| Code figure | Meaning |
| --- | --- |
| 0 | Undefined |
| 1 | Unmodified |
| 2 | Snow-covered |
| 3 | Flooded |
| 4 | Ice covered |
| 5–191 | Reserved |
| 192–254 | Reserved for local use |
| 255 | Missing |

Code table 4.242 – Tile Classification

| Code figure | Meaning |
| --- | --- |
| 0 | Reserved |
| 1 | Land use classes according to ESA-GLOBCOVER GCV2009 |
| 2 | Land use classes according to European Commission - Global Land Cover Project GLC2000 |
| 3–191 | Reserved |
| 192–254 | Reserved for local use |
| 255 | Missing |

Code table 4.243 – Tile Class

| Code figure | Meaning |
| --- | --- |
| 0 | Reserved |
| 1 | Evergreen broadleaved forest |
| 2 | Deciduous broadleaved closed forest |
| 3 | Deciduous broadleaved open forest |
| 4 | Evergreen needle-leaf forest |
| 5 | Deciduous needle-leaf forest |
| 6 | Mixed leaf trees |
| 7 | Fresh water flooded trees |
| 8 | Saline water flooded trees |
| 9 | Mosaic tree/natural vegetation |
| 10 | Burnt tree cover |
| 11 | Evergreen shrubs closed-open |
| 12 | Deciduous shrubs closed-open |
| 13 | Herbaceous vegetation closed-open |
| 14 | Sparse herbaceous or grass |
| 15 | Flooded shrubs or herbaceous |
| 16 | Cultivated and managed areas |
| 17 | Mosaic crop/tree/natural vegetation |
| 18 | Mosaic crop/shrub/grass |
| 19 | Bare areas |
| 20 | Water |
| 21 | Snow and ice |
| 22 | Artificial surface |
| 23 | Ocean |
| 24 | Irrigated croplands |
| 25 | Rain fed croplands |
| 26 | Mosaic cropland (50-70%) - vegetation (20-50%) |
| 27 | Mosaic vegetation (50-70%) - cropland (20-50%) |
| 28 | Closed broadleaved evergreen forest |
| 29 | Closed needle-leaved evergreen forest |
| 30 | Open needle-leaved deciduous forest |
| 31 | Mixed broadleaved and needle-leaved forest |
| 32 | Mosaic shrubland (50-70%) - grassland (20-50%) |
| 33 | Mosaic grassland (50-70%) - shrubland (20-50%) |
| 34 | Closed to open shrubland |
| 35 | Sparse vegetation |
| 36 | Closed to open forest regularly flooded |
| 37 | Closed forest or shrubland permanently flooded |
| 38 | Closed to open grassland regularly flooded |
| 39 | Undefined |
| 40–32767 | Reserved |
| 32768– | Reserved for local use |

- ANNEX TO PARAGRAPH 2.2.7 [ABC2015 but effectively to be in the list for CBS session
/Rec. 7 (CBS-Ext. (2014))/4 November 2015]

Add a new note:

GRIB Product definition template 4.44

Note: It is recommended not to use this template.  PDT 4.48 should be used instead with optical wave length range set to missing.

- ANNEX TO PARAGRAPH 2.2.8 [FT2014-2/valid from 5 November 2014]

Add new entries:

Code table 4.3 (Type of generating process)

Code figure		Meaning

14			Nowcast

15			Hindcast

- ANNEX TO PARAGRAPH 3.1.1 [For reference]

FOR REFERENCE:

COMMON CODE TABLE C-15: Physical quantity kinds

Note: The Unique Resource Identifier (URI) of each physical quantity kind is composed by the prefix http://codes.wmo.int/common/c-15/ and the notation. As an example the URI of airTemperature is http://codes.wmo.int/common/c-15/airTemperature.  The URI can be used in the XML code format and is also a URL providing comprehensive information regarding the physical quantity kind.

| Label | Notation | Description | Dimensions |
| --- | --- | --- | --- |
| Aerodrome maximum wind gust speed | aerodromeMaximumWindGustSpeed | Maximum wind speed in the 10 minute period of observation. It is reported only if exceeds the mean speed by 5 m s–1 (10 knots). | LT-1 |
| Aerodrome mean wind direction | aerodromeMeanWindDirection | The mean true direction in degrees from which the wind is blowing over the 10-minute period immediately preceding the observation. When the 10-minute period includes a marked discontinuity in the wind characteristics (1), only data after the discontinuity shall be used for mean wind direction and variations of the wind direction, hence the time interval in these circumstances shall be correspondingly reduced. | dimensionless |
| Aerodrome mean wind speed | aerodromeMeanWindSpeed | The mean speed of the wind over the 10-minute period immediately preceding the observation. When the 10-minute period includes a marked discontinuity in the wind characteristics (1), only data after the discontinuity shall be used for obtaining mean wind speed, hence the time interval in these circumstances shall be correspondingly reduced. | LT-1 |
| Aerodrome minimum horizontal visibility | aerodromeMinimumHorizontalVisibility | The minimum horizontal visibility that is reported when the horizontal visibility is not the same in different directions and when the minimum visibility is different from the prevailing visibility, and less than 1500 metres or less than 50% of the prevailing visibility, and less than 5000 metres. | L |
| Aerodrome minimum visibility direction | aerodromeMinimumVisibilityDirection | When the minimum horizontal visibility is reported, its general direction in relation to the aerodrome reference point has to be reported and indicated by reference to one of the eight points of the compass. If the minimum visibility is observed in more than one direction, the Dv shall represent the most operationally significant direction. | dimensionless |
| Aeronautical prevailing horizontal visibility | aeronauticalPrevailingHorizontalVisibility | The greatest visibility value, observed in accordance with the definition of “visibility”, which is reached within at least half the horizon circle or within at least half of the surface of the aerodrome. These areas could comprise contiguous or non-contiguous sectors. | L |
| Aeronautical visibility | aeronauticalVisibility | The greater of:(a) The greatest distance at which a black object of suitable dimensions, situated near the ground, can be seen and recognized when observed against a bright background; (b) The greatest distance at which lights in the vicinity of 1000 candelas can be seen and identified against an unlit background. | L |
| Air temperature | airTemperature | The temperature indicated by a thermometer exposed to the air in a place sheltered from direct solar radiation. | Θ |
| Altimeter setting (QNH) | altimeterSettingQnh | Altimeter setting (also known as QNH) is defined as barometric pressure adjusted to sea level. It is a pressure setting used by pilots, air traffic control (ATC), and low frequency weather beacons to refer to the barometric setting which, when set on an aircraft's altimeter, will cause the altimeter to read altitude above mean sea level within a certain defined region. | ML-1T-2 |
| Atmospheric pressure | atmosphericPressure | The atmospheric pressure on a given surface is the force per unit area exerted by virtue of the weight of the atmosphere above. The pressure is thus equal to the weight of a vertical column of air above a horizontal projection of the surface, extending to the outer limit of the atmosphere. | ML-1T-2 |
| Depth of runway deposit | depthOfRunwayDeposit | Depth of deposit on surface of runway | L |
| Dew-point temperature | dewPointTemperature | The temperature to which a given air parcel must be cooled at constant pressure and constant water vapour content in order for saturation to occur. | Θ |
| Height of base of cloud | heightOfBaseOfCloud | For a given cloud or cloud layer, vertical distance (measured from local ground surface) of the lowest level in the atmosphere at which the air contains a perceptible quantity of cloud particles. | L |
| Horizontal visibility | horizontalVisibility | The greatest distance determined in the horizontal plane at the ground surface that prominent objects can be seen and identified by unaided, normal eyes. | L |
| Maximum wind gust speed | maximumWindGustSpeed | Nominal maximum speed of wind during a given period; usually determined as a mean wind speed over a short duration (e.g. 1-minute) within a longer period (e.g. 10-minutes). | LT-1 |
| Runway contamination coverage | runwayContaminationCoverage | Proportion of runway that is contaminated. A runway is considered to be contaminated when more than 25% of the runway surface area(whether in isolated areas or not) within the required length and width being used is covered by the following:(a) Surface water more than 3 mm deep, or by slush or loose snow equivalent to more than 3 mm of water; (b) Snow which has been compressed into a solid mass which resists further compression and will hold together or break into lumps if picked up (compacted snow); or (c) Ice, including wet ice. | dimensionless |
| Runway friction coefficient | runwayFrictionCoefficient | Quantitative assessment of friction coefficient of runway surface. | dimensionless |
| Runway visual range (RVR) | runwayVisualRangeRvr | The range over which the pilot of an aircraft on the centre line of a runway can see the runway surface markings or the lights delineating the runway or identifying its centre line. | L |
| Sea surface temperature | seaSurfaceTemperature | Temperature of the sea water at surface. | Θ |
| Vertical visibility | verticalVisibility | Maximum distance at which an observer can see and identify an object on the same vertical as himself, above or below. | L |

Notes:

(1)	A marked discontinuity occurs when there is an abrupt and sustained change in wind direction of 30° or more, with a wind speed of 5 ms–1 (10 KT) or more before or after the change, or a change in wind speed of 5 ms–1 (10 KT) or more, lasting at least two minutes.

- ANNEX TO PARAGRAPH 3.1.2 [CBS session/Rec. 7 (CBS-Ext. (2014))/4 November 2015]

Amend Regulations:

94.1.5	Missing values shall be expressed by all bits set to 1 within the data width of the element. This shall apply to all Table B elements, including elements defined as CCITT IA5, code tables and flag tables, with the exception of data description operator qualifiers in Class 31.

Note: Flag tables are always augmented to contain an additional bit as the least significant bit of the table.  All bits, including this additional bit, shall be set to 1 to express a missing value, but in all other cases this additional bit shall be set to 0. This note does not apply to Data present indicator 0 31 031.

Amend Regulations:

94.1.6	The convention for representing missing data for compressed data within the binary Data section shall be to set the corresponding increments to fields of all bits set to 1.

94.1.7	When a local reference value for a set of element values for compressed data is represented as all bits set to 1, this shall imply that all values in the set are missing.

94.6.3	...

Notes: ...

(2)	...

(iii)	If all values of an element are missing, R0 shall be coded with all bits set to 1;

(vi)	Missing values will be denoted by setting all bits of the corresponding I to 1;

- ANNEX TO PARAGRAPH 3.1.4 [REVISED]

STATEMENT TO CBS:

TAC (traditional alphanumeric codes) is no longer supported but sometimes used as a national format.  This can lead to cases where changes need to be recommended as a national practice rather than as an official changes to a WMO code.  Members who still use conversion are encouraged to use the reporting practices from the B/C regulations.  For example, if TAC is used in national practice, appropriate measures need to be taken in order to report zero snow depth. Specifically, if zero snow depth reporting is required, it is suggested that the code figure 000 from code table 3889 be used.

- ANNEX TO PARAGRAPH 3.2.1 [FT2014-2/valid from 5 November 2014]

Add new entries:

Common Code table C-5     Satellite identifier

| 061 | 61 | 61 | Sentinel 3A |
| --- | --- | --- | --- |
| 287 | 287 | 287 | DMSP-19 |
| 288 | 288 | 288 | GPM-core |
| 516 | 516 | 516 | FY-2F |
| 517 | 517 | 517 | FY-2G |
| 522 | 522 | 522 | FY-3C |

Common Code table C-8     Satellite Instruments

| 178 | ESA | Radar altimeter | SRAL | Synthetic aperture radar altimeter |
| --- | --- | --- | --- | --- |
| 179 | ESA | Moderate resolution optical imager | OLCI | Ocean and land colour imager |
| 180 | ESA | Moderate resolution optical imager | SLSTR | Sea and land surface temperature radiometer |
| 518 | JAXA | Cloud and precipitation radar | DPR | Dual-frequency precipitation radar |
| 519 | NASA | MW imaging/sounding radiometer, conical scanning | GMI | GPM microwave imager |
| 953 | CMA | Microwave sounding radiometer, crosstrack scanning | MWHS-2 | Microwave humidity sounder-2 |
| 954 | CMA | Microwave sounding radiometer, crosstrack scanning | MWTS-2 | Microwave temperature sounder-2 |
| 955 | CMA | Cross-nadir scanning IR sounder | HIRAS | Hyperspectral infrared atmospheric sounder |

BUFR  Code table 0-02-020 - Satellite classification

| 20 | GPM-core |
| --- | --- |
| 92 | Sentinel-3 |
| 382 | FY-3 |

- ANNEX TO PARAGRAPH 3.2.2 [FT2014-2/valid from 5 November 2014]

Add a new entry:

| Sequence code | Sequence composition |  | Description |
| --- | --- | --- | --- |
|  |  |  | Snow observation |
| 3 07 101 | 3 01 089 |  | National station identification |
|  |  | 0 01 101 | State identifier |
|  |  | 0 01 102 | National station number |
|  | 0 01 019 |  | Long station or site name |
|  | 0 02 001 |  | Type of station |
|  | 3 01 011 |  | Year, month, day |
|  |  | 0 04 001 | Year |
|  |  | 0 04 002 | Month |
|  |  | 0 04 003 | Day |
|  | 3 01 012 |  | Hour, minute |
|  |  | 0 04 004 | Hour |
|  |  | 0 04 005 | Minute |
|  | 3 01 021 |  | Latitude/longitude (high accuracy) |
|  |  | 0 05 001 | Latitude (high accuracy) |
|  |  | 0 06 001 | Longitude (high accuracy) |
|  | 0 07 030 |  | Height of station ground above mean sea level |
|  | 0 07 032 |  | Height of sensor above local ground (or deck of marine platform) |
|  | 0 12 101 |  | Temperature/air temperature |
|  | 0 07 032 |  | Height of sensor above local ground (or deck of marine platform) |
|  | 0 02 177 |  | Method of snow depth measurement |
|  | 0 20 062 |  | State of the ground (with or without snow) |
|  | 0 13 013 |  | Total snow depth |

- ANNEX TO PARAGRAPH 3.2.3 [FT2015-1/valid from 6 May 2015]

Add a new entry:

BUFR Table D

3 07 074 – Supplemental daily extreme temperature and precipitation values for monthly climate report

| 3 01 001 | WMO block and station numbers |  |
| --- | --- | --- |
| 0 04 001 | Year |  |
| 0 04 002 | Month |  |
| 3 01 021 | Latitude/longitude (high accuracy) |  |
| 0 07 030 | Height of station ground above mean sea level |  |
| 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
| 1 12 000 | Delayed replication of 12 descriptors |  |
| 0 31 001 | Delayed descriptor replication factor | Set to the number of days in the particular month for which data are being reported |
| 0 04 003 | Day |  |
| 0 04 004 | Hour |  |
| 0 04 024 | Time period or displacement | Typically set to -24 to denote the time period beginning 24 hours prior to and ending at the specified time |
| 1 02 003 | Replicate 2 descriptors 3 times |  |
| 0 08 023 | First-order statistics | = 2 Daily maximum temperature, = 3 Daily minimum temperature, = 4 Daily average temperature |
| 0 12 101 | Temperature/air temperature |  |
| 0 08 023 | First-order statistics | Set to missing (cancel) |
| 0 04 004 | Hour |  |
| 0 04 024 | Time period or displacement |  |
| 0 13 060 | Total accumulated precipitation |  |
| 0 13 012 | Depth of fresh snow |  |
| 0 13 013 | Total snow depth |  |

- ANNEX TO PARAGRAPH 3.2.4 [FT2014-2/Pre-operational/valid from 5 November 2014]

Add a new entry:

BUFR Table B

| F X Y | Element name | BUFR Unit | BUFR Scale | BUFR Ref. val | BUFR Bits | CREX Unit | CREX Scale | CREX width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 08 087 | Corner position of observation | Code table | 0 | 0 | 3 | Code table | 0 | 1 |

Add a new Code table:

Code table 0 08 087 - Corner position of observation

| Code figure | Description |
| --- | --- |
| 0 | Upper left |
| 1 | Upper right |
| 2 | Lower right |
| 3 | Lower left |
| 4-6 | Reserved |
| 7 | Missing value |

- ANNEX TO PARAGRAPH 3.2.5 [REVISED]

Add new entries:

BUFR Table D

|  | (SARAL Altika) |
| --- | --- |
| 3 40 011 | 0 01 007 | Satellite identifier |  |
|  | 0 02 019 | Satellite instruments |  |
|  | 0 01 096 | Station acquisition |  |
|  | 0 25 061 | Software identification and version number |  |
|  | 0 05 044 | Satellite cycle number |  |
|  | 0 05 040 | Orbit number |  |
|  | 0 01 030 | Numerical model identifier |  |
|  | 0 04 001 | Year |  |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour |  |
|  | 0 04 005 | Minute |  |
|  | 0 04 007 | Seconds within a minute (microsecond accuracy) |  |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 0 08 029 | Surface type |  |
|  | 0 08 077 | Radiometer sensed surface type |  |
|  | 0 40 011 | Interpolation flag |  |
|  | 0 25 097 | Three-dimensional error estimate of the navigator orbit |  |
|  | 0 25 112 | Band specific altimeter data quality flag |  |
|  | 0 25 113 | Band specific altimeter correction quality flag |  |
|  | 0 21 148 | Trailing edge variation flag |  |
|  | 0 21 169 | Ice presence indicator |  |
|  | 0 40 024 | Meteorological map availability |  |
|  | 0 40 025 | Interpolation flag for mean diurnal tide |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 22 189 | Specific band ocean range |  |
|  | 0 22 191 | RMS of specific band ocean range |  |
|  | 0 22 192 | Number of valid points for specific band |  |
|  | 0 25 167 | Specific band net instrumental correction |  |
|  | 0 25 166 | Sea state bias correction on specific band |  |
|  | 0 22 190 | Specific band significant wave height |  |
|  | 0 22 193 | RMS specific band significant wave height |  |
|  | 0 22 194 | Number of valid points for specific band sign wave height |  |
|  | 0 22 195 | Specific band net instrument correction for significant wave height |  |
|  | 0 21 183 | Specific band corrected ocean backscatter coefficient |  |
|  | 0 21 184 | STD specific band corrected ocean backscatter coefficient |  |
|  | 0 22 196 | Number of valid points for specific band backscatter |  |
|  | 0 21 185 | Specific band net instrumental correction for agc |  |
|  | 0 21 118 | Attenuation correction on sigma-0 |  |
|  | 0 21 186 | Specific band automatic gain control |  |
|  | 0 21 187 | RMS specific band automatic gain control |  |
|  | 0 21 188 | Number of valid points for specific band automatic gain control |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 12 063 | Brightness temperature |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 12 063 | Brightness temperature |  |
|  | 0 13 090 | Radiometer water vapour content |  |
|  | 0 13 160 | Radiometer liquid content for saral |  |
|  | 0 07 002 | Height or altitude |  |
|  | 0 11 097 | Wind speed from altimeter |  |
|  | 0 07 002 | Height or altitude |  |
|  | 0 11 095 | u-component of the model wind vector |  |
|  | 0 11 096 | v-component of the model wind vector |  |
|  | 0 10 096 | Mean dynamic topography |  |
|  | 0 10 081 | Altitude of COG above reference ellipsoid |  |
|  | 0 10 082 | Instantaneous altitude rate |  |
|  | 0 10 083 | Squared off-nadir angle of the satellite from platform data |  |
|  | 0 10 101 | Squared off-nadir angle of the satellite from waveform data |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 25 165 | Ionospheric correction from model on specific band |  |
|  | 0 25 126 | Model dry tropospheric correction |  |
|  | 0 25 128 | Model wet tropospheric correction |  |
|  | 0 25 164 | Radiometer wet tropospheric correction |  |
|  | 0 10 085 | Mean sea-surface height |  |
|  | 0 10 086 | Geoid's height |  |
|  | 0 10 087 | Ocean depth/land elevation |  |
|  | 0 10 092 | Solid Earth tide height |  |
|  | 0 10 088 | Total geocentric ocean tide height (solution 1) |  |
|  | 0 10 089 | Total geocentric ocean tide height (solution 2) |  |
|  | 0 10 098 | Loading tide height geocentric ocean tide solution 1 |  |
|  | 0 10 099 | Loading tide height geocentric ocean tide solution 2 |  |
|  | 0 10 090 | Long period tide height |  |
|  | 0 10 100 | Non-equilibrium long period tide height |  |
|  | 0 10 093 | Geocentric pole tide height |  |
|  | 0 25 127 | Inverted barometer correction |  |
|  | 0 40 014 | High-frequency fluctuations of the sea-surface topography correction |  |
|  | 0 10 102 | Sea-surface height anomaly |  |

BUFR/CREX Table B

| F X Y | Element Name | BUFR Units | BUFR Scale | BUFR Ref. | BUFR Width | CREX Units | CREX Scale | CREX Width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 13 160 | Radiometer liquid content for saral | kg m-2 | 2 | -350 | 10 | kg m-2 |  |  |
| 0 21 148 | Trailing edge variation flag | Flag table | 0 | 0 | 2 | Flag table |  |  |
| 0 21 183 | Specific band corrected ocean backscatter coefficient | dB | 2 | -32768 | 16 | dB |  |  |
| 0 21 184 | STD specific band corrected ocean backscatter coefficient | dB | 2 | -32768 | 16 | dB |  |  |
| 0 21 185 | Specific band net instrumental correction for agc | dB | 2 | -2048 | 12 | dB |  |  |
| 0 21 186 | Specific band automatic gain control | dB | 2 | 0 | 13 | dB |  |  |
| 0 21 187 | RMS specific band automatic gain control | dB | 2 | 0 | 8 | dB |  |  |
| 0 21 188 | Number of valid points for specific band automatic gain control | Numeric | 0 | 0 | 7 | Numeric |  |  |
| 0 22 189 | Specific band ocean range | m | 3 | 0 | 31 | m |  |  |
| 0 22 190 | Specific band significant wave height | m | 3 | 0 | 16 | m |  |  |
| 0 22 191 | RMS of specific band ocean range | m | 4 | 0 | 16 | m |  |  |
| 0 22 192 | Number of valid points for specific band | Numeric | 0 | 0 | 10 |  |  |  |
| 0 22 193 | RMS specific band significant wave height | m | 3 | 0 | 16 |  |  |  |
| 0 22 194 | Number of valid points for specific band sign wave height | Numeric | 0 | 0 | 10 |  |  |  |
| 0 22 195 | Specific band net instrument correction for significant wave height | m | 3 | -1000 | 11 |  |  |  |
| 0 22 196 | Number of valid points for specific band backscatter | Numeric | 0 | 0 | 10 |  |  |  |
| 0 25 112 | Band specific altimeter data quality flag | Flag table | 0 | 0 | 9 | Flag table |  |  |
| 0 25 113 | Band specific altimeter correction quality flag | Flag table | 0 | 0 | 9 | Flag table |  |  |
| 0 25 165 | Ionospheric correction from model on specific band | m | 4 | -32768 | 16 | m |  |  |
| 0 25 166 | Sea state bias correction on specific band | m | 4 | -32768 | 16 | m |  |  |
| 0 25 167 | Specific band net instrumental correction | m | 4 | -120000 | 18 | m |  |  |

| 0 21 148 |
| --- |
| Trailind edge variation flag Bit No. (0 is good, 1 is bad) |
| 1 | No short scale variation |
| 2 | Short scale variation |
| 3-8 | Reserved |
| All 9 | Missing value |

| 0 25 112 |
| --- |
| Band specific altimeter data quality flag Bit No. (0 is good, 1 is bad) |
| 1 | Band specific range |
| 2 | Band specific SWH* |
| 3 | Band specific backscatter coefficient |
| 4 | Off nadir angle from band specific waveform parameters |
| 5 | Off nadir angle from platform |
| 6-8 | Reserved |
| All 9 | Missing value |

| 0 25 113 |
| --- |
| Band specific altimeter correction quality flag Bit No. (0 is good, 1 is bad) |
| 1 | Band specific range instrumental correction |
| 2 | Band specific SWH* instrumental correction |
| 3 | Band specific backscatter coefficient instrumental correction |
| 4-8 | Reserved |
| All 9 | Missing value |

- ANNEX TO PARAGRAPH 3.2.6 [Further development]

BUFR Table B

| F X Y | Element Name | BUFR Units | BUFR Scale | BUFR Ref. | BUFR Width | CREX Units | CREX Scale | CREX Width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 05 062 | Spacecraft latitude (see Note x) | ° | 5 | –9000000 | 25 | ° | 5 | 7 |
| 0 06 041 | Spacecraft longitude (see Note x+1) | ° | 5 | –18000000 | 26 | ° | 5 | 8 |
| 0 40 027 | Spacecraft orientation (see Note x+2) | ° | 2 | 0 | 16 | ° | 2 |  |
| 0 40 028 | Sun-glint angle (see Note x+3) | ° | 5 | 0 | 26 | ° | 5 |  |

Notes:

(x)	The geodetic latitude of the spacecraft at the Scan mid-Time

(x+1)	The geodetic longitude of the spacecraft at the Scan mid-Time

(x+2)	The positive angle of the spacecraft vector (v) from the satellite forward direction of motion, measured clockwise facing down

(x+3)	The angle between the sun and the instrument view direction as reﬂected of the Earth’s surface.

- ANNEX TO PARAGRAPH 3.2.7 [Validation] <to be combined with 2013-3.2.1 DRMM-I>

Add new entries:

BUFR Table D

|  |  | (Temperature and humidity instrumentation) |  |
| --- | --- | --- | --- |
| 3 01 130 | 0 03 002 | Generic type of humidity instrument |  |
|  | 0 03 003 | Configuration of sensors |  |
|  | 0 03 004 | Type of shield or screen |  |
|  | 0 03 005 | Horizontal width of screen or shield (x) |  |
|  | 0 03 006 | Horizontal depth of screen or shield (y) |  |
|  | 0 03 007 | Vertical height of screen or shield (z) |  |
|  | 0 03 008 | Artificially ventilated screen or shield |  |
|  | 0 03 009 | Amount of forced ventilation at time of reading |  |

BUFR/CREX Table B

| F X Y | Element Name | BUFR Units | BUFR Scale | BUFR Ref. | BUFR Width | CREX Units | CREX Scale | CREX Width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 03 001 | Surface station type | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 03 002 | Generic type of humidity instrument | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 03 003 | Configuration of sensors | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 03 004 | Type of shield or screen | Code table | 0 | 0 | 5 | Code table | 0 | 2 |
| 0 03 005 | Horizontal width of screen or shield (x) | m | 2 |  |  | m | 2 |  |
| 0 03 006 | Horizontal depth of screen or shield (y) | m | 2 |  |  | m | 2 |  |
| 0 03 007 | Vertical height of screen or shield (z) | m | 2 |  |  | m | 2 |  |
| 0 03 008 | Artificially ventilated screen or shield | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 03 009 | Amount of forced ventilation at time of reading | m-3 s-1 | 1 |  |  | m-3 s-1 | 1 |  |

Code tables

0 03 001  Surface station type

Code figure

0	Land station (synoptic network)

1	Shallow water station (fixed to sea/lake floor)

2	Ship

3	Rig/platform

4	Moored buoy

5	Drifting buoy (or drifter)

6	Ice buoy

7	Land station (local network)

8	Land vehicle

9	Autonomous marine vehicle

10-14	Reserved

15	Missing value

0 03 002   Generic type of humidity instrument

Code figure

0	Psychrometer [too generic]

1	Capacitive sensor (unheated)

2	Capacitive sensor (heated)

3	Resistive sensor [too generic]

4	Ordinary human hair

5	Rolled hair

6	Goldbeater’s skin

7	Chilled mirror hygrometer

8	Dew cell

9	Optical absorption sensor

10-14	Reserved

15	Missing value

0 03 003  Configuration of Sensors [already full]

Code figure

0	Solar radiation shield or screen (double v section louvers)

1	No solar radiation shield or screen

2	Solar radiation shield or screen (single v section louvers)

3	Solar radiation shield or screen (overlapping louvers)

4	Solar radiation shield or screen (non-overlapping louvers)

5	Solar radiation shield or screen (not louvered)

6	Integrated e.g. chilled mirror

7	Missing value

0 03 004 Type of Shield or Screen [entries need to be checked]

Code figure

0	Within Stevenson screen (wooden)

1	Within Stevenson screen (plastic)

2	Within marine Stevenson screen (wooden)

3	Within marine Stevenson screen (plastic)

4	Within cylindrical section plate shield (metal)

5	Within cylindrical section plate shield (wooden)

6	Within cylindrical section plate shield (plastic)

7	Within concentric tube (metal)

8	Within concentric tube (wooden)

9	Within concentric tube (plastic)

10	Within rectangular section shield (metal)

11	Within rectangular section shield (wooden)

12	Within rectangular section shield (plastic)

13	Within rectangular section shield (metal)

14	Within square section shield (wooden)

15	Within square section shield (plastic)

16	Within square section shield (metal)

17	Within triangular section shield (wooden)

18	Within triangular section shield (plastic)

19	Within triangular section shield (metal)

20	Within open covered lean-to (reed/grass/leaf)

21	Within open covered inverted v roof (reed/grass/leaf)

22-29	Reserved

30	Not Applicable, e.g. chilled mirror manufacturers enclosure

31	Missing value

0 03 008 Artificially Ventilated Screen or Shield

Code figure

0	Natural ventilation in use

1	Artificial aspiration in use: constant flow at time of reading

2	Artificial aspiration in use: variable flow at time of reading

3 -6	Reserved

7	Missing value

REVISED TEMPLATE

|  |  | National station identification |  |
| --- | --- | --- | --- |
| 3 01 089 | 0 01 101 | State identifier (1) | Code table, 0 |
|  | 0 01 102 | National station number (1) | Numeric, 0 |
|  |  | Fixed surface station identification; time, horizontal and vertical co-ordinates |  |
| 3 01 090 | 3 01 004 | Surface station identification |  |
|  |  | WMO block number | Numeric, 0 |
|  |  | WMO station number | Numeric, 0 |
|  |  | Station or site name | CCITT IA5, 0 |
|  |  | Type of station | Code table, 0 |
|  | 3 01 011 | Year(2) | Year, 0 |
|  |  | Month(2) | Month, 0 |
|  |  | Day(2) | Day, 0 |
|  | 3 01 012 | Hour(2) | Hour, 0 |
|  |  | Minute(2) | Minute, 0 |
|  | 3 01 021 | Latitude (high accuracy) | Degree, 5 |
|  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, 1 |
| 0 03 001 |  | Surface station type | Code table, 0 |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  | Surface station instrumentation |  |
|  | 0 02 180 | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 | Visibility measurement system | Code table, 0 |
|  | 0 02 183 | Cloud detection system | Code table, 0 |
|  | 0 02 184 | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 | Capability to discriminate lightning strikes | Flag table, 0 |
| 0 04 015 |  | Time increment (= - n minutes) | Minute, 0 |
| 0 04 065 |  | Short time increment ( = 1 minute) | Minute, 0 |
| 1 33 000 |  | Delayed replication of 33 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor (= n) | Numeric, 0 |
| 0 10 004 |  | Pressure | Pa, –1 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
| 3 02 070 |  | Wind data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 | Maximum wind gust speed | m s-1, 1 |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
|  |  | Temperature and humidity instrumentation |  |
| 3 01 130 | 0 03 002 | Generic type of humidity instrument | Code table, 0 |
|  | 0 03 003 | Configuration of sensors | Code table, 0 |
|  | 0 03 004 | Type of Shield or Screen | Code table, 0 |
|  | 0 03 005 | Horizontal Width of Screen or Shield (x) | m, 2 |
|  | 0 03 006 | Horizontal Depth of Screen or Shield (y) | m, 2 |
|  | 0 03 007 | Vertical Height of Screen or Shield (z) | m, 2 |
|  | 0 03 008 | Artificially Ventilated Screen or Shield | Code table, 0 |
|  | 0 03 009 | Degree of Forced Ventilation at time of reading | m-3 s-1, 1 |
|  | 0 33 003 | Quality of humidity measurement | Code table, 0 |
|  |  | Temperature and humidity data |  |
| 3 02 072 | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 12 101 | Temperature/Air-temperature (scale 2) | K, 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
| 0 07 032 |  | Height of sensor above local ground(6) | m, 2 |
| 0 08 010 |  | Surface qualifier | Code table, 0 |
| 0 12 120 |  | Ground temperature | K, 2 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 08 010 |  | Surface qualifier (set to missing to cancel the previous value) | Code table, 0 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  | Replicate 1 descriptor five times |  |
| 3 07 063 | 0 07 061 | Depth below land surface | m, 2 |
|  | 0 12 130 | Soil temperature (scale 2) | K, 2 |
| 0 07 061 |  | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 |  | Visibility data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 001 | Horizontal visibility | m, –1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 073 |  | Cloud data |  |
|  | 0 20 010 | Cloud cover (total) | %, 0 |
|  | 1 05 004 | Replicate 5 descriptors four times |  |
|  | 0 08 002 | Vertical significance | Code table, 0 |
|  | 0 20 011 | Cloud amount | Code table, 0 |
|  | 0 20 012 | Cloud type | Code table, 0 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 013 | Height of base of cloud | m, –1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 076 |  | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 | Type of precipitation | Flag table, 0 |
|  | 0 20 022 | Character of precipitation | Code table, 0 |
|  | 0 26 020 | Duration of precipitation(3) | Minute, 0 |
|  | 0 20 023 | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 | Obscuration | Flag table, 0 |
|  | 0 20 026 | Character of obscuration | Code table, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 13 155 |  | Intensity of precipitation | kgm-2s-1, 4 |
| 0 13 058 |  | Size of precipitation element | m, 4 |
|  |  | (end of the replicated sequence) |  |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  | Rate of ice accretion | Code table, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 |  | State of ground and snow depth measurement |  |
|  | 0 02 176 | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 | Total snow depth | m, 2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 079 |  | Precipitation measurement |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 02 175 | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 | Method of liquid water content measurement of Precipitation | Code table, 0 |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 13 011 | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 080 |  | Evaporation measurement |  |
|  | 0 02 185 | Method of evaporation measurement | Code table, 0 |
|  | 0 04 025 | Time period or displacement ( = - n minutes) | Minute, 0 |
|  | 0 13 033 | Evaporation /evapotranspiration | kg m-2, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 081 |  | Total sunshine data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 14 031 | Total sunshine | Minute, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 082 |  | Radiation data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 14 002 | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - n minutes) | Minute |
| 0 13 059 |  | Number of flashes | Numeric |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 |  | First order statistics of P, W, T, U data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 08 023 | First order statistics (= 9; best estimate of standard deviation) (4) | Code table, 0 |
|  | 0 10 004 | Pressure | Pa, –1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 12 101 | Temperature/air temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 08 023 | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  | Internal measurement status information (AWS) | Code table, 0 |

- ANNEX TO PARAGRAPH 3.2.8 [Validation]

Add new entries:

BUFR/CREX Table B

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F XX YYY |  | Unit | Scale | Ref. value | Data width (bits) | Units | Scale | Data width (char) |
| 0 01 114 | Encrypted ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 352 | CCITT IA5 | 0 | 44 |
| 0 03 014 | Type of marine hygrometer | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 03 015 | Exposure of marine thermometer / hygrometer | Code table | 0 | 0 | 4 | Code table | 0 | 2 |
| 0 03 013 | Type of marine thermometer | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 10 015 | Maximum height of deck cargo above summer load line | m | 0 | 0 | 6 | m | 0 | 2 |
| 0 10 016 | Departure of reference level (summer maximum load line) from actual sea level | m | 0 | -32 | 6 | m | 0 | 3 |
| 0 11 007 | Relative wind direction (in degrees off bow) | ° | 0 | 0 | 9 | ° | 0 | 3 |
| 0 11 008 | Relative wind speed | m s-1 | 1 | 0 | 12 | m s-1 | 1 | 4 |
| 0 25 185 | Encryption method | Code table | 0 | 0 | 8 | Code table | 0 | 3 |
| 0 25 186 | Encryption key version | CCITT IA5 | 0 | 0 | 96 | CCITT IA5 | 0 | 12 |

BUFR/CREX Table D

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
|  |  |  |  |  |  | (Encrypted ship's call sign and encryption method) |  |
| 3 | 01 | 018 | 0 | 01 | 114 | Encrypted ship or mobile land station identifier |  |
|  |  |  | 0 | 25 | 185 | Encryption method |  |
|  |  |  | 0 | 25 | 186 | Encryption key version |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
|  |  |  |  |  |  | (Ship “instantaneous” data) |  |
| 3 | 02 | 062 | 3 | 02 | 001 | Pressure and 3-hour pressure change |  |
|  |  |  | 3 | 02 | 093 | Extended ship temperature and humidity data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 053 | Ship visibility data |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 004 | General cloud information |  |
|  |  |  | 3 | 02 | 005 | Cloud layer |  |
|  |  |  | 0 | 08 | 002 | Vertical significance (surface observations) | Set to missing (cancel) |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 055 | Icing and ice |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 056 | Sea/water temperature |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 021 | Waves |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 024 | Wind and swell waves |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
|  |  |  |  |  |  | (Ship “period” data) |  |
| 3 | 02 | 063 | 3 | 02 | 038 | Present and past weather |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 040 | Precipitation measurement |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 034 | Precipitation past 24 hours |  |
|  |  |  | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 058 | Ship extreme temperature data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 064 | Ship wind data |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
|  |  |  |  |  |  | (Ship wind data) |  |
| 3 | 02 | 064 | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 0 | 02 | 002 | Type of instrumentation for wind measurement |  |
|  |  |  | 0 | 08 | 021 | Time significance | = 2 Time averaged |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 001 | Wind direction |  |
|  |  |  | 0 | 11 | 002 | Wind speed |  |
|  |  |  | 0 | 08 | 021 | Time significance | Set to missing (cancel) |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 0 | 04 | 025 | Time period or displacement |  |
|  |  |  | 0 | 11 | 043 | Maximum wind gust direction |  |
|  |  |  | 0 | 11 | 041 | Maximum wind gust speed |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
|  |  |  |  |  |  | (VOSClim data elements) |  |
| 3 | 02 | 092 | 0 | 01 | 012 | Direction of motion of moving observing platform | Ship’s heading |
|  |  |  | 0 | 01 | 012 | Direction of motion of moving observing platform | Ship’s course over ground |
|  |  |  | 0 | 01 | 013 | Speed of motion of moving observing platform | Ship’s speed over ground |
|  |  |  | 0 | 10 | 038 | Maximum height of deck cargo above summer load line |  |
|  |  |  | 0 | 10 | 039 | Departure of reference level (summer maximum load line) from actual sea level |  |
|  |  |  | 0 | 11 | 007 | Relative wind direction (in degrees off bow) |  |
|  |  |  | 0 | 11 | 008 | Relative wind speed |  |

| Table reference | Table references | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | X | YYY |  |  |
|  |  |  |  |  |  | (Extended ship temperature and humidity data) |  |
| 3 | 02 | 093 | 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  |  |  | 0 | 07 | 033 | Height of sensor above water surface |  |
|  |  |  | 0 | 03 | 013 | Type of marine thermometer |  |
|  |  |  | 0 | 03 | 015 | Exposure of marine thermometer/hygrometer |  |
|  |  |  | 0 | 12 | 101 | Temperature/air temperature |  |
|  |  |  | 0 | 02 | 039 | Method of wet-bulb temperature measurement |  |
|  |  |  | 0 | 03 | 014 | Type of marine hygrometer |  |
|  |  |  | 0 | 03 | 015 | Exposure of marine thermometer/hygrometer |  |
|  |  |  | 0 | 12 | 102 | Wet-bulb temperature |  |
|  |  |  | 0 | 12 | 103 | Dewpoint temperature |  |
|  |  |  | 0 | 13 | 003 | Relative humidity |  |
|  |  |  | 0 | 03 | 015 | Exposure of marine thermometer/hygrometer | Set to missing (cancel) |
|  |  |  | 0 | 03 | 013 | Type of marine thermometer | Set to missing (cancel) |
|  |  |  | 0 | 03 | 014 | Type of marine hygrometer | Set to missing (cancel) |

| Table reference | Table References | Element name | Element description |
| --- | --- | --- | --- |
| F | XX | YYY | F | XX | YYY |  |  |
|  |  |  |  |  |  | (Synoptic reports from sea stations suitable for VOS observation data) |  |
| 3 | 08 | 014 | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 01 | 018 | Encrypted ship’s call sign and encryption method |  |
|  |  |  | 3 | 01 | 093 | Ship identification, movement, date/time, horizontal and vertical coordinates |  |
|  |  |  | 3 | 02 | 062 | Ship “instantaneous” data |  |
|  |  |  | 3 | 02 | 063 | Ship “period” data |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 000 | Short delayed descriptor replication factor |  |
|  |  |  | 3 | 02 | 092 | VOSClim data elements |  |

Add new code tables:

0 03 013

Type of marine thermometer

| Code Figure | Meaning |
| --- | --- |
| 0 | Alcohol thermometer |
| 1 | Dry bulb mercury thermometer |
| 2 | Electric (resistance) thermometer |
| 3 – 7 | Reserved |

0 03 014

Type of marine hygrometer

| Code Figure | Meaning |
| --- | --- |
| 0 | Capacitance |
| 1 | Chilled mirror |
| 2 | Electric |
| 3 | Hair hygrometer |
| 4 | Hygristor |
| 5 | Psychrometer |
| 6 | Torsion |
| 7 | Other |
| 8 – 15 | Reserved |

0 03 015

Exposure of marine thermometer / hygrometer

| Code Figure | Meaning |
| --- | --- |
| 0 | Aspirated (Assmann type) |
| 1 | Screen (non-ventilated, i.e. natural ventilation) |
| 2 | Screen (ventilated, i.e. assisted ventilation) |
| 3 | Ship's screen (property of the ship) |
| 4 | Ship's sling (property of the ship) |
| 5 | Unscreened |
| 6 | Whirling or sling psychrometer |
| 7 – 15 | Reserved |

0 25 185

Encryption method

| Code Figure | Meaning |
| --- | --- |
| 0 | AES 256 |
| 1 – 254 | Reserved |
| 255 | Missing value |

- ANNEX TO PARAGRAPH 3.2.9 [Validation]

Add new entries:

BUFR/CREX Table B

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Units | Scale | Data width (characters) |
| 0 | 02 | 008 | Type of offshore platform | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Editorial note: this descriptor may be replaced by 0 03 001.

BUFR Table D

|  |  | (Sequence for platform identification, type, time and location of the observation report) |
| --- | --- | --- |
| 3 01 056 | 0 01 087 | WMO marine observing platform extended identifier | WMO number (extended 7 digit identifier) |
|  | 0 01 011 | Ship or mobile land station identifier | Call sign (where allocated) |
|  | 0 01 015 | Station or site name | Platform name |
|  | 0 02 008 | Type of offshore platform |  |
|  | 0 02 001 | Type of station |  |
|  | 3 01 011 | Year, month, day |  |
|  | 3 01 012 | Hour, minute |  |
|  | 3 01 021 | Latitude/longitude (high accuracy) |  |
|  | 0 07 030 | Height of station ground above mean sea level | Height of station platform above mean sea level |
|  | 0 07 031 | Height of barometer above mean sea level |  |

|  |  | (Sequence for reporting observations from offshore platforms) |
| --- | --- | --- |
| 3 08 017 | 3 01 056 | Sequence for platform identification, type, time and location of the observation report |  |
|  | 3 02 001 | Pressure and 3-hour pressure change |  |
|  | 3 02 052 | Ship temperature and humidity data |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 056 | Sea/water temperature | Optional |
|  | 3 02 064 | Ship wind data (see Note) |  |
|  | 3 02 053 | Ship visibility data |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 004 | General cloud information | Optional |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 005 | Cloud layer | Optional |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 038 | Present and past weather | Optional |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 06 039 | Sequence for representation of basic wave measurements | Optional |

Note: Sequence 3 02 064 has previously been approved for validation and is also used in the sequence for synoptic reports from sea stations suitable for VOS data.

Add new code tables:

0 02 008

Type of offshore platform

| Code figure | Meaning |
| --- | --- |
| 0 | Fixed platform |
| 1 | Mobile offshore drill ship |
| 2 | Jack-up rig |
| 3 | Semi-submersible platform |
| 4 | FPSO (floating production storage and offloading unit) |
| 5 | Light vessel |
| 6 – 14 | Reserved |
| 15 | Missing value (or not known) ["or not known" to be separated from missing value] |

BUFR Template for reporting observations from offshore platforms

Items in red are new descriptors/sequences suggested for review and incorporation in the WMO Manual on Codes.

Template for reporting observations from offshore platforms

| 3 08 017 | 3 01 056 | Sequence for representation of platform identification type, time and location of the observation report |
| --- | --- | --- |
|  | 3 02 001 | Sequence for pressure data |
|  | 3 02 052 | Sequence for temperature and humidity data |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 056 | Sequence for sea temperature data (optional) |
|  | 3 02 064 | Sequence for wind data |
|  | 3 02 053 | Sequence for visibility data |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 004 | Sequence for cloud information (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 005 | Sequence for cloud layer information (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 02 038 | Sequence for present and past weather (optional) |
|  | 1 01 000 | Replicate next sequence |
|  | 0 31 000 | Short delayed replication factor |
|  | 3 06 039 | Sequence for representation of basic wave measurements (optional) |

Sequences for platform identification, pressure, temperature, wind and visibility are mandatory. Sequences for sea temperature, cloud data, present/past weather and waves are optional and used only when the relevant data are measured or reported.

Description of sequences

Sequence for platform identification, type, time and location of the observation report

| 3 01 056 |  | 0 01 087 | WMO number (extended 7 digit identifier) |
| --- | --- | --- | --- |
|  |  | 0 01 011 | Call sign (where allocated) |
|  |  | 0 01 015 | Platform name |
|  |  | 0 02 008 | Type of offshore platform* |
|  |  | 0 02 001 | Type of station |
|  | 3 01 011 | 0 04 001 | Year |
|  |  | 0 04 002 | Month |
|  |  | 0 04 003 | Day |
|  | 3 01 012 | 0 04 004 | Hour |
|  |  | 0 04 005 | Minute |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) |
|  |  | 0 06 001 | Longitude (high accuracy) |
|  |  | 0 07 030 | Height of station platform above mean sea level |
|  |  | 0 07 031 | Height of barometer above mean sea level |

* suggest new code table to define platform type

Sequence for pressure data

| 3 02 001 |  | 0 10 004 | Pressure (as measured) |
| --- | --- | --- | --- |
|  |  | 0 10 051 | Pressure corrected to mean sea level |
|  |  | 0 10 061 | 3-hour pressure change* |
|  |  | 0 13 003 | Characteristic of pressure tendency* |

* would normally be omitted for hourly (or more frequent) reports

Sequence for temperature and humidity data

| 3 02 052 |  | 0 07 032 | Height of sensor above marine deck platform |
| --- | --- | --- | --- |
|  |  | 0 07 033 | Height of sensor above water surface |
|  |  | 0 12 101 | Temperature (dry bulb) |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement* |
|  |  | 0 12 102 | Wet bulb temperature* |
|  |  | 0 12 103 | Dew point temperature** |
|  |  | 0 13 003 | Relative humidity*** |

* for manual observations only otherwise code as missing

** this will normally be calculated

*** include only when measured otherwise code as missing

Sequence for sea temperature data

| 3 02 056 |  | 0 02 038 | Method of sea temperature measurement |
| --- | --- | --- | --- |
|  |  | 0 07 063 | Depth below sea water surface of sensor |
|  |  | 0 22 043 | Sea/water temperature |
|  |  | 0 07 063 | Depth below sea water surface of sensor (set to missing to cancel) |

Sequence for wind data*

| 3 02 064 |  | 0 07 032 | Height of sensor above marine deck platform |
| --- | --- | --- | --- |
|  |  | 0 07 033 | Height of sensor above water surface |
|  |  | 0 02 002 | Type of instrumentation for wind measurement |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |
|  |  | 0 11 001 | Wind direction |
|  |  | 0 11 002 | Wind speed |
|  |  | 0 08 021 | Time significance (= missing value) |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |
|  |  | 0 31 001 | Delayed descriptor replication factor (0 if no gust data, 1 otherwise) |
|  |  | 0 04 025 | Time period in minutes |
|  |  | 0 11 043 | Maximum wind gust direction |
|  |  | 0 11 041 | Maximum wind gust speed |

* sequence under validation

Sequence for visibility data

| 3 02 053 |  | 0 07 032 | Height of sensor above marine deck platform |
| --- | --- | --- | --- |
|  |  | 0 07 033 | Height of sensor above water surface |
|  |  | 0 20 001 | Horizontal visibility |

Sequences for cloud data

| 3 02 004 |  | 0 20 010 | Cloud cover (total) |
| --- | --- | --- | --- |
|  |  | 0 08 002 | Vertical significance |
|  |  | 0 20 011 | Cloud amount |
|  |  | 0 20 013 | Height of base of cloud |
|  |  | 0 20 012 | Cloud type (low clouds) |
|  |  | 0 20 012 | Cloud type (middle clouds) |
|  |  | 0 20 012 | Cloud type (high clouds) |

| 3 02 005 |  | 0 08 002 | Vertical significance |
| --- | --- | --- | --- |
|  |  | 0 20 011 | Cloud amount |
|  |  | 0 20 012 | Cloud type |
|  |  | 0 20 013 | Height of base of cloud |

Sequence for present and past weather data

| 3 02 038 |  | 0 20 003 | Present weather |
| --- | --- | --- | --- |
|  |  | 0 04 024 | Time period |
|  |  | 0 20 004 | Past weather (1) |
|  |  | 0 20 005 | Past weather (2) |

Sequence for basic wave data

| 3 06 039 |  | 0 22 078 | Duration of wave record |
| --- | --- | --- | --- |
|  |  | 0 22 070 | Significant wave height |
|  |  | 0 22 073 | Maximum wave height |
|  |  | 0 22 074 | Average wave period |
|  |  | 0 22 071 | Spectral peak wave period |
|  |  | 0 22 076 | Direction from which dominant waves are coming |
|  |  | 0 22 077 | Directional spread of dominant waves |

New code table 0 02 008 for platform type

0 – fixed platform

1 – mobile offshore drill ship

2 – jack-up rig

3 – semi-submersible platform

4 – FPSO (floating production storage and offloading unit)

5 – light vessel

6-14 - reserved

15 – missing value (or not known).

- ANNEX TO PARAGRAPH 3.2.10 [Validation]

Add new table B class

| F | X | Class | Comments |
| --- | --- | --- | --- |
| 0 | 41 | Marine bio-geochemical data |  |

Add new table B entries

| Table reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F | XX | YYY |  | Unit | Scale | Ref. value | Data width (bits) | Units | Scale | Data width (characters) |
| 0 | 08 | 034 | Type of temperature/ salinity measurement | Code table | 0 | 0 | 4 | Code table | 0 | 2 |

Add new table D entries

3 06 017

Near surface depth (pressure) and temperature profile from floats

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
|  |  |  |  |  |  | (Sub-surface temperature profile (high accuracy/precision) with quality flags) |  |
| 3 06 017 | 0 | 02 | 032 | Indicator for digitization | = 0 Fixed sensor depths |
|  | 0 | 08 | 034 | Type of temperature/salinity measurement |  |
|  | 1 | 06 | 000 | Delayed replication of 6 descriptors |  |
|  | 0 | 31 | 001 | Delayed descriptor replication factor | Number of depths |
|  | 0 | 07 | 065 | Water pressure | In Pa |
|  | 0 | 08 | 080 | Qualifier for GTSPP quality flag |  |
|  | 0 | 33 | 050 | Global GTSPP quality flag |  |
|  | 0 | 22 | 043 | Sea/water temperature | In K to 2 decimal places |
|  | 0 | 08 | 080 | Qualifier for GTSPP quality flag |  |
|  | 0 | 33 | 050 | Global GTSPP quality flag |  |
|  | 0 | 08 | 034 | Type of temperature/salinity measurement | Set to missing (cancel) |

3 06 018

Near surface depth (pressure), temperature and salinity profile from floats

| Table Reference | Table References | Element Name |  |
| --- | --- | --- | --- |
| F | X | Y |  |  |  |
|  |  |  |  |  |  | (Sub-surface temperature profile (high accuracy/precision) with quality flags) |  |
| 3 06 018 | 0 | 02 | 032 | Indicator for digitization | = 0 Fixed sensor depths |
|  | 0 | 08 | 034 | Type of temperature/salinity measurement |  |
|  | 1 | 09 | 000 | Delayed replication of 9 descriptors |  |
|  | 0 | 31 | 001 | Delayed descriptor replication factor | Number of depths |
|  | 0 | 07 | 065 | Water pressure | In Pa |
|  | 0 | 08 | 080 | Qualifier for GTSPP quality flag |  |
|  | 0 | 33 | 050 | Global GTSPP quality flag |  |
|  | 0 | 22 | 043 | Sea/water temperature | In K to 2 decimal places |
|  | 0 | 08 | 080 | Qualifier for GTSPP quality flag |  |
|  | 0 | 33 | 050 | Global GTSPP quality flag |  |
|  | 0 | 22 | 064 | Salinity |  |
|  | 0 | 08 | 080 | Qualifier for GTSPP quality flag |  |
|  | 0 | 33 | 050 | Global GTSPP quality flag |  |
|  | 0 | 08 | 034 | Type of temperature/salinity measurement | Set to missing (cancel) |

Add new code tables

0 08 034

Temperature / salinity measurement qualifier

| Code figure | Meaning |
| --- | --- |
| 0 | Un-pumped float temperature and salinity data |
| 1 | Auxiliary STS sensor data |
| 2 – 14 | Reserved |
| 15 | Missing value |

- ANNEX TO PARAGRAPH 4.1

Implementation of amendments during the intersessional period, including those approved the period

1.	Adoption between CBS sessions 2013 (implemented on 14 November 2013)

2.	Fast-track 2013-2 (implemented on 14 November 2013)

3.	Fast-track 2014-1 (scheduled for 7 May 2014)

4.	Adoption between CBS sessions 2014 (scheduled for 5 November 2014)

Status of proposals on amendments to GRIB edition 2

1.	IPET-DRMM-I and later

| Para. | Title | Implementation date/validation |
| --- | --- | --- |
| 2.1.1 | Reporting quality information in GRIB2 | Ongoing |
| 2.2.1 | GRIB2 new compression method – CCSDS libaec | Ongoing |
| 2.2.3 | Distribution functions in GRIB Edition 2 | Superseded by 2.2.4 of this meeting |
| 2.2.5 | Proposed amendments to GRIB2 Code tables 4.2, 4.3 and 4.10 (amendments other than Code table 4.10 were implemented by FT2014-1) | Ongoing (to be closed along with 2.1.1 above) |

2.	IPET-DRC-IV and before IPET-DRMM-I

| Para. | Title | Implementation date/validation |
| --- | --- | --- |
| 2.2.9 | GRIB template for 4-D Trajectory grid definition | Ongoing |
| Email | GRIB template for analysis or forecast of wave parameters at the sea surface, Annex 1, Annex 2 | Abandoned |

3.	The IPET-DRC-III and before IPET-DRC-IV

| Para. | Title | Implementation date / validation |
| --- | --- | --- |
| 2.3.2 | Arakawa E grids in GRIB2 | Superseded by 2.1.1 of this meeting |
| 2.3.5 | GRIB template for rotated tilted Mercator projection | Original by France - to be confirmed |
| 2.3.12 | Space Weather in GRIB2 | Ongoing |

4.	The IPET-DRC-II and before IPET-DRC-III

| Para. | Title | Implementation date / validation |
| --- | --- | --- |
| 2.3.1/2.3.2 (combined) | Encoding wave spectra in GRIB Edition 2 Waves parameters (amendments other than 46-48 were implemented) | Ongoing |

Status of proposals on amendments to BUFR and CREX

I.	The IPET-DRMM-I and later

| Paragraph | Title | Implementation date / validation |
| --- | --- | --- |
| 3.1.2 | JCOMM Proposal for the encryption of Ship’s callsigns within BUFR reports | Superseded by 3.2.8 |
| 3.2.1 | Additions to the BUFR template for n-minute AWS data (3 07 092) | Ongoing |
| 3.2.2 | Proposal for a BUFR template for radar wind profiler | Ongoing |
| 3.2.4 | Satellite-derived winds in BUFR | Ongoing |
| 3.2.5 | Daily climate observations via monthly CLIMAT messages | Superseded by 3.2.3 of this meeting |

II.	The IPET-DRC-IV and before IPET-DRMM-I

| Paragraph | Title | Implementation date / validation |
| --- | --- | --- |
| 3.2.7 | Sequence 3 02 067 | Ongoing |
| 3.2.11 | A BUFR Sequence to append data for national use to Canadian SYNOP reports | Ongoing |
| 3.2.12 | New BUFR/CREX entries for dual polarization radar data * (REVISED) | Ongoing |

*   The proposal has been modified as follows.

| F X Y | Element name | BUFR | CREX |
| --- | --- | --- | --- |
|  |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 33 029 | Correlation coefficient | Numeric | 2 | -100 | 8 | Numeric | 2 | 3 |
| 0 21 028 | Specific differential phase | deg/m | 5 | -200 | 11 | deg/m | 2 | 4 |

III.	The IPET-DRC-II and before IPET-DRC-III

| Paragraph | Title | Implementation date / validation |
| --- | --- | --- |
| 3.3.12 | Examples of usage TM 307093 for representation of nominal values | Ongoing |

IV.	The IPET-DRC-I and before IPET-DRC-II

| Paragraph | Title | Implementation date / validation |
| --- | --- | --- |
| 3.3.2 | Update from JCOMM on developments for BUFR templates: New XBT template and queries about a revised VOS template | Ongoing |

V.	Status of proposals at the Joint meeting of CT-MTDCF and ET-DRC

| Paragraph | Title | Implementation date / validation |
| --- | --- | --- |
| 3.1.2 | Template for synoptic reports from sea stations suitable for ship observation data from VOS stations | Superseded by 3.2.8 of this meeting |
| 3.1.4 | IEEE representation (for BUFR Edition 5) | BUFR edition 5 |
| 3.1.8.2 | BUFR/CREX Templates for Tide Elevation Data | To be implemented on 7 May 2014 |
| 3.1.15 | Template for the wave observations from different platforms suitable for WAVEOB data (table references shall be changed) | Ongoing (almost validated) |

- ANNEX TO PARAGRAPH 4.2.1 [FT2014-2/pre-operational/valid from 5 November 2014]

For originating center #7 (U.S. National Weather Service, NCEP)

  - Rename subcenter #5 from “Hydrometeorological Prediction Center” to “Weather Prediction Center”

For originating center #160 (U.S. NOAA/NESDIS)

  - Add subcenter #1 as “National Climatic Data Center”

  - Add subcenter #2 as “National Geophysical Data Center”

  - Add subcenter #3 as “National Oceanographic Data Center”

  - Add subcenter #4 as “Center for Satellite Applications and Research (STAR)”

  - Add subcenter #5 as “Joint Polar Satellite System”

- ANNEX TO PARAGRAPH 5.1 [CBS session/Rec. 2.3(1)/3 (CBS-Ext.(2014))/4 November 2015]

Amend Regulations B/C 30.4 and 32.4:

B/C 30.4	Data required by Regional or national reporting practices

B/C 30.4.1	Data required by regional or national reporting practices

No additional data are currently required by regional or national reporting practices for CLIMAT data in Manual on Codes, WMO-No. 306, Volume II.

B/C 30.4.2	Reference period for the data of the month

If the regional or national reporting practices require reporting monthly data (with the exception of precipitation data) for one-month period different from the local time month as recommended in B/C 30.2.2.1, short time displacement (0 04 074) shall be adjusted accordingly.

B/C 30.4.3	Date/time (of beginning of the period for monthly precipitation data)

If the regional or national reporting practices require reporting monthly precipitation data for period different from the period recommended in Note (1) to B/C 30.2.6.1, then hour (0 04 004) shall be adjusted accordingly. This regulation does not apply if the beginning of the period for monthly precipitation data starts on the last day of the previous month in UTC.

B/C 32.4	Data required by Regional or national reporting practices

B/C 32.4.1	Data required by regional or national reporting practices

No additional data are currently required by regional or national reporting practices for CLIMAT SHIP data in Manual on Codes, WMO-No. 306, Volume II.

B/C 32.4.2	Reference period for the data of the month

If the regional or national reporting practices require reporting monthly data (with the exception of precipitation data) for one-month period different from the local time month as recommended in B/C 32.2.2.1, short time displacement (0 04 074) shall be adjusted accordingly.

B/C 32.4.3	Date/time (of beginning of the one-month period for precipitation data)

If the regional or national reporting practices require reporting monthly precipitation data for one-month period different from the period recommended in Note (1) to B/C 32.2.3.1, then hour (0 04 004) shall be adjusted accordingly. This regulation does not apply if the beginning of the period for monthly precipitation data starts on the last day of the previous month in UTC.

Amend entries of BUFR Table D:

In 3 07 071, 3 07 072, 3 08 011 and 3 08 012, modify LST to LT.

Amend templates of B/C Regulations:

In TM3 07 073 and TM3 08 013, modify LST to LT.

In the Notes 1 and 2 to TM3 07 073 and TM3 08 013,

(1)	The time identification refers to the beginning of the one-month period. Except for precipitation measurements, the one-month period is recommended to correspond to the local standard time (LT) month. [7]

(2)	In case of precipitation measurements, the one-month period begins at 06 UTC on the first day of the month and ends at 06 UTC on the first day of the following month. [5]

Amend B/C Regulations:

In B/C 30.2.2.1 and B/C 32.2.2.1,

Monthly data (with the exception of precipitation data) are recommended to be reported for one-month period, corresponding to the local standard time (LT) month [Handbook on CLIMAT and CLIMAT TEMP Reporting (WMO/TD-No.1188)].  In that case, short time displacement (0 04 074) shall specify the difference between UTC and LT (set to non-positive values in the eastern hemisphere, non-negative values in the western hemisphere).

Time period (0 04 023) represents the number of days in the month for which the data are reported, and shall be expressed as a positive value in days.

In Note 1 to B/C 30.2.6.1 and B/C 32.2.3.1,

Day (0 04 003) and hour (0 04 004) of the beginning of the one-month period for monthly precipitation data are reported. Day (0 04 003) shall be set to 1 and hour (0 04 004) shall be set to 6.

Notes:

(1)	In case of precipitation measurements, a month begins at 0600 hours UTC on the first day of the month and ends at 0600 hours UTC on the first day of the following month [Handbook on CLIMAT and CLIMAT TEMP Reporting (WMO/TD-No.1188)].

In B/C 30.3.1.2 and B/C 32.3.1.2,

The one-month period for which the normal values are reported shall be specified by month (0 04 002), day (0 04 003) being set to 1, hour (0 04 004) being set to 0, short time displacement (0 04 074) being set to (UTC – LT) and time period (0 04 022) being set to 1, i.e. 1 month.  Short time displacement (0 04 074) shall be set to non-positive values in the eastern hemisphere, non-negative values in the western hemisphere.

In B/C 30.2.5.3,

B/C 30.2.5.3	Occurrence of the lowest daily mean temperature

………..

Lowest daily mean temperature (0 12 153) shall be reported in degrees Kelvin (with precision in hundredths of a degree Kelvin); if produced in CREX, in degrees Celsius (with precision in hundredths of a degree Celsius).

- ANNEX TO PARAGRAPH 6.1 [further development]

###### FM 15–XV METAR	Aerodrome routine meteorological report (with or without
	trend forecast

###### FM 16–XV SPECI	Aerodrome special meteorological report (with or without
	trend forecast

CODE  F ORM :

METAR	KT

or	COR	CCCC	YYGGggZ	NIL	AUTO	dddffGfmfm	or	dndndnVdxdxdx

SPECI	MPS

NsNsNshshshs

or

VVhshshs

or

VVVV	VNVNVNVNDv	RDRDR/VRVRVRVRi	w´w´	NSC

or	or

CAVOK	NCD

WS RDRDR	(WTsTs/SS´)

T´T´/T´dT´d	QPHPHPHPH	REw´w´	or	or	(RDRDR/ERCReReRBRBR)

WS ALL RWY	(WTsTs/HHsHsHs)

NsNsNshshshs

KT	VVVV	w´w´	or

(TTTTT	TTGGgg	dddffGfmfm	or	or	or	VVhshshs

or		MPS	CAVOK	NSW	or

NOSIG)				NSC

(RMK . . . . . . . . . . )

…

RE GUL AT I ONS :

…

NsNsNshshshs

or

VVhshshs

15.9	Group	or

NSC

or

NCD

15.9.1	Cloud amount and cloud height NsNsNshshshs

…

15.9.1.6	When cumulonimbus clouds or towering cumulus clouds are detected by the automatic observing 	system and the cloud amount and/or the height of cloud base cannot be observed, the cloud 	amount and/or the height of cloud base elements should each be replaced by ///.

…

15.13	Supplementary information – groups

WS RDRDR	(W TsTs/S S´)

REw´w´	or	or	(RDRDR/ERCReReRBRBR)

WS ALL RWY	(W TsTs/H HsHsHs)

15.13.1	For international dissemination, the section on supplementary information shall be used only to report recent weather phenomena of operational significance, available information on wind shear in the  lower layers and, subject to regional air navigation agreement, sea-surface temperature and state of the sea or significant wave height, and also subject to regional air navigation agreement, the state of the runway.

- ANNEX TO PARAGRAPH 7.1

# Figure 1: Surface BUFR reports for RBSN stations captured by the SMM exercise during 1-15 October 2013 shown as a percentage of the expected number of reports. Both TDCF (Large chart) and TAC (small chart) are shown.

# Figure 2: Upper air BUFR reports for RBSN stations captured by the SMM exercise during 1-15 October 2013 shown as a percentage of the expected number of reports. Both TDCF (Large chart) and TAC (small chart) are shown.

# Figure 3: Climate BUFR reports for RBSN stations captured by the SMM exercise during 1-15 October 2013 shown as a percentage of the expected number of reports. Both TDCF (Large chart) and TAC (small chart) are shown.

# Table 1: Average by country of the number of surface reports from RBSN stations recorded in BUFR messages during the SMM of 1-15 October 2013. The number of reports expected from each station is 60.

| RA | Country/Territory | Count of STN | Average Number |
| --- | --- | --- | --- |
| 1 | Algeria | 49 | 52 |
|  | Angola | 14 | 0 |
|  | Benin | 6 | 0 |
|  | Botswana | 12 | 0 |
|  | Bouvet Island | 1 | 0 |
|  | Burkina Faso | 9 | 0 |
|  | Burundi | 1 | 0 |
|  | Cameroon | 14 | 0 |
|  | Cape Verde | 3 | 0 |
|  | Central African Republic | 13 | 0 |
|  | Chad | 11 | 0 |
|  | Comoros | 2 | 30 |
|  | Congo | 8 | 0 |
|  | Cote D'Ivoire | 14 | 0 |
|  | Democratic Republic of the Congo | 29 | 0 |
|  | Djibouti | 1 | 0 |
|  | Egypt | 28 | 0 |
|  | Equatorial Guinea | 2 | 0 |
|  | Eritrea | 2 | 0 |
|  | Ethiopia | 16 | 0 |
|  | Gabon | 9 | 0 |
|  | Gambia | 2 | 0 |
|  | Ghana | 13 | 0 |
|  | Guinea | 12 | 0 |
|  | Guinea-Bissau | 1 | 0 |
|  | Kenya | 18 | 0 |
|  | Lesotho | 3 | 0 |
|  | Liberia | 1 | 0 |
|  | Libyan Arab Jamahiriya | 26 | 0 |
|  | Madagascar | 26 | 0 |
|  | Madeira | 3 | 60 |
|  | Malawi | 2 | 1 |
|  | Mali | 17 | 0 |
|  | Mauritania | 13 | 0 |
|  | Mauritius | 6 | 0 |
|  | Morocco | 24 | 0 |
|  | Mozambique | 15 | 0 |
|  | Namibia | 15 | 0 |
|  | Niger | 14 | 0 |
|  | Nigeria | 25 | 0 |
|  | Ocean Islands | 5 | 24 |
|  | Ocean islands between 0 ° and 30 ° | 5 | 56 |
|  | Ocean islands between 30 ° and 60 ° | 3 | 40 |
|  | Rwanda | 1 | 0 |
|  | Senegal | 12 | 0 |
|  | Seychelles | 3 | 19 |
|  | Sierra Leone | 1 | 0 |
|  | Somalia | 14 | 0 |
|  | South Africa | 87 | 37 |
|  | Spain (Canary Islands) | 8 | 40 |
|  | Spain (Ceuta and Melilla) | 1 | 45 |
|  | Sudan | 28 | 0 |
|  | Swaziland | 1 | 0 |
|  | Togo | 5 | 0 |
|  | Tunisia | 19 | 24 |
|  | Uganda | 10 | 0 |
|  | United Republic of Tanzania | 16 | 0 |
|  | Western Sahara | 2 | 0 |
|  | Zambia | 26 | 0 |
|  | Zimbabwe | 17 | 0 |
| 1 Total |  | 744 | 10 |
| 2 | Afghanistan, Islamic State of | 13 | 0 |
|  | Bahrain | 7 | 4 |
|  | Bangladesh | 11 | 21 |
|  | Cambodia | 8 | 0 |
|  | China | 219 | 54 |
|  | Democratic People's Republic of Korea | 27 | 59 |
|  | Hong Kong, China | 1 | 60 |
|  | India | 82 | 59 |
|  | Iran, Islamic Republic of | 77 | 0 |
|  | Iraq | 11 | 0 |
|  | Japan | 52 | 60 |
|  | Kazakhstan (In Asia) | 62 | 0 |
|  | Kuwait | 2 | 15 |
|  | Kyrgyzstan | 7 | 0 |
|  | Lao People's Democratic Republic | 14 | 0 |
|  | Macao, China | 1 | 57 |
|  | Maldives | 5 | 53 |
|  | Mongolia | 35 | 58 |
|  | Myanmar | 27 | 0 |
|  | Nepal | 15 | 0 |
|  | Oman | 23 | 12 |
|  | Pakistan | 54 | 53 |
|  | Qatar | 1 | 33 |
|  | Republic of Korea | 41 | 55 |
|  | Russian Federation (In Asia) | 324 | 58 |
|  | Saudi Arabia | 35 | 43 |
|  | Sri Lanka | 9 | 0 |
|  | Tajikistan | 14 | 0 |
|  | Thailand | 87 | 0 |
|  | Turkmenistan | 20 | 0 |
|  | United Arab Emirates | 5 | 40 |
|  | Uzbekistan | 19 | 0 |
|  | Viet Nam | 25 | 0 |
|  | Yemen | 22 | 7 |
| 2 Total |  | 1355 | 37 |
| 3 | Argentina | 59 | 0 |
|  | Bolivia | 35 | 25 |
|  | Brazil | 159 | 40 |
|  | Chile | 22 | 3 |
|  | Colombia | 24 | 39 |
|  | Ecuador | 13 | 10 |
|  | French Guiana | 4 | 60 |
|  | Guyana | 6 | 0 |
|  | Islands (88: 800 - 998) | 2 | 60 |
|  | Paraguay | 19 | 41 |
|  | Peru | 29 | 30 |
|  | Suriname | 7 | 19 |
|  | Uruguay | 6 | 36 |
|  | Venezuela | 22 | 0 |
| 3 Total |  | 407 | 26 |
| 4 | Antigua and Barbuda | 1 | 0 |
|  | Bahamas | 12 | 0 |
|  | Barbados | 1 | 0 |
|  | Belize | 2 | 0 |
|  | Bermuda | 1 | 60 |
|  | Canada | 172 | 0 |
|  | Cayman Islands | 1 | 0 |
|  | Clipperton | 1 | 0 |
|  | Colombia (San Andres and Providencia Islands) | 2 | 47 |
|  | Costa Rica | 4 | 0 |
|  | Cuba | 20 | 0 |
|  | Dominica | 2 | 0 |
|  | Dominican Republic | 6 | 0 |
|  | El Salvador | 8 | 0 |
|  | Grenada | 1 | 0 |
|  | Guadeloupe, St Martin, St Barthelemy (and other French Islands in the vicinity) | 3 | 0 |
|  | Guatemala | 9 | 0 |
|  | Haiti | 2 | 0 |
|  | Honduras | 14 | 0 |
|  | Jamaica | 2 | 0 |
|  | Martinique | 2 | 30 |
|  | Mexico | 50 | 3 |
|  | Netherlands Antilles and Aruba | 5 | 0 |
|  | Nicaragua | 7 | 0 |
|  | Panama | 3 | 0 |
|  | Puerto Rico and US Possessions in the Caribbean area | 2 | 57 |
|  | RA-IV automatic marine stations | 27 | 0 |
|  | Saint Lucia | 2 | 0 |
|  | St. Pierre and Miquelon | 1 | 0 |
|  | Trinidad and Tobago | 2 | 0 |
|  | United States of America | 180 | 56 |
|  | United States of America (Alaska) | 19 | 49 |
|  | Venezuela (Isla De Aves) | 1 | 0 |
| 4 Total |  | 565 | 20 |
| 5 | Australia | 129 | 48 |
|  | Brunei Darussalam | 1 | 0 |
|  | Cook Islands | 7 | 15 |
|  | Detached Islands | 3 | 20 |
|  | East Timor | 2 | 0 |
|  | Fiji | 12 | 47 |
|  | French Polynesia (Austral Islands) | 2 | 60 |
|  | French Polynesia (Marquesas Islands) | 1 | 60 |
|  | French Polynesia (Society Islands) | 2 | 60 |
|  | French Polynesia (Tuamotu And Gambier Islands) | 4 | 55 |
|  | Indonesia | 60 | 56 |
|  | Islands in the Pacific Ocean North of the Equator | 51 | 16 |
|  | Kiribati | 2 | 0 |
|  | Malaysia | 14 | 60 |
|  | Nauru | 1 | 0 |
|  | New Caledonia | 6 | 30 |
|  | New Zealand | 29 | 57 |
|  | Niue | 1 | 15 |
|  | Papua New Guinea | 11 | 15 |
|  | Philippines | 27 | 57 |
|  | Phoenix Islands | 1 | 0 |
|  | Samoa And American Samoa | 12 | 5 |
|  | Singapore | 1 | 60 |
|  | Solomon Islands | 5 | 49 |
|  | Tokelau (and Swains Is.) | 1 | 0 |
|  | Tonga | 5 | 0 |
|  | Tuvalu | 4 | 0 |
|  | Vanuatu | 6 | 0 |
| 5 Total |  | 400 | 41 |
| 6 | Armenia | 3 | 0 |
|  | Austria | 7 | 59 |
|  | Azerbaijan | 7 | 0 |
|  | Belarus | 10 | 54 |
|  | Belgium | 3 | 0 |
|  | Bosnia and Herzegovina | 4 | 56 |
|  | Bulgaria | 9 | 0 |
|  | Croatia | 7 | 54 |
|  | Cyprus | 2 | 57 |
|  | Czech Republic | 7 | 60 |
|  | Denmark and Faroe Islands | 7 | 57 |
|  | Estonia | 7 | 59 |
|  | Finland | 22 | 54 |
|  | France | 44 | 35 |
|  | The Former Yugoslav Republic of Macedonia | 3 | 0 |
|  | Georgia | 11 | 0 |
|  | Germany | 28 | 58 |
|  | Gibraltar | 1 | 60 |
|  | Greece | 22 | 53 |
|  | Greenland | 30 | 33 |
|  | Hungary | 7 | 59 |
|  | Iceland | 10 | 0 |
|  | Ireland | 9 | 53 |
|  | Israel | 4 | 60 |
|  | Italy | 48 | 58 |
|  | Jordan | 4 | 0 |
|  | Kazakhstan | 3 | 0 |
|  | Latvia | 6 | 0 |
|  | Lebanon | 2 | 0 |
|  | Lithuania | 7 | 60 |
|  | Luxembourg | 1 | 57 |
|  | Malta | 1 | 0 |
|  | Montenegro | 6 | 35 |
|  | Netherlands | 9 | 60 |
|  | Norway | 40 | 56 |
|  | Poland | 22 | 60 |
|  | Portugal | 16 | 53 |
|  | Republic of Moldova | 1 | 0 |
|  | Romania | 23 | 60 |
|  | Russian Federation (In Europe) | 131 | 58 |
|  | Serbia | 28 | 55 |
|  | Slovakia | 4 | 60 |
|  | Slovenia | 2 | 60 |
|  | Spain | 33 | 55 |
|  | Sweden | 44 | 60 |
|  | Switzerland and Liechtenstein | 7 | 17 |
|  | Syria | 9 | 12 |
|  | Turkey | 58 | 55 |
|  | Ukraine | 36 | 0 |
|  | United Kingdom of Great Britain and Northern Ireland | 30 | 57 |
| 6 Total |  | 835 | 47 |
| 7 | Stations operated by Argentina | 6 | 0 |
|  | Stations operated by Australia | 18 | 10 |
|  | Stations operated by Brazil | 1 | 0 |
|  | Stations operated by Chile | 2 | 6 |
|  | Stations operated by China | 2 | 30 |
|  | Stations operated by Finland | 1 | 0 |
|  | Stations operated by France | 1 | 60 |
|  | Stations operated by Germany | 1 | 60 |
|  | Stations operated by India | 1 | 0 |
|  | Stations operated by Italy | 7 | 8 |
|  | Stations operated by Japan | 1 | 60 |
|  | Stations operated by Netherlands | 3 | 0 |
|  | Stations operated by Norway | 1 | 60 |
|  | Stations operated by South Africa | 1 | 60 |
|  | Stations operated by Spain | 1 | 0 |
|  | Stations operated by the Republic of Korea | 1 | 0 |
|  | Stations operated by the Russian Federation | 8 | 38 |
|  | Stations operated by the United Kingdom | 4 | 42 |
|  | Stations operated by the United States of America | 4 | 30 |
|  | Stations operated by the USA (University of Wisconsin) | 28 | 26 |
|  | Stations operated by Ukraine | 1 | 60 |
|  | Stations operated by Uruguay | 1 | 0 |
| 7 Total |  | 94 | 21 |
| Grand Total | 4400 | 31 |

# Table 2: Average by country of the number of upper air reports from RBSN stations recorded in BUFR messages during the SMM of 1-15 October 2013. The number of reports expected from each station is 30.

| RA | Country/Territory | Count of STN | Average Number |
| --- | --- | --- | --- |
| 1 | Algeria | 5 | 23 |
|  | Angola | 2 | 0 |
|  | Botswana | 4 | 0 |
|  | Burkina Faso | 1 | 0 |
|  | Cameroon | 2 | 0 |
|  | Cape Verde | 1 | 0 |
|  | Central African Republic | 1 | 0 |
|  | Chad | 2 | 0 |
|  | Congo | 2 | 0 |
|  | Cote D'ivoire | 1 | 0 |
|  | Democratic Republic of the Congo | 3 | 0 |
|  | Egypt | 6 | 0 |
|  | Eritrea | 1 | 0 |
|  | Ethiopia | 2 | 0 |
|  | Ghana | 2 | 0 |
|  | Guinea | 1 | 0 |
|  | Kenya | 1 | 0 |
|  | Libya | 4 | 0 |
|  | Madagascar | 2 | 0 |
|  | Madeira | 1 | 0 |
|  | Malawi | 1 | 0 |
|  | Mali | 2 | 0 |
|  | Mauritania | 1 | 0 |
|  | Mauritius | 1 | 0 |
|  | Morocco | 2 | 0 |
|  | Mozambique | 3 | 0 |
|  | Namibia | 1 | 0 |
|  | Niger | 2 | 0 |
|  | Nigeria | 3 | 0 |
|  | Ocean islands | 5 | 7 |
|  | Senegal | 2 | 15 |
|  | Somalia | 1 | 0 |
|  | South Africa | 2 | 15 |
|  | Spain (Canary Islands) | 1 | 30 |
|  | Sudan | 2 | 0 |
|  | Tunisia | 2 | 0 |
|  | United Republic of Tanzania | 3 | 0 |
|  | Zambia | 1 | 0 |
|  | Zimbabwe | 2 | 0 |
| 1 Total |  | 81 | 3 |
| 2 | Afghanistan, Islamic State of | 2 | 0 |
|  | Bangladesh | 2 | 0 |
|  | Cambodia | 1 | 0 |
|  | China | 82 | 30 |
|  | Democratic People's Republic of Korea | 1 | 0 |
|  | Hong Kong, China | 1 | 30 |
|  | India | 34 | 24 |
|  | Iran, Islamic Republic of | 9 | 0 |
|  | Iraq | 1 | 0 |
|  | Japan | 16 | 30 |
|  | Kazakhstan | 8 | 0 |
|  | Kuwait | 1 | 0 |
|  | Maldives | 1 | 0 |
|  | Mongolia | 6 | 18 |
|  | Myanmar | 5 | 0 |
|  | Oman | 2 | 0 |
|  | Pakistan | 3 | 29 |
|  | Qatar | 1 | 0 |
|  | Republic of Korea | 7 | 0 |
|  | Russian Federation (In Asia) | 69 | 0 |
|  | Saudi Arabia | 8 | 0 |
|  | Sri Lanka | 1 | 0 |
|  | Tajikistan | 2 | 0 |
|  | Thailand | 5 | 0 |
|  | Turkmenistan | 2 | 0 |
|  | United Arab Emirates | 1 | 0 |
|  | Viet Nam | 3 | 0 |
| 2 Total |  | 274 | 15 |
| 3 | Argentina | 7 | 0 |
|  | Bolivia | 2 | 0 |
|  | Brazil | 26 | 24 |
|  | Chile | 5 | 12 |
|  | Colombia | 3 | 5 |
|  | Ecuador | 1 | 16 |
|  | French Guiana | 1 | 28 |
|  | Guyana | 1 | 0 |
|  | Islands (88: 800 - 998) | 1 | 15 |
|  | Peru | 2 | 0 |
|  | Venezuela | 4 | 2 |
| 3 Total |  | 53 | 15 |
| 4 | Bahamas | 1 | 0 |
|  | Barbados | 1 | 30 |
|  | Belize | 1 | 27 |
|  | Bermuda | 1 | 20 |
|  | Canada | 30 | 27 |
|  | Cayman Islands | 1 | 6 |
|  | Colombia (San Andres and Providencia Islands) | 1 | 15 |
|  | Costa Rica | 1 | 11 |
|  | Curacao and Bonaire | 1 | 0 |
|  | Dominican Republic | 1 | 11 |
|  | Guadeloupe, St Martin, St Barthelemy (and other French islands in the vicinity) | 1 | 30 |
|  | Jamaica | 1 | 0 |
|  | Mexico | 9 | 15 |
|  | Netherlands Antilles and Aruba | 1 | 30 |
|  | Nicaragua | 1 | 0 |
|  | Puerto Rico and US possessions in the Caribbean area | 1 | 30 |
|  | Trinidad and Tobago | 1 | 30 |
|  | United States of America | 64 | 30 |
|  | United States of America (Alaska) | 14 | 29 |
| 4 Total |  | 132 | 26 |
| 5 | Australia | 34 | 19 |
|  | Brunei Darussalam | 1 | 0 |
|  | Cook Islands | 1 | 0 |
|  | Fiji | 1 | 28 |
|  | French Polynesia (Austral Islands) | 1 | 0 |
|  | French Polynesia (Marquesas Islands) | 1 | 15 |
|  | French Polynesia (Society Islands) | 1 | 30 |
|  | French Polynesia (Tuamotu Islands and Gambier Islands) | 1 | 15 |
|  | Indonesia | 13 | 26 |
|  | Islands (96: 995, 996) | 1 | 15 |
|  | Islands in the Pacific Ocean North of the Equator | 9 | 27 |
|  | Kiribati | 1 | 1 |
|  | Malaysia | 8 | 0 |
|  | Nauru | 1 | 0 |
|  | New Caledonia | 1 | 30 |
|  | New Zealand | 4 | 26 |
|  | Papua New Guinea | 2 | 14 |
|  | Philippines | 4 | 30 |
|  | Samoa and American Samoa | 1 | 30 |
|  | Singapore | 1 | 30 |
|  | Tuvalu | 1 | 3 |
|  | Vanuatu | 1 | 0 |
| 5 Total |  | 89 | 19 |
| 6 | Armenia | 1 | 0 |
|  | Austria | 1 | 29 |
|  | Belgium | 1 | 12 |
|  | Bulgaria | 1 | 0 |
|  | Croatia | 1 | 30 |
|  | Cyprus | 1 | 0 |
|  | Czech Republic | 1 | 30 |
|  | Denmark and Faroe Islands | 1 | 29 |
|  | Estonia | 1 | 0 |
|  | Finland | 3 | 20 |
|  | France | 5 | 29 |
|  | Germany | 10 | 30 |
|  | Gibraltar | 1 | 0 |
|  | Greece | 3 | 4 |
|  | Greenland | 4 | 30 |
|  | Hungary | 2 | 23 |
|  | Iceland | 1 | 0 |
|  | Ireland | 1 | 30 |
|  | Israel | 1 | 0 |
|  | Italy | 4 | 30 |
|  | Jordan | 1 | 0 |
|  | Latvia | 1 | 0 |
|  | Lebanon | 1 | 0 |
|  | Lithuania | 1 | 0 |
|  | Netherlands | 1 | 18 |
|  | Norway | 7 | 25 |
|  | Poland | 3 | 30 |
|  | Portugal | 2 | 0 |
|  | Romania | 2 | 15 |
|  | Russian Federation (In Europe) | 26 | 3 |
|  | Serbia | 1 | 29 |
|  | Slovakia | 1 | 30 |
|  | Slovenia | 1 | 0 |
|  | Spain | 7 | 25 |
|  | Sweden | 4 | 20 |
|  | Switzerland and Liechtenstein | 1 | 30 |
|  | The Former Yugoslav Republic of Macedonia | 1 | 0 |
|  | Turkey | 7 | 30 |
|  | Ukraine | 8 | 0 |
|  | United Kingdom of Great Britain and Northern Ireland | 5 | 23 |
| 6 Total |  | 125 | 16 |
| 7 | Stations in the Antarctic | 15 | 13 |
| 7 Total |  | 15 | 13 |
| Grand Total | 769 | 16 |

# Table 3: Average by country of the number of climate reports from RBSN stations recorded in BUFR messages during the SMM of 1-15 October 2013. The number of reports expected from each station is 1.

| RA | Country/Territory | Count of STN | Average Number |
| --- | --- | --- | --- |
| 1 | Algeria | 51 | 0 |
|  | Angola | 17 | 0 |
|  | Benin | 6 | 0 |
|  | Botswana | 1 | 0 |
|  | Bouvet Island | 1 | 0 |
|  | Burkina Faso | 8 | 0 |
|  | Burundi | 2 | 0 |
|  | Cameroon | 14 | 0 |
|  | Cape Verde | 3 | 0 |
|  | Central African Republic | 13 | 0 |
|  | Chad | 12 | 0 |
|  | Comoros | 1 | 0 |
|  | Congo | 8 | 0 |
|  | Cote D'ivoire | 13 | 0 |
|  | Democratic Republic of the Congo | 29 | 0 |
|  | Djibouti | 1 | 0 |
|  | Egypt | 15 | 0 |
|  | Equatorial Guinea | 2 | 0 |
|  | Eritrea | 2 | 0 |
|  | Ethiopia | 16 | 0 |
|  | Gabon | 6 | 0 |
|  | Gambia | 2 | 0 |
|  | Ghana | 17 | 0 |
|  | Guinea | 12 | 0 |
|  | Guinea-Bissau | 1 | 0 |
|  | Kenya | 18 | 0 |
|  | Lesotho | 3 | 0 |
|  | Liberia | 1 | 0 |
|  | Libya | 25 | 0 |
|  | Madagascar | 26 | 0 |
|  | Madeira | 3 | 0 |
|  | Malawi | 3 | 0 |
|  | Mali | 18 | 0 |
|  | Mauritania | 13 | 0 |
|  | Mauritius | 6 | 0 |
|  | Morocco | 11 | 0 |
|  | Mozambique | 15 | 0 |
|  | Namibia | 14 | 0 |
|  | Niger | 14 | 0 |
|  | Nigeria | 26 | 0 |
|  | Ocean Islands | 13 | 0 |
|  | Other Stations In Region I | 4 | 0 |
|  | Rwanda | 3 | 0 |
|  | Senegal | 12 | 0 |
|  | Seychelles | 3 | 0 |
|  | Sierra Leone | 1 | 0 |
|  | Somalia | 14 | 0 |
|  | South Africa | 89 | 0 |
|  | Spain (Canary Islands) | 8 | 1 |
|  | Spain (Ceuta and Melilla) | 1 | 1 |
|  | Sudan | 24 | 0 |
|  | Swaziland | 1 | 0 |
|  | Togo | 5 | 0 |
|  | Tunisia | 22 | 0 |
|  | Uganda | 8 | 0 |
|  | United Republic of Tanzania | 15 | 0 |
|  | Western Sahara | 1 | 0 |
|  | Zambia | 28 | 0 |
|  | Zimbabwe | 18 | 0 |
| 1 Total |  | 719 | 0 |
| 2 | Afghanistan, Islamic State of | 4 | 0 |
|  | Bahrain | 1 | 0 |
|  | Bangladesh | 6 | 1 |
|  | Cambodia | 2 | 0 |
|  | China | 82 | 1 |
|  | Democratic People's Republic of Korea | 7 | 0 |
|  | Hong Kong, China | 1 | 1 |
|  | India (Stations North of latitude 20N) | 30 | 0 |
|  | India (Stations South of latitude 20N) | 18 | 0 |
|  | Iran, Islamic Republic of | 13 | 0 |
|  | Iraq | 7 | 0 |
|  | Japan | 52 | 1 |
|  | Kazakhstan | 42 | 0 |
|  | Kuwait | 1 | 0 |
|  | Kyrgyzstan | 5 | 0 |
|  | Lao People's Democratic Republic | 4 | 0 |
|  | Macao, China | 1 | 0 |
|  | Maldives | 2 | 0 |
|  | Mongolia | 36 | 0 |
|  | Myanmar | 5 | 0 |
|  | Nepal | 2 | 0 |
|  | Oman | 12 | 0 |
|  | Pakistan | 25 | 1 |
|  | Qatar | 1 | 0 |
|  | Republic Of Korea | 11 | 0 |
|  | Russian Federation (In Asia) | 184 | 0 |
|  | Saudi Arabia | 31 | 0 |
|  | Sri Lanka | 6 | 0 |
|  | Tajikistan | 13 | 0 |
|  | Thailand | 13 | 0 |
|  | Turkmenistan | 13 | 0 |
|  | United Arab Emirates | 2 | 0 |
|  | Uzbekistan | 12 | 0 |
|  | Viet Nam | 17 | 0 |
|  | Yemen | 4 | 0 |
| 2 Total |  | 665 | 0 |
| 3 | Argentina | 65 | 0 |
|  | Bolivia | 20 | 0 |
|  | Brazil | 78 | 1 |
|  | Chile | 17 | 0 |
|  | Colombia | 20 | 1 |
|  | Ecuador | 7 | 0 |
|  | French Guiana | 4 | 1 |
|  | Guyana | 1 | 0 |
|  | Islands (88: 800 - 998) | 1 | 1 |
|  | Paraguay | 15 | 0 |
|  | Peru | 23 | 0 |
|  | Suriname | 1 | 0 |
|  | Uruguay | 9 | 0 |
|  | Venezuela | 29 | 0 |
| 3 Total |  | 290 | 0 |
| 4 | Bahamas | 1 | 0 |
|  | Barbados | 1 | 0 |
|  | Belize | 1 | 0 |
|  | Bermuda | 1 | 0 |
|  | Canada | 115 | 0 |
|  | Cayman Islands | 1 | 0 |
|  | Colombia (San Andres and Providencia Islands) | 2 | 1 |
|  | Costa Rica | 2 | 0 |
|  | Cuba | 4 | 0 |
|  | Curacao And Bonaire | 1 | 0 |
|  | Dominican Republic | 3 | 0 |
|  | El Salvador | 4 | 0 |
|  | Guadeloupe, St Martin, St Barthelemy (and other French islands in the vicinity) | 1 | 0 |
|  | Guatemala | 9 | 0 |
|  | Honduras | 4 | 0 |
|  | Jamaica | 2 | 0 |
|  | Martinique | 1 | 0 |
|  | Mexico | 53 | 0 |
|  | Netherlands Antilles And Aruba | 1 | 0 |
|  | Nicaragua | 1 | 0 |
|  | Panama | 1 | 0 |
|  | Puerto Rico and US possessions in the Caribbean Area | 1 | 0 |
|  | Trinidad And Tobago | 1 | 0 |
|  | United States of America (Alaska) | 14 | 0 |
|  | United States of America | 91 | 0 |
| 4 Total |  | 316 | 0 |
| 5 | Australia (Additional Islands) | 3 | 1 |
|  | Australia (Lat 10S - 15S) | 5 | 1 |
|  | Australia (Lat 15S - 20S) | 8 | 1 |
|  | Australia (Lat 20S - 25S) | 13 | 1 |
|  | Australia (Lat 25S - 30S) | 17 | 1 |
|  | Australia (Lat 30S - 35S) | 32 | 1 |
|  | Australia (Lat 35S - 40S) | 19 | 1 |
|  | Australia (Lat 40S - 45S) | 6 | 1 |
|  | Brunei Darussalam | 1 | 0 |
|  | Cook Islands | 5 | 0 |
|  | Detached Islands (91 : 753, 754) | 1 | 1 |
|  | Detached Islands (91: 960 - 998) | 1 | 0 |
|  | Fiji | 5 | 0 |
|  | French Polynesia (Austral Islands) | 2 | 1 |
|  | French Polynesia (Marquesas Islands) | 1 | 1 |
|  | French Polynesia (Society Islands) | 2 | 1 |
|  | French Polynesia (Tuamotu Islands and Gambier Islands) | 3 | 1 |
|  | Indonesia (Jawa) | 5 | 1 |
|  | Indonesia (Kalimantan) | 2 | 1 |
|  | Indonesia (Maluku And / Et Irian Jaya) | 11 | 1 |
|  | Indonesia (Nusatenggara) | 4 | 1 |
|  | Indonesia (Sulawesi) | 6 | 1 |
|  | Indonesia (Sumatra) | 7 | 1 |
|  | Islands (96: 995, 996) | 2 | 1 |
|  | Islands in the Pacific Ocean North of the Equator | 13 | 0 |
|  | Kiribati | 1 | 0 |
|  | Malaysia (Peninsular Malaysia) | 7 | 0 |
|  | Malaysia (Sabah and Sarawak) | 8 | 0 |
|  | Nauru | 1 | 0 |
|  | New Caledonia | 2 | 1 |
|  | New Zealand | 14 | 0 |
|  | Niue | 1 | 0 |
|  | Papua New Guinea | 10 | 0 |
|  | Philippines | 8 | 1 |
|  | Phoenix Islands | 1 | 0 |
|  | Samoa And American Samoa | 2 | 0 |
|  | Singapore | 1 | 1 |
|  | Solomon Islands | 2 | 0 |
|  | Timor-Leste | 3 | 0 |
|  | Tokelau (and Swains Is.) | 1 | 0 |
|  | Tonga | 5 | 0 |
|  | Tuvalu | 2 | 0 |
|  | Vanuatu | 3 | 0 |
| 5 Total |  | 246 | 1 |
| 6 | Albania | 1 | 0 |
|  | Armenia | 4 | 0 |
|  | Austria | 9 | 0 |
|  | Azerbaijan | 6 | 0 |
|  | Belarus | 12 | 0 |
|  | Belgium | 1 | 0 |
|  | Bosnia And Herzegovina | 5 | 0 |
|  | Bulgaria | 4 | 0 |
|  | Croatia | 2 | 1 |
|  | Cyprus | 2 | 0 |
|  | Czech Republic | 9 | 1 |
|  | Denmark And Faroe Islands | 4 | 0 |
|  | Estonia | 3 | 0 |
|  | Finland | 11 | 0 |
|  | France | 42 | 1 |
|  | Georgia | 6 | 0 |
|  | Germany | 56 | 1 |
|  | Gibraltar | 1 | 1 |
|  | Greece | 9 | 1 |
|  | Greenland | 8 | 0 |
|  | Hungary | 7 | 0 |
|  | Iceland | 6 | 0 |
|  | Ireland | 8 | 1 |
|  | Israel | 3 | 1 |
|  | Italy | 34 | 1 |
|  | Jordan | 4 | 0 |
|  | Kazakhstan (Europe) | 2 | 0 |
|  | Latvia | 4 | 0 |
|  | Lebanon | 2 | 0 |
|  | Lithuania | 5 | 0 |
|  | Luxembourg | 1 | 0 |
|  | Malta | 1 | 0 |
|  | Montenegro | 2 | 0 |
|  | Netherlands | 6 | 1 |
|  | Norway | 14 | 1 |
|  | Poland | 10 | 1 |
|  | Portugal | 12 | 0 |
|  | Republic of Moldova | 2 | 0 |
|  | Romania | 14 | 0 |
|  | Russian Federation (In Europe) | 53 | 0 |
|  | Serbia | 3 | 0 |
|  | Slovakia | 5 | 0 |
|  | Slovenia | 4 | 0 |
|  | Spain | 46 | 1 |
|  | Sweden | 13 | 1 |
|  | Switzerland And Liechtenstein | 8 | 0 |
|  | Syrian Arab Republic | 7 | 0 |
|  | The Former Yugoslav Republic of Macedonia | 4 | 0 |
|  | Turkey | 56 | 1 |
|  | Ukraine | 30 | 0 |
|  | United Kingdom of Great Britain and Northern Ireland | 20 | 1 |
| 6 Total |  | 581 | 1 |
| 7 | Stations in the Antarctic | 101 | 0 |
| 7 Total |  | 101 | 0 |
| (blank) | (blank) |  |  |
| (blank) Total |  |  |
| Grand Total | 2918 | 0 |

- ANNEX TO PARAGRAPH 7.2.1

[Efforts made towards migration]

Despite limited computing and human resources few countries have sourced for funds and made some progress on the migration path. Summary of these efforts are as follows;

| Country | Migration Efforts |
| --- | --- |
| Tanzania | The ECMWF software for BUFR encoding has been implemented for encoding of SYNOPS in a number of observatories. Efforts are being made to have these messages transmitted to GTS. |
| Kenya | The country has been gradually implementing TDCF operations since 2010 on data Category 1 using CLIMSOFT for encoding and transferring BUFR messages to the local message switching system via FTP for forward transmission to GTS |
| Rwanda | Since 2012 has been implementing CLIMSOFT to encode SYNOPS and AWS data through Template TM307091. The BUFR messages are being transferred to Nairobi RTC via FTP |
| Madagascar | From March 2014 installed CLIMSOFT to encode SYNOPS and AWS data and transfer the BUFR messages to the local message switching system. The process is currently being undertaken on test basis |
| Botswana | As early as 2012 Botswana had indicated to have installed TAC-BUFR converter through the assistance of Pretoria |
| Malawi and Burundi | Have indicated they are sourcing for funding and soon will approach Kenya for assistance in the implementation of TDCF operations |

[Major Challenges towards migration]

Lack of TDCF encoding and transmission systems

Even after undergoing training and getting the concept on TDCF requirements many countries are unable to proceed with the migration due to the lack of capacity to implement TDCF processing systems. Although there are a number of freely available TDCF decoder software their connectivity with the data transmission systems poses a big challenge.

Capability of the message switching systems

Some message switching systems require upgrading to fully process TDCF messages. Where funds are unavailable for such investment transfer of messages becomes difficult. An example is the Nairobi messages switch which can only forward BUFR messages but cannot compile them into bulletins. Software for compiling had to be separately developed.

Connectivity to RTCs

Many countries have been using simple means of transferring TAC messages to the responsible RTCs such as email. Transfer of TDCF messages requires upgrading to more complex means such as FTP. Many countries have not been able to upgrade to such communication means.

Management of the new headers

Even after managing to transmit BUFR messages it has been found to take long for the managers of the message switching systems to configure the routing of the newly generated BUFR headers. Examples of the headers that have been affected are from Kenya – ISH01 HKNC, Rwanda – ISH01 HRYR, ISH01 HRYR and Madagascar – ISH01 FMMD, ISAH01 HRYR.

Parallel Transmission

The requirement for parallel transmission was an extra work in those countries that had started generating some TDCF messages. In cases where staff capacity was low the newly implemented TDCF operations were given a lower priority thereby reversing gains made towards migration.

- ANNEX TO PARAGRAPH 7.2.2

[RA-II Member activities related to TDCF]

Several activities related to TDCF were reported by RA-II Members since May 2013:

Thailand:

Thailand started disseminating SYNOP and TEMP reports in BUFR format in December 2013. GTS headings are: ISMC[20 | 21 | 40 | 41 | 42 | 43], ISIC[20 | 21 | 40 | 41 | 42 | 43], IUSC01 VTBB. Thailand had discussion on TAC-TDCF conversion for Lao Republic in case it is not ready to process at its own site.

Vietnam:

Vietnam has developed its TDCF decoding and encoding system for surface synoptic, upper-air sounding and climate data. It partly started disseminating BUFR SYNOP data in March 2014, and is planning to start BUFR TEMP, PILOT and CLIMAT in near future.

[Monitoring and Analysis of Migration Status]

Monitoring method

Statistics were collected for the period of January 1 through 15, 2014. Resources were derived from the results of Special MTN Monitoring (SMM) pre-analysis and Integrated WWW Monitoring (IWM) created by WMC Melbourne/RTH Tokyo and from the latest version of the surface and upper-air (RBSN) station list of Regional Basic Synoptic Networks at the time of analysis.

In addition to WWW monitoring, the status of TDCF data communication is also monitored based on a catalogue created by GISC Tokyo (available at http://www.wis-jma.go.jp/csv/catalog.csv).

Migration progress and status

(1)	SYNOP, TEMP and PILOT reports

The figures below show numerical representations of the progress of stations issuing BUFR-format bulletins equivalent to SYNOP and TEMP reports over the past two years. In the latest monitoring period from January 1 to 15, 2014, RTH Tokyo received (i) at least one surface synoptic observation report (excluding NIL reports) in BUFR format from 51% of RA-II observation stations registered as part of RBSN (TAC format from 78%), and (ii) at least one upper-air sounding report in BUFR format from 36% of registered stations (TAC format from 82%). Fifteen BUFR reports equivalent to PILOT reports were received by RTH Tokyo in the monitoring period, while TAC bulletins were received from 15 stations.

Number of RA-II RBSN stations issuing surface synoptic observation (SYNOP) and upper-air sounding (TEMP) reports in TAC and BUFR format from April 2012 to January, 2014

(2) CLIMAT reports

As of April 2014, nine Members were reporting CLIMAT data in BUFR format: China; India; Mongolia; Saudi Arabia; Pakistan; Japan; Bangladesh; Hong Kong, China; and Macao, China.

(3) Marine reports

As of April 2014, Hong Kong, China (SHIP) and Japan (TESAC, TRACKOB, SHIP) were routinely disseminating marine observation data in BUFR format.

[October 2013 RA-II Questionnaire on Migration to Table Driven Code Forms]

Summary of response

The theme leader sent a questionnaire to all listed focal points in October 2013 and received responses from 18 Members by November 2013. The purposes of the survey were to determine the current status of migration and related plans, and to ascertain how Members view the challenges and benefits of migration to TDCF.

Findings obtained from the survey results

(1) Creation and dissemination of TDCF

- Out of 18 respondents, 10 members (56%) are already disseminating TDCF reports, 3 centers (17%) have made arrangements for TAC-TDCF conversion with other centers and 3 centers (17%) are planning to start in near future, while 3 centers have no plan.

- Two members are planning to discontinue TAC dissemination by the end of 2014.

- Main challenges or obstacles in migrating TDCF are encoding software (56%), GTS communication (11%) and lack of awareness about the benefits of TDCF (33%). Management is also raised as a challenge.

(2) Use of TDCF

- Out of 18 respondents, 6 members (33%) are already using TDCF reports for daily forecasts, numerical weather prediction system and/or statistics, 4 centers (22%) are planning to start in near future, while 8 centers (44%) have no plan.

- Eight members (44%) out of 18 respondents answered that they need TAC reports even after November 2014.

- Most members recognize the greater variety of data and the metadata included in reports are the benefits of TDCF.

- Some members consider the higher quality of data as a benefit of TDCF, while other members express concern about lack of data quality and quality control as an obstacle in using TDCF.

- Lack of awareness about the benefits of TDCF is one of the major obstacles in using TDCF, as one third of respondents indicated it as a main challenge, which is nearly as many as respondents who answered that decoding is the main issue.

(3) Processing of TDCF

- Eighty-three percent of respondents said they prefer to encode and decode TDCF at their own site, while only one center preferred TAC-TDCF conversion by other center.

- ANNEX TO PARAGRAPH 7.2.3

[Status in Region III]

Argentina

RTH Buenos Aires operates a Message Switching System and excutes conversion on behalf of other NMC´s in its area of responsibility.  Nevertheless, they also installed the libecBUFR package from Environment Canada, trained people, defined a team and developed a graphic tool to ingest observations from meteorological stations and encode and decode SYNOP bulletins.

Chile

The representative of Chile informed they have done a lot of effort to disseminate the knowledge received in Montevideo, as well as producing data. Soon the bulletins will be available into the GTS.

Ecuador

The authorities of the Meteorological Service of Ecuador as well as producers and users of information are now aware of the Migration Plan to TDCF. The plan will start in May 2014 to complete the process of implementation by November 2014 as requested WMO. The plan includes the acquisition of 21 automatic observation stations including, 10 with CLIMAT and 2 upper-air.

Colômbia

NMC Bogota is still working the data base access in order to generate the BUFR bulletins directly from the database.

Peru

The representative of SENAMHI installed the libecBUFR package, passed the knowledge to his team and they started the tests.

Uruguay

NMC Montevideo produces BUFR bulletins in a sort of “beta testing” phase. They plan to test them soon with RTH Brasilia.

No information from NMC Bolívia and Venezuela.

Brazil regarding Category I data:

- The Message Switching System at RTH Brasilia automatically converts SYNOP, TEMP and PILOT bulletins collected from the Air Force and the Navy network, in BUFR.

- All the AWS observation data are encoded in BUFR and inserted in the GTS.

- Since January 2014, the CLIMAT reports are coded in BUFR directly using the libecBUFR tool. No more conversion as before. The SYNOP reports from manned stations are the next in the list.

- INMET had replaced all its upper air equipment and they are able to generate BUFR reports on the site. Right now, we are collecting the TEMP, PILOT and BUFR bulletins.

- The Air Force also replaced their ground equipment but do not collect the BUFR bulletins yet. The PR of Brazil initiate negotiation with the Air Force representative in order to make these data available to GTS.

- RTH Brasilia and RTH Buenos Aires also convert Category I bulletins from other centres in Region III to distribute into the GTS.

- In addition to Category I data, RTH Brasilia expects to convert also the AMDAR bulletins into BUFR, as soon as the template be available to the Message Switching System.

In addition:

- The main meteorological organizations in Brazil already possess software capable of ingesting, processing and displaying meteorological data in BUFR format. Each meteorological organization in the country uses a mix of commercial and free software.

- The University of São Paulo, in collaboration with INPE (National Institute of Space Research) is planning to deliver meteorological data in BUFR, derived from an ATLAS moored buoy to the GTS.  The bulletin abbreviated heading will be IOBE01 SBBR.  There was a problem when releasing the first buoy in the end of the 2013 and they expect to fix the problem and launch it again late this year.

- ANNEX TO PARAGRAPH 7.2.4

Example "migration progress sheet" in Spanish drafted by the Chilean attendee at the November 2013 Montevideo BUFR/MTDCF workshop.  The idea would be to use such a spreadsheet to track and compare progress and capacity across a group of States or stakeholders engaged in the MTDCF.

|  |  | Nombre del País 1 | Nombre del País 2 | Comentarios |
| --- | --- | --- | --- | --- |
| 1 | Tiene plan nacional de migración | no | si | Pero se está trabajando en ello |
| 2 | Tiene un equipo multidisciplinario formado en su servicio para BUFR | no | si |  |
| 3 | Las estaciones de su país tienen una intranet nacional | no | no |  |
| 4 | Las estaciones se conectan vía internet u otro medio a un centro nacional | SI | SI | Vía FTP |
| 5 | Tienen un equipo informático en su servicio | SI | SI | pero limitado |
| 6 | Tiene un compromiso de sus autoridades para abordar el tema de la migración a BUFR | SI | SI | Aunque faltan acuerdos |
| 7 | Ya codifica en BUFR los datos de los Sinópticos | SI | SI | Decodificador Europeo |
| 8 | Ya codifica en BUFR los datos de los mensajes CLIMAT | NO | NO |  |
| 9 | Ya codifica en BUFR los datos de los mensajes TEMP | NO | NO |  |
| 10 | Recibe los datos de la observaciones en tiempo real | NO | NO | Se obtienen de terceros |
| 11 | Recibe a nivel central mensajes alfanuméricos tradicionales | NO | NO |  |
| 12 | Tiene algún software que permita capturar los datos y enviarlos a un centro nacional | NO | NO |  |
| 13 | Sus datos son almacenados en una base de datos relacional | NO | NO | Solo datos climáticos pero no datos observados |
| 14 | Tiene un centro informático con la capacidad de instalación de libecbufr | SI | SI |  |
| 15 | Tiene un enlace VPN con un centro regional | SI | SI |  |
| 16 | Tiene capacidad técnica para instalar y mantener la librería libecbufr | SI | SI |  |
| 17 | Sabe como contactarse a nivel regional | SI | SI |  |
| 18 | Ha designado un punto focal estable en su país. | NO | NO | No está claramente definido |
| 19 | Tiene una base de datos actualizada con metadata de las estaciones | NO | NO |  |
| 20 | Ha realizado capacitación local en la clave BUFR | NO | NO | Pero se está planeando |
| 21 | Tiene actualizada la información de las estaciones en la OMM | SI | SI | De las estaciones que transmite SYNOPS |

- ANNEX TO PARAGRAPH 7.2.5

Status of migratrion in RA V

At least one type of Category 1 data from the following countries are produced in TDCF:

Australia, Cooks Islands, French Polynesia, Fiji, Indonesia, Malaysia, New Zealand,

Papua NewGuinea, Philippines, Samoa, Singapore, New Caledonia,

Federated States of Micronesia

Countries that yet to produce any TDCF reports, as of April 2014, are:

Nauru, Vanuatu, Tonga, Niue, Brunei, East Timor, Kiribati, Tuvalu, Tokelau

- ANNEX TO PARAGRAPH 7.2.6

Status of Migration to TDCF in RA VI - April 2014

At least one type of Category 1 data from the following countries of RA VI are produced in TDCF (Albania, Armenia, Austria, Belarus, Bosnia and Herzegovina, Belgium, Croatia, Cyprus, Czech Republic, Denmark and Faroe Islands, Estonia, Finland, France, Germany, Georgia, Greece, Hungary, Ireland, Israel, Italy, Jordan, Latvia, Lithuania, Lebanon, Luxembourg, Montenegro, Netherlands, Norway, Poland, Portugal, Romania, Russian Federation, Serbia, Slovakia, Slovenia, Spain, Sweden, Switzerland, Syria, The Former Yugoslav Republic of Macedonia, Turkey, United Kingdom of Great Britain and Northern Ireland); the underlined countries (28) produce all types of their Category 1 data in BUFR. Synoptic data in BUFR are produced by 39 countries, upper-air data in BUFR by 29 countries, CLIMAT data in BUFR by 25 countries. High resolution radiosonde data are produced by Cyprus, Czech Republic, Denmark and Faroe Islands, Germany, Greece, Ireland, Netherlands, Norway, Russian Federation, Slovakia, Spain, Sweden and Switzerland, the underlined countries at all their stations. SHIP data from France, Israel, Netherlands, Norway and Sweden are produced in BUFR.

Activities in RA VI

The Task Team on Migration to TDCF under the leadership of Dr Eva Červená has supported the migration process in RA VI.  In accordance with the decision by the 16th Session of RA VI (Helsinki, Finland, September 2013), the RA VI Working Group on Technology Development and Implementation (WG/TDI) and the Task Teams, including TT-MTDCF will be formed by the RA VI Management Group meeting (14-15 May 2014).

ECMWF has created a wiki page “TAC To BUFR Migration” which is accessible in view mode under https://software.ecmwf.int/wiki/display/TCBUF/TAC+To+BUFR+Migration and where the information on BUFR and TAC data availability (completeness, timeliness, duplicates, structure) is provided. There are also two latest versions of the program synop2bufr available, prepared mainly by Mr. Perisa Sunderic (Serbia). Detailed description of the updates is included.

The Norwegian Meteorological Institute has made freely available several programs for BUFR decoding and encoding under https://wiki.met.no/bufr.pm/start, most notably the CPAN module Geo::BUFR.

The Irish Meteorological Service is preparing a program for conversion of SHIP data to BUFR. After additional testing it may be available to NMSs within a few months.

- ANNEX TO PARAGRAPH 7.2.9

status of BUFR templates for marine data AS REPORTED TO THE IPET-DRMM-II

| TAC | Description | Current template(s) | Status | Plans/comments |
| --- | --- | --- | --- | --- |
| FM13-XIV SHIP | VOS data | B/C10 - Regulations for reporting SHIP data in TDCF | Operational (TM308009) |  |
|  | VOS data | Synoptic reports from sea stations suitable for SHIP observation data from VOS stations (see Appendix B) | Validation | Template should be revised to allow for the encryption of the ship’s call sign (proposed at IPET-DRMM-II). |
| FM18-XII BUOY | Drifting buoy data | Template for the representation from drifting buoys | Operational May 2014 (TM 315009) | Simplified template specific to drifting buoys |
|  | Moored buoy data | Template for the representation of data from moored buoys | Operational May 2014 (TM 315008) | Simplified template specific to moored buoys, including directional and non-directional wave data |
|  | Wave buoy data | Template for the representation of data from moored buoys | Operational May 2014 (TM 315008) | Simplified template specific to moored buoys, including directional and non-directional wave data |
|  | Argo data | Sub-surface profiling floats | Operational (TM315003) | No specific plan for this template |
| FM36-XI Ext. TEMP SHIP | ASAP data | B/C25 - Regulations for reporting TEMP, TEMP SHIP, TEMP MOBIL data in TDCF | Operational (TM309052) | No specific plan for this template |
|  | ASAP data | UKMO template for representation of radiosonde data with geopotential height as the vertical coordinate | Operational (revisited in July 2010) |  |
| FM62-VIII Ext. TRACKOB | TRACKOB data | TRACKOB data – ThermoSalinoGraph (TSG) data and metadata | Operational (TM308010) | No specific plan for this template |
| FM63-XI Ext. BATHY | XBT data | New BUFR template for XBT Temperature Profile data | Operational (TM315004) as from 7 Nov. 2012 |  |
| FM64-XI Ext. TESAC | CTD / TESAC | Template for the representation of data derived from a ship based lowered instrument measuring subsurface seawater temperature, salinity and current profiles. | Operational May 2014 (TM 315007) |  |
| FM65-XI Ext. WAVEOB | Wave buoy data | Templates for the wave observations from different platforms suitable for WAVEOB data | Validation | Template should be imminently validated and operational |
| N/A | Sea-level data | BUFR/CREX templates for tsunameter data and dart buoy system messages | Operational (TM306027) | No specific plan for this template |
|  | Sea-level data | BUFR/CREX templates for reporting time series of tide data | Implemented on 7 May 2014 | Template should undergo validation |

- ANNEX TO PARAGRAPH 7.3

Criteria for the migration be considered complete [CBS session/General Summary 2.3(1).16]:

a)	WMO no longer maintains the World Weather Watch Traditional Alphanumeric Codes (but OPMET codes will be maintained as long as ICAO requires them),

b)	all centres using information that is exchanged on the GTS Main Telecommunications Network can operate based on the TDCF information flow,

c)	no National Centre is required to produce information in TAC for the purpose of GTS exchange.

Recommendations on migration by participants

RA I:

a)	More support should be provided to Kenya and Tanzania so that they can continue with their efforts in assisting other countries in the region to expedite their migration process.

b)	More support should be extended to the RTCs in the region so that they can acquire sufficient capacity to support the NMHS under their responsibilities in the TDCF messages processing and routing.

d)	System developers need to be encouraged to develop TDCF processing systems that are simple and integrate well with the region’s data processing practices.

e)	The November 2014 migration deadline need to be maintained and plans for termination of parallel transmission are put in place immediately.

RA II:

a)	all centers not to stop TAC dissemination, because 1) many members are not ready to continue daily forecasts, numerical weather prediction and other operational activities without TAC reports and 2) NWP centers have not fully assessed qualities of TDCF reports available.

b)	RTHs and GISCs to assist members to establish TDCF processing systems at their own site.

c)	RTHs and GISCs to assist members to promote the use of TDCF reports for daily forecasts, numerical weather prediction systems and/or statistics, especially help their systems to be changed to use TDCF or decoded data instead of using TAC data as inputs.

d)	NWP centers to assess quality of both TDCF and TAC reports in near-real time basis and to consider establishing a mechanism to perform systematic quality monitoring in their data assimilation system and to publish the results to help improvement of data quality.

RA III:

I suggest WMO to make sure the countries are aware of the Migration plan and the Permanente Representative should give support to the local team in charge of this process.

RA IV:

a)	We recommend to quickly build on the positive effects of the Training workshop by forming an RA  IV task group and establishing regional migration plans in support of national plans. This is conceptually similar to what was done with a great deal of success in RA VI. We believe all those things are still very much needed, even in the closing phase of the official Migration for SYNOP, TEMP/PILOT and CLIMAT conversion. The visible and concrete commitment an mutual support of NMHCs toward completing the migration will be necessary to provide participants with the resources required to accomplish its objectives.

b)	Observing the continuing need for training, and noting that Region III authorities kindly invited members of Region IV to the Montevideo workshop, we recommend that Region IV reciprocate by organizing a workshop for its own area and invite members of Region III who were unable to attend the first workshop. As a further capacity building mechanism, some of the participants in the Montevideo workshop could be called upon as speakers for this proposed workshop.

c)	Noting that the planned deadline for the ultimate completion of Category 1 data in the Migration Schedule is practically upon us, and noting further that numerous countries, notably in Regions I, III and IV, are very unlikely to be able to complete the migration within this deadline, we recommend the undertaking of a technical review of the Migration plan that would ensure both the continued implementation of the MTDCF beyond its originally planned deadline, and a supportive environment that would ensure that it is completed as quickly as possible in an orderly and successful manner.

RA V:

Although the assessment has not been finalized for all PCI, some patterns have been emerged in terms of the impact of MTDCF and the solutions. It is expected that

a)	TAC => TDCF conversion has to be done centrally for PCI. RTH Melbourne and RTH Wellington will take action on the conversion. This has already been happing for some PCI. We endeavourer to meet the deadline of the Nov 2014 for the Cat 1 bulletins.

b)	For countries that has the requirement of using data that only exist in TDCF after the migration, assistance is needed to meet this requirement. RTH Melbourne will assist in TDCF => TAC conversion centrally, which can be delivered in the WIS framework by GISC Melbourne or provide the conversion capability locally.

c)	TAC, in particular SYNOP, will still be used “internally” for quite some time in those countries.

RA VI:

The RA VI seems to be an advanced Region regarding Migration to TDCF and some countries, already processing the data in BUFR, are troubled by the necessity to deal with both formats. There are some countries, however, that would need TAC data not only in November 2014, but probably for considerable time after it. These countries have been invited to ask for assistance from a GISC or a DCPC to perform conversion TDCF <=> TAC for them, e.g. GISC Offenbach or DCPC Prague. Postponing the termination of all Category 1 data distribution in TAC would lead merely to repetition of the current situation in the future. The gradual termination of parallel dissemination of TAC and BUFR data should be recommended. It would speed up the finalization of BUFR data processing or encourage the NMSs to make the relevant arrangements for conversion TDCF <=> TAC by another Centre.

- ANNEX TO PARAGRAPH 9.1.1 [CBS session/Rec. 2.3(1)/1 (CBS-Ext.(2014))]

Add to Table C6 of the Manual on the GTS (Data type designator A1 (when T1 = I or J)):

| T1T2 | A1 | ii | Data type | TAC correspondence | Data category subcategory (Common Table C13) |
| --- | --- | --- | --- | --- | --- |
| IN | C |  | CrIS (selected channels) |  | 03/30 |
| IN | I |  | IRAS |  | 03/20 |
| IN | J |  | HIRAS |  | 03/30 |
| IN | K |  | MWHS/MWHS-2 |  | 03/40 |
| IN | Q |  | IASI (Principle component scores) |  | 03/7 |
| IN | S |  | ATMS |  | 03/40 |
| IN | T |  | MWTS/MWTS-2 |  | 03/40 |

- ANNEX TO PARAGRAPH 10.1

Membership and work plan of TT-AvCI

1.     IPET-DRMM agreed to form the Task Team on Aviation Coding Issues (TT-AvCI) as follows.

Lead: Yves Pelletier (Canada)

Members: Japan, Turkey, UK, Germany, Australia, Burt Nikorai (Belgocontrol) or someone from TT-AvXML

2.   Work plan of the TT-AvCI on the Amendment 77 to the ICAO Annex 3 cynchronized to the progress of ICAO's formality.

July 2014

(1)	TT receives the result of ICAO Meteorology Divisional Meeting (Montreal, July 2014) with respect to the Amendment 77.

(2)	TT starts to collect and review information on draft amendments to the Manual on Codes to be developed by ICAO.

November 2014

(3)	TT is to be involved in the drafting work of amendments to the Manual on Codes in accordance with the ICAO Air Navigation Commission (ANC) preliminary review of proposed Amendment 77.

February to June 2015

(4)	TT is notified briefly the result of consultation of the proposed Amendment with ICAO Contracting States and concerned international organizations.

October 2015

(5)	TT finalizes the amendments to the Manual on Codes with a view to ICAO ANC final review of proposed Amendment 77 in cooperation with ICAO Secretariat.

December 2015

(6)	WMO Secretariat initiates the procedure for adoption of amendments to the Manual on Codes between CBS sessions.

3.	IPET-DRMM further agreed the lead (or members) of TT-AvCI are to be involved in the discussion of TT-AvXML to contribute to the WMO Logical Data Model (LDM), reflecting amendments to the Manual on Codes.

- ANNEX TO PARAGRAPH 11.1 [CBS session/Rec. 2.3(1)/2 and 3 (CBS-Ext.(2014))]

Draft Recommendation (CBS Ext. (14))

## AUTHORIZING USE OF THE PROCEDURE FOR AMENDING THE MANUALS BETWEEN CBS SESSIONS IN RESPONSE TO AMENDMENTS TO ICAO ANNEX 3

THE COMMISSION FOR BASIC SYSTEMS

Noting that responsibility for updating the regulations for exchanging meteorological information of relevance to international civil aviation is shared between the World Meteorological Organization (WMO) and the International Civil Aviation Organization (ICAO);

Noting further:

(1)	that the pertinent technical regulations of the ICAO are documented in ICAO Annex 3 and that the WMO Technical Regulations, Volume II (WMO No. 49) has the same content as ICAO Annex 3;

(2)	that the sixty-first session of EC approved the procedure for adoption of amendments to the Manual on Codes (WMO No. 306) between sessions of the Commission for Basic Systems (CBS) (Resolution 7 (EC-LXI));

(3)	that in paragraph 3.5.2.1 of its final report the sixty-second session of EC (EC-LXII) requested the CBS to limit amendments for adoption between CBS sessions to those that had no operational impact or financial burden on Members;

(4)	that the schedules for decision making sessions of the ICAO Council and the WMO CBS are not synchronized, such that decisions by the ICAO Council may need to be implemented before the next session of the CBS;

(5)	that amendments adopted by the ICAO Council will have operational impacts for those (WMO) Members that are also (ICAO) Contracting States and that the amendments may consequently place a financial burden on such Members;

(6)	that Members who are also Contracting States to the ICAO will have been consulted by the ICAO in the preparation of Amendments to ICAO Annex 3;

Recommends that Executive Council authorizes the CBS to use the procedure for adoption of amendments between CBS sessions for changes to the Manual on Codes (WMO No. 306), the Manual on the Global Telecommunications System (WMO No 386) and the Manual on the WMO Information System (WMO No. 1060) that are required to support the implementation of Amendments to ICAO Annex 3.

Draft Recommendation (CBS Ext. (14))

## Amendments to the Manual on Codes (WMO-No. 306), Volume I.2

THE COMMISSION FOR BASIC SYSTEMS

Noting:

(1)	Resolution 1 (Cg-XVI) – World Weather Watch Programme for 2012–2015,

(2)	Resolution 4 (Cg-XVI) – Report of the Extraordinary Session (2010) of the Commission for Basic Systems Relevant to Technical Regulations Concerning the Global Telecommunica-
tion System, Data Management and the WMO Information System,

(3)	The Manual on Codes (WMO-No. 306), Volume I.2,

(4)	The report of the First Meeting of Inter-Programme Expert Team on Data Representation Maintenance and Monitoring (Tokyo, July 2013),

Considering the urgent requirements for correct reporting of height and amount of clouds, which have not been specified by the regulations for reporting traditional observation data in TDCF,

Recommends that the amendments to the regulations for reporting traditional observation data in TDCF, as defined in the annex to the present recommendation, be adopted for implementation from 4 November 2015,

Requests the Secretary-General to arrange for the inclusion of these amendments to Volume I.2 of the Manual on Codes,

Further requests the Secretary-General to notify the amendments through the WWW Operational Newsletter so that Members can incorporate them in relevant software when it is possible to meet the urgent requirements;

Authorizes the Secretary-General to make any consequent purely editorial amendments to the Manual on Codes – Volume I.2.

Annex to Recommendation xx (CBS Ext. (14))

AMENDMENTS TO REGULATIONS FOR REPORTING TRADITIONAL OBSERVATION DATA IN TDCF: BUFR OR CREX

Add new regulations:

B/C 1.4.4.4.4, B/C 5.4.4.4.4 and B/C 10.4.4.4.3

If synoptic data are produced in BUFR or CREX by conversion from a TAC report, the following approach shall be used: Height of base of the lowest cloud 0 20 013 shall be derived from the hshs in the first group 8 in section 3, i.e. from the hshs of the lowest cloud. If and only if groups 8 are not reported in section 3, 0 20 013 may be derived from h. The lower limit of the range defined for hshs and for h shall be used. However, if groups 8 are not reported in section 3 and h = 9 and Nh ≠ 0, then 0 20 013 shall be 4000 m; if groups 8 are not reported in section 3 and h = 9 and Nh = 0, then 0 20 013 shall be 8000 m.

Add items (d), (e) and (f) in the regulations below:

B/C 1.4.4.3.1, B/C 5.4.4.3.1 and B/C 10.4.4.3.1

(d)	If no clouds are observed (clear sky), then the cloud amount shall be reported as 0.

(e)	If sky is obscured by fog and/or other meteorological phenomena, then the cloud amount shall be reported as 9.

(f)	If cloud cover is indiscernible for reasons other than fog or other meteorological phenomena, or observation is not made, the cloud amount shall be reported as missing.

- ANNEX TO PARAGRAPH 11.2 [Validation]

Add entries in BUFR/CREX Table B.

Class 01 – BUFR/CREX Identification

|  |  | BUFR | CREX |
| --- | --- | --- | --- |
| TABLE |  |  |  |  | DATA |  |  | DATA |
| REFERENCE | ELEMENT NAME | UNIT | SCALE | REFERENCE | WIDTH | UNIT | SCALE | WIDTH |
| F X Y |  |  |  | VALUE | (Bits) |  |  | (Characters) |
| 0 01 125 | WIGOS Identifier Series | Numeric | 0 | 0 | 4 | Numeric | 0 | 2 |
| 0 01 126 | Issuer of Identifier | Numeric | 0 | 0 | 16 | Numeric | 0 | 5 |
| 0 01 127 | Issue Number | Numeric | 0 | 0 | 16 | Numeric | 0 | 5 |
| 0 01 128 | Local Identifier (Character) | CCITT IA5 | 0 | 0 | 128 | Character | 0 | 16 |

Add entries in BUFR/CREX Table D.

Category 01 – Location and identification sequences

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME | ELEMENT DESCRIPTION |
| --- | --- | --- | --- |
| F X Y |  |  |  |
|  |  | (WIGOS Identifier) |  |
| 3 01 150 | 0 01 125 | WIGOS Identifier Series |  |
|  | 0 01 126 | Issuer of Identifier |  |
|  | 0 01 127 | Issue Number |  |
|  | 0 01 128 | Local Identifier (Character) |  |

For reference:

Structure of the new station identifier

| int.wmo.wigos | WIGOS unique identifier | WIGOS supplementary identifier |
| --- | --- | --- |

Figure 1. Structure of a full WIGOS identifier

The first component of the WIGOS identifier (int.wmo.wigos) allows the identifier to be recognized as a WIGOS identifier when used in contexts where it may be ambiguous as to what type of identifier is being used.  This is optional and need not be represented in BUFR, because the entries for the WIGOS unique identifier provide this information.

The second component (WIGOS unique identifier) is the component of the WIGOS identifier that uniquely identifies an entity.  Within a WIGOS context it is the only component of the WIGOS identifier that is always required.

The final component of the WIGOS identifier (WIGOS supplementary identifier) is optional and is used to associate identifiers issued using other systems to be associated with the WIGOS unique identifier. A single WIGOS unique identifier may be associated with many WIGOS supplementary identifiers (such as an observing site that is used for both synoptic and aviation reporting), and a WIGOS supplementary identifier may be associated with many WIGOS unique identifiers (such as a World Weather Watch drifting buoy identifier that has been issued to many drifting buoys).  In BUFR, this would be specified through a specific table entry (such as IIiii for World Weather Watch station identifier).

The WIGOS Unique Identifier is described in more detail as follows.

| WIGOS Identifier series | Issuer of Identifier | Issue Number | Local Identifier |
| --- | --- | --- | --- |

Figure 2. Structure of WIGOS identifier

Use of the components of the WIGOS identifier is given in Table 1.

| Component | Description | Initial Range – series 0 (Stations) See Note 1 | Initial Range – series 1 (Instruments) See Note 1 |
| --- | --- | --- | --- |
| WIGOS Identifier Series | This is used to distinguish between different systems for allocating identifiers. It allows future expansion of the system so that entities do not have to be issued with new identifiers if the structure of the WIGOS identifiers proves unable to meet future requirements. Different values of the WIGOS Identifier Series may correspond to different structures of the WIGOS identifier. Initial permitted range: 0-3 | 0 (0 – 3) | 1 (0 – 3) |
| Issuer of Identifier | A number that is used to distinguish between identifiers issued by different organizations | 0-1023 See note 2 | 0-1023 See note 2 |
| Issue Number | An identifier that an organization responsible for issuing an identifier may use to ensure global uniqueness of its identifiers. For example, allocating one issue number for hydrological stations and another for voluntary climate observing stations would enable the managers of the two networks to issue Local Identifiers independently without needing to check with each other that they were not duplicating identifiers. | 0-1023 See Note 3 | 0-1023 See Note 3 |
| Local Identifier | This is the individual identifier issued for each entity. An organization issuing identifiers must ensure that the combination of Issue Number and Local Identifier is unique; in that way global uniqueness is guaranteed. | 10 characters See Note 4 | 10 characters See Note 4 |

Notes:

(1)	Although the table proposes initial ranges of permitted values of the components that make up a WIGOS identifier, future changes in requirements may result in these ranges being increased. IT systems must, therefore, be designed to process identifiers whose components are of arbitrary length. BUFR encodings will need to be prepared for WIGOS identifiers to allow efficient representation and these may use code lists to represent components of the WIGOS identifier that are shared by many entities.  Currently, station identifier = 0, instrument identifier = 1.

(2)	For instruments, the “Issuer of Identifier” corresponds to the manufacturer of the instrument.

(3)	For instruments, the “Issue Number” corresponds to the manufacturer’s model identifier for the instrument.

(4)	For instruments, the “Local Identifier” corresponds to the manufacturer’s serial number/
identifier of the instrument.

[END OF ANNEX TO THE REPORT]

[NEW PROPOSALS THROUGH PFC]

The following lists new amendments proposed through the practice between meetings of IPET-DRMM.

- 2014-01(PFC-2)/New entries in GRIB Code table 1.3 for UERRA [FT2015-1/valid from 6 May 2015]

Add new entries:

GRIB Code table 1.3

8			Uncertainties in ensembles of regional reanalysis project (UERRA)

9			Uncertainties in ensembles of regional reanalysis project (UERRA) test

- 2014-02(PFC-2)/New entries in GRIB Code table 4.2 for freezing precipitation and hybrid scan reflectivity [FT2015-1/valid from 6 May 2015]

Add new entries:

GRIB Code table 4.2, discipline 0, category 1

95	Freezing or frozen precipitation rate	kg m–2 s–1

GRIB Code table 4.2, discipline 0, category 15

15	Hybrid scan reflectivity					dB

16			Hybrid scan reflectivity height			m

- 2014-03(PFC-2)/New entries in GRIB Code table 4.2 for ICON Model [FT2015-1/valid from 6 May 2015]

Add new entries:

Product discipline 0 – Meteorological products, parameter category 1: moisture

| Number | Parameter | Unit | Remarks |
| --- | --- | --- | --- |
| 96 | Mass density of rain | kg m–3 | Mass of particles per unit volume of air |
| 97 | Mass density of snow | kg m–3 |  |
| 98 | Mass density of graupel | kg m–3 |  |
| 99 | Mass density of hail | kg m–3 |  |
| 100 | Specific number concentration of rain | kg–1 | Number of particles per unit mass of air |
| 101 | Specific number concentration of snow | kg–1 |  |
| 102 | Specific number concentration of graupel | kg–1 |  |
| 103 | Specific number concentration of hail | kg–1 |  |
| 104 | Number density of rain | m–3 | Number of particles per unit volume of air |
| 105 | Number density of snow | m–3 |  |
| 106 | Number density of graupel | m–3 |  |
| 107 | Number density of hail | m–3 |  |

Product discipline 0 – Meteorological products, parameter category 6: cloud

| Number | Parameter | Unit | Remarks |
| --- | --- | --- | --- |
| 38 | Mass density of cloud droplets | kg m–3 | Mass of particles per unit volume of air |
| 39 | Mass density of cloud ice | kg m–3 |  |

COMMON CODE TABLE C–14:	Atmospheric chemical or physical constituent type

Code figure	Meaning		Chemical formula

62025		Volcanic ash	-

- 2014-52(PFC-2)/New entries for radiosondes of Republic of Korea in Common Code table C-2 [FT2015-1/valid from 6 May 2015]

Amend entries:

Common Code table C-2, 12/112 and 20-21/120-121

Date of	Code figure for	Code figure for

assignment of	rara	BUFR

number (necessary	(Code table	(Code table

after 30/06/2007)	3685)	 0 02 011)

(06/05/2015)	12	112	Jin Yang RSG-20A with derived pressure from GPS
 				height/GL-5000P (Republic of Korea)

20	120	Not vacant

(06/05/2015)	21	121	Jin Yang 1524LA LORAN-C/GL5000 (Republic of 
				Korea)

- 2014-53(PFC-2)/New entries for radiosondes of Russian Federation in Common Code table C-2 [FT2015-1/valid from 6 May 2015]

Amend entries:

Common Code table C-2, 53-59/153-159, 60/160 and 62-66/162-166

Date of	Code figure for	Code figure for

assignment of	rara	BUFR

number (necessary	(Code table	(Code table

after 30/06/2007)	3685)	 0 02 011)

(06/05/2015)	53	153	AVK - I-2012 (Russian Federation)

54-59	154-159	Not vacant

(06/05/2015)	60	160	MARL-A or Vektor-M - I-2012 (Russian Federation)

(06/05/2015)	62	162	MARL-A or Vektor-M - MRZ-3MK (Russian 
				Federation)

63-66	163-166	Not vacant

- 2014-54(PFC-2)/New entries for COSMIC satellite in Common Code table C-5 [FT2015-1/valid from 6 May 2015]

Add new entries:

Common Code table C-5

Code figure for	Code figure for

Code figure for	BUFR	GRIB

I6I6I6   	(Code table 0 01 007)	Edition 2

724	724	724	COSMIC-2 P1

725	725	725	COSMIC-2 P2

726	726	726	COSMIC-2 P3

727	727	727	COSMIC-2 P4

728	728	728	COSMIC-2 P5

729	729	729	COSMIC-2 P6

750	750	750	COSMIC-2 E1

751	751	751	COSMIC-2 E2

752	752	752	COSMIC-2 E3

753	753	753	COSMIC-2 E4

754	754	754	COSMIC-2 E5

755	755	755	COSMIC-2 E6

- 2015-51(minor adjustment)/New entries for originating centres of Canada in Common Code tables C-1 and C-11 [FT2015-1/valid from 6 May 2015]

Add a new entry and modify an existing entry:

| CREX Edition 2 B 01 035 (5 characters) and Group 3 in Section 1 | GRIB Edition 2 Octets 6–7 in Section 1 BUFR Edition 4 0 01 035 (16 bits) and Octets 5–6 in Section 1 |  |
| --- | --- | --- |
| 00053 | 53 | MSC Monitoring |
| 00054 | 54 | Montreal RSMC |

- 2015-52(minor adjustment)/New entries for satellites and instruments in Common Code table C-5 and C-8 [FT2015-1/valid from 6 May 2015]

Add new entries:

Common Code table C-5

| Code figure for I6I6I6 | Code figure for BUFR (Code table 0 01 007) | Code figure for GRIB Edition 2 |  |
| --- | --- | --- | --- |
| 289 | 289 | 289 | Orbiting Carbon Observatory - 2 (OCO-2, NASA) |
| 502 | 502 | 502 | Hai Yang 2A (HY-2A, SOA/NSOAS China) |
| 801 | 801 | 801 | International Space Station (ISS) |

Add new entries:

Common Code table C-8

| Code | Agency | Type | Instrument short name | Instrument long name |
| --- | --- | --- | --- | --- |
| 314 | NASA | Radar | RapidScat | RapidScat scatterometer |
| 432 | NASA | Spectrometer | OCO | Orbiting carbon observatory |
| 686 | SOA | Scatterometer | SCAT | Scatterometer |
| 687 | SOA | Radar altimeter | ALT | Radar altimeter |
| 688 | SOA | Microwave radiometer | MWI | Microwave radiometer |
| 956 | CMA | Spectrometer | SBUS | Solar Backscatter Ultraviolet Sounder |
| 957 | CMA | Spectrometer | TOU | Total Ozone Unit |

- 2015-53(minor adjustment)/New entries for satellite instruments in Common Code table C-8 [FT2015-1/valid from 6 May 2015]

Add new entries:

Common Code table C-8

| Code | Agency | Type | Instrument short name | Instrument long name |
| --- | --- | --- | --- | --- |
| 956 | CMA |  | SBUS | Solar Backscatter Ultraviolet Sounder |
| 957 | CMA |  | TOU | Total Ozone Unit |

[REVISIONS AND ADDITIONS IN RELATION TO IPET-DRMM-II]

The following lists amendments revised or additionally proposed in relation to the IPET-DRMM-II for approval.

Some amendments editorially corrected may not be shown here, e.g. center to centre, sea surface to sea-surface, dew point to dewpoint.

- REV2014-2.2.1(DRMM-II) [FT2015-2/pre-operational option/valid from 4 November 2015] <initial version>

Add new entries:

Code table 4.2

| Parameter | Product discipline | Parameter category | Parameter number | Units |
| --- | --- | --- | --- | --- |
| Brightness temperature | 0 | 5 | 7 | K |
| Soil volumetric ice content (water equivalent) (see note) | 2 | 0 | 38 | m3 m–3 |
| Liquid water in snow pack | 2 | 3 | 23 | kg m–2 |
| Glacier temperature | 2 | New category: 5 (Glaciers and inland ice) | 1 | K |

Note: For parameter 38 (Parameter category 0), ice volume is expressed as if the ice content were melted to liquid water and then its volume measured in the liquid state. This may be understood in the same manner as water equivalent snow depth.

Code Table 4.5

| Code Figure | Meaning | Unit |
| --- | --- | --- |
| 174 | Top surface of ice on sea, lake or river | none |
| 175 | Top surface of ice, under snow cover, on sea, lake or river | none |
| 176 | Bottom surface (underside) ice on sea, lake or river | none |
| 177 | Deep soil (of indefinite depth) | none |
| 178 | Reserved |  |
| 179 | Top surface of glacier ice and inland ice | none |
| 180 | Deep inland or glacier ice (of indefinite depth) | none |
| 181 | Grid tile land fraction as a model surface | none |
| 182 | Grid tile water fraction as a model surface | none |
| 183 | Grid tile ice fraction on sea, lake or river as a model surface | none |
| 184 | Grid tile glacier ice and inland ice fraction as a model surface | none |

- REV2014-2.2.4(DRMM-II) [FT2015-1/valid from 6 May 2015 ] <initial version>

Add a new template:

Product definition template 4.57 - analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function

| Octet No. | Contents |
| --- | --- |
| 10 | Parameter category (see Code table 4.1) |
| 11 | Parameter number (see Code table 4.2) |
| 12–13 | Atmospheric chemical constituent type (see Code table 4.230) |
| 14–15 | Number of mode (N) of distribution (see Note 2) |
| 16–17 | Mode number (l) |
| 18–19 | Type of distribution function (see Code table 4.240) |
| 20 | Number of following function parameters (Np), defined by type given in octet 18–19 (Type of distribution function) |
|  | Repeat the following 5 octets for the number of function parameters (n = 1,Np), if Np > 0 |
| 21+5(n-1) | List of scale factor of fixed distribution function parameter (p1–pNp)), defined by type of distribution in octet 18-19 |
| (22+5(n-1))– (25+5(n-1)) | List of scaled value of fixed distribution function parameter (p1–pNp)), defined by type of distribution in octet 18-19 |
| 21+5Np | Type of generating process (see Code table 4.3) |
| 22+5Np | Background generating process identifier (defined by originating centre) |
| 23+5Np | Analysis or forecast generating process identifier (defined by originating centre) |
| (24+5Np)– (25+5Np) | Hours of observational data cut-off after reference time (see Note 1) |
| 26+5Np | Minutes of observational data cut-off after reference time |
| 27+5Np | Indicator of unit of time range (see Code table 4.4) |
| (28+5Np)– (31+5Np) | Forecast time in units defined by the previous octet |
| 32+5Np | Type of first fixed surface (see Code table 4.5) |
| 33+5Np | Scale factor of first fixed surface |
| (34+5Np)– (37+5Np) | Scaled value of first fixed surface |
| 38+5Np | Type of second fixed surface (see Code table 4.5) |
| 39+5Np | Scale factor of second fixed surface |
| (40+5Np)– (43+5Np) | Scaled value of second fixed surface |

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	If Number of mode (N) > 1, then between x*N fields with mode number l = 1, …, N define the distribution function.  x is the number of variable parameters in the distribution function.

(3)	For more information, see Attachment III (Distribution functions in GRIB) in Part B of this volume (I.2 – Att.III/GRIB – 1 to x).

Add a new entry:

Code table 4.0 – Product definition template number

| Code figure | Meaning |
| --- | --- |
| 57 | Analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function |

Add a new code table:

Code table 4.240 – Type of distribution function

| Code figure | Meaning |
| --- | --- |
| 0 | No specific distribution function given |
| 1 | Delta functions with spatially variable concentration and fixed diameters Dl (p1) in meter (see Note 1) |
| 2 | Delta functions with spatially variable concentration and fixed masses Ml (p1) in kg (see Note 2) |
| 3 | Gaussian (Normal) distribution with spatially variable concentration and fixed mean diameter Dl (p1) and variance σ (p2) (see Note 3) |
| 4 | Gaussian (Normal) distribution with spatially variable concentration, mean diameter and variance (see Note 4) |
| 5 | Log-normal distribution with spatially variable number density, mean diameter and variance (see Note 5) |
| 6 | Log-normal distribution with spatially variable number density, mean diameter and fixed variance σ (p1) (see Note 6) |
| 7 | Log-normal distribution with spatially variable number density and mass density and fixed variance σ (p1) and fixed particle density ρ (p2) (see Note 7) |
| 8-49151 | Reserved |
| 49152–65534 | Reserved for local use |
| 65535 | Missing |

Notes:

(1)	Bin-Model or delta function with N concentrations cl(r) in class (or mode) l. 
Concentration-density function:

where

N – number of modes in the distribution

δ – delta-function

d – diameter

Dl –diameter of mode l (p1)

(2)	Bin-Model or delta function with N concentrations cl(r) in class (or mode) l. 
Concentration-density function:

where 
N – number of modes in the distribution
δ – delta-function
m – mass
Ml –mass of mode l (p1)

(3)	N-modal concentration-density function consisting of Gaussian-functions:

where
N – number of modes in the distribution
d – diameter
Dl –mean diameter of mode l (p1)
σl – variance of mode l (p2)

with N fields of concentration cl(r).

(4)	N-modal concentration-density function consisting of Gaussian-functions:

with 3N fields of concentration cl(r), variance σl(r) and mean diameter Dl(r).

(5)	N-modal log-normal-distribution for the number density:

where 
d – diameter
	with 3N fields of number density nl(r), variance σl(r) and mean diameter Dl(r).

(6)	N-modal log-normal-distribution for the number density:

where
σl – variance of mode l (p1)
with 2N fields of number density nl(r) and mean diameter Dl(r).

(7)	N-modal log-normal-distribution for the number density as in Note (6), but with a prescribed mass density ml(r), from which the diameter Dl(r) is calculated by:

where
σl – variance of mode l (p1)

ρp,l – particle density (p2)

with 2N fields of number density nl(r)  and mass density ml(r).

Add a new attachment:

ATTACHMENT III

Distribution functions in GRIB

Goal: representation of fields, that depends not only on space and time, but also on an additional continuous parameter, e.g. diameter d or particle mass m. Such fields at the end are (density) distribution functions f(x, y, z, t; d)  f(r, t; d). They describe e.g. the distribution of particles with different particle sizes in the air. For simplicity, the time variable t is omitted in the following; in GRIB this would be superfluous because times are noted in the PDS (product definition section).

Furthermore, this is an attempt to describe unimodal and multimodal distribution functions in a common GRIB2-framework.

A GRIB file contains one or several fields, which describe the distribution function (concentrations, number densities, ...).  The purpose of the GRIB template 4.57–analysis or forecast at a horizontal level or in a horizontal layer at a point in time for atmospheric chemical constituents based on a distribution function is to enable the user to calculate additional interesting variables (mostly integrals) from these fields, if the user knows the underlying distribution function.  Examples are the mass density of cloud droplets

(1.1)

(with the density of water ρw = 1000 kg/m3) or the radar reflectivity of rain droplet distributions

(1.2)

These are examples of distribution functions:

1.	bin-model with concentrations  in the class (or mode) l.  A concentration distribution function is described by 

 	 	(1.3)

In this model, the numbers  for the diameter in these N classes are fixed and prescribed. 
Area of application: bin-models in the cloud microphysics, volcanic ash, ...

2.	N-modal concentration distribution function, composed by a Gaussian functions

 	 	(1.4)

Again, N concentrations  must be stored. The N modes are defined by fixed values for diameter  and width .

3.	N-modal concentration distribution function, composed by Gaussian function, whose diameter and width can vary from grid point to grid point:

     
 	 	(1.5)

Now, 3N fields ,  and  must be stored.

4.	N-modal log-normal distribution for the number density

  
 	 	(1.6)

It is described by 3N fields ,  and .

5.	N-modal log-normal distribution for the number density at fixed variance

   
 	 	(1.7)

It is described by 2N fields ,  and N fixed numbers . (therefore, )

6.	N-modal log-normal distribution for the number density at fixed variance and the prescription of number density and mass density. Again, equation (1.7) is used. However, the field  is not stored, but is expressed via

  
 	  	(1.8)

by the mass density .
It is described by 2N fields number density  and mass density , N values  and N values for the particle densities .
 
(C. Hoose (2004) master thesis, Univ. Karlsruhe)
Application area: aerosol fields

7.	N-modal exponential distribution function with prescribed specific mass :

 		(1.9)

with a fixed intercept-parameter  for the mode l.
For the case of spherical particles and (cloud droplets, rain droplets) the inverse length depends on the specific mass  and the air density  by 

 		

This formula also contains the density   (e.g. density of liquid water. In general this value is the same for all modes l).
 
Application area: for an exponential distribution is assumed for most cloud physics particles (cloud ice, graupel, ...)

8.	Skew Gaussian function (e.g. for temperature distributions)

 		(1.11)

with 3 fields , , . The ’left-sided’ and ’right-sided’ variances  have the same physical dimension (temperature). To distinguish them, it is recommended to define two different GRIB-elements.  and  are appropriate norms (not given here).

9. . .

Though there is an extremely large amount of possible functional forms of distribution functions, in practice, only a few are used.  However, the shown examples indicate that even for the same underlying distribution function, the parameters and fields that are prescribed or derived by others, as well as the independent variable, can differ significantly. In these examples this was the diameter d, the particle mass m could be another. Consequently, this list can become quite large during the lifetime of GRIB2. In the end, this GRIB template is an attempt to deliver a minimum of order together with complete information for users of GRIB data.

- REV2014-3.1.4(DRMM-II) [CBS session/General Summary 2.3(1).12-13 ] <initial version>

Reporting zero snow depth

2.3(1).12	Groundbased snow observations are important for monitoring, model validation, validation of satellite-derived data, and increasingly for assimilation into numerical weather prediction models. The Commission noted, however, snow depth is generally reported only when snow is present and this leads to an ambiguity in that users cannot distinguish between missing snow depth data meaning no snow or meaning no observation due to a technical problem at the station, for instance an instrument failure or system outage. This has been identified as an issue by the Global Cryosphere Watch (GCW) Snow Watch initiative.

2.3(1).13	Explicit reporting of zero snow depth is standard practice in TDCF but is not possible in Traditional Alphanumeric Codes (TAC). The Commission had already decided that the TAC should not be changed, but recognized that the TAC are often used for collecting observations nationally. The Commission agreed to facilitate reporting zero snow depth by suggesting that those Members using TAC nationally might consider using the unallocated entry 000 of code table 3889 to indicate zero snow depth, so that the information is available when national reports are converted to TDCF.

- REV2014-3.2.5(DRMM-II) [FT2014-2/pre-operational option/valid from 5 November 2014] <initial version>

Add new entries:

BUFR Table D

|  | (SARAL Altika) |
| --- | --- |
| 3 40 011 | 0 01 007 | Satellite identifier |  |
|  | 0 02 019 | Satellite instruments |  |
|  | 0 01 096 | Station acquisition |  |
|  | 0 25 061 | Software identification and version number |  |
|  | 0 05 044 | Satellite cycle number |  |
|  | 0 05 040 | Orbit number |  |
|  | 0 01 030 | Numerical model identifier |  |
|  | 0 04 001 | Year |  |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day |  |
|  | 0 04 004 | Hour |  |
|  | 0 04 005 | Minute |  |
|  | 0 04 007 | Seconds within a minute (microsecond accuracy) |  |
|  | 0 05 001 | Latitude (high accuracy) |  |
|  | 0 06 001 | Longitude (high accuracy) |  |
|  | 0 08 029 | Surface type |  |
|  | 0 08 077 | Radiometer sensed surface type |  |
|  | 0 40 011 | Interpolation flag |  |
|  | 0 25 097 | Three-dimensional error estimate of the navigator orbit |  |
|  | 0 25 112 | Band specific altimeter data quality flag |  |
|  | 0 25 113 | Band specific altimeter correction quality flag |  |
|  | 0 21 148 | Trailing edge variation flag |  |
|  | 0 21 169 | Ice presence indicator |  |
|  | 0 40 024 | Meteorological map availability |  |
|  | 0 40 025 | Interpolation flag for mean diurnal tide |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 22 189 | Specific band ocean range |  |
|  | 0 22 191 | RMS of specific band ocean range |  |
|  | 0 22 130 | Number of valid points for specific band |  |
|  | 0 25 167 | Specific band net instrumental correction |  |
|  | 0 25 166 | Sea state bias correction on specific band |  |
|  | 0 22 190 | Specific band significant wave height |  |
|  | 0 22 131 | RMS specific band significant wave height |  |
|  | 0 22 132 | Number of valid points for specific band significant wave height |  |
|  | 0 22 133 | Specific band net instrument correction for significant wave height |  |
|  | 0 21 183 | Specific band corrected ocean backscatter coefficient |  |
|  | 0 21 184 | STD specific band corrected ocean backscatter coefficient |  |
|  | 0 22 134 | Number of valid points for specific band backscatter |  |
|  | 0 21 185 | Specific band net instrumental correction for agc |  |
|  | 0 21 118 | Attenuation correction on sigma-0 |  |
|  | 0 21 186 | Specific band automatic gain control |  |
|  | 0 21 187 | RMS specific band automatic gain control |  |
|  | 0 21 188 | Number of valid points for specific band automatic gain control |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 12 063 | Brightness temperature |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 12 063 | Brightness temperature |  |
|  | 0 13 090 | Radiometer water vapour content |  |
|  | 0 13 160 | Radiometer liquid content |  |
|  | 0 07 002 | Height or altitude |  |
|  | 0 11 097 | Wind speed from altimeter |  |
|  | 0 07 002 | Height or altitude |  |
|  | 0 11 095 | u-component of the model wind vector |  |
|  | 0 11 096 | v-component of the model wind vector |  |
|  | 0 10 096 | Mean dynamic topography |  |
|  | 0 10 081 | Altitude of COG above reference ellipsoid |  |
|  | 0 10 082 | Instantaneous altitude rate |  |
|  | 0 10 083 | Squared off-nadir angle of the satellite from platform data |  |
|  | 0 10 101 | Squared off-nadir angle of the satellite from waveform data |  |
|  | 0 02 153 | Satellite channel centre frequency |  |
|  | 0 25 165 | Ionospheric correction from model on specific band |  |
|  | 0 25 126 | Model dry tropospheric correction |  |
|  | 0 25 128 | Model wet tropospheric correction |  |
|  | 0 25 164 | Radiometer wet tropospheric correction |  |
|  | 0 10 085 | Mean sea-surface height |  |
|  | 0 10 086 | Geoid's height |  |
|  | 0 10 087 | Ocean depth/land elevation |  |
|  | 0 10 092 | Solid Earth tide height |  |
|  | 0 10 088 | Total geocentric ocean tide height (solution 1) |  |
|  | 0 10 089 | Total geocentric ocean tide height (solution 2) |  |
|  | 0 10 098 | Loading tide height geocentric ocean tide solution 1 |  |
|  | 0 10 099 | Loading tide height geocentric ocean tide solution 2 |  |
|  | 0 10 090 | Long period tide height |  |
|  | 0 10 100 | Non-equilibrium long period tide height |  |
|  | 0 10 093 | Geocentric pole tide height |  |
|  | 0 25 127 | Inverted barometer correction |  |
|  | 0 40 014 | High-frequency fluctuations of the sea-surface topography correction |  |
|  | 0 10 102 | Sea-surface height anomaly |  |

BUFR/CREX Table B

| F X Y | Element Name | BUFR Units | BUFR Scale | BUFR Ref. | BUFR Width | CREX Units | CREX Scale | CREX Width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 13 160 | Radiometer liquid content | kg m–2 | 2 | –350 | 10 | kg m–2 | 2 | 3 |
| 0 21 148 | Trailing edge variation flag | Flag table | 0 | 0 | 9 | Flag table | 0 | 3 |
| 0 21 183 | Specific band corrected ocean backscatter coefficient | dB | 2 | –32768 | 16 | dB | 2 | 5 |
| 0 21 184 | STD specific band corrected ocean backscatter coefficient | dB | 2 | –32768 | 16 | dB | 2 | 5 |
| 0 21 185 | Specific band net instrumental correction for agc | dB | 2 | –2048 | 12 | dB | 2 | 4 |
| 0 21 186 | Specific band automatic gain control | dB | 2 | 0 | 13 | dB | 2 | 4 |
| 0 21 187 | RMS specific band automatic gain control | dB | 2 | 0 | 8 | dB | 2 | 3 |
| 0 21 188 | Number of valid points for specific band automatic gain control | Numeric | 0 | 0 | 7 | Numeric | 0 | 3 |
| 0 22 130 | Number of valid points for specific band | Numeric | 0 | 0 | 10 | Numeric | 0 | 4 |
| 0 22 131 | RMS specific band significant wave height | m | 3 | 0 | 16 | m | 3 | 5 |
| 0 22 132 | Number of valid points for specific band significant wave height | Numeric | 0 | 0 | 10 | Numeric | 0 | 4 |
| 0 22 133 | Specific band net instrument correction for significant wave height | m | 3 | –1000 | 11 | m | 3 | 4 |
| 0 22 134 | Number of valid points for specific band backscatter | Numeric | 0 | 0 | 10 | Numeric | 0 | 4 |
| 0 22 189 | Specific band ocean range | m | 3 | 0 | 31 | m | 3 | 10 |
| 0 22 190 | Specific band significant wave height | m | 3 | 0 | 16 | m | 3 | 5 |
| 0 22 191 | RMS of specific band ocean range | m | 4 | 0 | 16 | m | 4 | 5 |
| 0 25 112 | Band specific altimeter data quality flag | Flag table | 0 | 0 | 9 | Flag table | 0 | 3 |
| 0 25 113 | Band specific altimeter correction quality flag | Flag table | 0 | 0 | 9 | Flag table | 0 | 3 |
| 0 25 165 | Ionospheric correction from model on specific band | m | 4 | –32768 | 16 | m | 4 | 5 |
| 0 25 166 | Sea state bias correction on specific band | m | 4 | –32768 | 16 | m | 4 | 5 |
| 0 25 167 | Specific band net instrumental correction | m | 4 | –120000 | 18 | m | 4 | 6 |

BUFR/CREX Flag tables

| 0 21 148 |
| --- |
| Trailing edge variation flag Bit No. |
| 1 | Non short scale variation |
| 2 | Short scale variation |
| 3–8 | Reserved |
| All 9 | Missing value |

| 0 25 112 |
| --- |
| Band specific altimeter data quality flag Bit No. (0 is good, 1 is bad) |
| 1 | Band specific range |
| 2 | Band specific significant wave height |
| 3 | Band specific backscatter coefficient |
| 4 | Off nadir angle from band specific waveform parameters |
| 5 | Off nadir angle from platform |
| 6–8 | Reserved |
| All 9 | Missing value |

| 0 25 113 |
| --- |
| Band specific altimeter correction quality flag Bit No. (0 is good, 1 is bad) |
| 1 | Band specific range instrumental correction |
| 2 | Band specific significant wave height instrumental correction |
| 3 | Band specific backscatter coefficient instrumental correction |
| 4–8 | Reserved |
| All 9 | Missing value |

- ADD2014-01(DRMM-II) [FT2014-2/valid from 5 November 2014]

Add new entries:

BUFR Table D

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME | ELEMENT DESCRIPTION |
| --- | --- | --- | --- |
| F X Y |  |  |  |
|  |  | (Monthly values from a land station in compliance with regional or national reporting practices) |  |
| 3 07 076 | 3 01 090 | Surface station identification; time, horizontal and vertical coordinates |  |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 023 | Time period or displacement | Number of days in the month |
|  |  | Monthly mean values of pressure, temperature, extreme temperatures and vapour pressure |  |
|  | 0 08 023 | First-order statistics | = 4 Mean value |
|  | 0 10 004 | Pressure |  |
|  | 0 10 051 | Pressure reduced to mean sea level |  |
|  | 0 07 004 | Pressure | Standard level ¦ Set to missing for lowland stations |
|  | 0 10 009 | Geopotential height | Standard level ¦ Set to missing for lowland stations |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 12 101 | Temperature/air temperature |  |
|  | 0 02 051 | Indicator to specify observing method for extreme temperatures |  |
|  | 0 04 051 | Principal time of daily reading of maximum temperature |  |
|  | 0 12 118 | Maximum temperature at height specified, past 24 hours |  |
|  | 0 04 052 | Principal time of daily reading of minimum temperature |  |
|  | 0 12 119 | Minimum temperature at height specified, past 24 hours |  |
|  | 0 13 004 | Vapour pressure |  |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  | 0 12 151 | Standard deviation of daily mean temperature |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  | Number of days for which values are missing |  |
|  | 1 02 005 | Replicate 2 descriptors 5 times |  |
|  | 0 08 050 | Qualifier for number of missing values in calculation of statistic | = 1 Pressure, = 2 Temperature, = 4 Vapour pressure, = 7 Maximum temperature, = 8 Minimum temperature |
|  | 0 08 020 | Total number of missing entities (with respect to accumulation or average) | Days |
|  |  | Sunshine duration |  |
|  | 0 14 032 | Total sunshine |  |
|  | 0 14 033 | Total sunshine |  |
|  | 0 08 050 | Qualifier for number of missing values in calculation of statistic | = 6 Sunshine duration |
|  | 0 08 020 | Total number of missing entities (with respect to accumulation or average) | Days |
|  |  | Number of days of occurrence |  |
|  | 1 02 018 | Replicate 2 descriptors 18 times |  |
|  | 0 08 052 | Condition for which number of days of occurrence follows for: wind ≥ 10 m/s, wind ≥ 20 m/s, wind ≥ 30 m/s, maximum temperature < 273.15 K, maximum temperature ≥ 298.15 K, maximum temperature ≥ 303.15 K, maximum temperature ≥ 308.15 K, maximum temperature ≥ 313.15 K, minimum temperature < 273.15 K, sss > 0.00 m, sss > 0.01 m, sss > 0.10 m, sss > 0.50 m, horizontal visibility < 50 m, horizontal visibility < 100 m, horizontal visibility < 1000 m, hail, thunderstorm |  |
|  | 0 08 022 | Total number (with respect to accumulation or average) | Days |
|  |  | Occurrence of extreme values of temperature and wind speed |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 08 053 | Day of occurrence qualifier | = 0 On 1 day only, = 1 On 2 or more days |
|  | 0 04 003 | Day |  |
|  | 0 12 152 | Highest daily mean temperature |  |
|  | 0 08 053 | Day of occurrence qualifier | = 0 On 1 day only, = 1 On 2 or more days |
|  | 0 04 003 | Day |  |
|  | 0 12 153 | Lowest daily mean temperature |  |
|  | 0 08 053 | Day of occurrence qualifier | = 0 On 1 day only, = 1 On 2 or more days |
|  | 0 04 003 | Day |  |
|  | 0 08 023 | First-order statistics | = 2 Maximum value |
|  | 0 12 101 | Temperature/air temperature |  |
|  | 0 08 053 | Day of occurrence qualifier | = 0 On 1 day only, = 1 On 2 or more days |
|  | 0 04 003 | Day |  |
|  | 0 08 023 | First-order statistics | = 3 Minimum value |
|  | 0 12 101 | Temperature/air temperature |  |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 02 002 | Type of instrumentation for wind measurement |  |
|  | 0 08 053 | Day of occurrence qualifier | = 0 On 1 day only, = 1 On 2 or more days |
|  | 0 04 003 | Day |  |
|  | 0 11 046 | Maximum instantaneous wind speed |  |
|  | 0 08 053 | Day of occurrence qualifier | Set to missing (cancel) |
|  |  | Precipitation |  |
|  | 0 04 003 | Day | = 1 |
|  | 0 04 004 | Hour | = 0 |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 023 | Time period or displacement | Number of days in the month |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 13 060 | Total accumulated precipitation |  |
|  | 0 13 051 | Frequency group, precipitation |  |
|  | 0 04 053 | Number of days with precipitation equal to or more than 1 mm |  |
|  | 0 08 050 | Qualifier for number of missing values in calculation of statistic | = 5 Precipitation |
|  | 0 08 020 | Total number of missing entities (with respect to accumulation or average) | Days |
|  |  | Numbers of days of occurrence |  |
|  | 1 02 006 | Replicate 2 descriptors 6 times |  |
|  | 0 08 052 | Condition for which number of days of occurrence follows |  |
|  | 0 08 022 | Total number (with respect to accumulation or average) | Days |
|  |  | Occurrence of extreme precipitation |  |
|  | 0 08 053 | Day of occurrence qualifier | = 0 On 1 day only, = 1 On 2 or more days |
|  | 0 04 003 | Day |  |
|  | 0 13 052 | Highest daily amount of precipitation |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  | (Monthly normals for a land station in compliance with regional or national reporting practices) |  |
| 3 07 077 | 0 04 001 | Year | Beginning of the reference period |
|  | 0 04 001 | Year | Ending of the reference period |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day | = 1 |
|  | 0 04 004 | Hour | = 0 |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 022 | Time period or displacement | = 1 |
|  | 0 08 023 | First-order statistics | = 4 Mean value |
|  | 0 10 004 | Pressure |  |
|  | 0 10 051 | Pressure reduced to mean sea level |  |
|  | 0 07 004 | Pressure | Standard level |
|  | 0 10 009 | Geopotential height | Standard level |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 12 101 | Temperature/air temperature |  |
|  | 0 02 051 | Indicator to specify observing method for extreme temperatures |  |
|  | 0 04 051 | Principal time of daily reading of maximum temperature |  |
|  | 0 12 118 | Maximum temperature at height specified, past 24 hours |  |
|  | 0 04 052 | Principal time of daily reading of minimum temperature |  |
|  | 0 12 119 | Minimum temperature at height specified, past 24 hours |  |
|  | 0 13 004 | Vapour pressure |  |
|  | 0 12 151 | Standard deviation of daily mean temperature |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  | 0 14 032 | Total sunshine |  |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  |  | Normals of precipitation |  |
|  | 0 04 001 | Year | Beginning of the reference period |
|  | 0 04 001 | Year | Ending of the reference period |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day | = 1 |
|  | 0 04 004 | Hour | = 0 |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 022 | Time period or displacement | = 1 |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 08 023 | First-order statistics | = 4 Mean value |
|  | 0 13 060 | Total accumulated precipitation |  |
|  | 0 04 053 | Number of days with precipitation equal to or more than 1 mm |  |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  | 1 02 008 | Replicate 2 descriptors 8 times |  |
|  | 0 08 050 | Qualifier for number of missing values in calculation of statistic for: pressure, temperature, extreme temperatures, vapour pressure, precipitation, sunshine duration, maximum temperature, minimum temperature |  |
|  | 0 08 020 | Total number of missing entities (with respect to accumulation or average) | Years |
|  |  | (Sequence for representation of monthly values suitable for CLIMAT data in compliance with regional or national reporting practices) |  |
| 3 07 078 | 3 07 076 | Monthly values from a land station in compliance with regional or national reporting practices |  |
|  | 3 07 077 | Monthly normals for a land station in compliance with regional or national reporting practices |  |

|  |  | (Monthly values from an ocean weather station in compliance with regional or national reporting practices) |  |
| --- | --- | --- | --- |
|  |  | Station identification, date/time, horizontal and vertical coordinates |  |
| 3 08 021 | 0 01 011 | Ship or mobile land station identifier | Ship’s call sign |
|  | 0 02 001 | Type of station |  |
|  | 3 01 011 | Year, month, day |  |
|  | 3 01 012 | Hour, minute |  |
|  | 3 01 023 | Latitude/longitude (coarse accuracy) |  |
|  | 0 07 030 | Height of station ground above mean sea level |  |
|  | 0 07 031 | Height of barometer above mean sea level |  |
|  |  | Monthly mean values of pressure, temperature, vapour pressure and sea/water temperature |  |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 023 | Time period or displacement | Number of days in the month |
|  | 0 08 023 | First-order statistics | = 4 Mean value |
|  | 0 10 051 | Pressure reduced to mean sea level |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Temperature measurement |
|  | 0 07 033 | Height of sensor above water surface | Temperature measurement |
|  | 0 12 101 | Temperature/air temperature |  |
|  | 0 13 004 | Vapour pressure |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  | 0 07 033 | Height of sensor above water surface | Set to missing (cancel) |
|  | 3 02 056 | Sea/water temperature | Sea-surface temperature, method of measurement and depth below sea surface |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  |  | Precipitation |  |
|  | 0 04 003 | Day | = 1 |
|  | 0 04 004 | Hour | = 0 |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 023 | Time period or displacement | Number of days in the month |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) |  |
|  | 0 13 060 | Total accumulated precipitation |  |
|  | 0 13 051 | Frequency group, precipitation |  |
|  | 0 04 053 | Number of days with precipitation equal to or more than 1 mm |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  |  | (Monthly normals for an ocean weather station in compliance with regional or national reporting practices) |  |
|  |  | Normals of pressure, temperature, vapour pressure and sea/water temperature |  |
| 3 08 022 | 0 04 001 | Year | Beginning of the reference period |
|  | 0 04 001 | Year | Ending of the reference period |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day | = 1 |
|  | 0 04 004 | Hour | = 0 |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 022 | Time period or displacement | = 1 |
|  | 0 08 023 | First-order statistics | = 4 Mean value |
|  | 0 10 051 | Pressure reduced to mean sea level |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Temperature measurement |
|  | 0 07 033 | Height of sensor above water surface | Temperature measurement |
|  | 0 12 101 | Temperature/air temperature |  |
|  | 0 13 004 | Vapour pressure |  |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Set to missing (cancel) |
|  | 0 07 033 | Height of sensor above water surface | Set to missing (cancel) |
|  | 3 02 056 | Sea/water temperature | Sea-surface temperature, method of measurement and depth below sea surface |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  |  | Normals of precipitation |  |
|  | 0 04 001 | Year | Beginning of the reference period |
|  | 0 04 001 | Year | Ending of the reference period |
|  | 0 04 002 | Month |  |
|  | 0 04 003 | Day | = 1 |
|  | 0 04 004 | Hour | = 0 |
|  | 0 04 074 | Short time period or displacement |  |
|  | 0 04 022 | Time period or displacement | = 1 |
|  | 0 07 032 | Height of sensor above local ground (or deck of marine platform) | Precipitation measurement |
|  | 0 08 023 | First-order statistics | = 4 Mean value |
|  | 0 13 060 | Total accumulated precipitation |  |
|  | 0 04 053 | Number of days with precipitation equal to or more than 1 mm |  |
|  | 0 08 023 | First-order statistics | Set to missing (cancel) |
|  |  | (Sequence for representation of monthly values suitable for CLIMAT SHIP data in compliance with regional or national reporting practices) |  |
| 3 08 023 | 3 08 021 | Monthly values from an ocean weather station in compliance with regional or national reporting practices |  |
|  | 3 08 022 | Monthly normals for an ocean weather station in compliance with regional or national reporting practices |  |

- ADD2014-02(DRMM-II)/New entries in Common Code table C–3 [FT2014-2/valid from 5 November 2014]

Add new entries:

Common code table C–3

Code figure for	Meaning

Code figure	BUFR	Instrument

for IXIXIX	(Code table 0 22 067)	make and type	Equation Coefficients

a 	b

866	866	ALAMO, No Conductivity sensor

867	867	ALAMO, RBR Conductivity sensor

868	868	ALAMO, SBE Conductivity sensor

- ADD2014-03(DRMM-II)/New entry in Common Code table C–1 and C–11 [FT2014-2/valid from 5 November 2014]

Add a new entry:

Common Code table C–1 and C–11

Not applicable	249	249	Barcelona Dust Forecast Center

00249	249	Barcelona Dust Forecast Center

[PAST PROPOSALS UNDER VALIDATION]

FM 92 GRIB

- 2013-2.1.1(DRMM-I)/Reporting quality information in GRIB2 <para 4.1>

Add new entries to Code table 4.10:

12	Confidence index (see Note 4)

13	Quality indicator (see Note 5 and Code table 4.244)

Editorial note: the new entry 12 is also used in the 2013-03.

Add new notes to Code table 4.10:

(4)	The original data value is a non-dimensional number from 0 to 1, where 0 indicates no confidence and 1 indicates maximal confidence.

(5)	The original data value is defined by Code table 4.244.

New Code table 4.244:

Quality indicator

Code
figure	        Meaning

0		No quality information available

1	Failed

2 	Passed

- 2013-2.2.1(DRMM-I)/GRIB2 new compression method – CCSDS libaec <para 4.1>

Note: For most templates, details of the packing process are described in regulation 92.9.4

| Data Representation Template 5.42 - Grid point and spectral data - CCSDS recommended lossless compression |
| --- |
| Octet No. | Contents |
| 12 – 15 | Reference value (R) (IEEE 32-bit floating-point value) |
| 16 – 17 | Binary scale factor (E) |
| 18 – 19 | Decimal scale factor (D) |
| 20 | Number of bits required to hold the resulting scaled and referenced data values (see Note 1) |
| 21 | Type of original field values (see Code Table 5.1) |
| 22 | compression scheme version number of CCSDS 121.0-B recommended standard blue book (currently 2) (see Note 3) |
| 23 | compression options mask (see Note 3) |
| 24 | compression input/output bits per pixel (see Note 3) |
| 25 – 26 | compression input/output pixels per block (see Note 3) |
| 27 – 28 | compression input/output pixels per scan line (see Note 3) |
| 29 – 36 | length of the uncompressed grib message in octets |
| 37 – 40 | size of uncompressed data in octets |

Notes:

(1)		The intent of this template is to scale the grid point data to obtain the desired precision, if appropriate, and then subtract out reference value from the scaled field as is done using Data Representation Template 5.0.  After this, the resulting grid point field can be treated as a grayscale image and is then encoded into the CCSDS recommended standard for lossless data compression code stream format. To unpack the data field, the CCSDS recommended standard for lossless data compression code stream is decoded back into an image, and the original field is obtained from the image data as described in regulation 92.9.4 Note (4).

(2)		The Consultative Committee for Space Data Systems (CCSDS) recommended standard for lossless data compression is the standard used by space agencies for the compression of scientific data transmitted from satellites and other space instruments. CCSDS recommended standard for lossless data compression is a very fast predictive compression algorithm based on the extended-Rice algorithm. It uses Golomb-Rice codes for entropy coding. The sequence of prediction errors is divided into blocks. Each block is compressed using a two-pass algorithm. In the first pass the best coding method for the whole block is determined. In the second pass, output of the marker of the selected coding method as a side information is done along with prediction errors encoded.

The coding methods include:

  - Golomb-Rice codes of a chosen rank

  - Unary code for transformed pairs of prediction errors

  - Fixed-length natural binary code if the block is found to be incompressible

  - Signaling to the decoder empty block if all prediction errors are zeroes

(3)		 Consultative Committee for Space Data Systems: Lossless Data Compression.

CCSDS Recommendation for Space Data System Standards, 
CCSDS 121.0-B-2, Blue Book, May 2012.

| Data Template 7.42 - Grid point and spectral data - CCSDS recommended lossless compression. |
| --- |
| Octet No. | Contents |
| 6 - nn | CCSDS recommended standard for lossless data compression code stream |

Code table 5.0 – Data representation template number

| Octet No. | Contents |
| --- | --- |
| 42 | Grid point and spectral data - CCSDS recommended lossless compression. |

- 2013-2.2.5(DRMM-I)/Proposed amendments to GRIB2 Code tables 4.2, 4.3 and 4.10 
(amendments other than Code table 4.10 were implemented by FT2014-1) <para 4.1>

Add new entries:

GRIB2 Code tables 4.2

| Code Table 4.2 |
| --- |
| Product Discipline | Parameter Category | Parameter number | Parameter | Units |
| 10 | 002 | 010 | Zonal vector component of vertically integrated ice internal pressure | Pa m |
| 10 | 002 | 011 | Meridional vector component of vertically integrated ice internal pressure | Pa m |
| 10 | 002 | 012 | Compressive ice Strength | N/m |
| 10 | 191 | 3 | Days since last observation | Day |
| 0 | 191 | 3 | Days since last observation | Day |

Add new entries:

GRIB2 Code tables 4.3

Code table 4.3 – Type of generating process

| Code figure | Meaning |
| --- | --- |
| 12 | Post-processed analysis |
| 13 | Post-processed forecast |

Note:	Code figures 12 and 13 are intended in cases where code figures 0 and 2 may not be sufficient to indicate that significant post-processing has taken place on an initial analysis or forecast output.

Add new entries: [validation]

GRIB2 Code tables 4.10

Code table 4.10 – Type of statistical processing

| Code figure | Meaning |
| --- | --- |
| 12 | Confidence index |

Note:	It is expected confidence will be a non-dimensional value from 0 to 1, where 0 indicates no confidence and 1 indicates maximal confidence. This may be used, for instance (but not exclusively), in cases where one wishes to show the horizontal distribution of confidence in analyzed values of a given field.

Editorial note: the new entry 12 is also used in the 2013-01.

Delete the Note (4) in Table 4.5 and renumber the Note (5).

Amend number 9 in Product discipline 10, parameter category 2 of Table 4.2 and add a new note to the category:

9	Module of ice internal pressure*	Pa m

*	Ice internal pressure or stress (Pa m) is the integrated pressure across the vertical thickness of a layer of ice. It is produced when concentrated ice reacts to external forces such as wind and ocean currents.

- 2012-2.2.9(DRC-IV)/GRIB template for 4-D Trajectory grid definition <para 4.1>

Validate templates:

Grid definition template 3.1010 – 4-D trajectory grid definition

Octet No.	Contents

15	Shape of the Earth (see Code table 3.2)

16	Scale factor of radius of spherical Earth

17–20	Scaled value of radius of spherical Earth

21	Scale factor of major axis of oblate spheroid Earth

22–25	Scaled value of major axis of oblate spheroid Earth

26	Scale factor of minor axis of oblate spheroid Earth

27–30	Scaled value of minor axis of oblate spheroid Earth

31–32	Number of horizontal points in slice (see Note 1)

33–34	Number of vertical points in slice (see Note 1)

35–38	Di – slice horizontal grid length (see Note 2)

39–42	Dj – slice vertical grid length (see Note 2)

43–46	Pi – horizontal location of trajectory point within slice (see Note 3)

47–50	Pj – vertical location of trajectory point within slice (see Note 3)

51	Scanning mode (flags – see Flag table 3.4) (see Note 1)

52–53	NW – Number of way points (see Note 4)

54–(53+NW×24)	Waypoint descriptions to define 4-D coordinates

Waypoint descriptions:

30+(N×24+0–N×24+3)	LaN – latitude of Nth trajectory way point

30+(N×24+4–N×24+7)	LoN – longitude of Nth trajectory way point

30+(N×24+8)	Type of Nth’s trajectory way point surface (see Code table 4.5) (see
		Note 5)

30+(N×24+9)	Scale factor of Nth’s trajectory way point surface

30+(N×24+10–N×24+13)	Scaled value of Nth’s trajectory way point surface

30+(N×24+14)	Indicator of unit of time range (see Code table 4.4)

30+(N×24+15–N×24+18)	Waypoint time in units defined by octet N×24+14 (see Note 6)

30+(N×24+19–N×24+22)	Number of slices per trajectory segment (see Note 7)

30+(N×24+23)	Number of additional leading and trailing slices (see Note 8)

Notes:

(1)		Horizontal and vertical points in slice indicate orthogonal grid slice perpendicular to point along the trajectory segment. Therefore scanning mode describes scanning within single slice.

(2)	Grid lengths are in units of 10–3 m. Trajectory is always positioned in the centre of the slice.

(3)	Location of trajectory point within slice is in units of 10–3 m relative from first grid point of this slice.

(4)	Type of line for way segments is assumed to be Great Circle.

(5)	Each of waypoints can be in different types of surface coordinates. For the purpose of light transition level, point of transition can be repeated in both meters above surface and isobaric level equivalent to height reduction based on QNH valid for FIR at that moment. Waypoint can be also repeated for stopover on the trajectory with same 3-D coordinates but different waypoint time. First point of transition level or stopover description can have MISSING slices in this case.

(6)	Waypoint time is relative to reference time of data defined in Section 1.

(7)	Slices are defined as perpendicular planes which are equidistantly spaced along the trajectory segment. First slice is always located in first point of trajectory segment and last slice in last point of trajectory segment. Therefore minimum number of slices is 2, unless set to MISSING (for last point of trajectory or for transition level repeated point).

Figure 3: Example of trajectory segment with 5 slices (circles represent trajectory waypoints)

(8)	Number of leading slices is same as number of trailing slices, and represents additional slices outside the trajectory segment but within its direction using same equidistant spacing as for corresponding trajectory segment itself.

Figure 4: Example of trajectory segment with 5 slices and 1 leading and trailing slice (circles represent trajectory waypoints)

(9)	A scaled value of radius of spherical Earth, or major or minor axis of oblate spheroid Earth, is derived by applying the appropriate scale factor to the value expressed in metres.

Product definition template 4.1010 – 4-D trajectory

Octet No.	Contents

10	Parameter category (see Code table 4.1)

11	Parameter number (see Code table 4.2)

12	Type of generating process (see Code table 4.3)

13	Background generating process identifier (defined by originating centre)

14	Analysis or forecast generating process identifier (defined by originating centre)

15–16	Hours of observational data cutoff after reference time (see Note)

17	Minutes of observational data cutoff after reference time

Note: Hours greater than 65534 will be coded as 65534.

Product definition template 4.1011 – 4-D trajectory ensemble forecast, control and perturbed

Octet No.	Contents

10	Parameter category (see Code table 4.1)

11	Parameter number (see Code table 4.2)

12	Type of generating process (see Code table 4.3)

13	Background generating process identifier (defined by originating Centre)

14	Forecast generating process identifier (defined by originating Centre)

15–16	Hours after reference time of data cutoff (see Note)

17	Minutes after reference time of data cutoff

18	Type of ensemble forecast (see Code table 4.6)

19	Perturbation number

20	Number of forecasts in ensemble

Note: Hours greater than 65534 will be coded as 65534.

Product definition template 4.1015 – 4-D trajectory probability forecasts

Octet No.	Contents

10	Parameter category (see Code table 4.1)

11	Parameter number (see Code table 4.2)

12	Type of generating process (see Code table 4.3)

13	Background generating process identifier (defined by originating centre)

14	Forecast generating process identifier (defined by originating centre)

15–16	Hours after reference time of data cutoff (see Note)

17	Minutes after reference time of data cutoff

18	Forecast probability number

19	Total number of forecast probabilities

20	Probability type (see Code table 4.9)

21	Scale factor of lower limit

22–25	Scaled value of lower limit

26	Scale factor of upper limit

27–30 	Scaled value of upper limit

Note: Hours greater than 65534 will be coded as 65534.

- 2011-2.3.5(DRC-III)/GRIB template for rotated tilted Mercator projection <para 4.1>

Add new entry to Code table 3.1

Code table 3.1 - Grid definition template number

Code figure 	Meaning

11	Rotated Mercator projection

Add new Grid definition template

Product Definition Template 3.11:	Rotated Mercator projection

Octet Number(s)		Contents

15	Shape of the earth (see Code Table 3.2)

16	Scale factor of radius of spherical earth

17-20		Scaled value of radius of spherical earth

21		Scale factor of major axis of oblate spheroid earth

22-25		Scaled value of major axis of oblate spheroid earth

26		Scale factor of minor axis of oblate spheroid earth

27-30		Scaled value of minor axis of oblate spheroid earth

31-34		Ni - number of points along a parallel

35-38		Nj - number of points along a meridian

39-42		La1 - latitude of first grid point

43-46		Lo1 - longitude of first grid point

47		Resolution and component flags (see Flag Table 3.3)

48-51		LaD - Latitude(s) at which the Mercator projection intersects the Earth 						(Latitude(s) where Di and Dj are specified)

52-55		La2 - latitude of last grid point

56-59		Lo2 - longitude of last grid point

60		Scanning mode (flags - see Flag Table 3.4)

61-64		Orientation of the grid, angle between i direction on the map and the equator 
		(see Note 1)

65-68		Di - longitudinal direction grid length (see Note 2)

69-72		Dj - latitudinal direction grid length (see Note 2)

73-76		La0 - geographical latitude of the point to be brought to the origin of the 			projection, in the case of a rotation of the sphere prior to the projection

77-80		Lo0 - geographical longitude of the point to be brought to the origin of the 			projection, in the case of a rotation of the sphere prior to the projection

81-84		beta – tilting angle of the sphere around the origin point of the rotated 				sphere

85-nn		List of number of points along each meridian or parallel (These octets are 			only present for quasi-regular grids as described in notes 2 and 3 of GDT 			3.1)

Notes:

(1)	Limited to the range of 0 to 90 degrees; if the angle of orientation of the grid is neither 0 nor 	90 degrees, Di and Dj must be equal to each other.

(2)	Grid lengths are in units of 10-3 m, at the latitude specified by LaD.

(3)	A scaled value of radius of spherical Earth, or major or minor axis of oblate spheroid Earth is 	derived from applying appropriate scale factor to the value expressed in metres.

(4)	Transformation formulas from geographical (lat,lon)=(θ,λ) to projected grid point coordinates 	(x,y) :

Reverse transformation formulas from gridpoint (x,y) to (lat,lon):

Where:

- La0 is θ0

- Lo0 is λ0

- Beta is β

- x and y are metric coordinates in the i and j direction, in standard units (m). (x,y)=(0,0) corresponds to the coordinate of the reference point (La0,Lo0), provided this point is kept as the center of the grid point domain.

- the other variables are intermediate ones. More explanation can be found in the Technical Note by P. Bénard (2011), “rotated/tilted Mercator geometry in Aladin”.

- 2011-2.3.12(DRC-III)/Space Weather in GRIB2 <para 4.1>

Rename Code table 3.2 as “Shape of the reference system” and add the following new entries

Code table 3.2 – Shape of the reference system

Code figure	Meaning

10		Earth model assumed WGS84 with corrected geomagnetic coordinates (latitude and longitude) defined by Gustafsson et al., 1992

11	Sun assumed spherical with radius = 695,990,000 m (Allen, C.W., 1976 Astrophysical Quantities (3rd Ed.; London: Athlone)) and Stonyhurst latitude and longitude system with origin at the intersection of the solar central meridian (as seen from Earth) and the solar equator (Thompson, W, Coordinate systems for solar image data, A&A 449, 791–803 (2006)).

12	Sun assumed spherical with radius = 695,990,000 m (Allen, C.W., 1976 Astrophysical Quantities (3rd Ed.; London: Athlone)) and Carrington latitude and longitude system that rotates with a sidereal period of 25.38 days (Thompson, W, Coordinate systems for solar image data, A&A 449, 791–803 (2006)).

Add the following new entries to Code table 4.5

Code table 4.5 - Fixed surface types and units

Code figure	Meaning

170	Ionospheric D-region level

171	Ionospheric E-region level

172	Ionospheric F1-region level

173	Ionospheric F2-region level

In Code table 0.0, rename existing entry #3 as “Satellite remote sensing products” and add new entry #4

Code table 0.0 - Discipline of processed data in the GRIB message, number of GRIB Master
   	  table

Code figure	Meaning

3	Satellite remote sensing products

4	Space weather products

Add the following new entries to Code table 4.1

Code table 4.1 - Parameter category by product discipline

| Product Discipline 4 – Space Weather Products |
| --- |
| Category (octet 10) | Description |
| 0 | Temperature |
| 1 | Momentum |
| 2 | Charged particle mass and number |
| 3 | Electric and magnetic fields |
| 4 | Energetic particles |
| 5 | Waves |
| 6 | Solar electromagnetic emissions |
| 7 | Terrestrial electromagnetic emissions |
| 8 | Imagery |
| 9 | Ion-neutral coupling |
| 10-191 | Reserved |
| 192-254 | Reserved for local use |
| 255 | Missing |

Add the following new entries to Code table 4.2

Code table 4.2 - Parameter number by product discipline and parameter category

Product discipline 4 – Space weather products, parameter category 0: Temperature

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Temperature | K |
| 1 | Electron temperature | K |
| 2 | Proton temperature | K |
| 3 | Ion temperature | K |
| 4 | Parallel temperature | K |
| 5 | Perpendicular temperature | K |
| 6-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 1: Momentum

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Velocity magnitude (Speed) | m s-1 |
| 1 | 1st vector component of velocity (coordinate system dependent) | m s-1 |
| 2 | 2nd vector component of velocity (coordinate system dependent) | m s-1 |
| 3 | 3rd vector component of velocity (coordinate system dependent) | m s-1 |
| 4-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 2: Charged particle mass and number

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Particle number density | m-3 |
| 1 | Electron density | m-3 |
| 2 | Proton density | m-3 |
| 3 | Ion density | m-3 |
| 4 | Vertical electron content | m-2 |
| 5 | HF absorption frequency | Hz |
| 6 | HF absorption | dB |
| 9 | Spread F | m |
| 10 | h’F | m |
| 11 | Critical frequency | Hz |
| 13 | Scintillation | Numeric |
| 14-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 3: Electric and magnetic fields

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Magnetic field magnitude | T |
| 1 | 1st vector component of magnetic field | T |
| 2 | 2nd vector component of magnetic field | T |
| 3 | 3rd vector component of magnetic field | T |
| 4 | Electric field magnitude | V m-1 |
| 5 | 1st vector component of electric field | V m-1 |
| 6 | 2nd vector component of electric field | V m-1 |
| 7 | 3rd vector component of electric field | V m-1 |
| 8-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 4: Energetic particles

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Proton flux (differential) | (m2 s sr eV)-1 |
| 1 | Proton flux (integral) | (m2 s sr )-1 |
| 2 | Electron flux (differential) | (m2 s sr eV)-1 |
| 3 | Electron flux (integral) | (m2 s sr)-1 |
| 4 | Heavy ion flux (differential) | (m2 s sr eV/nuc)-1 |
| 5 | Heavy ion flux (integral) | (m2 s sr)-1 |
| 6 | Cosmic ray neutron flux | h-1 |
| 7-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 5: Waves

| Number | Parameter | Units |
| --- | --- | --- |
| 0-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 6: Solar electromagnetic emissions

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Integrated Solar Irradiance | W m-2 |
| 1 | Solar X-ray Flux (XRS Long) | W m-2 |
| 2 | Solar X-ray Flux (XRS Short) | W m-2 |
| 3 | Solar EUV Irradiance | W m-2 |
| 5 | Solar Spectral Irradiance | W m-2 nm-1 |
| 6 | F10.7 | W m-2 Hz-1 |
| 7 | Solar radio emissions | W m-2 Hz-1 |
| 8-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 7: Terrestrial electromagnetic emissions

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Limb intensity | m-2 s-1 |
| 1 | Disk intensity | m-2 s-1 |
| 2 | Disk intensity day | m-2 s-1 |
| 3 | Disk intensity night | m-2 s-1 |
| 4-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 8: Imagery

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | X-ray radiance | W sr-1 m-2 |
| 1 | EUV radiance | W sr-1 m-2 |
| 2 | H-alpha radiance | W sr-1 m-2 |
| 3 | White light radiance | W sr-1 m-2 |
| 4 | CaII-K radiance | W sr-1 m-2 |
| 5 | White light coronagraph radiance | W sr-1 m-2 |
| 6 | Heliospheric radiance | W sr-1 m-2 |
| 7 | Thematic mask | numeric |
| 8-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

Product discipline 4 – Space weather products, parameter category 9: Ion-neutral coupling

| Number | Parameter | Units |
| --- | --- | --- |
| 0 | Pedersen conductivity | S m-1 |
| 1 | Hall conductivity | S m-1 |
| 2 | Parallel conductivity | S m-1 |
| 3-191 | Reserved |  |
| 192-254 | Reserved for local use |  |
| 255 | Missing |  |

- 2010-2.3.1/2(DRC-II)/Encoding wave spectra in GRIB Edition 2 Waves parameters (amendments other than 46-48 were implemented) <para 4.1>

The prognostic variable of a wave model is the distribution of wave energy with respect to frequency and direction, called the "Wave Spectrum".

The spectrum is a statistical quantity representing the average sea state of a certain region within a certain time period. However, this averaging is implicitly assumed and it is not applied in the post-processing of the model.

In order to reduce the number of degrees of freedom there exists a number of "integrated" parameters that characterize the spectrum. For example, the significant wave height is determined from the spectrum by integrating over all frequencies f (and directions)

Hs = 4 * sqrt(m0), where m0 = integral (f * E(f)) df

Hs approximates the average over the higher third of all waves that might be observed by a ship officer. Similarly, other integrated parameters like the "Mean Wave Period" or the "Maximum Height of an Individual Wave" can be derived (in a more or less complicated way) from the wave spectrum without any averaging in space or time.

Since wave models are not capable of describing the development of single waves it makes no sense to define a parameter "Height of an Individual Wave".

Thus, using expressions like "maximum" or "mean" in the spectral context is not contradictory to the GRIB2-orthonogality requirement.

The "Wave Directional Width" is a relative measure (like the relative humidity) and therefore dimensionless.

#### Add the new entries in Code table 4.2

Product discipline 10:	Oceanographic products, parameter category 0:	Waves

| Number | Parameter | Units |
| --- | --- | --- |
| 16 | Coefficient of drag with waves | - |
| 17 | Friction Velocity | m s-1 |
| 18 | Wave stress | N m-2 |
| 19 | Normalised Wave Stress | - |
| 20 | Mean square slope of waves | - |
| 21 | U-component surface Stokes drift | m s-1 |
| 22 | V-component surface Stokes drift | m s-1 |
| 23 | Period of maximum individual wave height | s |
| 24 | Maximum individual wave height | m |
| 25 | Inverse mean wave frequency | s |
| 26 | Inverse mean frequency of the wind waves | s |
| 27 | Inverse mean frequency of the total swell | s |
| 28 | Mean zero-crossing wave period | s |
| 29 | Mean zero-crossing period of the wind waves | s |
| 30 | Mean zero-crossing period of the total swell | s |
| 31 | Wave directional width | - |
| 32 | Directional width of the wind waves | - |
| 33 | Directional width of the total swell | - |
| 34 | Peak wave period | s |
| 35 | Peak period of the wind waves | s |
| 36 | Peak period of the total swell | s |
| 37 | Altimeter wave height | m |
| 38 | Altimeter corrected wave height | m |
| 39 | Altimeter range relative correction | - |
| 40 | 10 metre neutral wind speed over waves | m s-1 |
| 41 | 10 metre wind direction over waves | degrees |
| 42 | Wave energy spectrum | m2 s radian-1 |
| 43 | Kurtosis of the sea surface elevation due to waves | - |
| 44 | Benjamin-Feir index | - |
| 45 | Spectral peakedness factor | s-1 |
| 46 | 2-dim Spectral Energy Density E(f,θ) | m² s |
| 47 | Frequency Spectral Energy Density E(f) = ∫E(f,θ)dθ | m² s |
| 48 | Directional Spectral Energy Density E(θ)= ∫E(f,θ)df / m0 | - |
| 49-254 | Reserved |  |
| 255 | Missing |  |

Product discipline 10:  Oceanographic products, parameter category 4: Sub-surface properties

Number	Parameter		Units

7	Bathymetry		m

Add the new note to the Product discipline 10, parameter category 0 in Code table 4.2

*	Further information concerning the wave parameters can be found in WMO Publication No 702, “Guide to Wave Analysis and Forecasting (http://www.wmo.int/pages/prog/amp/mmop/documents/WMO%20No%20702/WMO702.pdf)

FM 94 BUFR/FM 95 CREX

- 2013-3.2.1(DRMM-I)/Additions to the BUFR template for n-minute AWS data (3 07 092) 
<para 4.1 and 3.2.7>

A new D descriptor 3 01 130 is proposed that would be placed in front of the current 3 02 072, which would indicate the following -:

- Whether the system is subject to ‘aspiration’. In general most systems are either permanently aspirated or not. The exception being where aspiration is applied ‘where most needed’.

- The type of humidity instrument used. In some systems two different instruments may be in use.

|  |  | BUFR |
| --- | --- | --- |
| TABLE |  |  |  |  | DATA |
| REFERENCE | ELEMENT NAME | UNIT | SCALE | REFERENCE | WIDTH |
| F* X Y |  |  |  | VALUE | (Bits) |
| 3 01 130 |  |  |  |  |  |
| 0 03 002 | Generic type of humidity instrument | Code Table | 0 | 0 | 4 |
| 0 03 003 | Configuration of sensors | Code Table | 0 | 0 | 3 |
| 0 03 004 | Type of Shield or Screen | Code Table | 0 | 0 | 5 |
| 0 03 005 | Horizontal Width of Screen or Shield (x) | m | 2 | 0 | 16 |
| 0 03 006 | Horizontal Depth of Screen or Shield (y) | m | 2 | 0 | 16 |
| 0 03 007 | Vertical Height of Screen or Shield (z) | m | 2 | 0 | 16 |
| 0 03 008 | Artificially Ventilated Screen or Shield | Code Table | 0 | 0 | 3 |
| 0 03 009 | Degree of Forced Ventilation at time of reading | m3s-1 | 1 | 0 | 16 |

The new D sequence 3 01 130 will include four new code tables. In addition a new descriptor 0 03 001 is proposed to indicate the type of platform from which the observation is made. Details of the code tables associated with the new entries are given below.

0 03 001    Surface station type

0	Land station (synoptic network)

1	Shallow water station (fixed to sea/lake floor)

2	Ship

3	Rig/Platform

4	Moored buoy

5	Drifting buoy (or drifter)

6	Ice buoy

7	Land station (local network)

8	Land vehicle

9	Autonomous marine vehicle

10-14	Reserved

15	Missing value

Notes:

(1)	The last three categories are for possible future use.

(2)	"Land station (local network)" distinguishes "non-synoptic" stations these aren't currently distributed on the GTS but might be stored in BUFR in the future.

(3)	There could be separate tables for marine and land stations but there are marginal cases (shallow water fixed stations in the southern North Sea and some rigs reporting in SYNOP code).

0 03 002

Generic type of humidity instrument

- Psychrometer

- Capacitive sensor (unheated)

- Capacitive sensor (heated)

- Resistive sensor

- Ordinary human hair

- Rolled hair

- Goldbeater’s skin

- Chilled mirror hygrometer

- Dew Cell

- Optical absorption sensor

  - Reserved

15	Missing value

0 03 003

Configuration of Sensors

0  	Solar Radiation Shield or Screen (Double V Section Louvers)

1   	No Solar Radiation Shield or Screen

2   	Solar Radiation Shield or Screen (Single V section Louvers)

3   	Solar Radiation Shield or Screen (overlapping Louvers)

4   	Solar Radiation Shield or Screen (non-overlapping louvers)

5   	Solar Radiation Shield or Screen (not Louvered)

6   	Integrated e.g. Chilled Mirror

7   	Missing value

0 03 004

Type of Shield or Screen

0        	Within Stevenson screen (Wooden)

1        	Within Stevenson Screen (Plastic)

2        	Within Marine Stevenson Screen (wooden)

3        	Within Marine Stevenson Screen (Plastic)

4        	Within Cylindrical Section Plate Shield (metal)

5        	Within Cylindrical Section Plate Shield (wooden)

6        	Within Cylindrical Section Plate Shield (Plastic)

7        	Within Concentric tube (metal)

8        	Within Concentric tube (wooden)

9        	Within Concentric tube (plastic)

10      	Within Rectangular section Shield (metal)

11      	Within Rectangular section Shield (wooden)

12      	Within Rectangular section Shield (plastic)

13      	Within Rectangular section Shield (metal)

14      	Within Square section Shield (wooden)

15      	Within Square section Shield (plastic)

16      	Within Square section Shield (metal)

18      	Within Triangular section Shield (wooden)

19      	Within Triangular section Shield (plastic)

20      	Within Triangular section Shield (metal)

21      	Within open covered lean-to (reed/grass/leaf)

22      	Within open covered inverted v roof (reed/grass/leaf)

23-29  Reserved

30       Not Applicable e.g. Chilled mirror manufacturers enclosure

31       Missing Value

0 03 008

Artificially Ventilated Screen or Shield

0	Natural ventilation in use

1   	Artificial aspiration in use: constant flow at time of reading

2   	Artificial aspiration in use: variable flow at time of reading

3 -6  	Reserved

7    	Missing value

Add a template:

BUFR template for surface observations from n-minute period

# TM 307092

|  |  |  | Unit, scale |
| --- | --- | --- | --- |
| 3 01 089 |  | National station identification |  |
|  | 0 01 101 | State identifier (1) | Code table, 0 |
|  | 0 01 102 | National station number (1) | Numeric, 0 |
| 3 01 090 |  | Fixed surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 | Surface station identification |  |
|  |  | WMO block number | Numeric, 0 |
|  |  | WMO station number | Numeric, 0 |
|  |  | Station or site name | CCITT IA5, 0 |
|  |  | Type of station | Code table, 0 |
|  | 3 01 011 | Year(2) | Year, 0 |
|  |  | Month(2) | Month, 0 |
|  |  | Day(2) | Day, 0 |
|  | 3 01 012 | Hour(2) | Hour, 0 |
|  |  | Minute(2) | Minute, 0 |
|  | 3 01 021 | Latitude (high accuracy) | Degree, 5 |
|  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, 1 |
| 0 03 001 |  | Surface station type | Code table, 0 |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  | Surface station instrumentation |  |
|  | 0 02 180 | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 | Visibility measurement system | Code table, 0 |
|  | 0 02 183 | Cloud detection system | Code table, 0 |
|  | 0 02 184 | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 | Capability to discriminate lightning strikes | Flag table, 0 |
| 0 04 015 |  | Time increment (= - n minutes) | Minute, 0 |
| 0 04 065 |  | Short time increment ( = 1 minute) | Minute, 0 |
| 1 33 000 |  | Delayed replication of 33 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor (= n) | Numeric, 0 |
| 0 10 004 |  | Pressure | Pa, –1 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
| 3 02 070 |  | Wind data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 | Maximum wind gust speed | m s-1, 1 |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
| 3 01 130 |  | Temperature and humidity instrumentation |  |
|  | 0 03 002 | Generic type of humidity instrument | Code table, 0 |
|  | 0 03 003 | Configuration of sensors | Code table, 0 |
|  | 0 03 004 | Type of shield or screen | Code table, 0 |
|  | 0 03 005 | Horizontal width of screen or shield (x) | m, 2 |
|  | 0 03 006 | Horizontal depth of screen or shield (y) | m, 2 |
|  | 0 03 007 | Vertical height of screen or shield (z) | m, 2 |
|  | 0 03 008 | Artificially ventilated screen or shield | Code table, 0 |
|  | 0 03 009 | Degree of forced ventilation at time of reading | m-3 s-1, 1 |
| 3 02 072 |  | Temperature and humidity data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 12 101 | Temperature/Air-temperature (scale 2) | K, 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 33 003 | Quality of humidity measurement | Code table, 0 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
| 0 07 032 |  | Height of sensor above local ground (6) | m, 2 |
| 0 08 010 |  | Surface qualifier | Code table, 0 |
| 0 12 120 |  | Ground temperature | K, 2 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 08 010 |  | Surface qualifier (set to missing to cancel the previous value) | Code table, 0 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  | Replicate 1 descriptor five times |  |
| 3 07 063 | 0 07 061 | Depth below land surface | m, 2 |
|  | 0 12 130 | Soil temperature (scale 2) | K, 2 |
| 0 07 061 |  | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 |  | Visibility data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 001 | Horizontal visibility | m, –1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 073 |  | Cloud data |  |
|  | 0 20 010 | Cloud cover (total) | %, 0 |
|  | 1 05 004 | Replicate 5 descriptors four times |  |
|  | 0 08 002 | Vertical significance | Code table, 0 |
|  | 0 20 011 | Cloud amount | Code table, 0 |
|  | 0 20 012 | Cloud type | Code table, 0 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 013 | Height of base of cloud | m, –1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 076 |  | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 | Type of precipitation | Flag table, 0 |
|  | 0 20 022 | Character of precipitation | Code table, 0 |
|  | 0 26 020 | Duration of precipitation(3) | Minute, 0 |
|  | 0 20 023 | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 | Obscuration | Flag table, 0 |
|  | 0 20 026 | Character of obscuration | Code table, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 13 155 |  | Intensity of precipitation | kgm-2s-1, 4 |
| 0 13 058 |  | Size of precipitation element | m, 4 |
|  |  | (end of the replicated sequence) |  |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  | Rate of ice accretion | Code table, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 |  | State of ground and snow depth measurement |  |
|  | 0 02 176 | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 | Total snow depth | m, 2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 079 |  | Precipitation measurement |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 02 175 | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 | Method of liquid water content measurement of Precipitation | Code table, 0 |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 13 011 | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 080 |  | Evaporation measurement |  |
|  | 0 02 185 | Method of evaporation measurement | Code table, 0 |
|  | 0 04 025 | Time period or displacement ( = - n minutes) | Minute, 0 |
|  | 0 13 033 | Evaporation /evapotranspiration | kg m-2, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 081 |  | Total sunshine data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 14 031 | Total sunshine | Minute, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 082 |  | Radiation data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 14 002 | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - n minutes) | Minute |
| 0 13 059 |  | Number of flashes | Numeric |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 |  | First order statistics of P, W, T, U data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 08 023 | First order statistics (= 9; best estimate of standard deviation) (4) | Code table, 0 |
|  | 0 10 004 | Pressure | Pa, –1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 08 023 | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  | Internal measurement status information (AWS) | Code table, 0 |

Notes:

(1)	0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) shall be used to identify a station within the national numbering system that is completely independent of the WMO international numbering system. The WMO international identification 0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station.

(2)	The time identification refers to the end of the n-minute period.

(3)	Duration of precipitation (in minutes) represents number of minutes in which any precipitation was registered.

(4)	Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

(5)	If reporting nominal values is required, the template shall be supplemented with 3 07 093.

(6)	The height above local ground 0 07 032 referring to ground temperature shall be considered as a variable. After a snowfall, the sensor is placed at the top of the snow layer and the changed value of 0 07 032 shall indicate this procedure (total snow depth is reported in 0 13 013).

- 2013-3.2.2(DRMM-I)/Proposal for a BUFR template for radar wind profiler <para 4.1>

Add templates:

Radar Wind Profiler Data Sequence:

| TABLE REFERENCE | TABLE REFERENCES | TABLE REFERENCES | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- | --- | --- |
| 3 09 021 |  |  |  | RWP Wind data (product data) NEW |
|  | 3 01 001 |  |  | WMO block and station numbers |
|  |  | 0 01 001 |  | WMO Block Number |
|  |  | 0 01 002 |  | WMO Station Number |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy), height of station) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  |  | 0 07 001 |  | Height of station |
|  | 3 01 014 |  |  | Time period |
|  |  | 1 02 002 |  | Replicate 2 descriptors 2 times |
|  |  | 3 01 011 |  | Year, month, day |
|  |  |  | 0 04 001 | Year |
|  |  |  | 0 04 002 | Month |
|  |  |  | 0 04 003 | Day |
|  |  | 3 01 012 |  | Hour, minute |
|  |  |  | 0 04 004 | Hour |
|  |  |  | 0 04 005 | Minute |
|  | 0 02 003 |  |  | Type of measuring equipment used |
|  | 1 12 000 |  |  | Delayed replication of 12 descriptors |
|  | 0 31 001 |  |  | Delayed descriptor replication factor (typically between 20 and 100) |
|  | 0 07 007 |  |  | Height |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy)) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  | 0 11 003 |  |  | u-component |
|  | 0 11 099 0 11 110 |  |  | Uncertainty in u-component NEW |
|  | 0 11 004 |  |  | v-component |
|  | 0 11 100 0 11 111 |  |  | Uncertainty in v-component NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 11 006 |  |  | w-component |
|  | 0 11 101 0 11 112 |  |  | Uncertainty in w-component NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 10 071 |  |  | Vertical resolution NEW |
|  | 0 05 062 |  |  | Horizontal width of sampled volume NEW |

RASS Data Sequence:

| TABLE REFERENCE | TABLE REFERENCES | TABLE REFERENCES | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- | --- | --- |
| 3 09 022 |  |  |  | RASS virtual temperature (product data) NEW |
|  | 3 01 001 |  |  | WMO block and station numbers |
|  |  | 0 01 001 |  | WMO Block Number |
|  |  | 0 01 002 |  | WMO Station Number |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy), height of station) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  |  | 0 07 001 |  | Height of station |
|  |  | 0 02 003 |  | Type of measuring equipment |
|  | 3 01 014 |  |  | Time period |
|  |  | 1 02 002 |  | Replicate 2 descriptors 2 times |
|  |  | 3 01 011 |  | Year, month, day |
|  |  |  | 0 04 001 | Year |
|  |  |  | 0 04 002 | Month |
|  |  |  | 0 04 003 | Day |
|  |  | 3 01 012 |  | Hour, minute |
|  |  |  | 0 04 004 | Hour |
|  |  |  | 0 04 005 | Minute |
|  | 0 02 003 |  |  | Type of measuring Equipment used |
|  | 1 10 000 |  |  | Delayed replication of 10 descriptors |
|  | 0 31 001 |  |  | Delayed descriptor replication factor |
|  | 0 07 007 |  |  | Height |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy)) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  | 0 12 007 |  |  | Virtual temperature |
|  | 0 12 008 |  |  | Uncertainty in virtual temperature NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 11 006 |  |  | w-component |
|  | 0 11 101 0 11 112 |  |  | Uncertainty in w-component NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 10 071 |  |  | Vertical resolution NEW |
|  | 0 05 062 |  |  | Horizontal width of sampled volume NEW |

Add descriptors:

|  |  | BUFR | CREX |
| --- | --- | --- | --- |
| TABLE |  |  |  |  | DATA |  |  | DATA |
| REFERENCE | ELEMENT NAME | UNIT | SCALE | REFERENCE | WIDTH | UNIT | SCALE | WIDTH |
| F* X Y |  |  |  | VALUE | (Bits) |  |  | (Characters) |
| 0 11 099 0 11 110 | Uncertainty in u-component | m s-1 | -1 | 0 | 10 | m s-1 | -1 | 4 |
| 0 11 100 0 11 111 | Uncertainty in v-component | m s-1 | -1 | 0 | 10 | m s-1 | -1 | 4 |
| 0 11 101 0 11 112 | Uncertainty in w-component | m s-1 | -2 | 0 | 10 | m s-1 | -2 | 4 |
| 0 10 071 | Vertical resolution | m | 0 | 0 | 14 | m | 0 | 5 |
| 0 05 062 | Horizontal width of sampled volume | m | -1 | 0 | 20 | m | -1-1 | 7 |
| 0 12 008 | Uncertainty in virtual temperature | K | -1 | 0 | 10 | K | 0-1 | 4 |

- 2013-3.2.4(DRMM-I)/Satellite-derived winds in BUFR <para 4.1>

Add an entry:

|  |  | (Satellite-derived winds) |
| --- | --- | --- |
| 3 10 067 | 0 01 007 | Satellite identifier |
|  | 0 01 033 | Identification of originating/generating centre |
|  | 0 01 034 | Identification of originating/generating sub-centre |
|  | 0 02 019 | Satellite instruments |
|  | 0 02 020 | Satellite classification |
|  | 3 01 011 | Year, month, day |
|  | 3 01 012 | Hour, minute |
|  | 2 07 003 | Increase scale, reference value and bit data width |
|  | 0 04 006 | Second |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 3 01 021 | Latitude, L/longitude (high accuracy) |
|  | 0 07 024 | Satellite zenith angle |
|  | 0 02 153 | Satellite channel centre frequency |
|  | 0 02 014 | Tracking technique/status of system used |
|  | 0 02 023 | Satellite derived wind computation method |
|  | 0 08 072 | Pixel(s) type (target type) |
|  | 0 02 028 | Segment size at nadir in X x-direction (target scene width) |
|  | 0 02 029 | Segment size at nadir in Y y-direction (target scene height) |
|  | 0 04 025 | Time period or displacement (in minutes) |
|  | 0 10 004 | Pressure |
|  | 0 12 101 | Temperature/air temperature |
|  | 2 07 002 | Increase scale, reference value and bit data width |
|  | 0 11 001 | Wind direction |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 0 33 007 | Per cent confidence (for wind direction) |
|  | 2 07 001 | Increase scale, reference value and bit data width |
|  | 0 11 002 | Wind speed |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 0 33 007 | Per cent confidence (for wind speed) |
|  | 0 08 041 | Data significance (14 = Expected error) |
|  | 0 11 002 | Wind speed |
|  | 0 08 041 | Data significance (15 = Representative error) |
|  | 0 10 004 | Pressure |
|  | 0 12 101 | Temperature/air temperature |
|  | 0 08 041 | Data significance (Missing = Cancel) |
|  | 0 08 021 | Time significance (4 = Forecast) |
|  | 0 04 004 | Hour |
|  | 0 04 005 | Minute |
|  | 0 04 006 | Second |
|  | 2 07 002 | Increase scale, reference value and bit data width |
|  | 0 11 001 | Wind direction |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 2 07 001 | Increase scale, reference value and bit data width |
|  | 0 11 002 | Wind speed |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 0 08 021 | Time significance (28 = Start of scan) |
|  | 0 04 004 | Hour |
|  | 0 04 005 | Minute |
|  | 0 04 006 | Second |
|  | 3 01 021 | Latitude, L/longitude (high accuracy) |
|  | 2 07 001 | Increase scale, reference value and bit data width |
|  | 0 11 003 | u-component |
|  | 0 11 004 | v-component |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 0 11 110 0 11 113 | Tracking correlation of vector |
|  | 0 08 023 | First order statistics (10 = Standard deviation) |
|  | 0 11 002 | Wind speed |
|  | 0 08 023 | First order statistics (Missing = Cancel) |
|  | 0 25 147 | Size of largest cluster (in pixels) |
|  | 0 08 021 | Time significance (29 = End of scan or time of ending) |
|  | 0 04 004 | Hour |
|  | 0 04 005 | Minute |
|  | 0 04 006 | Second |
|  | 3 01 021 | Latitude, L/longitude (high accuracy) |
|  | 2 07 001 | Increase scale, reference value and bit data width |
|  | 0 11 003 | u-component |
|  | 0 11 004 | v-component |
|  | 2 07 000 | Cancel increase scale, reference value and bit data width |
|  | 0 11 110 0 11 113 | Tracking correlation of vector |
|  | 0 08 023 | First order statistics (10 = Standard deviation) |
|  | 0 11 002 | Wind speed |
|  | 0 08 023 | First order statistics (Missing = Cancel) |
|  | 0 25 147 | Size of largest cluster (in pixels) |
|  | 0 08 021 | Time significance (Missing = Cancel) |
|  | 0 04 004 | Hour |
|  | 0 04 005 | Minute |
|  | 0 04 006 | Second |
|  | 0 08 003 | Vertical significance (satellite observations) (2=Cloud top) |
|  | 0 08 023 | First order statistics (2=Maximum value) |
|  | 0 10 004 | Pressure (Maximum cloud top pressure in target scene) |
|  | 0 12 101 | Temperature/air temperature (Maximum cloud top temperature in target scene) |
|  | 0 08 023 | First order statistics (3=Minimum value) |
|  | 0 10 004 | Pressure (Minimum cloud top pressure in target scene) |
|  | 0 12 101 | Temperature/air temperature (Minimum cloud top temperature in target scene) |
|  | 0 08 023 | First order statistics (10 = Standard deviation) |
|  | 0 10 004 | Pressure (Standard deviation of cloud top pressure in target scene) |
|  | 0 08 023 | First order statistics (Missing = Cancel) |
|  | 0 08 003 | Vertical significance (satellite observations) (Missing = Cancel) |
|  | 0 20 056 | Cloud phase (Dominant cloud phase of target scene) |
|  | 0 12 133 | NWP vertical temperature gradient (+/- 200hpa about pressure assignment of tracer) |
|  | 0 11 111 0 11 114 | NWP vertical wind shear (+/- 200hpa about pressure assignment of tracer) |
|  | 0 12 134 | Low-level inversion flag |

Add entries:

| F X Y | Element name | BUFR Unit | BUFR Scale | BUFR Refval | BUFR Bits | CREX Unit | CREX Scale | CREX Bytes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 11 110 0 11 113 | Tracking correlation of vector | Numeric | 3 | -1000 | 12 | Numeric | 3 | 4 |
| 0 11 111 0 11 114 | NWP vertical wind shear (+/- 200hPa about pressure assignment of tracer) | m/s | 2 | -8192 | 14 | m/s | 2 | 5 |
| 0 12 133 | NWP vertical termperature gradient (+/- 200hPa about pressure assignment of tracer) | K | 2 | 0 | 16 | C | 2 | 4 |
| 0 12 134 | Low-level inversion flag | Code table | 0 | 0 | 2 | Code table | 0 | 1 |
| 0 25 147 | Size of largest cluster (in pixels) | Numeric | 0 | 0 | 10 | Numeric | 0 | 4 |

Add entries:

Code table 0 02 014/Common Code table C-7 (Tracking technique/status of system used)

71 	Nested tracking disabled

Code table 0 20 056 (Cloud phase)

5		Supercooled liquid water

Code table 0 08 041 (Data significance)

14		Expected error

15		Representative error

0 12 134 – Low-level inversion flag

| Code figure | DESCRIPTION |
| --- | --- |
| 0 | No inversion |
| 1 | Inversion |
| 2 | Reserved |
| 3 | Missing value |

- 2012-3.2.7(DRC-IV)/Sequence 3 02 067 <para 4.1>

Validate a new descriptor:

Category 02 – Meteorological sequences common to surface data

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT DESCRIPTION |
| --- | --- | --- |
| F X Y |  |  |
|  |  | Additional synoptical parameters |
| 3 02 067 | 0 01 023 | Observation sequence number |  |
|  | 0 04 025 | Time period or displacement | Time period (= 0 minutes) |
|  | 0 02 177 | Method of snow depth measurement |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 20 003 | Present weather |  |
|  | 1 02 000 | Delayed replication of 2 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 05 021 | Bearing or azimuth |  |
|  | 0 20 001 | Horizontal visibility |  |
|  | 0 05 021 | Bearing or azimuth | set to missing to cancel previous entry |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 056 | (Sea/water temperature) |  |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 33 041 | Attribute of following value |  |
|  | 0 20 058 | Visibility seawards from a coastal station |  |
|  | 0 22 061 | State of the sea |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 3 02 022 | (Wind waves) |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 3 02 023 | (Swell waves) |  |
|  | 1 04 000 | Delayed replication of 4 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving or in which they are observed of a phenomenon or clouds |  |
|  | 0 20 137 | Evolution of clouds |  |
|  | 0 20 012 | Cloud type |  |
|  | 0 20 090 | Special clouds |  |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving or in which they are observed of a phenomenon or clouds |  |
|  | 0 20 137 | Evolution of clouds |  |
|  | 0 20 136 | Supplementary cloud type |  |
|  | 0 04 025 | Time period or displacement | Reference period of fresh fallen snow |
|  | 0 13 012 | Depth of fresh snow |  |
|  | 0 04 025 | Time period or displacement | Time period in minutes ( =-60 ) |
|  | 0 11 042 | Maximum wind speed (10-minute mean wind) |  |
|  | 1 04 000 | Delayed replication of 4 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 08 021 | Time significance | = 30 (time of occurrence) or = 17 (start of phenomenon) |
|  | 0 04 025 | Time period or displacement | Time displacement (=-xx ) |
|  | 0 11 042 | Maximum wind speed (10-minute mean wind) |  |
|  | 0 08 021 | Time significance | set to missing to cancel previous entry |
|  | 1 15 000 | Delayed replication of 15 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 08 021 | Time significance | = 30 (time of occurrence) or = 17 (start of phenomenon) |
|  | 0 04 015 | Time increment | Time increment (=-xx1 ) |
|  | 0 08 021 | Time significance | = 2 (time averaged) |
|  | 0 04 025 | Time period or displacement | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |
|  | 0 11 001 | Wind direction |  |
|  | 0 11 002 | Wind speed |  |
|  | 0 08 021 | Time significance | =22 (time of occurrence of wind shift) |
|  | 0 04 015 | Time increment | Time increment (=+xx2 ) |
|  | 0 08 021 | Time significance | = 2 (time averaged) |
|  | 0 04 025 | Time period or displacement | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |
|  | 0 11 001 | Wind direction |  |
|  | 0 11 002 | Wind speed |  |
|  | 0 08 021 | Time significance | set to missing to cancel previous entry |
|  | 0 04 025 | Time period or displacement | Time displacement (= 0 minutes) |
|  | 0 04 015 | Time increment | Time increment (=+(xx1-xx2), non negative to reset the time to the actual time ) |
|  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 04 025 | Time period or displacement | Time period in minutes (=-xx i.e. from) |
|  | 0 04 025 | Time period or displacement | Time period in minutes (=-xx i.e. to) |
|  | 0 20 003 | Present weather |  |
|  | 1 10 000 | Delayed replication of 10 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor |  |
|  | 0 04 025 | Time period or displacement | Time period in minutes (=-xx i.e. from) |
|  | 0 04 025 | Time period or displacement | Time period in minutes (=-xx i.e. to) |
|  | 0 05 021 | Bearing or azimuth |  |
|  | 0 05 021 | Bearing or azimuth |  |
|  | 0 20 054 | True direction from which a phenomenon or clouds are moving or in which they are observed of a phenomenon or clouds |  |
|  | 0 20 024 | Intensity of phenomena |  |
|  | 0 20 025 | Obscuration |  |
|  | 0 20 026 | Character of obscuration |  |
|  | 0 20 027 | Phenomena occurrence |  |
|  | 0 20 063 | Special phenomena |  |

And in Template Form:

| 3 02 067 |  |  | Additional synoptical parameters |  |  |
| --- | --- | --- | --- | --- | --- |
|  | 0 01 023 |  | Observation Sequence number |  | Numeric, 0 |
|  |  |  | Additional “instantaneous” data |  |  |
|  | 0 04 025 |  | Time period (= 0 minutes) |  | Minute, 0 |
|  | 0 02 177 |  | Method of snow depth measurement 0 Manual observation 1 Ultrasonic method 2 Video camera method 3-13 Reserved 14 Others 15 Missing value |  | Code table, 0 |
|  |  |  | Additional present weather |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 003 |  | Present weather | 960ww 961ww | Code table, 0 |
|  |  |  | Visibility in different directions |  |  |
|  | 1 02 000 |  | Delayed replication of 2 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 05 021 |  | Bearing or azimuth | 981VV-988VV | Degreetrue, 0 |
|  | 0 20 001 |  | Horizontal visibility | VV | m, –1 |
|  | 0 05 021 |  | Bearing or azimuth (=set to missing to cancel previous entry) |  | Degreetrue, 0 |
|  |  |  | Sea data (Observations from a coastal station) |  |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |  |
|  |  | 0 02 038 | Method of sea/water temperature measurement |  | Code table, 0 |
|  |  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) |  | m, 2 |
|  |  | 0 22 043 | Sea/water temperature | 222.. 0sTwTwTw | K, 2 |
|  |  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) |  | m, 2 |
|  | 1 03 000 |  | Delayed replication of 3 descriptors |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 33 041 |  | Attribute of following value |  | Code tabel, 0 |
|  | 0 20 058 |  | Visibility seawards from a coastal station | 980VsVs | m,-1 |
|  | 0 22 061 |  | State of the sea | 924SVs | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 022 |  | Wind waves |  |  |
|  |  | 0 22 002 | Direction of wind waves |  | Degreetrue, 0 |
|  |  | 0 22 012 | Period of wind waves | 222.. 2PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves | HwHw | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 3 02 023 |  | Swell waves |  |  |
|  |  | 0 22 003 | Direction of swell waves | 222.. 3dw1dw1 dw2dw2 | Degreetrue, 0 |
|  |  | 0 22 013 | Period of swell waves | 4Pw1Pw1, 5Pw2Pw2 | s, 0 |
|  |  | 0 22 023 | Height of swell waves | Hw1Hw1, Hw2Hw2 | m, 1 |
|  |  |  | Clouds | 941CDp, 943CLDp |  |
|  | 1 04 000 |  | Delayed replication of 4 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 137 |  | Evolution of Clouds | 940Cn3 | Code table, 0 |
|  | 0 20 012 |  | Cloud type (C) | 941CDp, 943CLDp | Code table, 0 |
|  | 0 20 090 |  | Special clouds | 993CSDa | Code table, 0 |
|  | 1 03 000 |  | Delayed replication of 3 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da | Degreetrue, 0 |
|  | 0 20 137 |  | Evolution of Clouds | n3, n4 | Code table, 0 |
|  | 0 20 136 |  | Supplementary Cloud type | 948C0Da, 949CaDa, 950Nmn3, 951Nvn4 | Code table, 0 |
|  |  |  | Additional “period” data |  |  |
|  | 0 04 025 |  | Time period in minutes ( = reference period of fresh fallen snow ) |  | Minute, 0 |
|  | 0 13 012 |  | Depth of fresh snow |  | m, 2 |
|  |  |  | Additional wind data |  |  |
|  | 0 04 025 |  | Time period in minutes ( =-60 ) |  | Minute, 0 |
|  | 0 11 042 |  | Maximum wind gust speed (10 min mean wind) | 912ff | m s-1, 1 |
|  |  |  | 902tt 912ff .. mandatory ff>=18 |  |  |
|  | 1 04 000 |  | Delayed replication of 4 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (=-xx ) | 902tt | Minute, 0 |
|  | 0 11 042 |  | Maximum wind gust speed (10 min mean wind) | 912ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  |  |  | Significant change in wind speed and/or direction | e.g. 913ff 904tt 913ff |  |
|  | 1 15 000 |  | Delayed replication of 15 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 08 021 |  | Time significance (=30 time of occurrence or =17 start of phenomenon) |  | Code table, 0 |
|  | 0 04 015 |  | Time increment (=-xx1 ) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=22 time of occurrence of wind shift) |  | Code table, 0 |
|  | 0 04 015 |  | Time increment (=+xx2 ) |  | Minute, 0 |
|  | 0 08 021 |  | Time significance (= 2 (time averaged)) |  | Code table, 0 |
|  | 0 04 025 |  | Time period (= - 10 minutes, or number of minutes after a significant change of wind) |  | Minute, 0 |
|  | 0 11 001 |  | Wind direction | 915dd | Degreetrue, 0 |
|  | 0 11 002 |  | Wind speed | 913ff | m s-1, 1 |
|  | 0 08 021 |  | Time significance (=set to missing to cancel previous entry) |  | Code table, 0 |
|  | 0 04 025 |  | Time displacement (= 0 minutes) |  | Minute, 0 |
|  | 0 04 015 |  | Time increment (=+(xx1-xx2), non negative to reset the time to the actual time ) |  | Minute, 0 |
|  |  |  | Additional weather |  |  |
|  | 1 03 000 |  | Delayed replication of 3 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 20 003 |  | Present weather | 962ww, 963w1w1, 964ww, 965w1w1, 966ww, 967w1w1 | Code table, 0 |
|  |  |  | Additional 9SpSpspsp groups |  |  |
|  | 1 10 000 |  | Delayed replication of 10 descriptors |  |  |
|  | 0 31 001 |  | Delayed descriptor replication factor |  | Numeric, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. from) |  | Minute, 0 |
|  | 0 04 025 |  | Time period in minutes (=-xx i.e. to) |  | Minute, 0 |
|  | 0 05 021 |  | Bearing or azimuth * | Da, Dp | Degreetrue, 0 |
|  | 0 05 021 |  | Bearing or azimuth * | Da, Dp | Degreetrue, 0 |
|  | 0 20 054 |  | True direction from which a phenomenon or clouds are moving | Da, Dp | Degreetrue, 0 |
|  | 0 20 024 |  | Intensity of phenomena (1= Light, 2 = Moderate, 3 = Heavy, 4 = Violent, 5 = Severe) |  | Code table, 0 |
|  | 0 20 025 |  | Obscuration |  | Flag table, 0 |
|  | 0 20 026 |  | Character of obscuration |  | Code table, 0 |
|  | 0 20 027 |  | Phenomenon occurrence |  | Flag table, 0 |
|  | 0 20 063 |  | Special phenomena |  | Code table, 0 |

- 2012-3.2.11(DRC-IV)/A BUFR Sequence to append data for national use to Canadian 
SYNOP reports <para 4.1>

Validate a template, relevant descriptors and a code table:

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT DESCRIPTION |
| --- | --- | --- |
| F X Y |  | Synoptic data for national use (Canada) |
| 3 07 100 |  |  |  |
|  | 0 04 024 | Time period or displacement | (value = -6): following values apply to the 6 hour period preceding reference time. |
|  | 1 02 000 | Short d Delayed descriptor replication of two 2 descriptors |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 13 057 | Time of beginning/end of precipitation | Time of Precipitation beginning/end (National Use SYNOP code 909RtDc) |
|  | 0 26 020 | Duration of precipitation |  |
|  |  | Depth of newly-fallen snow |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 000 | Short delayed descriptor replication factor |  |
|  | 0 13 012 | Depth of fresh snow | (National SYNOP code 931ss) |
| 3 01 002 |  |  |  |
|  | 0 04 004 | Hour | set to 6 reporting time is always 0600Z |
|  | 0 04 005 | Minute | set to 0 |
|  | 0 04 024 | Time period or displacement in hours | Set to -24 ; values apply to the 24 hour period ending at the last T=06Z |
|  | 1 03 000 | Delayed replication of 3 descriptors replication | Bright sunshine |
|  | 0 31 000 | Delayed descriptor replication factor |  |
|  | 0 02 006 | Data obtained by | Value=1, obtained by derivation |
|  | 0 14 031 | Bright sunshine | (National Use SYNOP code 5SSSS) |
|  | 0 02 006 | Data obtained by | Value=0, Obtained by measurement |
|  | 1 04 000 | Short Delayed replication of 4 descriptors | Snowfall Amount/Water Equivalent |
|  | 0 31 000 | Short D delayed descriptor replication factor |  |
|  | 0 02 175 | Method of precipitation measurement |  |
|  | 0 13 119 | Snowfall amount | New descriptor (National SYNOP code 1SSSS) |
|  | 0 02 175 | Method of precipitation measurement |  |
|  | 0 13 120 | Amount of water equivalent of snow | New descriptor (National SYNOP code 2SwSwSwSw) |
|  | 1 07 000 | Short Delayed replication of 7 descriptors | Max wind speed/direction |
|  | 0 31 000 | Short D delayed descriptor replication factor |  |
|  | 0 08 021 | Time significance | Value=30, "time of occurrence" |
|  | 0 04 004 | Hour | Time of occurrence in hours (National SYNOP code 4FhFTFTFI) |
|  | 0 04 005 | Minutes | Time of occurrence minutes |
|  | 0 11 001 | Wind direction | (National Use SYNOP code 3dmdm) |
|  | 0 08 023 | First order statistics | max, value=2 |
|  | 0 11 002 | Wind speed | (National Use SYNOP code fmfm) |
|  | 0 08 021 | Time significance | Value=0, cancel |
|  | 0 04 024 | Time period in hours | Value=0, reset to initial time value |
| 3 01 002 |  |  |  |
|  | 0 04 004 | Hour | Reset to original value, the observation time |
|  | 0 04 005 | Minute | Reset to original value, the observation time |

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 02 006 | Data obtained by | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 13 119 | Snowfall amount | m | 3 | -10 | 14 | m | 3 | 5 |
| 0 13 120 | Snow amount, water equivalent | kg/m2 | 1 | -10 | 14 | kg/m2 | 1 | 5 |

0 02 006

Data obtained by

| Code figure |  |
| --- | --- |
| 0 | Measurement |
| 1 | Derivation from other data |
| 2-6 | Reserved |
| 7 | Missing |

- 2012-3.2.12(DRC-IV)/New BUFR/CREX entries for dual polarization radar data <para 4.1>

Validate new entries:

|  | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 33 029 | Correlation coefficient | Numeric | 2 | -100 | 8 | Numeric | 2 | 3 |
| 0 21 028 | Specific differential phase | deg/m | 5 | -200 | 11 | deg/m | 2 | 4 |

Add new entries:

Updated on 19 December 2014

|  | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 21 004 | Differential reflectivity | dB | 2 | -800 | 11 | dB | 2 | 4 |
| 0 21 028 | Differential phase | deg | 1 | 0 | 12 | deg | 1 | 4 |
| 0 33 029 | Correlation coefficient | Numeric | 2 | -100 | 8 | Numeric | 2 | 3 |

- 2009-3.3.2(DRC-I)/Update from JCOMM on developments for BUFR templates: New XBT template and queries about a revised VOS template (3 06 032 and 3 15 006 are under validation- being confirmed - others have been implemented with revisions) <para 4.1>

The template makes use of existing BUFR descriptors and proposes additional ones. Existing descriptors are indicated with no colour highlighting in the table. New descriptors are indicated with a coloured background. A notes column has been added to provide additional information.

## The XBT template (3 15 005)

| F | X | Y | Name | Unit | Scale | Ref value | Data Width (bits) | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 22 | 176 | Unique identifier for the profile | Numeric | 0 | 0 | 33 | (1) |
| 0 | 01 | 011 | Ship or mobile land station identifier | CCITT IA5 | 0 | 0 | 72 | (2) |
| 0 | 01 | 103 | IMO Number. Unique Lloyd's registry. | Numeric | 0 | 0 | 24 | (3) |
| 0 | 01 | 087 | WMO Marine observing platform extended identifier | Numeric | 0 | 0 | 23 | (4) |
| 0 | 01 | 019 | Long Station or site name | CCITT IA5 | 0 | 0 | 256 | (5) |
| 0 | 01 | 080 | Ship line number according to SOOP | CCITT IA5 | 0 | 0 | 32 |  |
| 0 | 05 | 036 | Ship transect number according to SOOP | Numeric | 0 | 0 | 7 | (6) |
| 0 | 01 | 013 | Speed of motion of moving observing platform | m/s | 0 | 0 | 10 |  |
| 0 | 01 | 012 | Direction of motion of moving observing platform | degree true | 0 | 0 | 9 |  |
| 3 | 01 | 011 | Date |  |  |  |  |  |
| 3 | 01 | 012 | Time |  |  |  |  |  |
| 3 | 01 | 021 | Latitude and longitude (high accuracy) |  |  |  |  |  |
| 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | m | 2 | 0 | 16 | (7) |
| 0 | 07 | 033 | Height of sensor above water surface | m | 1 | 0 | 12 | (7) |
| 0 | 02 | 002 | Type of instrumentation for wind measurement | Flag table | 0 | 0 | 4 | (8) |
| 0 | 11 | 002 | Wind speed | m/s | 1 | 0 | 12 |  |
| 0 | 11 | 001 | Wind direction | degree true | 0 | 0 | 9 |  |
| 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) | m | 2 | 0 | 16 | (9) |
| 0 | 07 | 033 | Height of sensor above water surface | m | 1 | 0 | 12 | (9) |
| 0 | 12 | 101 | Temperature/Dry-bulb temperature | K | 2 | 0 | 16 |  |
| 0 | 12 | 103 | Dew-point temperature | K | 2 | 0 | 16 |  |
| 0 | 07 | 032 | Height of sensor above local ground (or deck of marine platform) (set to missing to cancel previous value) | m | 2 | 0 | 16 |  |
| 0 | 07 | 033 | Height of sensor above water surface (set to missing to cancel previous value) | m | 1 | 0 | 12 |  |
| 3 | 02 | 021 | Waves |  |  |  |  |  |
| 3 | 02 | 056 | Sea Surface Temperature |  |  |  |  | (10) |
| 0 | 02 | 031 | Duration and time of current measurement | code table | 0 | 0 | 5 |  |
| 0 | 22 | 005 | Direction of sea surface current | degrees true | 0 | 0 | 9 |  |
| 0 | 22 | 032 | Speed of sea surface current | m/s | 0 | 0 | 13 |  |
| 0 | 02 | 032 | Indicator for digitization | code table | 0 | 0 | 2 | (11) |
| 3 | 15 | 004 | Water temperature profile (Temperature profile observed by XBT or Buoy) |  |  |  |  | (12) |
| 0 | 22 | 063 | Total depth of water | m | 0 | 0 | 14 |  |
| 0 | 08 | 080 | Qualifier for quality class | code table | 0 | 0 | 6 | (13) |
| 0 | 33 | 050 | Global GTSPP quality class | code table | 0 | 0 | 4 |  |
| 0 | 22 | 178 | XBT/XCTD launcher Type | code table | 0 | 0 | 8 | (14) |
| 0 | 22 | 177 | Height of XBT/XCTD Launcher above sea level | Numeric | 0 | 0 | 6 | (15) |
| 0 | 22 | 067 | Instrument type for water temperature profile measurement | code table | 0 | 0 | 10 |  |
| 0 | 02 | 191 | Instrument serial number for water temperature profile measurement | CCITT IA5 | 0 | 0 | 64 | (16) |
| 0 | 08 | 041 | Data significance | Code table | 0 | 0 | 5 | (17) |
| 0 | 26 | 021 | Year | year | 0 | 0 | 12 |  |
| 0 | 26 | 022 | Month | month | 0 | 0 | 4 |  |
| 0 | 26 | 023 | Day | day | 0 | 0 | 6 |  |
| 0 | 22 | 068 | Water temperature profile recorder type | code table | 0 | 0 | 7 |  |
| 0 | 25 | 061 | Data acquisition software type (or name) and version number | CCITT IA5 | 0 | 0 | 96 | (18) |
| 0 | 01 | 036 | Agency in charge of operating the observing platform | code table | 0 | 0 | 20 |  |

Notes:

(1)	Currently some countries are using a 32 bit CRC calculation to generate a unique identifier for the individual BATHY messages. Since missing values in a template have all bits set to 1 and since this may be a legitimate CRC result, we have set the bit width to be 33.

(2)	Place the ship call sign here.

(3)	Values are restricted to be between 0 and 9999999.

(4)	If field 0-01-011 is used, this field will be left missing and vice versa.

(5)	Place the ship name here.

(6)	Integer, assigned by the operator, incremented for each new transect (i.e. all drops have the same transect number while the ship is moving from one end point of the line to the other end point; as soon as the ship arrived to port and goes back to start a new transect then transect number is incremented). The initial value and subsequent values for transect numbers do not matter provided that each new transect by a ship on a line has a transect number higher than previous transect numbers for the same line and the same ship. In case a single cruise follows more than one SOOP line in a row, then the transect number should be incremented each time the cruise changes line.

(7)	This field records the height of the instrument used to make the wind speed and direction measurements.

(8)	Introduced to ensure that information about the certification, or not, of the instrument is retained as present in BATHY.

(9)	This was added to record the height of the instrument used to make the dry bulb temperature measurement.

(10)	This sequence as it stands allows 2 decimal precision on SST with descriptor 0-22-043. As temperatures are stored in kelvin, to convert we must add 273.15. By allowing only 2 decimals we may incur a rounding error. We propose a new sequence as follows:

3-02-090: Sea/water temperature high precision

0 02 038 Method of sea/water temperature measurement

0 07 063 Depth below sea/water surface (cm).  For sea surface temperature measurement

0 22 045 Sea/water temperature

0 07 063 Depth below sea/water surface (cm). Set to missing value to cancel the previous value.

(11)	This descriptor applies to the method used to select depths for the temperature profile encoded through 3-15-004. If temperatures are reported at signiﬁcant depths, the values shall:

(a) Be sufficient to reproduce basic features of the proﬁle and;

(b) Deﬁne the top and the bottom of isothermal layers.

(12) Proposed new sequence as follows. Note that temperatures are stored in K.

3-15-004: Water Temperature Profile

1-06-000	Delayed replication of 6 descriptors

0-31-001	Delayed descriptor replication factor

0-07-063	Depth below sea surface

0-08-080	Qualifier for quality class. Note: set to qualifier = 13

0-33-050	GTSPP quality class

0-22-043	Subsurface sea temperature

0-08-080	Qualifier for quality class. Note: set to qualifier = 11

0-33-050	GTSPP quality class

With an addition (in yellow) in code table 0-08-080 as follows:

0 08 080  Qualifier for GTSPP quality flag

Code	Meaning

figure

0	Total water pressure profile

1	Total water temperature profile

2	Total water salinity profile

3	Total water conductivity profile

4	Total water depth

5-9	Reserved

10	Water pressure at a level

11	Water temperature at a level

12	Salinity at a level

13	Water depth at a level

14-19	Reserved

20	Position

21-62	Reserved

63	Missing value

And an addition (in yellow) in code table 0-33-050 as follows:

0 33 050  Global GTSPP quality flag

Code	Meaning

figure

0	Unqualified

1	Correct value (all checks passed)

2	Probably good but value inconsistent with statistics (differ from climatology)

3	Probably bad (spike, gradient, … if other tests passed)

4	Bad value, Impossible value (out of scale, vertical instability, constant profile)

5	Value modified during quality control

6-7	Reserved

8	Interpolated value

9	Good for operational use; Caution; check literature for other uses

10-14	Reserved

15	Missing value

(13) We require a new entry in table 0 08 080. This has been inserted as code figure 4 and highlighted in yellow in note 12.

(14)	Propose new code table 0-22-178 as follows:

0 22 178  XBT/XCTD Launcher Type

Code

figure

0	Unknown

1	LM-2A Deck-mounted

2	LM-3A Hand-Held

3	LM-4A Thru-Hull

4-9	Reserved

10	AL-12 TSK Autolauncher (up to 12 Probes)

11-19	Reserved

20	SIO XBT Autolauncher (up to 6 probes)

21-29	Reserved

30	AOML XBT V6 Autolauncher (up to 6 Deep Blue probes)

31	AOML XBT V8.0 Autolauncher (up to 8 Deep Blue probes)

32	AOML XBT V8.1 Autolauncher (up to 8 Deep Blue&Fast Deep probes)

33-89	Reserved

90	CSIRO Devil Autolauncher

91-99	Reserved

100	MFSTEP Autolauncher (Mediterranean)

101-254	Reserved

255	Missing

(15)	Values are restricted to 0 to 50m in units of whole m.

(16)	New descriptor to record XBT serial number. Allows up to 8 characters.

(17)	Set the value for this descriptor to be 8 and we require a new code figure in table 0-08-041:

Code 	Meaning

0 	Parent site

1 	Observation site

2 	Balloon manufacture date

3 	Balloon launch point

4 	Surface observation

5 	Surface observation displacement from launch point

6 	Flight level observation

7 	Flight level termination point

8	Instrument manufacture date

9-30 Reserved

31 Missing value

The subsequent date fields then record year, month and day of the manufacturing date of the instrument.

(18)	If 12 characters is insufficient to recorder both name and version, the field width can be extending with the descriptor 2-08-YYY where YYY is the number of characters of the total field. For example, for a name and version number that requires 16 characters, the descriptor would be 2-08-016 and would preceed the 0-25-061 descriptor in the message format part of the BUFR message.

Add proposed template for buoy data including directional and non-directional wave data for validation.

| 3 | 06 | 032 | 0 | 02 | 032 | Indicator for digitization |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 0 | 02 | 033 | Method of salinity/depth measurement |
|  |  |  | 1 | 03 | 000 | Delayed replication of 3 descriptors |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |
|  |  |  | 0 | 07 | 062 | Depth below sea/water surface |
|  |  |  | 0 | 22 | 043 | Subsurface s Sea/water temperature |
|  |  |  | 0 | 22 | 062 | Salinity |
|  |  |  | 0 | 22 | 066 | Water Conductivity |

Add 3 15 006 as an alternative to 3 15 002 having 3 06 004 replaced by 3 06 032 for validation.

|  |  |  |  |  |  | (Typically reported underwater sounding without optional fields) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 15 | 006 | 0 | 01 | 011 | Ship or mobile land station identifier Ship’s call sign |
|  |  |  | 3 | 01 | 011 | Year, month, day Date |
|  |  |  | 3 | 01 | 012 | Hour, minute Time |
|  |  |  | 3 | 01 | 023 | Latitude/ and longitude (coarse accuracy) |
|  |  |  | 3 | 06 | 032 | Buoy data including directional and non-directional wave data Depth, temperature, salinity |

- 2008-3.1.15(JM-MTDCF/DRC)/Templates for the wave observations from different platforms suitable for WAVEOB data (revision 4)

<para 4.1>

TM 308015 – BUFR template for WAVEOB data expressed as frequency (Ia=0 in FM-65 WAVEOB)

| # | Descriptor | Name (unit) | Expanded descriptors | Remark, Corresponding groups in FM-65 WAVEOB |
| --- | --- | --- | --- | --- |
|  |  | Identification |  |  |
| 1 | 001003 | WMO Region number/geographical area | 001003 | A1 - First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO Region sub-area | 001020 | bw - Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | nb - Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 001011 | Ship or mobile land station identifier | 001011 | D …… D |
| 5 | 001007 | Satellite Identifier | 001007 | I6 I6 I6 |
| 6 | 001001 | WMO block number | 001001 | II |
| 7 | 001002 | WMO station number | 001002 | iii – IIiii only apply to fixed sea stations. |
| 8 | 002044 | Indicator for method of calculating spectral wave data. | 002044 | Im – TAC code table 1744, BUFR code table 2044 |
| 9 | 002045 | Indicator for type of platform | 002045 | Ip – TAC code table 1747, BUFR code table 2045 |
| 10 | 301011 | Year, month, day Date | 004001 (year) 004002 (month) 004003 (day) | J - Date of observation MM YY |
| 11 | 301012 | Hour, minute Time | 004004 (Hour) 004005 (Minutes) | GG - Time of observation Gg |
| 12 | 301021 | Latitude and /longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Qc La La La La Lo Lo Lo Lo Lo |
|  |  | Basic data (WAVEOB Section 0) |  |  |
| 13 | 022063 | Total water depth (m) | 022063 | 1hhhh |
| 14 | 022076 | Direction of coming dominant waves (deg) | 022076 | 9dd dd - section 0 |
| 15 | 022077 | Directional spread of dominant wave (deg) | 022077 | ds ds - section 0 |
| 16 | 022094 | Total number of wave bands | 022094 | 111 BT BT – Section 1 |
| 17 | 025043 | Wave sampling interval (Time, s) | 025043 | SSSS – Section 1 |
| 18 | 022078 | Duration of wave record (s) | 022078 | D’D’D’D’ – Section 1 |
| 19 | 105002 | Replecate ion 5 descriptors 2 times | 105002 | Replicate over sensor type |
| 20 | 002046 | Wave measurement instrumentation Type of wave sensor | 002046 | Code table 2046, 1=heave sensor. 2=slope sensor. |
| 21 | 022070 | Significant wave height (m) | 022070 | 2HsHsHsHs or 6HseHseHseHse - section 0 |
| 22 | 022071 | Spectral peak wave period (s) | 022071 | 3PpPpPpPp or 7PspPspPspPsp - section 0 |
| 23 | 022073 | Maximum wave height | 022073 | 4Hm Hm Hm Hm |
| 24 | 022074 | Average wave period (s) | 022074 | 5PaPaPaPa or 8PsaPsaPsaPsa - section 0 |
|  |  | Spectral Data (WAVEOB Section 1 – 5) |  |  |
| 25 | 121000 | Delayed Replication of 21 descriptors | 121000 | Replication over sensor type |
| 26 | 031001 | Delayed descriptor replication factor | 031001 | (0,1,2) normally 1 |
| 27 | 002046 | Wave measurement instrumentation Type of wave sensor | 002046 | Code table 2046, 1=heave sensor. 2=slope sensor. |
| 28 | 022082 | Maximum non-directional spectral wave density (m2/Hz) | 022082 | Cm Cm Cm - Section 2 or Csm Csm Csm - Section 3 |
| 29 | 022084 | Band containing maximum non-directional spectral wave density | 022084 | nmnm - Section 2 or nsmnsm - Section 3 |
| 30 | 116000 | Delayed replication 16 descriptors | 116000 | Replication over bands. |
| 31 | 031001 | Replication Factor | 031001 | 111 BT BT – Section 1 (Num of band) |
| 32 | 022080 | Waveband central frequency (Hz) | 022080 | 1f1 f1 f1 f1 x …. – Section 1 |
| 33 | 022085 | Spectral wave density ratio | 022085 | 1 c1 c1 c2 c2 …. – Section 2 or 1 cs1 cs1 cs2 cs2 …. – Section 3 |
| 34 | 022086 | Mean direction from which waves are coming (deg) | 022086 | 1da1da1 – Section 4 |
| 35 | 022087 | Principal direction from which waves are coming (deg) | 022087 | da2da2 - Section 4 |
| 36 | 022088 | First normalized polar coordinate from Fourier coefficients | 022088 | r1r1 - Section 4 |
| 37 | 022089 | Second normalized polar coordinate from Fourier coefficients | 022089 | r2r2 - Section 4 |
| 38 | 103000 | Delayed replication of 3 descriptors | 103000 |  |
| 39 | 031001 | Delayed descriptor replication factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 1 (Directional) |
| 40 | 022090 | Non-directional spectral estimate by wave frequency (m2/Hz) | 022090 | 1 A1 A1 A1 x…… - Section 5 |
| 41 | 022186 | Direction from which waves are coming (deg) | 022186 | 1 d1 d1 - Section 5 |
| 42 | 022187 | Directional spread of wave (deg) | 022187 | ds ds - Section 5 |
| 43 | 103000 | Delayed replication of 3 descriptors | 103000 |  |
| 44 | 031001 | Delayed descriptor replication factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 0 (Non-Drectional) |
| 45 | 022092 | Directional Spectral Estimate By Wave Frequency (M2/Hz/Radian) | 022092 | 1 A1 A1 A1 x…… - Section 5 |
| 46 | 022186 | Direction from which waves are coming (deg) | 022186 | 1 d1 d1 - Section 5 |
| 47 | 022187 | Directional spread of wave (deg) | 022187 | ds ds - Section 5 |

TM 308016 - BUFR template for WAVEOB data expressed as the wave number (Ia=1 in FM-65 WAVEOB).

| # | Descriptor | Name | Expanded descriptors | Remark, Corresponding groups in FM-65 WAVEOB |
| --- | --- | --- | --- | --- |
|  |  | Identification |  |  |
| 1 | 001003 | WMO Region number/geographical area | 001003 | A1 - First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO Region sub-area | 001020 | bw - Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | nb - Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 001011 | Ship or mobile land station identifier | 001011 | D …… D |
| 5 | 001007 | Satellite identifier | 001007 | I6 I6 I6 |
| 6 | 001001 | WMO block number | 001001 | II |
| 7 | 001002 | WMO station number | 001002 | iii – IIiii only apply to fixed sea stations. |
| 8 | 002044 | Indicator for method of calculating spectral wave data. | 002044 | Im – TAC code table 1744, BUFR code table 2044 |
| 9 | 002045 | Indicator for type of platform | 002045 | Ip – TAC code table 1747, BUFR code table 2045 |
| 10 | 301011 | Year, month, day Date | 004001 (year) 004002 (month) 004003 (day) | J - Date of observation MM YY |
| 11 | 301012 | Hour, minute Time | 004004 (Hour) 004005 (Minutes) | GG - Time of observation Gg |
| 12 | 301021 | Latitude and /longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Qc La La La La Lo Lo Lo Lo Lo |
|  |  | Basic data (WAVEOB Section 0) |  |  |
| 13 | 022063 | Total water depth (m) | 022063 | 1hhhh |
| 14 | 022076 | Direction of coming dominant waves (deg) | 022076 | 9dd dd - section 0 |
| 15 | 022077 | Directional spread of dominant wave (deg) | 022077 | ds ds - section 0 |
| 16 | 022094 | Total number of wave bands | 022094 | 111 BT BT – Section 1 |
| 17 | 025044 | Wave sampling interval (Space, m) | 025044 | SSSS – Section 1 |
| 18 | 022079 | Length of wave record (m) | 022079 | D’D’D’D’ – Section 1 |
| 19 | 105002 | Replecateion 5 descriptors 2 times | 105002 | Replication over sensor type |
| 20 | 002046 | Wave measurement instrumentation Type of wave sensor | 002046 | Code table 2046, 1=heave sensor. 2=slope sensor. |
| 21 | 022070 | Significant wave height (m) | 022070 | 2HsHsHsHs or 6HseHseHseHse - section 0 |
| 22 | 022072 | Spectral peak wave length (m) | 022072 | 3PpPpPpPp - section 0 |
| 23 | 022073 | Maximum wave height | 022073 | 4Hm Hm Hm Hm |
| 24 | 022075 | Average wave length (m) | 022075 | 5PaPaPaPa - section 0 |
|  |  | Spectral Data (WAVEOB Section 1 – 5) |  |  |
| 25 | 121000 | Delayed replication of 21 descriptor | 121000 | Replication over sensor type |
| 26 | 031001 | Delayed descriptor replication factor | 031001 | (0,1,2) normally 1 |
| 27 | 002046 | Wave measurement instrumentation Type of wave sensor | 002046 | Code table 2046, 1=heave sensor. 2=slope sensor. |
| 28 | 022083 | Maximum non-directional spectral wave number (m3) | 022083 | Cm Cm Cm - Section 2 or Csm Csm Csm - Section 3 |
| 29 | 022084 | Band containing maximum non-directional spectral wave density | 022084 | nmnm - Section 2 or nsmnsm - Section 3 |
| 30 | 116000 | Delayed replication of 16 descriptors | 116000 | Replication over band |
| 31 | 031001 | Delayed descriptor replication factor | 031001 | 111 BT BT – Section 1 (Num of band) |
| 32 | 022081 | Waveband central wave number (1/m) | 022081 | 1f1 f1 f1 f1 x …. – Section 1 |
| 33 | 022085 | Spectral wave density ratio | 022085 | 1 c1 c1 c2 c2 …. – Section 2 or 1 cs1 cs1 cs2 cs2 …. – Section 3 |
| 34 | 022086 | Mean direction from which waves are coming (deg) | 022086 | 1da1da1 - Section 4 |
| 35 | 022087 | Principal direction from which waves are coming (deg) | 022087 | da2da2 - Section 4 |
| 36 | 022088 | First normalized polar coordinate from Fourier coefficients | 022088 | r1r1 - Section 4 |
| 37 | 022089 | Second normalized polar coordinate from Fourier coefficients | 022089 | r2r2 - Section 4 |
| 38 | 103000 | Delayed replication of 3 descriptors | 103000 |  |
| 39 | 031001 | Delayed descriptor replication factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 1 (Directional) |
| 40 | 022091 | Non-directional spectral estimate by wave number (m3) | 022091 | 1 A1 A1 A1 x…… - Section 5 |
| 41 | 022186 | Direction from which waves are coming (deg) | 022186 | 1 d1 d1 - Section 5 |
| 42 | 022187 | Directional spread of wave (deg) | 022187 | ds ds - Section 5 |
| 43 | 103000 | Delayed replication of 3 Descriptors | 103000 |  |
| 44 | 031001 | Delayed descriptor replication factor | 031001 | n - Section 5 (Num of directions counted); =0 if Ib = 0 (Non-Drectional) |
| 45 | 022093 | Directional dpectral estimate by eave number (m4) | 022093 | 1 A1 A1 A1 x…… - Section 5 |
| 46 | 022186 | Direction from which waves are coming (deg) | 022186 | 1 d1 d1 - Section 5 |
| 47 | 022187 | Directional spread of wave (deg) | 022187 | ds ds - Section 5 |

Notes:

1. Because WAVEOB can be reported from different platform, the descriptors for identification of all possible platforms are all included in the template. The irrelevant descriptors for identification shell be set to missing.

2. New descriptors

022186 is introduced to express the direction of “any wave”, as appose to the direction of “dominant wave” (022076), “mean direction” (022086), and “principal direction” (022087).

022187 is introduced to express the directional spread of “any wave”, as appose to the directional spread of “dominant wave” (022077).

| TABLE REFERENCE | TABLE ELEMENT NAME | BUFR | CREX |
| --- | --- | --- | --- |
|  |  | UNIT | SCALE | REFERENCE VALUE | DATA WIDTH (Bits) | UNIT | SCALE | DATA WIDTH (Characters) |
| F | X | Y |  |  |  |  |  |  |  |  |
| 0 | 22 | 186 | Direction from which waves are coming | Degree true | 0 | 0 | 9 | Character | 0 | 3 |
| 0 | 22 | 187 | Directional spread of wave | Degree | 0 | 0 | 9 | Character | 0 | 3 |

- 2006-5.4.3(JM-MTDCF/DRC)/BUFR template for buoy wave data <para 4.1>

Proposed new template for buoy data, including directional and non-directional wave data

| # | Descriptor | Name | Expanded descriptors | Comment, encoding |
| --- | --- | --- | --- | --- |
| 1 | 001003 | WMO region | 001003 | First digit of WMO number (e.g. 62024 => 6) |
| 2 | 001020 | WMO region sub-area | 001020 | Second digit of WMO number (e.g. 62024 => 2) |
| 3 | 001005 | Buoy/platform identifier | 001005 | Last 3 digits of WMO number (e.g. 62024 => 024) |
| 4 | 002001 | Type of station | 002001 | 1=Manned station |
| 5 | 002036 | Buoy type | 002036 | 1=Fixed buoy |
| 6 | 002149 | Type of data buoy | 002149 | 16=unspecified moored buoy 24=Omnidirectional waverider 25=Directional waverider |
| 7 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | Date of observation |
| 8 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | Time of observation |
| 9 | 008021 | Time significance | 008021 | Value = 26 (time of last known position) |
| 10 | 301011 | Date | 004001 (year) 004002 (month) 004003 (day) | Date of last known position coded here; coded missing for fixed station |
| 11 | 301012 | Time | 004004 (Hour) 004005 (Minutes) | Time of last known position coded here; coded missing for fixed station |
| 12 | 008021 | Time significance | 008021 | Value = “missing” |
| 13 | 301021 | Latitude and longitude (high accuracy) | 005001 (Lat; high accuracy) 006001 (Lon; high accuracy) | Coarse accuracy descriptors (005002 and 006002 respectively) were used with PDE buoys |
| 14 | 027004 | Alternate latitude (high accuracy) | 027004 | Coded if Argos is used for location; otherwise coded missing |
| 15 | 028004 | Alternate longitude (high accuracy) | 028004 | Coded if Argos is used for location; otherwise coded missing |
| 16 | 007030 | Height of station above MSL | 007030 |  |
| 17 | 001051 | Platform Transmitter ID | 001051 | If Argos is used, Argos ID number; |
| 18 | 002148 | Data collection and/or Location system | 002148 | 1=Argos 2=GPS Coded missing if none |
| 19 | 001012 | Platform drift direction | 001012 | Coded missing for moored buoys |
| 20 | 001014 | Platform drift speed | 001014 | Coded missing for moored buoys |
| 21 | 002040 | Method of removing platform direction and speed from current | 002040 | Coded missing for moored buoys |
| 22 | 033022 | Quality of buoy satellite transmission | 033022 | 0=Good 1=Dubious 3=missing |
| 23 | 033023 | Quality of buoy location | 033023 | 0=Reliable 1=Last known position 2=Dubious 3=missinh |
| 24 | 033027 | Location quality class (range of radius of 66% confidence) | 033027 | 0: >= 1500m 1: 500m to 1500m |
| 25 | 022063 | Total water depth | 022063 | Mooring depth; otherwise coded missing |
| 26 | 302021 | Waves | 022001 (direction of waves) 022011 (period of waves) 022021 (height of waves) |  |
| 27 | 302022 | Wind waves | 022002 (direction wind wv) 022012 (period wind wv) 022022 (height wind wv) |  |
| 28 | 302023 | Swell waves | 022003 (direction swell wv) 022013 (period swell wv) 022023 (height swell wv) |  |
| 29 | 008081 | Type of equipment (observing platform) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=3: Equipment = “platform” |
| 30 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Platform battery voltage |
| 31 | 008081 | Type of equipment (transmitter) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=1: Equipment = “transmitter” |
| 32 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Transmitter battery voltage |
| 33 | 008081 | Type of equipment (receiver) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=2: Equipment = “receiver” |
| 34 | 025026 | Battery voltage | 025026 | (New descriptor, Volts, scale=0, ref=0, bits=6) Receiver battery voltage |
| 35 | 008081 | Type of equipment – value Missing = cancel | 008081 | 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value = “missing” |
| 36 | 002034 | Drogue type | 002034 | Coded missing for moored buoys |
| 37 | 022060 | Lagrangian drifter drogue status | 022060 | (New descriptor, scale=0, ref=0, bits=3) 0=detached 1=attached 3=missing Coded missing for moored buoys |
| 38 | 007070 | Drogue depth | 007070 | Coded missing for moored buoys |
| 39 | 002190 | Lagrangian drifter submergence | 002190 | Coded missing for moored buoys |
| 40 | 025086 | Depth correction indicator for sub-surface measurements along cable | 025086 | 0=depths are not corrected 1=depths are corrected 3=missing |
| 41 | 002035 | Cable length | 002035 | Depth of hydrostatic pressure sensor at bottom of cable |
| 42 | 002168 | Hydrostatic pressure of lower end of cable | 002168 |  |
| 43 | 020031 | Ice deposit (thickness) | 020031 | Ice thickness |
| 44 | 002038 | Method of temperature and/or velocity measurement | 002038 | e.g. 2=hull contact sensor 8=thermistor chain |
| 45 | 306004 | Digitization, depth/salinity method, depths/salinities/temperatures | 002032 (indicator for digit) 002033 (method sal/depth) 103000 (delayed repl 3 desc) 031001 (replication factor) 007062 (depth) 022043 (sea temperature) 022062 (salinity) | Replication factor indicates number of (depth, temp., salinity) data points that are encoded |
| 46 | 002030 | Method of current measurement | 002030 |  |
| 47 | 306005 | Time/duration of current measurement, depths/directions/speeds | 002031 (method current) 103000 (delayed repl 3 desc) 031001 (replicationfactor) 007062 (depth) 022004 (direction current) 022031 (speed current) | Replication factor indicates number of (pepth, dir, speed) data points that are encoded |
| 48 | 007031 | Height of barometer above MSL | 007031 |  |
| 49 | 008081 | Type of equipment (sensor) | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value=0: Equipment = “sensor” |
| 50 | 012064 | Instrument temperature | 012064 | Temperature of air pressure sensor |
| 51 | 302001 | Pressure and pressure change | 010004 (pressure at station) 010051 (MSLP) 010061 (3-hour tendency) 010063 (tend. Characteristic) | Mean Seal Level Pressure to be computed based upon pressure at station level and sensor height |
| 52 | 008081 | Type of equipment – value missing = cancel | 008081 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor 1=transmitter 2=receiver 3=observing system Here coded with value = “missing” |
| 53 | 007032 | Height of sensor above marine deck platform (for temp.&hum. measurement) | 007032 | Height of thermometer above marine desck |
| 54 | 007033 | Height of sensor above water surface (for temp.&hum. measurement) | 007033 | Height of thermometer (assumed should be coded with value = 2 metres for PDE buoys) |
| 55 | 012101 | Dry-bulb temperature (scale 2) | 012101 | Dry-bulb temperature at 2m (012004) was used for PDE buoys |
| 56 | 012103 | Dew-point temperature (scale 2) | 012103 |  |
| 57 | 013003 | Relative humidity | 013003 |  |
| 58 | 007032 | Height of sensor above marine deck platform (for wind measurement) | 007032 | Real height of anemometer above marine deck |
| 59 | 007033 | Height of sensor above water surface (for wind measurement) | 007033 | Real height of anemometer above average water surface |
| 60 | 008082 | Artificial correction of sensor height to another value | 008082 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor height is not corrected 1=sensor height is artificially corrected 7=missing Assumed should be coded to value 1 for PDE buoys |
| 61 | 007033 | Height of sensor above water surface (here height of anemometer to which it is artificially corrected) | 007033 | Here height of anemometer to which it is artificially corrected Assumed should be coded with value = 10 metres for PDE buoys |
| 62 | 002169 | Anemometer type | 002169 | e.g. 0=rotor 1=propeller rotor |
| 63 | 002002 | Type of instrumentation for wind measurement | 002002 |  |
| 64 | 008021 | Time significance | 008021 | Value = 2 (time averaged) |
| 65 | 004025 | Time period in minutes | 004025 | Value for averaging period (e.g. 10 minutes) |
| 66 | 011001 | Wind direction | 011001 | Wind direction at 10m (011011) was used with PDE buoys |
| 67 | 011002 | Wind speed | 011002 | Wind speed at 10m (011012) was used with PDE buoys |
| 68 | 008021 | Time significance | 008021 | Value = 23 (monitoring period) |
| 69 | 004025 | Time period in minutes | 004025 | Period during which gust is being monitored prior to observation time |
| 70 | 011043 | Maximum wind gust direction | 011043 |  |
| 71 | 011041 | Maximum wind gust speed | 011041 |  |
| 72 | 008082 | Artificial correction of sensor height to another value (set to missing to reset previous value) | 008082 | (New descriptor, scale=0, ref=0, bits=6) 0=sensor height is not corrected 1=sensor height is artificially corrected 7=missing Here coded with value = “missing” |
| 73 | 007033 | Height of sensor above water surface (set to missing to cancel previous value) | 007033 | Value=”missing”: Redefine height to previous level |
| 74 | 007032 | Height of sensor above marine deck platform (for precipitation measurement) | 007032 | Here height of precipitations |
| 75 | 004024 | Time period in hours | 004024 | Period during which precipitation is being monitored prior to observation time |
| 76 | 013011 | Total precipitation | 013011 | Total precipitation during monitoring period |
| 77 | 007032 | Height of sensor above marine deck platform (set to missing to cancel the previous value) | 007032 | Value = “missing” |
| 78 | 008021 | Time significance | 008021 | Value = 3 (accumulated) |
| 79 | 004024 | Time period in hours | 004024 | Period during which global radiation is being accumulated prior to observation time |
| 80 | 014021 | Global radiation, integrated over period specified | 014021 |  |
| 81 | 008021 | Time significance | 008021 | Value = “missing” |
| 82 | 025028 | Operator or manufacturer defined parameter (#1) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 1 |
| 83 | 025028 | Operator or manufacturer defined parameter (#2) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 2 |
| 84 | 025028 | Operator or manufacturer defined parameter (#3) | 025028 | (New descriptor, scale=1, ref=-16384, bits=15) Housekeeping parameter number 3 |
| 85 | 022073 | Maximum wave height | 022073 |  |
| 86 | 022070 | Significant wave height | 022070 | HsHsHsHs in WAVEOB section 0 |
| 87 | 022074 | Average wave period | 022074 | PaPaPaPa in WAVEOB section 0 |
| 88 | 022076 | Direction from which dominant waves are coming | 022076 | dddd in WAVEOB section 0 |
| 89 | 022077 | Directional spread of dominant waves | 022077 | dsds in WAVEOB section 0 |
| 90 | 022071 | Spectral peak wave period | 022071 | PpPpPpPp in WAVEOB section 0 |
| 91 | 022078 | Duration of wave record | 022078 | D’D’D’D’ in WAVEOB section 1 |
| 92 | 022082 | Maximum non-directional spectral wave density | 022082 | CmCmCm in WAVEOB section 2 |
| 93 | 022084 | Band containing maximum non-directional spectral wave density | 022084 | nmnm in WAVEOB section 2 |
| 94 | 025043 | Wave sampling interval (time) | 025043 | SSSS in WAVEOB (Ia=0) |
| 95 | 025044 | Wave sampling interval (space) | 025044 | SSSS in WAVEOB (Ia=1) |
| 96 | 112000 | Delayed replication of 12 descriptors | 112000 | Replication for frequency bands. PDE buoys did not used delayed replication |
| 97 | 031001 | Replication factor | 031001 | Delayed replication therefore added. Replication factor = Number of frequency bands |
| 98 | 022080 | Waveband central frequency | 022080 | fnfnfn in WAVEOB section 1 |
| 99 | 201134 | Add 6 bits to data width | 201134 |  |
| 100 | 022096 | Spectral band width | 022096 | Here coded with 10 bits as descriptor requires 4 bits and we have 6 bits added due to previous operation descriptor |
| 101 | 201000 | Reset data width to normal | 201000 |  |
| 102 | 022090 | Non-directional spectral estimate by wave frequency | 022090 | AnAnAn in WAVEOB (Ib=0) section 5 |
| 103 | 022086 | Mean direction from which waves are coming | 022086 | da1da1 in WAVEOB section 4 |
| 104 | 022087 | Principal direction from which waves are coming | 022087 | da2da2 in WAVEOB section 4 |
| 105 | 022095 | Directional spread of individual waves | 022095 |  |
| 106 | 022085 | Spectral wave density ratio | 022085 | cncn in WAVEOB section 2 |
| 107 | 022088 | First normalized polar coordinate from Fourier coefficients | 022088 | r1r1 in WAVEOB section 4 |
| 108 | 022089 | Second normalized polar coordinate from Fourier coefficients | 022089 | r2r2 in WAVEOB section 4 |
| 109 | 022092 | Directional spectral estimate by wave frequency | 022092 | AnAnAn in WAVEOB (Ib=1) section 5 |

# Text boxes

As of 7 May 2015

TDCF Reports

TAC reports

TDCF Reports

TAC reports

TDCF Reports

TAC reports

ANNEX II