| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING TOKYO, JAPAN, 1 - 5 JULY 2013 |  | IPET-DRMM-I / Doc. 2.2 (6) (xx. x. 2013) ------------------------- ITEM 2.2 ENGLISH ONLY |
| --- | --- | --- |

GRIB templates for reforecast ensemble data

Submitted by by

Enrico Fucile (ECMWF)

Eizi Toyoda (JMA)

_______________________________________________________________________

Summary and Purpose of Document

New GRIB product definition templates are proposed to represent reforecast data from an ensemble forecast system and for continuous or non-continuous time interval

_______________________________________________________________________

ACTION PROPOSED

The Team is invited to evaluate the proposal and accept it for validation.

ANNEX:

DISCUSSIONS

A WWRP/THORPEX-WCRP joint research project, Subseasonal to Seasonal Prediction Project (http://www.wmo.int/pages/prog/arep/wwrp/new/S2S_project_main_page.html) has been established to improve forecast skill and understanding on the subseasonal to seasonal timescale, and promote its uptake by operational centres and exploitation by the applications community.

Reforecasts (sometimes known as hindcasts) are needed in the subseasonal to seasonal range as the model error is too large to be ignored. Therefore, there is the need to represent reforecast data in GRIB Edition 2.

The objective of this proposal is to submit for approval the following two new templates:

- Template 4.60 – Individual ensemble reforecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time

- Template 4.61 – Individual ensemble reforecast, control and perturbed, at a horizontal level or in a horizontal layer, in a continuous or non-continuous interval

PROPOSALS

New Templates

The following new templates are proposed:

| Template 4.60 – Individual ensemble reforecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time |
| --- |
| Octet No. | Contents |

10        		Parameter category (see Code Table 4.1)

11        		Parameter number (see Code Table 4.2)

12        		Type of generating process (see Code Table 4.3)

13        		Background generating process identifier (defined by originating centre)

14        		Analysis or forecast generating process identified

15-16   		Hours of observational data cutoff after reference time (see Note 1)

17        		Minutes of observational data cutoff after reference time

18        		Indicator of unit of time range (see Code Table 4.4)

19-22   		Forecast time in units defined by octet 18

23 			Type of first fixed surface (see Code table 4.5)

24 			Scale factor of first fixed surface

25–28 		Scaled value of first fixed surface

29 			Type of second fixed surface (see Code table 4.5)

30 			Scale factor of second fixed surface

31–34 		Scaled value of second fixed surface

35 			Type of ensemble forecast (see Code table 4.6)

36 			Perturbation number

37 			Number of forecasts in ensemble

38–39 		Year of Model Version (see Note 2)

40 			Month of Model Version

41 			Day of Model Version

42 			Hour of Model Version

43 			Minute of Model Version

44 			Second of Model Version

Notes:

(1) Hours greater than 65534 will be coded as 65534.

(2) This is the date when the reforecast is produced with a particular version of the model

Template 4.61 – Individual ensemble reforecast, control and perturbed, at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

| Octet No. | Contents |
| --- | --- |

10		Parameter category (see Code Table 4.1)

11		Parameter number (see Code Table 4.2)

12		Type of generating process (see Code Table 4.3)

13		Background generating process identifier (defined by originating centre)

14		Forecast generating process identifier (defined by originating centre)

15-16	Hours after reference time of data cut-off (see Note 1)

17		Minutes after reference time of data cut-off

18		Indicator of unit of time range (see Code Table 4.4)

19-22	Forecast time in units defined by octet 18 (see Note 2)

23		Type of first fixed surface (see Code Table 4.5)

24		Scale factor of first fixed surface

25-28	Scaled value of first fixed surface

29		Type of second fixed surface (see Code Table 4.5)

30		Scale factor of second fixed surface

31-34	Scaled value of second fixed surface

35		Type of ensemble forecast (see Code Table 4.6)

36		Perturbation number

37		Number of forecasts in ensemble

38-39	Year of Model Version (see Note 4)

40 		Month of Model Version

41 		Day of Model Version

42 		Hour of Model Version

43 		Minute of Model Version

44 		Second of Model Version

45-46	Year of end of overall time interval

47		Month of end of overall time interval

48		Day of end of overall time interval

49		Hour of end of overall time interval

50		Minute of end of overall time interval

51		Second of end of overall time interval

52		n - number of time range specifications describing the time intervals used

to calculate the statistically- processed field

53-56	Total number of data values missing in statistical process

57-68	Specification of the outermost (or only) time range over which statistical

processing is done

57		Statistical process used to calculate the processed field from the field at

each time increment during the time range (see Code Table 4.10)

58		Type of time increment between successive fields used in the statistical

processing (see Code Table 4.11)

59		Indicator of unit of time for time range over which statistical processing is

done (see Code Table 4.4)

60-63	Length of the time range over which statistical processing is done, in units

defined by the previous octet

64		Indicator of unit of time for the increment between the successive fields

used (see Code Table 4.4)

65-68	Time increment between successive fields, in units defined by the previous

octet (see Note 3)

69-nn	These octets are included only if n>1, where nn=56 + 12 x n

69-80	As octets 57 to 68, next innermost step of processing

81-nn	Additional time range specifications, included in accordance with the value

of n. Contents as octets 57 to 68, repeated as necessary

Notes:

(1) Hours greater than 65534 will be coded as 65534.

(2) The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3) An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples. Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a raingauge. The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 51, 63, 75 ...). For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

(4) This is the date when the reforecast is produced with a particular version of the model

Changes to existing table

The following new entries are to be added to code table 4.0.

Code table 4.0

Code		Meaning

60	Individual ensemble reforecast, control and perturbed, at a horizontal level or in a horizontal layer at a point in time

61	Individual ensemble reforecast, control and perturbed, at a horizontal level or in a horizontal layer, in a continuous or non-continuous interval

Example

A re-forecast is a forecast starting from a date in the past in which a recent version of the model is used.

For example the only difference between a 10 days forecast starting at 12:00 on the 15th June 1998 and a re-forecast of the same period (10 days from 12:00 15th June 1998) is that the re-forecast is produced with a newer version of the model which was not available at the time of the forecast. It could use as an example the model which is operational today.

Therefore in relation to the re-forecast we can say that there is another date which is important to uniquely define the product, which is the date when the run is executed with a particular version of the model. This second date which we are calling "model version date" is the date of the model version and is representing the time when the forecast was executed.

This is an example using the proposed PDT 4.61 to represent step 12 of the re-forecast starting at 00:00:00 13th June 1993 produced with the model version which is operational at 00:00:00 13th June 2013.

| section | octet | content | value | comments |
| --- | --- | --- | --- | --- |
| 1 | 13-14 | Reference Year | 1993 | start of forecast |
| 1 | 15 | Reference Month | 06 |  |
| 1 | 16 | Reference Day | 13 |  |
| 1 | 17 | Reference hour | 00 |  |
| 1 | 18 | Reference minute | 00 |  |
| 1 | 19 | Reference second | 00 |  |
| 4 | 18 | Indicator of unit of time range | 1 (hours) |  |
| 4 | 19-22 | Forecast time | 12 | step |
| 4 | 38-39 | Year of Model Version | 2013 | when the forecast is run == when the version of the forecast used was operational |
| 4 | 40 | Month of Model Version | 06 |  |
| 4 | 41 | Day of Model Version | 13 |  |
| 4 | 42 | Hour of Model Version | 00 |  |
| 4 | 43 | Minute of Model Version | 00 |  |
| 4 | 44 | Second of Model Version | 00 |  |