| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS ----------------------------- FIRST MEETING OF INTER-PROGRAMME EXPERT TEAM ON DATA REPRESENTATION MAINTENANCE AND MONITORING TOKYO, JAPAN, 1 - 5 JULY 2013 |  | IPET-DRMM-I / Doc. 3.2 (2) (27. VI. 2013) ------------------------- ITEM 3.2 ENGLISH ONLY |
| --- | --- | --- |

Proposal for a BUFR template for radar wind profiler

A harmonized implementation of the BUFR code for the exchange of radar windprofiler data in real time

Submitted by Alexander Haefele (MeteoSwiss), Myles Turp (UK Met Office),

and Volker Lehmann (DWD)

_______________________________________________________________________

Summary and Purpose of Document

A radar windprofiler (RWP) is a ground based remote sensing instrument to measure vertical profiles of wind. A number of RWP networks exist worldwide and the data are encoded in BUFR to be exchanged over the GTS. However, each of these networks uses a different implementation of the BUFR code. In this document we propose a harmonized implementation of BUFR for RWP data. The proposal is based on a review of the existing implementations and on data user requirements.

This proposal is an initiative of the E-PROFILE programme of EUMETNET.

_______________________________________________________________________

ACTION PROPOSED

- To add the new descriptors and code table entries to the BUFR tables.

- To accept the proposed sequences as the official implementation of the BUFR code to exchange wind and virtual temperature data from RWP and RASS, respectively.

ANNEX: BUFR Specification for Active Ground Based Remote Sensing Profiler Data

PROPOSAL

A full description of the proposed implementation and the motivation behind can be found in the annex. Here, only a summary of the proposal is given. The proposal covers the implementation of wind data from RWP as well as virtual temperature data from RASS (Radio Acoustic Sounding System).

The proposed template is a “product message”, that contains only the essential information needed for a proper use of the remote sensing data. It is user oriented, clear and well defined, not leaving room for interpretation. Complementary information on hard- and software configuration and system performance for network monitoring as well as additional parameters like signal-to-noise ratio and raw data will be exchanged in a “raw data message”. The definition of a raw data BUFR template is beyond the scope of this document. Other formats than BUFR might be more suitable for the storage of  raw data, e.g. netCDF.

The proposed template is based on the review of all templates for RWP that were known to be currently in use and accessible to the authors. The proposed template  consists of a header part that is generic for active ground based remote sensing data and a replication (data) part that is specific for the measured quantity, e.g. wind, virtual temperature.

This proposal does not cover backscatter data from lidar since a consensus on how to represent this kind of information has not been found yet in the community. However, the full document in the annex discusses lidar backscatter data representation. The interested reader is invited to have a look at Section 3.7 and to make comments to the authors.

Radar Wind Profiler Data Sequence:

The replication part of the template relates to the number of descriptors to be repeated for each height level reported. For this we intend to use a Delayed Description Replication Factor  '1 XX YYY' The number of height levels reported is typically between 20 and 100.

| TABLE REFERENCE | TABLE REFERENCES | TABLE REFERENCES | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- | --- | --- |
| 3 09 021 |  |  |  | RWP Wind data (Product Data) NEW |
|  | 3 01 001 |  |  | WMO block and station numbers |
|  |  | 0 01 001 |  | WMO Block Number |
|  |  | 0 01 002 |  | WMO Station Number |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy), height of station) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  |  | 0 07 001 |  | Height of station |
|  | 3 01 014 |  |  | Time period |
|  |  | 1 02 002 |  | Replicate 2 descriptors 2 times |
|  |  | 3 01 011 |  | Year, month, day |
|  |  |  | 0 04 001 | Year |
|  |  |  | 0 04 002 | Month |
|  |  |  | 0 04 003 | Day |
|  |  | 3 01 012 |  | Hour, minute |
|  |  |  | 0 04 004 | Hour |
|  |  |  | 0 04 005 | Minute |
|  | 0 02 003 |  |  | Type of measuring Equipment used |
|  | 1 12 000 |  |  | Delayed replication of 12 descriptors |
|  | 0 31 001 |  |  | Delayed descriptor replication factor |
|  | 0 07 007 |  |  | Height |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy)) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  | 0 11 003 |  |  | U-Component |
|  | 0 11 099 |  |  | Uncertainty in U-Component NEW |
|  | 0 11 004 |  |  | V-Component |
|  | 0 11 100 |  |  | Uncertainty in V-Component NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 11 006 |  |  | W-Component |
|  | 0 11 101 |  |  | Uncertainty in W-Component NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 10 071 |  |  | Vertical Resolution NEW |
|  | 0 05 062 |  |  | Horizontal width of sampled volume NEW |

Comments on the header section can be found in the annex in Section 3.3.

Comments on the wind data replication section can be found in the annex in Section 3.5.

RASS Data Sequence:

| TABLE REFERENCE | TABLE REFERENCES | TABLE REFERENCES | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- | --- | --- |
| 3 09 022 |  |  |  | RASS virtual temperature (Product Data) NEW |
|  | 3 01 001 |  |  | WMO block and station numbers |
|  |  | 0 01 001 |  | WMO Block Number |
|  |  | 0 01 002 |  | WMO Station Number |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy), height of station) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  |  | 0 07 001 |  | Height of station |
|  |  | 0 02 003 |  | Type of measuring equipment |
|  | 3 01 014 |  |  | Time period |
|  |  | 1 02 002 |  | Replicate 2 descriptors 2 times |
|  |  | 3 01 011 |  | Year, month, day |
|  |  |  | 0 04 001 | Year |
|  |  |  | 0 04 002 | Month |
|  |  |  | 0 04 003 | Day |
|  |  | 3 01 012 |  | Hour, minute |
|  |  |  | 0 04 004 | Hour |
|  |  |  | 0 04 005 | Minute |
|  | 0 02 003 |  |  | Type of measuring Equipment used |
|  | 1 10 000 |  |  | Delayed replication of 10 descriptors |
|  | 0 31 001 |  |  | Delayed descriptor replication factor |
|  | 0 07 007 |  |  | Height |
|  | 3 01 022 |  |  | (Latitude/longitude (high accuracy)) |
|  |  | 0 05 001 |  | Latitude (high accuracy) |
|  |  | 0 06 001 |  | Longitude (high accuracy) |
|  | 0 12 007 |  |  | Virtual Temperature |
|  | 0 12 008 |  |  | Uncertainty in Virtual Temperature NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 11 006 |  |  | W-Component |
|  | 0 11 101 |  |  | Uncertainty in W-Component NEW |
|  | 0 33 002 |  |  | Quality information |
|  | 0 10 071 |  |  | Vertical Resolution NEW |
|  | 0 05 062 |  |  | Horizontal width of sampled volume NEW |

Code tables:

To represent in a slightly more specific way the different observation methods, the following entries are suggested to be added to code table 0 02 003:

| 10 | Doppler radar wind profiler |
| --- | --- |
| 11 | Doppler lidar wind profiler |
| 12 | Backscatter lidar |
| 13 | Spaced antenna wind profiler |

Summary of New Table B Descriptors

|  |  | BUFR | CREX |
| --- | --- | --- | --- |
| TABLE |  |  |  |  | DATA |  |  | DATA |
| REFERENCE | ELEMENT NAME | UNIT | SCALE | REFERENCE | WIDTH | UNIT | SCALE | WIDTH |
| F* X Y |  |  |  | VALUE | (Bits) |  |  | (Characters) |
| 0 11 099 | Uncertainty in U component | ms-1 | -1 | 0 | 10 | ms-1 | -1 | 4 |
| 0 11 100 | Uncertainty in V component | ms-1 | -1 | 0 | 10 | ms-1 | -1 | 4 |
| 0 11 101 | Uncertainty in W component | ms-1 | -2 | 0 | 10 | ms-1 | -2 | 4 |
| 0 10 071 | Vertical resolution | m | 0 | 0 | 14 | m | 0 | 5 |
| 0 05 062 | Horiz Width Of Sampled Volume | m | -1 | 0 | 20 | m | -1-1 | 7 |
| 0 12 008 | Uncertainty in Virtual Temperature | K | -1 | 0 | 10 | K | 0-1 | 4 |