TABLE

Characteristics of meteorological radars in Japan

| Characteristics | Radar C11 | Radar C12 | Radar C13 |
| --- | --- | --- | --- |
| Function | Meteorological | Meteorological | Meteorological |
| Platform type (airborne, shipborne, ground) | Ground | Ground | Ground |
| Tuning range (MHz) | 5 250-5 350 | 5 330-5 370 | 5 250-5 370 |
| Modulation | Conventional | With Doppler capability | With Doppler capability |
| Tx power into antenna | 250 kW peak | 250 kW peak | 200 kW peak |
| Pulse width (s) | 2.5-2.8 | 1 and 2.5 | 1 |
| Pulse rise/fall time (s) | 0.1-0.8 | 0.1-0.9 | 0.2-0.5 |
| Pulse repetition rate (pps) | 260 | 260-1 500 | 400-2 000 |
| Output device | Coaxial magnetron | Klystron | Klystron |
| Antenna pattern type (pencil, fan, cosecant-squared, etc.) | Pencil | Pencil | Pencil |
| Antenna type (reflector, phased array, slotted array, etc.) | Parabolic | Parabolic | Parabolic |
| Antenna polarization | Horizontal | Horizontal | Horizontal |
| Antenna main beam gain (dBi) | 41-45 | 42-45 | 48-50 |

TABLE (end)

| Characteristics | Radar C11 | Radar C12 | Radar C13 |
| --- | --- | --- | --- |
| Antenna elevation beamwidth (degrees) | 1-1.5 | 1-1.2 | 0.58-0.65 |
| Antenna azimuthal beamwidth (degrees) | 1-1.5 | 1- 1.2 | 0.6-0.65 |
| Antenna horizontal scan rate (degrees/s) | 24 | 6-36 | 12/24 |
| Antenna horizontal scan type (continuous, random, 360, sector, etc.) (degrees) | 360 | 360 | 360 |
| Antenna vertical scan rate (degrees/s) | –2 to +45 within 15 s | –2 to +45 within 15 s | -2 to +90 within 10 s |
| Antenna vertical scan type (continuous, random, 360, sector, etc.) (degrees) | –2 to +45 | –2 to +45 | –2 to +90 |
| Antenna side-lobe (SL) levels (1st SLs and remote SLs) (dB) | –25 to –33 | –26 to –35 | –28 to –34 |
| Antenna height (m) | 18-53 | 10-60 | 33-44 |
| Receiver IF 3 dB bandwidth (MHz) | 1.2 to 1.6 | 0.4 to 1.4 | 1.0 to 1.4 |
| Receiver noise figure (dB) | 1.2-5 | 1.9- 3 | 1-2 |
| Minimum discernable signal (dBm) | –108 to –114 | –110 to –114 | –110 to –112 |