CHAPTER  6

OTHER  RADIOCOMMUNICATION  SYSTEMS  FOR METEOROLOGICAL  ACTIVITIES

Page

6	Introduction		88

6.1	Broadcasting and dissemination systems		88

6.2	Examples of hydrological radio systems		89

6.2.1	Introduction		89

6.2.2	Representative hydrological systems		89

6.3	Other satellite systems		90

6.4	Fixed remote systems		90

6.5	Meteorological uses of radionavigation systems		91

6.5.1	Terrestrial services		91

6.5.2	Global navigation satellite systems (GNSSs)		91

6.6	Lightning detection and location systems		92

6.7	Ground-based remote sensing		95

# 6	Introduction

As discussed in Chapter 1 meteorological services need to collect observations from many remote sites, both on land and over the sea. Thus, the meteorological observing system is dependent on many other radiocommunication services in addition to the MetSat and MetAids services described in the earlier Chapters.It is also essential that meteorologists disseminate information and warnings to customers with minimal delay, whether in densely populated areas or in remote sparsely populated areas. Meteorological services are supplied to support maritime operations and to support aviation operations worldwide. The broadcasting and dissemination systems for meteorological products also utilize a wide range of radiocommunication services.

## 6.1	Dissemination systems

Of importance equal to the collection and archiving of weather data and the preparation of forecasts is the dissemination of these forecasts. Only by making these predictions available to the public can lives be saved, because only by knowing what is coming, can people take the steps necessary to protect their lives and property.

A number of specialized radio systems have been developed over the years by which forecasts and other meteorological data are distributed. Among the simplest of these is voice broadcasting. Typically using VHF radio, these systems require minimal equipment to be used by the general public. These systems serve to warn the public of threatened storms, floods, extreme temperatures and other natural and man-made hazards. Enhancements may be provided such as brief data transmissions accessible to deaf persons using special equipment. These systems may also be

designed to provide continuous data distribution, or to remain silent until triggered by an alert tone signifying a special event such as foul weather or other imminent hazard. Dissemination systems may be found in the fixed and mobile services, including maritime mobile service. Other dissemination systems operate via radio and television broadcasts and on MetSat downlinks.

Over the years, high frequency radio has been used by many administrations to provide weather and warning information to ships at sea and to aircraft. These systems typically provide voice transmissions and weather facsimile (WEFAX). However, the unreliable nature of HF has caused a transition of many such systems to satellite transmission.

## 6.2	Hydrologic radio systems

Floods are a natural and inevitable part of life in much of the world, and systems that can aid in predicting their occurrence, location and magnitude have saved many lives and a significant amount of property. Advance knowledge permits the evacuation of vulnerable populations, the construction of levees and dams, and the relocation of such valuable and vulnerable property as can be removed. Hydrologic systems typically are used to measure such things as precipitation, stream height and the depth of snow pack, all of which are useful in predicting flooding and in estimating the availability of water resources. They typically operate in the VHF or UHF bands in the fixed or mobile services.

Annual average flood damage in the United States of America alone now approaches $4 billion. Communities with persistent flood problems and those vulnerable to great losses when flooding does occur are continually seeking ways to minimize these losses. Automated hydrologic systems are an attractive solution because of their low cost of operation and because they can enhance the operation of other flood mitigation methods such as reservoir floodgate operation, flood insurance, or floodplain zoning.

An automated hydrologic system consists of event-reporting meteorological and hydrologic sensors, communications equipment, and computer software and hardware. In its simplest form, hydrologic sensors transmit coded signals, usually via very high frequency (VHF) and ultra high frequency (UHF) radio, to a base station, often through repeater

sites (see Fig. 6-1). The base station collects these coded signals and processes them into meaningful hydrometeorological information that can be displayed or tied to an alarm system and may notify emergency managers when preset criteria are exceeded.

Figure  6-1

Schematic of a hydrologic system

## 6.3	Fixed remote systems

Technical characteristics, including operating frequencies, of these systems vary widely and almost any of the meteorological RF bands may be used. Selection is frequently made based on the necessary bandwidth, which in turn is determined by the type and quantity of information to be carried. Fixed remote systems in meteorology serve a variety of purposes and operate in a number of RF bands. As would be expected from their name, they operate in fixed allocations. Typical uses include:

Voice keying or feeder links used to carry control or data signals to data dissemination transmitter sites, which are often located remotely (e.g. on mountain tops) to maximize their coverage areas.

Radar remoting used to carry radar return signals from the radar itself (frequently located remotely) to the office where data are processed. Operators also use RF for remote control of equipment at the radar site.

Data collection used to convey from remotely-located collection sites to a central repository or processing facility the data collected by hydrological and meteorological sensors used to measure wind, rain, temperature, snow depth, earth tremors (for the detection or prediction of earthquakes), or any number of other natural phenomena.

## 6.4	Meteorological uses of radionavigation systems

### 6.4.1	Terrestrial services

Meteorologists utilize radionavigation service signals for a variety of purposes. The use of Omega navigation signals (frequencies between 10 to 13 kHz) became widespread for tracking radiosondes in the MetAids service from about 1985 onwards until its termination of operation. This was because the radiosonde systems could be used with simple base station antenna, processing was automated and the systems were easy to maintain in remote locations. Loran-C signals at 100 kHz were also used for the same purpose and the use of Loran-C has increased in areas where suitable coverage has been maintained.

At the time of the closure of the Omega transmitters in 1997, more than 20% of the radiosonde systems in the WMO network had to be changed. Most of these ground systems were modified or replaced to use radiosondes receiving and processing GPS navigation signals.

### 6.4.2	Global navigation satellite systems (GNSSs)

GPS signals currently transmitted at 1 575.42 MHz (designated L1) and 1 227.6 MHz (designated L2) (and those of GLONASS and the proposed Galileo system) are used by meteorologists for the following purposes:

–	Location of mobile meteorological observing platforms:  for example radiosondes carried by weather balloons, dropsondes falling on parachutes, pilotless aircraft carrying meteorological sensors (see Chapter 3), or marine meteorological systems such as ocean buoys.

–	Very accurate synchronization of time:  between remote observing sites, as required for instance by lightning detection systems (see § 6.5).

–	Measurement of total water vapour in the atmosphere:  derived from the phase delay in the GPS signals received by ground based receivers. Computation of total water vapour requires extremely accurate computations of the position of the various GPS satellites and the timing of the satellite clocks. The position of the ground receiver must also be known very accurately. The GPS receivers are usually installed on a fixed mount suitable for accurate tracking of position on the Earth’s surface as well as providing meteorological information. Thus, the measurements may be produced as a byproduct of geodetic/ seismological observations or from sensors deployed specifically by meteorologists. Phase delays introduced in signal transmission through the ionosphere are identified from the differences in the phase delays between the two GPS frequencies, L1 and L2. If the surface

pressure and temperature are known, the dry hydrostatic phase delay introduced by the atmosphere can be estimated, and the remaining phase delay is then proportional to the total water vapour along the path to the satellite. The GPS sensor at the surface receives GPS signals from many directions in a short period of time. Thus, it is possible to estimate the total water vapour in the vertical, as well as gradients in total water vapour in the horizontal direction around the sensor. This technique has relevance for atmospheric propagation studies, since it allows a direct measurement of water vapour content along a slant path from the ground receiver to a satellite. See also [Coster et al., 1997].

–	Measurement of temperature and relative humidity as a function of height derived from space-based occultation measurements of the GPS signals:  in this application, a receiver on an independent satellite receives signals from the GPS constellation passing through the atmosphere at grazing incidence to the Earth’s surface. The refraction of the GPS signals is measured at a range of heights above the Earth’s surface. This allows the refractive index of the air to be derived as a function of height. At upper levels in the neutral atmosphere, relative humidity is very low and the refractive index of air can be assumed to be directly dependent on temperature. At levels closer to the surface below the tropopause, both temperature and partial pressure of water vapour influence the refractive index. The partial pressure of water vapour can be estimated if the temperature is already known from another source. The measurement of meteorological variables derived from this technique will have a better vertical resolution than the output from nadir viewing passive sensing radiometers, see Chapter 5, but will be averaged over relatively long distances in the horizontal. As with the total water vapour measurement, this technique requires very precise timing and knowledge of the position of both satellites. GNSS receivers are planned for the next generation of polar orbiting meteorological satellites.

## 6.5	Lightning detection systems

The need by operational meteorologists for remote sensing of lightning activity is rapidly increasing. Customer requirements are developing in conjunction with developments in the use of weather radar and meteorological satellite products, and have a high priority given the need to automate surface weather observations in many developed countries. The reliable operation of these systems has clear links to considerations of public safety on land, sea and air. Provision of an effective forecast service impacts the efficiency of commercial and defence activities. The safety of engineers working on power lines and personnel handling explosive devices are examples of activities that benefit from effective lightning forecasts.

The detection of lightning is a passive activity involving the use of radio receivers to detect wave fronts resulting from lightning. Data from individual detection sites may be distributed by any of the usual means including fixed links, telephone, Internet etc.

In current operational systems, the position of the lightning flash is either determined by measuring the direction of arrival of the associated spheric (atmospheric wave), or by measuring the time of arrival of the spheric, or a combination of both.

Measurements are required at more than three widely spaced sensing sites. The number of sites used in practice is usually larger than the minimum in order to improve the reliability of the reported locations. Time of arrival systems usually provide more accurate locations than direction finding systems when observing at ranges over several hundred kilometres. This is due to the direction of reception of skywaves sensed at the site, which usually differs slightly from the actual direction of the discharge, and will vary according to the state of the surface layers near the sensing site. Time of arrival systems usually rely heavily on GPS radionavigation signals to achieve the necessary time synchronization at the various sensing sites. All systems rely on cost effective, reliable communications from the remote sites to the central processor. The radio frequency used to locate lightning activity varies according to the area of monitoring required and the specific purpose of the system.

Very long-range locations at ranges of several thousand kilometres are achieved operationally by observing frequencies centred at 10 kHz (2-15 kHz) (see Fig. 6-3). In this system, the spherics are received at the remote outstations located around Europe [Lee, 1986] with spacings of up to 2 000 km apart. The spherics are Fourier analysed and time stamped at the sensor sites. The timed samples are immediately transmitted back to a central control station where the locations of the lightning discharges are computed from the differences in arrival times at the sites. Interference is extremely detrimental to the operation of the system and each outstation is equipped with adjustable notch filters to discriminate against local contamination.

Figure  6-3

Map of lightning data for one day for long range system

The most widely used operational systems cover a more limited area in detail. In this case, the spherics are observed at higher frequencies centred around 200 kHz (the wideband receivers used are most sensitive in the middle of their range of 1 kHz to 350 kHz), and the sensing sites are usually spaced between 100 km and 400 km apart, depending on whether the emphasis is on cloud-to-ground or cloud-to-cloud flashes. At these higher frequencies, a discharge from the cloud-to-ground can be identified by a pronounced rise in amplitude defining a leading edge to the spheric. The arrival of this leading edge can be accurately timed. The times from the network sites are transmitted to a central processor and used to compute the positions of the discharges. In many cases, the network arrival time differences are operated in conjunction with magnetic direction finding systems installed in earlier years. [Holle and Lopez, 1993] review different lightning detection systems and [Diendorfer et al., 1994] discuss observations from their own network in Austria.

In addition, in some areas it is necessary to observe all the electrical discharges associated with thunderstorm activity, both cloud-to-ground and cloud-to-cloud discharges. This is achieved by observing at very much higher frequencies (63 MHz and 225 MHz are used by the lightning detection and ranging system (LDAR), while the SAFIR system uses 110 to 118 MHz). =Figure 6-4 shows the real-time LDAR display. The storms must remain within line-of-sight if all the activity is to be observed. This requires that the ground sensors be located in a short baseline configuration – the sensors need to be 30 km apart, and about 50 m from the ground to fulfill the radar horizon criteria. However, in practice some operational systems observing cloud-to-cloud activity are operated with the ground sensors further apart, relying on the cloud-to-ground systems at lower frequencies to fill in the details of the discharges at lower levels.

The lower left panel of Fig. 6-4 shows LDAR data on a map of the East coast of Florida (partially shown). The data are then projected on an East-West vs. altitude panel (upper left) and a North-South vs. altitude panel (lower right, note that this panel is turned 90 on its side). A histogram (upper right) displays the data in five one-minute increments.

Figure  6-4

Real-time LDAR display

## 6.6	Ground-based remote sensing

Vertical atmospheric sounding using passive remote sensing from satellites has been discussed in detail in § 5.1. Meteorologists making detailed local forecasts or scientists investigating the planetary boundary have requirements for atmospheric sounding with better vertical resolution near the ground than can be provided by the satellite systems.

One method of providing this information is to use upward-looking passive remote sensing, with a radiometer mounted at the Earth’s surface. Radiometers are now commercially available for this purpose. These use a selection of channels in the oxygen band between 50 GHz and 58 GHz to produce a measurement of temperature structure. Channels between 21 GHz and 24 GHz are used

to provide information on the variation of water vapour in the vertical, and a window observation in the region of 30 GHz is used for cloud identification. Measurement of water vapour in the future may also benefit from additional observations in the lower wings of the water vapour absorption band at 183 GHz.

Although the channels for ground based remote sensing of temperature and humidity are in a similar region to passive satellite remote sensing, they are not identical to those used by satellites. At some frequencies, satellite remote sensing can safely share with terrestrial services, but ground-based radiometers may need protection. The number of ground-based radiometers in operation is still small, but if current developments are successful, larger numbers may be deployed in the future. A pragmatic method of sharing may have to be developed where radiometers are deliberately sited to avoid interference from the other services.

Passive remote sensing of other atmospheric constituents, e.g. ozone, is also expected to benefit from a significant number of ground-based radiometry sites.

6.7   Unmanned Aerial Systems (UAS)

Unmanned Aircraft Systems (UAS) are becoming increasingly important for meteorological and Earth observations operations. UAS address observation requirements in areas where traditional systems cannot be deployed, where manned aircraft flights are not possible due to long flight durations and where hazardous conditions exist.  Current UAS operations (2008) for meteorological purposes often use unlicensed spectrum for command and control of the aircraft, though some systems do use licensed frequencies.  UAS are used for applications that include routine release of dropsondes over ocean areas where radiosonde data has historically been missing, flights into hurricanes and cyclones for insitu data collection, aerial reconnaissance of areas impacted severe weather or drought conditions, and monitoring of arctic ice melt.  Use of UAS for meteorological operations improve the prediction hurricane landfall areas and extend lead times provided to the public,  and allow us to obtain a better understanding of our climate.  Future ITU-R work and possible WRC decisions should better define the spectrum that is used for UAS command and control.  In addition to the command and control of the UAS, spectrum is needed for payload data transmission.  This can occur in suitable bands allocated for meteorological purposes or in other frequency bands.

References

COSTER, A. J., NIELL, A. E., BURKE, H. K. and CZERWINSKI, M. G. [17 December 1997] The Westford water vapor experiment: use of GPS to determine total precipitable water vapour. MIT/Lincoln Laboratories.

DIENDORFER et al., [1994] Results of performance analysis of the Austrian lightning location network. ALDIS, 22nd International Conference on Lightning Protection, Budapest, Hungary.

HOLLE, R. L. and LOPEZ, R. E. [1993] Overview of real-time lightning detection systems and their meteorological uses. NOAA Technical Memorandum ERL NSSL-102, National Severe Storms Laboratory, Norman, Oklahoma, United States of America, p. 68.

LEE, A. C. L. [1986] An experimental study of the remote location of lightning flashes using a VLF arrival time difference technique. Quarterly J. R. Meteorological Society.

LENNON, C. and MAIER, L. [1991] Lightning mapping system. Proc. of International Aerospace and Ground Conference on Lightning and Static Electricity, Cocoa Beach, FL., United States of America. NASA Conf. Pub. 3106, Vol. II, p. 89-1, 89-10.

KAWASAKI, Z. I., YAMAMOTO, K., MATSURA, K., RICHARD, P., MATSUI, T., SONOI, Y. and SHIMOKURA, N. [1994] SAFIR operation and evaluation of its performance, Geophys. Res. Lett., Vol. 21, 12, p. 1133-1136.

Annex  1

ACRONYMS  AND  ABBREVIATIONS  COMMONLY  USED
IN  METEOROLOGY

| A |  |
| --- | --- |
| A/D | Analog-to-Digital |
| AAAS | American Association for the Advancement of Science |
| AARS | Automated Aircraft Reporting System |
| ABSN | Antarctic Basic Synoptic Network |
| ACARS | Aircraft Communications Addressing and Reporting System |
| ACCAD | Advisory Committee on Climate Applications and Data |
| ACMAD | African Centre of Meteorological Applications for Development |
| ADAS | Airborne Data Acquisition System |
| ADC | Analog-to-Digital Converter |
| ADP | Automatic Data Processing |
| ADPE | Automatic Data Processing Equipment |
| ADEOS | Advanced Earth Observation Satellite (Japan) |
| AFC | Automatic Frequency Control |
| AFOS | Automatic Forecasting and Observing System |
| AGC | Automatic Gain Control |
| AGRHYMET | Regional Training Centre for Agrometeorology and Operational Hydrology and its Applications |
| AHRPT | Advance High Resolution Picture Transmission |
| AIRS | Advanced Infrared Sounder (NASA instrument) |
| ALC | Automatic Level Control |
| AM | Amplitude Modulation |
| AMDAR | Aircraft Meteorological Data Relay |
| AMI | American Meteorological Society |
| AMSR | Advanced Meteorological Temperature Sounder |
| ANSI | American National Standards Institute |
| AOPC | Atmospheric Observation Panel for Climate |
| AOS | Acquisition of Signal |
| APT | Automatic Picture Transmission |
| ARGOS | Data collection and location system on NOAA series satellites |
| ASCII | American Standard Code for Information Interchange |
| ASIC | Application Specific Integrated Circuit |
| ATMS | Advanced Technology Microwave Sounder (NPOESS/NASA) |
| ATOVS | Advanced TIROS Operational Vertical Sounder |
| ATSR | Along-Track Scanning Radiometer |
| AVCS | Advanced Video Camera System |
| AVHRR | Advanced Very High Resolution Radiometer |
| AWIPS | Advanced Weather Information Processing System |
| B |  |
| BCD | Binary Coded Decimal |
| BER | Bit Error Rate |
| BPS | bits per second |
| BPSK | Binary Phase Shift Keying |
| BR | ITU Radiocommunication Bureau |
| BW | Bandwidth |
| C |  |
| C/N0 | Carrier-to-Noise density ratio |
| C&DH | Command and Data Handling |
| CaeM | Commission for Aeronautical Meteorology |
| CAgM | Commission for Agricultural Meteorology |
| CAS | Commission for Atmospheric Sciences |
| CBS | Commission for Basic Systems |
| CCD | Charge Coupled Device |
| CCIR | International Consultative Committee on Radio (see ITU-R) |
| CCl | Commission for Climatology |
| CCRS | Canada Centre for Remote Sensing |
| CCSDS | Consultative Committee for Space Data Systems |
| CDA | Command and Data Acquisition |
| CDAS | Command and Data Acquisition Station |
| CEOS | Commission on Earth Observation Satellites |
| CERES | Cloud and Earth’s Radiative Energy System |
| CGMS | Co-ordination Group for Meteorological Satellites |
| CHy | Commission for Hydrology (WMO) |
| CIESIN | Consortium for International Earth Science Information Networks |
| CIMO | Commission for Instruments and Methods of Observation |
| CIMSS | Cooperative Institute for Meteorological Satellite Studies |
| CLICOM | Climate Computing |
| CLINO | Climatological Normals |
| CLIPS | Climate Information and Prediction Services |
| CLIVAR | Climate Variability and Predictability |
| CMA | China Meteorological Administration |
| CMD | Command |
| CMIS | Conical-scanning Microwave Imager/Sounder (NPOESS instrument) |
| CMM | Commission for Marine Meteorology |
| CNES | Centre National D'Etudes Spatiales |
| CNIE | Comision Nacional de Investigaciones Espaciales |
| COADS | Comprehensive Ocean-Atmosphere Data Set |
| CONUS | Continental United States |
| COP | Conference of the Parties |
| COPUOS | Committee on the Peaceful Uses of Outer Space |
| CORSSAC | Civil Operational Remote Sensing Satellite Advisory Committee |
| COSPAS | A Russian satellite-borne search and rescue system. See SARSAT |
| CPCSA | Climate Program Coordination and Support Activities |
| CPR | Cloud Physics Radiometer, or Cardio-pulmonary Resuscitation |
| CPU | Central Processing Unit |
| CRC | Cyclic Redundancy Check/Cyclic Redundancy Code |
| CrMIS | Cross-track Microwave Imager-Sounder (NPOESS instrument) |
| CrIS | Cross-track Infrared Sounder (NPOESS instrument) |
| CRT | Cathode Ray Tube |
| CSA | Canadian Space Agency |
| CS&C | Communications Switching and control (CDA portion of GMACS System) |
| CSIRO | Commonwealth Scientific and Industrial Research Organization |
| CSIS | Centralised Storm Information System |
| CSM | Climate System Monitoring |
| CSMA/CD | Carrier Sensing Multiple Access with Collision Detection |
| CSTR | Council for Scientific and Technical Research |
| CTCS | CDA Telemetry and Command System (CDA portion of GIMTACS System) |
| CW | Continuous Wave |
| CZCS | Coastal Zone Color Scanner |
| D |  |
| D/A | Digital-to-Analog |
| DAAC | Distributed Active Archive Center |
| DADS | Data Archive and Distribution System |
| DAPS | DCS Automated Processing System |
| DAS | Data Acquisition System |
| DAS | Data Base Administration System |
| DAS | Direct Access System |
| dB | Decibel |
| DB | Direct Broadcast |
| DBMS | Database Management System |
| DCPLS | Data Collection Platform Location System |
| DCP | Data Collection Platform |
| DCPI | Data Collection Platform Interrogation |
| DCPR | Data Collection Platform Reception |
| DCR | Differential Correlation Radiometer |
| DCS | Data Collection System |
| DEMUX | De-Multiplexer |
| DIFAX | Digital Facsimile |
| DIR | Daytime Infrared |
| DLI | Down-Link Interface (DM/PM) |
| DLM | Down-Link Monitor |
| DLR | German Space Agency (Deutsche Zentrum fur Lüft- und Raumfahrt) |
| DMSP | Defense Meteorological Satellite Program |
| DN | Descending Node |
| DOMSAT | Domestic (Communications) Satellite |
| DPT | Digital Picture Terminal |
| DR | Direct Readout |
| DRGS | Direct Readout Ground Stations |
| DS | Dwell Sounding or Sounding (GOES-4/7 VAS operating node) |
| DSARS | DAMUS Satellite Archive and Retrieval System |
| DSB | Direct Sounder Beacon |
| DSB | Direct Sounder Broadcasts |
| DSN | Deep Space Network |
| DUS | Data Utilisation System |
| E |  |
| EBR | Electron Beam Recorder |
| EC/AGE | Executive Council Advisory Group on the Exchange of Meteorological and Electronics Calibration |
| ECMWF | European Centre for Medium-range Weather Forecasts |
| EDC | EROS Data Center |
| EDIMS | Environmental Data & Information Management Systems |
| EES | Earth Exploration Satellite |
| EESS | Earth Exploration-Satellite Service |
| EIRP | Equivalent Isotropically Radiated Power |
| EIRPSD | Equivalent Isotropically Radiated Power Spectral Density |
| ELT | Emergency Locator Transmitter |
| ELV | Expendable Launch Vehicle |
| EMC | Electromagnetic Compatibility |
| EMI | Electromagnetic Interference |
| ENSO | El Niño/Southern Oscillation |
| ENVISAT | Environmental Satellite |
| EOS | Earth Observation Satellites |
| EOS | Earth Observation Satellites |
| EPIRB | Emergency Position-Indicating Radio Beacon |
| EPOCS | Equatorial Pacific Ocean Climate Studies |
| EPS | Energetic Particle Sensor |
| ERB | Earth Radiation Budget |
| ERBE | Earth Radiation Budget Experiment |
| ERL | Environmental Research Laboratory |
| EROS | Earth Resources Observing Satellite |
| ERS | ESA Remote Sensing Satellite |
| ESA | European Space Agency |
| ESD | Electrostatic Discharge |
| ESMR | Electronically Scanning Microwave Radiometer |
| ETA | Estimated Time of Arrival |
| ETM | Enhanced Thematic Mapper |
| ETM | Engineering Test Model |
| ETS | Engineering Test Satellite |
| EUMETSAT | European Organization for the Exploitation of Meteorological Satellites |
| EUV | Extreme Ultraviolet |
| F |  |
| FAX | Facsimile |
| FC | False Color |
| FCC | False Color Composite |
| FCC | Federal Communications Commission |
| FDM | Frequency Division Multiplexing |
| FFT | Fast Fourier Transform |
| FIFO | First-In-First-Out |
| FM | Frequency Modulation |
| FOV | Field of view |
| fps | Frames Per Second |
| FSK | Frequency Shift Keying |
| FSS | Fixed-Satellite Service |
| FSS | Flight Scheduling Software System |
| G |  |
| GAC | Global Area Coverage |
| GAME | GEWEX Asian Monsoon Experiment |
| GARP | Global Atmospheric Research Program |
| GARS | GOES Archive and Retrieval System |
| GAW | Global Atmosphere Watch |
| GC | Ground Clutter |
| GCIP | GEWEX Continental-scale International Project |
| GCM | General Circulation Model |
| GCOS | Global Climate Observing System |
| GDTA | Groupemant pour le Developpement de la Teledetection Aerospatiale |
| GEO | Geostationary Earth Orbit |
| GEWEX | Global Energy and Water Cycle Experiment |
| GHz | Gigahertz |
| GIMGSP | GOES I-M Ground System Project |
| GIMTACS | GOES I/M Telemetry and Command System |
| GIS | Geographical Information Systems |
| GMACS | GOES Monitoring and Control system (current GIMTACS) |
| GMDSS | Global Maritime Distress and Safety System |
| GMS | Geostationary Meteorological Satellite |
| GMT | Greenwich Mean Time |
| GOES | Geostationary Operational Environmental Satellite |
| GOMS | Geostationary Operational Meteorological Satellite |
| GOOS | Global Ocean Observing System |
| GOS | Global Observing System |
| GOSSP | Global Observing Systems Space Panel |
| GPCP | Global Precipitation Climatology Project |
| GPS | Global Positioning System |
| GPSOS | GPS Occultation Sensor |
| GRC | Glenn Research Center formerly the Lewis Research Center (LeRC) |
| GRS | Ground Receiving Station |
| GRT | GOES Real-time (database) |
| GSFC | Goddard Space Flight Center |
| GSN | GCOS Surface Network |
| GSTDN | Ground Spaceflight Tracking and Data Network |
| G/T | Antenna Gain to System Noise Temperature Ratio (dB/K) |
| GTOS | Global Terrestrial Observing System |
| GTS | Global Telecommunications System |
| GUAN | GCOS Upper-air Network |
| GVAR | GOES VARiable |
| GWC | Global Weather Center |
| H |  |
| H1/3 | Significant wave height |
| HEPAD | High Energy Proton and Alpha Detector |
| HiRID | High Resolution Imager Data |
| HIRS | High-resolution Infrared Sounder (TIROS instrument) |
| HOMS | Hydrological Operational Multipurpose System |
| HRD | Hurricane Research Day -or- High Rate Data |
| HRD (10) | Hurricane Research Day - GOES-East scans every 10 minutes at selected times. |
| HRI | High Resolution Image |
| HRIS | High Resolution Infrared Sounder, or High Resolution Interferometric Sounder |
| HRIT | High Rate Information Transmission |
| HRPT | High Resolution Picture Transmission |
| HRSD (S) | Hurricane Rapid Scan Day (Stereo) GOES-East and West scan every 7 1/2 |
| Hz | Hertz formerly cycles per second |
| I |  |
| I/S | Imager and Sounder |
| I/O | Input/Output |
| IAHS | International Association of Hydrological Sciences |
| IAMAS | International Association of Meteorology and Atmospheric Sciences |
| IASI | Infrared Atmospheric Sounding Interferometer |
| ICES | International Council for the Exploration of the Sea |
| ICSAR | International Committee for Search and Rescue |
| ICSU | International Council of Scientific Unions |
| ICDS | International Data Collection and Distribution System |
| IEEE | Institute of Electrical and Electronics Engineers |
| IF | Intermediate Frequency |
| IFOV | Instantaneous Field of View |
| IFRB | International Frequency Registration Board (see BR) |
| IGBP | International Geosphere-Biosphere Programme |
| IGF | Image Generation Facility |
| IGFOV | Instantaneous Geometric Field of View |
| IGOSS | Integrated Global Ocean Services System |
| IHP | International Hydrological Programme |
| INDOEX | Indian Ocean Experiment |
| INPE | Instituto de Pesquisas Espaciales |
| INR | Image Navigation and Registration |
| INR | Interference to Noise Ratio |
| INSAT | Indian Satellite |
| IOC | Intergovernmental Oceanographic Commission |
| IODE | International Oceanographic Data and Information Exchange |
| IPCC | Intergovernmental Panel on Climate Change |
| lPD | IF Presence Detector (CDA) |
| IR | Infrared |
| IRIG | Inter-Range Instrumentation Group |
| IRIS | Infrared Interferometer Spectrometer |
| IRS | Indian Remote Sensing Satellite |
| IRU | Inertial Reference Unit |
| ISETAP | Intergovernmental Science Engineer-ing & Technology Advisory Panel |
| ISO | International Organization for Standardization |
| ISM | Industrial, Scientific and Medical |
| ITOS | Improved TIROS Operational System |
| ITPR | Inferred Temperature Profile Radiometer |
| ITU | International Telecommunication Union |
| ITU-R | ITU Radiocommunication Sector (former CCIR and IFRB) |
| J |  |
| JDIMP | Joint GCOS/GOOS/GTOS Data Management and Information Panel |
| JERS | Japanese Earth Resources Satellite |
| JIC | Joint Ice Center |
| JMA | Japan Meteorological Agency |
| JPL | Jet Propulsion Laboratory |
| JSC | Joint Scientific Committee Johnson Space Center |
| JSTC | Joint Scientific and Technical Committee |
| K |  |
| K | Kelvin |
| kb | kilobit(s) |
| kB | kilobyte(s) |
| KBPS or Kb/s | Kilobits per second |
| keV | Thousand Electron Volts |
| kHz | Kilohertz |
| KSC | Kennedy Space Center |
| KSPS | kilo samples per second |
| L |  |
| LANDSAT | U.S. earth remote sensing satellite |
| LANDSAT-TM | Landsat Thematic Mapper instrument |
| LaRC | Langley Research Center |
| LAT/LON | Latitude/Longitude |
| LE | Landmark Extraction |
| LEO | Low Earth Orbit |
| LEOP | Launch and Early Orbit Phase |
| LeRC | see GRC |
| LGSOWG | LANDSAT Ground Station Operations Working Group |
| LHCP | Left-Hand Circular Polarisation |
| LIDAR | Light Detection and Ranging |
| LMT | Local Mean Time |
| LOS | Loss of Signal |
| LPA | Low Power Amplifier |
| lpi | lines per inch |
| lpm | lines per minute |
| LRIT | Low Rate Information Transmission |
| LRPT | Low Resolution Picture Transmission |
| LUT | Look-up Table, or Local User Terminal |
| LW | Long Wave |
| LWIR | Long Wave Infra-Red |
| M |  |
| mb | Millibars |
| Mbps | Megabits per second |
| MBps | Megabytes per second |
| MCC | Mission Control Center |
| MCDW | Monthly Climatic Data for the World |
| MCS | Moisture Channel Support |
| MDHS | Meteorological Data Handling System |
| MDUS | Medium-scale Data Utilisation Stations |
| MEO | Medium Earth Orbit |
| MEPED | Medium Energy Proton and Electron Detector |
| MetAids | Meteorological Aids |
| METEOSAT | European Geostationary Meteorological Satellite |
| METOP | European Polar-orbiting Meteorological Satellite |
| MetSat | Meteorological Satellite |
| MeV | Million Electron Volts |
| MeV/n | Million Electron Volts Per Nucleon |
| MHS | Microwave Humidity Sounder |
| MHz | Megahertz |
| MLS | Microwave Limb Sounder |
| MODEM | Modulator/Demodulator |
| MODIS | Moderate Resolution Imaging Spectroradiometer (NASA instrument) |
| MOPITT | Measurement of Pollution in the Troposphere (NASA) |
| MOS | Marine Observation Satellite (Japan) |
| MPERSS | Marine Pollution Emergency Response Support System |
| MPT | Mission Picture Transmission |
| mr | Milliradians |
| MSFC | Marshall Space Flight Center |
| MSI | Multi-spectral Imaging |
| MSS | Mobile-Satellite Service |
| MSS | Multi-spectral Scanner |
| MSU | Microwave Sounding Unit |
| MTF | Modulation Transfer Function |
| MTBF | Mean Time Between Failures |
| MUX | Multiplexer |
| MW | Momentum Wheel Medium wave Microwave Megawatt |
| N |  |
| N/S | North/South |
| NASA | National Aeronautics and Space Administration |
| NASCOM | NASA Communications Network |
| NASDA | National Space Development Agency |
| NCDC | National Climatic Data Center |
| NE-delta-N | Noise Equivalent Change in Radiance |
| NE-delta-T | Noise Equivalent Change in Temperature |
| NERC | National Environmental Research Council |
| NESDIS | National Environmental Satellite Data and Information Service |
| NF | Noise Figure |
| NHC | National Hurricane Center |
| NHS | National Hydrological Service |
| NIR | Night Infrared, or Near Infrared |
| NMC | National Meteorological Center |
| NMS | National Meteorological or Hydrometeorological Service |
| NNODS | NOAA/NOSS Ocean Data System |
| NOAA | National Oceanic and Atmospheric Administration |
| NOAA | Polar METSAT |
| NOS | National Ocean Survey |
| NPOESS | National Polar-Orbiting Operational Environmental Satellite System |
| NRCT | National Research Council of Thailand |
| NROSS | Navy Remote Ocean Sensing System |
| NRSA | National Remote Sensing Agency |
| NRZ | Non-Return to Zero |
| NRZ-L | Non-Return to Zero Level |
| NSSFC | National Severe Storms Forecast Center |
| NSSL | National Severe Storms Laboratory |
| nT | Nano Tesla |
| NWP | Numerical Weather Prediction |
| NWS | National Weather Service |
| O |  |
| O&M | Operations and Maintenance |
| OAD | Orbit and Attitude Determination |
| OAR | Office of Oceanic and Atmospheric Research |
| OCTS | Ocean Color Temperature Sensor |
| OHP | Operational Hydrology Programme |
| OMI | Ozone Measuring Instrument |
| OMPS | Ozone Mapping and Profiler Suite (NPOESS) |
| OOPC | Ocean Observations Panel for Climate |
| OQPSK | Offset QPSK |
| P |  |
| P/SEC | Pulses per Second |
| P-P | Peak to Peak |
| PA | Power Amplifier |
| PAM | Pulse Amplitude Modulation |
| PCM | Pulse Code Modulation |
| PDL | Processor Data Load |
| PDR | Processed Data Relay (GVAR RF link) |
| PE | Primitive Equation |
| PEP | Peak Envelope Power |
| PEP | Polynomial Error Protection (NASA) |
| PFD | Power Flux-Density |
| Pixels | Picture Elements |
| PKM | Perigee Kick Motor |
| PLL | Phase Locked Loop |
| PM | Phase Modulation |
| PN | Pseudonoise |
| POES | Polar-orbiting Operational Environmental Satellite |
| PPM | Parts Per Million |
| PPS | Pulses Per Second |
| PR | Precipitation Radar |
| PRF | Pulse Repetition Frequency |
| PROFS | Program for Regional Observing and Forecasting Service |
| PROMET | Working Group on the Provision of Meteorological Information |
| PSK | Phase Shift Keying |
| PWM | Pulse-width Modulation |
| Q |  |
| QC | Quality Control |
| QPSK | Quadrature PSK |
| R |  |
| R | Rayleighs |
| RA | Radar Altimeter |
| RASS | Radio Acoustic Sounding System |
| R/Y | Roll/Yaw |
| R&D | Research and Development |
| RBSN | Regional Basic Synoptic Network |
| RCS | Reaction Control System |
| RF | Radio Frequency |
| RFI | Radio Frequency Interference |
| RGB | Red/Green/Blue |
| RH | Relative Humidity |
| RHCP | Right-Hand Circular Polarisation |
| RMDCN | Regional Meteorological Data Communication Network |
| RMS | Root Mean Square |
| RPM | Revolutions Per Minute |
| RSS | Root Sum of the Squares |
| RSU | Remote Sensing Unit |
| RT | Real Time |
| RW | Reaction Wheel |
| RWA | Reaction Wheel Assembly |
| S |  |
| S/C | Spacecraft |
| S/N0 | Signal-to-Noise density ratio |
| S-VAS | Stretched Visible Infrared Spin Scan Radiometer Atmospheric Sounder |
| S-VISSR | Stretched Visible Infrared Spin Scan Radiometer |
| S/N | Signal-to-Noise ratio |
| SAD | Sounder/Auxiliary Data |
| SAGE | Stratospheric Aerosol and Gas Experiment |
| SAR | Synthetic Aperture Radar, or Search and Rescue |
| SARSAT | Search And Rescue Satellite-Aided Tracking; see COSPAS |
| SATCOM | Satellite Communications |
| SBUV | Solar Backscatter Ultraviolet |
| SC/OMS | Subcommittee on Operational Meteorological Satellites |
| SC/OES | Subcommittee on Operational Environmental Satellites |
| SC/N0 | Subcarrier-to-Noise density ratio |
| SCHOTI | Standing Conference of Heads of Training Institutions of National Meteorological Services |
| SCIAMACHY | Scanning Imaging Absorption Spectrometer for Atmospheric Cartography |
| SCO | Subcarrier Oscillator |
| SCSMEX | South China Sea Monsoon Experiment |
| SDUS | Small-scale Data Utilisation Station |
| SeaWiFS | Sea-viewing Wide Field-of-view Sensor |
| SEC | Second |
| SEM | Space Environment Monitor |
| SEU | Single Event Upset |
| SGLS | Space Ground Link System |
| SIGWX | Significant Weather |
| SIR | Shuttle Imaging Radar |
| SIRS | Satellite Infrared Spectrometer |
| SIT | CEOS Strategic Implementation Team |
| SLAR | Side-looking Airborne Radar |
| SN | Space Network |
| SNR | Signal-to-Noise Ratio |
| SOCC | Spacecraft Operations Control Center |
| SOES | Subcommittee on Operational Environmental Satellites |
| SOLAS | International Convention for the Safety of Life at Sea |
| SPM | Solar Proton Monitor |
| SPOT | Satellite Probatoire d'Observation de la Terre |
| SQPSK | Staggered QPSK |
| SPREP | South Pacific Regional Environment Programme |
| sr | Steradian |
| SR | Scanning Radiometer |
| SR-IR | Scanning Radiometer-Infrared Channel |
| SR-VIS | Scanning Radiometer-Visible Channel |
| SSA | WWW System Support Activities |
| SSM/I | Special Sensor Microwave/Imager |
| SST | Sea Surface Temperature |
| SSU | Stratospheric Sounding Unit |
| STA | Science and Technology Agency |
| STC | Scientific and Technical Committee |
| Ster | Steradian |
| STS | Space Transportation System |
| SW | Short wave |
| SW | Switch |
| SWIR | Short Wave Infrared |
| SXI | Solar X-ray Imager |
| SXT | Solar X-ray Telescope (Solar-A mission) |
| T |  |
| T/P | Topex/Poseidon |
| T/V | Thermal Vacuum |
| T&C | Telemetry and Command |
| TBUS | A 4-1etter designator for Ephemeris data message |
| TDM | Time Division Multiplexing |
| TDRS | Tracking and Data Relay Satellite |
| TDRSS | Tracking and Data Relay Satellite System |
| TED | Total Energy Detector, or Turtle Excluder Device |
| TEMS | Terrestrial Ecosystem Monitoring System |
| TES | Tropospheric Emission Spectrometer |
| TIR | Thermal Infrared |
| TIP | TIROS Information Processor |

| TIROS | Television Infra-Red Observational Satellite |
| --- | --- |
| TLM | Telemetry |
| TM | Thematic Mapper |
| TMI | TRMM Microwave Imager |
| TMR | Topex Microwave Radiometer |
| TO | Transfer Orbit |
| TOGA | Tropical Ocean and Global Atmosphere |
| TOPC | Terrestrial Observation Panel for Climate |
| TOMS | Total Ozone Mapping Spectrometer |
| TOS | TIROS Operational System |
| TOVS | TIROS Operational Vertical Sounder |
| TRMM | Tropical Rainfall Measurement Mission |
| TRUCE | Tropical Urban Climate Experiment |
| TT&C | Tracking Telemetry |
| TV | Thermal Vacuum, or Television |
| TVM | Transparent VAS Mode |
| TWT | Traveling Wave Tube |
| U |  |
| UAS | Unmanned Aircraft System |
| UHF | Ultra High Frequency |
| UNEP | United Nations Environment Programme |
| μrad | Microradian |
| μs | Microsecond |
| UTC | Universal Time Coordinated |
| UV | Ultraviolet |
| UWB | Ultrawideband |
| V |  |
| VAS | VISSR Atmospheric Sounder |
| VCP | Voluntary Cooperation Programme |
| VDB | VISSR Data Base |
| VDUC | VAS Data Utilisation Center |
| VHF | Very High Frequency |
| VIIRS | Visible Infrared Imager/Radiometer Suite (NPOESS instrument) |
| VIP | VAS Image Processor (with P/DU current SPS) |
| VIRGS | VISSR Image Registration and Gridding System |
| VISSR | Visible & Infrared Spin Scan Radiometer |
| VOS | Voluntary Observing Ship |
| VREC | Very High Resolution Radiometer Data Recorder |
| VSWR | Voltage Standing Wave Ratio |
| VTPR | Vertical Temperature Profile Radiometer |
| W |  |
| WAFC | World Area Forecast Centre |
| WCASP | World Climate Applications and Services Programme |
| WCDA | Wallops Command and Data Acquisition (Station) |
| WCDMP | World Climate Data and Monitoring Programme |
| WCFP | World Climate Data Programme |
| WCP | World Climate Programme |
| WCRP | World Climate Research Programme |
| WDC | World Data Centre |
| WEFAX | Weather Facsimile |
| WHYCOS | World Hydrological Cycle Observing System |
| WINDAS | Wind Profiler Network and Data Acquisition System |
| WMO | World Meteorological Organization |
| WRC | World Radiocommunications Conference |
| WSFO | Weather Service Forecast office |
| WSFO-Tap | WSFO ground communications link relaying GOES data |
| WTC | Wind Turbine Clutter |
| WWRP | World Weather Research Programme |
| WWW | World Weather Watch |
| WX | Weather |
| X |  |
| XBT | Expendable Bathythermograph |
| XRI | X-Ray Imager |
| XRS | (Solar) X-Ray Sensor |
| Y |  |
| yr | Year |
| Z |  |
| Z | Common abbreviation for Greenwich Meridian Time or Universal Time |

_______________

# Comments

Page: 95
(LT) Adds no technical info.