# Workshop on Aircraft Observing System Data Management. Geneva, Switzerland, 5 – 8 June 2012

# Session 1 Group 2, AO Metadata Management, lead: Stewart taylor

- BRIEF SUMMARY.

The Aircraft Observation (AO) Data Management (DM) Workshop Breakout Session on Metadata discussed the following:

  - Current status of National and Regional Metadata datasets,

    - The varying degree of differences in these datasets clearly showed the need for a generic dataset,

  - What was envisaged as Mandatory and Optional parameters,

  - What parameters would be achievable in the near and long term,

  - Metadata and the relation to ARINC620 and BUFR Template upgrades,

  - Look at requirements for a “global” AMDAR Metadata dataset – not just US and Europe, to account for developing countries.

  - Definition of customer – and associated requirements,

  - Being mindful of overloading the dataset,

  - Inclusion of Quality Flags and Event Records,

  - Willingness of the airlines to provide information, any proprietary and IP issues and restrictions on data usage.

  - Metadata Management responsibilities – population and maintenance of dataset,

  - Any resource issues in maintaining the dataset.

- RECOMMENDATIONS.

The following recommendations were put forward by the group for consideration;

- Ensure that the dataset meets the requirements of WMO WIS as well as considering the needs of AMDAR, NWP, Climate and NWS communities,

- Population of the Metadata dataset(s) to be the remit of the Regional AMDAR Programme,

  - Responsible for contact with airlines, avionics vendors, DSPs and Aviation Authorities for data input,

  - There is a clear need for a good working relationship with the airlines to ensure the data input will be supplied – if available; being mindful not to put unnecessary resource demand on the airline.

- Consider infrastructure of developing countries with regards to accessing AMDAR Metadata dataset,

- Historical Records/Event Log – this would be used to track events relative to AMDAR Metadata:

  - This should be separate from the AMDAR Metadata dataset. Would this dataset be the responsibility of the AMDAR Programme Metadata Manager?

  - Need to agree what constitutes an “Event”,

    - Typical examples could be changes to software configuration, reporting resolution, sensor upgrade etc,

  - Not to include Quality Control (QC) issues – this is not seen as pertaining to the AMDAR Metadata dataset,

- Event Log would need to be intuitive and have “filter” capabilities;

  - Input by Metadata Manager,

  - Plain text with information boxes to be completed (Aircraft ID, Date, Types of Event etc). A VBasic script or perhaps utilisation open source application for Fault Ticketing.

  - Ability to track an event,

  - Data retrieval - select Aircraft ID (option of airline for fleet-wide changes?),

  - Selectable time period – otherwise an Aircraft Event Log could provide a lot of information!

  - Drop down menus to search for Types of Event (Configuration change, software upgrade/change etc).

M = Mandatory		O = Optional

C= Conditional (if an optional component is recorded, an associated conditional component may be required).

| Parameter | Description | Examples | Additional Comments |
| --- | --- | --- | --- |
| Programme | AMDAR Programme responsible for AMDAR data. | E-AMDAR |  |
| Country/Member | Country Member responsible for AMDAR report | UK |  |
| Originating Centre | Centre for issuing the AMDAR report (ICAO Code) | EGRR |  |
| Metadata File Identifier |  | amdar-bulletin-eamdar-en | To be defined |
| Metadata Publication Date |  | yyyymmdd |  |
| Resource Name |  | AMDAR data | Aircraft Observations? |
| Publisher Person Name |  | Stewart Taylor |  |
| Publisher Organization Name |  | Met Office |  |
| Publisher Phone |  | +44 (0)1695 555 128 |  |
| Publisher Fax |  | +44 (0) 1392 88 5681 |  |
| Publisher Person Email |  | stewart.taylor@metoffice.gov.uk |  |
| Resource Publication Date |  | 2012 |  |
| AMDAR Programme Identifier | Unique AMDAR aircraft identifier | EU1234 | List of aircraft decodes should be held by Regional Programme TC |
| Aircraft Tail Number | Assigned by Airline | BA123 |  |
| Aircraft Registration | CAA dataset | G-ABCD |  |
| Airline Organization Name |  | British Airways | Ensure proprietary requests are maintained. |
| Airline Contact Name | Person (s) responsible – aircraft configuration, calibration & maintenance | AMDAR Point of Contact – this should be nominated from technical/ operational staff. | Contact details should include deputy contacts. |
| Airline Phone |  | Contact details at airline |  |
| Airline Fax |  | Contact details at airline |  |
| Airline Person Email |  | Contact details at airline |  |
| Airline operating Quality Management System (QMS) | Do the airline's calibration and maintenance procedures conform to ISO Standards. | Yes/No | Airline responsible for updating the AMDAR Programme on any amendments to their Standards. |
| Airline QMS Details |  | ISO9001 |  |
| Date Aircraft was activated for AMDAR |  | yyyymmdd |  |
| Aircraft Manufacturer |  | Boeing/Airbus/ Embraer | All AMs to be included |
| Aircraft MSN | Airframe unique identifier | nnnn |  |
| Aircraft Model |  | B747 | All types to be identified, Next Gen aircraft and beyond |
| Aircraft Series |  | 436 |  |
| AMDAR Software | Software type/format. | AAA |  |
| AMDAR Software Version |  | v3 |  |
| Software configurable |  | Yes/No | Via optimization systems |
| Aircraft Type |  | Fixed-wing Landplane |  |
| Aircraft Engine |  | 4 x RR RB211-524G2-19 |  |
| EASA Category |  | CS-25 Large Aeroplane | This could be FAA or other Aviation Authority. |
| Avionics manufacturer |  | Teledyne/Honeywell/ Rockwell Collins | All vendors to be included |
| Avionics Hardware part no. |  | 222-100-3-45 | Airline to update if any changes to aircraft. |
| Avionics Software part no. |  | 212-100-2-44 | Airline to update if any changes to aircraft. |
| Navigation System | (GPS or Inertia) | GPS | For issues with magnetic north |
| GNSS reporting |  | Yes/No | ?? |
| AMDAR Software Temperature Smoothing | Yes/No | Yes | Information in the avionics software. |
| AMDAR Software Wind Speed & Direction Smoothing | Yes/No | Yes |  |
| AMDAR Software Humidity Smoothing | Yes/No | Yes |  |
| Ascent/Descent interval (reporting resolution) Default Settings |  | nnn seconds nnn hPa | Do we need to know if these reporting resolutions are configurable |
| En-route interval (reporting resolution) Default Settings |  | nnn seconds |  |
| Aircraft Temperature Sensor Manufacturer | All information relating to the measurement of temperature | Rosemount | Is this a requirement for all onboard sensors? (1,2,3) |
| Aircraft Turbulence (EDR software) Version |  | ?? | Parameter requirement. |
| Aircraft Temperature Sensor Type | Is the sensor “aspirated or non-aspirated”? | A/NA |  |
| Aircraft Temperature Sensor Part no. |  | PT100 | Which sensor(s) is used for AMDAR – primary etc? |
| Aircraft Temperature Sensor Serial no. |  | nnnn |  |
| Aircraft Temperature Sensor Measurement |  | oC |  |
| Aircraft Temperature Sensor Resolution |  | 1.0 0.1 0.01 |  |
| Aircraft Pressure Sensor Manufacturer | All information relating to the measurement of Pressure | Rosemount |  |
| Aircraft Pressure Sensor Part no. |  | PT100 |  |
| Aircraft Pressure Sensor Serial no. |  | nnnn |  |
| Aircraft Pressure Sensor Measurement |  | hPa |  |
| Aircraft Pressure Sensor Resolution |  | 0.1 hPa? |  |
| Aircraft Pitot Sensor Manufacturer | All information relating to the measurement of Pitot | Rosemount |  |
| Aircraft Pitot Sensor Part no. |  | PT100 |  |
| Aircraft Pitot Sensor Serial no. |  | nnnn |  |
| Aircraft Humidity Sensor Manufacturer | All information relating to the measurement of Humidity | Spectrasensors |  |
| Aircraft Humidity Sensor Part no. |  | PT100 |  |
| Aircraft Humidity Sensor Serial no. |  | nnnn |  |
| Aircraft Humidity Sensor Measurement |  | g/kg |  |
| Aircraft Humidity Sensor Resolution |  | 0.001 |  |
| Aircraft Turbulence Sensor Manufacturer | All information relating to the measurement of Turbulence | ?? |  |
| Aircraft Turbulence Sensor Part no. |  | PT100 |  |
| Aircraft Turbulence Sensor Serial no. |  | nnnn |  |
| Aircraft Icing Sensor Manufacturer | All information relating to the measurement of Icing | ?? | Parameter requirement. |
| Aircraft Icing Sensor Part no. |  | PT100 |  |
| Aircraft Icing Sensor Serial no. |  | nnnn |  |

The shaded parameters are seen as long term requirements.

These will be dependant on willingness of airline to provide information – if available.