| WORLD METEOROLOGICAL ORGANIZATION COORDINATION MEETING ON ANTARCTIC METEOROLOGY AND RELATED IPY ACTIVITIES ST.-PETERSBURG, RUSSIAN FEDERATION 21-23 NOVEMBER 2005 |  | COORD-ANT-IPY/Doc. 2.1(2) (03.X.2005) _________ Item: 2.1 Original: ENGLISH |
| --- | --- | --- |

Australian activities relating to the operation of the exchange of

observational data and processed information in the Antarctic,

and related IPY activities

(Submitted by Steven Pendlebury.)

Summary and Purpose of Document The document provides a consolidated report on the status of implementation of the collection and distribution of data and products; a review of monitoring results; a review of the collection of Antarctic data within the Antarctic; a review of observational data and processed products required at Antarctic stations; and some information for the planning of IPY activities.

ACTION PROPOSED

The meeting is invited to note the information contained in this document when considering recommendations to improve the operation of the exchange of observational data and processed information in the Antarctic.

## Attachment 1: Links to Australian Bureau of Meteorology Antarctic–related products available on the Internet

_______________

Australian Activities relating to the

WMO Coordination Meeting on Antarctic Meteorology

and related IPY Activities

##### Re Agenda Item 2.1: Status of implementation of the collection and distribution of observational data and processed information

### Collection of data from Antarctic Basic Synoptic Network (ABSN) stations at the collection centres

Australia continues to have two collection centres for ABSN data: Davis Station, Antarctica and Hobart, Tasmania.

Davis Station collects data from:

Zhongshan (89573),

and, of course, its own (89571) data.

Hobart collects data from:

Mawson Station (89564); and

Casey Station (89611); and

on forwards data collected at Davis Station.

### Insertion of the Antarctic data into the GTS by the collection centres

The Australian Bureau of Meteorology is investigating with the Australian Antarctic Division improved methods of transmitting data from Zhongshan to Davis. The current method is by HF voice: Zhongshan contacts Davis once per day at 0600UTC and passes the last four x 6 hourly synops (AAXX messages). A more robust method would be, for example, via HF modem.

Davis Station sends its collected data to Hobart via a satellite circuit. These data, along with other ABSN data collected at Hobart, are sent to the WMC/RTH at Melbourne via the Internet.

### Distribution of products to Antarctic stations

Australia has a range of mechanisms for providing products to Antarctic stations, especially those products tuned for East Antarctica:

Internet: http://www.bom.gov.au/weather/ant/. Attachment 1 has links to available products.

HF broadcast from VMC (Charleville) and VMW (Wiluna), Australia. The HF schedule may be found at: http://www.bom.gov.au/nmoc/rad_sch/  Attachment 2 has links to some of the products available.

Specialised products for use at the Antarctic Meteorological Centre at Casey and at the Forecasting Office at Davis Forecasting Office are sent via satellite circuit from the Australian Bureau of Meteorology in Melbourne

Similarly, specialised products may be sent via satellite circuit from the Antarctic Meteorological Centre at Casey to Davis and Mawson Stations, or from the Hobart Regional Forecasting Centre to Casey, Davis, or Mawson.

##### Re Agenda Item 2.2: Review of the monitoring results

### Specific Monitoring on the exchange of Antarctic data (SAM) carried out from 1-15 January 2005 (Tables II-VIII at http://www.wmo.int/web/www/ois/monitor/sam/sam051.htm)

###### Table II SYNOP reports

Things to note about this table are:

(i) when accessed in September 2005, the column for the Melbourne RTH seemed to be poorly formatted with “10 %” being shown where this should read “100 %.

(ii) at least one other point of contention with the statistics in this table relates to reported reception rates from 89573 (Zhongshan). As mentioned above the data from 89573 are collected at Davis Station and are then transmitted to RTH Melbourne via Hobart. RTH Melbourne reports a maximum 68% reception rate after 12 hours so the 92% and 100% rates reported from RTH Exeter and Rome respectively cannot be correct.

(iii) It should be noted that due to the method of collection of 89573 data reported in Agenda Item 2.1 above the 43% rates after 1 and 3 hours after observation time reported from RTH Melbourne (et al) are artificial. At most only the 0600UTC observations from 89573 would be available with in 1 to 3 hours after observation time.

(iv) stations 89576; 89610; 89614 and 89618 are incorrectly shown as being collected by Hobart – each of these report via ARGOS through Toulouse and should be shown in part 1 of Table II. However, please note that 89618 has closed: see Agenda Item 2.3. below

(v) it is not clear why Automatic Weather Station (AWS) 89767 (part 1 of table) would achieve 100% reporting when it reports via ARGOS via Toulouse as do all the adjacent AWS but none of these show more than about 88% reception by the RTHs. It is suspected that this is chance statistic given that the NOOA satellites rarely overpass the AWS at precisely the synoptic hour.

(vi) it is not known why AWS 89757; 89762; and 89774 show zero% reporting: the Australian Bureau of Meteorology will investigate this with the operator, the Australian Antarctic Division. AWS 89618 is closed: see Agenda Item 2.3.

(vii) there are additional Australian stations operating that are not in this table: see Agenda Item 2.3.

###### Table III Part A of TEMP reports

Australia ceased 1200UTC radiosondes at Mawson (89564); Davis (89571); and Casey (89611) in 2004, except for “adaptive ‘sondes” over summer at the latter two and weekly 1200UTC radiosondes at Davis Station for ozone and NWP verification purposes. Hence the near 50% reception rates for these stations. Australia intends to reinstate a year–round 1200UTC radiosonde program at Casey Station in 2006.

###### Table IV Part B of TEMP reports

Comments as per part A above.

The 47% (1 missed flight) Part B reception rate from Mawson (89564) does not reflect that one missed flight at 2300 UTC was re–done between 0000 and 0100UTC on that day, and so, in effect, the full program was completed.

###### Table V Part C of TEMP reports

Comments as for Table IV, Part B above.

###### Table VI Part D of TEMP reports

Comments as for Table IV, Part B above.

###### Table VII CLIMAT reports

100% for the Australian; nil for Zhongshan, which does not pass CLIMAT reports to Davis Station and so should be removed from this table.

###### Table VIII CLIMAT TEMP reports

100% for the Australian; nil for Zhongshan, which does not pass CLIMAT TEMP reports to Davis Station and so should be removed from this table.

##### Re Agenda Item 2.3: Review of the collection of Antarctic data within the Antarctic, their insertion into the GTS and their distribution on the GTS

### Review of the list of stations comprising the Antarctic Basic Synoptic Network (ABSN)

The current list of ABSN stations is assumed to be that shown at:

ftp://www.wmo.ch/GTS_monitoring/SAM/From_WMO/200501/table-1.pdf

The Australian deletion from this list is 89618 – this station (“Casey (Halfway)”) closed in February 2004 and its WMO number cancelled.

The Australian additions to this list are as follows:

| Station | Latitude | Longitude | Elevation | WMO No. | Transition method |
| --- | --- | --- | --- | --- | --- |
|  |  |  | metres above mean sea level |  |  |
| DSS-A Law Dome Summit South | 65°46'09"S | 112°48'38" | 1376m | 89616 | ARGOS - download Toulouse then GTS |
| Mt. Brown-A | 69°07'52''S | 85°59'55''E | 2064m | 89586 | ARGOS - download Toulouse then GTS |
| East Law Dome | 66°43'59"S | 114°30'00" | 923m | 89620 | ARGOS - download Toulouse then GTS |
| Snyder Rocks | 66°33'00"S | 107°45'00" | 40m | 89807 | ARGOS - download Toulouse then GTS |
| Haupt Nunataks | 66°34'54"S | 110°41'38" | 63m | 89815 | ARGOS - download Toulouse then GTS |

There are three additional AWS operated by the Australian Antarctic Division. The Australian Bureau of Meteorology will apply for WMO numbers for these stations, the details of which are:

| Station | Latitude | Longitude | Elevation | WMO No. | Transition method |
| --- | --- | --- | --- | --- | --- |
|  |  |  | metres above mean sea level |  |  |
| AM01 | 69°26'31''S | 71°25'02''E | 65m | TBA | ARGOS - download Toulouse then GTS |
| AM02 | 69°42'48''S | 72°38'24''E | 47m | TBA | ARGOS - download Toulouse then GTS |
| B9Biceberg | 67°14'14''S | 148°27'46''E | 35m | TBA | ARGOS - download Toulouse then GTS |

TBA = to be advised.

##### Re Agenda Item 2.4: Review of the distribution of observational data and processed information required at Antarctic stations

During 2005 the HF station VLM operated by the Australian Bureau of Meteorology at Casey Station was formally decommissioned after a year or two of non–operation. This step was taken due to the equipment being expensive for the Australian Antarctic Division to maintain and due to there being limited demand. It is noted that the use of the Internet alluded to in Agenda Item 2.1 above more than offsets the closure of VLM.

##### RE Agenda Item 3: Review of planning and coordination of activities related to the International Polar Year 2007–2008 (IPY) in the Antarctic

Australian Expressions of Interest (EOI) for the IPY are given in the table below (from http://www.ipy.org/development/eoi/browseAntarctic.php?show=1 )

With the acronym CASO (Climate in Antarctica and the Southern Ocean) the key Australian project for Antarctic meteorology and oceanography is EOI 109. The CASO EOI is not a “project,” in the sense of a stand-alone research project that will be submitted as a funding proposal, but it is a coordination strategy. For example, the proposed (AFIN (Antarctic Fast-Ice Network) Project), EOI 277, will be, in effect, a project contributing to the EOI 109 vision.

However, the Australian Bureau of Meteorology is also exploring ways that it might contribute to IPY through a SH THORPEX (http://www.wmo.int/thorpex/ ) in collaboration with the US THORPEX EOI 410 (see http://www.ipy.org/development/eoi/details.php?id=410 ) and with the CASO EOI.

| EOI |  | Brief project description and link |
| --- | --- | --- |
| 59 |  | Paleoclimate records from the subpolar islands of the Southern Ocean |
| 81 |  | The Royal Society of Victoria’s International Research Expedition Polar Inter-Disciplinary Voyage. |
| 83 |  | A Census of Antarctic Marine Life – to be conducted under the auspices of the international Census of Marine Life (CoML - see www.coml.org) |
| 109 |  | Role of Antarctica and the Southern Ocean in Past, Present and Future Climate: A strategy for the International Polar Year 2007-2008 |
| 200 |  | Human influences and global change on polar top order predators: past and present. |
| 274 |  | Antarctic Space Weather: Using routine ground-based and relevant, freely available, space-based data sets daily space weather reports will be prepared |

| 277 |  | Antarctic fast-ice monitoring to study ocean-ice-atmosphere changes |
| --- | --- | --- |
| 348 |  | Dome A – evaluating the world’s premier site for observational astronomy |
| 384 |  | Geoscientific Insights of Greater Antarctica in the area from Gamburtsev Mountains, Amery Ice Shelf to Prydz Bay |
| 426 |  | Micronutrients in Antarctic coastal seawaters — determinants of primary production |
| 479 |  | Terrestrial and Lacustrine Ecology of the Prince Charles Mountains |
| 852 |  | Aliens in Antarctica |

## ATTACHMENT 1: Links to Australian Bureau of Meteorology Antarctic–related products available on the Internet

Analyses and Forecasts Indian Ocean Mean Sea Level Analysis Pressure Charts 00 ¦ 12 UTC Loops: 1 ¦ 2 ¦ 3 ¦ 4 ¦ 5 ¦ 6 ¦ 7 Days Pacific Ocean Mean Sea Level Analysis Pressure Charts 00 ¦ 12 UTC Loops: 1 ¦ 2 ¦ 3 ¦ 4 ¦ 5 ¦ 6 ¦ 7 Days Numerical Weather Prediction charts http://www.bom.gov.au/nmoc/NWP.shtml#sh Antarctica-Casey High Seas Chart Antarctic Total Wave Height(m): +00Hr ¦ +12Hr ¦ +24Hr ¦ +36Hr ¦ +48Hr Indian Ocean Wave Height(m): Swell+24Hr ¦ Wind+24Hr Indian Ocean Wave Height(m): Swell+48Hr ¦ Wind+48Hr ¦ Total+48Hr Pacific Ocean Total Wave Height(m):+48Hr Southern Hemisphere Total Wave Height(m):+36Hr Weather Observations Latest Observations from Australian Antarctic Stations Daily Observations for Antarctica Satellite Imagery (note: only available to “Registered Users” – however, application to become a “Registered User” is straight forward; see: http://www.bom.gov.au/reguser/ Climate Information Climate Averages for Antarctic Sites Catalogue of Antarctic Climate Data Field Offices Casey Davis Mawson Macquarie Island Publications The International Antarctic Weather Forecasting Handbook is now available. Overview Extended Summary PDF file Size 25.1MB / 685 pages

See also the following Marine Products available at:

## ATTACHMENT 2: Extract from VMC and VMW HF schedules – showing products of relevance to the Antarctic

FAX BROADCAST FREQUENCIES:

VMC (Charleville) - Night | Day

VMW (Wiluna) - Night | Day

### Schedule and Products of Relevance to the Antarctic

| TIME (UTC) | DESCRIPTION OF ITEM and Current Chart | Samples or IDCODE |
| --- | --- | --- |
| 0100-0130 | IPS Recommended Frequencies for VMC (Charleville) | IDX0470 |
| 0130-0200 | IPS Recommended Frequencies for VMW (Wiluna) | IDX0473 |
| 0730-0745 | Indian Ocean MSLP Anal (Manual) Valid 0000 | IDX0033 |
| 0745-0800 | Australian Wind Waves Ht(m) Prog Valid 0000 (H+24) | IDX0049 |
| 1015-1030 | Casey Eastern and Western High Seas (H+24) valid 0000 | IDX1087 |
| 1030-1045 | S.H. 500 hPa Prog (H+48) Valid 0000 | IDX0004 |
| 1045-1100 | S.H. MSLP Prog (H+48) Valid 0000 | IDX0003 |
| 1100-1115 | Casey Eastern and Western High Seas (H+36) valid 0000 | IDX1088 |
| 1115-1130 | S.H. 500 hPa Anal Valid 0000 | IDX0008 |
| 1245-1300 | Indian Ocean MSLP Prog (H+36) Valid 1200 | IDX0002 |
| 1315-1330 | South Pacific Ocean Total Waves (H+48) Valid 0000 | IDX0949 |
| 1330-1345 | Indian Ocean Total Waves (H+48) Valid 0000 | IDX0948 |
| 1345-1400 | Pacific Ocean Sea Surface Temps (Weekly) | IDX0942 |
| 1400-1415 | Indian Ocean Sea Surface Temps (Weekly) | IDX0946 |
| 1415-1430 | Casey Eastern and Western High Seas (H+48) valid 0000 | IDX1089 |

| 1630-1700 | IPS Recommended Frequencies for VMC (Charleville) | IDX0470 |
| --- | --- | --- |
| 1700-1730 | IPS Recommended Frequencies for VMW (Wiluna) | IDX0473 |
| 1915-1930 | Indian Ocean MSLP Anal (Manual) Valid 1200 | IDX0533 |
| 2000-2015 | South Pacific Ocean MSLP Anal (Manual) Valid 1200 | IDX0532 |
| 2015-2030 | Casey Eastern and Western High Seas (H+24) valid 1200 | IDX1087 |
| 2215-2230 | Casey Eastern and Western High Seas (H+36) valid 1200 | IDX1088 |
| 2230-2245 | S.H. 500 hPa Prog (H+48) Valid 1200 | IDX0004 |
| 2245-2300 | S.H. MSLP Prog (H+48) Valid 1200 | IDX0003 |
| 2300-2315 | S.H. 500 hPa Anal Valid 1200 | IDX0008 |
| 2315-2330 | Casey Eastern and Western High Seas (H+48) valid 1200 | IDX1089 |
| 2345-0000 | Indian Ocean MSLP Prog (H+48) Valid 1200 | DX0006 |

______________