| WORLD METEOROLOGICAL ORGANIZATION __________________ EXECUTIVE COUNCIL WORKING GROUP ON ANTARCTIC METEOROLOGY NINTH SESSION St. PETERSBURG, RUSSIAN FEDERATION 28-30 NOVEMBER 2006 | EC/WGAM-IX/Doc. 2.1(5) (8.X1.2006) _________ ITEM: 2 Original: ENGLISH |
| --- | --- |

THE NATIONAL METEOROLOGICAL SERVICE (NMS) OF ARGENTINA IN THE ANTARCTIC

(Submitted by Mr. Héctor Sosa, National Meteorological Service, Argentina)

Summary and Purpose of Document This document contains a summary of the tasks performed by the NMS of Argentina in the Antarctic, on the Data Processing and on the review of the monitoring results recently performed. It also includes the Meteorological Services provided by the Marambio Antarctic Meteorological Centre along with details on its Telecommunication System components. The planning for the Antarctic Campaign 2006-2007 and the NMS proposal contributions to the IPY has been included in this document.

# ACTION PROPOSED

The meeting is invited to note the information contained in this document when considering the different agenda items.

_______________

THE NATIONAL METEOROLOGICAL SERVICE (NMS) OF ARGENTINA IN THE ANTARCTIC

##### Status of implementation of the data collection, distribution and processed information.

1. Observation system.

1.1	The NMS of Argentina keeps 6 surface synoptic stations working on operational basis, which also provide climatological, aeronautical, environmental and glaciological data as well.  At Base Marambio it is located the Antarctic Meteorological Centre Marambio (AMC MBI) which is also the Collecting Center for Antarctic Data and Broadcasting Center (ADCC/BC) for the Meteorological Products produced by the AMC MBI itself.

Fig 1 Location of the Antarctic stations operated by Argentina

1.2	During the current Antarctic campaign, all the Argentine surface synoptic stations report for main and intermediate standard hours (00, 03, 06, 09, 12, 15, 18 and 21:00 UTC).  Since May 2006 MARAMBIO had increased its observation hourly. Since March 2006 BELGRANO II reduced its observational schedule, every three hours, since 12 to 00 UTC.

1.3	The following table shows the Argentine Antarctic Stations considered into the ABCN.  On the right side of the table was included the year of the first observations.  It is important to remark Orcadas Station as a centenary meteorological and geo-magnetic observatory (1904-2004).

Fig 2 Contribution to ABSN and ABCN by Argentinean Antarctic Stations.

1.4	At Marambio Base, and regarding the work on environmental observations, the tasks performed are:  global radiation and UV radiation (Solar Light 501) and total amount of atmospheric ozone measurements (Dobson espectrofotometer).  Also are performed, under the auspices of an agreement signed with the Finnish Meteorolocal Institute (FMI), ozonosondings in accordance to the following schedule:

Fig  3. Marambio Ozonosonding Plan

1.5	As part of the same agreement between both national meteorological institutions, during 2005 there have been installed two new instruments in order to measure global radiation, aerosol optical thickness, Beryllium - 7, Radon - 222 and Lead - 210 radionucleides.

1.6	Unfortunately, at the present time, and due to severe budgetary constrains, the radiosonding Work Plan for MBI has been reduced.  Nevertheless, the SMN has the necessary logistic infrastructure in the mentioned Base (facilities, personnel and communication systems for data transmission in operational time) which would allow to resume the radiosondings on regular basis as long as the provision of supplies required (radiosonds, balloons and Helium gas) be available through the signature of agreements with other Institutions, NMSs or Organizations willing to provide such material.

1.7	Taking into account the importance of Marambio facilities available, NMS of Argentina has been offering the logistic infrastructure mentioned above as part of its contribution to the IPY.

##### 1.8	Nevertheless, during 2005, 62 upper air observations were performed and introduced into the GTS, via RTH Buenos Aires.  From January to October 2006, 55 upper air observations have been done and 90 % of them measured more than 10 hPA.

Fig 4. Marambio Upper air observations from 2000 to October 2006

##### 2. Data Processing System

2.1	According to the monitoring performed at the NMS Data Processing Center (DPC) in Buenos Aires, the reports from the Argentine Antarctic Stations show a presence rate that surpasses the 95% during January 2005 to October 2006, and Marambio, in particular, higher than 97%.

MARAMBIO STATION SYNOP JANUARY 2005 -NOVEMBER 2006

Fig 5. Presence monthly average, in operational time, from Marambio Synoptic Surface Station, received at the DPC Buenos Aires.

2.2	It is worth pointing out that the data are submitted to a double process of quality control; the first of which is performed at the very same meteorological station through an automatic system applied on the raw data (SOM), this process is followed by a more detailed internal quality control process at the DPC Buenos Aires, the review of the quality control results during 2005-05 shows an average monthly error rate under the 7%

##### 2.3	Geo REMC BUE runs operationally a ETA/SMN model (Horizontal resolution: 0.25º lat, Vertical resolution: 36 levels). At requirement of the Argentina AMC, it is run a special domain called “MARAMBIO” as showing in figure 7.

##### 2.4	In agreement with Navy Hydrographical Service (SHN), NMS runs a wave model (SMARA/WAM Model) covering all the METAREA VI, including Antarctic Peninsula Area.

Fig 7. ETA SMN “MARAMBIO” domain                                  Fig 8. SMARA WAM model

##### 3. Review of the monitoring results.

3.1	The monitoring of the Argentine Antarctic Stations incoming data to the Regional Telecommunication Hub Buenos Aires (RTH BUE) recently performed (1 to 15 January 2006) shows satisfactory results (better than 2005).  The lower number of data received came from BELGRANO II station, because it had a reduced observational schedule, nevertheless, it sent their bulletins properly.

3.2	It is important to point out that during this monitoring period, the following technical problems were found:

01/01/2006, 00:00 UTC to 15:00 UTC, equipment out of order in SAWB.

Fig 9. Comparison of delay control of synop reports incoming from the Argentine Antarctic Stations

3.3	During the same control period, the bulletins corresponding at Frei Collection Center were transmitted from RTH Buenos Aires to WTC Washington satisfactorily.

Fig 10. Delay control of synop reports from Frei Centre at RTH Buenos Aires (1 to 15 January 2006)

3.4	Unfortunately, the bulletins collected by Rothera Centre (89061, 89062 and 89063) and received on the RTH Buenos Aires via KWBC shown some retards during the monitoring period.

Fig 11. Delay control of synop reports from Rothera Collecting Centre at RTH Buenos Aires

(1 to 15 January 2006)

3.5	Regarding CLIMAT Reports, 100% of Marambio and Frei Collection Centre bulletins were transmitted from the RTH Buenos Aires (SABM) before the 5th day of January 2006.

##### 4. Review of the collections of Antarctic data within the Antarctic, their insertion into the GTS and their distribution on the GTS and review of the distribution of observational data and processed information required at Antarctic stations.

4.1	Marambio Base has the following links for the meteorological exchange and broadcasting of AMC MBI products:

- AMC MBI – RTH BUE:  VSAT link, point to point at 64 Kbps,

Alternatives AFTN via VSAT and Internet

- AMC MBI – RSMC-NMC BUE Internet via VSAT, alternative RTH BUE and phone

- AMC MBI – ETC SOUTHBURY (USA): Via RTH SABM  and KWBC, via GTS

- AMC MBI – ANTARCTIC STATIONS: HF. Alternative Internet and phone.

4.2		RTH Buenos Aires – NMC Santiago Point to Point 9600 bit/s.

4.3	As a complement to the NMS Marine bulletins for METAREA VI, AMC MBI provides forecasts covering the following area: 60ºS – Antarctic Costs, and 20ºW - 90ºW.  The broadcast schedule assigned, coordinated via CES Southbury for AOR (W), is: 02:30 and 17:30 UTC.  (English version).  Additionally, this information is also available at the GMDSS web page (http://weather.gmdss.org/VI.html) and in the National Meteorological Service of Argentina’s web site in both English and Spanish languages (http://www.meteofa.mil.ar , item: “Productos elaborados”, “Met. marítima y fluvial” ).

4.4	In addition, the broadcasting of raw and processed data (forecasts, satellite images, numerical model outputs, tables and other graphic products) is done through the SMN web site (www.meteofa.mil.ar), its access is free for aeronautical and maritime users and for the general public as well.

##### 4.5	Collecting Centre MBI has defined bulletins in order to introduce on the GTS, as available, SHIPs and AIREPs reports.

##### 5. Review of planning and coordination of activities related to the International Polar Year 2007-2008 (IPY) in the Antarctic.

5.1	It is planned to continue with the same observational surface schedule work during the summer antarctic campaign 2006/07 and winter 2007.

5.2	It is planned to continue with the ozonosondings in Marambio (in cooperation with the FMI) and with the rest of the environmental parameters observations.  Also, in agreement with Spain INM, is been coordinated a similar upper air observation schedule and solar radiation measurements in Usuahia to contribute at the ozone layer studies.

5.3	National Meteorological Service, on agreement with the argentine space agency, Comisión Nacional de Actividades Espaciales (CONAE), is in process to install a new HRPT station in AMC MBI.  This station will provide ATOVS information to South American RARS. Also, SMN – CONAE will receive GOES 10 satellite images, according the new re-position scheduled (every 15 minutes, including sub polar areas).

Fig 12. HRPT station at Marambio AMC, scanned area

5.4	The AMC MBI will continue providing Aeronautical and Marine Meteorological Services for the Antarctic Sector, and the broadcasting of Publich Weather products through Base Marambio broadcasting facilities, the RTH Buenos Aires, Internet and Safetynet of INMARSAT.

##### 6. Final conclusions

6.1	Strong efforts are being made to keep the total number of Argentine Antarctic Stations working on operational basis during the next years and, at the same time, increase the observational schedule, as well as NWP outputs.

6.2	It will continue being applied a double quality control process (at the stations themselves and at the REMC Buenos Aires) in order to keep the quality standards and the high levels of data presence achieved.

6.3	The access to raw data and products from the AMC MBI will be optimized for forecasting purposes.

6.4	The NMS is open to the evaluation of possible agreement projects, oriented to increase the soundings in Marambio and to coordinate logistical support in the Argentine bases related to the IPY projects.

6.5	During 2007 is expected put in operation a HRPT station in AMC Marambio (CONAE-NMS of Argentina).

6.6	All the observational data are introduced on the GTS and most of them are available on free access mode on the MNS Web side.

  - NMS has informed his intention to participate at the COMPASS project.

_______________