| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON REQUIREMENTS FOR DATA FROM AUTOMATIC WEATHER STATIONS FIFTH SESSION GENEVA, SWITZERLAND, 5 MAY – 9 MAY 2008 | CBS/OPAG-IOS (ET-AWS-5)/Doc. 3 (28.IV.2008) _________ ITEM: 3 Original: ENGLISH ONLY |
| --- | --- |

AWS FUNCTIONAL SPECIFICATIONS

Submitted by J. van der Meulen (Netherlands)

_________________________________________________________________________

Summary and Purpose of Document

The document contains AWS Functional Specifications as approved by ET-AWS-4.

_________________________________________________________________________

ACTION PROPOSED

The meeting is invited to consider and update AWS Functional Specifications if needed.

References:

- Abridged Final Report, CBS-Ext. (2006), Seoul, Republic of Korea, 2006 (WMO-No. 1017)

- Final report, CBS/OPAG-IOS ET-AWS-4, Geneva, 2006

Background

CBS-Ext. (2006) requested the ET AWS to update AWS Functional Specifications in collaboration with CIMO and other WMO Technical Commissions concerned. ET AWS has received no request for updating the AWS Functional Specifications approved by ET-AWS-5 as they are reproduced in the Annex 1 for reference.

The session is invited to consider any adjustment of the AWS Functional Specifications and update them if needed.

Annex 1

Functional Specifications for Automatic Weather Stations

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) |
| --- | --- | --- | --- | --- |
| ATMOSPHERIC PRESSURE |  |  |  |  |
| Pressure | 500 – 1080 hPa | 10 Pa | I, V | 0 10 004 |
| TEMPERATURE |  |  |  |  |
| Ambient air temperature (over specified surface) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 101 |
| Dew-point temperature | -80 °C – +60 °C | 0.1 K | I, V | 0 12 103 |
| Ground (surface) temperature (over specified surface) | -80 °C – +80 °C | 0.1 K | I, V | 0 12 113 |
| Soil temperature | -50 °C – +50 °C | 0.1 K | I, V | 0 12 130 |
| Snow temperature | -80 °C – 0 °C | 0.1 K | I, V | N |
| Water temperature - river, lake, sea, well | -2 °C – +100 °C | 0.1 K | I, V | 0 13 082 |
| HUMIDITY |  |  |  |  |
| Relative humidity | 0 – 100% | 1% | I, V | 0 13 003 |
| Mass mixing ratio | 0 – 100% | 1% | I, V | N |
| Soil moisture, volumetric or water potential | 0 – 103 g kg-1 | 1 g kg-1 | I, V | N |
| Water vapour pressure | 0 – 100 hPa | 10 Pa | I, V | 0 13 004 |
| Evaporation / evapotranspiration | 0 – 0.1 m | 0.1 kg m-2, 0.0001 m | T | 0 13 033 |
| Object wetness duration | 0 – 86 400 s | 1 s | T | N |
| WIND |  |  |  |  |
| Direction | 0 – 360 degrees | 1 degree | I, V | 0 11 001 |
| Speed | 0 – 75 m s-1 | 0.1 m s-1 | I, V | 0 11 002 |
| Gust Speed | 0 – 150 m s-1 | 0.1 m s-1 | I, V | 0 11 041 |
| X,Y,Z component of wind vector (horizontal and vertical profile) | 0 – 150 m s-1 | 0.1 m s-1 | I, V | N |
| Turbulence type (Low levels and wake vortex) | up to 15 types | BUFR Table | I, V | N |
| Turbulence intensity | up to 15 types | BUFR Table | I, V | N |
| RADIATION6) |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 |
| Background luminance | 1∙10-6 – 2∙104 Cd m-2 | 1∙10-6 Cd m-2 | I, V | N |
| Global downward solar radiation | 0 – 6∙106 J m-2 | 1 J m-2 | I, T, V | N |
| Global upward solar radiation | 0 – 4∙106 J m-2 | 1 J m-2 | I, T, V | N |
| Diffuse solar radiation | 0 – 4∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 023 |
| Direct solar radiation | 0 – 5∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 025 |
| Downward long-wave radiation | 0 – 3∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 002 |
| Upward long-wave radiation | 0 – 3∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 002 |
| Net radiation | 0 – 6∙106 J m-2 | 1 J m-2 | I, T, V | 0 14 016 |
| UV-B radiation | 0 – 1.2∙103 J m-2 | 1 J m-2 | I, T, V | N |
| Photosynthetically active radiation | 0 – 3∙106 J m-2 | 1 J m-2 | I, T, V | N |
| Surface albedo | 1 – 100% | 1% | I, V | 0 14 019 |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) |
| --- | --- | --- | --- | --- |
| CLOUDS |  |  |  |  |
| Cloud base height | 0 – 30 km | 10 m | I, V | 0 20 013 |
| Cloud top height | 0 – 30 km | 10 m | I, V | 0 20 014 |
| Cloud type, convective vs. other types | up to 30 classes | BUFR Table | I | 0 20 012 |
| Cloud hydrometeor concentration | 1 – 700 hydrometeors dm-3 | 1 hydrometeor dm-3 | I, V | N |
| Effective radius of cloud hydrometeors | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | N |
| Cloud liquid water content | 1∙10-5–1.4∙10-2 kg m-3 | 1∙10-5 kg m-3 | I, V | N |
| Optical depth within each layer | Not specified yet | Not specified yet | I, V | N |
| Optical depth of fog | Not specified yet | Not specified yet | I, V | N |
| Height of inversion | 0 – 1 000 m | 10 m | I, V | N |
| Cloud cover | 0 – 100% | 1% | I, V | 0 20 010 |
| Cloud amount | 0 – 8/8 | 1/8 | I, V | 0 20 011 |
| PRECIPITATION |  |  |  |  |
| Accumulation | 0 – 500 mm | 0.1 kg m-2, 0.0001 m | T | 0 13 011 |
| Duration | up to 86 400 s | 60 s | T | 0 26 020 |
| Size of precipitating element | 1∙10-3 – 0.5 m | 1∙10-3 m | I, V | N |
| Intensity - quantitative | 0 – 2000 mm h-1 | 0.1 kg m-2 s-1, 0.1 mm h-1 | I, V | 0 13 055 |
| Type | up to 30 types | BUFR Table | I, V | 0 20 021 |
| Rate of ice accretion | 0 – 1 kg dm-2 h-1 | 1∙10-3 kg dm-2 h-1 | I, V | N |
| OBSCURATIONS |  |  |  |  |
| Obscuration type | up to 30 types | BUFR Table | I, V | 0 20 025 |
| Hydrometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 |
| Lithometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 |
| Hydrometeor radius | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | N |
| Horizontal - extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | N |
| Slant - extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | N |
| Meteorological Optical Range | 1 – 100 000 m | 1 m | I, V | N |
| Runway visual range | 1 – 4 000 m | 1 m | I, V | 0 20 061 |
| Other weather type | up to 18 types | BUFR Table | I, V | 0 20 023 |
| LIGHTNING |  |  |  |  |
| Lightning rates of discharge | 0 – 100 000 | Number h-1 | I, V | 0 13 059 |
| Lightning discharge type (cloud to cloud, cloud to surface) | up to 10 types | BUFR Table | I, V | N |
| Lightning discharge polarity | 2 types | BUFR Table | I, V | N |
| Lightning discharge energy | Not specified yet | Not specified yet | I, V | N |
| Lightning - distance from station | 0 – 3∙104 m | 103 m | I, V | N |
| Lightning - direction from station | 1 – 360 degrees | 1 degree | I, V | N |