| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON REQUIREMENTS AND IMPLEMENTATION AWS PLATFORMS (ET-AWS) Sixth Session GENEVA, SWITZERLAND, 20 – 23 APRIL 2010 | CBS/OPAG-IOS (ET-AWS-6)/Doc. 10.1 Rev. 1 (15.5.2010) _______ ITEM: 10 Original: ENGLISH |
| --- | --- |

BUFR descriptors related to AWS

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains a set of new BUFR/CREX descriptors recommended by IPET-DRC for validation and a revised version

of the Annex to Recommendation 6.1/2 (CBS-XIV).

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and the suggested recommendations.

References:

[1]  Manual on Codes, WMO-No. 306, Volume I.2.

[2]  Draft Recommendation 6.1/2 (CBS-XIV), Commission for Basic Systems, Fourteenth

Session, Dubrovnik, Croatia, 2009.

[3] Joint Meeting of the CT on Migration to Table Driven Code Forms and of the ET on

Data Representation and Codes. Final Report. Geneva, 1 - 5 September 2008.

[4] First meeting of the Inter-Programme Expert Team on Data Representation and

Codes. Final Report. Geneva, 15 - 18 September 2009

[5] Červená, E.: BUFR descriptors required by Recommendation 6.1/2 (CBS-XIV). First

Meeting of the IPET-DRC. Doc. 3.3(3).  Geneva, 15 - 18 September 2009.5 - 8  December 2005ntion on International Civil Aviation

1. 	Background

14th Session of the Commission for Basic Systems (Dubrovnik, Croatia, 25 March to 2 April 2009) reviewed the Functional Specifications for Automatic Weather Stations and adopted draft Recommendation 6.1/2 (CBS-XIV). The Commission requested the OPAG-ISS to develop BUFR descriptors for all the variables listed in the “Functional Specifications for Automatic Weather Stations” as included in the Annex to Recommendation 6.1/2.

Analysis of the Annex to Recommendation 6.1/2 indicated that some of the listed variables might be represented by already existing BUFR descriptors. On the other hand, there were several variables with the assigned BUFR descriptors not capable to meet the requested “Maximum Effective Range” or “Minimum Reported Resolution”. Document IPET-DRC/Doc 3.3(3) submitted to the IPET-DRC meeting (Geneva, 15 – 18 September 2009), contained detailed analysis of the requirements for representation of the listed variables and a proposal for several new BUFR/CREX descriptors. The IPET-DRC meeting invited the ET-AWS to perform validation of the new descriptors and to examine carefully all suggestions and proposals that were included in a concise form in the “Revised Annex to Recommendation 6.1/2 (CBS-XIV) of September 2009” in [4] and in more detail in document IPET-DRC/Doc 3.3(3) [5].

2. 	Descriptors proposed for validation

2. 1 	A descriptor proposed for validation in 2008 [3]

For UV-B radiation

In 2008, a proposal for representation of UV-B radiation was developed in cooperation of Météo-France and Czech Hydrometeorological Institute. The proposed descriptor 0 14 072 was recommended for validation in September 2008 [3] with a note as included below.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 072 | Global UV irradiation | J m-2 | –3 | –8192 | 14 | J m-2 | –3 | 4 |

Note:

- Global UV irradiation (0 14 072) is UV energy integrated over period specified for spectral band specified. 0 14 072 shall be preceded by a time period descriptor and by 0 02 071 (Spectrographic wavelength) and 0 02 072 (Spectrographic width). E.g. If 0 14 072 is used for Global UV-B irradiation, 0 02 071 and 0 02 072 shall specify spectral band 280 to 315 nm.

2. 2 Descriptors proposed for validation in 2009 [4]

For Temperature

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 12 120 | Ground temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |
| 0 12 131 | Snow temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |

For Humidity

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 110 | Mass mixing ratio | % | 0 | 0 | 7 | % | 0 | 3 |
| 0 13 111 | Soil moisture, volumetric or water potential | g kg-1 | 0 | 0 | 10 | g kg-1 | 0 | 4 |
| 0 13 112 | Object wetness duration | s | 0 | 0 | 17 | s | 0 | 5 |

For Radiation

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 14 056 | Background luminance | Cd m-2 | 0 | 0 | 18 | Cd m-2 | 0 | 6 |
| 0 14 052 | Global upward solar radiation, integrated over period specified | J m-2 | -2 | - 1048574 | 20 | J m-2 | -2 | 7 |
| 0 14 053 | Net radiation (high accuracy), integrated over period specified | J m-2 | -2 | - 1048574 | 21 | J m-2 | -2 | 7 |
| 0 14 054 | Photosyntetically active radiation, integrated over period specified | J m-2 | –3 | 0 | 16 | J m-2 | –3 | 5 |

It is suggested to use the term “irradiation” instead of “radiation integrated over period specified” in the names of 0 14 052, 0 14 053 and 0 14 054 in compliance with the terminology used for Global UV irradiation (0 14 072).

For Clouds

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 130 | Cloud hydrometeor concentration | Numeric | 0 | 0 | 10 | Numeric | 0 | 3 |
| 0 20 131 | Effective radius of cloud hydrometeors | m | 5 | 0 | 6 | m | 5 | 2 |
| 0 20 132 | Cloud liquid water content | kg m-3 | 5 | 0 | 11 | kg m-3 | 5 | 4 |
| 0 20 093 | Height of inversion | m | -1 | 0 | 8 | m | -1 | 3 |

And a Note under Class 20:

Cloud hydrometeor concentration 0 20 130 represents the number of hydrometeors in 1 dm3.

For Precipitation

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 114 | Rate of ice accretion | kg m-2 h-1 | 1 | 0 | 11 | kg m-2 h-1 | 1 | 4 |

Moreover, the name of 0 20 032 is proposed to be changed from the current “Rate of ice accretion” to “Rate of ice accretion (estimated)".

For Obscuration

It is proposed to introduce two new descriptors (0 20 133 and 0 15 051) and to modify the already existing descriptor 0 15 029 (Extinction coefficient, m-1, 0, 0, 10), currently under validation:

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 133 | Hydrometeor radius | m | 5 | 0 | 6 | m | 5 | 2 |
| 0 15 051 | Meteorological Optical Range | m | 0 | 0 | 18 | m | 0 | 6 |
| 0 15 029 | Extinction coefficient | m-1 | 9 | 0 | 30 | m-1 | 9 | 10 |

For Lightning

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 20 126 | Lightning rates of discharge | Number h-1 | 0 | 0 | 23 | Number h-1 | 0 | 7 |
| 0 20 127 | Lightning - distance from station | m | -3 | 0 | 6 | m | -3 | 2 |
| 0 20 128 | Lightning - direction from station | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| 0 20 119 | Lightning discharge polarity | Code table | 0 | 0 | 2 | Code table | 0 | 1 |

0 20 119 - Lightning discharge polarity:

| Code figure |  |
| --- | --- |
| 0 | Not defined |
| 1 | Positive |
| 2 | Negative |
| 3 | Missing value |

For Hydrologic and marine data

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 23 040 | Flow discharge – river | m3 s-1 | 1 | 0 | 22 | m3 s-1 | 1 | 7 |
| 0 23 041 | Flow discharge – well | m3 s-1 | 3 | 0 | 16 | m3 s-1 | 3 | 5 |
| 0 13 074 | Ground water level | m | 2 | 0 | 18 | m | 2 | 6 |
| 0 12 132 | Ice surface temperature | K | 2 | 0 | 16 | ˚C | 2 | 4 |
| 0 13 115 | Ice thickness | m | 2 | 0 | 19 | m | 2 | 6 |
| 0 20 135 | Ice mass (on a rod) | kg m-1 | 1 | 0 | 10 | kg m-1 | 1 | 3 |
| 0 13 117 | Snow density (liquid water content) | kg m-3 | 0 | 0 | 10 | kg m-3 | 0 | 3 |

And a Note under Class 13:

Ice thickness 0 13 115 shall be preceded by 0 08 029 (Surface type) set to 11, 12, 13 or 14 to specify river, lake, sea or glacier, respectively.

Moreover, the name of 0 08 029 is proposed to be changed from the current “Remotely sensed surface type” to “Surface type” and the following code figures introduced:

0 08 029 - Surface type:

| Code figure |  |
| --- | --- |
| 11 | river |
| 12 | lake |
| 13 | sea |
| 14 | glacier |

For Other

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 24 014 | Gamma radiation dose rate | nSv h-1 | 1 | 0 | 14 | nSv h-1 | 1 | 4 |

And a Note under Class 24:

Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.

2.3 An additional new descriptor proposed for validation in 2010

For Depth of fresh snow

The existing BUFR/CREX descriptor 0 13 012 Depth of fresh snow (m, 2, -2, 12) is not capable to meet the requested demand for high precision (in 0.001 m). To avoid the necessity to apply all three operators 201Y, 202Y and 203Y, a new descriptor 0 13 118 is proposed for validation.  This proposal has been discussed with IPET-DRC members, but it has not yet been submitted to an IPET-DRC meeting.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 13 118 | Depth of fresh snow (high accuracy) | m | 3 | 0 | 14 | m | 3 | 5 |

2.4. Usage of operators with descriptors for hydrologic and marine data

Several problems were detected in the requirements for representation of hydrologic and marine data in the Annex to Recommendation 6.1/2, i.e. majority of the selected descriptors did not have sufficient scale and/or reference value and/or data width to meet the requirements (highlighted in the table below).

Oceanographic experts were contacted in July 2009 to provide their comments on this part of Annex to Recommendation 6.1/2. Mr. Robert Keeley expressed his opinion that the ranges of existing BUFR descriptors would be mostly sufficient, apart from the extreme conditions in some cases.

Several new descriptors have been proposed for representation of hydrologic and marine data (see part 2.2 of this document). If the requirements for the remaining variables are confirmed, the IPET DRC suggested usage of the selected descriptors suitable for the normal operating conditions combined with appropriate operator descriptors to allow representation of the extreme values or the required high precision.

| VARIABLE | Required Maximum Effective Range | Required Minimum Resolution | Range provided by existing BUFR descriptors | Precision provided by existing BUFR descriptors | BUFR / CREX |
| --- | --- | --- | --- | --- | --- |
| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |
| Wave period | 0 – 100 s | 1 s | 0 – 62 s | 1 s | 2 01 129 0 22 011 2 01 000 |
| 1D spectral wave energy density | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | 0 - 4194.302 m2Hz-1 | 0.001 m2Hz-1 | 2 01 135 0 22 069 2 01 000 |
| 2D spectral wave energy density | 0 – 5x105 m2Hz-1 | 10-3 m2Hz-1 | 0 - 4194.302 m2Hz-1 | 0.001 m2Hz-1 | 2 01 135 0 22 069 2 01 000 |
| Water salinity | 0 – 40 % [0 – 400 psu] | 10-4 % [10-3 psu] | 0.000– 131.070 psu | 0.001 psu | 2 01 130 0 22 064 2 01 000 |
| Water conductivity | 0 – 600 S m-1 | 10-6 S m-1 | 0 – 67.108862 S m-1 | 0.000001 S m-1 | 2 01 132 0 22 066 2 01 000 |
| Water pressure | 0 – 11x107 Pa | 100 Pa | 0 – 131 070 000 Pa | 1000 Pa | 2 07 001 0 22 065 2 07 000 see Note a) |
| Ice thickness | 0 – 3 m | 0.015 m | 0 – 1.26 m | 0.01 m | 2 01 133 2 02 129 0 20 031 2 02 000 2 01 000 |
| Tidal elevation with respect to local chart datum | -10 – +30 m | 0.001 m | -10.000 – 22.766 m | 0.001 m | 2 01 129 0 22 038 2 01 000 |
| Tidal elevation with respect to national land datum | -10 – +30 m | 0.001 m | -10.000 – 22.766 m | 0.001 m | 2 01 129 0 22 037 2 01 000 |
| Meteorological residual tidal elevation (surge or offset) | -10 – +16m | 0.001 m | -5.000 – 11.382 m | 0.001 m | 0 22 040 see Note b) |

Notes:

- In case of Water pressure 0 22 065 (Pa, -3, 0, 17), usage of operator 2 07 Y is suggested in the table above (if the data are produced in BUFR, Edition 4). The same result, i.e. change to (Pa, -2, 0, 21) would be obtained by  the combined use of the less sophisticated operators 201Y and 202Y:

2 01 132

2 02 129

0 22 065 Reported value of “Water pressure”

2 02 000

2 01 000

- In case of 0 22 040 (m, 3, -5000, 14), reference value and data width is not sufficient. The following sequence is to be used to change the data width and the reference value to become (m, 3, -10000, 15):

2 01 129

2 03 015

0 22 040 New reference value = -10000

2 03 255

0 22 040 Reported value of “Meteorological residual tidal elevation”

2 01 000

2 03 000

3. Revised Annex to draft Recommendation 6.1/2 (CBS-XIV) – March 2010

Functional Specifications for Automatic Weather Stations

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | Status 5) |
| --- | --- | --- | --- | --- | --- |
| ATMOSPHERIC PRESSURE |  |  |  |  |  |
| Atmospheric Pressure | 500 – 1080 hPa | 10 Pa | I, V | 0 10 004 | OP |
| TEMPERATURE 9) |  |  |  |  |  |
| Ambient air temperature (over specified surface) 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 101 | OP |
| Dew-point temperature 14) | -80 °C – +60 °C | 0.1 K | I, V | 0 12 103 | OP |
| Ground (surface) temperature (over specified surface) 14) | -80 °C – +80 °C | 0.1 K | I, V | 0 12 120 | VAL |
| Soil temperature14) | -50 °C – +50 °C | 0.1 K | I, V | 0 12 130 | OP |
| Snow temperature 14) | -80 °C – 0 °C | 0.1 K | I, V | 0 12 131 | VAL |
| Water temperature - river, lake, sea, well | -2 °C – +100 °C | 0.1 K | I, V | 0 13 082 or 0 22 043 | OP OP |
| HUMIDITY 9) |  |  |  |  |  |
| Relative humidity | 0 – 100% | 1% | I, V | 0 13 003 | OP |
| Mass mixing ratio | 0 – 100% | 1% | I, V | 0 13 110 | VAL |
| Soil moisture, volumetric or water potential | 0 – 103 g kg-1 | 1 g kg-1 | I, V | 0 13 111 | VAL |
| Water vapour pressure | 0 – 100 hPa | 10 Pa | I, V | 0 13 004 | OP |
| Evaporation/evapotranspiration | 0 – 0.2 m | 0.1 kg m-2, 0.0001 m | T | 0 13 033 | OP |
| Object wetness duration | 0 – 86 400 s | 1 s | T | 0 13 112 | VAL |
| WIND |  |  |  |  |  |
| Direction | 0 11,13); 1( – 360( | 1( | I, V | 0 11 001 | OP |
| Speed | 0 – 75 m s-1 | 0.1 m s-1 | I, V | 0 11 002 | OP |
| Gust Speed | 0 – 150 m s-1 | 0.1 m s-1 | I, V | 0 11 041 | OP |
| X,Y component of wind vector Z component of wind vector (horizontal and vertical profile) | 0 – 150 m s-1 0 – 40 m s-1 | 0.1 m s-1 | I, V | 0 11 003 0 11 004 0 11 006 | OP OP OP |
| Turbulence type (Low levels and wake vortex) 16) | up to 15 types | BUFR Table Not specified yet | I, V | - | N |
| Turbulence intensity 16) | up to 15 types | BUFR Table Not specified yet | I, V | - | N |
| RADIATION 6) |  |  |  |  |  |
| Sunshine duration | 0 – 86 400 s | 60 s | T | 0 14 031 | OP |
| Background luminance | 0 – 1∙105 Cd m-2 | 1 Cd m-2 | I, V | 0 14 056 | VAL |
| Global downward solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 028 | OP |
| Global upward solar radiation | -1∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 052 | VAL |
| Diffuse solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 029 | OP |
| Direct solar radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 030 | OP |
| Downward long-wave radiation | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | OP |
| Upward long-wave radiation | -1∙107 – 0 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 002 | OP |
| Net radiation | -1∙107 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 053 | VAL |
| UV-B radiation 8) | 0 – 1∙107 J m-2 | 1. 103 J m-2 | I, T, V | 0 14 072 | VAL |
| Photosynthetically active radiation 22) | 0 – 1∙107 J m-2 | 1∙103 J m-2 | I, T, V | 0 14 054 | VAL |
| Surface albedo | 0 – 100% | 1% | I, V | 0 14 019 | OP |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | Status 5) |
| --- | --- | --- | --- | --- | --- |
| CLOUDS |  |  |  |  |  |
| Cloud base height | 0 – 30 km | 10 m | I, V | 0 20 013 | OP |
| Cloud top height | 0 – 30 km | 10 m | I, V | 0 20 014 | OP |
| Cloud type, convective vs. other types | up to 30 classes | BUFR Table | I | 0 20 012 | OP |
| Cloud hydrometeor concentration | 1 – 700 hydrometeors dm-3 | 1 hydrometeor dm-3 | I, V | 0 20 130 | VAL |
| Effective radius of cloud hydrometeors | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 131 | VAL |
| Cloud liquid water content | 1∙10-5–1.4∙10-2 kg m-3 | 1∙10-5 kg m-3 | I, V | 0 20 132 | VAL |
| Optical depth within each layer | Not specified yet | Not specified yet | I, V | - | N |
| Optical depth of fog | Not specified yet | Not specified yet | I, V | - | N |
| Height of inversion | 0 – 1 000 m | 10 m | I, V | 0 20 093 | VAL |
| Cloud cover | 0 – 100% | 1% | I, V | 0 20 010 | OP |
| Cloud amount | 0 – 8/8 | 1/8 | I, V | 0 20 011 | OP |
| PRECIPITATION |  |  |  |  |  |
| Accumulation 7) | 0 – 1000 mm | 0.1 kg m-2, 0.0001 m | T | 0 13 011 | OP |
| Depth of fresh snowfall | 0 –1000 cm | 0.001 m | T | 0 13 118 | VAL |
| Duration | up to 86 400 s | 60 s | T | 0 26 020 | OP |
| Size of precipitating element 17) | 1∙10-3 – 0.25 m | 1∙10-3 m | I, V | 0 13 058 0 20 066 | OP OP |
| Intensity - quantitative | 0 – 2000 mm h-1 | 0.1 kg m-2 s-1, 0.1 mm h-1 | I, V | 0 13 155 | OP |
| Type | up to 30 types | BUFR Table | I, V | 0 20 021 | OP |
| Rate of ice accretion | 0 – 1 kg dm-2 h-1 | 1∙10-3 kg dm-2 h-1 | I, V | 0 13 114 | VAL |
| OBSCURATIONS |  |  |  |  |  |
| Obscuration type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Hydrometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Lithometeor type | up to 30 types | BUFR Table | I, V | 0 20 025 | OP |
| Hydrometeor radius | 2∙10-5 – 32∙10-5 m | 2∙10-5 m | I, V | 0 20 133 | VAL |
| Extinction coefficient | 0 – 1 m-1 | 0.001 m-1 | I, V | 0 15 029 | VAL |
| Meteorological Optical Range 10) | 1 – 100 000 m | 1 m | I, V | 0 15 051 | VAL |
| Runway visual range | 1 – 4 000 m | 1 m | I, V | 0 20 061 | OP |
| Other weather type | up to 18 types | BUFR Table | I, V | 0 20 023 | OP |
| LIGHTNING |  |  |  |  |  |
| Lightning rates of discharge | 0 – 4 500 000 | Number h-1 | I, V | 0 20 126 | VAL |
| Lightning discharge type (cloud to cloud, cloud to surface) | 3 types | BUFR Code Table | I, V | 0 20 023 | OP |
| Lightning discharge polarity | 2 types | BUFR Code Table | I, V | 0 20 119 | VAL |
| Lightning discharge energy | Not specified yet | Not specified yet | I, V | - | N |
| Lightning - distance from station | 0 – 3∙104 m | 103 m | I, V | 0 20 127 | VAL |
| Lightning - direction from station | 1( – 360( | 1 degree | I, V | 0 20 128 | VAL |

| VARIABLE 1) | Maximum Effective Range 2) | Minimum Reported Resolution 3) | Mode of Observation 4) | BUFR / CREX 5) | Status 5) |
| --- | --- | --- | --- | --- | --- |
| HYDROLOGIC AND MARINE OBSERVATIONS |  |  |  |  |  |
| Flow discharge – river | 0 – 2.5∙105 m3 s-1 | 0.1 m3 s-1 | I, V | 0 23 040 | VAL |
| Flow discharge – well | 0 – 50 m3 s-1 | 0.001 m3 s-1 | I, V | 0 23 041 | VAL |
| Ground water level | 0 – 1 800 m | 0.01 m | I, V | 0 13 074 | VAL |
| Ice surface temperature 14) | -80 °C – +0 °C | 0.5 K | I, V | 0 12 132 | VAL |
| Ice thickness - river, lake 15) | 0 – 50 m | 0.01 m | I, V | 0 08 029 0 13 115 | VAL |
| Ice thickness - glacier, sea 15) | 0 – 4 270 m | 1 m | I, V | 0 08 029 0 13 115 | VAL |
| Water level | 0 – 100 m | 0.01 m | I, V | 0 13 071 0 13 072 | OP OP |
| Wave height | 0 – 50 m | 0.1 m | V | 0 22 021 | OP |
| Wave period 18) | 0 – 100 s ?? | 1 s | V | 2 01 129 0 22 011 2 01 000 | OP |
| Wave direction | 0 13); 1 – 360 degrees | 1 degrees | V | 0 22 001 | OP |
| 1D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 ?? | 10-3 m2Hz-1 | V, T | 2 01 135 0 22 069 2 01 000 | OP |
| 2D spectral wave energy density 18) | 0 – 5x105 m2Hz-1 ?? | 10-3 m2Hz-1 | V, T | 2 01 135 0 22 069 2 01 000 | OP |
| Water salinity 18) | 0 – 40 % 12) [0 – 400 psu] ?? | 10-4 % [10-3 psu] | I, V | 2 01 130 0 22 064 2 01 000 | OP |
| Water conductivity 18) | 0 – 600 S m-1 ?? | 10-6 S m-1 | I, V | 2 01 132 0 22 066 2 01 000 | OP |
| Water pressure 18) 19) | 0 – 11x107 Pa | 100 Pa ?? | I, V | 2 07 001 0 22 065 2 07 000 | OP |
| Ice thickness 18) | 0 – 3 m ?? | 0.015 m ?? | T | 2 01 133 2 02 129 0 20 031 2 02 000 2 01 000 | OP |
| Ice mass | 0 – 50 kg m-1 | 0.5 kg m-1 (on 32 mm rod) | T | 0 20 135 | VAL |
| Snow density (liquid water content) | 100 – 700 kg m-3 | 1 kg m-3 | T | 0 13 117 | VAL |
| Tidal elevation with respect to local chart datum 18) | -10 – +30 m ?? | 0.001 m | I, V | 2 01 129 0 22 038 2 01 000 | OP |
| Tidal elevation with respect to national land datum 18) | -10 – +30 m ?? | 0.001 m | I, V | 2 01 129 0 22 037 2 01 000 | OP |
| Meteorological residual tidal elevation (surge or offset) 18) 20) | -10 – +16m ?? | 0.001 m | I, V | 0 22 040 Note 20) | OP |
| Ocean Current - Direction | 0 13); 1( – 360( | 1( | I, V | 0 22 004 or 0 22 005 | OP OP |
| Ocean Current - Speed | 0 – 10 m s-1 | 0.01 m s-1 | I, V | 0 22 031 or 0 22 032 | OP OP |
| OTHER SURFACE VARIABLES |  |  |  |  |  |
| Runway conditions | up to 10 types | BUFR Table | I, V | 0 20 085 | OP |
| Braking action/friction coefficient | up to 7 types | BUFR Table | I, V | 0 20 089 | OP |
| State of ground | up to 30 types | BUFR Table | I, V | 0 20 062 | OP |
| Type of surface specified | up to 15 types | BUFR Table | I, V | 0 08 010 | OP |
| Snow depth | 0 – 25 m | 0.01 m | T | 0 13 013 | OP |
| OTHER |  |  |  |  |  |
| Gamma radiation dose rate 21) | 1 – 103 nSv h-1 | 0.1 nSv h-1 | I, T | 0 24 014 | VAL |
| Categories of stability | 9 types | BUFR Table | I, V | 0 13 041 | OP |

Notes:

- Name of variable, in line with WMO vocabulary and Technical Regulations.

- Maximum Effective Range - Maximum range of measuring capability; units traceable to SI.

- Minimum Reported Resolution – Lower resolution of reporting is not permitted.

- Mode of Observation – Type of data being reported:

I:  Instantaneous – 1-minute value (instantaneous as defined in WMO-No. 8, Part II, paragraph 1.3.2.4);

V:  Variability – Average (mean), Standard Deviation, Maximum, Minimum, Range, Median, etc. of samples – those reported depend upon meteorological variable;

T: Total – Integrated value over defined period; maximum 24 hours for all parameters except radiation which requires a maximum of one hour (exception, see note 6), and precipitation accumulation (6 hours maximum). The relevant element descriptor shall be preceded by a time period descriptor 0 04 024 (in hours) or 0 04 025 (in minutes).

A:  Average (mean) value.

- BUFR/CREX descriptors for representation of the listed variables;

OP:   Operational descriptors of BUFR/CREX Table B, Version Number 14.

VAL: Descriptors to be validated.

N:     Not yet specified requirements.

- Radiation energy amounts are given over a 24-hour period.

- Maximum interval: 6 hours.

- Definition of UV-B according to WMO-No. 8 (Vol. 1, Chapter on Radiation). Descriptor 0 14 072 (Global UV irradiation) was recommended for validation in September 2008.

- Humidity related variables (i.e. dew point) expressed as temperature are collected under temperature.

- MOR uniquely related to "extinction coefficient", (, by MOR = -ln(5%)/(.

- Direction to indicate 0 (zero) if speed = 0.

- Salinity of 1% (1 g of salt per 100 g of water), or 10 ‰ converts to 10.000 ppm (parts per million), which equals 10 psu (practical salinity units). Ocean water is about 3.5% salt, i.e. 35.000 ppm or 35 psu. Lake Asal (Ethiopia) is the most saline body of water on earth with 34.8% [348 psu] salt concentration.

- Calm.

- Temperature data represented by 0 12 101, 0 12 103, 0 12 113, 0 12 120, 0 12 130, 0 12 131 and 0 12 132 shall be reported with precision in hundredths of a degree even if they are measured with the accuracy in tenths of a degree. This requirement is based on the fact that conversion from the Kelvin to the Celsius scale has often resulted into distortion of the data values. Temperature t (in degrees Celsius) shall be converted into temperature T (in degrees Kelvin) using equation: T = t + 273.15.

- Ice thickness 0 13 115 shall be preceded by 0 08 029 (Surface type) set to 11, 12, 13 or 14 to specify river, lake, sea or glacier, respectively.

- If the UNIT is specified as “BUFR Table”, the BUFR descriptor cannot be proposed without the content of the table being available.

- 0 13 058 (Size of precipitation element) is capable to express size of any precipitation element, apart from hailstones. Size of hailstones shall be represented by 0 20 066.

- If these requirements are confirmed, it has to be noted that the selected descriptors are suitable for the normal operating conditions and shall be combined with appropriate operator descriptors to allow representation of the extreme values or the requested high precision.

- Operator 2 07 Y is recommended to be used with Water pressure 0 22 065 (Pa, -3, 0, 17), if the data are produced in BUFR, Edition 4. The same result, i.e. change to (Pa, -2, 0, 21) would be obtained by the combined use of the less sophisticated operators 201Y and 202Y:

2 01 132

2 02 129

0 22 065 Reported value of “Water pressure”

2 02 000

2 01 000

- The following sequence is to be used to change data width and reference value of 0 22 040 (m, 3, -5000, 14) to become (m, 3, -10000, 15):

2 01 129

2 03 015

0 22 040 New reference value = -10000

2 03 255

0 22 040 Reported value of “Meteorological residual tidal elevation”

2 01 000

2 03 000

- Gamma radiation dose rate 0 24 014 is intended to be used for reporting of this element under normal conditions, nuclear accidents excluded.

- Photosynthetically active radiation (PAR). The electromagnetic energy in the 400 – 700 nm wavelength range. Measured as the photosynthetic photon flux (PPF) in quanta per second per square meter, or mole of quanta per second per square meter or microeinsteins per second per square meter.  Approximate conversion is 1 J m-2 s-1 equivalent to 5 μE m-2 s-1 (suggested by Chairman of ET AWS).

The introduced changes are written in blue or marked by side bars.