| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON REQUIREMENTS AND IMPLEMENTATION AWS PLATFORMS (ET-AWS) Sixth Session GENEVA, SWITZERLAND, 20 – 23 APRIL 2010 | CBS/OPAG-IOS (ET-AWS-6)/Doc. 10.2 (17.3.2010) ________ ITEM: 10 Original: ENGLISH |
| --- | --- |

BUFR templates for AWS data

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains information on the development and validation of BUFR templates for AWS data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate corresponding recommendations.

__________________

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Meeting of Expert Team on Data Representation and Codes. Darmstadt, 23 to 27 April 2007.

[3] Meeting of Expert Team on Requirements for Data from Automatic Weather Stations.

Geneva, 5 to 9 May 2008.

[4] Joint Meeting of the CT on Migration to Table Driven Code Forms and of the ET on Data

Representation and Codes. Geneva, 1 to 5 September 2008.

[5]  Recommendation 6.2/2 (CBS-XIV), Commission for Basic Systems, Fourteenth Session.

Dubrovnik, Croatia, 25 March to 2 April 2009.

Annex:

[1] BUFR template for surface observations from n-minute period with national and WMO         station identification

1.	BUFR templates for representation of AWS data (3 07 091, 3 07 092 and 3 07 093)

The proposal of sequence 3 07 091 (BUFR template for surface observations from one-hour period with national and WMO station identification) was submitted to the Meeting of Expert Team on Data Representation and Codes (Darmstadt, 23 to 27 April 2007). The Meeting requested also development of sequence 3 07 092 (BUFR template for surface observations from n-minute period with national and WMO station identification) and recommended the sequences  3 07 091, 3 07 092 and 3 07 093 for validation [2].

The complete proposal (descriptors 0 01 101, 0 01 102 and 3 01 089 for National station identification and the templates 3 07 091, 3 07 092 and 3 07 093)  was submitted to the Meeting of Expert Team on Requirements for Data from Automatic Weather Stations (ET- AWS) held in Geneva from 5 to 9 May 2008. No objections to the proposed templates and descriptors were expressed by the meeting [3].

In 2008, IBL Software Engineering in cooperation with ET-DR&C performed validation of the template for surface observations from one-hour period (3 07 091), including the system of national station identification. Consequently, 3 07 091 and the descriptors 0 01 101, 0 01 102 and 3 01 089 for National station identification were pronounced pre-operational by the Joint Meeting of the CT-MTDCF and ET-DR&C (Geneva, 1 to 5 September 2008) [4] and recommended for operational implementation as from 4 November 2009 by the CBS-XIV [5].

The sequences 3 07 092 and 3 07 093 (see Annex to this document) were recommended to be left in the stage of validation in September 2008 [4]. They are still waiting for validation now.

| Table reference | Element name | Status |
| --- | --- | --- |
| 3 07 092 | BUFR template for surface observations from n-minute period with national and WMO station identification | To be validated |
| 3 07 093 | Nominal values | To be validated |

2. 	BUFR template for representation of SYNOP data with supplementary information on one-hour observations (3 07 096)

In 2006, Mr. Michel Leroy, the representative of EUMETNET, developed a proposal for a BUFR template, blending the current AWS and SYNOP BUFR templates. A revised version of this template was submitted to the Meeting of ET DR&C (Darmstadt, 23 to 27 April 2007) that discussed the usage of this combined template and its consequences and recommended the template for further validation [2].

The Meeting of ET-AWS (Geneva, 5 to 9 May 2008) noted that the requirements for the “merged” BUFR template for surface observations from one-hour period and for reporting SYNOP data in BUFR was addressed by ET-DR&C, but it still requires validation. The meeting recommended that the validation of the template including proposed national station identification should be done as a matter of urgency. It accepted with pleasure an offer by M. Leroy, Météo-France, to take lead in this validation. The ET- AWS emphasized the need for the adoption of the relevant amendments to the Manual on Codes (WMO-No. 306) by CBS-XIV so that this “merged” template could be used instead of the TM 307080 - BUFR template for reporting SYNOP data in BUFR during and after the transition phase for the migration from traditional alphanumeric codes (TAC) to Table Driven Codes Forms (TDCF) [3].

A new version of the BUFR AWS-SYNOP template was submitted to the Joint Meeting of CT-MTDCF and ET-DR&C (Geneva, 1 - 5 September 2008) as “TM 307096 - BUFR template for representation of SYNOP data with supplementary information on one-hour observations”. It included national station identification and the extensive usage of delayed replications in compliance with the template TM 307091 for surface observations from one-hour period. Moreover, Météo-France agreed with modifications that had been suggested in June 2006. The problem of specification of data subcategories was also discussed and the addition of three subcategories for surface data in Common Table C-13 was suggested. The Meeting recommended  this template to be validated as soon as possible for approval of pre-operational status before CBS XIV [4].

Template TM 307096 was validated by Météo-France and the Czech Hydrometeorological Institute in the winter 2008/2009, including the newly requested descriptor 0 13 155 for “Intensity of precipitation (high accuracy)”, and consequently recommended for operational implementation as from 4 November 2009 by the CBS-XIV [5].

3. 	Relevant BUFR descriptors recommended for operational use by the CBS-XIV [5]

BUFR descriptors recommended for operational implementation as from 4 November 2009 (BUFR Table B, Version Number 14), available in the Manual on Codes, WMO-No. 306, Volume I.2 [1] at http://www.wmo.int/pages/prog/www/WMOCodes.html

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 01 101 | State identifier | Code table | 0 | 0 | 10 | Code table | 0 | 3 |
| 0 01 102 | National station number | Numeric | 0 | 0 | 30 | Numeric | 0 | 9 |
| 0 13 155 | Intensity of precipitation (high accuracy) | kg m-2 s-1 | 5 | -1 | 16 | mm h-1 | 1 | 5 |

And a note under Class 13 referring to 0 13 155:

An intensity of precipitation value of -0.00001 kg m-2 s-1  before scaling (-1 after scaling)  and  of  -0.1 mm h-1 before scaling (-1 after scaling) shall indicate a "trace" in BUFR and in CREX, respectively.

BUFR descriptors recommended for operational implementation as from 4 November 2009 (BUFR Table D, Version Number 14), available in the Manual on Codes, WMO-No. 306, Volume I.2 [1] at http://www.wmo.int/pages/prog/www/WMOCodes.html

| Table reference | Element name |
| --- | --- |
| 3 07 091 | BUFR template for surface observations from one-hour period with national and WMO station identification |
| 3 07 096 | BUFR template for representation of SYNOP data with supplementary one-hour observations |
| 3 01 089 | National station identification |
| 3 02 084 | “Instantaneous” data of sequence 307096 |
| 3 02 085 | “Period” data of sequence 307096 |
| 3 02 175 | Intensity of precipitation (high accuracy), size of precipitation element |

Data sub-categories were added in Common Code Table C-13 [1] to be used for data represented by template TM 307096:

| Data categories | International data sub-categories (BUFR Ed. 4, CREX Ed.2) |
| --- | --- |
| Code figure | Name | Code figure | Name |
| 000 | Surface data — land | 50 | Hourly synoptic observations with supplementary one-hour data |
|  |  | 51 | Intermediate synoptic observations with supplementary one-hour data |
|  |  | 52 | Main synoptic observations with supplementary one-hour data |

Annex 1
BUFR template for surface observations from n-minute period

TM 307092

|  |  |  | Unit, scale |
| --- | --- | --- | --- |
| 3 01 089 |  | National station identification |  |
|  | 0 01 101 | State identifier (1) | Code table, 0 |
|  | 0 01 102 | National station number (1) | Numeric, 0 |
| 3 01 090 |  | Fixed surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 | Surface station identification |  |
|  |  | WMO block number | Numeric, 0 |
|  |  | WMO station number | Numeric, 0 |
|  |  | Station or site name | CCITT IA5, 0 |
|  |  | Type of station | Code table, 0 |
|  | 3 01 011 | Year(2) | Year, 0 |
|  |  | Month(2) | Month, 0 |
|  |  | Day(2) | Day, 0 |
|  | 3 01 012 | Hour(2) | Hour, 0 |
|  |  | Minute(2) | Minute, 0 |
|  | 3 01 021 | Latitude (high accuracy) | Degree, 5 |
|  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, 1 |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  | Surface station instrumentation |  |
|  | 0 02 180 | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 | Visibility measurement system | Code table, 0 |
|  | 0 02 183 | Cloud detection system | Code table, 0 |
|  | 0 02 184 | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 | Capability to discriminate lightning strikes | Flag table, 0 |
| 0 04 015 |  | Time increment (= - n minutes) | Minute, 0 |
| 0 04 065 |  | Short time increment ( = 1 minute) | Minute, 0 |
| 1 25 000 |  | Delayed replication of 25 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor (= n) | Numeric, 0 |
| 0 10 004 |  | Pressure | Pa, –1 |
| 3 02 070 |  | Wind data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 | Maximum wind gust speed | m s-1, 1 |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
| 3 02 072 |  | Temperature and humidity data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
| 0 07 032 |  | Height of sensor above local ground (for ground temperature) | m, 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature (scale 2) (for ground temperature) | K, 2 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  | Replicate 1 descriptor five times |  |
| 3 07 063 | 0 07 061 | Depth below land surface | m, 2 |
|  | 0 12 130 | Soil temperature (scale 2) | K, 2 |
| 0 07 061 |  | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 |  | Visibility data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 001 | Horizontal visibility | m, –1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 073 |  | Cloud data |  |
|  | 0 20 010 | Cloud cover (total) | %, 0 |
|  | 1 05 004 | Replicate 5 descriptors four times |  |
|  | 0 08 002 | Vertical significance | Code table, 0 |
|  | 0 20 011 | Cloud amount | Code table, 0 |
|  | 0 20 012 | Cloud type | Code table, 0 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 013 | Height of base of cloud | m, –1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 076 |  | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 | Type of precipitation | Flag table, 0 |
|  | 0 20 022 | Character of precipitation | Code table, 0 |
|  | 0 26 020 | Duration of precipitation(3) | Minute, 0 |
|  | 0 20 023 | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 | Obscuration | Flag table, 0 |
|  | 0 20 026 | Character of obscuration | Code table, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 13 155 |  | Intensity of precipitation (high accuracy) | kg m-2 s-1, 5 |
| 0 13 058 |  | Size of precipitation element | m, 4 |
|  |  | (end of the replicated sequence) |  |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  | Rate of ice accretion | Code table, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 |  | State of ground and snow depth measurement |  |
|  | 0 02 176 | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 | Total snow depth | m, 2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 079 |  | Precipitation measurement |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 02 175 | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 | Method of liquid water content measurement of precipitation | Code table, 0 |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 13 011 | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 080 |  | Evaporation measurement |  |
|  | 0 02 185 | Method of evaporation measurement | Code table, 0 |
|  | 0 04 025 | Time period or displacement ( = - n minutes) | Minute, 0 |
|  | 0 13 033 | Evaporation /evapotranspiration | kg m-2, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 081 |  | Total sunshine data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 14 031 | Total sunshine | Minute, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 082 |  | Radiation data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 14 002 | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - n minutes) | Minute |
| 0 13 059 |  | Number of flashes | Numeric |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 |  | First order statistics of P, W, T, U data |  |
|  | 0 04 025 | Time period (= - n minutes) | Minute, 0 |
|  | 0 08 023 | First order statistics (= 9; best estimate of standard deviation) (4) | Code table, 0 |
|  | 0 10 004 | Pressure | Pa, –1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 08 023 | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) shall be used to identify a station within the national numbering system that is completely independent of  the WMO international numbering system. The WMO international identification  0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station.

- The time identification refers to the end of the n-minute period.

- Duration of precipitation (in minutes) represents number of minutes in which any precipitation was registered.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

- If reporting nominal values is required, the template shall be supplemented with 3 07 093.

3 07 093 - Representation  of nominal values

| 3 07 093 |  | Nominal values |  |
| --- | --- | --- | --- |
|  | 2 23 000 | Substituted values operator |  |
|  | 2 36 000 | Backward reference bit map |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor = number of element descriptors | Numeric, 0 |
|  | 0 31 031 | Data present indicator | Numeric, 0 |
|  | 0 01 033 | Indication of originating/generating center | Code table, 0 |
|  | 0 01 032 | Generating application | Code table, 0 |
|  | 0 08 083 | Nominal value indicator | Flag table, 0 |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 255 | Substituted values |  |
|  | 1 08 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 000 | Substituted values operator |  |
|  | 2 37 000 | Use previously defined bit map |  |
|  | 0 01 033 | Indication of originating/generating center | Code table, 0 |
|  | 0 01 032 | Generating application | Code table, 0 |
|  | 0 08 083 | Nominal value indicator | Flag table, 0 |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 255 | Substituted values |  |