| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON REQUIREMENTS AND IMPLEMENTATION AWS PLATFORMS (ET-AWS) Sixth Session GENEVA, SWITZERLAND, 20 – 23 APRIL 2010 | CBS/OPAG-IOS (ET-AWS-6)/Doc. 10.3 (2.4.2010) _______ ITEM: 10 Original: ENGLISH |
| --- | --- |

Examples of usage TM 307093 for representation of nominal values

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains examples of usage TM 307093 for representation of representative heights of sensors and nominal values of selected elements of TM 307091.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the content of this document

and to formulate relevant recommendations.

__________________

.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.2.

[2] Meeting of Expert Team on Data Representation and Codes.

Darmstadt, 23 to 27 April 2007.

[3] Meeting of Expert Team on Requirements for Data from Automatic Weather Stations.

Geneva, 5 to 9 May 2008.

[4] Guide to WMO Table driven Code Forms: FM 94 BUFR and FM 95 CREX. Layer 3:

Detailed Description of the Code Forms.

1. 	Background

The Meeting of Expert Team on Data Representation and Codes (Darmstadt, 23 to 27 April 2007) recommended the sequence 3 07 093 (Representation of nominal values) for validation [2]. The Meeting of Expert Team on Requirements for Data from Automatic Weather Stations (Geneva, 5 to 9 May 2008) expressed no objections to the proposed approach [3]. The Joint Meeting of the CT-MTDCF and ET-DR&C (Geneva, 1 to 5 September 2008) and the First Meeting of the IPET-DRC (Geneva, 15  to 18 September 2009) recommended sequence 3 07 093 to be left in the stage of validation.

In March 2010, a draft version of the presented document was sent to IPET-DRC members. The author wishes to thank Mr. Akira Nakamori (JMA) for his valuable comments.

2. 	Operators 2 23 Y (Substituted values operators) in template TM 307093

Template TM 307093 is capable to express representative heights of sensors as well as nominal values of selected variables (elements) of a BUFR template to which it is appended; TM 307093 is appended to TM 307091 in the included examples.

Operators 2 23 000 and 2 23 255 allow presentation of substituted values (representative heights of sensors and nominal values of selected elements in 3 07 093). The process is initiated by 2 23 000, followed by defining of a “data present bit-map”. Construction of the bit-map is precisely described in the Guide to WMO Table driven Code Forms: FM 94 BUFR and FM 95 CREX [4]. Within 3 07 093, the data present bit-map is constructed by

| 2 36 000 | Backward reference bit map (to allow using the bit-map more than once) |
| --- | --- |
| 1 01 000 | Delayed replication of 1 descriptor |
| 0 31 001 | Delayed descriptor replication factor = number of data items |
| 0 31 031 | Data present indicator |

The data present bit-map is a bit string, where a bit set to 0 means “data present”, i.e. nominal value or representative height is required for the corresponding data item; a bit set to 1 means “data not present”, i.e. neither nominal value nor representative height is required for the corresponding data item. In the examples below, there are 13 bits set to 0 within the bit-map, i.e. representative height or nominal value is required for the corresponding 13 data items within TM 307091:

- Height of sensor above local ground (for temperature and humidity)

- Temperature/ air temperature

- Dew point temperature

- Relative humidity

- Height of sensor above local ground (for wind speed)

- Wind speed

- Maximum wind speed gust speed (10 minutes)

- Maximum wind speed gust speed  (60 minutes)

- Height of sensor above local ground (for temperature and humidity)

- Maximum temperature

- Minimum temperature

- Height of sensor above local ground (for precipitation)

- Total precipitation

Template for surface observations from one-hour period TM 307091 contains several short delayed replication factors to allow reduction of the data volume in case of reports from stations that are not equipped sufficiently to be capable to report values of all elements of TM 307091. Consequently, also the number of bits in the “data present bit-map” has to be reduced accordingly  (shown in Example 2).

3. 	Examples of usage TM 307093 for representation of nominal values of TM 307091

In the examples below, usage of TM 307093 for representation of representative heights of sensors and nominal values of selected elements of BUFR template for surface observations from one-hour period (TM 307091), is demonstrated. TM 307091 is included in the Annex to this document.

3 07 093 - Representation  of nominal values

| 3 07 093 |  | Nominal values |  |
| --- | --- | --- | --- |
|  | 2 23 000 | Substituted values operator |  |
|  | 2 36 000 | Backward reference bit map |  |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor = number of data items | Numeric, 0 |
|  | 0 31 031 | Data present indicator | Numeric, 0 |
|  | 0 01 033 | Indication of originating/generating center | Code table, 0 |
|  | 0 01 032 | Generating application | Code table, 0 |
|  | 0 08 083 | Nominal value indicator | Flag table, 0 |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 255 | Substituted values |  |
|  | 1 08 000 | Delayed replication of 8 descriptors |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 000 | Substituted values operator |  |
|  | 2 37 000 | Use previously defined bit map |  |
|  | 0 01 033 | Indication of originating/generating center | Code table, 0 |
|  | 0 01 032 | Generating application | Code table, 0 |
|  | 0 08 083 | Nominal value indicator | Flag table, 0 |
|  | 1 01 000 | Delayed replication of 1 descriptor |  |
|  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  | 2 23 255 | Substituted values |  |

008083

Nominal value indicator

Bit No.		Meaning

1		Adjusted with respect to representative height of sensor above local ground (or deck of marine platform)

2		Adjusted with respect to representative height of sensor above water surface

3		Adjusted with respect to standard surface roughness

4		Adjusted with respect to wind speed

5		Adjusted with respect to temperature

6		Adjusted with respect to pressure

7		Adjusted with respect to humidity

8		Adjusted with respect to evaporation

9		Adjusted with respect to wetting losses

10-14		Reserved

All 15	Missing value

Example 1:

Template TM 307093 is used to express representative height of sensors and nominal values of temperature, dew-point temperature, relative humidity, wind speed and total precipitation reported in TM 307091. The measured values of all selected elements are adjusted with respect to the representative height of sensors above local ground (Bit No.1 is set to 1 in 0 08 083).  Moreover, the measured value of wind speed is adjusted also with respect to standard surface roughness (Bit No.3 is set to 1 in 0 08 083). The amount of total precipitation is adjusted with respect to the representative height of sensor above local ground and with respect to wind speed (Bit No.1 and Bit No.4 are set to 1 in 0 08 083 for precipitation).

In Example 1, 307093 is applied to 307091, where all short delayed replication factors are set to 1, i.e. this station is equipped sufficiently to report all elements in TM 307091.

3 07 093 used for the expanded 3 07 091:

|  | Nominal values |  |
| --- | --- | --- |
| 2 23 000 | Substituted values operator |  |
| 2 36 000 | Backward reference bit map |  |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = number of expanded descriptors of 3 07 091 = 172 in Example 1 | Numeric |
| 0 31 031 | Data present indicator = 1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1, 0,1,0,0,0,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,0,1,1,1,1,0,1,1,1,0,1,1,0,1,1,1,0,1,1,0,0,1,1,1,1,1,0,1,1,1,0,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1 in Example 1 | Numeric 0 31 031 = 1 written in red correspond to 0 31 000 in 3 07 091 |
|  | Representative height of sensors and nominal values of temperature, dew-point temperature, relative humidity and extreme temperatures |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator Bit No.1=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values In 1st replication = Representative height of sensor above local ground (for temperature and humidity), in 2nd replication = Nominal value of temperature, in 3rth replication = Nominal value of dew-point temperature, in 4th replication = Nominal value of relative humidity, in 5th to 8th replication = Missing in 9th replication = Representative height of sensor above local ground (for temperature), in 10th replication = Nominal value of maximum temperature, in 11th replication = Nominal value of minimum temperature, in 12th and 13th replication = Missing. |  |
| 1 08 000 | Delayed replication of 8 descriptors is expanded as shown below |  |
| 0 31 001 | Delayed descriptor replication factor = 4 Representative height of sensor for wind speed Nominal values of wind speed Representative height of sensor for precipitation Nominal value of total precipitation |  |
|  | (1) Representative height of sensor for wind speed |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator Bit No.1=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (representative value of height) In 1st to 4th replication = Missing, in 5th replication = Representative height of sensor above local ground (for wind speed), in 6th to 13th replication = Missing. |  |
|  | (2) Nominal values of wind speed |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator (for wind speed) Bit No.1=1, Bit No.3=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (nominal values) In 1st to 5th replication = Missing, in 6th replication = Nominal value of wind speed, in 7th replication = Nominal value of maximum wind gust speed, in 8th replication = Nominal value of maximum wind gust speed, in 9th to 13th replication = Missing. |  |
|  | (3) Representative height of sensor for precipitation |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator Bit No.1=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (representative value of height) In 1st to 11th replication = Missing, in 12th replication = Representative height of sensor above local ground (for precipitation), in 13th replication = Missing. |  |
|  | (4) Nominal value of total precipitation |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator (for precipitation) Bit No.1=1, Bit No.4 = 1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (nominal values) In 1st to 12th replication = Missing, in 13th replication = Nominal value of total precipitation. |  |

Example 2:

Template TM 307093 is again used to express representative height of sensors and nominal values of temperature, dew-point temperature, relative humidity, wind speed and total precipitation  reported in TM 307091. The measured values of all selected elements are adjusted with respect to the representative height of sensors above local ground (Bit No.1 set to 1 in  0 08 083).  Moreover, the measured value of wind speed is adjusted also with respect to standard surface roughness (Bit No.3 set to 1 in  0 08 083). The amount of precipitation is adjusted with respect to the representative height of sensor above local ground and with respect to the wind speed (Bit No.1 and Bit No. 4 are set to 1 in  0 08 083 for precipitation).

In the Example 2, however, 307093 is applied to 307091, where only 0 31 000 preceding  302073 (Cloud data) and 302079 (Precipitation data) are set to 1, but all other short delayed replication factors are set to 0. This station is not equipped to report all elements in TM 307091, the short delayed replication factors being set to 0 reduce the number of data items of TM 307091 and therefore also the extent of the bit map is reduced accordingly.

3 07 093 used for the expanded 3 07 091:

|  | Nominal values |  |
| --- | --- | --- |
| 2 23 000 | Substituted values operator |  |
| 2 36 000 | Backward reference bit map |  |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = number of expanded descriptors of 3 07 091 = 107 in Example 2 | Numeric |
| 0 31 031 | Data present indicator = 1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1, 0,1,0,0,0,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,1,0,1,1,1,1,0,1,1,1,0,1,1,0,1,1,1,0,1,1,0,0,1,1,1,1,1,0,1,1,1,0,1,1,1,1,1,1,1,1 in Example 2 | Numeric 0 31 031 = 1 written in red correspond to 0 31 000 in 3 07 091 |
|  | Representative height of sensors and nominal values of temperature, dew-point temperature, relative humidity and extreme temperatures |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator Bit No.1=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values In 1st replication = Representative height of sensor above local ground (for temperature and humidity), in 2nd replication = Nominal value of temperature, in 3rth replication = Nominal value of dew-point temperature, in 4th replication = Nominal value of relative humidity, in 5th to 8th replication = Missing in 9th replication = Representative height of sensor above local ground (for temperature), in 10th replication = Nominal value of maximum temperature, in 11th replication = Nominal value of minimum temperature, in 12th and 13th replication = Missing. |  |
| 1 08 000 | Delayed replication of 8 descriptors is expanded as shown below |  |
| 0 31 001 | Delayed descriptor replication factor = 4 Representative height of sensor for wind speed Nominal values of wind speed Representative height of sensor for precipitation Nominal value of total precipitation |  |
|  | (1) Representative height of sensor for wind speed |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator Bit No.1=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (representative value of height) In 1st to 4th replication = Missing, in 5th replication = Representative height of sensor above local ground (for wind speed), in 6th to 13th replication = Missing. |  |
|  | (2) Nominal values of wind speed |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator (for wind speed) Bit No.1=1, Bit No.3 = 1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (nominal values) In 1st to 5th replication = Missing, in 6th replication = Nominal value of wind speed, in 7th replication = Nominal value of maximum wind gust speed, in 8th replication = Nominal value of maximum wind gust speed, in 9th to 13th replication = Missing. |  |
|  | (3) Representative height of sensor for precipitation |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator Bit No.1=1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (representative value of height) In 1st to 11th replication = Missing, in 12th replication = Representative height of sensor above local ground (for precipitation), in 13th replication = Missing. |  |
|  | (4) Nominal value of total precipitation |  |
| 2 23 000 | Substituted values operator |  |
| 2 37 000 | Use previously defined bit map |  |
| 0 01 033 | Indication of originating/generating center | Code table |
| 0 01 032 | Generating application | Code table |
| 0 08 083 | Nominal value indicator (for precipitation) Bit No.1=1, Bit No.4 = 1 | Flag table |
| 1 01 000 | Delayed replication of 1 descriptor |  |
| 0 31 001 | Delayed descriptor replication factor = 13 | Numeric |
| 2 23 255 | Substituted values (nominal values) In 1st to 12th replication = Missing, in 13th replication = Nominal value of total precipitation. |  |

ANNEX

TM 307091 - BUFR template for surface observations from one-hour period

|  |  |  | Unit, scale |
| --- | --- | --- | --- |
| 3 01 089 |  | National station identification |  |
|  | 0 01 101 | State identifier (1) | Code table, 0 |
|  | 0 01 102 | National station number (1) | Numeric, 0 |
| 3 01 090 |  | Fixed surface station identification; time, horizontal and vertical co-ordinates |  |
|  | 3 01 004 | Surface station identification |  |
|  |  | WMO block number(1) | Numeric, 0 |
|  |  | WMO station number(1) | Numeric, 0 |
|  |  | Station or site name | CCITT IA5, 0 |
|  |  | Type of station | Code table, 0 |
|  | 3 01 011 | Year(2) | Year, 0 |
|  |  | Month(2) | Month, 0 |
|  |  | Day(2) | Day, 0 |
|  | 3 01 012 | Hour(2) | Hour, 0 |
|  |  | Minute(2) | Minute, 0 |
|  | 3 01 021 | Latitude (high accuracy) | Degree, 5 |
|  |  | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, 1 |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table, 0 |
| 3 01 091 |  | Surface station instrumentation |  |
|  | 0 02 180 | Main present weather detecting system | Code table, 0 |
|  | 0 02 181 | Supplementary present weather sensor | Flag table, 0 |
|  | 0 02 182 | Visibility measurement system | Code table, 0 |
|  | 0 02 183 | Cloud detection system | Code table, 0 |
|  | 0 02 184 | Type of lightning detection sensor | Code table, 0 |
|  | 0 02 179 | Type of sky condition algorithm | Code table, 0 |
|  | 0 02 186 | Capability to detect precipitation phenomena | Flag table, 0 |
|  | 0 02 187 | Capability to detect other weather phenomena | Flag table, 0 |
|  | 0 02 188 | Capability to detect obscuration | Flag table, 0 |
|  | 0 02 189 | Capability to discriminate lightning strikes | Flag table, 0 |
| 3 02 001 | 0 10 004 | Pressure | Pa, –1 |
|  | 0 10 051 | Pressure reduced to mean sea level | Pa, –1 |
|  | 0 10 061 | 3-hour pressure change(3) | Pa, –1 |
|  | 0 10 063 | Characteristic of pressure tendency(3) | Code table, 0 |
| 0 07 004 |  | Pressure (standard level) | Pa, –1 |
| 0 10 009 |  | Geopotential height of the standard level | gpm, 0 |
| 3 02 072 |  | Temperature and humidity data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 12 101 | Temperature/air-temperature (scale 2) | K, 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
| 1 03 000 |  | Delayed replication of 3 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 1 01 005 |  | Replicate 1 descriptor five times |  |
| 3 07 063 | 0 07 061 | Depth below land surface | m, 2 |
|  | 0 12 130 | Soil temperature (scale 2) | K, 2 |
| 0 07 061 |  | Depth below land surface (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 069 |  | Visibility data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 001 | Horizontal visibility | m, –1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 05 000 |  | Delayed replication of 5 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 20 031 |  | Ice deposit (thickness) | m, 2 |
| 0 20 032 |  | Rate of ice accretion | Code table, 0 |
| 0 02 038 |  | Method of sea surface temperature measurement | Code table, 0 |
| 0 22 043 |  | Sea/water temperature (scale 2) | K, 2 |
| 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  | 0 22 011 | Period of waves | s, 0 |
|  | 0 22 021 | Height of waves | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 078 |  | State of ground and snow depth measurement |  |
|  | 0 02 176 | Method of state of ground measurement | Code table, 0 |
|  | 0 20 062 | State of ground (with or without snow) | Code table, 0 |
|  | 0 02 177 | Method of snow depth measurement | Code table, 0 |
|  | 0 13 013 | Total snow depth | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 073 |  | Cloud data |  |
|  | 0 20 010 | Cloud cover (total) | %, 0 |
|  | 1 05 004 | Replicate 5 descriptors four times |  |
|  | 0 08 002 | Vertical significance | Code table, 0 |
|  | 0 20 011 | Cloud amount | Code table, 0 |
|  | 0 20 012 | Cloud type | Code table, 0 |
|  | 0 33 041 | Attribute of following value | Code table, 0 |
|  | 0 20 013 | Height of base of cloud | m, -1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 074 |  | Present and past weather |  |
|  | 0 20 003 | Present weather(4) | Code table, 0 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 20 004 | Past weather (1) (4) | Code table, 0 |
|  | 0 20 005 | Past weather (2) (4) | Code table, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 175 |  | Intensity of precipitation, size of precipitation element |  |
|  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 13 155 | Intensity of precipitation (high accuracy) | Kg m-2 s-1, 5 |
|  | 0 13 058 | Size of precipitation element | m, 4 |
|  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute, 0 |
| 3 02 076 |  | Precipitation, obscuration and other phenomena |  |
|  | 0 20 021 | Type of precipitation | Flag table, 0 |
|  | 0 20 022 | Character of precipitation | Code table, 0 |
|  | 0 26 020 | Duration of precipitation (5) | Minute, 0 |
|  | 0 20 023 | Other weather phenomena | Flag table, 0 |
|  | 0 20 024 | Intensity of phenomena | Code table, 0 |
|  | 0 20 025 | Obscuration | Flag table, 0 |
|  | 0 20 026 | Character of obscuration | Code table, 0 |
| 3 02 071 |  | Wind data from one-hour period |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind, if any) | Minute, 0 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  | 0 04 025 | Time period (= - 10 minutes in the first replication, = - 60 minutes in the second replication) | Minute, 0 |
|  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  | 0 11 041 | Maximum wind gust speed | m s-1, 1 |
|  | 0 04 025 | Time period (= - 10 minutes) | Minute, 0 |
|  | 0 11 016 | Extreme counterclockwise wind direction of a variable wind | Degree true, 0 |
|  | 0 11 017 | Extreme clockwise wind direction of a variable wind | Degree true, 0 |
| 3 02 077 |  | Extreme temperature data |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 07 033 | Height of sensor above water surface | m, 1 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified | K, 2 |
|  | 0 07 032 | Height of sensor above local ground (for ground temperature) | m, 2 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified (for ground temperature) | K, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 079 |  | Precipitation measurement |  |
|  | 0 07 032 | Height of sensor above local ground | m, 2 |
|  | 0 02 175 | Method of precipitation measurement | Code table, 0 |
|  | 0 02 178 | Method of liquid water content measurement of precipitation | Code table, 0 |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 13 011 | Total precipitation / total water equivalent of snow | kg m-2, 1 |
| 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 080 |  | Evaporation measurement |  |
|  | 0 02 185 | Method of evaporation measurement | Code table, 0 |
|  | 0 04 025 | Time period ( = - 60 minutes) | Minute, 0 |
|  | 0 13 033 | Evaporation /evapotranspiration | kg m-2, 1 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 081 |  | Total sunshine data |  |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 14 031 | Total sunshine | Minute, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 082 |  | Radiation data |  |
|  | 0 04 025 | Time period (= - 60 minutes) | Minute, 0 |
|  | 0 14 002 | Long-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 004 | Short-wave radiation, integrated over period specified | J m-2, -3 |
|  | 0 14 016 | Net radiation, integrated over period specified | J m-2, -4 |
|  | 0 14 028 | Global solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 029 | Diffuse solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
|  | 0 14 030 | Direct solar radiation (high accuracy), integrated over period specified | J m-2, -2 |
| 1 02 000 |  | Delayed replication of 2 descriptors |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 0 04 025 |  | Time period (= - 10 minutes) | Minute, 0 |
| 0 13 059 |  | Number of flashes | Numeric, 0 |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
| 3 02 083 |  | First order statistics of P, W, T, U data |  |
|  | 0 04 025 | Time period (= -10 minutes ) | Minute, 0 |
|  | 0 08 023 | First order statistics (= 9 (best estimate of standard deviation)) (6) | Code table, 0 |
|  | 0 10 004 | Pressure | Pa, –1 |
|  | 0 11 001 | Wind direction | Degree true, 0 |
|  | 0 11 002 | Wind speed | m s-1, 1 |
|  | 0 12 101 | Temperature/air-temperature (scale 2) | K, 2 |
|  | 0 13 003 | Relative humidity | %, 0 |
|  | 0 08 023 | First order statistics (= missing value) | Code table, 0 |
| 0 33 005 |  | Quality information (AWS data) | Flag table, 0 |
| 0 33 006 |  | Internal measurement status information (AWS) | Code table, 0 |

Notes:

- 0 01 101 (WMO Member State identifier) and 0 01 102 (National AWS number) shall be used to identify a station within the national numbering system that is completely independent of the WMO international numbering system. The WMO international identification 0 01 001 (WMO block number) and 0 01 002 (WMO station number) shall be reported if available for the particular station.

- The time identification refers to the end of the one-hour period.

- 0 10 061 (3-hour pressure change) and 0 10 063 (Characteristic of pressure tendency) are included in this template, although they refer to 3-hour period preceding the time of observation.

- Present weather may be represented only by 0 20 003, especially if reported from a manned non-automated station. When encoding present weather reported from an automatic weather station, the sequence of descriptors (proposed under 3 02 076) should be used, if applicable.

- Duration of precipitation (in minutes) represents number of minutes in which any precipitation was registered.

- Best estimate of standard deviation is counted out of a set of samples (signal measurements) recorded within the period specified; it should be reported as a missing value, if the measurements of the relevant element are not available from a part of the period specified by 0 04 025.

- If reporting nominal values is required, the template shall be supplemented with 3 07 093.