| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON REQUIREMENTS AND IMPLEMENTATION AWS PLATFORMS (ET-AWS) Sixth Session GENEVA, SWITZERLAND, 20 – 23 APRIL 2010 | CBS/OPAG-IOS (ET-AWS-6)/Doc. 6 (18.6.2010) _______ ITEM: 6 Original: ENGLISH |
| --- | --- |

Requirements for AWS in support of the validation of space-based observations

Submitted by Karl Monnik (Australia)

________________________________________________________________

Summary and Purpose of Document

The document provides a summary on the developments of the proposal to utilise AWS observations to support the validation of space-based observations

________________________________________________________________

ACTION PROPOSED

The meeting is invited to discuss the information contained in this document when considering its recommendations.

Appendix:

References:

ET-AWS-5, Doc5.doc. Requirements and Subsequent Implementation Plan for AWS Hosted Sensors to Contribute Directly to the Calibration and Ground Truth of Space-Based Observations

Dossier on the space-based component of the GOS (January 2010)

Requirements for AWS in support of the validation of space-based observations

Introduction

- ET-AWS-5 proposed the consideration of using surface-based observations to contribute to the ground-truthing of remotely sensed observations, such as sensors based on satellite platforms.

- The initiative was welcomed by ET-SAT and ET-SUP to consider the potential of AWS networks to support calibration of space-based observations and product validation. The approach was considered particularly relevant in the context of WIGOS and space-surface integration. However the proposal was lacking in details concerning what networks and surface-based observations could be candidates.

Discussion

- Recognising that in the “Vision for the Global Observing System in 2025” stated that the surface-based GOS will provide, inter alia, data for calibration and validation of space-based data; the following concept should be considered.

- Modern AWS networks provide the following opportunities.

- AWS platforms are able to record, process and transmit observations from a wide range of electronic sensors; these sensors are no longer limited to the standard meteorological variables. Sensors which observe parameters in a manner similar to satellite remotely-sensed observations.

- AWS platforms are able to process and transmit data over a range of temporal periods which can be aligned with observation frequency of other systems;

- The GTS is capable to transmit messages in BUFR which is flexible and adaptable;

- National AWS networks can satisfy international standards for the GOS providing consistency in observation;

- AWS networks have a global reach which covers all continents and climates;

- On the other hand, spaced-based observations in the GOS:

- provide spatial coverage at a global scale;

- provide gridded observations at specific horizontal and vertical scales and at a observing cycle;

- provide geophysical observations which are remotely-sensed and therefore not exactly the same as the traditional observations made by surface networks.

- The initial proposal was examine the opportunities for ground-truthing of satellite observations. While this approach may have merit, a broader approach of integration between space-based and surface-based observations may provide greater value to the GOS.

- The following table lists geophysical parameters which are potentially observed by instruments on satellite platforms (Source: GOS-2010, January - Volume III (Gap Analysis); page 6). The highlighted cells indicate surface parameters which could be potentially observed by automated surface-based instruments on a global scale.

| Geophysical parameters addressed by the multi-purpose VIS/IR imagery mission in LEO |
| --- |
| Cloud imagery | Total aerosol optical depth | Snow detection (mask) |
| Cloud cover (total column) | Total aerosol type | Snow cover |
| Cloud type | Short-wave cloud reflectance | Snow surface temperature |
| Cloud optical depth | Downwelling SW irradiance at Earth’s surface | Snow albedo |
| Cloud top height | Downwelling LW irradiance at Earth’s surface | Frozen soil and permafrost |
| Cloud top temperature | Earth’s surface albedo | Leaf Area Index (LAI) |
| Cloud drop effective radius at cloud top | Surface emissivity in TIR window channels | Normalised Difference Vegetation Index (NDVI) |
| Cloud ice total column | Sea surface temperature | Photosynthetically Active Radiation (PAR) |
| Cloud ice effective radius at cloud top | Sea-ice surface temperature | Fractional Absorbed PAR (FAPAR) |
| Water vapour imagery | Sea-ice cover | Fire temperature |
| Wind vectors in polar regions | Land surface temperature | Fire fractional cover |
| Water vapour total column | Surface soil moisture (index) | Fire radiative power |

| Geophysical parameters addressed by the multi-purpose VIS/IR imagery mission in GEO |
| --- |
| Cloud imagery | Total aerosol optical depth | Snow detection (mask) |
| Cloud cover (total column) | Total aerosol type | Snow cover |
| Cloud type | Short-wave cloud reflectance | Snow surface temperature |
| Cloud optical depth | Downwelling SW irradiance at Earth’s surface | Snow albedo |
| Cloud top height | Downwelling LW irradiance at Earth’s surface | Frozen soil and permafrost |
| Cloud top temperature | Earth’s surface albedo | Leaf Area Index (LAI) |
| Cloud drop effective radius at cloud top | Surface emissivity in TIR window channels | Normalised Difference Vegetation Index (NDVI) |
| Cloud ice effective radius at cloud top | Sea surface temperature | Photosynthetically Active Radiation (PAR) |
| Water vapour imagery | Sea-ice surface temperature | Fractional Absorbed PAR (FAPAR) |
| Water vapour total column | Sea-ice cover | Fire temperature |
| Wind vectors from trace motion | Land surface temperature | Fire fractional cover |
| Precipitation rate at surface | Surface soil moisture (index) | Fire radiative power |
| Accumulated precipitation |  |  |

- The document “Evaluation of the potential quality of post-2020 satellite products” (Source: GOS-2010, January - Volume IV (Products)), indicates the following satellite products which have potential to be observed by surface-based instruments. Further information concerning these products is listed in Appendix I.

| Ref | Geophysical parameter |
| --- | --- |
| 024 | Precipitation rate at surface (liquid or solid) |
| 025 | Accumulated precipitation (over 24 hours) |
| 035 | Downwelling LW irradiance at Earth’s surface |
| 036 | Downwelling SW irradiance at Earth’s surface |
| 037 | Earth’s surface albedo |
| 041 | Photosynthetically Active Radiation (PAR) |
| 059 | Land surface temperature |
| 061 | Soil moisture at surface |
| 062 | Soil moisture profile (in the roots region) |

- These parameters could potentially be reported by surface-based AWSs at a temporal resolution which could be aligned with the satellite observing cycle.

Conclusion

- That ET-AWS consider the opportunity of providing observations in a more generic and flexible when reviewing standards and functional requirements for AWSs.

Appendix I

Excerpt from: Dossier on the space-based component of the GOS Vol. IV. Estimated performance of products from typical satellite instruments

| 024 | Precipitation rate at surface (liquid or solid) |
| --- | --- |

| 024.1 | Precipitation radar |
| --- | --- |
| Principle | Backscattered radiation from cloud drops by medium frequency radar (dual-frequency preferred, 14 and 35 GHz). Doppler capability also useful. |
| Accuracy | Generally good, depending on drop size and liquid/ice ratio. |
| Coverage | Infrequent, due to limited scanning capability. |
| (x | Better at 35 GHz than at 14 GHz, but drawback of saturation for heavy rain. |
| Conditions | Night and day. |
| Reference | Applicable only in LEO (see instrument 19). |

| 024.2 | MW/Sub-mm sounding |
| --- | --- |
| Principle | MW/Sub-mm radiation in window channels (typically, ~ 10, 19, 37, 90, 150 GHz) with dual polarisation, and absorption bands (typically, ( 54, 118, 183, 380, 425 GHz). Actually, the precipitation profile is retrieved with the help of an associated NWP model, possibly cloud-resolving. |
| Accuracy | Depending on drop size and liquid/ice ratio. Lower frequencies more sensitive to liquid water. |
| Coverage | Frequent, due to cross-nadir relatively large swath (from LEO, often conical scanning). |
| (x | Limited by antenna size. |
| Conditions | Night and day. |
| Reference | Applicable both in LEO (see instruments 05 and 07) and GEO (see instrument 06). |

| 024.3 | VIS/IR radiometry |
| --- | --- |
| Principle | Inferred from cloud imagery in a few discrete channels selected so as to detect all cloud types, assisted by conceptual models, generally more responsive to convective rain. |
| Accuracy | Difficult to be stated. Better for convective precipitation. Frequent imagery essential. |
| Coverage | Frequent, due to large cross-nadir swath of the originating image. |
| (x | Several pixels have to be co-processed to have sufficient statistics to derive cluster properties. |
| Conditions | Night and day. More information available in daylight. |
| Reference | Applicable only in GEO (see instrument 02). |

| 024.4 | Fusion between MW from LEO and IR from GEO |
| --- | --- |
| Principle | Combined product of LEO/MW-derived accurate/infrequent measurements with GEO/IR frequent images used either to be ‘calibrated’ by MW measurements or to enable dynamical interpolation between MW-derived precipitation data. |
| Accuracy | Changing with ‘distance’ from the closest accurate MW determination. Better performance for convective precipitation. |
| Coverage | Frequent, due to large cross-nadir swath of the originating images. |
| (x | Several pixels have to be co-processed to have sufficient statistics to derive cluster properties. |
| Conditions | Night and day. |
| Reference | Applicable by using MW in LEO (see instruments 05 and 07) and IR in GEO (see instrument 02). |

Estimated potential quality of product “Precipitation rate at surface (liquid or solid)” (> 2020)

| Parameter 024 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Precipitation rate at surface (liquid or solid) | LEO | Precipitation radar | 10 | % | 5 | - | 120 | 1 | - |
|  | LEO | MW radiometry | 20 | % | 10 | - | 3 | 8 (GPM) | Heavily model-aided |
|  | GEO | MW/Sub-mm sounding | 30 | % | 10 | - | 0.25 | 1 | Heavily model-aided |
|  | GEO | VIS/IR radiometry | 100 | % | 10 | - | 0.1 | 1 | Convection only |
|  | GEO | LEO/MW + GEO/IR fusion | 50 | % | 10 | - | 0.1 | 1 | Product from data-fusion |

| 025 | Accumulated precipitation (over 24 hours) |
| --- | --- |

| 025.1 | From fusion between MW from LEO and IR from GEO |
| --- | --- |
| Principle | Derived by time integration of frequent precipitation rate measured by merging MW precipitation rate data from LEO with IR imagery from GEO. For technique and characteristics, see table 25.4. |
| Reference | Applicable by using MW in LEO (see instruments 05 and 07) and IR in GEO (see instrument 02). |

| 025.2 | From MW/Sub-mm sounding |
| --- | --- |
| Principle | Derived by time integration of frequent precipitation rate measured by MW/Sub-mm sounders in GEO. For technique and characteristics, see table 25.2. |
| Reference | Applicable only in GEO (see instrument 06). |

Estimated potential quality of product “Accumulated precipitation (over 24 hours)” (> 2020)

| Parameter 025 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Accumulated precipitation (over 24 hours) | GEO | LEO/MW + GEO/IR fusion | 50 | % | 10 | - | 3 | 1 | Product from data-fusion |
|  | GEO | MW/Sub-mm sounding | 30 | % | 10 | - | 3 | 1 | Heavily model-aided |

| 035 | Downwelling LW irradiance at Earth’s surface |
| --- | --- |

| 035.1 | From IR/MW sounding |
| --- | --- |
| Principle | High-level product derived mostly from atmospheric temperature and water vapour profiles (see tables 001 and 004 respectively). Contributions also from cloud cover profile (table 014), specifically cloud base height (table 015), defective to be observed. Atmospheric modelling necessary. |
| Reference | Applicable both in LEO (see instruments 01, 03 and 05) and GEO (see instruments 02, 04 and 06). |

Estimated potential quality of product “Downwelling LW irradiance at Earth’s surface” (> 2020)

| Parameter 035 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Downwelling LW irradiance at Earth’s surface | LEO | From IR/MW sounding | 5 | W/m2 | 20 | - | 4 | 3 | Model-aided |
|  | GEO | From IR/MW sounding | 5 | W/m2 | 20 | - | 0.25 | 1 | Model-aided |

| 036 | Downwelling SW irradiance at Earth’s surface |
| --- | --- |

| 036.1 | SW radiometry |
| --- | --- |
| Principle | High-level product derived from observation of scattered solar radiation in several narrow-band channels of VIS, NIR and SWIR to estimate attenuation from clouds and aerosol. Multiple viewing and multi-polarisation help. |
| Accuracy | Depending on number and bandwidths of channels and on the atmospheric model utilised. |
| Coverage | Frequent, due to cross-nadir large swath. |
| (x | Several pixels have to be co-processed to search for the least contaminated from clouds. |
| Conditions | Daylight only. Cloud-free or broken cloudiness. |
| Reference | Applicable both in LEO (see instrument 01 and 16) and GEO (see instrument 02). |

Estimated potential quality of product “Downwelling SW irradiance at Earth’s surface” (> 2020)

| Parameter 036 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Downwelling SW irradiance at Earth’s surface | LEO | SW radiometry | 10 | W/m2 | 4 | - | 4 | 3 | Clear-air, model-aided |
|  | GEO | SW radiometry | 15 | W/m2 | 8 | - | 0.1 | 1 | Clear-air, model-aided |

| 037 | Earth’s surface albedo |
| --- | --- |

| 037.1 | SW radiometry |
| --- | --- |
| Principle | High level product after measuring scattered solar radiation in several channels of VIS under several viewing angles and solar angles to estimate anisotropy effects and improve radiative fluxes computations. Channels for atmospheric corrections also included. |
| Accuracy | Depending on the number of different viewing conditions and the atmospheric model utilised. |
| Coverage | Infrequent, due to the need for collecting observations under different viewing conditions. |
| (x | Several pixels have to be co-processed to search for the least contaminated from clouds. |
| Conditions | Daylight only. Cloud-free or broken cloudiness. |
| Reference | Applicable both in LEO (see instruments 01 and 16) and GEO (see instrument 02). |

Estimated potential quality of product “Earth surface albedo” (> 2020)

| Parameter 037 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Earth’s surface albedo | LEO | Multi-view SW radiometry | 1 | % | 10 | - | 168 | 1 | Clear-air, model-aided |
|  | LEO | SW radiometry | 3 | % | 4 | - | 168 | 3 | Clear-air, heavily model-aided |
|  | GEO | SW radiometry | 5 | % | 8 | - | 72 | 1 | Clear-air, heavily model-aided |

| 041 | Photosynthetically Active Radiation (PAR) |
| --- | --- |

| 041.1 | VIS radiometry |
| --- | --- |
| Principle | High-level product similar to “37 - Downwelling short-wave irradiance at Earth surface” except that it refers to the interval 0.4-0.7 (m used by vegetation for photosynthesis. |
| Accuracy | Depending on information on clouds and aerosol and on the atmospheric model utilised. |
| Coverage | Frequent, due to cross-nadir large swath. |
| (x | Several pixels have to be co-processed to search for the least contaminated from clouds. |
| Conditions | Daylight only. Cloud-free or broken cloudiness. |
| Reference | Applicable both in LEO (see instruments 01 and 16) and GEO (see instrument 02). |

Estimated potential quality of product “Photosynthetically Active Radiation (PAR)” (> 2020)

| Parameter 041 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Photosynthetically Active Radiation (PAR) | LEO | VIS radiometry | 10 | W/m2 | 4 | - | 4 | 3 | Clear-air, model-aided |
|  | GEO | VIS radiometry | 10 | W/m2 | 8 | - | 0.1 | 1 | Clear-air, model-aided |

| 059 | Land surface temperature |
| --- | --- |

| 059.1 | IR radiometry |
| --- | --- |
| Principle | Derived from IR imagery in a number of channels including “windows” and other ones necessary to evaluate emissivity and atmospheric attenuation (from water vapour). Dual-view improves the accuracy of atmospheric correction, |
| Accuracy | Depending on number of channels and the knowledge (or estimate) of emissivity. |
| Coverage | Frequent, due to large cross-nadir swath of the originating image. |
| (x | Several pixels have to be co-processed to search for the least contaminated from clouds. |
| Conditions | Night and day. Cloud-free or broken cloudiness. |
| Reference | Applicable both in LEO (see instrument 01) and GEO (see instrument 02). |

| 059.2 | IR spectroscopy |
| --- | --- |
| Principle | Derived from the multiple number of narrow windows through the IR spectrum, associated to all possible information on atmospheric corrections. This enables to estimate emissivity. |
| Accuracy | Good, compatibly with the larger IFOV of sounders as compared to imagers. |
| Coverage | Frequent, due to large cross-nadir swath. |
| (x | Several pixels have to be co-processed to search for the least contaminated from clouds. |
| Conditions | Night and day. Cloud-free or broken cloudiness. |
| Reference | Applicable both in LEO (see instrument 03) and GEO (see instrument 04). |

| 059.3 | MW radiometry |
| --- | --- |
| Principle | Emitted and scattered MW radiation in atmospheric windows at low-medium frequencies (e.g., 5, 10 GHz). More polarisations needed, to correct for wetness effects. |
| Accuracy | Depending on wetness and vegetation. Good for bare and dry soil. |
| Coverage | Frequent, due to relatively large cross-nadir swath (conical scanning used). |
| (x | Limited by antenna size. |
| Conditions | Night and day. All weather. |
| Reference | Applicable only in LEO (see instrument 08). |

Estimated potential quality of product “Land surface temperature” (> 2020)

| Parameter 059 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Land surface temperature | LEO | IR radiometry | 2 | K | 8 | - | 4 | 3 | Clear-air |
|  | GEO | IR radiometry | 4 | K | 24 | - | 0.1 | 1 | Clear-air |
|  | LEO | IR spectroscopy | 1 | K | 20 |  | 4 | 3 | Clear-air |
|  | GEO | IR spectroscopy | 1 | K | 20 |  | 0.25 | 1 | Clear-air |
|  | LEO | MW radiometry | 1 | K | 50 | - | 8 | 3 | All weather |

| 061 | Soil moisture at surface |
| --- | --- |

| 061.1 | MW radiometry |
| --- | --- |
| Principle | Emitted MW radiation at low frequencies (e.g., 1.4 and 2.7 GHz). More polarisations needed, to correct for roughness effects. More channels desirable, to correct for temperature. Higher frequencies (5, 10 GHz) also useful, particularly for bare soil. |
| Accuracy | Good at lower frequencies, progressively worse at higher frequencies (vegetation sensitive). |
| Coverage | Frequent, due to relatively large cross-nadir swath (conical scanning used). |
| (x | Limited by antenna size. Synthetic aperture possible, at the expenses of sensitivity. |
| Conditions | Night and day. All weather. |
| Reference | Applicable only in LEO (see instrument 08). |

| 061.2 | Radar scatterometry |
| --- | --- |
| Principle | Backscattered MW radiation at relatively low frequencies (e.g., 5 GHz). The multiple viewing angle capability is exploited to correct for roughness. |
| Accuracy | Good for bare soil. |
| Coverage | Frequent, due to relatively large cross-nadir swath. |
| (x | Limited by antenna size. |
| Conditions | Night and day. All weather. |
| Reference | Applicable only in LEO (see instrument 12). |

| 061.3 | SAR imagery |
| --- | --- |
| Principle | Backscattered MW radiation at frequencies 1.3 or 5 or 11 GHz collected by synthetic aperture radar. |
| Accuracy | Lower frequencies have better performance, especially over vegetation. |
| Coverage | Infrequent, due to limited cross-track swath and limited instrument duty cycle. |
| (x | Synthesised by signal processing. Relatively good resolution used for this purpose. |
| Conditions | Night and day. All weather. |
| Reference | Applicable only in LEO (see instrument 29). |

| 061.4 | VIS/IR radiometry |
| --- | --- |
| Principle | Several proxies possible. Examples: damping of reflectivity from VIS/NIR to SWIR; from Apparent Thermal Inertia (ATI) derived by measuring the delay of land temperature rising in response to incoming solar radiation (valid for bare soil). |
| Accuracy | Discontinuous, depending on knowledge of soil structure and conditions. |
| Coverage | Frequent, due to large cross-nadir swath of the originating image. |
| (x | Several pixels have to be co-processed to search for the least contaminated from clouds. |
| Conditions | Daylight only, following soil heating. Cloud-free or broken cloudiness. |
| Reference | Applicable both in LEO (see instrument 01) and GEO (see instrument 02). |

Estimated potential quality of product “Soil moisture at surface” (> 2020)

| Parameter 061 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Soil moisture at surface | LEO | MW radiometry | 5 | m3(m-3 % | 30 | - | 8 | 3 | All weather, vegetation-sensitive |
|  | LEO | Radar scatterometry | 5 | m3(m-3 % | 20 | - | 36 | 1 | All weather, vegetation-sensitive |
|  | LEO | SAR imagery | 10 | m3(m-3 % | 0.1 | - | 360 | 2 | All weather, vegetation-sensitive |
|  | LEO | VIS/IR radiometry | 50 | m3(m-3 % | 4 | - | 4 | 3 | Clear-air, vegetation-sensitive |
|  | GEO | VIS/IR radiometry | 50 | m3(m-3 % | 12 | - | 0.1 | 1 | Clear-air, vegetation-sensitive |

| 062 | Soil moisture profile (in the roots region) (required from surface to 2 m below) |
| --- | --- |

| 062.1 | L-band MW radiometry |
| --- | --- |
| Principle | Emitted MW radiation at low frequencies (e.g., 1.4 GHz). More polarisations needed, to correct for roughness effects. |
| ∆z | Reconstructed by modelling in a depth of about 2 m below surface. |
| Accuracy | Good except for thick forests. |
| Coverage | Frequent, due to relatively large cross-nadir swath (conical scanning used). |
| (x | Limited by antenna size. Synthetic aperture used. |
| Conditions | Night and day. All weather. |
| Reference | Applicable only in LEO (see instrument 08). |

| 062.2 | L-band SAR imagery |
| --- | --- |
| Principle | Backscattered MW radiation at low frequency (typical, 1.3 GHz) collected by SAR. Lower frequency (P-band, ~ 300 MHz) also possible. |
| ∆z | Reconstructed by modelling in a depth of about 2 m below surface. |
| Accuracy | Good except for thick forests, that would require P-band. |
| Coverage | Infrequent, due to limited cross-track swath and limited instrument duty cycle. |
| (x | Synthesised by signal processing. Relatively good resolution used for this purpose. |
| Conditions | Night and day. All weather. |
| Reference | Applicable only in LEO (see instrument 29). |

Estimated potential quality of product “Soil moisture profile” (> 2020)

| Parameter 062 | Orbit | Technique | Accuracy | (RMS) | (x (km) | (z (km) | (t (h) | Number of sats | Conditions |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Soil moisture profile (in the roots region) Surface to 2 m below | LEO | L-band MW radiometry | 5 | m3(m-3 % | 50 | 0.0001 | 72 | 1 | All weather, model-aided |
|  | LEO | L-band SAR imagery | 10 | m3(m-3 % | 0.1 | 0.0001 | 1440 | 1 | All weather, model-aided |