| WORLD METEOROLOGICAL ORGANIZATION ______________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON EVOLUTION OF THE GLOBAL OBSERVING SYSTEM SECOND SESSION GENEVA, SWITZERLAND, 10 – 14 JULY 2006 |  | CBS/OPAG-IOS/ET-EGOS-2/Doc. 5, ADD 1 (26.VI.2006) ____________ ITEM: 5 Original: ENGLISH |
| --- | --- | --- |

# EXPECTED PERFORMANCE OF OPERATIONAL AND R&D SATELLITES IN THE SPACE-BASED GLOBAL OBSERVING SYSTEM

(Submitted by the WMO Secretariat)

1.	For satellite instruments only, it should be noted that the database contains two sets of expected performances: space agencies; and user (provided by the former Expert Team on Observational Data Requirements and Redesign of the Global Observing System [ETODRRGOS]) and now called the Expert Team on Evolution of the GOS (ET-EGOS).  While in the Rolling Review of Requirements process only WMO (user) provided estimates are utilized, there are several requirements for which no expected performances exist in the WMO (user) estimates, whereas estimates do exist from the space agency.  A list of WMO requirements that have no corresponding user estimates but for which there are space agency estimates of satellite system performances is contained in Appendix B.  Appendix B may serve the Expert Team as a guide in developing new user estimates.

2.	It is anticipated that the meeting will review and update Appendix A using Appendix B where appropriate.

Appendices:	A.	User Estimates of Observing System Performances

B.	WMO requirements without match in user estimates but with a match in space agency estimates

# APPENDIX A

# USER ESTIMATES OF OBSERVING SYSTEM PERFORMANCES

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

AATSR	Cloud cover	15	km	10	% (Max)	36	h	3	h	Reasonable

AATSR	Cloud imagery	1	km	36	h	3	h	Reasonable

AATSR	Cloud type	15	km	8	classes	36	h	3	h	Speculative

AATSR	Fire area	1	m2	20	% (Max)	1.5	d	0.125	d	Reasonable

AATSR	Fire temperature	1	K	50	K	1.5	d	0.125	d	Reasonable

AATSR	Land cover	1000	m	10	classes	0.01	y	1	d	Reasonable

AATSR	Leaf Area Index (LAI)	1	km	20	% (Max)	30	d	1	d	Tentative

AATSR	Long-wave Earth surface emissivity	1	km	2	% (Max)	36	h	3	h	Reasonable

AATSR	Sea surface bulk temperature	1	km	0.4	36	h	3	h	Firm

AATSR	Vegetation type	1000	m	10	classes	30	d	0.125	d	Reasonable

AIRS	Atmospheric temperature profile	Lower troposphere (LT)	25	km	1	km	1	K	12	h	3	h	Firm

AIRS	Atmospheric temperature profile	Lower stratosphere (LS)	25	km	2	km	1	K	12	h	3	h	Firm

AIRS	Atmospheric temperature profile	Higher troposphere (HT)	25	km	1	km	1	K	12	h	3	h	Firm

AIRS	Cloud cover	25	km	10	% (Max)	12	h	3	h	Reasonable

AIRS	Cloud optical thickness	25	km	20	%	12	h	3	h	Speculative

AIRS	Cloud top height	25	km	0.5	km	12	h	3	h	Speculative

AIRS	Cloud top temperature	25	km	2	K	12	h	3	h	Speculative

AIRS	Land surface temperature	25	km	0.5	K	12	h	3	h	Speculative

AIRS	Outgoing long-wave radiation at 	25	km	5	m/s	12	h	3	h	Firm

AIRS	Outgoing short-wave radiation at 	25	km	5	W/m2	12	h	3	h	Firm

AIRS	Ozone profile	Total column	25	km	20	DU	12	h	3	h	Speculative

AIRS	Ozone profile	Higher troposphere (HT)	25	km	5	km	15	%	12	h	3	h	Tentative

AIRS	Sea surface bulk temperature	25	km	0.3	12	h	3	h	Firm

AIRS	Specific humidity profile	Total column	25	km	2	kg/m2	12	h	3	h	Reasonable

AIRS	Specific humidity profile	Higher troposphere (HT)	25	km	1	km	10	%	12	h	3	h	Firm

AIRS	Specific humidity profile	Lower troposphere (LT)	25	km	1	km	10	%	12	h	3	h	Firm

ALADIN	Aerosol profile	Lower troposphere (LT)	200	km	0.5	km	%	2	h	3	h	Tentative

ALADIN	Aerosol profile	Lower stratosphere (LS)	200	km	2	km	%	2	h	3	h	Tentative

ALADIN	Aerosol profile	Higher troposphere (HT)	200	km	1	km	%	2	h	3	h	Tentative

AMI/SAR/Image	Iceberg fractional cover	30	km	% (Max)	0.5	d	0.1	d	Speculative

AMI/SAR/Image	Iceberg height	30	km	m	0.5	d	0.1	d	Speculative

AMI/SAR/Image	Land cover	30	m	10	classes	0.01	y	1	d	Speculative

AMI/SAR/Image	Land surface imagery	30	m	3	d	0.1	d	Speculative

AMI/SAR/Image	Land surface topography	30	m	3	m (vert.)	0.5	y	1	d	Speculative

AMI/SAR/Image	Sea-ice cover	0.1	km	30	% (Max)	0.5	d	2.4	d	Speculative

AMI/SAR/Image	Soil moisture	0.1	km	g/kg	30	d	2.4	d	Speculative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

AMI/SAR/Image	Vegetation type	30	m	15	classes	30	d	1	d	Speculative

AMI/SAR/wave	Dominant wave direction	5	km	degrees	48	h	2	h	Speculative

AMI/SAR/wave	Dominant wave period	5	km	s	48	h	2	h	Speculative

AMI/SAR/wave	Ocean surface currents (vector)	0.1	km	cm/s	2	d	2.4	d	Speculative

AMI/scatterometer	Sea-ice cover	50	km	50	% (Max)	3	d	2.4	d	Speculative

AMI/scatterometer	Soil moisture	50	km	g/kg	3	d	2.4	d	Speculative

AMI/scatterometer	Wind vector over sea surface 	25	km	2	m/s	72	h	3	h	Speculative

(horizontal)

AMSR	Sea surface bulk temperature	25	km	1	12	h	24	h	Reasonable

AMSR	Sea-ice cover	10	km	30	% (Max)	0.5	d	0.25	d	Reasonable

AMSR	Snow cover	10	km	10	% (Max)	12	h	24	h	Tentative

AMSR	Snow water equivalent	10	km	5	mm	12	h	6	h	Speculative

AMSR	Soil moisture	60	km	g/kg	0.5	d	1	d	Speculative

AMSR	Specific humidity profile	Total column	10	km	1.5	kg/m2	12	h	3	h	Reasonable

AMSU-A	Atmospheric temperature profile	Lower stratosphere (LS)	50	km	2	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-A	Atmospheric temperature profile	Higher stratosphere & 	50	km	2	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

mesosphere (HS & M)	reception

AMSU-A	Atmospheric temperature profile	Lower troposphere (LT)	50	km	1	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-A	Atmospheric temperature profile	Higher troposphere (HT)	50	km	1	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-A	Cloud water profile (< 100 µm)	Total column	50	km	300	kg/m2	12	h	2	h	Delay is quicker for local 	Tentative

reception

AMSU-A	Land surface temperature	50	km	3	K	12	h	2	h	Delay is quicker for local 	Speculative

reception

AMSU-A	Precipitation rate (liquid) at the 	50	km	5	m/s	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-A	Precipitation rate (solid) at the 	50	km	5	mm/h	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-A	Sea-ice cover	50	km	30	% (Max)	0.5	d	0.08	d	Delay is quicker for local 	Reasonable

reception

AMSU-A	Snow cover	50	km	50	% (Max)	12	h	6	h	Delay is quicker for local 	Reasonable

reception

AMSU-B	Cloud water profile (< 100 µm)	Total column	15	km	200	kg/m2	12	h	2	h	Delay is quicker for local 	Tentative

reception

AMSU-B	Precipitation rate (liquid) at the 	15	km	5	m/s	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-B	Precipitation rate (solid) at the 	15	km	5	mm/h	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-B	Sea-ice cover	15	km	30	% (Max)	0.5	d	0.08	d	Delay is quicker for local 	Reasonable

reception

AMSU-B	Snow cover	15	km	50	% (Max)	12	h	6	h	Delay is quicker for local 	Reasonable

reception

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

AMSU-B	Specific humidity profile	Total column	15	km	1	kg/m2	12	h	2	h	Delay is quicker for local 	Reasonable

reception

AMSU-B	Specific humidity profile	Lower troposphere (LT)	15	km	1	km	15	%	12	h	2	h	Delay is quicker for local 	Firm

reception

AMSU-B	Specific humidity profile	Higher troposphere (HT)	15	km	1	km	15	%	12	h	2	h	Delay is quicker for local 	Firm

reception

ASAR	Land cover	1000	m	5	classes	0.01	y	2	d	Speculative

ASAR	Land surface imagery	1000	m	2	d	1	d	Speculative

ASAR	Soil moisture	1	km	g/kg	2	d	2	d	Speculative

ASAR (image mode)	Iceberg fractional cover	30	km	% (Max)	2	d	0.1	d	Speculative

ASAR (image mode)	Iceberg height	30	km	m	2	d	0.1	d	Speculative

ASAR (image mode)	Land cover	30	m	10	classes	0.01	y	1	d	Speculative

ASAR (image mode)	Land surface imagery	30	m	2	d	0.1	d	Speculative

ASAR (image mode)	Land surface topography	30	m	3	m (vert.)	0.5	y	1	d	Speculative

ASAR (image mode)	Sea-ice cover	0.1	km	30	% (Max)	0.5	d	2.4	d	Speculative

ASAR (image mode)	Soil moisture	0.1	km	g/kg	2	d	2.4	d	Speculative

ASAR (image mode)	Vegetation type	30	m	15	classes	30	d	1	d	Speculative

ASAR (wave mode)	Dominant wave direction	5	km	degrees	48	h	2	h	Firm

ASAR (wave mode)	Dominant wave period	5	km	s	48	h	2	h	Firm

ASAR (wave mode)	Ocean surface currents (vector)	0.1	km	cm/s	2	d	2.4	d	Speculative

ASCAT	Sea-ice cover	50	km	50	% (Max)	1.5	d	0.75	d	Tentative

ASCAT	Soil moisture	50	km	0.1	g/kg	1.5	d	0.75	d	Speculative

ASCAT	Wind vector over sea surface 	50	km	2	m/s	18	h	0.75	h	Reasonable

(horizontal)

ASTER	Fractional Photosynthetically Active	0.015	km	25	% (Max)	16	d	1	d	Speculative

Radiation (FPAR)

ASTER	Land cover	15	m	20	classes	0.04	y	1	d	Reasonable

ASTER	Land surface imagery	15	m	16	d	d	Speculative

ASTER	Land surface temperature	0.09	km	1	K	400	h	24	h	Tentative

ASTER	Land surface topography	15	m	7	m (vert.)	0.5	y	24	d	Speculative

ASTER	Leaf Area Index (LAI)	0.015	km	20	% (Max)	16	d	1	d	Tentative

ASTER	Normalized Differential Vegetation 	0.015	km	5	% (Max)	16	d	1	d	Tentative

Index (NDVI)

ATLID	Cloud optical thickness	km	10	%	24	h	144	h	Tentative

ATMS	Atmospheric temperature profile	Lower stratosphere (LS)	50	km	2	km	2	K	12	h	2	h	Tentative

ATMS	Atmospheric temperature profile	Lower troposphere (LT)	50	km	1	km	2	K	12	h	2	h	Tentative

ATMS	Atmospheric temperature profile	Higher troposphere (HT)	50	km	1	km	2	K	12	h	2	h	Tentative

ATMS	Atmospheric temperature profile	Higher stratosphere & 	50	km	2	km	2	K	12	h	2	h	Tentative

mesosphere (HS & M)

ATMS	Cloud water profile (< 100 µm)	Total column	15	km	200	kg/m2	12	h	2	h	Tentative

ATMS	Land surface temperature	50	km	3	K	12	h	2	h	Speculative

ATMS	Precipitation rate (liquid) at the 	15	km	5	m/s	12	h	2	h	Tentative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

ATMS	Precipitation rate (solid) at the 	15	km	5	mm/h	12	h	2	h	Tentative

ATMS	Sea-ice cover	15	km	30	% (Max)	0.5	d	0.08	d	Tentative

ATMS	Snow cover	15	km	50	% (Max)	12	h	2	h	Tentative

ATMS	Specific humidity profile	Lower troposphere (LT)	15	km	1	km	15	%	12	h	2	h	Tentative

ATMS	Specific humidity profile	Total column	15	km	1	kg/m2	12	h	2	h	Tentative

ATMS	Specific humidity profile	Higher troposphere (HT)	15	km	1	km	15	%	12	h	2	h	Tentative

ATOVS (HIRS/3 + 	Atmospheric temperature profile	Lower troposphere (LT)	40	km	1	km	2	K	12	h	2	h	Firm

AMSU + AVHRR/3)

ATOVS (HIRS/3 + 	Atmospheric temperature profile	Higher troposphere (HT)	40	km	1	km	2	K	12	h	2	h	Firm

AMSU + AVHRR/3)

ATOVS (HIRS/3 + 	Atmospheric temperature profile	Lower stratosphere (LS)	40	km	2	km	1.5	K	12	h	2	h	Firm

AMSU + AVHRR/3)

ATOVS (HIRS/3 + 	Specific humidity profile	Total column	15	km	1	kg/m2	12	h	2	h	Reasonable

AMSU + AVHRR/3)

ATSR	Cloud cover	15	km	10	% (Max)	36	h	3	h	Speculative

ATSR	Cloud imagery	1	km	36	h	3	h	Speculative

ATSR	Cloud type	15	km	5	classes	36	h	3	h	Speculative

ATSR	Long-wave Earth surface emissivity	1	km	2	% (Max)	36	h	3	h	Speculative

ATSR	Sea surface bulk temperature	1	km	0.4	36	h	3	h	Firm

ATSR-2	Cloud imagery	1	km	36	h	3	h	Reasonable

ATSR-2	Cloud type	15	km	5	classes	36	h	3	h	Speculative

ATSR-2	Fire area	0.1	m2	20	% (Max)	1.5	d	0.125	d	Speculative

ATSR-2	Fire temperature	0.1	K	200	K	1.5	d	0.125	d	Speculative

ATSR-2	Land cover	1000	m	10	classes	0.01	y	1	d	Speculative

ATSR-2	Leaf Area Index (LAI)	1	km	30	% (Max)	30	d	1	d	Tentative

ATSR-2	Sea surface bulk temperature	1	km	0.4	36	h	3	h	Firm

AVHRR/2	Aerosol profile	Total column	1	km	10	%	12	h	2	h	Tentative

AVHRR/2	Cloud cover	5	km	10	% (Max)	12	h	2	h	Reasonable

AVHRR/2	Cloud imagery	4	km	12	h	2	h	Firm

AVHRR/2	Cloud top height	4	km	1.5	km	12	h	2	h	Reasonable

AVHRR/2	Cloud top temperature	4	km	2	K	12	h	2	h	Reasonable

AVHRR/2	Cloud type	15	km	5	classes	12	h	2	h	Reasonable

AVHRR/2	Fire area	1	m2	20	% (Max)	0.5	d	0.125	d	Firm

AVHRR/2	Fire temperature	1	K	200	K	0.5	d	0.125	d	Firm

AVHRR/2	Fractional Photosynthetically Active	1	km	25	% (Max)	7	d	1	d	Speculative

Radiation (FPAR)

AVHRR/2	Land surface temperature	1	km	1	K	12	h	2	h	Reasonable

AVHRR/2	Normalized Differential Vegetation 	1	km	10	% (Max)	0.5	d	1	d	Tentative

Index (NDVI)

AVHRR/2	Sea surface bulk temperature	4	km	0.5	12	h	2	h	Firm

AVHRR/3	Aerosol profile	Total column	1	km	10	%	12	h	2	h	Tentative

AVHRR/3	Cloud cover	5	km	10	% (Max)	12	h	2	h	Reasonable

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

AVHRR/3	Cloud imagery	4	km	12	h	2	h	Reasonable

AVHRR/3	Cloud optical thickness	4	km	20	%	12	h	2	h	Reasonable

AVHRR/3	Cloud top height	10	km	1.5	km	12	h	2	h	Tentative

AVHRR/3	Cloud type	15	km	5	classes	12	h	2	h	Reasonable

AVHRR/3	Fire area	1	m2	20	% (Max)	0.5	d	0.125	d	Firm

AVHRR/3	Fire temperature	1	K	200	K	0.5	d	0.125	d	Firm

AVHRR/3	Fractional Photosynthetically Active	1	km	25	% (Max)	1	d	1	d	Speculative

Radiation (FPAR)

AVHRR/3	Land cover	1000	m	10	classes	0.01	y	1	d	Tentative

AVHRR/3	Leaf Area Index (LAI)	1	km	25	% (Max)	1	d	1	d	Tentative

AVHRR/3	Normalized Differential Vegetation 	1	km	10	% (Max)	0.5	d	1	d	Tentative

Index (NDVI)

AVHRR/3	Sea surface bulk temperature	4	km	0.5	12	h	2	h	Firm

AVHRR/4	Aerosol profile	Total column	1	km	10	%	12	h	2	h	Tentative

AVHRR/4	Cloud cover	5	km	8	% (Max)	12	h	2	h	Reasonable

AVHRR/4	Cloud imagery	4	km	12	h	2	h	Reasonable

AVHRR/4	Cloud optical thickness	4	km	20	%	12	h	2	h	Reasonable

AVHRR/4	Cloud top height	10	km	1.5	km	12	h	2	h	Tentative

AVHRR/4	Cloud type	15	km	5	classes	12	h	2	h	Reasonable

AVHRR/4	Fire area	1	m2	20	% (Max)	0.5	d	0.125	d	Firm

AVHRR/4	Fire temperature	1	K	200	K	0.5	d	0.125	d	Firm

AVHRR/4	Fractional Photosynthetically Active	1	km	25	% (Max)	1	d	1	d	Speculative

Radiation (FPAR)

AVHRR/4	Land cover	1000	m	10	classes	0.01	y	1	d	Tentative

AVHRR/4	Leaf Area Index (LAI)	1	km	25	% (Max)	1	d	1	d	Tentative

AVHRR/4	Normalized Differential Vegetation 	1	km	10	% (Max)	0.5	d	1	d	Tentative

Index (NDVI)

AVHRR/4	Sea surface bulk temperature	4	km	0.5	12	h	2	h	Firm

AVNIR	Land surface imagery	8	m	41	d	d	Firm

AVNIR-2	Land cover	10	m	25	classes	0.04	y	d	Speculative

AVNIR-2	Land surface topography	2.5	m	m (vert.)	0.04	y	d	Speculative

AVNIR-2	Vegetation type	2.5	m	35	classes	41	d	1	d	Speculative

BTVK	Cloud imagery	1.5	km	1	h	0.5	h	Reasonable

BUFS-2	Ozone profile	Lower troposphere (LT)	50	km	5	km	10	%	12	h	24	h	Speculative

BUFS-2	Ozone profile	Lower stratosphere (LS)	270	km	5	km	10	%	12	h	24	h	Speculative

CCD	Land surface imagery	19.5	m	26	d	d	Speculative

CrIS	Atmospheric temperature profile	Lower troposphere (LT)	25	km	1	km	1	K	12	h	2	h	Firm

CrIS	Atmospheric temperature profile	Higher troposphere (HT)	25	km	1	km	1	K	12	h	2	h	Firm

CrIS	Atmospheric temperature profile	Lower stratosphere (LS)	25	km	2	km	1	K	12	h	2	h	Firm

CrIS	Cloud cover	25	km	10	% (Max)	12	h	3	h	Reasonable

CrIS	Cloud optical thickness	25	km	20	%	12	h	3	h	Speculative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

CrIS	Cloud top height	25	km	0.5	km	12	h	2	h	Tentative

CrIS	Cloud top temperature	25	km	2	K	12	h	3	h	Speculative

CrIS	Land surface temperature	25	km	0.5	K	12	h	3	h	Speculative

CrIS	Outgoing long-wave radiation at 	25	km	5	m/s	12	h	3	h	Firm

CrIS	Outgoing short-wave radiation at 	25	km	5	W/m2	12	h	3	h	Firm

CrIS	Ozone profile	Total column	25	km	20	DU	12	h	3	h	Speculative

CrIS	Ozone profile	Higher troposphere (HT)	25	km	5	km	15	%	12	h	3	h	Tentative

CrIS	Sea surface bulk temperature	25	km	0.3	12	h	3	h	Firm

CrIS	Specific humidity profile	Total column	25	km	2	kg/m2	12	h	2	h	Reasonable

CrIS	Specific humidity profile	Higher troposphere (HT)	25	km	1	km	10	%	12	h	2	h	Firm

CrIS	Specific humidity profile	Lower troposphere (LT)	25	km	1	km	10	%	12	h	2	h	Firm

ETM+	Fractional Photosynthetically Active	0.03	km	15	% (Max)	1	d	1	d	Speculative

Radiation (FPAR)

ETM+	Land cover	30	m	20	classes	0.04	y	2	d	Reasonable

ETM+	Land surface imagery	30	m	16	d	1	d	Tentative

ETM+	Leaf Area Index (LAI)	0.03	km	20	% (Max)	16	d	1	d	Reasonable

ETM+	Normalized Differential Vegetation 	0.03	km	5	% (Max)	1	d	1	d	Tentative

Index (NDVI)

ETM+	Vegetation type	30	m	20	classes	16	d	2	d	Reasonable

GIFTS	Atmospheric temperature profile	Lower stratosphere (LS)	25	km	2	km	1	K	12	h	2	h	Firm

GIFTS	Atmospheric temperature profile	Higher troposphere (HT)	25	km	1	km	1	K	12	h	2	h	Firm

GIFTS	Atmospheric temperature profile	Lower troposphere (LT)	25	km	1	km	1	K	12	h	2	h	Firm

GIFTS	Cloud cover	25	km	10	% (Max)	12	h	3	h	Reasonable

GIFTS	Cloud optical thickness	25	km	20	%	12	h	3	h	Speculative

GIFTS	Cloud top height	25	km	0.5	km	12	h	2	h	Tentative

GIFTS	Cloud top temperature	25	km	2	K	12	h	3	h	Speculative

GIFTS	Land surface temperature	25	km	0.5	K	12	h	3	h	Speculative

GIFTS	Outgoing long-wave radiation at 	25	km	5	m/s	12	h	3	h	Firm

GIFTS	Outgoing short-wave radiation at 	25	km	5	W/m2	12	h	3	h	Firm

GIFTS	Ozone profile	Higher troposphere (HT)	25	km	5	km	15	%	12	h	3	h	Tentative

GIFTS	Ozone profile	Total column	25	km	20	DU	12	h	3	h	Speculative

GIFTS	Sea surface bulk temperature	25	km	0.3	12	h	3	h	Firm

GIFTS	Specific humidity profile	Lower troposphere (LT)	25	km	1	km	10	%	12	h	2	h	Firm

GIFTS	Specific humidity profile	Higher troposphere (HT)	25	km	1	km	10	%	12	h	2	h	Firm

GIFTS	Specific humidity profile	Total column	25	km	2	kg/m2	12	h	2	h	Reasonable

GIFTS	Wind profile (horizontal component)	Higher troposphere (HT)	40	km	2	km	3	m/s	1	d	1	h	Speculative

GIFTS	Wind profile (horizontal component)	Lower troposphere (LT)	40	km	2	km	1	m/s	1	h	1	h	Reasonable

GLI	Cloud imagery	0.25	km	12	h	720	h	Reasonable

GLI	Cloud optical thickness	0.25	km	1	%	12	h	720	h	Firm

GLI	Iceberg fractional cover	0.25	km	% (Max)	0.5	d	30	d	Tentative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

GLI	Iceberg height	0.25	km	m	0.5	d	30	d	Tentative

GLI	Land cover	250	m	15	classes	0.01	y	3	d	Reasonable

GLI	Sea-ice cover	0.25	km	50	% (Max)	0.5	d	30	d	Reasonable

GLI	Snow cover	1	km	10	% (Max)	12	h	24	h	Tentative

GLI	Specific humidity profile	Total column	0.25	km	5	kg/m2	12	h	720	h	Reasonable

GLI	Vegetation type	250	m	10	classes	3	d	1	d	Tentative

GOME	Ozone profile	Lower stratosphere (LS)	960	km	5	km	10	%	3	h	14	h	Reasonable

GOME-2	Ozone profile	Lower stratosphere (LS)	960	km	5	km	10	%	3	h	2	h	Reasonable

GOMOS	Ozone profile	Lower stratosphere (LS)	300	km	1	km	%	36	h	3	h	Speculative

GRAS	Atmospheric temperature profile	Higher troposphere (HT)	1000	km	1	km	1	K	12	h	2	h	Reasonable

GRAS	Atmospheric temperature profile	Lower stratosphere (LS)	1000	km	1	km	1	K	12	h	2	h	Reasonable

GRAS	Atmospheric temperature profile	Higher stratosphere & 	1000	km	1	km	1	K	12	h	2	h	Reasonable

mesosphere (HS & M)

GRAS	Specific humidity profile	Lower troposphere (LT)	1000	km	1	km	10	%	12	h	2	h	Reasonable

HALOE	Ozone profile	Lower stratosphere (LS)	km	3	km	10	%	576	h	24	h	Speculative

HIRS/2	Atmospheric temperature profile	Lower stratosphere (LS)	80	km	2	km	2	K	12	h	2	h	Firm

HIRS/2	Atmospheric temperature profile	Higher troposphere (HT)	80	km	1	km	2.5	K	12	h	2	h	Firm

HIRS/2	Atmospheric temperature profile	Lower troposphere (LT)	80	km	1	km	2.5	K	12	h	2	h	Firm

HIRS/2	Cloud cover	80	km	20	% (Max)	12	h	2	h	Reasonable

HIRS/2	Cloud optical thickness	80	km	20	%	12	h	2	h	Speculative

HIRS/2	Cloud top height	80	km	0.7	km	12	h	2	h	Tentative

HIRS/2	Ozone profile	Total column	80	km	30	DU	12	h	2	h	Speculative

HIRS/2	Specific humidity profile	Total column	80	km	2	kg/m2	12	h	2	h	Reasonable

HIRS/2	Specific humidity profile	Lower troposphere (LT)	80	km	1	km	20	%	12	h	2	h	Firm

HIRS/2	Specific humidity profile	Higher troposphere (HT)	80	km	1	km	20	%	12	h	2	h	Firm

HIRS/3	Atmospheric temperature profile	Lower stratosphere (LS)	40	km	2	km	2	K	12	h	2	h	Firm

HIRS/3	Atmospheric temperature profile	Lower troposphere (LT)	40	km	1	km	2.5	K	12	h	2	h	Firm

HIRS/3	Atmospheric temperature profile	Higher troposphere (HT)	40	km	1	km	2.5	K	12	h	2	h	Firm

HIRS/3	Cloud cover	40	km	20	% (Max)	12	h	2	h	Reasonable

HIRS/3	Cloud optical thickness	40	km	20	%	12	h	2	h	Speculative

HIRS/3	Cloud top height	40	km	0.7	km	12	h	2	h	Reasonable

HIRS/3	Cloud top temperature	40	km	2	K	12	h	2	h	Reasonable

HIRS/3	Land surface temperature	40	km	2	K	12	h	2	h	Reasonable

HIRS/3	Outgoing long-wave radiation at 	40	km	10	m/s	12	h	2	h	Firm

HIRS/3	Outgoing short-wave radiation at 	40	km	10	W/m2	12	h	2	h	Firm

HIRS/3	Ozone profile	Total column	40	km	30	DU	12	h	2	h	Speculative

HIRS/3	Sea surface bulk temperature	40	km	0.5	12	h	2	h	Firm

HIRS/3	Specific humidity profile	Higher troposphere (HT)	40	km	1	km	20	%	12	h	2	h	Firm

HIRS/3	Specific humidity profile	Lower troposphere (LT)	40	km	1	km	20	%	12	h	2	h	Firm

HIRS/3	Specific humidity profile	Total column	40	km	2	kg/m2	12	h	2	h	Reasonable

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

HIRS/4	Atmospheric temperature profile	Lower troposphere (LT)	40	km	1	km	2.5	K	12	h	2	h	Firm

HIRS/4	Atmospheric temperature profile	Lower stratosphere (LS)	40	km	2	km	2	K	12	h	2	h	Firm

HIRS/4	Atmospheric temperature profile	Higher troposphere (HT)	40	km	1	km	2.5	K	12	h	2	h	Firm

HIRS/4	Cloud cover	40	km	20	% (Max)	12	h	2	h	Reasonable

HIRS/4	Cloud optical thickness	40	km	20	%	12	h	2	h	Speculative

HIRS/4	Cloud top height	40	km	0.7	km	12	h	2	h	Reasonable

HIRS/4	Cloud top temperature	40	km	2	K	12	h	2	h	Reasonable

HIRS/4	Land surface temperature	40	km	2	K	12	h	2	h	Reasonable

HIRS/4	Outgoing long-wave radiation at 	40	km	10	m/s	12	h	2	h	Firm

HIRS/4	Outgoing short-wave radiation at 	40	km	10	W/m2	12	h	2	h	Firm

HIRS/4	Ozone profile	Total column	40	km	30	DU	12	h	2	h	Speculative

HIRS/4	Sea surface bulk temperature	40	km	0.5	12	h	2	h	Firm

HIRS/4	Specific humidity profile	Total column	40	km	2	kg/m2	12	h	2	h	Reasonable

HIRS/4	Specific humidity profile	Lower troposphere (LT)	40	km	1	km	20	%	12	h	2	h	Firm

HIRS/4	Specific humidity profile	Higher troposphere (HT)	40	km	1	km	20	%	12	h	2	h	Firm

HRG	Land cover	10	m	20	classes	0.04	y	3	d	Tentative

HRG	Land surface imagery	5	m	26	d	30	d	Speculative

HRG	Land surface topography	5	m	8	m (vert.)	0.5	y	12	d	Speculative

HRG	Vegetation type	10	m	25	classes	26	d	10	d	Tentative

HRV	Fire area	10	m2	20	% (Max)	5	d	3	d	Speculative

HRV	Fire temperature	10	K	200	K	5	d	3	d	Speculative

HRV	Land cover	20	m	20	classes	0.07	y	3	d	Tentative

HRV	Land surface imagery	10	m	26	d	30	d	Tentative

HRV	Land surface topography	10	m	15	m (vert.)	0.5	y	12	d	Speculative

HRV	Normalized Differential Vegetation 	0.01	km	5	% (Max)	26	d	1	d	Tentative

Index (NDVI)

HRV	Vegetation type	20	m	20	classes	26	d	10	d	Tentative

HRVIR	Land cover	20	m	20	classes	0.04	y	3	d	Tentative

HRVIR	Land surface imagery	10	m	26	d	30	d	Tentative

HRVIR	Land surface topography	10	m	15	m (vert.)	0.5	y	12	d	Speculative

HRVIR	Vegetation type	20	m	20	classes	26	d	10	d	Tentative

IASI	Atmospheric temperature profile	Higher troposphere (HT)	25	km	1	km	1	K	12	h	2	h	Firm

IASI	Atmospheric temperature profile	Lower stratosphere (LS)	25	km	2	km	1	K	12	h	2	h	Firm

IASI	Atmospheric temperature profile	Lower troposphere (LT)	25	km	1	km	1	K	12	h	2	h	Firm

IASI	Cloud cover	25	km	10	% (Max)	12	h	2	h	Reasonable

IASI	Cloud optical thickness	25	km	20	%	12	h	2	h	Speculative

IASI	Cloud top height	25	km	0.5	km	12	h	2	h	Speculative

IASI	Cloud top temperature	25	km	2	K	12	h	2	h	Speculative

IASI	Land surface temperature	25	km	0.5	K	12	h	2	h	Speculative

IASI	Long-wave Earth surface emissivity	25	km	1	% (Max)	12	h	2	h	Tentative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

IASI	Outgoing long-wave radiation at 	25	km	5	m/s	12	h	2	h	Firm

IASI	Outgoing short-wave radiation at 	25	km	5	W/m2	12	h	2	h	Firm

IASI	Ozone profile	Higher troposphere (HT)	25	km	5	km	15	%	12	h	2	h	Tentative

IASI	Ozone profile	Lower stratosphere (LS)	25	km	5	km	10	%	12	h	2	h	Tentative

IASI	Ozone profile	Total column	25	km	20	DU	12	h	2	h	Speculative

IASI	Sea surface bulk temperature	25	km	0.3	12	h	2	h	Firm

IASI	Specific humidity profile	Total column	25	km	2	kg/m2	12	h	2	h	Reasonable

IASI	Specific humidity profile	Lower troposphere (LT)	25	km	1	km	10	%	12	h	2	h	Firm

IASI	Specific humidity profile	Higher troposphere (HT)	25	km	1	km	10	%	12	h	2	h	Firm

ILAS	Aerosol profile	Higher troposphere (HT)	km	2	km	%	h	720	h	Reasonable

ILAS-II	Aerosol profile	Higher troposphere (HT)	km	1	km	%	h	720	h	Tentative

Imager	Cloud cover	4	km	10	% (Max)	0.5	h	0.5	h	Firm

Imager	Cloud imagery	4	km	0.5	h	0.1	h	Firm

Imager	Cloud top height	50	km	1	km	1	h	1	h	Firm

Imager	Cloud top temperature	50	km	2	K	1	h	0.5	h	Firm

Imager	Fire area	4	m2	10	% (Max)	0.08	d	1	d	Speculative

Imager	Fire temperature	4	K	50	K	0.08	d	1	d	Speculative

Imager	Land surface temperature	4	km	2	K	1	h	0.5	h	Reasonable

Imager	Precipitation rate (liquid) at the 	10	km	30	m/s	1	h	0.5	h	Firm

Imager	Precipitation rate (solid) at the 	4	km	30	mm/h	0.5	h	0.5	h	Firm

Imager	Sea surface bulk temperature	4	km	0.5	1	h	0.5	h	Firm

Imager	Specific humidity profile	Lower troposphere (LT)	50	km	2	km	20	%	1	h	0.5	h	Firm

Imager	Specific humidity profile	Higher troposphere (HT)	50	km	3	km	20	%	1	h	1	h	Firm

Imager	Wind profile (horizontal component)	Lower troposphere (LT)	150	km	5	km	3	m/s	1	h	1	h	Firm

Imager	Wind profile (horizontal component)	Higher troposphere (HT)	150	km	5	km	5	m/s	1	d	1	h	Firm

IMAGER/MTSAT-2	Wind profile (horizontal component)	Higher troposphere (HT)	150	km	5	km	5	m/s	1	d	1	h	Reasonable

IMAGER/MTSAT-2	Wind profile (horizontal component)	Lower troposphere (LT)	150	km	5	km	3	m/s	1	h	1	h	Reasonable

IMG	Atmospheric temperature profile	Higher troposphere (HT)	100	km	1	km	1	K	984	h	336	h	Firm

IMG	Atmospheric temperature profile	Lower stratosphere (LS)	100	km	2	km	1	K	984	h	336	h	Firm

IMG	Atmospheric temperature profile	Lower troposphere (LT)	100	km	1	km	1	K	984	h	336	h	Tentative

IMG	Ozone profile	Lower stratosphere (LS)	80	km	km	16	%	984	h	288	h	Tentative

IMG	Specific humidity profile	Lower stratosphere (LS)	100	km	1	km	%	984	h	336	h	Speculative

IMG	Trace gas profile CH4	Lower troposphere (LT)	80	km	5	km	20	%	984	h	288	h	Tentative

IMG	Trace gas profile CH4	Lower stratosphere (LS)	80	km	12	km	20	%	984	h	288	h	Tentative

IMG	Trace gas profile CH4	Higher troposphere (HT)	80	km	8	km	20	%	984	h	288	h	Tentative

IMG	Trace gas profile CO	Lower stratosphere (LS)	80	km	12	km	20	%	984	h	288	h	Tentative

IMG	Trace gas profile CO	Lower troposphere (LT)	80	km	5	km	20	%	984	h	288	h	Tentative

IMG	Trace gas profile CO	Higher troposphere (HT)	80	km	8	km	20	%	984	h	288	h	Tentative

IMG	Trace gas profile CO2	Total column	80	km	2	%	984	h	288	h	Tentative

Klimat	Cloud cover	2.5	km	20	% (Max)	12	h	6	h	Reasonable

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

LISS-I	Land surface imagery	72.5	m	22	d	d	Speculative

LISS-II	Land surface imagery	37	m	27	d	d	Speculative

LISS-III	Land surface imagery	23.5	m	24	d	d	Speculative

MERIS	Cloud top height	0.3	km	0.2	km	12	h	3	h	Tentative

MERIS	Cloud type	0.3	km	8	classes	12	h	3	h	Firm

MERIS	Land cover	300	m	15	classes	0.01	y	1	d	Reasonable

MERIS	Land surface imagery	250	m	30	d	0.125	d	Speculative

MERIS	Leaf Area Index (LAI)	0.3	km	20	% (Max)	7	d	1	d	Reasonable

MERIS	Snow cover	300	km	10	% (Max)	12	h	24	h	Tentative

MERIS	Specific humidity profile	Total column	0.3	km	5	kg/m2	12	h	3	h	Speculative

MERIS	Vegetation type	300	m	10	classes	0.5	d	1	d	Tentative

MESSR	Land surface imagery	50	m	17	d	d	Speculative

MHS	Cloud water profile (< 100 µm)	Total column	15	km	200	kg/m2	12	h	2	h	Tentative

MHS	Precipitation rate (liquid) at the 	15	km	5	m/s	12	h	0.5	h	Firm

MHS	Precipitation rate (solid) at the 	15	km	5	mm/h	12	h	0.5	h	Firm

MHS	Sea-ice cover	15	km	30	% (Max)	0.5	d	0.08	d	Tentative

MHS	Specific humidity profile	Total column	15	km	1	kg/m2	12	h	2	h	Reasonable

MHS	Specific humidity profile	Higher troposphere (HT)	15	km	1	km	15	%	12	h	2	h	Firm

MHS	Specific humidity profile	Lower troposphere (LT)	15	km	1	km	15	%	12	h	2	h	Firm

MIPAS	Ozone profile	Lower stratosphere (LS)	300	km	3	km	%	36	h	3	h	Speculative

MIPAS	Specific humidity profile	Lower stratosphere (LS)	300	km	3	km	%	36	h	3	h	Speculative

MISR	Leaf Area Index (LAI)	1	km	25	% (Max)	30	d	1	d	Tentative

MIVZA	Precipitation rate (liquid) at the 	80	km	5	m/s	12	h	24	h	Firm

MIVZA	Sea-ice cover	80	km	30	% (Max)	0.5	d	1	d	Speculative

MIVZA	Snow cover	60	km	20	% (Max)	12	h	24	h	Speculative

MIVZA	Specific humidity profile	Total column	60	km	2.5	kg/m2	12	h	24	h	Speculative

MODIS	Aerosol profile	Total column	5	km	%	12	h	24	h	Tentative

MODIS	Atmospheric temperature profile	Lower troposphere (LT)	5	km	1	km	2.5	K	12	h	24	h	Firm

MODIS	Atmospheric temperature profile	Higher troposphere (HT)	5	km	1	km	2.5	K	12	h	24	h	Firm

MODIS	Cloud cover	5	km	5	% (Max)	12	h	24	h	Reasonable

MODIS	Cloud imagery	0.25	km	12	h	24	h	Speculative

MODIS	Cloud optical thickness	5	km	20	%	12	h	24	h	Firm

MODIS	Cloud top height	5	km	0.7	km	12	h	24	h	Speculative

MODIS	Cloud top temperature	5	km	2	K	12	h	24	h	Speculative

MODIS	Cloud type	1	km	8	classes	12	h	24	h	Speculative

MODIS	Fire area	1	m2	5	% (Max)	0.5	d	1	d	Tentative

MODIS	Fire temperature	1	K	50	K	0.5	d	1	d	Tentative

MODIS	Fractional Photosynthetically Active	0.25	km	15	% (Max)	0.5	d	24	d	Speculative

Radiation (FPAR)

MODIS	Land cover	250	m	15	classes	0.01	y	1	d	Reasonable

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

MODIS	Land surface imagery	250	m	2	d	24	d	Tentative

MODIS	Land surface temperature	1	km	1	K	12	h	24	h	Reasonable

MODIS	Leaf Area Index (LAI)	0.25	km	20	% (Max)	30	d	1	d	Reasonable

MODIS	Normalized Differential Vegetation 	0.25	km	5	% (Max)	0.5	d	1	d	Reasonable

Index (NDVI)

MODIS	Outgoing long-wave radiation at 	5	km	10	m/s	12	h	24	h	Firm

MODIS	Outgoing short-wave radiation at 	5	km	10	W/m2	12	h	24	h	Firm

MODIS	Ozone profile	Total column	5	km	50	DU	12	h	24	h	Firm

MODIS	Sea surface bulk temperature	1	km	0.3	12	h	24	h	Firm

MODIS	Snow cover	0.25	km	5	% (Max)	12	h	24	h	Speculative

MODIS	Specific humidity profile	Total column	5	km	2.5	kg/m2	12	h	24	h	Firm

MODIS	Specific humidity profile	Lower troposphere (LT)	5	km	2	km	20	%	12	h	24	h	Firm

MODIS	Specific humidity profile	Higher troposphere (HT)	5	km	3	km	20	%	12	h	24	h	Firm

MODIS	Vegetation type	250	m	10	classes	1	d	1	d	Firm

MR-2000M1	Cloud imagery	1.4	km	12	h	6	h	Firm

MR-900	Cloud imagery	2	km	12	h	6	h	Firm

MSR	Cloud cover	1	km	10	% (Max)	12	h	6	h	Tentative

MSR	Cloud top height	1	km	1	km	24	h	6	h	Tentative

MSR	Cloud top temperature	1	km	2	K	24	h	6	h	Tentative

MSR	Cloud type	1	km	5	classes	24	h	6	h	Speculative

MSR	Fractional Photosynthetically Active	1	km	25	% (Max)	14	d	14	d	Speculative

Radiation (FPAR)

MSR	Land surface temperature	1	km	2	K	12	h	12	h	Tentative

MSR	Normalized Differential Vegetation 	1	km	10	% (Max)	14	d	14	d	Tentative

Index (NDVI)

MSR	Sea surface bulk temperature	1	km	1	12	h	12	h	Tentative

MSR	Sea-ice cover	1	km	30	% (Max)	0.5	d	0.5	d	Tentative

MSR	Snow cover	1	km	20	% (Max)	12	h	6	h	Tentative

MSU	Atmospheric temperature profile	Higher troposphere (HT)	160	km	1	km	2.5	K	12	h	2	h	Firm

MSU	Atmospheric temperature profile	Lower troposphere (LT)	160	km	1	km	2.5	K	12	h	2	h	Firm

MSU	Atmospheric temperature profile	Lower stratosphere (LS)	160	km	2	km	2	K	12	h	2	h	Firm

MSU	Precipitation rate (liquid) at the 	160	km	m/s	12	h	0.5	h	Firm

MSU	Precipitation rate (solid) at the 	160	km	mm/h	10	h	0.5	h	Firm

MSU-E	Land cover	25	m	10	classes	0.04	y	1	d	Speculative

MSU-E	Land surface imagery	25	m	16	d	0.063	d	Speculative

MSU-E	Leaf Area Index (LAI)	0.025	km	20	% (Max)	14	d	1	d	Reasonable

MSU-E	Vegetation type	25	m	10	classes	7	d	1	d	Speculative

MSU-SK	Iceberg fractional cover	0.2	km	% (Max)	7	d	1	d	Speculative

MSU-SK	Iceberg height	0.2	km	m	7	d	1	d	Speculative

MSU-SK	Land cover	200	m	10	classes	0.04	y	1	d	Reasonable

MSU-SK	Land surface imagery	200	m	14	d	1	d	Tentative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

MSU-V	Fire area	0.27	m2	20	% (Max)	7	d	1	d	Speculative

MSU-V	Fire temperature	0.27	K	200	K	7	d	1	d	Speculative

MSU-V	Land cover	50	m	10	classes	0.04	y	1	d	Speculative

MSU-V	Land surface imagery	50	m	30	d	1	d	Speculative

MVIRI	Cloud cover	20	km	15	% (Max)	0.5	h	2	h	Firm

MVIRI	Cloud imagery	5	km	0.5	h	0.1	h	Firm

MVIRI	Cloud top height	20	km	1.5	km	0.5	h	0.5	h	Firm

MVIRI	Cloud top temperature	5	km	2	K	0.5	h	0.5	h	Firm

MVIRI	Cloud type	150	km	4	classes	1	h	2	h	Reasonable

MVIRI	Outgoing long-wave radiation at 	160	km	30	m/s	0.5	h	12	h	Firm

MVIRI	Outgoing short-wave radiation at 	160	km	50	W/m2	0.5	h	12	h	Firm

MVIRI	Sea surface bulk temperature	15	km	2	0.5	h	2	h	Firm

MVIRI	Specific humidity profile	Higher troposphere (HT)	150	km	3	km	20	%	0.5	h	1	h	Firm

MVIRI	Wind profile (horizontal component)	Lower troposphere (LT)	150	km	5	km	3	m/s	1	h	2	h	Firm

MVIRI	Wind profile (horizontal component)	Higher troposphere (HT)	150	km	5	km	5	m/s	1	d	2	h	Firm

MVISR (10 channels)	Aerosol profile	Total column	1	km	10	%	12	h	12	h	Reasonable

MVISR (10 channels)	Cloud cover	4	km	10	% (Max)	12	h	12	h	Reasonable

MVISR (10 channels)	Cloud imagery	4	km	12	h	12	h	Reasonable

MVISR (10 channels)	Cloud optical thickness	4	km	20	%	12	h	12	h	Reasonable

MVISR (10 channels)	Cloud top height	10	km	1.5	km	12	h	12	h	Reasonable

MVISR (10 channels)	Cloud type	10	km	5	classes	12	h	12	h	Reasonable

MVISR (10 channels)	Fire area	1	m2	5	% (Max)	0.5	d	1	d	Reasonable

MVISR (10 channels)	Fire temperature	1	K	200	K	0.5	d	1	d	Reasonable

MVISR (10 channels)	Fractional Photosynthetically Active	1	km	25	% (Max)	0.5	d	1	d	Reasonable

Radiation (FPAR)

MVISR (10 channels)	Land cover	1000	m	8	classes	0.005	y	1	d	Reasonable

MVISR (10 channels)	Leaf Area Index (LAI)	1	km	25	% (Max)	1	d	1	d	Reasonable

MVISR (10 channels)	Normalized Differential Vegetation 	1	km	10	% (Max)	0.5	d	1	d	Reasonable

Index (NDVI)

MVISR (10 channels)	Sea surface bulk temperature	4	km	1	12	h	12	h	Reasonable

MVZA	Specific humidity profile	Lower troposphere (LT)	20	km	1	km	15	%	12	h	24	h	Speculative

MZOAS	Permafrost	50	km	40	% (Max)	1	d	2	d	Speculative

MZOAS	Precipitation rate (liquid) at the 	160	km	5	m/s	12	h	24	h	Firm

MZOAS	Sea surface bulk temperature	80	km	3	12	h	24	h	Speculative

MZOAS	Sea-ice cover	10	km	30	% (Max)	0.5	d	1	d	Speculative

MZOAS	Soil moisture	50	km	g/kg	15.5	d	1.5	d	Speculative

MZOAS	Wind vector over sea surface 	80	km	2	m/s	12	h	24	h	Speculative

(horizontal)

NSCAT	Sea-ice cover	25	km	50	% (Max)	0.5	d	0.25	d	Firm

NSCAT	Wind vector over sea surface 	25	km	2	m/s	12	h	4	h	Speculative

(horizontal)

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

OCTS	Sea-ice cover	0.25	km	30	% (Max)	0.5	d	0.25	d	Firm

PAN (IRS-1C/1D)	Land surface imagery	10	m	24	d	1	d	Speculative

PR	Precipitation rate (liquid) at the 	5	km	5	m/s	250	h	720	h	Reasonable

RA	Sea level	20	km	10	cm	d	20	d	Firm

RA-2	Sea level	20	km	10	cm	d	20	d	Firm

SAGE II	Aerosol profile	Lower stratosphere (LS)	100	km	1	km	%	24	h	720	h	Speculative

SAGE II	Aerosol profile	Higher troposphere (HT)	100	km	1	km	%	24	h	720	h	Speculative

SAGE II	Specific humidity profile	Lower stratosphere (LS)	100	km	1	km	10	%	48	h	720	h	Firm

SAGE III	Aerosol profile	Higher troposphere (HT)	300	km	1	km	%	336	h	12	h	Speculative

SAGE III	Aerosol profile	Higher stratosphere & 	300	km	1	km	10	%	336	h	12	h	Speculative

mesosphere (HS & M)

SAGE III	Aerosol profile	Lower stratosphere (LS)	300	km	1	km	10	%	336	h	12	h	Speculative

SAGE III	Ozone profile	Lower stratosphere (LS)	300	km	1	km	5	%	336	h	24	h	Speculative

SAGE III	Specific humidity profile	Lower stratosphere (LS)	100	km	0.5	km	10	%	336	h	12	h	Reasonable

SAR (JERS-1)	Land surface imagery	18	m	30	d	1	d	Speculative

SAR (RADARSAT)	Land surface imagery	25	m	30	d	1	d	Speculative

SBUV/2	Ozone profile	Total column	183	km	30	DU	24	h	3	h	Speculative

SBUV/2	Ozone profile	Lower stratosphere (LS)	183	km	5	km	10	%	24	h	3	h	Reasonable

SBUV/3	Ozone profile	Lower stratosphere (LS)	183	km	5	km	10	%	24	h	3	h	Speculative

SBUV/3	Ozone profile	Total column	183	km	30	DU	24	h	3	h	Speculative

SBUV/3	Ozone profile	Lower troposphere (LT)	183	km	5	km	10	%	24	h	3	h	Speculative

ScaRaB	Outgoing long-wave radiation at 	60	km	10	m/s	12	h	24	h	Reasonable

ScaRaB	Outgoing short-wave radiation at 	60	km	5	W/m2	12	h	24	h	Tentative

SCIAMACHY	Ozone profile	Lower stratosphere (LS)	500	km	3	km	%	12	h	3	h	Speculative

SeaWinds	Sea-ice cover	25	km	50	% (Max)	0.5	d	0.25	d	Reasonable

SeaWinds	Wind vector over sea surface 	25	km	2	m/s	12	h	4	h	Speculative

(horizontal)

SEVIRI	Aerosol profile	Total column	3	km	%	0.25	h	0.25	h	Tentative

SEVIRI	Atmospheric stability index	15	km	K	0.25	h	0.25	h	Firm

SEVIRI	Cloud cover	3	km	10	% (Max)	0.25	h	0.5	h	Reasonable

SEVIRI	Cloud imagery	3	km	0.25	h	0.1	h	Reasonable

SEVIRI	Cloud top height	10	km	0.7	km	0.25	h	0.5	h	Reasonable

SEVIRI	Cloud top temperature	3	km	2	K	0.25	h	0.5	h	Reasonable

SEVIRI	Cloud type	100	km	8	classes	0.25	h	1	h	Reasonable

SEVIRI	Fire area	3	m2	5	% (Max)	0.08	d	1	d	Speculative

SEVIRI	Fire temperature	3	K	50	K	0.08	d	1	d	Speculative

SEVIRI	Fractional Photosynthetically Active	3	km	25	% (Max)	1	d	1	d	Speculative

Radiation (FPAR)

SEVIRI	Land surface temperature	10	km	2	K	0.25	h	0.25	h	Reasonable

SEVIRI	Long-wave Earth surface emissivity	3	km	3	% (Max)	0.25	h	24	h	Tentative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

SEVIRI	Normalized Differential Vegetation 	3	km	10	% (Max)	0.08	d	1	d	Tentative

Index (NDVI)

SEVIRI	Outgoing long-wave radiation at 	50	km	10	m/s	0.25	h	24	h	Firm

SEVIRI	Outgoing short-wave radiation at 	50	km	10	W/m2	0.25	h	24	h	Firm

SEVIRI	Ozone profile	Total column	50	km	50	DU	0.25	h	2	h	Firm

SEVIRI	Precipitation rate (liquid) at the 	10	km	30	m/s	0.25	h	0.5	h	Firm

SEVIRI	Precipitation rate (solid) at the 	10	km	30	mm/h	0.25	h	0.5	h	Firm

SEVIRI	Sea surface bulk temperature	3	km	0.5	1	h	2	h	Firm

SEVIRI	Specific humidity profile	Total column	100	km	2	kg/m2	1	h	3	h	Reasonable

SEVIRI	Specific humidity profile	Lower troposphere (LT)	50	km	2	km	20	%	1	h	0.5	h	Firm

SEVIRI	Specific humidity profile	Higher troposphere (HT)	100	km	3	km	20	%	1	h	1	h	Firm

SEVIRI	Wind profile (horizontal component)	Higher troposphere (HT)	100	km	5	km	4	m/s	1	d	1	h	Firm

SEVIRI	Wind profile (horizontal component)	Lower stratosphere (LS)	100	km	10	km	10	m/s	1	h	1	h	Reasonable

SEVIRI	Wind profile (horizontal component)	Lower troposphere (LT)	100	km	5	km	2	m/s	1	h	1	h	Firm

Sounder	Atmospheric stability index	10	km	K	1	h	0.5	h	Firm

Sounder	Atmospheric temperature profile	Lower troposphere (LT)	30	km	1	km	2.5	K	1	h	0.5	h	Firm

Sounder	Atmospheric temperature profile	Higher troposphere (HT)	30	km	1	km	2.5	K	1	h	0.5	h	Firm

Sounder	Atmospheric temperature profile	Lower stratosphere (LS)	30	km	2	km	2	K	1	h	0.5	h	Firm

Sounder	Cloud cover	10	km	5	% (Max)	1	h	0.5	h	Reasonable

Sounder	Cloud optical thickness	30	km	20	%	1	h	0.5	h	Firm

Sounder	Cloud top height	10	km	0.7	km	1	h	0.5	h	Reasonable

Sounder	Cloud top temperature	30	km	2	K	1	h	0.5	h	Reasonable

Sounder	Land surface temperature	10	km	2	K	1	h	0.5	h	Reasonable

Sounder	Outgoing long-wave radiation at 	30	km	10	m/s	1	h	12	h	Firm

Sounder	Outgoing short-wave radiation at 	30	km	10	W/m2	1	h	12	h	Firm

Sounder	Ozone profile	Total column	30	km	30	DU	1	h	0.5	h	Firm

Sounder	Sea surface bulk temperature	10	km	0.5	1	h	0.5	h	Firm

Sounder	Specific humidity profile	Lower troposphere (LT)	30	km	1	km	20	%	1	h	0.5	h	Firm

Sounder	Specific humidity profile	Higher troposphere (HT)	30	km	1	km	20	%	1	h	0.5	h	Firm

Sounder	Specific humidity profile	Total column	30	km	2	kg/m2	1	h	0.5	h	Reasonable

Sounder	Wind profile (horizontal component)	Higher troposphere (HT)	150	km	5	km	5	m/s	1	d	1	h	Firm

SPECTRA	Leaf Area Index (LAI)	0.05	km	20	% (Max)	d	0.125	d	Speculative

SPECTRA	Long-wave Earth surface emissivity	0.2	km	0.5	% (Max)	72	h	3	h	Reasonable

SPECTRA	Snow melting conditions	0.05	km	5	classes	h	h	Speculative

SPECTRA	Snow water equivalent	0.05	km	5	mm	168	h	72	h	Speculative

SPECTRA	Vegetation type	50	m	10	classes	d	3	d	Tentative

SSM/I	Cloud water profile (< 100 µm)	Total column	75	km	30	kg/m2	12	h	3	h	Firm

SSM/I	Permafrost	50	km	40	% (Max)	0.5	d	2	d	Speculative

SSM/I	Precipitation rate (liquid) at the 	15	km	m/s	12	h	3	h	Firm

SSM/I	Sea-ice cover	15	km	20	% (Max)	0.5	d	24	d	Firm

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

SSM/I	Snow cover	20	km	10	% (Max)	12	h	24	h	Tentative

SSM/I	Snow melting conditions	8	km	5	classes	12	h	24	h	Tentative

SSM/I	Snow water equivalent	75	km	mm	12	h	3	h	Firm

SSM/I	Specific humidity profile	Total column	75	km	1.5	kg/m2	12	h	3	h	Firm

SSM/I	Wind speed over sea surface 	75	km	1.5	m/s	12	h	3	h	Firm

(horizontal)

SSM/T-1	Atmospheric temperature profile	Lower stratosphere (LS)	200	km	2	km	2	K	12	h	3	h	Firm

SSM/T-1	Atmospheric temperature profile	Lower troposphere (LT)	200	km	1	km	2.5	K	12	h	3	h	Firm

SSM/T-1	Atmospheric temperature profile	Higher troposphere (HT)	200	km	1	km	2.5	K	12	h	3	h	Firm

SSM/T-2	Specific humidity profile	Lower troposphere (LT)	50	km	2	km	15	%	12	h	3	h	Firm

SSM/T-2	Specific humidity profile	Higher troposphere (HT)	50	km	1	km	20	%	12	h	3	h	Reasonable

SSMIS	Atmospheric temperature profile	Higher troposphere (HT)	75	km	1	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

reception

SSMIS	Atmospheric temperature profile	Lower troposphere (LT)	75	km	1	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

reception

SSMIS	Atmospheric temperature profile	Lower stratosphere (LS)	75	km	2	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

reception

SSMIS	Atmospheric temperature profile	Higher stratosphere & 	75	km	2	km	2	K	12	h	2	h	Delay is quicker for local 	Firm

mesosphere (HS & M)	reception

SSMIS	Cloud water profile (< 100 µm)	Total column	75	km	30	kg/m2	12	h	3	h	Firm

SSMIS	Land surface temperature	75	km	3	K	12	h	2	h	Delay is quicker for local 	Speculative

reception

SSMIS	Permafrost	50	km	40	% (Max)	0.5	d	2	d	Speculative

SSMIS	Precipitation rate (liquid) at the 	15	km	m/s	12	h	3	h	Firm

SSMIS	Precipitation rate (solid) at the 	75	km	5	mm/h	12	h	2	h	Delay is quicker for local 	Firm

reception

SSMIS	Sea-ice cover	15	km	20	% (Max)	0.5	d	24	d	Firm

SSMIS	Snow cover	75	km	50	% (Max)	12	h	2	h	Delay is quicker for local 	Reasonable

reception

SSMIS	Snow water equivalent	75	km	mm	12	h	3	h	Firm

SSMIS	Specific humidity profile	Higher troposphere (HT)	75	km	1	km	15	%	12	h	2	h	Delay is quicker for local 	Firm

reception

SSMIS	Specific humidity profile	Lower troposphere (LT)	75	km	1	km	15	%	12	h	2	h	Delay is quicker for local 	Firm

reception

SSMIS	Specific humidity profile	Total column	75	km	1.5	kg/m2	12	h	3	h	Firm

SSMIS	Wind speed over sea surface 	75	km	1.5	m/s	12	h	3	h	Firm

(horizontal)

SSU	Atmospheric temperature profile	Lower stratosphere (LS)	200	km	2	km	2	K	12	h	2	h	Firm

SSU	Atmospheric temperature profile	Higher stratosphere & 	200	km	2	km	2	K	12	h	2	h	Firm

mesosphere (HS & M)

TM	Land cover	30	m	20	classes	0.04	y	2	d	Reasonable

TM	Vegetation type	30	m	20	classes	16	d	7	d	Firm

TMI	Specific humidity profile	Total column	10	km	1.5	kg/m2	80	h	720	h	Speculative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

TOMS	Ozone profile	Total column	50	km	20	DU	12	h	2	h	Speculative

TOVS (HIRS/2 + MSU + 	Atmospheric temperature profile	Lower stratosphere (LS)	80	km	2	km	1.5	K	12	h	2	h	Firm

SSU)

TOVS (HIRS/2 + MSU + 	Atmospheric temperature profile	Higher troposphere (HT)	80	km	1	km	2	K	12	h	2	h	Firm

SSU)

TOVS (HIRS/2 + MSU + 	Atmospheric temperature profile	Lower troposphere (LT)	80	km	1	km	2	K	12	h	2	h	Firm

SSU)

TOVS (HIRS/2 + MSU + 	Specific humidity profile	Higher troposphere (HT)	80	km	1	km	20	%	12	h	2	h	Firm

SSU)

TOVS (HIRS/2 + MSU + 	Specific humidity profile	Total column	80	km	2	kg/m2	12	h	2	h	Reasonable

SSU)

TOVS (HIRS/2 + MSU + 	Specific humidity profile	Lower troposphere (LT)	80	km	1	km	15	%	12	h	2	h	Firm

SSU)

VAS	Atmospheric stability index	100	km	K	1	h	0.5	h	Firm

VAS	Atmospheric temperature profile	Lower troposphere (LT)	100	km	1	km	2.5	K	1	h	0.5	h	Firm

VAS	Atmospheric temperature profile	Lower stratosphere (LS)	100	km	2	km	2	K	1	h	0.5	h	Firm

VAS	Atmospheric temperature profile	Higher troposphere (HT)	100	km	1	km	2.5	K	1	h	0.5	h	Firm

VAS	Cloud cover	10	km	15	% (Max)	1	h	0.5	h	Reasonable

VAS	Cloud top height	100	km	0.7	km	1	h	0.5	h	Reasonable

VAS	Cloud top temperature	100	km	2	K	1	h	0.5	h	Reasonable

VAS	Land surface temperature	10	km	2	K	1	h	0.5	h	Reasonable

VAS	Outgoing long-wave radiation at 	100	km	10	m/s	1	h	12	h	Firm

VAS	Outgoing short-wave radiation at 	100	km	10	W/m2	1	h	12	h	Firm

VAS	Precipitation rate (liquid) at the 	10	km	m/s	1	h	0.5	h	Firm

VAS	Precipitation rate (solid) at the 	50	km	mm/h	1	h	0.5	h	Firm

VAS	Sea surface bulk temperature	10	km	0.5	1	h	0.5	h	Firm

VAS	Specific humidity profile	Lower troposphere (LT)	100	km	1	km	15	%	1	h	0.5	h	Firm

VAS	Specific humidity profile	Higher troposphere (HT)	100	km	1	km	20	%	1	h	0.5	h	Firm

VEGETATION	Land cover	1000	m	15	classes	0.01	y	3	d	Speculative

VEGETATION	Leaf Area Index (LAI)	1	km	20	% (Max)	30	d	3	d	Tentative

VHRR	Wind profile (horizontal component)	Higher troposphere (HT)	150	km	5	km	6	m/s	1	d	2	h	Reasonable

VHRR	Wind profile (horizontal component)	Lower troposphere (LT)	150	km	5	km	4	m/s	1	h	2	h	Firm

VIIRS	Aerosol profile	Total column	5	km	%	12	h	2	h	Tentative

VIIRS	Atmospheric temperature profile	Lower troposphere (LT)	5	km	1	km	2.5	K	12	h	2	h	Tentative

VIIRS	Atmospheric temperature profile	Higher troposphere (HT)	5	km	1	km	2.5	K	12	h	2	h	Tentative

VIIRS	Cloud cover	5	km	5	% (Max)	12	h	2	h	Tentative

VIIRS	Cloud imagery	0.4	km	12	h	2	h	Speculative

VIIRS	Cloud optical thickness	5	km	20	%	12	h	2	h	Tentative

VIIRS	Cloud top height	5	km	0.7	km	12	h	2	h	Speculative

VIIRS	Cloud top temperature	5	km	2	K	12	h	2	h	Speculative

VIIRS	Cloud type	1	km	8	classes	12	h	2	h	Speculative

VIIRS	Fire area	1	m2	5	% (Max)	0.5	d	0.08	d	Tentative

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

VIIRS	Fire temperature	1	K	50	K	0.5	d	0.08	d	Tentative

VIIRS	Fractional Photosynthetically Active	0.4	km	15	% (Max)	0.5	d	2	d	Speculative

Radiation (FPAR)

VIIRS	Land cover	400	m	15	classes	0.01	y	0.08	d	Tentative

VIIRS	Land surface imagery	400	m	2	d	2	d	Tentative

VIIRS	Land surface temperature	1	km	1	K	12	h	2	h	Tentative

VIIRS	Leaf Area Index (LAI)	0.4	km	20	% (Max)	30	d	0.08	d	Tentative

VIIRS	Normalized Differential Vegetation 	0.4	km	5	% (Max)	0.5	d	0.08	d	Tentative

Index (NDVI)

VIIRS	Outgoing long-wave radiation at 	5	km	10	m/s	12	h	2	h	Tentative

VIIRS	Outgoing short-wave radiation at 	5	km	10	W/m2	12	h	2	h	Tentative

VIIRS	Ozone profile	Total column	5	km	30	DU	12	h	2	h	Tentative

VIIRS	Sea surface bulk temperature	1	km	0.3	12	h	2	h	Tentative

VIIRS	Snow cover	0.4	km	5	% (Max)	12	h	2	h	Speculative

VIIRS	Specific humidity profile	Lower troposphere (LT)	5	km	2	km	20	%	12	h	2	h	Tentative

VIIRS	Specific humidity profile	Total column	5	km	2.5	kg/m2	12	h	2	h	Tentative

VIIRS	Specific humidity profile	Higher troposphere (HT)	5	km	3	km	20	%	12	h	2	h	Tentative

VIIRS	Vegetation type	400	m	10	classes	1	d	0.08	d	Tentative

VISSR (FY-2)	Cloud cover	20	km	15	% (Max)	1	h	1	h	Reasonable

VISSR (FY-2)	Cloud imagery	5	km	1	h	1	h	Reasonable

VISSR (FY-2)	Cloud top height	50	km	1	km	1	h	1	h	Reasonable

VISSR (FY-2)	Cloud top temperature	50	km	2	K	1	h	1	h	Reasonable

VISSR (FY-2)	Cloud type	50	km	3	classes	1	h	1	h	Reasonable

VISSR (FY-2)	Outgoing long-wave radiation at 	50	km	20	m/s	1	h	12	h	Reasonable

VISSR (FY-2)	Outgoing short-wave radiation at 	50	km	20	W/m2	1	h	12	h	Reasonable

VISSR (FY-2)	Precipitation rate (liquid) at the 	5	km	10	m/s	1	h	3	h	Reasonable

VISSR (FY-2)	Sea surface bulk temperature	50	km	1	1	h	3	h	Reasonable

VISSR (FY-2)	Wind profile (horizontal component)	Higher troposphere (HT)	50	km	5	km	5	m/s	1	d	2	h	Reasonable

VISSR (FY-2)	Wind profile (horizontal component)	Lower troposphere (LT)	50	km	5	km	2	m/s	1	h	2	h	Reasonable

VISSR (GMS-5)	Cloud cover	20	km	15	% (Max)	1	h	1.5	h	Firm

VISSR (GMS-5)	Cloud imagery	5	km	1	h	0.1	h	Firm

VISSR (GMS-5)	Cloud top height	50	km	1	km	1	h	1.5	h	Firm

VISSR (GMS-5)	Cloud top temperature	50	km	2	K	3	h	1.5	h	Firm

VISSR (GMS-5)	Cloud type	50	km	2	classes	3	h	1.5	h	Firm

VISSR (GMS-5)	Outgoing long-wave radiation at 	50	km	30	m/s	1	h	6	h	Firm

VISSR (GMS-5)	Outgoing short-wave radiation at 	50	km	W/m2	1	h	6	h	Firm

VISSR (GMS-5)	Precipitation rate (liquid) at the 	50	km	m/s	1	h	0.1	h	Firm

VISSR (GMS-5)	Precipitation rate (solid) at the 	50	km	mm/h	1	h	0.1	h	Firm

VISSR (GMS-5)	Sea surface bulk temperature	50	km	1	1	h	1.5	h	Firm

VISSR (GMS-5)	Specific humidity profile	Lower troposphere (LT)	50	km	2	km	20	%	1	h	0.5	h	Firm

Instrument	Parameter	Hor Res	Vert Res	Accuracy	Obsv Cycle	Delay 	Comment	Con

VISSR (GMS-5)	Specific humidity profile	Higher troposphere (HT)	50	km	3	km	20	%	1	h	1	h	Firm

VISSR (GMS-5)	Wind profile (horizontal component)	Lower troposphere (LT)	150	km	5	km	3	m/s	1	h	2	h	Firm

VISSR (GMS-5)	Wind profile (horizontal component)	Higher troposphere (HT)	150	km	5	km	5	m/s	1	d	2	h	Firm

APPENDIX B

## WMO requirements without match in user estimates but with a match in space agency estimates

WMO requirements without match in user estimates but with a match in space agency estimates

29-Oct-03

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Cloud ice profile Higher troposphere (HT)

CPR (Cloudsat)	3	km	0.5	km	50	%	h	h

Cloud ice profile Lower troposphere (LT)

CPR (Cloudsat)	3	km	0.5	km	50	%	h	h

# Cloud ice profile Total column

CMIS	50	km	5	g/m2	12	h	2	h

Cloud water profile (< 100 µm) Higher troposphere (HT)

CPR (Cloudsat)	3	km	0.5	km	25	%	h	h

Cloud water profile (< 100 µm) Lower troposphere (LT)

ACE-FTS	km	km	%	h	h

AMSR-E	km	km	%	h	h

AMSU-B	km	km	%	h	h

APS	km	km	%	h	h

ATLID	km	km	%	h	h

CPR	km	km	%	h	h

CPR (Cloudsat)	3	km	0.5	km	         25%	                                                              h	h

GIFTS	km	km	%	h	h

HSB	km	km	%	h	h

IIR	km	km	%	h	h

IKFS-2	km	km	%	h	h

IVISSR (FY-2)	km	km	%	h	h

MAESTRO	km	km	%	h	h

MERIS	km	km	%	h	h

MHS	km	km	%	h	h

MR-2000M1	km	km	%	h	h

MTVZA	km	km	%	h	h

RM-08	km	km	%	h	h

Cloud water profile (> 100 µm) Higher troposphere (HT)

CPR (Cloudsat)	3	km	0.5	km	25	%	h	h

Cloud water profile (> 100 µm) Lower troposphere (LT)

CPR (Cloudsat)	3	km	0.5	km	25	%	h	h

TMI	21	km	2.5	km	%	24	h	24	h

# Cloud water profile (> 100 µm) Total column

ATMS	50	km	30	kg/m2	12	h	2	h

CPR (Cloudsat)	km	 kg/m2	 h	h

MHS	30	km	10	kg/m2	12	h	3	h

1

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Ozone profile Higher stratosphere & mesosphere (HS & M)

GOMOS	300	km	1	km	 %	36	h	3	h

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS	km	km	 %	 h	 h

ILAS-II	300	km	1	km	 %	 h 	 h

MIPAS	300	km	3	km	 %	36	h	3	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

OSIRIS	km	km	5	%	 h	 h

SAGE III	100	km	1	km	6	%	48	h	24	h

SBUV/2	200	km	8	km	5	%	24	h	3	h

SBUV/3	200	km	8	km	10	%	24	h	3	h

SCIAMACHY	500	km	3	km	 %	36	h	3	h

SOFIS	300	km	1	km	 %	 h	 h

SOPRANO	50000	km	2	km	 %	3	h	 h

Specific humidity profile Higher stratosphere & mesosphere (HS & M)

AIRS	50	km	2	km	30	%	12	h	24	h

GOMOS	300	km	1	km	 %	36	h	3	h

HiRDLS	400	km	1	km	 %	12	h	24	h

ILAS-II	300	km	1	km	 %	 h	 h

MIPAS	300	km	3	km	 %	36	h	3	h

MLS (EOS-Aura)	200	km	2	km	10	%	12	h	 h

SAGE III	100	km	1	km	 %	48	h	24	h

SMR	km	km	 %	 h	 h

SOFIS	300	km	1	km	 %	 h	 h

SOPRANO	50000	km	4	km	 %	3	h	 h

Trace gas profile BrO Higher stratosphere & mesosphere (HS & M)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

OSIRIS	km	km	20	%	 h	 h

Trace gas profile BrO Higher troposphere (HT)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

Trace gas profile BrO Lower stratosphere (LS)

MASTER	1000000	km	4	km	 %	3	h	 h

MIPAS	300	km	3	km	 %	36	h	 h

Trace gas profile CH4 Higher stratosphere & mesosphere (HS & M)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

OSIRIS	km	km	20	%	 h	 h

SAGE III	100	km	1	km	20	%	48	h	 h

SCIAMACHY	500	km	3	km	 %	36	h	3	h

SOPRANO	50000	km	4	km	 %	3	h	 h

Trace gas profile BrO Lower troposphere (LT)

SAGE I	km	km	 %	 h	 h

SAGE II	km	km	 %	 h	 h

2

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Trace gas profile CFC 11 Higher stratosphere & mesosphere (HS & M)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS	km	km	 %	h	h

ILAS-II	300	km	1	km 	 %	h	h

SOFIS	300	km	1	km	 %	h	h

Trace gas profile CFC 11 Higher troposphere (HT)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	h

SOFIS	300	km	1	km	%	h	h

Trace gas profile CFC 11 Lower stratosphere (LS)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	h

SOFIS	300	km	1	km	%	h	h

Trace gas profile CFC 12 Higher stratosphere & mesosphere (HS & M)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

Trace gas profile CFC 12 Higher troposphere (HT)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

SOFIS	300	km	1	km	%	h	h

Trace gas profile CFC 12 Lower stratosphere (LS)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	h

SOFIS	300	km	1	km	%	h	h

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS	km	km	%	h	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	3	h

SOFIS	300	km	1	km	%	h	h

TES	169	km	6	km	%	96	h	24	h

Trace gas profile ClO Higher stratosphere & mesosphere (HS & M)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SMR	km	km	%	h	h

Trace gas profile ClO Higher troposphere (HT)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

3

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Trace gas profile ClO Lower stratosphere (LS)

MASTER	1000000	km	4	km	 %	3	h	h

MIPAS	300	km	3	km	 %	36	h	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SAGE III	100	km	1	km	20	%	48	h	 h

SCIAMACHY	500	km	3	km 	 %	36	h	3	h

SMR	500	km	2	km	20	%	 h	 h

SOPRANO	50000	km	4	km	 %	3	h	 h

Trace gas profile ClONO2 Higher stratosphere & mesosphere (HS & M)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	 %	 h	 h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SOFIS	300	km	1	km	 %	 h	 h

Trace gas profile ClONO2 Higher troposphere (HT)

ILAS-II	300	km	1	km	 %	 h	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SOFIS	300	km	1	km	 %	 h	h

Trace gas profile ClONO2 Lower stratosphere (LS)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	 %	 h	 h

MASTER	1000000	km	4	km	 %	3	h	 h

MIPAS	300	km	3	km	 %	36	h	 h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SAGE III	100	km	1	km	20	%	48	h	 h

SCIAMACHY	500	km	3	km	 %	36	h	3	h

SOFIS	300	km	1	km	 %	 h	h

SOPRANO	50000	km	4	km	 %	3h	h

Trace gas profile HCl Higher stratosphere & mesosphere (HS & M)

SOPRANO	50000	km	2	km	 %	3	h	h

Trace gas profile HCl Higher troposphere (HT)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

Trace gas profile HCl Lower stratosphere (LS)

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SOPRANO	50000	km	2	km	 %	3	h	h

Trace gas profile HNO3 Higher stratosphere & mesosphere (HS & M)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS	km	km	 %	 h	h

ILAS-II	300	km	1	km	 %	 h	h

MIPAS	300	km	3	km	 %	36	h	3	h

SOFIS	300	km	1	km	 %	 h	h

4

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Trace gas profile HNO3 Higher troposphere (HT)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	3	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SOFIS	300	km	1	km	%	h	h

TES	169	km	3	km	%	96	h	24	h

Trace gas profile HNO3 Lower stratosphere (LS)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MASTER	50000	km	2.5	km	%	3	h	h

MIPAS	300	km	3	km	%	36	h	3	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SMR	km	km	%	h	h

SOFIS	300	km	1	km	%	h	h

TES	169	km	3	km	%	96	h	24	h

Trace gas profile HNO3 Lower troposphere  (LT)

TES	169	km	3	km	%	96	h	24	h

Trace gas profile N2O Higher stratosphere & mesosphere (HS & M)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS	km	km	%	h	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	3	h

SOFIS	300	km	1	km	%	h	h

SOPRANO	50000	km	2	km	%	3	h	h

Trace gas profile N2O Higher troposphere (HT)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	3	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SOFIS	300	km	1	km	%	h	h

TES	169	km	6	km	%	96	h	24	h

Trace gas profile N2O Lower stratosphere (LS)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	3	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	24	h

SMR	km	km	%	h	h

SOFIS	300	km	1	km	%	h	h

SOPRANO	50000	km	2	km	%	3	h	h

TES	169	km	6	km	%	96	h	24	h

5

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Trace gas profile NO Higher stratosphere & mesosphere (HS & M)

MIPAS	300	km	3	km	%	36	h	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	h

SOPRANO	50000	km	2	km	%	3	h	h

Trace gas profile NO Higher troposphere (HT)

TES	169	km	3	km	%	96	h	24	h

Trace gas profile NO Lower stratosphere (LS)

MIPAS	300	km	3	km	%	36	h	h

MLS (EOS-Aura)	200	km	2	km	5	%	12	h	h

SOPRANO	50000	km	4	km	%	3	h	h

TES	169	km	3	km	%	96	h	24	h

Trace gas profile NO Lower troposphere (LT)

TES	169	km	3	km	%	96	h	24	h

Trace gas profile NO2 Higher stratosphere & mesosphere (HS & M)

GOMOS	300	km	1	km	%	36	h	3	h

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MIPAS	300	km	3	km	%	36	h	h

OSIRIS	km	km	15	%	h	h

SAGE III	100	km	1	km	10	%	48	h	720	h

SOFIS	300	km	1	km	%	h	h

TES	169	km	3	km	%	96	h	24	h

Trace gas profile NO2 Higher troposphere (HT)

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MASTER	50000	km	2.5	km	%	3	h	h

SAGE III	100	km	1	km	10	%	48	h	720	h

SOFIS	300	km	1	km	%	h	h

TES	169	km	3	km	%	96	h	24	h

Trace gas profile NO2 Lower stratosphere (LS)

GOMOS	300	km	1	km	%	36	h	3	h

HiRDLS	400	km	1	km	10	%	12	h	24	h

ILAS-II	300	km	1	km	%	h	h

MASTER	50000	km	2.5	km	%	3	h	h

MIPAS	300	km	3	km	%	36	h	h

OSIRIS	km	km	15	%	h	h

SAGE III	100	km	1	km	10	%	48	h	720	h

SOFIS	300	km	1	km	%	h	h

6

Parameter	Hor Res	Vert Res	Accuracy	Observing Cycle	Delay of availability

Instrument

Trace gas profile NO2 Lower troposphere  (LT)

SAGE I	km	km	%	h	h

SAGE II	km	km	%	h	h

TES	169	km	3	km	%	96	h	24	h

Trace gas profile NO2 Total column

GOME	320	km	20	%	72	h	336	h

SCIAMACHY	320	km	%	36	h	h