| WORLD METEOROLOGICAL ORGANIZATION ___________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON EVOLUTION OF THE GLOBAL OBSERVING SYSTEM THIRD SESSION GENEVA, SWITZERLAND, 9-13 July 2007 |  | CBS/OPAG-IOS/ET-EGOS-3/Doc. 7.2.8 (04.VII.2007) _______ ITEM: 7.2 Original: ENGLISH |
| --- | --- | --- |

Status of individual Statements of Guidance and

recommended update strategy

STATEMENT OF GUIDANCE FOR HYDROLOGY AND WATER RESOURCES

(Submitted by the Secretariat)

SUMMARY AND PURPOSE OF DOCUMENT This document presents the updated status of the Hydrology and Water Resources Statement of Guidance (SOG).

ACTION PROPOSED

The meeting is invited to consider these updates and to incorporate as appropriate into a revised Statement of Guidance.

__________________

Statement of Guidance for HDROLOGY AND WATER RESOURCES

(Updated July 2007)

3.10	Statement of Guidance for Hydrology

The collection of hydrological data is crucial to improve our understanding of the hydrological cycle for weather and climate-related scientific and application issues as well as for water resources management through improved assessment methods and the reduction of disasters following observations of hydrological extremes. For most of the presently available observations, the adequacy of observational networks varies largely from region to region and observations for some of the variables described below are inadequate in terms of spatial and temporal coverage. As a methodological approach it has become evident, that observations of hydrological variables on global and regional scale in a continued and consistent manner will require integrated observation systems making use of both terrestrial as well as satellite observations and the generation of products on the basis of data assimilation products generated from these integrated networks and multi-platform observations.

### 3.10.1	Hydrology Requirements

The Terrestrial Observation Panel on Climate (TOPC) has identified 11 hydrometeorological variables with a high observation priority (GCOS, 1997). An expert meeting on the Establishment of a Global Terrestrial Network – Hydrology (GTN-H) confirmed these 11 variables (GCOS, 2000) recognizing that several of these variables have both an in-situ as well as a satellite observation component. These variables and their current state of observation are briefly discussed in the paragraphs below. All variables are also discussed in detail in the integrated Water Cycle Observations (IGWCO) theme of the IGOS Partners in 2004. Latest progress on both in situ and space based observations are documented in the report of the 3rd meeting of the IGWCO, Washington 2007 (http://www.wmo.int/pages/prog/igwco/reports/documents/igwco.plmtg.rpt.2007.igos14.pdf). Likewise, progress is being made in contributing to the Water Tasks of GEOSS. It needs to be cautioned however, that observational requirements over the oceans are not reflected in the SOGs from Hydrology and Water Resources. In this regard, a critical field where global observations are required is the early detection of storm surges, in particular in combination with riverine floods in low-lying coastal zones. Storm surge detection is possible using satellite-based altimetry. At present, global observations are not undertaken on a routine basis.

Temporal requirements for data used operational hydrology are classified in two ways: (i) the first is non- or slowly-time dependent data such as topography and land use; and (ii) the second is time dependent data needed to initialize and update forecast models such as rainfall rates or soil moisture. Satellite data is the only means for providing high spatial and temporal resolution data in key regions (e.g. forested areas). In situ data provide acceptable coverage in limited regions and are also used for calibration and validation of hydrological models. To meet hydrological forecasting needs, the data must be available within 1/2 to 6 hours, depending upon the size of the basin and forecasting requirements. Products useful to hydrology are listed below with a description of how well they meet the hydrological model needs and whether or not they are time-sensitive. For example, hydrologic variables such as snow cover, snow water equivalent and soil moisture are dynamic variables that must be updated fairly frequently. Variables where data delivery is time sensitive (less than 6 hours) are indicated.

### 3.10.2	Hydrology Requirements versus GOS Capabilities

-  Surface Water Discharge

Discharge is typically calculated at a particular location in a river from measured water levels by means of a transformation or rating curve developed for the particular channel cross-section at which the water level is measured. Flow in a channel can be influenced by factors such as changes in land use, withdrawal for water use, or contributions from artificial water storage reservoirs, and thus discharge does not necessarily represent a response to climatic conditions. On a global scale, terrestrial hydrological observations are marginal and generally unacceptable in remote and mountain areas. Access to hydrological data is frequently impeded due to a number of factors including fragmentation of data holdings and access restrictions. A new approach is the planned implementation of the Hydrological Applications and Runoff Network (HARON) in cooperation with WMO, GCOS, GRDC and facilitated by GEOSS. Likewise, WMO’s WHYCOS programme contributes to the improvement of surface hydrological networks on a regional basis for operational purposes Satellite water-level observations based on altimetry methods are available for large rivers and can now be utilized for major basins and lakes in a semi-operational mode. Several satellite-based methods are available on demand to map the extent of flooding in floodplains or large riverine systems as well as the duration of flooding, including visual, IR and radar sensors.

-  Surface water storage fluxes

This variable is directly related to the retention of surface fluxes in lakes, reservoirs and wetlands. There is also the issue of water storage in river channels, flood plains and large estuaries. While terrestrial observations are being made for lakes and reservoirs (levels of lakes and reservoirs, volumetric observations), space-based observations such as those derived from altimetric observations are also becoming available. Generally, observations are not yet available for wetlands, large floodplains and estuaries. The availability of surface water storage fluxes for the major lakes and reservoirs would contribute to a more accurate modelling of lateral fluxes in climate circulation models. Presently, the ability of the ICES/GLAS instrument to provide accurate measurements of lake level is being tested. However, many observations uncertainties still exist with regard to flow retention in dams, reservoirs, lakes and wetlands; and the evaporative loss of water from storage surfaces.

-  Ground water fluxes

Groundwater fluxes have a major influence on the dynamics of the global hydrological cycle. Because groundwater tends to respond more slowly to short term climatic variations than do surface water resources, this variable is often not considered to be of first-order importance from a climate perspective. Terrestrial observations are being made but overall global access to groundwater data (rates of recharge and abstraction in particular) is highly limited. Gravimetric observation techniques (such as from GRACE) for very large groundwater bodies are available on satellite platforms approach a semi-operational status. The use of GOCE data is being explored.

-  Precipitation (liquid/solid)

Various meteorological variables including precipitation depth and type are routinely observed on an hourly to daily basis at synoptic weather stations. Global coverage from in-situ observations exhibits with large regional differences. Exchange of data is achieved in real-time and near real-time mode and subsets of the precipitation measurements made are accessible through global networks and data centres. Increasingly, spatial and temporal coverage of rainfall observations is improving using ground radar techniques. Satellite observations from on-board radars as well as microwave imagers and sounders are also available, where precipitation information can be derived on a global scale. Merged data products using direct terrestrial observations and satellite observations are routinely available on a global scale. However, quantitative precipitation observations from satellite measurements at present do not meet accuracy requirements; when combined with terrestrial observations they provide precipitation estimates with an improving resolution.  Especially information from TRMM satellites and the emerging precipitation network through the virtual constellation network of CEOS provide improved precipitation information that can be used flood forecasting. Major progress is expected when the Global Precipitation Mission (GPM) will be launched from 2013 onwards. A focus is now in improving satellite-based rainfall information in real-time for the use in flash flood forecasting. This is operationally achieved by the spreading use of hydrological S-band Doppler radars and improved satellite-based observations.

-  Isotope signatures

To improve understanding of the hydrological cycle, investigations of environmental isotopes in precipitation are required. Isotope signatures in precipitation also constitute an essential tool for calibration and validation of atmospheric circulation models. At present, only a small global network of terrestrial isotope stations exists where all data are accessible. Especially for water balance studies, isotope observations using water stable isotopes could be used on an operational scale in riverine environments.

-  Evaporation

Evaporation is a critical value in the water balance equation as well as in regional water budget estimations. However, direct observations are sparse and most evaporation values are in fact derived estimates. Evaporation in the context of the SOG’s refers to "direct" measurements of actual evaporation. Because of the observing methods, even direct measurements are estimates. Terrestrial measurements on a global scale are declining in terms of spatial coverage at a time when traditional in-situ observations like evaporation pans and lysimeters are discontinued. Replacing traditional observation methods by using flux towers, evaporation estimates are made using eddy correlation and Bowen Ratio techniques. The number of these towers is very limited and data are not readily available on a global scale. Isotopic measurements can provide an effective method to derive evaporation as ratio of change of water stable isotopes between vapor and the residual liquid.

-  Vapor pressure / Relative humidity

Relative humidity is observed from in-situ networks with generally sufficient global coverage and is a basic variable for estimation of evapotranspiration as well as in use for water cycle studies and modelling. An equally suitable variable is vapor pressure as this variable is reported through the GTS, is directly useful for NWP modelling and estimation of the water vapor greenhouse effect and, given air temperature, can again be used to compute relative humidity. Sounding instruments using both IR and Microwave are used on satellite-born platforms. Radiosondes are routinely used to observe vertical water vapor distribution. Column water vapor or precipitable water is estimated by microwave radiometers.

-  Soil moisture/Soil wetness

The observation of soil moisture or soil wetness (as a proxy for soil moisture) is important for hydrological forecasting in large river basins and likewise for modelling of the land surface module in coupled land-atmosphere models. A number of networks for soil moisture measurements exist in different parts of the globe. The establishment of a global in-situ network on soil moisture is in an advanced planning stage. This will involve network enhancement by expansion and standardization, dedicated soil moisture missions (support for SMOS, ESA’s soil moisture ocean salinity satellite mission), and improved coordination of soil moisture data network planning, observing standards, and data exchange.  The use of advanced scatterometers allows derivation of soil wetness of the first few centimetres that however is only partially useful for hydrological studies and forecasting and need to be augmented by infiltration models, for example. On terrain, soil wetness can also be observed by passive microwave emission radiometry. On a global scale, with a spatial resolution of about 30-50 km, L-Band radar may provide spatial coverage. On a regional basis, a soil moisture index for Europe and Africa is derived from meteorological satellite data; this work is done within the framework of the EUMETSAT Satellite Application Facility for Land Surface Analysis (Land-SAF).

Most of the active and passive microwave instruments provide some soil moisture information for regions of limited vegetation cover. However, under many conditions remote sensing data are inadequate, and information regarding moisture depth remains elusive. Unfortunately, none of the instruments provide a satisfactory combination of spatial resolution and repeat cycle time (2 to 3 days). The AMSR data comes close to providing soil moisture or land wetness information that may be marginally useful for mesoscale models but the timeliness of these data remains challenging.

-  Snow cover, depth, and water equivalent and glaciers

Seasonal snow cover is an important storage of water and largely regulates streamflow regimes and water resources management practices. Due to its high albedo, snow cover plays an important role in radiance and the land-atmosphere energy budget. Water stored in snow and ice especially in mountain regions of the earth are critical for water resources management for a large population. Conventional terrestrial observation methods include snow-pillow networks and regularly worked snow depth measurement courses as well as networks of snow gauges. Derived from measured snow densities, snow water equivalent is calculated as an important hydrologic derived variable. On the northern hemisphere, snow observations are generally adequate but areal representativeness of snow cover thickness can often not be assessed with a high reliability. Satellite-based systems include AVHRR sensors. On a regional basis, passive microwave sensors such as SSM/I can be used to map extent and depth of moderate-thick snow covers. The overall important snow-water equivalent of snow packs should be derived on the basis of improved algorithms from microwave brightness temperature.

Current and planned polar orbiting satellites should provide acceptable data on snow cover. AVHRR provides adequate snow cover information; the addition of the 1.6 micron channel has been useful in discriminating snow from clouds. Snow maps are being made available from the multichannel (36 channels in the visible and near infrared wavelengths) MODIS instrument within 48 hours after data collection. The passive microwave instruments (i.e. SSM/I, AMSR) have all weather and day/night monitoring capability and are able to estimate the thickness of dry snow up to about 80 cm deep. These snow cover measurements are acceptable for mesoscale modelling and snowmelt runoff forecasting.

The passive microwave AMSR and SSM/I provide useful estimates of snow water equivalents where there are validated regional algorithms. Current acceptable algorithms are based on the brightness temperature difference between the 19 and 37 GHz channels. There is no general algorithm that can be applied to all regions. Regional modifications are necessary to account for snow grain size (climate related), vegetation (especially forested areas) and elevation. The measurements are acceptable for water balance studies and snowmelt runoff forecasting in large basins.

-  Land surface temperature

There are a number of satellites that provide acceptable land surface temperature changes. A few hydrologic energy and water balance models make direct use of time sensitive data that are most valuable for extrapolating between meteorological station data, large areas, and data sparse areas.

-  Vegetation type and NDVI

AVHRR and MODIS are providing acceptable and in some cases, good NDVI and vegetation type data. However, in some cases, the NDVI and vegetation type products may not be interchangeable because of slightly different spectral bands. The cycle times in most cases are acceptable for NDVI and adequate for vegetation type because they do not change very rapidly. METEOSAT Second Generation offers the opportunity to investigate diurnal changes in NDVI.

-  Short-wave and Long-wave outgoing radiation at TOA

Most of the satellite instruments will provide acceptable short-wave and long-wave outgoing radiation at TOA at acceptable resolution, cycle time and accuracy for most hydrologic applications. These time sensitive data are useful for basin scale modelling of water and energy balances. Some of the satellites are good for cycle time and accuracy.

-  Biogeochemical (BGC) fluxes from land to ocean

These observations are intended to quantify the transport of matter and pollutants from the continents into the oceans. For global change analysis, especially carbon, amongst other elements is of major interest. Terrestrial observations are being made but temporal and spatial coverage as well as global access to such observations is insufficient at present. While the technology exists to provide water quality data with high precision for a large number of organic and inorganic components, space-based observations are so far very limited and not available in an operational mode.  Through IGWCO, a project: “Multisensor Space borne Monitoring of Global Large Lakes: Towards an Operational Assessment of Trends in Water Quantity and Quality” is being supported.

-  Water Use

In the management of water resources as well as the assessment of the potential natural flow of water in rivers for General Circulation Models and climate change studies, amongst others, information on water use is critical. However, at present only anecdotal information is available on this critical variable that is also highly heterogeneous in quality and availability (administrative, spatial and temporal). While sectoral information (mostly estimates) are available on a country basis, global consolidated information on water use both consumptive and non-consumptive is not yet existing and most existing information is extrapolated or derived from relatively few accessible data sources. The probably most advanced data base on water use, focusing on irrigation is AQUASTAT that is maintained by FAO. In this situation, appropriate national organizations should be encouraged to develop a reporting model of spatially resolved sectoral water use. The USGS scheme (reporting by both political and hydrologic spatial units, for various economic/industrial sectors, on a five-year time step) could be used as an appropriate model format. Furthermore, countries should make the information on water use internationally available.

### 3.10.3	Examples of Hydrology Products Generated from Selected Variables

Table 3.10.1 below provides examples of products that can be developed on the basis of the selected variables as described above and the spatial and temporal resolution that could be achieved if the products were supplied in an operational mode. Some of these products are expected to be generated in activities related to the Global Terrestrial Network – Hydrology (GTN-H). Table 3.10.2 below provides a summary overview of the importance and usefulness of individual hydrological variables in relation to five thematic areas that are also served by information resulting from the operation of Global Observing Systems.

Table 3.10.1 - Examples for variable-derived products for hydrology,

water resources, weather and climate applications

| Product name | Content | Use (examples only) | Spatial resolution | Temporal resolution | Timelines |
| --- | --- | --- | --- | --- | --- |
| Discharge | Gridded runoff fields | Water balance computation | 1o x 1o | Monthly | DT (delayed time) |
| Discharge | Point data | Weather and flow fore-casting; model validation | N/A | Daily | NRT (near-real time) |
| Discharge | Point data | Global water cycle analysis | By station (river-basin) | Daily/ Monthly | DT |
| Soil moisture | Gridded (preferably) | Weather and flow fore- casting; assimilation in models | TBD | Daily to monthly | NRT |
| BGC flux into oceans | By major watershed | Global BGC cycles analysis | By watershed | Daily to monthly | DT |
| Isotope composition | d 18O, d 2H, 3H | Various | By station | Weekly to monthly | DT |
| Precipitation | Solid and liquid separately; point data | Regional water cycle analysis; Hydrological forecasting | 1dx1d globally; 0.5o x 0.5o regionally; point data | Daily and monthly | DT |
| Precipitation, evapotranspiration | Point data | Real time data for assimilation in models, water budgets | Point | Daily | RT |
| Snow water equivalent | Gridded | Various | TBD | TBD | DT |
| Ground water fluxes | Aquifer withdrawal/recharge rates | Various | By aquifer | TBD | DT |
| Water use | Differentiated consumptive/non-consumptive use | Various | Point or polygon | Monthly, annual | DT |
| Water use | Gridded consumptive/non-consumptive use | Various | 0.5o x 0.5o | Monthly | DT |
| Surface storage Flux | Volume changes in lakes and reservoirs | Water cycle analysis | Polygon | Monthly or seasonal | DT |

Table 3.10.2 -  Summary table of applications vs. hydrological variables

| Variable | Hydrologic, climate and weather forecasting | Climate variability, trend | Diagnosis, mitigation, adaptation | Sustainable development | Improved understanding of water cycle |
| --- | --- | --- | --- | --- | --- |
| Surface water – discharge | e (v) | E | e | e | e |
| Surface water storage fluxes | e (v) | E | d | e | e |
| Ground water fluxes | D | E | d | e | e |
| Water use | - | - | d | e | e |
| BGC transport | - | - | e | d | e |
| Isotopic signatures | - | D | - | d | e |
| Precipitation | e (i,v) | E | - | e | e |
| Evaporation | D | - | - | d | e |
| Vapor pressure/ relative humidity | E | - | - | - | d |
| Soil moisture | e (v) | - | - | d | e (v) |
| Snow water equivalent | e (i) | E | - | e | e |

e= essential; d= desirable; v= validation; i= input

### 3.10.4	Summary of Hydrology SOG

The following key points summarize the SOG for hydrology applications:

- The Terrestrial Observation Panel on Climate (TOPC) has identified 11 hydrometerological variables with a high observation priority (GCOS, 1997). An expert meeting on the Establishment of a Global Terrestrial Network – Hydrology (GTN-H) confirmed these 11 variables (GCOS, 2000).

- Satellite data (currently from Landsat, AVHRR, and MODIS) is the only means for providing high resolution data in key regions where in-situ observations are sparse or not existing.

- Precipitation depth and type are routinely observed on an hourly to daily basis at synoptic weather stations but there are large regional differences in coverage; spatial and temporal coverage of rainfall observations is improving using ground radar techniques. Global scale observations from satellite borne radars as well as microwave imagers and sounders are routinely available, but quantitative precipitation observations from satellite measurements at present do not meet accuracy requirements. For operational purposes, the number of established Hydrological Radars is increasing.

- Terrestrial measurements of evaporation are declining in terms of spatial coverage; flux towers numbers are very limited, with data not readily available on a global scale.

- Acceptable data on areal extent of snow cover has improved with the transition from AVHRR to MODIS; passive microwave instruments (i.e. AMSR) have improved estimates of the thickness of dry snow. These snow cover measurements will be acceptable for mesoscale modelling and snowmelt runoff forecasting.

- Addition of microwave instruments (AMSU and AMSR) provide enhanced observational capabilities for snow water equivalent and soil moisture, however operational continuity of AMSR is not assured.

- Observations on snow and ice is expected to improve after the launch of CRYOSAT II.

- Runoff observations (levels in rivers, lakes and reservoirs) can now be supplemented by radar altimetry instruments flown on ENVISAT and likewise JASON and TOPEX may be used for this purpose.

- Gravimetric measurements of changes in large aquifers from GRACE and GOCE are nearing a stage where they could be used operationally.

- A number of additional satellite-derived variables are, or will be, extremely useful to hydrology, including but not limited to: precipitation rates and totals, latent and sensible heat, surface air temperature and humidity, and surface winds.

- In most fields of applications, satellite information has not been used operationally for hydrological purposes.

- Focus needs to be laid on the integration of in-situ and space based observations for hydrological applications in a comparable space and time domain and of acceptable accuracy.  The latter would require increased efforts to assess observation quality through intercomparison and (re)-calibration projects.

- In general, access to hydrological data and observations of all variables mentioned in insufficient for many research and development purposes and for practical applications by national Hydrological Services.

_______________