| WORLD METEOROLOGICAL ORGANIZATION __________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON EVOLUTION OF THE GLOBAL OBSERVING SYSTEM THIRD SESSION GENEVA, SWITZERLAND, 9-13 JULY 2007 |  | CBS/OPAG-IOS/ET-EGOS-3/Doc. 9.3.4 (05.VII.2007) _______ ITEM: 9.3 Original: ENGLISH |
| --- | --- | --- |

REVIEW OF PROGRESS AND ACTIONS CONCERNING IP-EGOS

IN REGIONS II (ASIA) AND V (SOUTH-WEST PACIFIC)

(Submitted by R. Stringer)

SUMMARY AND PURPOSE OF DOCUMENT This document summarizes the current status of the GOS in Regions II and V.

ACTION PROPOSED

The meeting is invited to consider this document when preparing updates to the IP-EGOS.

____________

REVIEW OF PROGRESS AND ACTIONS CONCERNING

IP-EGOS IN REGIONS II AND V

Progress and Actions Concerning IP-EGOS in WMO Region II

(Information provided by Yongqing Chen, RA II Rapporteur on GOS)

An Implementation Plan for Surface-Based Sub-Systems of the GOS in RA II has been drafted based on the plan from RA I, but will be further modified before being sent to the secretariat.  The plan will also be submitted to the RA II WG on PIW, fifth session which will be held in third quarter 2007, for review. Finally it will be submitted to the next RA II session which will be held in the next year for approval.

The draft plan considers the following matters:

1.	At first, it should be studied what hurdles exist in member countries for the implementation of plan. Then the way to solve the problems should be analyzed.  This is a difficult task and the process is not yet finished.

2.	The plan will provide significant help for members to understand clearly their responsibilities in the implementation of the plan.

3.	Some regional programs and working groups can be set up to study the resolution to specific problems.

4.	The plan from RA II mainly comes from the Implementation Plan for Space and Surface-Based Sub-Systems of the GOS. I am not sure whether it is helpful for the members to just repeat the items from the Implementation Plan for Space and Surface-Based Sub-Systems of the GOS, however it is very difficult to find new solutions and this needs a group of experts to carry out the task.

Progress and Actions Concerning IP-EGOS in WMO Region V

It was decided to continue the Working Group on Planning and Implementation of the WWW in Region V (WG-PIW) at the Fourteenth Session of RA V held in May 2006.

Amongst the specific tasks identified for WG-PIW, the following is relevant:

“Integrated Observing System (IOS):  Develop a regional action plan for the evolution of the GOS which addresses Member needs and priorities, and which is integrated into the WMO plan for integrated observations.  Ensure the plan addresses:

(a)	Enhanced access to and utilization of a broader range of satellite data, through both direct reception and Advanced Dissemination Mechanisms such as SATAID and provision of appropriate training.  (HIGH PRIORITY).

(b)	Investigation of low cost lightning detection systems as a complementary observing tool, with particular benefit for countries without weather watch radar.  (HIGH PRIORITY).

(c)	Establishment of an affordable AMDAR programme for the Region to extend the coverage of aircraft reports over the region.”

The Chair of WG-PIW prepared a commentary, to help guide plans and actions within countries, on the parts of IP-EGOS with particular relevance to RA V as follows:

Space-based subsystem:

- Plans for more satellites and more instruments

- Geostationary and polar orbiting, both with soundings.

- Geostationary coverage over Indian Ocean.

- Microwave and hyperspectral IR.

- More frequent imagery.

- Global Precipitation measurements

NASA has extended TRMM until 2009 (from earlier intended date of 2004) but follow-up missions may not occur until 2012.

- Extension of wind measurements over the ocean

QuikScat will continue until 2008 but no replacement is planned. Scatterometer measurements are now available from the ASCAT instrument on the European operational polar orbiting series (METOP), launched October 2006.

(d)	Radio occultation soundings from measuring time delays in communications satellite signals. These offer the prospect improved upper tropospheric and stratospheric soundings, with improved analysis of jet streams. They are operational in UK Met Office.

## Surface-based sub-system

NMHSs are encouraged to enhance the network of surface-based observations where they can through:

- Distribution of observations

- Where observations are made more frequently than normal synoptic reporting hours these should also be exchanged on the GTS with a target of hourly observations where available.

- Exchanging data that may be available but is not currently exchanged on the GTS such as radar, local networks, high density precipitation networks; wave rider buoy data.

(b)	Timely radiosonde observations at full vertical resolution.

(c)	Maintaining baseline system especially upper winds in the tropics.

(d)	Investigation of the benefits of targeted observations (a THORPEX aim).

(e)	AMDAR

- New technologies for smaller aircraft.

- Humidity/water vapour sensors.

- Optimising of reporting.

(f)	Measurement of atmospheric moisture using ground-based GPS

- Tropical moorings

- These are being extended to Indian Ocean (improved seasonal prediction).

- Drifting buoys

- More will have pressure sensors.

- XBT and Argo floats

- These have demonstrated their value but need to be sustained.

- Automatic Weather Stations (AWS)

- Are being encouraged.

- Standards developed.

- CBS asked for improvements for those exposed to severe weather.

- Inexpensive lightning detection systems

- Several commercial systems for short range and long-range.

- European system could be extended globally for NMHS use.”

With respect to THORPEX, a Southern Hemisphere Regional Committee (SHRC) was formed and a Science Plan developed. A Southern Hemisphere THORPEX Implementation Plan is now at a draft stage.  The Committee has strong representation from RA V countries (Australia, New Zealand, Indonesia and Cook Islands).

The table (see next page) is a template to document the tasks required for implementation – with details as applies to Australia.

General issues regarding implementation:

- Are changes needed to Technical Regulations and Guides?

- National points of contact – it was intended that there be national points of contact for implementation of the IOS, recognising that most of the action falls under the responsibility of the NMHSs. Has this been followed up after CBS? Australia not received a letter inviting the nomination of such a focal point?

______________

# Table

# Implementation Plan for the Evolution of the Global Observing System – application to Australia

| Recommendation | Comment | Issues | Area of Responsibility | Tasks |
| --- | --- | --- | --- | --- |
| G1 Distribution |  |  |  |  |
| a. hourly distribution of observations where available | technically feasible from AWS already more sent than RBSN (see Volume C) 1 minute AWS on WIS SIMDAT prototype are global centres using METAR? even greater flexibility with Next Generation AWS | some limits in SYNOP code? CMSS already transmits surface observations in BUFR, in parallel with SYNOP messages restrictions on use of METAR outside of aviation, but international METARs are exchanged on GTS | OEB CCSB (W Qu/SRRT) Coordinator: SRRT | Provide list of all stations transmitted on GTS and how this compares with RBSN (SRRT) Distribute hourly from all AWS in BUFR |
| b. exchange of potentially valuable data not currently exchanged: |  |  |  |  |
| (i) radar (reflectivity, radial winds) | 60 stations (approx.) available with radial winds from 3 stations (and growing) but in an internal format. Could potentially provide some data from other countries (Fiji, etc.) | Only want calibrated data? Format (BUFR?) Frequency Which stations? Volumetric data or PPI composite? Urgency, priority for making data available | STNM CCSB (W Qu/SRRT) Coordinator: STNM/SRRT | Needs specification: STNM to obtain advice from ET EGOS (based on European experience) |
| (ii) meso-networks | Data already switched if it has a WMO number – even if not in RBSN any available stations without WMO number? |  | STNM | Action covered under G1 ? |
| (iii) soil temp and moisture | Available from manual observing sites but need to move to BUFR before they can be encoded |  | STNM CCSB (W Qu/SRRT) Coordinator: SRRT | Include when enhanced surface observations are transmitted in BUFR (rather than merely BUFR version of SYNOP as is current practice) |
| (iv) high density precipitation networks | much rainfall data available from hydro networks, but in local code forms | All required? If so – daily, hourly, event? (many flood networks are event-driven) Some issues on ownership of data no WMO number for many stations – need to migrate to BUFR with lat/lon – adequate? | STNM/STHY | Needs some specification: STNM to obtain advice from ET EGOS (based on European experience) |
| (v) wave rider buoy data | Reports already sent for 15 buoys around the Australian coast (2 operated by the Bureau of Meteorology and 13 by state agencies) in WAVEOB (MMXX) format | need to migrate to BUFR | SROD and W Qu (for migration to BUFR) | STNM to advise ET of data availability Add to list of codes for migration to BUFR – target March 2008 |
| c. metadata | needs specification if requirements go beyond what is specified in Vol A, etc. |  |  | STNM to seek advice from ET EGOS |
| G2 Documentation | As for G1 (c) unclear what is required here |  |  | STNM to seek advice from ET EGOS |
| G3 Timeliness and Completeness |  |  |  |  |
| (a)Full resolution radiosonde soundings | 10 second information available in EDT (proprietary Vaisala format) – needs work before fully operational, but potentially possible would be useful domestically | need encoding in BUFR with all the additional information requested (such as position of each data point,..) Can be provided directly from Vaisala equipment? | STNM CCSB (W Qu/SRRT) Coordinator: STNM/SRRT | Transmit current TEMP/PILOT in BUFR by November 2007 A later phase - transmit full resolution and detailed radiosonde reports in BUFR Target? |
| (b) Timely receipt of drifting buoy data? | Any action for Australia? |  |  |  |
| G4 Baseline System | Will do what we can given resource constraints Special effort to maintain GSN and GUAN Will consider impact on tropical wind measurements in network changes |  |  |  |
| G5 Stratospheric observations | Will attempt to maintain commitment for GUAN stations (to 5 hPa) as a priority, other radiosondes to stratospheric levels under routine program |  | OEB |  |
| G6 Ozone sondes | Available in near real-time Need to be encoded in BUFR | ECMWF have requested these data but require it in BUFR format Could also encode data on behalf of NZ? | STNM CCSB (W Qu/SRRT) Coordinator: STNM/SRRT | Add to list for migration to BUFR |
| G7 Targeted observations | Still a research topic, principally in THORPEX |  |  |  |
| G8 Optimization of RAOBs | Not applicable in Australia |  |  |  |
| G9 AMDAR | Australia operates a very successful program An RA V program developed to which Australia will contribute (details from Technical Coordinator – M Bercheree) | Optimising the reporting from popular airports and routes Monitoring development of humidity sensors Data only in AMDAR format not BUFR | STNM | Encode aircraft reports in BUFR as well as AMDAR Target? Update on RA V plan (M Bercheree) |
| G13 Ground-based GPS | Progress in establishing some stations expected in the 2007/8 financial year. Data will be disseminated on the GTS when available | Encoding of data when available | STNM CCSB (W Qu/SRRT) Coordinator: STNM | Encode GPS water vapour measurements in BUFR when available and transmit on GTS Target? |
| G14 More profiles over oceans | No plans |  |  |  |
| G15 Improvements in marine observations telecommunications | Not applicable – apart from encoding XBT data in BUFR |  | OEB and CSIRO CCSB (SRRT) Coordinator: STNM | encode XBT data in BUFR Target? |
| G16 Tropical moorings | No plans |  |  |  |
| G17 Drifting buoys | Australia maintains a drifting buoy program; all buoys have pressure sensors |  |  |  |
| G18 XBT and Argo | Australia contributes as resources permit |  |  |  |
| G19 Ice buoys | No plans |  |  |  |
| G20 More profiles in tropics | Will consider in any changes to network |  | OEB |  |
| G21 AWS | Australia maintains an extensive network. | Metadata requirements need specifying Data need to be encoded into BUFR or CREX (see G1) | OEB, CCSB | STNM to obtain information from ET-AWS Need to migrate to BUFR (as in G1) |
| G22 New systems |  |  |  |  |
| (a) wind profilers | Australia now operates several of these Encoding to BUFR from local AXF format ready completed but not used | Data are not transmitted internationally, but in principle could be. Some issues: Format, frequency of reporting, number of vertical levels? | STNM CCSB (W Qu/SRRT) Coordinator: STNM/SRRT | Encode available reports in BUFR and transmit Target? |
| (b) sea level observations | Any requirement for tide gauge or DART buoy data? | Australia sends 1 minute data every 3 minutes in CREX format on the GTS for 24 stations (Indian and Pacific Oceans, and Australia) Bureau has deployed one DART buoy so far; data transmitted on the GTS in a proprietary format. Need to develop CREX tables for deep ocean buoy (DART) data | Kelvin Wong | STNM to ask ET if such data are included as part of the evolution of the GOS |
| (c) lightning detection systems | Some systems are operational Consideration of contribution to a UK initiative for a global system investigation of PC-based options | Investigation of cost effective lightning detection system was a priority for RA V |  | OEB (SRPP?) to prepare a short summary of options available with a broad indication of costs. Target: September 2007? |

___________________