| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON EVOLUTION OF THE GLOBAL OBSERVING SYSTEM THIRD SESSION GENEVA, SWITZERLAND, 9–13 JULY 2007 |  | CBS/OPAG-IOS/ET-EGOS-3/Doc. 9.5.1 (26.VI.2007) _______ ITEM: 9.5 Original: ENGLISH |
| --- | --- | --- |

REVIEW PLANS FOR PREPARATION OF REVISED VISION FOR THE GOS

(Submitted by Messrs J. Eyre and A. Karpov)

SUMMARY AND PURPOSE OF DOCUMENT This document presents a brief overview of the current vision for the GOS in 2015, as given in an annex to the EGOS-IP.

ACTION PROPOSED

The meeting is invited to note the information contained in this document when preparing its revised Vision for the GOS in 2025.

_______________

VISION FOR THE GOS in 2015

In drafting the recommendations for an evolved GOS and then the Implementation Plan, the ET was guided by the following vision for the GOS in 2015 and beyond, as adopted by CBS (CBS Extr., Cairns, 1-12 December 2002).

For the space-based sub-system, there would be:

6 operational GEOs

• all with multi-spectral imager (IR/VIS)

• some with hyper-spectral sounder (IR)

4 operational LEOs

• optimally spaced in time

• all with multi-spectral imager (MW/IR/VIS/UV)

• all with sounder (MW)

• three with hyper-spectral sounder (IR)

• all with radio occultation (RO)

• two with altimeter

• three with conical scan MW or scatterometer

Several R&D satellites serving WMO members

• constellation of small satellites for radio occultation (RO)

• LEO with wind lidar

• LEO with active and passive microwave precipitation instruments

• LEO and GEO with advanced hyper-spectral capabilities

• GEO lightning

• possibly GEO microwave

All with improved inter-calibration and operational continuity.

For the surface-based sub-system, there would be:

Automation to enable

• targeting of observations in data sensitive areas

• optimal operation of

o radiosondes

o ASAP systems

o aircraft in flight

Radiosondes

• optimized utilization

• stable and functioning RBSN, RBCN and GUAN

• supplemented by

o AMDAR ascent/descent

o ground-based GPS water vapour information

o wind profilers

o satellite soundings

• automatically launched

• computerized data processing

• real-time data transmission

• high vertical resolution

Commercial aircraft observations

• of temperature & wind plus humidity on some aircraft

• In-flight and ascent/descent data

• high temporal resolution

• available from most airports including currently data void airports in Asia, Africa and South America.

• possibly supplemented with UAVs

Surface observations

• stable and functioning RBSN, RBCN and GSN

• automated systems

• land sensors at high spatial resolution, supporting local applications such as road

weather

• ocean platforms (ship, buoys, profiling floats, moorings) in adequate number to complement satellite measurements

Radar observing systems measuring

• radial winds

• hydrometeor distribution and size

• precipitation phase, rate, and accumulation

• multiple cloud layers, including base and top height

Data collection and transmission

• digital in a highly compressed form

• entirely computerized data processing

• role of humans in observing chain reduced to minimum

• information technology in all areas of life will provide new opportunities for obtaining

and communicating observations

• for satellite data in particular

- use of ADM including regional/special DCPC in the context of FWIS

- DB for special local applications in need on minimal time delay and backup

__________________