| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON EVOLUTION OF THE GLOBAL OBSERVING SYSTEM THIRD SESSION GENEVA, SWITZERLAND, 9–13 JULY 2007 |  | CBS/OPAG-IOS/ET-EGOS-3/Doc. 9.5.2 (4.VII.2007) _______ ITEM: 9.5 Original: ENGLISH |
| --- | --- | --- |

REVIEW PLANS FOR PREPARATION OF REVISED VISION FOR THE GOS

(Submitted by the WMO Space Programme)

SUMMARY AND PURPOSE OF DOCUMENT This document includes a gap analysis that was performed as an input to the Workshop on Re-design and Optimization of the Space-based GOS on 21 and 22 June 2007.

ACTION PROPOSED

The meeting is invited to take note of the document and to consider the recommendations put forward as conclusion of the gap analysis for each mission.

__________________

Appendix:	Gap Analysis input to the Workshop on Re-design and Optimization of the Space-based Component of GOS

It presents the status of planning for the space-based component of GOS.  For each type, in a typology of 29 instruments/missions, the document records:

- definition of “nominal” instrument characteristics;

- addressed geophysical parameters;

- assumed/suggested observing strategy;

- current and planned programmes until year 2020;

- comments on the situation as projected beyond 2020;

- recommendations.

A synoptic table of geophysical parameters (127) versus instrument/mission types (29) is provided in Annex 1 to the Appendix.

In Annex 2 to the Appendix, for each instrument mentioned in the main text (157), a descriptive table is provided.  The nominal level of update is, for most programmes, September 2006, i.e. what was contained in the yearly report on the status of GOS presented at CGMS-34.  However, follow-on developments that affected the scenario have been taken into account to the best of our knowledge.

Gap Analysis input to the Workshop on Re-design and Optimization of the Space-based Component of GOS

INDEX

Explanations

1.	Multi-purpose VIS/IR imagery from LEO

2.	Multi-purpose VIS/IR imagery from GEO

3.	IR temperature/humidity sounding from LEO

4.	IR temperature/humidity sounding from GEO

5.	MW temperature/humidity sounding from LEO

6.	MW temperature/humidity sounding from GEO

7.	Conical-scanning MW imagery (intermediate frequencies)

8.	Low-frequency MW imagery

9.	Radio occultation sounding

10.	Earth radiation budget from LEO

11.	Earth radiation budget from GEO

12.	Wind scatterometry

13.	Radar altimetry

14.	Ocean colour imagery from LEO

15.	Ocean colour imagery from GEO

16.	Imagery with special viewing geometry

17.	Lightning imagery from LEO

18.	Lightning imagery from GEO

19.	Cloud and precipitation radar

20.	Lidar-based missions (for wind, for cloud/aerosol, for water vapour, for altimetry)

21.	Cross-nadir short-wave spectrometry (for chemistry) from LEO

22.	Cross-nadir short-wave spectrometry (for chemistry) from GEO

23.	Cross-nadir IR spectrometry (for chemistry) from LEO

24.	Cross-nadir IR spectrometry (for chemistry) from GEO

25.	Limb-sounding short-wave spectrometry

26.	Limb-sounding IR spectrometry

27.	Limb-sounding Sub-millimetre wave spectrometry

28.	High-resolution short-wave imagery for land observation

29.	Synthetic Aperture Radar

Synoptic table of geophysical parameters (127) versus instrument types (29)

Annex 1: Plotting board of geophysical parameters v/s remote sensing techniques

Annex 2: Information on satellites and instruments

- List of all satellites mentioned in the text

- List of all instruments mentioned in the text (with deployment of acronyms)

- Descriptive tables for each current or planned instrument mentioned in the text

Explanations

This Gap analysis is intended to collect information as “factual” as possible, to provide the rationale for orienting the development of the satellite-based component of GOS.

Missions/instruments are selected on the basis of established heritage, consolidated plans or, at least, demonstrated or being demonstrated concepts.

For each mission/instrument, generic characteristics are defined, so as to encompass most of what is currently considered desirable and feasible (not necessarily affordable) for the post-2020 timeframe.

A list of geophysical parameters that could be potentially retrieved from the mission/instrument of specified reference characteristics is provided.  The achievable data quality will be evaluated in a dedicated study to be performed for WMO by the end of 2007.

For each mission/instrument, an observing strategy is recommended, as follows:

- For missions/instruments in GEO the observing strategy is simply the most recent one adopted by WMO (6 regularly-spaced stationarity longitudes, plus adequate contingency).  The perspective situation for post-2020 shows that this strategy can be implemented.

- For the missions/instruments in LEO presumably to be flown on the backbone operational meteorological satellite system, the WMO requirement is “4 satellites in optimally spaced orbital planes”.  When the system was implemented by two NOAA satellites, the orbital planes were around 7:30 and 13:30 LST (at the equatorial crossing node).  Moving to four satellites, the other two should have been added around 10:30 and 16:30 LST.  However, when EUMETSAT entered the scenario, they selected 9:30 LST as optimal for Europe, whereas 13:30 LST was optimal for the USA (these two orbits serve East-Atlantic and East-Pacific respectively around 12 UTC, optimal for merging with conventional observations at the main synoptic hours).  With the advent of four-dimensional assimilation these motivations are no longer valid, but at that time they fixed the scenario, presumably still for a long time to come. With 9:30 and 13:30 as baseline, the optimal third orbital plane becomes 5:30 that also coincides with the peak of activity of meteorological services in the early morning.  This situation based on three orbital planes 4-hour dephased is difficult to be shifted to a four orbital planes 3-hour dephased.  It is preferable to stay with the three orbital planes configuration and provide for contingency in each orbital plane.

- For a number of missions in LEO, global coverage at 4-hour intervals is not requested.  Depending on the type of observation and the need for synergies, the strategy indicates:

  - in which of the orbital planes of the backbone system the mission should be flown;

  - whether the mission can be flown in other orbits, independent of the backbone system.

- There are cases when the observing strategy indicates the need for dedicated constellations.

The gap analysis follows.  It is differentiated by orbital planes and by class of the instrument as compared with the characteristics of the reference mission/instrument.  The main features of each instrument are recorded, and the instrument class as compared with the reference instrument is indicated by a coded colour.

A list of comments follows, differentiated by orbital planes.  The comments focus on the expected situation in year 2020 and compare with the stated observing strategy.  Contingency aspects in each orbital plane are considered.

Finally, a number of recommendations are proposed.  It is noted that these recommendations directly derive from the “factual” information collected in the document, and involve as little as possible subjective elements such as priorities, affordability and sustainability.  Therefore, the set of recommendations constitute only a background on which to build the overall recommendations stemming from the discussions in the Optimization Workshop.

1.	MULTI-PURPOSE VIS/IR IMAGERY FROM LEO

This mission is implemented by medium-resolution multi-channel radiometers operating in the VIS and IR parts of the spectrum.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of multi-purpose VIS/IR imagers in LEO (years 2020’s) |
| --- |
| Spectral range | Bandwidths | No. of channels | Typical SNR or NE(T | Resolution | Swath | Scanning |
| ~ 0.4 to ~14 (m | 0.02-1.0 (m | 5-40 | 50 @ 1 % albedo, 0.1 K @ 300 K | 0.3-1.0 km | > 2800 km | cross-track |

Addressed products are as follows.

| Geophysical parameters addressed by the multi-purpose VIS/IR imagery mission in LEO |
| --- |
| Cloud imagery | Total aerosol optical depth | Snow cover |
| Cloud cover | Total aerosol type | Snow surface temperature |
| Cloud type | Short-wave cloud reflectance | Snow albedo |
| Cloud optical depth | Downwelling SW irradiance at Earth’s surface | Frozen soil and permafrost |
| Cloud top height | Earth’s surface albedo | Leaf Area Index (LAI) |
| Cloud top temperature | Surface emissivity in TIR window channels | Normalized Difference Vegetation Index (NDVI) |
| Cloud drop effective radius at cloud top | Sea surface temperature | Photosynthetically Active Radiation (PAR) |
| Cloud ice effective radius at cloud top | Sea-ice surface temperature | Fractional Absorbed PAR (FAPAR) |
| Water vapour imagery | Sea-ice cover | Fire temperature |
| Water vapour total column | Land surface temperature | Fire fractional cover |
| Precipitation at surface (index) | Surface soil moisture (index) | Fire radiative power |

The recommended observing strategy is:

- three orbital planes (early morning: 5:30 ( 2 h;  mid-morning: 9:30 ( 2 h;  early afternoon: 13:30 ( 2 h);

- one fully compliant instrument in each plane, and one backup, as similar as possible.

The evolution of current and planned Multi-purpose VIS/IR imagers in LEO is shown below.

| Instrument class | ( 10 channels | Channels not optimal | High quality | Quality exceeding requirements |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| VIIRS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| MVISR | FY-1D | 08:20 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| AVHRR/3 | MetOp 1-3 | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| VIRR+MERSI | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| AVHRR/3 | NOAA-17 | 10:20 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| MSU-MR | Meteor-M 1&2 | 10:20 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| MODIS | EOS-Terra | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| MODIS | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| VIIRS | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| VIIRS | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X |
| AVHRR/3 | NOAA 18 | 13:40 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| AVHRR/3 | NOAA-19 | 14:00 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| VIRR+MERSI | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |
| VIRS | TRMM | 35° | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of multi-purpose VIS/IR imagers in LEO |
| --- |
| Feature | NPOESS VIIRS | NOAA & MetOp AVHHR | FY-1D MVISR | FY-3 VIRR+MERSI | Meteor-M MSU-MR | Terra & Aqua MODIS |
| No. of SW channels (0.4-2.4 (m) | 15 | 3 | 7 | 26 | 3 | 20 |
| No. of LW channels (3.5-15 (m) | 7 | 3 | 3 | 4 | 3 | 16 |
| Typical SW bandwidths | 20-60 nm | 100 nm | 50-100 nm | 20-50 nm | 200 nm | 10-30 nm |
| Typical LW bandwidths | 0.2-1.0 (m | 0.4-1.0 (m | 0.4-1.0 (m | 0.4-1.0 (m | 0.6-1.0 (m | 0.1-0.5 (m |
| Swath | 3000 km | 2900 km | 2800 | 2800 km | 3000 km | 2330 km |
| IFOV | 0.4 and 0.8 km | 1.1 km | 1.1 km | 0.25 and 1.0 km | 1.0 km | 0.25, 0.5 and 1.0 km |

Comments (with focus on the post-2020 range):

- In the early morning time slot, there will be no coverage until 2016 (NPOESS-2).  The instrument thereafter available, VIIRS, provides high quality data.  There will be no backup.

- In the mid-morning time slot, the MetOp AVHRR does not meet post-2020 quality requirements.  The FY-3 instrument complex (VIRR + MERSI) apparently meets but, going to details, the IR channels are defective (same as AVHRR on VIRR, none on MERSI): it would be a good backup.  However, a high-quality VIS/IR imager is not yet committed.

- In the early afternoon time slot, the post-2020 requirements will be met by VIIRS on NPOESS.  VIRR + MERSI on FY-3 would be a good backup.

Recommendations:

- In the early morning: to add a redundant VIS/IR imager, possibly of the class of VIIRS, or at least of the class of VIRR + MERSI.

- In the mid-morning time: to provide a high-quality VIS/IR imager, presumably on the follow-on of MetOp/EPS.  The FY-3 instrument complex (VIRR + MERSI) should possibly be upgraded to VIIRS level to provide full redundancy.

- In the early afternoon: to possibly upgrade VIRR + MERSI to VIIRS level to provide full redundancy.

2.	MULTI-PURPOSE VIS/IR IMAGERY FROM GEO

This mission is implemented by medium-resolution multi-channel radiometers operating in the VIS and IR parts of the spectrum.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of multi-purpose VIS/IR imagers in GEO (years 2020’s) |
| --- |
| Spectral range | Bandwidths | No. of channels | Typical SNR or NE(T | Resolution | Observing cycle |
| ~ 0.4 to ~14 (m | 0.03-1.0 (m | 5-20 | 30 @ 1 % albedo, 0.1 K @ 300 K | 0.5-2.0 km | < 15 min (full disk), less for limited areas |

Addressed products are as follows (same as from LEO, with possibly some lower quality, but much more frequently; plus winds from cloud and water vapour tracking).

| Geophysical parameters addressed by the multi-purpose VIS/IR imagery mission in GEO |
| --- |
| Cloud imagery (and derived wind) | Total aerosol optical depth | Snow cover |
| Cloud cover | Total aerosol type | Snow surface temperature |
| Cloud type | Short-wave cloud reflectance | Snow albedo |
| Cloud optical depth | Downwelling SW irradiance at Earth’s surface | Frozen soil and permafrost |
| Cloud top height | Earth’s surface albedo | Leaf Area Index (LAI) |
| Cloud top temperature | Surface emissivity in TIR window channels | Normalized Difference Vegetation Index (NDVI) |
| Cloud drop effective radius at cloud top | Sea surface temperature | Photosynthetically Active Radiation (PAR) |
| Cloud ice effective radius at cloud top | Sea-ice surface temperature | Fractional Absorbed PAR (FAPAR) |
| Water vapour imagery (and derived wind) | Sea-ice cover | Fire temperature |
| Water vapour total column | Land surface temperature | Fire fractional cover |
| Precipitation at surface (index) | Surface soil moisture (index) | Fire radiative power |

The recommended observing strategy is:

- six sectors, 60 degrees wide along the equator (centres: 0°, 60°E, 120°E, 180°E, 120°W, 60°W);

- at least one “SEVIRI-like” instrument in each sector, and one backup, as similar as possible.

The evolution of current and planned Multi-purpose VIS/IR imagers in GEO is shown below.

| Instrument class | < 5 channels | GOES IMAGER-like | State-of-art | Advanced generation |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SEVIRI | Meteosat 8-11 | 0° | X | X | X | X | X | X | X | X | X | X | X | X | X |  |  |
| FCI | Meteosat 12( | 0° |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| MSU-GS | Elektro-L 2 | 14.5°E |  |  |  | X | X | X | X | X | X | X | X |  |  |  |  |
| MVIRI | Meteosat-7 | 57°E | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| VHRR | Kalpana-1 | 74°E | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| MSU-GS | Elektro-L 1 & 3 | 76°E | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| IMAGER | INSAT-3D | 83°E | X | X | X | X | X | X | X | X |  |  |  |  |  |  |  |
| S-VISSR | FY-2 D & F | 86.5°E | X | X | X | X | X | X | X | X | X | X |  |  |  |  |  |
| MCSI (TBD) | FY-4 O/A( | 86.5°E |  |  |  |  |  | X | X | X | X | X | X | X | X | X | X |
| VHRR + CCD | INSAT-3A | 93.5°E | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| S-VISSR | FY-2 E & G | 123°E |  |  | X | X | X | X | X | X | X | X | X | X |  |  |  |
| MCSI (TBD) | FY-4 O/B( | 123°E |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| MI | COMS-1 | 128°E |  | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| Imager TBD | COMS-2 | 128°E |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |
| JAMI/IMAGER | MTSAT 1R & 2 | 140°E | X | X | X | X | X | X | X | X | X | X |  |  |  |  |  |
| Imager TBD | MTSAT 3( | 140°E |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| IMAGER | GOES-11/13/15 | 135°W | X | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| ABI | GOES-17 | 135°W |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X |
| IMAGER | GOES-12/14 | 75°W | X | X | X | X | X | X | X | X |  |  |  |  |  |  |  |
| ABI | GOES-16 (R) | 75°W |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |
| IMAGER | GOES-10 | 60°W | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of multi-purpose VIS/IR imagers in GEO |
| --- |
| Feature | Meteosat MVIRI | Meteosat SEVIRI | Meteosat FCI | GOES IMAGER | GOES ABI | Elektro-L MSU-GS | INSAT-3A VHRR+CCD | INSAT-3D IMAGER | Kalpana VHRR | FY-2 S-VISSR | COMS MI | MTSAT JAMI |
| Channels | 3 | 12 | 16 | 5 | 16 | 10 | 3 + 3 | 6 | 3 | 5 | 5 | 5 |
| Cycle | 30 min | 15 min | 2.5 & 10 min | 30 min | 15 min | 15 min | 180 min | 30 min | 180 min | 30 min | 30 min | 30 min |
| IFOV VIS | 2.5 km | 1 & 3 km | 0.5 & 1 km | 1 km | 0.5 & 1 km | 1 km | 1 & 2 km | 1 km | 2 km | 1.25 km | 1 km | 1 km |
| IFOV IR | 5.0 km | 3 km | 1 & 2 km | 4 km | 2 km | 4 km | 8 km | 4 & 8 km | 8 km | 5 km | 4 km | 4 km |

Comments (with focus on the post-2020 range):

- Sector 30°W-30°E: the Meteosat 3rd Generation FCI will meet post-2020 requirements, and backed by hot standby.

- Sector 30-90°E: the FY-4 O imager is being designed to meet post-2020 requirements.  The Elektro-L MSU-GS is already at SEVIRI level, and could be upgraded to meet post-2020 requirements.

- Sector 90-150°E: the FY-4 O imager is being designed to meet post-2020 requirements.  MTSAT-3 and follow-on have been announced to be upgraded to SEVIRI level.  The imager being defined for COMS-2 could be upgraded to SEVIRI level.

- Sector 150°E-150°W: nothing is planned.

- Sector 90-150°W: the GOES ABI (following GOES-R) meets post-2020 requirements.  It is backed by a standby GOES satellite at 105°W also backing GOES-E.

- Sector 30-90°W: the GOES-R ABI meets post-2020 requirements.  It is backed by a standby GOES satellite at 105°W also backing GOES-W.

Recommendations:

- The total gap in the Sector 180° ( 30° (Central Pacific Ocean) should be filled, at least to the extent necessary to provide winds by tracking cloud and water vapour patches.  An imager of the current GOES/IMAGER class, and another for redundancy, could be sufficient for this purpose (this could be achieved by means of spare satellites of the previous generation).

- In Sector 90-150°E, either COMS-2 or MTSAT-3 or both, currently being defined in respect of the VIR/IR imagery mission, should consider aiming at FCI/ABI level rather then to SEVIRI since, at the time of their expected launch (2014), the state-of-art of imagery from GEO will be fixed by the GOES-R ABI and the Meteosat 3rd Generation FCI, and also FY-4 O will have an advanced imager.

3.	IR TEMPERATURE/HUMIDITY SOUNDING FROM LEO

This mission is implemented by medium spectral resolution spectrometers or radiometers operating in the IR part of the spectrum.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of IR temperature/humidity sounders in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical NE(T | Resolution | Swath | Scanning |
| 3.6 to 16 µm | 0.25-0.5 cm-1 | 4000-8000 | 0.2 K @ 280 K | 4-12 km | > 2200 km | cross-track |

Addressed products are as follows.

| Geophysical parameters addressed by the IR temperature/humidity sounding mission in LEO |
| --- |
| Air temperature profile | Cloud cover profile | Sea surface temperature | NO2 total column |
| Water vapour profile | Cloud top height | Land surface temperature | CH4 total column |
| Water vapour total column | Cloud top temperature | O3 profile | CO2 total column |
| Height of the tropopause | Downwelling LW irradiance at Earth’s surface | O3 total column | CO total column |
| Height of the top of the PBL | Surface emissivity in TIR window channels | HNO3 total column | SO2 total column |

The recommended observing strategy is:

- three orbital planes (early morning: 5:30 ( 2 h;  mid-morning: 9:30 ( 2 h;  early afternoon: 13:30 ( 2 h);

- one fully compliant instrument in each plane, and one backup, as similar as possible.

The evolution of current and planned IR sounders in LEO is shown below.

| Instrument class | IR radiometer | IR spectrometer |
| --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CrIS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) |
| IASI | MetOp 1-3 | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| IRAS | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| HIRS | NOAA-17 | 10:20 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| IRFS-2 | Meteor-M2 | 10:20 |  | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| AIRS | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| CrIS | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| CrIS | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X |
| HIRS | NOAA 18 | 13:40 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| HIRS | NOAA-19 | 14:00 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| IRAS | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |

| Comparative characteristics of IR temperature/humidity sounders in LEO |
| --- |
| Feature | NPOESS CrIS | NOAA HIRS | MetOp IASI | FY-3 IRAS | Meteor-M IRFS | EOS-Aqua AIRS |
| No. of channels | 1300 | 20 | 8461 | 26 | 4000 | 2378 |
| Spectral resolution | 0.625-2.5 cm-1 | 10-20 cm-1 | 0.25 cm-1 | 10-20 cm-1 | 0.5 cm-1 | 0.5-2.0 cm-1 |
| Swath | 2230 km | 2200 km | 2230 km | 2250 km | 2500 km | 1650 km |
| IFOV | 14 km | 10 or 18 km | 12 km | 17 km | 35 km | 13.5 km |

Comments (with focus on the post-2020 range):

- In the early morning time slot, there will be no coverage until 2016 (NPOESS-2).  The instrument thereafter available, CrIS, would provide high quality data: but currently in not in the baseline.  Also, no backup is currently foreseen.

- In the mid-morning time slot, an instrument such as the MetOp IASI would meet the post-2020 quality requirements, but is not yet committed.  The FY-3 instrument, IRAS, would provide partial backup.

- In the early afternoon time slot, the post-2020 requirements will be met by CrIS on NPOESS.  IRAS on FY-3 would be a partial backup.

Recommendations:

- In the early morning: to baseline CrIS on NPOESS-2, and possibly add a backup sounder on another platform.

- In the mid-morning time: to continue with a high-quality sounding interferometer on the follow-on of MetOp/EPS.  The FY-3 instrument, IRAS, should possibly be upgraded to IASI level to provide full redundancy.

- In the early afternoon: to possibly upgrade IRAS to CrIS level to provide full redundancy.

4.	IR TEMPERATURE/HUMIDITY SOUNDING FROM GEO

This mission is implemented by medium spectral resolution spectrometers or radiometers operating in the IR part of the spectrum.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of IR temperature/humidity sounders in GEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical NE(T | Resolution | Observing cycle |
| 3.6 to 16 µm | 0.25-0.5 cm-1 | 4000-8000 | 0.2 K @ 280 K | 4-8 km | < 30 min (full disk), less for limited areas |

Addressed products are as follows (same as from LEO, with possibly somewhat lower quality, but much more frequently; plus wind profile from water vapour tracking).

| Geophysical parameters addressed by the IR temperature/humidity sounding mission in GEO |
| --- |
| Air temperature profile | Cloud cover profile | Sea surface temperature | NO2 total column |
| Water vapour profile (and derived wind profile) | Cloud top height | Land surface temperature | CH4 total column |
| Water vapour total column | Cloud top temperature | O3 profile | CO2 total column |
| Height of the tropopause | Downwelling LW irradiance at Earth’s surface | O3 total column | CO total column |
| Height of the top of the PBL | Surface emissivity in TIR window channels | HNO3 total column | SO2 total column |

The recommended observing strategy is:

- six sectors, 60 degrees wide along the equator (centres: 0°, 60°E, 120°E, 180°E, 120°W, 60°W)

- at least one hyperspectral instrument in each sector, and one backup, as similar as possible.

The evolution of current and planned IR sounders in GEO is shown below.

| Instrument class | Radiometer | Spectrometer |
| --- | --- | --- |

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IRS | Meteosat 12( | 0° |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| SOUNDER | INSAT-3D | 83°E | X | X | X | X | X | X | X | X |  |  |  |  |  |  |  |
| IIS TBD | FY-4 O/A( | 86.5°E |  |  |  |  |  | X | X | X | X | X | X | X | X | X | X |
| IIS TBD | FY-4 O/B( | 123°E |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| Sounder TBD | MTSAT 3( | 140°E |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SOUNDER | GOES-11/13/15 | 135°W | X | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| HES | GOES-17 | 135°W |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
| SOUNDER | GOES-12/14 | 75°W | X | X | X | X | X | X | X | X |  |  |  |  |  |  |  |
| HES | GOES-16 (R) | 75°W |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
| SOUNDER | GOES-10 | 60°W | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of IR temperature/humidity sounders in GEO |
| --- |
| Feature | Meteosat 3rd Generation IRS | GOES up to 15 SOUNDER | GOES-R HES | INSAT-3D SOUNDER |
| Range | 4.6-14.3 (m | 3.74-14.71 (m + 0.7 (m | 3.68-15.4 (m | 3.74-14.71 (m + 0.7 (m |
| Channels | 1736 | 18 (IR) + 1 (VIS) | 1508 | 18 (IR) + 1 (VIS) |
| Spectral resolution | 0.625 cm-1 | 13 to 100 cm-1 | 0.5 to 2.5 cm-1 | 13 to 100 cm-1 |
| Cycle (full disk) | 30 min | 8 h | 60 min | 8 h |
| IFOV IR | 4 km | 8 km | 2-20 km | 10 km |

Comments (with focus on the post-2020 range):

- Sector 30°W-30°E: the Meteosat 3rd Generation IRS will meet post-2020 requirements.  In this specific moment it is not sure that the IRS payload will have a backup in hot standby.

- Sector 30-90°E: the FY-4 O sounder is being designed to meet post-2020 requirements.  The backup policy for FY-4 O satellites is to have two satellites, one at 86.5°E, and one at 123° E.

- Sector 90-150°E: the FY-4 O imager is being designed to meet post-2020 requirements.  The backup is at 86.5°E.  MTSAT-3 also is announced to be compliant with post-2020 requirements.

- Sector 150°E-150°W: nothing is planned.

- Sector 90-150°W: the GOES HES (following GOES-R) would meet post-2020 requirements.  It would be backed by a standby GOES satellite at 105°W also backing GOES-E.  However, HES on GOES-R is currently not baselined.

- Sector 30-90°W: the GOES HES (following GOES-R) would meet post-2020 requirements.  It would be backed by a standby GOES satellite at 105°W also backing GOES-W.  However, HES on GOES-R is currently not baselined.

Recommendations:

- The most important problem is the confirmation of HES on GOES-R and follow-on.  Without that, three consecutive Sectors, 150°E-150°W + 90-150°W + 30-90°W, i.e. half of the total coverage from GEO, would have no sounder, that implies not only missing temperature/humidity profiles (that in some way are provided by LEO satellites), but also wind profile that is derived from frequent humidity profiling.

- Assuming that HES on GOES is finally confirmed, the problem of Sector 150°E-150-W should be addressed.

- In Sector 30°W-30°E, the hot-standby policy of Meteosat should be extended to the IRS mission.

5.	MW TEMPERATURE/HUMIDITY SOUNDING FROM LEO

This mission is implemented by MW radiometers supporting the IR sounder for nearly-all-weather conditions.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of MW temperature/humidity sounders in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical NE(T | Resolution | Swath | Scanning |
| 23 to 200 GHz | 10-4000 MHz | ~ 30 | 0.2 to 1.0 K | 10-50 km | > 2200 km | cross-track |

Addressed products are as follows.

| Geophysical parameters addressed by the MW temperature/humidity sounding mission in LEO |
| --- |
| Air temperature profile (nearly-all-weather) | Downwelling LW irradiance at Earth’s surface | Cloud liquid water total column |
| Water vapour profile (nearly-all-weather) | Freezing level height in clouds | Cloud ice total column |
| Water vapour total column (nearly-all-weather) | Melting layer depth in clouds | Precipitation rate at surface |

The recommended observing strategy is:

- three orbital planes (early morning: 5:30 ( 2 h;  mid-morning: 9:30 ( 2 h;  early afternoon: 13:30 ( 2 h);

- one fully compliant instrument in each plane, and one backup, as similar as possible.

The evolution of current and planned MW sounders in LEO is shown below.

| Instrument class | Water vapour only | MSU-like | AMSU-like, but conical scanning | AMSU-like |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ATMS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) |
| AMSU-A+MHS | MetOp 1-3 | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| MWTS+MWHS | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| AMSU-A+AMSU-B | NOAA-17 | 10:20 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| MTVZA | Meteor-M 1&2 | 10:20 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| AMSU-A+HSB | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| ATMS | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| ATMS | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X |
| AMSU-A+MHS | NOAA 18 | 13:40 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| AMSU-A+MHS | NOAA-19 | 14:00 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| MWTS+MWHS | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |
| SAPHIR | Megha-Tropiques | 20° |  |  |  | X | X | X | X | X |  |  |  |  |  |  |  |

| Comparative characteristics of MW temperature/humidity sounders in LEO |
| --- |
| Feature | NPOESS ATMS | NOAA & MetOp AMSU-A + AMSU-B or MHS | FY-3 MWTS+MWHS | Meteor-M MTVZA | EOS-Aqua AMSU-A + HSB |
| No. of channels | 22 | 15 + 5 | 4 + 5 | 29 | 15 + 5 |
| Bandwidths | 3 to 5000 MHz | 3 to 6000 MHz | 180 to 2000 MHz | 3 to 2500 MHz | 3 to 6000 MHz |
| Swath | 2300 km | 2200 km | 2250 km | 2200 km | 1650 km |
| IFOV | 32 and 16 km | 48 and 16 km | 70 and 15 km | 17 to 60 km | 40 and 13 km |

Comments (with focus on the post-2020 range):

- In the early morning time slot, there will be no coverage until 2016 (NPOESS-2).  The instrument thereafter available, ATMS, would provide high quality data, but currently is not in the baseline.  Also, no backup is currently foreseen.

- In the mid-morning time slot, instruments such as the MetOp AMSU-A + MHS would meet the post-2020 quality requirements, but are not yet committed.  Of the FY-3 instruments, MWTS is similar to the old MSU of TOVS, MWHS is state-of-art: they would provide partial backup.

- In the early afternoon time slot, the post-2020 requirements will be met by ATMS on NPOESS.  The FY-3 MWTS and MWHS would provide partial backup.

Recommendations:

- In the early morning: to baseline ATMS on NPOESS-2, and possibly add another sounder on another platform to provide redundancy.

- In the mid-morning time: to continue with a high-quality MW sounding package on the follow-on of MetOp/EPS.  On FY-3, the MWTS unit should possibly be upgraded to AMSU-A level to provide full redundancy.

- In the early afternoon: to possibly upgrade the MWTS unit to AMSU-A level to provide full redundancy.

6.	MW TEMPERATURE/HUMIDITY SOUNDING FROM GEO

This mission could be implemented by sounding/imaging radiometers operating in the millimetre and submillimetre range of the spectrum, so as to enable using antennas of practicable sizes.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of millimetre-submillimetre wave imaging sounders in GEO (years 2020’s) |
| --- |
| Spectral range | Bandwidths | No. of channels | Typical NE(T | Resolution | Observing cycle |
| 50 to 450 GHz | 50 to 4000 MHz | ~ 40 | 0.1 to 0.6 K | 10-50 km | 1 h (full disk) to 15 min for areas 1/10 of disk |

Addressed products are as follows (same as from LEO, with possibly somewhat lower quality, but much more frequently).

| Geophysical parameters addressed by the millimetre-submillimetre wave imaging/sounding mission in GEO |
| --- |
| Air temperature profile (nearly-all-weather) | Downwelling LW irradiance at Earth’s surface | Cloud liquid water total column |
| Water vapour profile (nearly-all-weather) | Freezing level height in clouds | Cloud ice total column |
| Water vapour total column (nearly-all-weather) | Melting layer depth in clouds | Precipitation rate at surface |

The recommended observing strategy is:

- six sectors, 60 degrees wide along the equator (centres: 0°, 60°E, 120°E, 180°E, 120°W, 60°W);

- at least one instrument in each sector, either viewing the full disk or addressing selected areas.

Currently there is only one plan being considered for millimetre-submillimetre sounders in GEO.

| Instrument class | To meet post-2020 requirements |
| --- | --- |

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 0° |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 60°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GEO-MW TBD | FY-4 M/A( | 123.5°E |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 120°W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 60°W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Comments (with focus on the post-2020 range):

- Although WMO recommended the introduction of millimetre-submillimetre sounding from GEO, especially for frequent precipitation observation, only China is considering an appropriate mission.

- Other project exists (GEM, GOMAS, GeoSTAR), only at conceptual stage.

Recommendations:

- To implement a demonstration mission in the context of the International Geostationary Laboratory initiative (IGeoLab).  According to the current situation, the initiative should be led by China.

- To perform the demonstration mission moving the satellite across the various Sectors, or at least across the Sectors covering Countries participating to the IGeoLab initiative for GEO-Microwave.

- The Countries cooperating with China to implement the demonstration mission should contribute by providing system elements (including support to the ground segment), airborne campaigns, and support to scientific studies.

7.	CONICAL-SCANNING MW IMAGERY (intermediate frequencies)

This mission is implemented by MW radiometers that need to exploit multi-polarisation for one or another reason (conical scanning provides constant zenith angle).  It is a multi-purpose mission, with particular emphasis on precipitation.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of MW conical scanning imagers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of frequencies | Typical NE(T | Resolution | Swath | Scanning |
| 6.5 to 190 GHz | 100-4000 MHz | 4 to 20 | 0.3 to 1.0 K | 5-50 km | > 1400 km | conical |

Addressed products are as follows.

| Geophysical parameters addressed by the conical scanning MW imagery mission in LEO |
| --- |
| Precipitation rate at surface | Sea surface temperature (nearly-all-weather) | Surface soil moisture |
| Cloud liquid water total column | Sea-ice surface temperature | Snow cover |
| Cloud ice total column | Sea-ice cover | Snow water equivalent |
| Precipitable water (over the sea) | Sea-ice type | Snow surface temperature |
| Horizontal wind over sea surface | Land surface temperature (nearly-all-weather) | Snow status (wet/dry) |

The recommended observing strategy is:

- three orbital planes (early morning: 5:30 ( 2 h;  mid-morning: 9:30 ( 2 h;  early afternoon: 13:30 ( 2 h);

- one fully compliant instrument in each plane, and one backup, as similar as possible;

- additional satellites in low-inclination non-sunsynchronous orbits.

The evolution of current and planned MW conical scanners in LEO is shown below.  It is noted that, pending the re-definition of the NPOESS CMIS (now “MIS”), the old CMIS specifications are still used.

| Instrument class | SSM/I-class | SSMIS-class | CMIS-class | High spatial resolution |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SSMIS | DMSP 17/19/20 | 05:30 | X | X | X | X | X | X | X | X | X | X | X |  |  |  |  |
| CMIS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| SSM/I | DMSP-F13 | 06:30 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SSMIS | DMSP-16 | 08:10 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| MWRI | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| MTVZA | Meteor-M 1&2 | 10:20 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| AMSR-E | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| AMSR-2 | GCOM-W 1 (2, 3) | 13:30 |  |  |  | X | X | X | X | X | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
| CMIS | NPOESS 3 | 13:30 |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| MWRI | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |
| TMI | TRMM | 35° | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| GMI | GPM “core” | 65° |  |  |  |  |  | X | X | X | X | X | X |  |  |  |  |
| MADRAS | Megha-Tropique | 20° |  |  |  | X | X | X | X | X |  |  |  |  |  |  |  |

| Comparative characteristics of conical scanning MW imagers in LEO |
| --- |
| Feature | DMSP SSM/I | DMSP SSMIS | NPOESS CMIS | FY-3 MWRI | Meteor-M MTVZA | Aqua/GCOM AMSR E/2 | TRMM TMI | GPM core GMI | Meg-Trop MADRAS |
| Frequencies | 4 | 21 | 63 | 6 | 21 | 6 | 5 | 7 | 5 |
| Channels | 7 | 24 | 77 | 12 | 29 | 12 | 9 | 13 | 9 |
| Range | 19-86 GHz | 19-183 GHz | 6.6-183 GHz | 10.6-150 GHz | 10.6-183 GHz | 6.9-89 GHz | 10.6-86 GHz | 10.6-183 GHz | 19-157 GHz |
| Swath | 1400 km | 1700 km | 1700 km | 1400 km | 2200 km | 1450 km | 760 km | 850 km | 1740 km |
| IFOV (90 GHz) | 13 km | 13 km | 4 km | 10 km | 17 km | 5 km | 6 km | 6 km | 8 km |

Comments (with focus on the post-2020 range):

- In the early morning time slot, the instrument meeting post-2020 requirements will be available in 2016 (CMIS on NPOESS).  No other satellite to serve as redundancy is currently planned.

- In the mid-morning time slot, no instrument is planned that meets post-2020 requirements.  Only partial fulfilment from MWRI on FY-3 (SSM/I-class).

- In the early afternoon time slot, the post-2020 requirements will be met by CMIS on NPOESS from 2020 onwards.  MWRI on FY-3 would be a partial backup.  GCOM-W 2 and 3 are not yet committed.

- Flights in non-sunsynchronous orbits are not committed for long-term continuation, not in low-inclination orbit, nor at the relatively high inclination orbit of the GPM “core”.

Recommendations:

- In the early morning: to add another MW conical scanner on another platform to provide redundancy.

- In the mid-morning: to provide a CMIS-class MW conical scanner.  On FY-3, to upgrade MWRI to provide full redundancy.

- In the early afternoon: to pursue long-term continuation of AMSR-2 on GCOM-W so as to have full redundancy with NPOESS CMIS/MIS.

- In non-sunsynchronous orbit: at least the GPM “core” mission should be provided with long-term continuity (its MW imager is associated to a dual-frequency radar to “calibrate” the full GPM mission).

8.	LOW-FREQUENCY MW IMAGERY

This mission is implemented by MW radiometers addressing applications that require low frequencies, thus large antennas.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of low-frequency MW conical scanning imagers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of frequencies | Typical NE(T | Resolution | Swath | Scanning |
| 1.4 to 37 GHz | 30-2000 MHz | 1 to 5 | 0.3 to 1.0 K | 5-50 km | > 1000 km | conical |

Addressed products are as follows.

| Geophysical parameters addressed by the low-frequency MW imagery mission in LEO |
| --- |
| Sea surface salinity | Sea surface temperature | Polar ice cover |
| Surface soil moisture | Land surface temperature | Polar ice type |
| Soil moisture in the roots region | Horizontal wind over sea surface | Sea-ice surface temperature |

The recommended observing strategy is:

- each main parameter to be observed by at least one satellite, generally of R&D nature.

The evolution of current and planned low-frequency MW imagers in LEO is shown below.

| Instrument objective | Soil moisture in the roots region and ocean salinity | Sea surface wind including direction, and temperature | Sea surface temperature, surface soil moisture |
| --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Aquarius | SAC-D | 06:00 |  |  | X | X | X | X |  |  |  |  |  |  |  |  |  |
| MIRAS | SMOS | 06:00 |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| WindSat | Coriolis | 06:00 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| MSMR | OceanSat 1 | 12:00 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of low-frequency MW imagers in LEO |
| --- |
| Feature | SAC-D Aquarius | SMOS MIRAS | Coriolis WindSat | OceanSat MSMR |
| Frequencies | 1.4 GHz passive radiometer, 1.3 GHz radar scatterometer | 1.4 GHz | 5 | 4 |
| Channels | up to 6 (full pol) | up to 6 (full pol) | 22 (full pol in 3 channels) | 8 |
| Range | - | - | 6.6-37 GHz | 6.6-21 GHz |
| Scanning | 3 parallel beams along track | synthetic aperture | conical | conical |
| Swath | 390 km | 1000 km | 1000 km | 1360 km |
| IFOV | 100 km | 50 km | 25 km @ 19 GHz, 70 km @ 6.6 GHz | 40 km @ 18 GHz, 110 @ 6.6 GHz |

Comments (with focus on the post-2020 range):

- Currently, there is no plan for continuing systems such as Aquarius and MIRAS beyond the R&D stage.

- WindSat was a risk-reduction mission for CMIS on NPOESS.  With the re-structuring of CMIS it seems that the polarimetric capability (for winds) will be retained, whereas the lowest frequency (for sea-surface temperature and surface soil moisture), if retained, will be associated to very coarse resolution.

Recommendations:

- The re-designed CMIS (i.e. MIS) should retain at least the full polarimetric channels for sea surface winds, and the 10 GHz frequency for surface soil moisture; and possibly the 6.6 GHz frequency for sea-surface temperature, avoiding that the reduction exercise brings to a marginal resolution.

- Long-term continuity should be arranged for a mission exploiting the 1.4 GHz frequency for ocean salinity and soil moisture in the roots regions.  Alternative solutions enabling association of frequencies up to 5 GHz should be studied, to extend the capability to sea-surface temperature.

9.	RADIO OCCULTATION SOUNDING

This mission is implemented by receivers of signals from navigation systems (GPS, GLONASS, Galileo) embarked on LEO satellites, during the occultation phase. Generic characteristics of the instruments are listed as follows.

| Generic characteristics of radio-occultation sounders (years 2020’s) |
| --- |
| Frequencies | No. of channels | Effective resolution | Observing cycle | Scanning |
| 1160 to 1600 MHz | ~ 16 | ~ 300 km | 1000-1500 occultations/day/satellite | Occultation of GNSS signals |

Addressed products are as follows.

| Geophysical parameters addressed by the radio occultation sounding mission in LEO |
| --- |
| Air temperature profile | Height of the tropopause | Electron density profile |
| Water vapour profile | Height of the top of the PBL | Geoid’s undulations |
| Air pressure profile | Total Electron Content (TEC) | Gravity anomalies |

The recommended observing strategy is:

- to have available as many satellites as necessary to achieve at least one sample in each 300 x 300 km2 cell of the Earth surface each 6 hours;

- this implies at least 24 satellites in several distinct orbital planes, not necessarily sun-synchronous.

The evolution of current and planned radio-occultation sounders in LEO is shown below.

| Instrument class | Fore- & aft- | Constellation, fore- & aft- | Only aft- (setting occultations) |
| --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ROSA | SAC-D | 06:00 |  |  | X | X | X | X |  |  |  |  |  |  |  |  |  |
| GRAS | MetOp | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| Radiomet | Meteor-M-2 | 10:20 |  | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| ROSA | OceanSat-2 | 12:00 |  | X | X | X | X | X | X |  |  |  |  |  |  |  |  |
| IGOS | COSMIC (6 sats) | 71° | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |
| BlackJack | CHAMP | 87° | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| BlackJack | GRACE | 89° | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of radio-occultation sounders in LEO |
| --- |
| Feature | MetOp GRAS | CHAMP BlackJack | GRACE BlackJack | COSMIC (6 sats) IGOS ≈ BlackJack | SAC-D ROSA | OceanSat-2 ROSA | Meteor-M-2 Radiomet |
| Viewing geometry | fore- & aft- | only aft- | only aft- | fore- & aft- | fore- & aft- | fore- & aft- | fore- & aft- |
| No. of soundings | 500 / day | 250 / day | 250 / day | 3000 / day | 500 / day | 500 / day | 500 / day |

Comments (with focus on the post-2020 range):

- The only programme extending to 2020 is MetOp.  GRAS provides only 500 soundings/day, not meeting the post-2020 requirements.

- To implement the required constellation of 24 satellites, each one with one radio-occultation receiver additional to the other instruments, is practically impossible.  The COSMIC constellation of 6 dedicated micro-satellites constitutes the optimal approach.

Recommendation:

- The provide continuity to the demonstrative COSMIC mission, and extend the concept aiming at 3 or 4 constellations of micro-satellites for a total number of about 24 satellites, to provide global 300 km sampling each 6 hours; or, as a minimum, 12 satellites to provide global 300 km sampling each 12 hours.

10.	EARTH RADIATION BUDGET FROM LEO

This mission is implemented by broad-band radiometry of the total radiation from Earth-Atmosphere to Space, and of its short-wave component (reflected solar radiation).  Provision of additional information from key narrow-band channels, and on multi-directional viewing (to retrieve irradiance) is necessary.  The incoming solar radiation (by cavity radiometer) also must be observed.

| Generic characteristics of the Earth radiation budget mission in LEO (years 2020’s) |
| --- |
| Spectral range | No. of channels | Accuracy | Resolution | Swath | Scanning |
| 0.2 (m to 300 (m | 2 broad-band plus 1-2 narrow-band | NE(R = 0.5 W(m-2(sr-1 | 20 km | 2800 km | cross-track + multi-view |
| 0.2 (m to 10 (m | 1 (active cavity) | Absolute: 0.2 W(m-2 | - | - | sun-pointing |

Addressed products are as follows.

| Geophysical parameters addressed by the Earth radiation budget mission in LEO |
| --- |
| Outgoing short-wave irradiance at TOA | Outgoing long-wave irradiance at TOA | Downwelling solar irradiance at TOA |

The recommended observing strategy is:

- to cover the diurnal cycle by observing at least at 3-hour intervals, that implies four LEO satellites;

- alternatively (better), to exploit synergy with GEO and reduce LEO to one satellite as a “calibrator”.

The evolution of current and planned Earth radiation radiometers in LEO is shown below.

| Instrument class | Cavity radiometers | ( 3 channels | Multi-viewing capability | < 3 channels |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TSIS | NPOESS 2/4 | 05:30 |  |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) |
| ERM | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| CERES | EOS-Terra | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ACRIM III | ACRIMSat | 10:30 | X | X | X | (X) | (X) | (X) |  |  |  |  |  |  |  |  |  |
| CERES | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| TIM | Glory | 13:30 |  |  | X | X | X | X | X |  |  |  |  |  |  |  |  |
| ERBS | NPOESS 1/3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | (X) | (X) |
| ERM | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |
| ScaRaB | Megha-Tropique | 20° |  |  |  | X | X | X | X | X |  |  |  |  |  |  |  |
| CERES | TRMM | 35° | failed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| TIM | SORCE | 40° | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of Earth radiation budget radiometers (TIM, TSIS, ACRIM-III not included) |
| --- |
| Features | EOS Terra & Aqua CERES | NPOESS-1 ERBS | FY-3 ERM | Megha-Tropique ScaRaB |
| Total energy channel | 0.3 - 100 (m | 0.3 - 100 (m | 0.2 - 50 (m | 0.2 - 50 (m |
| Short-wave channel | 0.3 - 5.0 (m | 0.3 - 5.0 (m | 0.2 - 3.8 (m | 0.2 - 4.0 (m |
| Narrow-band | 8 - 12 (m | 8 - 12 (m |  | 0.55 - 0.65 (m |
| channels |  |  |  | 10.5 - 12.5 (m |
| No. of channels | 3 | 3 | 2 | 4 |
| Swath | 3000 km | 3000 km | 2200 km | 3200 km |
| IFOV | 10 km (cross-track scanning), 20 km (bi-axial scanning) | 10 km (cross-track scanning), 20 km (bi-axial scanning) | 28 km (scanning unit), 2200 km (non-scanning unit) | 40 km |

Comments (with focus on the 2020 range):

- In the early morning time slot: nothing current and nothing planned for ERB.  There is a plan for solar irradiance (TSIS on NPOESS 2/4), but currently not in the baseline.  No backup.

- In the mid-morning time slot, ERM on FY-3 provides coverage but does not meet post-2020 requirements.  No backup.

- In the early afternoon time slot, the post-2020 requirements are met by ERBS on NPOESS.  However, current plan is only for NPOESS-1, i.e. till 2019.  ERM on FY-3 provides backup.

Recommendations:

- The need for capturing the diurnal cycle, due to strong dependence of ERB on the cloud evolution, requires sampling at least each 3 hours, better 1 hour.  The mission should therefore be structured so as to exploit synergy with GEO satellites.

- Assuming that an ERB payload is embarked on a sufficient number of GEO satellites, the effort in LEO could be limited to one advanced payload (e.g., ERBS on NPOESS-3 to provide continuity to NPOESS-1) plus some limited-performance payload (e.g. ERM on two FY-3 platforms) for completing coverage of high latitudes and as backup.

- The Total Solar Irradiance monitoring mission must have a follow-on.  The plan for TSIS on NPOESS 1 and 3 should be confirmed.

11.	EARTH RADIATION BUDGET FROM GEO

This mission is implemented by broad-band radiometry of the total radiation from Earth-Atmosphere to Space, and of its short-wave component (reflected solar radiation).

| Generic characteristics of the Earth radiation budget mission in GEO (years 2020’s) |
| --- |
| Spectral range | No. of channels | Accuracy (NE(R) | Resolution | Observing cycle |
| 0.2 (m to 300 (m | 2 broad-band (total + SW) | 0.5 W(m-2(sr-1 | 40 km | < 30 min (full disk) |

Addressed products are as follows (nearly the same as from LEO, with possibly somewhat lower quality, but much more frequently).

| Geophysical parameters addressed by the Earth radiation budget mission in GEO |
| --- |
| Outgoing short-wave irradiance at TOA | Outgoing long-wave irradiance at TOA |

The recommended observing strategy is:

- to include a broad-band radiometer on a number of operational GEO satellites such as to realise about 60° spacing around the equator;

- to exploit synergy with LEO using the instrument(s) in LEO (capable of multi-viewing and including solar irradiance measurement) for “calibration” so as to simplify the instrument in GEO to the maximum possible extent (two broadband channels only, since a multi-channel narrow-band imager will anyway be co-flying as primary payload of the same GEO satellite).

The evolution of current and planned Earth radiation radiometers in GEO is shown below.

| Instrument class | To meet post-2020 requirements |
| --- | --- |

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| GERB | Meteosat 8 to 11 | 0° | X | X | X | X | X | X | X | X | X | X | X | X | X |  |  |
|  |  | 60°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 120°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 120°W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 60°W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Characteristics of the GERB radiometer |
| --- |
| Features | GERB (Meteosat 8 to 11) |
| Total energy channel | 0.3 2- 30 (m |
| Short-wave channel | 0.32 - 4.0 (m |
| No. of channels | 2 |
| Coverage/cycle | Full disk each 15 min |
| IFOV | 42 km s.s.p. |

Comment (with focus on the post-2020 range):

- No plan exists to fly ERB missions in GEO.  This also holds for Meteosat Third Generation.

Recommendation:

- To re-design a composite Earth radiation mission based on GEO satellite to monitor the diurnal cycle (specifically due to clouds) and on one or more LEO satellites equipped for multi-viewing/multi-spectral observation and solar irradiance monitoring.

12.	WIND SCATTEROMETRY

This mission is implemented by radar scatterometers that provide backscatter coefficient observations under a number of viewing angles.

| Generic characteristics of the wind scatterometry mission in LEO (years 2020’s) |
| --- |
| Frequency | Swath | Look angles | Resolution | Scanning |
| C-band (preferred) or Ku-band | 700 - 1500 km | 3 - 4 | 20 - 50 km | pushbroom (preferred) or conical |

Addressed products are as follows.

| Geophysical parameters addressed by the wind scatterometry mission in LEO |
| --- |
| Horizontal vector wind over sea surface | Surface soil moisture | Leaf Area Index (LAI) | Snow water equivalent | Sea-ice type |

The recommended observing strategy is:

- to implement a composite system of satellites equipped with radar scatterometers and MW radiometers of the Coriolis/WindSat or NPOESS/CMIS type (i.e. with a few full-polarimetric channels); and to exploit other passive MW radiometers (speed only) so that the complex provides global coverage of sea-surface winds every 3 hours (accounting for limited swath);

- three orbital planes (early morning: 5:30 ( 2 h;  mid-morning: 9:30 ( 2 h;  early afternoon: 13:30 ( 2 h);

- one instrument (either radar or polarimetric MW) in each plan, and one backup;

- however, in the complex of radars + passive MW instruments, at least two should be radars.

The evolution of current and planned scatterometers in LEO is shown below.  For convenience, the polarimetric passive MW radiometers (Coriolis/WindSat and NPOESS/CMIS) also are indicated.

| Instrument class | Swath < 700 km | Swath > 700 km, Ku-band | Swath > 700 km, C-band | Polarimetric passive MW |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CMIS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| SeaWinds | QuikSCAT | 06:00 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| WindSat | Coriolis | 06:00 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| ASCAT | MetOp | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| AMI-SCAT | ERS-2 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| SCAT | OceanSat-2 | 12:00 |  | X | X | X | X | X | X |  |  |  |  |  |  |  |  |
| CMIS | NPOESS 3 | 13:30 |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| SeaWinds | GCOM-W 2, 3 | 13:30 |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) |

| Comparative characteristics of wind scatterometers |
| --- |
| Feature | SeaWinds (QuikSCAT and possibly GCOM-W 2,3) and SCAT (OceanSat-2) | ASCAT (MetOp) | AMI-SCAT (ERS-2) |
| Frequency | 13.4 GHz | 5.3 GHz | 5.3 GHz |
| Swath | 1800 km | 1100 km | 500 km |
| Look angles | 4 | 3 | 3 |
| IFOV | 50 km (conical scanning), or 25 km (sampling 12.5 km | 25 km (sampling 12.5 km) | 50 km (sampling 25 km) |

Comments (with focus on the 2020 range):

- In the early morning time slot: covered by polarimetric passive MW (NPOESS/CMIS).  No backup.

- In the mid-morning time slot: could be covered by an ASCAT-like instrument on post-EPS. No backup.

- In the early afternoon time slot: the planned GCOM-W 2 and 3 (not yet committed) would provide measurements by radar, NPOESS/CMIS by polarimetric passive MW.  SCAT on OceanSat-2 is currently not committed for long-term continuity.

- There is information (in the literature, not official) on a Chinese plan for a SeaWinds-like scatterometer to be embarked on HY-2 (HaiYang-2) sometimes around 2010.  Orbital LST unknown.

Recommendations:

- An ASCAT-like instrument should continue to be flown on post-EPS.

- The plan for GCOM-W 2 and 3, with SeaWinds, should be confirmed, and/or the Indian OceanSat-2 with SCAT should be extended to a long-term programme, aiming at having at least one radar scatterometer in the early afternoon orbit.

- Backup in the early morning and mid morning could be provided by non-polarimetric passive MW radiometers (only wind speed), equipped with frequencies such as 19 GHz (e.g., satellites of the GPM constellation).  These would also contribute to implement more frequent global coverage.

13.	RADAR ALTIMETRY

This mission is implemented by essentially nadir-pointing radar that measures the distance between the satellite and the reflecting sea surface.  It can also be used on land and ice.  It is possible to implement SAR capability to more accurately detect ice border and topography.  To be associated with co-aligned passive MW radiometers for water vapour correction.

| Generic characteristics of the altimetry mission in LEO (years 2020’s) |
| --- |
|  | Frequency | Resolution | Scanning |
| Altimeter | Two within the range 1.55 to 35.5 GHz | 20 to 30 km along track | none |
| MW radiometer | 23 GHz plus nearby window(s) (19 and/or 34 GHz) | 20 to 30 km along track | none |

Addressed products are as follows.

| Geophysical parameters addressed by the altimetry mission in LEO |
| --- |
| Ocean topography | Significant wave height | Ice sheet topography | Sea ice thickness | Total Electron Content (TEC) |

The recommended observing strategy is:

- two satellites (for more frequent coverage and redundancy) in high non-sunsynchronous orbit for large-scale and long-term application;

- two satellites (for more frequent coverage and redundancy) in low sunsynchronous orbit, with SAR capability, for sea ice and regional purposes.

The evolution of current and planned altimeters and associated MW radiometers in LEO is shown below.

| Instrument class | Two frequencies, no SAR | Single frequency, SAR | SAR capability | Single frequency, no SAR |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SRAL + MWR | Sentinel-3/1 | 10:00 |  |  |  |  |  | X | X | X | X | X | X | X |  |  |  |
| SRAL + MWR | Sentinel-3/2 | 10:00 |  |  |  |  |  |  |  | X | X | X | X | X | X | X |  |
| RA-2 + MWR | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| RA + MWR | ERS-2 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| Poseidon-2 + JMR | Jason-1 | 66° | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| Poseidon-3 + AMR | Jason-2 | 66° |  | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| SIRAL | CryoSat-2 | 92° |  |  | X | X | X | X |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of radar altimeters and associated MW radiometers |
| --- |
| Feature | ERS-2 RA | Envisat RA-2 | Poseidon 2 & 3 (Jason 1 & 2) | CryoSat-2 SIRAL | Sentinel-3 SRAL | ERS-2, Envisat & Sentinel-3: MWR | Jason 1 & 2 JMA = AMR |
| Frequency | 13.8 GHz | 3.2 & 13.8 GHz | 5.3 & 13.58 GHz | 13.56 GHz | 5.3 & 13.58 GHz | 23.8 and 36.5 GHz (+18.7 GHz on S-3) | 18.7, 23.8 and 34 GHz |
| Repeat cycle | 35 days | 35 days | 10 days | 30 days | 27 days | 27 or 35 days | 10 days |
| IFOV | 20 km | 20 km | 30 km | 15 km (SAR. 250 m) | 20 km (SAR: 300 m) | 20 km | 25 km |

Comments (with focus on the 2020 range):

- In low (sunsynchronous) orbit the requirements are not met even if Sentinel-3 is developed and continued after the first two demonstration flight units, still based on two satellites in orbit at the same time; in fact, the orbits of the two satellites are close to each other.

- In the high (non-sunsynchronous) orbit, post-EPS requirements are met if continuity is provided to the Ocean Surface Topography Mission (OSTM).

- There is information (in the literature !  not official) on a Chinese plan for an altimeter to be embarked on HY-2 (HaiYang-2) sometimes around 2010.  Orbital LST unknown.

Recommendations:

- To provide continuity to the Sentinel-3 programme keeping the feature of having two satellites in orbit at each time.

- To provide continuity to the Jason programme ensuring that the launches schedule overlap to the extent of having two satellites in orbit at each time.

- If the HY-2 programme materialises, the orbit should be well separated from the one of Sentinel-3 (ideally: LST 16:00).

14.	OCEAN COLOUR IMAGERY FROM LEO

This mission is implemented by VIS/NIR imagers specifically designed to work on low-level signals (because of low reflectivity of ocean) and narrow bandwidth channels to address specific water features.

| Generic characteristics of the ocean colour mission in LEO (years 2020’s) |
| --- |
| Spectral range | Bandwidths | No. of SW channels | Typical SNR | Resolution | Swath | Scanning |
| 400 to 900 nm | 4 to 10 nm | 8-15 | 1000 | 300-1000 m | 1400-2800 km | cross-track |

Addressed products are as follows.

| Geophysical parameters addressed by the ocean colour mission in LEO |
| --- |
| Chlorophyll concentration | Colour Dissolved Organic Matter (CDOM) | Leaf Area Index (LAI) |
| Diffuse attenuation coefficient (DAC) | Photosynthetically Active Radiation (PAR) | Normalised Difference Vegetation Index (NDVI) |
| Suspended sediments concentration | Fractional Absorbed PAR (FAPAR) | Oil spills |

The recommended observing strategy is:

- two satellites: one in mid-morning, one in early afternoon, to increase probability of cloud-free conditions; each one with backup, even if by instruments not optimal.

The evolution of current and planned ocean colour monitors in LEO is shown below.

| Instrument class | Channels with ( < 1 (m: > 10 most bandwidths ~ 10 nm | Channels with ( < 1 (m: > 10 some bandwidths < 10 nm | Channels with ( < 1 (m: < 10 all bandwidths > 10 nm |
| --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| VIIRS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| MERIS | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| OLCI | Sentinel-3/1 | 10:00 |  |  |  |  |  | X | X | X | X | X | X | X |  |  |  |
| OLCI | Sentinel-3/2 | 10:00 |  |  |  |  |  |  |  | X | X | X | X | X | X | X |  |
| MERSI | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| SGLI | GCOM-C 1 (2,3) | 10:30 |  |  |  |  | X | X | X | X | X | (X) | (X) | (X) | (X) | (X) | (X) |
| MODIS | EOS-Terra | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SeaWiFS | SeaStar | 12:00 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| OCM | OceanSat 1, 2 | 12:00 | X | X | X | X | X | X | X |  |  |  |  |  |  |  |  |
| MODIS | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| VIIRS | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| VIIRS | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X |
| MERSI | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |

| Comparative characteristics of ocean colour monitoring radiometers in LEO |
| --- |
| Feature | OceanSat OCM | SeaStar SeaWiFS | Terra/Aqua MODIS | Envisat MERIS | Sentinel-3 OLCI ≈ MERIS-2 | FY-3 MERSI | NPOESS VIIRS | GCOM-C SGLI |
| Channels ( < 1 (m | 8 | 8 | 12 | 15 | 15 | 12 | 7 | 13 |
| Bandwidths | 20-40 nm | 20-40 nm | 10-50 nm | 4-20 nm | 4-20 nm | 20 nm | 15-40 nm | 8-20 nm |
| Swath | 1420 km | 2800 km | 2230 | 1150 km | 1270 km | 2900 km | 3000 km | 1000 km |
| IFOV | 300 m | 1.1 km | 1.0 km | 300 m | 200-500 m | 1.0 km | 800 m | 250-1000 m |

Comments (with focus on the 2020 range):

- In the mid-morning Sentinel-3 (with OLCI), if continued, and GCOM-C 2 and 3 (with SGLI), if approved,  would cover the requirement for high-quality measurements, also with backup.

- In the early afternoon NPOESS/VIIRS and FY-3/MERSI will provide a basic service, also redundant. However, none of the two meet post-2020 requirements.

Recommendation:

- To provide long-term continuity of Sentinel-3.

- To approve GCOM-C 2/3 but improve the effectiveness of SGLI by placing it in an afternoon orbit (ideal: LST = 14:00).  Or upgrade MERSI on FY-3 (by narrowing the channel bandwidths).

15.	OCEAN COLOUR IMAGERY FROM GEO

This mission is implemented by VIS/NIR imagers specifically designed to work on low-level signals (because of low reflectivity of ocean) and narrow bandwidth channels to address specific water features.

| Generic characteristics of the ocean colour mission in GEO (years 2020’s) |
| --- |
| Spectral range | Bandwidths | No. of SW channels | Typical SNR | Resolution | Observing cycle |
| 400 to 900 nm | 10 to 40 nm | 8-15 | 1000 | 200-500 m | 60 min (area of 2500 x 2500 km2) |

Addressed products are as follows (the same as from LEO, with possibly somewhat lower quality, but much more frequently).

| Geophysical parameters addressed by the ocean colour mission in GEO |
| --- |
| Chlorophyll concentration | Colour Dissolved Organic Matter (CDOM) | Leaf Area Index (LAI) |
| Diffuse attenuation coefficient (DAC) | Photosynthetically Active Radiation (PAR) | Normalised Difference Vegetation Index (NDVI) |
| Suspended sediments concentration | Fractional Absorbed PAR (FAPAR) | Oil spills |

The recommended observing strategy is:

- no need for international coordination, except among countries in the same field of view: in fact, it is a mission for local purposes (on coastal waters).

The evolution of current and planned ocean colour monitors in GEO is shown below.

| Instrument class | To meet post-2020 requirements |
| --- | --- |

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 0° |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  | 60°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GOCI | COMS-1 & 2 | 128°E |  | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| HES | GOES-17 | 135°W |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
| HES | GOES-16 (R) | 75°W |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) |

| Comparative characteristics of ocean colour monitoring radiometers in GEO |
| --- |
| Feature | COMS (GOCI) | GOES-R (HES) |
| Channels ( < 1 (m | 8 | 14 |
| Bandwidths | 10-40 nm | 20-40 nm |
| Cycle | 60 min for sectors of 2500 x 2500 km 2 (or equivalent) | 60 min for sectors of 2500 x 2500 km 2 (or equivalent) |
| IFOV | 500 m | 150-300 m |

Comments (with focus on the 2020 range):

- The only consolidated plan for ocean colour monitoring from GEO is for GOCI on COMS.

- The plan for ocean colour from GOES-R / HES is no longer in the baseline.  HES itself is not confirmed.

Recommendation:

- None: ocean colour from GEO is considered of local interest.

16.	IMAGERY WITH SPECIAL VIEWING GEOMETRY

This mission is implemented by VIS/IR imagers specifically designed for viewing under different angles for one or another purpose (accurate atmospheric correction, anisotropy effects, best geometry to exploit multi-polarisation, need for reconstructing irradiances from observed radiances, etc.).

| Generic characteristics of imagers with special viewing geometry in LEO (years 2020’s) |
| --- |
|  | Spectral range | Bandwidths | No. of channels | Accuracy | Full-pol channels | Viewing angles | Resolution | Swath | Scanning |
| Sea-surface temperature | 3.5 to 12.5 (m | 0.3 to 1.0 (m | IR: 3 | NE(T = 0.05 @ 280 K | - | 2- | .0.5-1.0 km | 500-1000 km | conical |
| Aerosol, Cirrus clouds | SW: 340-2200 nm LW: 3.5-25 (m | SW: 6 to 40 nm LW: 0.4-2.0 (m | SW: 10 LW: 10 | SNR: 200 @ 10 % ( NE(T = 0.1 @ 300 K | 4 to 6 (in SW) | 2 to 10 | 1 to 5 km | 1400-2500 km | conical or pushbroom |
| Bi-directional reflectance | 400 to 900 nm | 20 to 40 nm | 4-10 | SNR = 300 @ 10 % ( | - | 10 | 0.3 to 5 km | 500-2500 km | mixed |

Addressed products are as follows.

| Geophysical parameters addressed by special viewing instruments in LEO |
| --- |
| Sea-surface temperature (IR) | Aerosol optical depth profile (short wave) | SW Earth’s surface bi-directional reflectance |
| Land-surface temperature (IR) | Total aerosol optical depth (short-wave) | Earth’s surface albedo |
| Cloud optical depth (short-wave) | Aerosol effective radius profile | Photosynthetically Active Radiation (PAR) |
| Cloud drop effective radius at cloud top | Total aerosol effective radius | Fractional Absorbed PAR (FAPAR) |
| Cloud ice effective radius at cloud top | Aerosol type profile | Snow albedo |
| Short-wave cloud reflectance | Downwelling SW irradiance at Earth’s surface | Oil spill cover |

The recommended observing strategy is:

- at least one instruments for accurate sea-surface temperature (backup is the VIS/IR imagery mission on the backbone satellites of GOS, i.e. those in the 05:30, 09:30 and 13:30 LST orbits);

- at least one instrument specifically designed for multi-angle/multi-spectral/multi-polarisation observation for aerosol, cirrus clouds and bidirectional reflectances (partial backup is the VIS/IR imagery mission on the backbone satellites of GOS, i.e. those in the 05:30, 09:30 and 13:30 LST orbits);

The evolution of current and planned special viewing instruments is shown below.

| Instrument class | For aerosol | For BRDF | For aerosol and BRDF | For temperature |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SLSTR | Sentinel-3/1 | 10:00 |  |  |  |  |  | X | X | X | X | X | X | X |  |  |  |
| SLSTR | Sentinel-3/2 | 10:00 |  |  |  |  |  |  |  | X | X | X | X | X | X | X |  |
| AATSR | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| ATSR-2 | ERS-2 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| MISR | EOS-Terra | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| POLDER | PARASOL | 13:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| APS | NPOESS 1/3 | 13:30 |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
| APS | Glory | 13:30 |  |  | X | X | X | X | X |  |  |  |  |  |  |  |  |

| Comparative characteristics of special viewing instruments in LEO |
| --- |
|  | ERS-2 and Envisat ATSR-2 = AATSR | Sentinel-3 SLSTR | EOS-Terra MISR | PARASOL POLDER | NPOESS, Glory APS |
| Channels | 4 VIS/NIR/SWIR, 3 MWIR/TIR | 6 VIS/NIR/SWIR, 3 MWIR/TIR | 4 channels, VIS/NIR | 9 channels, VIS/NIR | 11 channels, VIS/NIR/SWIR |
| Polarisations | - | - | none | 3, for 3 channels | 4, for all channels |
| Viewing angles | 2 | 2 | 9 | Several | Several within ( 60° along-track |
| Swath | 500 km | Dual view: 750 km ; single view: 1675 km | 360 km | 2200 km | N/A (non-scanning) |
| IFOV at s.s.p. | 1 km | VIS/NIR/SWIR: 500 m, MWIR/TIR 1.0 km | Selectable: 275 m or 550 m or 1100 m | 6 km | 10 km |

Comments (with focus on the 2020 range):

- Accurate sea-surface temperature for climate: the post-2020 requirement will be met if continuity is provided to Sentinel-3, which embarks the follow-on of the ATSR series operating since 1991.

- Aerosol and cirrus clouds: no provision is currently foreseen to provide continuity to POLDER and extend its capabilities.  The operational VIS/IR imagers being designed for post-2020 provide more information than what is available from the current instruments, but are far from meeting the required accuracy because of lack of information on multi-polarisation and multi-directionality.

- Bidirectional Reflectance Distribution Function (BRDF): nothing is planned beyond POLDER and MISR.

Recommendations:

- To provide long-term continuity to the Sentinel-3 mission, that would enable to continue the ATSR series of extremely accurate measurements of the sea-surface temperature for the purpose of climate monitoring.

- To focus the problem of the lack of planning for accurate observation of aerosol and cirrus clouds, that strongly affect atmospheric radiation processes.

- To associate the problem of aerosol and cirrus clouds that require multi-polarisation and multi-viewing observations in addition to multi-spectral, to that one of re-designing the Earth radiation budget mission.

17.	LIGHTNING IMAGERY FROM LEO

This mission is implemented by special cameras observing the earth all-time and recording rate and intensity of flashes in a given area (the IFOV).  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of lightning imagers in LEO (years 2020’s) |
| --- |
| Spectral range | Bandwidth | Detection efficiency (DE) | False alarm rate (FAR) | Resolution | Swath | Scanning |
| 777.4 nm | 1.2 nm | 90 % for 7 (J(m-2(sr-1, 40 % for 4 (J(m-2(sr-1 | 1 s-1 for 50 % cloud cover with clouds albedo 80 % | 5 km | 600 km | pushbroom |

Addressed products are as follows.

| Geophysical parameters addressed by a lightning mission in LEO |
| --- |
| Convective precipitation (proxy) | NOx generation (proxy) | Earth electric field |

The recommended observing strategy is:

- since from LEO it is not possible to have enough frequent observation, the synergy with GEO should be exploited.  One payload in LEO (two for redundancy) should be operated, both for extending the observation at high latitudes, and for “calibrating” the GEO system.

The evolution of current and planned lightning imagers in LEO is shown below.

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LIS | TRMM | 35° | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |

Comments (with focus on the post-2020 range):

- There is no plan for continuing a lightning mission in LEO.

- Consideration is being given to embarking a lightning imager on the “core” satellite of the GPM constellation.

Recommendation:

- To consider the continuation of a lightning mission in LEO in the framework of the GPM (and a possible GPM follow-on), in synergy with a number of lightning imagers flown on the GEO satellite system.

18.	LIGHTNING IMAGERY FROM GEO

This mission is implemented by special cameras observing the earth all-time and recording rate and intensity of flashes in a given area (the IFOV).  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of lightning imagers in GEO (years 2020’s) |
| --- |
| Spectral range | Bandwidth | Detection efficiency (DE) | False alarm rate (FAR) | Resolution | Observing cycle |
| 777.4 nm | 1.2 nm | 90 % for 7 (J(m-2(sr-1, 40 % for 4 (J(m-2(sr-1 | 1 s-1 for 50 % cloud cover with clouds albedo 80 % | 5-10 km | All time (~ 1 ms) |

Addressed products are as follows (the same as from LEO, with possibly somewhat lower quality, but much more frequently).

| Geophysical parameters addressed by a lightning mission in GEO |
| --- |
| Convective precipitation (proxy) | NOx generation (proxy) | Earth electric field |

The recommended observing strategy is:

- six sectors, 60 degrees wide along the equator (centres: 0°, 60°E, 120°E, 180°E, 120°W, 60°W);

- at least one instrument in each sector, and one backup, as similar as possible.

The evolution of current and planned lightning imagers in GEO is shown below.

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LI | Meteosat 12( | 0° |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| LM (TBD) | FY-4 O/A( | 86.5°E |  |  |  |  |  | X | X | X | X | X | X | X | X | X | X |
| LM (TBD) | FY-4 O/B( | 123°E |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GLM | GOES-17 | 135°W |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X |
| GLM | GOES-16 (R) | 75°W |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |

Comments (with focus on the post-2020 range):

- Sector 30°W-30°E: the Meteosat 3rd Generation LI will meet post-2020 requirements.  The Meteosat system has backup in hot standby.

- Sector 30-90°E: the FY-4 O LM is being designed to meet post-2020 requirements.  The backup policy for FY-4 O satellites is to have two satellites, one at 86.5°E, and one at 123° E.

- Sector 90-150°E: the FY-4 O LM is being designed to meet post-2020 requirements.  The backup is at 86.5°E.

- Sector 150°E-150°W: nothing is planned.

- Sector 90-150°W: the GOES GLM (following GOES-R) would meet post-2020 requirements.  It would be backed by a standby GOES satellite at 105°W also backing GOES-E.

- Sector 30-90°W: the GOES GLM (following GOES-R) would meet post-2020 requirements.  It would be backed by a standby GOES satellite at 105°W also backing GOES-W.

Recommendation:

- The problem of Sector 150°E-150°W should be addressed.

19.	CLOUD AND PRECIPITATION RADAR

This mission is implemented by radar of different characteristics depending on the type of addressed cloud: non-precipitating, with light-moderate precipitation, with heavy precipitation.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of radar for cloud and precipitation in LEO (years 2020’s) |
| --- |
|  | Frequency | Sensitivity | Resolution | Swath | Scanning |
| Heavy precipitation | ~ 14 GHz | < 18 dBZ @ 0.5 mm/h at ground | < 5 km (horiz.), 200-500 m (vert.) | 200-300 km | pushbroom |
| Light-moderate precipitation | ~ 35 GHz | < 12 dBZ @ 0.2 mm/h at ground | < 5 km (horiz), 200-500 m (vert.) | up to 200 km desirable, nadir-only acceptable | pushbroom |
| Non precipitating cloud | ~ 94 GHz | < -36 dBZ for total-column | 1-5 km (horiz), 200-500 m (vert.) | up to 50 km desirable, nadir-only acceptable | pushbroom |

Addressed products are as follows.

| Geophysical parameters addressed by cloud and precipitation radar in LEO |
| --- |
| Precipitation profile(liquid and solid) | Cloud liquid water profile (< 100 (m) | Cloud ice total column |
| Precipitation rate at surface (liquid or solid) | Cloud liquid water total column (< 100 (m) | Cloud ice effective radius profile |
| Freezing level height in clouds | Cloud drop effective radius profile | Cloud top height |
| Melting layer depth in clouds | Cloud ice profile | Cloud base height |

The recommended observing strategy is:

- to exploit the synergy with passive MW radiometers so as to limit the number of radar-equipped satellites to what is needed for having at least one radar of each type in orbit.

- since, in this concept, the radar is used to “calibrate” passive MW radiometers, the orbit should be non-sunsynchronous so as to intercept all sunsynchronous orbits of the GPM constellation.

The evolution of current and planned cloud and precipitation radar in LEO is shown below.

| Instrument class | Single frequency, nadir-only | Dual frequency, imaging | Single frequency, imaging |
| --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CPR (94 GHz) | Earth-CARE | 10:30 |  |  |  |  |  |  | X | X | X |  |  |  |  |  |  |
| CPR (94 GHz) | CloudSat | 13:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| PR (14 GHz) | TRMM | 35° | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| DPR (14 & 35 GHz) | GPM “core” | 65° |  |  |  |  |  | X | X | X | X | X | X |  |  |  |  |

| Comparative characteristics of cloud and precipitation radar in LEO |
| --- |
| Feature | PR (TRMM) | DPR (GPM “core”) | CPR (CloudSat) | CPR (Earth-CARE) |
| Frequency | 13.8 GHz | 13.6 GHz | 35.55 GHz | 94.05 GHz | 94.05 GHz, Doppler capability |
| Swath | 215 km | 245 km | 120 km | N/A | N/A |
| Vertical resolution | 250 m | 250 m | 250 m | 500 m | 400 m |
| IFOV | 4.3 km | 5.0 km | 5.0 km | 2 km | 1 km |

Comment (with focus on the 2020 range):

- No plan for any atmospheric radar after 2017.

Recommendations:

- To provide long-term continuity to the “core” satellite of the GPM constellation.

- For the 35 GHz component, non-scanning instruments additional to the scanning one on “core” GPM should be provided on some other satellite concurring to the GPM constellation, provided that the sensitivity is enhanced for the purpose of measuring light rain and rainfall in high latitudes.

- For the 94 GHz component, some follow-on of Earth-CARE and CloudSat should be provided.  Sensitivity is a priority requirement in respect of swath.

20.	LIDAR-BASED MISSIONS (for wind, for cloud/aerosol, for water vapour, for altimetry)

These missions are implemented by lidar of different characteristics depending on the type of addressed parameter: wind, cloud, aerosol, water vapour, ice topography.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of lidar for various observations from LEO (years 2020’s) |
| --- |
|  | Wavelength(s) | No. of channels | Resolution | Scanning |
| Doppler wind lidar | 355 nm | 2 (Mie & Rayleigh) | ~ 50 km | none (oblique) |
| Differential absorption lidar (DIAL) | 940 nm (H2O), 1.6 (m (CO2) ,.... plus nearby windows | 2 - 3 | ~ 50 km | none (nadir) |
| Aerosol profiling lidar | 1 or 2, 355 nm or 532 & 1064 nm | 3 (Mie co- & cross-polar, Rayleigh co-polar) | ~ 10 km | none (nadir) |
| Lidar altimeter | 2, e.g. 532 & 1064 nm | 2 | ~ 100 m | none (nadir) |

Addressed products are as follows.

| Geophysical parameters addressed by lidar in LEO |
| --- |
| Wind profile (horizontal vector) | Height of the tropopause | Aerosol optical depth profile | Aerosol type profile |
| Water vapour profile | Cloud top height | Total aerosol optical depth | Total aerosol type |
| Carbon dioxide profile | Cloud optical depth | Aerosol effective radius profile | PSC occurrence profile |
| Height of the top of the PBL | Cloud particle effective radius | Total aerosol effective radius | Sea ice thickness (from altimeter) |

The recommended observing strategy is:

- operational status to be pursued only for Doppler wind lidar, assuming satisfactory demonstration with ADM-Aeolus.  At least one satellite to be provided, possibly two to improve coverage and reliability;

- the other missions could stay, for the moment, in the R&D environment.

The evolution of current and planned lidar-based missions in LEO is shown below.

| Instrument class | Single wavelength | Two wavelengths | Doppler capability | Altimeter |
| --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ALADIN | ADM-Aeolus | 06:00 |  | X | X | X | X |  |  |  |  |  |  |  |  |  |  |
| ATLID | Earth-CARE | 10:30 |  |  |  |  |  |  | X | X | X |  |  |  |  |  |  |
| CALIOP | Calipso | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| GLAS | ICESat | 94° | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of lidars in LEO |
| --- |
| Feature | ALADIN (ADM-Aeolus) | ATLID (Eart-CARE) | CALIOP (Calipso) | GLAS (ICESat) |
| Wavelength(s) | 355 nm, High-Spectral Resolution Laser | 355 nm, High-Spectral Resolution Laser | 532 & 1064 nm | 532 & 1064 nm |
| FOV and sampling | 50 km each 200 km | 30 m each 100 m | 70 m each 333 m | 66 m each 170 m |
| Vertical resolution | 250 m to 2 km | 100 m | 30 m | 10 cm surface, 200 m cloud top |
| Viewing geometry | side-looking | 2° ahead along-track | nadir | nadir |

Comments (with focus on the 2020 range):

- No DIAL is currently operating or planned.  A proposal for CO2 (A-SCOPE) is being assessed.

- No follow-on mission is currently planned for ADM-Aeolus, pending demonstration.

- In general, no lidar-based mission is planned for the 2020 timeframe.

Recommendations:

- To focus efforts towards providing operational follow-on to ADM-Aeolus after successful mission demonstration.  This implies possible re-design of the mission in such a way as to improve effectiveness (specifically, observing cycle) and affordability.

- Also, to strengthen the observing capability of ADM-Aelous follow-on in respect of aerosol observation.

- As for lidar altimetry, to re-design a comprehensive mission in the overall context of the radar-based altimetry missions, including CryoSat.

21.	CROSS-NADIR SHORT-WAVE SPECTROMETRY (FOR CHEMISTRY) FROM LEO

This mission is implemented by UV/VIS/NIR/SWIR spectrometers designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of short-wave cross-nadir spectrometers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical SNR | Resolution | Swath | Scanning |
| 270 to 2400 nm | 0.05 to 0.8 nm | 8000-16000 | 1000 | 5-20 km | 2800 km | cross-track |

Addressed products are as follows.

| Geophysical parameters addressed by short-wave cross-nadir spectrometers in LEO |
| --- |
| Aerosol optical depth profile | O3 profile | BrO profile | H2O profile | CO2 profile | CO total column | SO2 total column |
| Total aerosol optical depth | O3 total column | NO2 profile | CH4 profile | CO2 total column | N2O profile | CH2O profile |
| Surface spectral reflectance | ClO profile | NO2 total column | CH4 total column | CO profile | SO2 profile | CH2O total column |

The recommended observing strategy is:

- at least two instruments on sunsynchronous satellites with LST in mid-morning and early afternoon.

The evolution of current and planned SW cross-nadir spectrometers in LEO is shown below.

| Instrument class | UV only, non-scanning | Limited to UV | Limited to UV/VIS | Close to post-2020 req. | Focus on few species |
| --- | --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| GOME-2 | MetOp 1-3 | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| TBD | Sentinel-5 | 09:30 |  |  |  |  |  |  |  |  |  |  |  |  |  | (X) | (X) |
| TOU/SBUS | FY-3 A/C/E/G | 10:00 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X |
| SCIAMACHY | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| SBUV/2 | NOAA-17 | 10:20 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| MOPITT | EOS-Terra | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| GOME | ERS-2 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| TANSO-FTS | GOSAT | 13:00 |  | X | X | X | X | X | X |  |  |  |  |  |  |  |  |
| OCO | OCO | 13:15 |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| OMPS-nadir | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| OMPS-nadir | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X |
| OMI | EOS-Aura | 13:45 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |
| SBUV/2 | NOAA 18 | 13:40 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| SBUV/2 | NOAA-19 | 14:00 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| TOU/SBUS | FY-3 B/D/F | 14:00 |  |  | X | X | X | X | X | X | X | X | X | X | X | X | X |

| Comparative characteristics of short-wave cross-nadir spectrometers in LEO |
| --- |
| Feature | ERS-2 GOME | MetOp GOME-2 | FY-3 TOU/SBUS | NOAA SBUV/2 | EOS-Terra MOPITT | Envisat SCIAMACHY | OCO | GOSAT TANSO-FTS | EOS-Aura OMI | NPOESS OMPS |
| Range | 240-790 nm | 240-790 nm | 250-360 nm | 250-340 nm | 2200-4700 nm | 240-2380 nm | 760-2080 nm | 750-2100 nm | 270-500 nm | 250-380 nm |
| (/(( | ~ 1500 | ~ 1500 | ~ 280 | ~ 300 | ~ 300 | ~ 1500 | ~ 20000 | ~ 25000 | ~ 700 | ~ 300 |
| Swath | 120-960 km | 960-1920 km | 3000 km | none | 640 km | 1000 km | 10 km | 790 km | 2600 km | 2800 km |
| IFOV ssp | 40 x 40 km2, 40 x 320 km2 | 40 x 40 km2, 40 x 80 km2 | 50 km (TOU), 200 km (SBUS) | 170 km | 22 km | 16 x 32 km2 | 1.29 x 2.25 km2 | 10.5 km | 13 x 24 km2, 36 x 48 km2 | 50 km, 250 km |

Comments (with focus on the 2020 range):

- The only instrument approaching post-2020 requirements is SCIAMACHY on Envisat, not available in the 2020 timeframe.  A “Sentinel-5” mission is being considered by ESA to provide continuity.

- The only instruments currently planned for the 2020 timeframe, both in the mid-morning and early afternoon orbits, are TOU/SBUS on FY-3 and OMPS on NPOESS, both limited to UV and nearly exclusively addressing ozone.

Recommendations:

- To materialise the Sentinel-5 programme and make provision for its long-term continuity.

- To continue flying at least a couple of instruments limited to UV for more frequent observation of O3.

22.	CROSS-NADIR SHORT-WAVE SPECTROMETRY (FOR CHEMISTRY) FROM GEO

This mission is implemented by UV/VIS/NIR spectrometers designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of short-wave cross-nadir spectrometers in GEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical SNR | Resolution | Observing cycle |
| 290 to 800 nm | 0.05 to 1 nm | 3000-5000 | 500-2000 | 5-10 km | 30-60 min (for areas 5000 x 3000 km2) |

Addressed products are as follows (nearly the same as from LEO, with possibly somewhat lower quality, but much more frequently).

| Geophysical parameters addressed by short-wave cross-nadir spectrometers in GEO |
| --- |
| Aerosol optical depth profile | Surface spectral reflectance | O3 profile | NO2 profile | SO2 profile | CH2O profile |
| Total aerosol optical depth | BrO profile | O3 total column | NO2 total column | SO2 total column | CH2O total column |

The recommended observing strategy is:

- no need for international coordination, except among countries in the same field of view: in fact, it is a mission for local/regional purposes.

The evolution of current and planned SW cross-nadir spectrometers in GEO is shown below.

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TBD | Sentinel-4 | 0° |  |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) |

Comment (with focus on the 2020 range):

- The only plan currently being pursued for UV/VIS spectroscopy from GEO is the ESA “Sentinel-5”, not yet fully defined and approved.

Recommendation:

- To materialise the Sentinel-4 programme and make provision for its long-term continuity.

23.	CROSS-NADIR IR SPECTROMETRY (FOR CHEMISTRY) FROM LEO

This mission is implemented by IR spectrometers designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of very-high-spectral-resolution IR cross-nadir spectrometers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical NE(T | Resolution | Swath | Scanning |
| 3.3 to 16 µm | 0.05-0.1 cm-1 | 10000-20000 | 0.1 K @ 280 K | 5-20 km | 2800 km | cross-track |

Addressed products are as follows.

| Geophysical parameters addressed by very-high-spectral-resolution IR cross-nadir spectrometers in LEO |
| --- |
| Air temperature profile | O3 profile | NO2 profile | CO2 profile | N2O profile | N2O5 profile |
| H2O profile | O3 total column | NO2 total column | CO2 total column | N2O total column | SF6 profile |
| H2O total column | HNO3 profile | CH4 profile | CO profile | SO2 profile | C2H6 profile |
| PAN profile | HNO3 total column | CH4 total column | CO total column | SO2 total column | C2H2 profile |

The recommended observing strategy is:

- considering that there will be operational IR spectrometer sounders for the basic temperature/humidity sounding mission, it will be sufficient to have one additional high-spectral-resolution sounder for atmospheric chemistry.

The evolution of current and planned IR cross-nadir spectrometers in LEO is shown below.

| Instrument class | Total columns possible | Closest to post-2020 req. | Marginal spectral resolution |
| --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CrIS | NPOESS 2&4 | 05:30 |  |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) |
| IASI | MetOp 1-3 | 09:30 | X | X | X | X | X | X | X | X | X | X | X | X | X | X |  |
| IRFS-2 | Meteor-M2 | 10:20 |  | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| TANSO | GOSAT | 13:00 |  | X | X | X | X | X | X |  |  |  |  |  |  |  |  |
| AIRS | EOS-Aqua | 13:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| CrIS | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| CrIS | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | X | X | X | X | X | X | X | X | X |
| TES-nadir | EOS-Aura | 13:45 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of IR cross-nadir spectrometers in LEO |
| --- |
| Feature | NPOESS CrIS | MetOp IASI | Meteor-M2 IRFS-2 | GOSAT TANSO-FTS | GOSAT TANSO-CAI | EOS-Aqua AIRS | EOS-Aura TES-nadir |
| Range | 3.92-15.40 (m | 3.62-15.50 (m | 5-15 (m | 0.76-14.3 (m | 0.38-1.6 (m | 3.74-15.40 (m | 3.28-15.38 (m |
| Spectral resolution | 0.625 to 2.5 cm-1 | 0.25 cm-1 | 0.5 cm-1 | 0.2 cm-1 | 4 channels | 0.5 to 2.0 cm-1 | 0.06 cm-1 |
| Swath | 2200 km | 2130 km | 1000 or 2500 km | 790 km | 1000 km | 1650 km | 885 km |
| IFOV ssp | 14 km | 12 km | 35 km | 10.5 km | 0.5-1.5 km | 13.5 km | 0.53 x 5.3 km2 |

Comments (with focus on the 2020 range):

- The only instrument approaching post-2020 requirements would be TES on EOS-Aura, not available in the 2020 timeframe.

- The only instrument currently considered for the 2020 timeframe is CrIS on NPOESS, with marginal spectral resolution for chemistry, and not baselined in the early morning.

- As IASI follow-on, consideration is given to an option for improved spectral resolution to cover atmospheric chemistry requirements.  On Sentinel-4 the Thermal IR range is not currently considered.

Recommendation:

- To provide a follow-on to the EOS-Aura TES.  To be noted that, without a very-high spectral resolution IR sounder, species such as HNO3. SF6, N2O5, PAN, C2H6 and C2H2 could not be observed.

24.	CROSS-NADIR IR SPECTROMETRY (FOR CHEMISTRY) FROM GEO

This mission is implemented by IR spectrometers designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of very-high-spectral resolution IR sounders in GEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical NE(T | Resolution | Observing cycle |
| 3.6 to 15 µm | 0.1-0.2 cm-1 | 5000-10000 | 0.1 K @ 280 K | 5-10 km | 30-60 min (for areas 5000 x 3000 km2) |

Addressed products are as follows (nearly the same as from LEO, with possibly somewhat lower quality, but much more frequently).

| Geophysical parameters addressed by very-high-spectral resolution IR sounders in GEO |
| --- |
| Air temperature profile | O3 profile | NO2 profile | CO2 profile | N2O profile |
| H2O profile | O3 total column | NO2 total column | CO2 total column | N2O total column |
| H2O total column | HNO3 profile | CH4 profile | CO profile | SO2 profile |
| PAN profile | HNO3 total column | CH4 total column | CO total column | SO2 total column |

The recommended observing strategy is:

- no need for international coordination, except among countries in the same field of view: in fact, it is a mission for local/regional purposes.

The evolution of current and planned IR cross-nadir spectrometers in GEO is shown below.

| Instrument class | Marginal spectral resolution |
| --- | --- |

| Instrument | Satellite | Long. | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IRS | Meteosat 12( | 0° |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| Sounder TBD | FY-4 O/A( | 86.5°E |  |  |  |  |  | X | X | X | X | X | X | X | X | X | X |
| Sounder TBD | FY-4 O/B( | 123°E |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |
| Sounder TBD | MTSAT 3( | 140°E |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |
|  |  | 180°E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| HES | GOES-17 | 135°W |  |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) |
| HES | GOES-16 ® | 75°W |  |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) |

| Comparative characteristics of very-high-spectral-resolution IR sounders in GEO |
| --- |
| Feature | Meteosat 3rd Generation IRS | GOES-R HES |
| Range | 4.6-14.3 (m | 3.68-15.4 (m |
| Channels | 1736 | 1508 |
| Spectral resolution | 0.625 cm-1 | 0.5 to 2.5 cm-1 |
| Cycle (full disk) | 30 min | 60 min |
| IFOV IR | 4 km | 2-20 km |

Comments (with focus on the 2020 range):

- No planned IR spectrometer sounder for GEO has enough high spectral resolution to meet post-2020 requirements from atmospheric chemistry.

- With the spectral resolution of currently planned IR sounders only total columns of few species will be observable.

Recommendation:

- If a requirement exists for frequent profiles of, e.g., HNO3, or if certain species need frequent observation in nigh time, the need for high-spectral-resolution IR sounding from GEO should be re-assessed.

25.	LIMB-SOUNDING SHORT-WAVE SPECTROMETRY

This mission is implemented by UV/VIS/NIR/SWIR spectrometers designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of short-wave limb-sounding spectrometers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical SNR | Resolution | Scanning |
| 270 to 2400 nm | 0.05 to 0.8 nm | 8000-16000 | 1000 | 2 km (vertical) | limb |

Addressed products are as follows.

| Geophysical parameters addressed by short-wave limb-sounding spectrometers in LEO |
| --- |
| Air temperature profile | O3 profile | NO2 profile | CO2 profile |
| Water vapour profile | ClO profile | H2O profile | N2O profile |
| Aerosol optical depth profile | BrO profile | CH4 profile | PSC occurrence profile |

The recommended observing strategy is:

- at least one instrument on a sunsynchronous satellite should be provided, to provide the necessary high vertical resolution in the stratosphere and above;

- at least the spectral range needed for ozone (UV/VIS) should be covered.

The evolution of current and planned SW limb-sounding spectrometers in LEO is shown below.

| Instrument class | Limited to UV/VIS/NIR | Closest to post-2020 req. | Occultation |
| --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SCIAMACHY | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| GOMOS | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| POAM-3 | SPOT-4 | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| OMPS-limb | NPP | 13:30 |  |  | X | X | X | X | X | X |  |  |  |  |  |  |  |
| OMPS-limb | NPOESS 1&3 | 13:30 |  |  |  |  |  |  | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) | (X) |

| Comparative characteristics of short-wave limb-sounding spectrometers in LEO |
| --- |
| Feature | Envisat SCIAMACHY-limb | Envisat GOMOS (occultation of stars) | SPOT-4 POAM-3 (occultation of sun) | NPOESS OMPS-limb |
| Range | 240-2380 nm | 248-956 nm | 350-1024 nm | 290-1000 nm |
| Resolving power (/(( | ~ 1500 | ~ 500 | 9 channels | ~ 200 |
| Vertical resolution | 3 km, range 10-100 km | 1.7 km, range 20-100 km | 0.6 km, range 10-60 km | 1 km, range 10-60 km |
| Horizontal coverage | swath:1000 km | ~ 500 occultations/day | few 10’s occultations/day | swath: 750 km |

Comments (with focus on the 2020 range):

- The only instrument approaching post-2020 requirements is SCIAMACHY on Envisat, not available in the 2020 timeframe.  The “Sentinel-5” mission being considered by ESA is not currently including a SW limb-sounding component.

- The only instrument planned for the 2020 timeframe was OMPS on NPOESS, limited to UV/VIS and nearly exclusively addressing ozone.  However, the limb-sounding component, now recovered for NPP, is no longer in the baseline for NPOESS.

Recommendations:

- To revise the situation of certain important trace species (e.g., ClO and BrO) that, in the stratosphere, in the absence of a SW limb sounder, could only be observed in the Sub-mm range for which, however, there is no plan currently being pursued (only proposals such as “PREMIER”).

- To confirm at least an ozone limb-sounder (e.g., OMPS on NPOESS).

26.	LIMB-SOUNDING INFRARED SPECTROMETRY

This mission is implemented by very-high-spectral-resolution sounders operated in limb mode, designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of limb-sounding IR spectrometers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical NE(T | Resolution | Scanning |
| 3.3 to 16 (m | 0.1 cm-1 | ~ 20000 | 0.1 K @ 200 K | 2 km (vertical) | limb |

Addressed products are as follows.

| Geophysical parameters addressed by limb-sounding IR spectrometers in LEO |
| --- |
| Air temperature profile | HNO3 profile | H2O profile | CO2 profile | SF6 profile |
| O3 profile | NO2 profile | CH4 profile | N2O profile | PSC occurrence profile |

The recommended observing strategy is:

- at least one instrument on a sunsynchronous satellite should be provided, to provide the necessary high vertical resolution in the stratosphere and above.

The evolution of current and planned IR limb-sounding spectrometers in LEO is shown below.

| Instrument class | Closest to post-2020 req. | Spectroradiometer |
| --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MIPAS | Envisat | 10:00 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| HIRDLS | EOS-Aura | 10:00 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |
| TES-limb | EOS-Aura | 13:45 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of limb-sounding IR spectrometers in LEO |
| --- |
| Feature | MIPAS (Envisat) | HIRDLS (EOS-Aura) | TES-limb (EOS-Aura) |
| Range | 4.15-14.6 (m | 6.12-17.76 (m | 3.28-15.38 (m |
| Spectral resolution | 0.035 cm-1 | 21 channels | 0.015 cm-1 |
| Vertical resolution | 3 km, range 5-150 km | 1 km, range 10-100 km | 2.3 km, range 0-37 km |
| Horizontal coverage | two views (fore- and side) | 2000-3000 km | none |

Comments (with focus on the 2020 range):

- Both the Envisat MIPAS and the EOS-Aura TES approach post-2020 requirements, but none will be available in the 2020 timeframe.  The “Sentinel-5” mission being considered by ESA is not currently including an IR limb-sounding component (or a SW limb sounder).

- Without limb sounders the vertical resolution required in the stratosphere and above cannot be achieved in any way.

Recommendation:

- To revise the situation of certain important trace species (e.g., HNO3) that, in the stratosphere, in the absence of an IR limb sounder, could only be observed in the Sub-mm range for which, however, there is no plan currently being pursued (only proposals such as “PREMIER”).

27.	LIMB-SOUNDING SUBMILLIMETRE SPECTROMETRY

This mission is implemented by limb sounders exploiting millimetre-submillimetre wavelengths, designed for use in atmospheric chemistry.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of limb-sounding mm-submm spectrometers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of bands / channels | Typical NE(T | Resolution | Scanning |
| 100 to 3000 GHz | 5-50 MHz | 5-10 bands, 500-2000 channels | 0.1 K @ 200 K | 2 km (vertical) | limb |

Addressed products are as follows.

| Geophysical parameters addressed by limb-sounding mm-submm spectrometers in LEO |
| --- |
| Air temperature profile | O3 profile | BrO profile | HCl profile | N2O profile |
| H2O profile | ClO profile | HNO3 profile | H2O profile | HDO profile |

The recommended observing strategy is:

- at least one instrument on a sunsynchronous satellite should be provided, to provide the necessary high vertical resolution in the stratosphere and above.

The evolution of current and planned mm-submm limb-sounding spectrometers in LEO is shown below.

| Instrument class | Close to post-2020 |
| --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MLS | EOS-Aura | 10:00 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |

| Comparative characteristics of limb-sounding mm-submm spectrometers in LEO |
| --- |
| Feature | MLS (EOS-Aura) |
| Bands and channels | Five bands: 118, 190, 240, 640 and 2500 GHz; for a total of ~ 1000 channels |
| Spectral resolution | 10 MHz |
| Vertical resolution | 1.5 km, range 5-120 km |

Comments (with focus on the 2020 range):

- The EOS-Aura MLS approaches post-2020 requirements, but will not be available in the 2020 timeframe.  The “Sentinel-5” mission being considered by ESA is not currently including an mm-submm limb-sounding component (nor SW and IR limb sounders).

- Without limb sounders the vertical resolution required in the stratosphere and above cannot be achieved in any way.

- Mm-submm and IR limb sounding are only at the stage of proposal (“PREMIER” in the ESA Earth Explorer missions), currently being assessed.

Recommendation:

- To revise the situation of certain important trace species (e.g., HCl and HDO) that can only be observed in the mm-submm range; but also of ClO and BrO, that are best observed in mm-submm.

28.	HIGH-RESOLUTION SHORT-WAVE IMAGERY FOR LAND OBSERVATION

This mission is implemented by imagers exploiting a variety of trade-offs between geometric resolution and swath, often offering the flexibility of in-flight selection of the area to be observed.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of high-resolution short-wave imagers in LEO (years 2020’s) |
| --- |
| Spectral range | Spectral resolution | No. of channels | Typical SNR | Resolution | Scanning |
| 0.5 to 1.6 nm | 20 nm | 5 to 10 | 50 @ 0.5 % albedo | < 1 to > 10 m | pushbroom |

Addressed products are as follows.

| Geophysical parameters addressed by high-resolution short-wave imagers in LEO |
| --- |
| Soil type | Photosynthetically Active Radiation (PAR) | Leaf Area Index (LAI) | Glacier cover |
| Vegetation type | Fractional Absorbed PAR (FAPAR) | Fire fractional cover | Snow cover |
| Fraction of vegetated land | Normalised Difference Vegetation Index (NDVI) | Sea-ice cover | Oil spill cover |

The recommended observing strategy is:

- to rely on programmes managed by R&D space agencies, since there are many, and are run with a fair degree of continuity;

- to complement, when necessary, with data from programmes run by private companies, that generally cover resolution ranges of the order of 1 m or less.

The evolution of current and planned high-resolution short-wave imagers in LEO is extremely variegated. Only programmes managed by CGMS-member space agencies are recorded below.  This implies that resolutions of the order of 1 m or less, that are managed by private companies, are not included.  Two instruments have been fit, that actually are not only short-wave (ASTER) or do not have high resolution (Vegetation); the reason is that in this text there isn’t another category where they fit better.

| Instrument class | IFOV > 10 m pointing many channels | IFOV > 10 m pointing many channels including TIR | IFOV > 10 m narrow swath hyperspectral | IFOV > 10 m large swath many channels | IFOV > 10 m large swath few channels | IFOV < 10 m pointing few channels | IFOV < 10 m not pointing few channels | IFOV ~ 1 km wide swath few channels |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MSS, TM | Landsat-5 | 10:00 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ETM+ | Landsat-7 | 10:00 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| OLI | LDCM | 10:00 |  |  |  | X | X | X | X | X | X | X | X | X | X | X |  |
| ALI, LAC | NMP EO-1 | 10:15 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hyperion | NMP EO-1 | 10:15 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| KMSS | Meteor-M 1/2 | 10:20 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| ASTER | EOS-Terra | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| HRV | SPOT-2 | 10:30 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| HRVIR | SPOT-4 | 10:30 | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| HRG, HRS | SPOT-5 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| Vegetation | SPOT 4 & 5 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| HiRI | Pléiades 1/2 | 10:30 |  |  | X | X | X | X | X | X | X | X |  |  |  |  |  |
| MSI | Sentinel-2 1/2 | 10:30 |  |  |  |  |  | X | X | X | X | X | X | X | X | X |  |
| AVNIR-2, PRISM | ALOS | 10:30 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |
| PAN, MS | Monitor-E | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| PAN-A, PAN-F | CartoSat 1 | 10:30 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| PAN | CartoSat 2 | 10:30 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| LISS-3, LISS-4 | ResourceSat 1/2 | 10:30 | X | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| AWiFS | ResourceSat 1/2 | 10:30 | X | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| Geoton | Resurs-DK | 70° | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |

Comment (with focus on the 2020 range):

- Apparently there isn’t and there will not be a problem of data availability.

Recommendation:

- To ensure that data access is friendly and costs and delivery time are minimal.

29.	SYNTHETIC APERTURE RADAR

This mission is implemented by side-looking radar associated to special signal analysis that enables achieving very-high resolution imagery.  The technology implies very restrictive conditions that require exploiting a variety of trade-offs between frequency, geometric resolution, swath and polarisation.  Frequency is the parameter that mostly characterises the measurement objectives.  Modern SAR’s offer large flexibility of in-flight alternating the operating mode: but not the frequency, which therefore is used here for the top-level instrument classification.  Generic characteristics of the instruments are listed as follows.

| Generic characteristics of SAR imagers in LEO (years 2020’s) |
| --- |
| Type | Frequency | Resolution | Swath | Polarisations | Scanning |
| L-band | ~ 1.4 GHz | 10-30 m associated to narrow swath; ~ 1 km associated to large swath | 50-100 km associated to high resolution; ~ 400 km associated to coarse resolution | HH or VV, or alternating: VV/HH, HH/HV, VV/VH | pushbroom |
| C-band | ~ 5.4 GHz |  |  |  |  |
| X-band | ~ 9.5 GHz |  |  |  |  |

Addressed products, mostly conditioned by the adopted frequency, are as follows.

| Geophysical parameters addressed by SAR imagers in LEO (depending on frequency) |
| --- |
| Soil moisture at surface | Fraction of vegetated land | Ocean ice sheet topography | Wave - Directional energy frequency spectrum |
| Soil moisture at surface (index) | Glacier cover | Sea-ice cover | Wave - Dominant direction |
| Soil moisture in the roots region | Vegetation type | Sea-ice cover (all-weather) | Wave - Dominant period |
| Snow status (wet/dry) | Soil type | Sea-ice thickness | Wave - Significant height |
| Snow water equivalent | Fire fractional cover | Sea-ice type | Oil spill cover |

The recommended observing strategy is:

- to rely on programmes managed by R&D space agencies, since there are many, and are run with a fair degree of continuity.

The evolution of current and planned SAR’s in LEO is shown below.  The German X-band SAR-Lupe constellation of 5 satellites (first already in orbit) is not listed since military-classified.  The Italian X-band COSMO-SkyMed is included because dual-use (military and civilian).

| Instrument class | C-band, non-multiparameter | X-band, non-multiparameter | L-band, multiparameter | C-band, multiparameter | X-band, multiparameter |
| --- | --- | --- | --- | --- | --- |

| Instrument | Satellite | LST | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | → |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SAR | RadarSat-1/2 | 06:00 | X | X | X | X | X | X | X | X |  |  |  |  |  |  |  |
| SAR-2000 | COSMO-SkyMed 1/4 | 06:00 | X | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| SAR-L | SAOCOM 1/2 | 06:00 |  | X | X | X | X | X | X | X | X |  |  |  |  |  |  |
| SAR-C | GMES 1/2 | 06:00 |  |  |  |  | X | X | X | X | X | X | X | X |  |  |  |
| Severjanin | Meteor 1/2 | 10:20 | X | X | X | X | X | X |  |  |  |  |  |  |  |  |  |
| AMI-SAR | ERS-2 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| AMI-Wave | ERS-2 | 10:30 | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |
| ASAR | Envisat | 10:30 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| ASAR-Wave | Envisat | 10:30 | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |
| PALSAR | ALOS | 10:30 | X | X | X | X | X |  |  |  |  |  |  |  |  |  |  |

Comments (with focus on the 2020 range):

- Continuing availability of C-band SAR, still the most popular, seems to be secured, especially if long-term continuity is provided to GMES-1 (former Sentinel-1).

- L-band SAR, the most useful for hydrology, seems to have attracted sufficient interest (see the Japanese ALOS/PALSAR and the Argentinean SAOCom).  It is hoped that it could have long-term continuity.

- X-band SAR, the most useful for recognition, is likely to be continued in the long-term, also thanks to the dual interest (civilian and military).

Recommendation:

To ensure that data access is friendly and costs and delivery time are minimal.

ANNEX 1

Table of geophysical parameters v/s remote sensing techniques

The attached table (two sheets) records in matrix form the relevance of the various instruments types (the 29 ones defined in this document) to the various geophysical parameters (127 have been identified in this document).  The information content is the same as what can be found in the second table of each instrument/mission Section (“Geophysical parameters addressed by ………”).

| Geophysical parameters and possible remote sensing techniques (sheet 1 of 2) |
| --- |
| Instrument type Geophysical parameter | 01. Multi-purpose VIS/IR imagery from LEO | 02. Multi-purpose VIS/IR imagery from GEO | 03. IR temperature/humidity sounding from LEO | 04. IR temperature/humidity sounding from GEO | 05. MW temperature/humidity sounding from LEO | 06. MW temperature/humidity sounding from GEO | 07. Conical-scanning MW imagery (mid-frequencies) | 08. Low-frequency MW imagery | 09. Radio occultation sounding | 10. Earth radiation budget from LEO | 11. Earth radiation budget from GEO | 12. Wind scatterometry | 13. Radar altimetry | 14. Ocean colour imagery from LEO | 15. Ocean colour imagery from GEO | 16. Imagery with special viewing geometry | 17. Lightning imagery from LEO | 18. Lightning imagery from GEO | 19. Cloud and precipitation radar | 20. Lidar-based missions (Doppler, backscatter, DIAL, ALT) | 21. Cross-nadir short-wave spectrometry from LEO | 22. Cross-nadir short-wave spectrometry from GEO | 23. Cross-nadir IR spectrometry from LEO | 24. Cross-nadir IR spectrometry from GEO | 25. Limb-sounding short-wave spectrometry | 26. Limb-sounding IR spectrometry | 27. Limb-sounding Sub-millimetre wave spectrometry | 28. High-resolution SW imagery for land observation | 29. Synthetic Aperture Radar |
| Temperature profile |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X |  |  |
| Temperature profile (nearly-all-weather) |  |  |  |  | X | X |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Water vapour (profile) |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | X | X |  |  | X |  |  |
| Water vapour (profile) (nearly-all-weather) |  |  |  |  | X | X |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Water vapour (total column) | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Water vapour (total column) (nearly-all-weather) |  |  |  |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wind at level of tracer (cloud, water vapour patch) |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wind over sea surface |  |  |  |  |  |  | X | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wind profile |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
| Height of the top of the PBL |  |  | X | X |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
| Height of the tropopause |  |  | X | X |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |
| Pressure profile |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Water vapour imagery | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cloud imagery | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cloud top height | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |  |  |
| Cloud top temperature | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cloud type | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cloud cover (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud cover (total column) | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cloud base height |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud optical depth | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X |  |  |  |  |  |  |  |  |  |
| Cloud liquid water (< 100 (m) (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud liquid water (< 100 (m) (total column) |  |  |  |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud drop effective radius (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud drop effective radius (top of cloud) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | X | X |  |  |  |  |  |  |  |  |  |
| Cloud ice (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud ice (total column) |  |  |  |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud ice effective radius (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Cloud ice effective radius (top of cloud) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  | X | X |  |  |  |  |  |  |  |  |  |
| Freezing level height |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Melting layer depth |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Precipitation accumulated at surface (index) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Precipitation profile (liquid and solid) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Precipitation rate at surface (liquid or solid) |  |  |  |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |
| Lightning detection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |
| Aerosol optical depth (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X | X |  |  |  |  |  |  |  |
| Aerosol optical depth (total column) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X | X |  |  |  |  |  |  |  |
| Aerosol effective radius (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X | X |  |  |  |  |  |  |  |
| Aerosol effective radius (total column) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X | X |  |  |  |  |  |  |  |
| Aerosol type (profile) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X | X |  |  |  |  |  |  |  |
| Aerosol type (total column) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  | X | X | X |  |  |  |  |  |  |  |
| Downwelling solar irradiance at TOA |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Outgoing spectral radiance at TOA |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Outgoing long-wave irradiance at TOA |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Outgoing short-wave irradiance at TOA |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Short-wave cloud reflectance | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Downwelling LW irradiance at Earth’s surface |  |  | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Downwelling SW irradiance at Earth’s surface | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Earth’s surface albedo | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Photosynthetically Active Radiation (PAR) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  | X |  |
| Fractional Absorbed PAR (FAPAR) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  | X |  |
| SW Earth’s surface bi-directional reflectance |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ocean topography |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ocean ice sheet topography |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Chlorophyll concentration |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Colour Dissolved Organic Matter (CDOM) |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Diffuse Attenuation Coefficient (DAC) |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Suspended sediments concentration |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Oil spill cover |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Wave directional energy frequency spectrum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Dominant wave direction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Dominant wave period |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Significant wave height |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |

| Geophysical parameters and possible remote sensing techniques (sheet 2 of 2) |
| --- |
| Instrument type Geophysical parameter | 01. Multi-purpose VIS/IR imagery from LEO | 02. Multi-purpose VIS/IR imagery from GEO | 03. IR temperature/humidity sounding from LEO | 04. IR temperature/humidity sounding from GEO | 05. MW temperature/humidity sounding from LEO | 06. MW temperature/humidity sounding from GEO | 07. Conical-scanning MW imagery (mid-frequencies) | 08. Low-frequency MW imagery | 09. Radio occultation sounding | 10. Earth radiation budget from LEO | 11. Earth radiation budget from GEO | 12. Wind scatterometry | 13. Radar altimetry | 14. Ocean colour imagery from LEO | 15. Ocean colour imagery from GEO | 16. Imagery with special viewing geometry | 17. Lightning imagery from LEO | 18. Lightning imagery from GEO | 19. Cloud and precipitation radar | 20. Lidar-based missions (Doppler, backscatter, DIAL, ALT) | 21. Cross-nadir short-wave spectrometry from LEO | 22. Cross-nadir short-wave spectrometry from GEO | 23. Cross-nadir IR spectrometry from LEO | 24. Cross-nadir IR spectrometry from GEO | 25. Limb-sounding short-wave spectrometry | 26. Limb-sounding IR spectrometry | 27. Limb-sounding Sub-millimetre wave spectrometry | 28. High-resolution SW imagery for land observation | 29. Synthetic Aperture Radar |
| Sea surface salinity |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sea surface temperature | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sea surface temperature (all-weather) |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sea-ice cover | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Sea-ice cover (all-weather) |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Sea-ice surface temperature | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sea-ice surface temperature (all-weather) |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sea-ice thickness |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  | X |
| Sea-ice type |  |  |  |  |  |  | X | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Land surface temperature | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Land surface temperature (all-weather) |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Fire fractional cover | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Fire radiative power | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Fire temperature | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Frozen soil and permafrost | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Fraction of vegetated land |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Vegetation type |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Leaf Area Index (LAI) | X | X |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |
| Normalised Difference Vegetation Index (NDVI) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |
| Soil emissivity in TIR window channels | X | X | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Soil moisture at surface |  |  |  |  |  |  | X | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Soil moisture at surface (index) | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Soil moisture in the roots region |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Glacier cover |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Soil type |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |
| Snow albedo | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Snow cover | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |
| Snow cover (all-weather) |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Snow status (wet/dry) |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Snow surface temperature | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Snow surface temperature (all-weather) |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Snow water equivalent |  |  |  |  |  |  | X |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |
| Solid Earth – Geoid’s undulations |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Solid Earth - Gravity anomalies |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Space Weather - Electron density profile |  |  |  |  |  |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Space Weather - Total Electron Content (TEC) |  |  |  |  |  |  |  |  | X |  |  |  | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Greenhouse & chemically active gas: O3 profile |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X |  |  |
| Greenhouse & chemically active gas: O3 total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Chemically active species: BrO profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  | X |  | X |  |  |
| Chemically active species: C2H2 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |
| Chemically active species: C2H6 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |
| Chemically active species: CH2O profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |
| Chemically active species: CH2O total column |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |  |  |
| Chemically active species: ClO profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  | X |  | X |  |  |
| Chemically active species: HCl profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |
| Chemically active species: HDO profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  |  |
| Chemically active species: HNO3 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  | X | X |  |  |
| Chemically active species: HNO3 total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |
| Chemically active species: N2O5 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |
| Chemically active species: NO2 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |  |  |  |
| Chemically active species: NO2 total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Chemically active species: PAN profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  |
| Chemically active species: PSC occurrence profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X |  |  | X | X |  |  |  |
| Chemically active species: SF6 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X |  | X |  |  |  |
| Chemically active species: SO2 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Chemically active species: SO2 total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Greenhouse gas: CH4 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X |  |  |  |
| Greenhouse gas: CH4 total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Greenhouse gas: CO profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Greenhouse gas: CO total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Greenhouse gas: CO2 profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X |  |  |  |
| Greenhouse gas: CO2 total column |  |  | X | X |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X |  |  |  |  |  |
| Greenhouse gas: H2O profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X | X |  |  |
| Greenhouse gas: N2O profile |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | X | X | X | X | X | X | X |  |  |

ANNEX 2

INFORMATION ON SATELLITES AND INSTRUMENTS

CONTENTS:

List of satellites mentioned in the main text, including information on:

- launch date (actual or expected)

- expected end of service

- orbital height (for LEO)

- Local Solar Time (LST) for sunsynchronous orbits, at the ascending (a) or descending (d) equatorial node; or orbital inclination for non-sunsynchronous orbits; or longitude of stationariness for GEO

- status of the satellite at the reference date of September 2006

- reference to the instruments mentioned in the main text, carried by the satellite.

List of instruments mentioned in the main text, including information on:

- deployment of the acronym

- satellites hosting the instrument (including those no longer operational)

- period of utilisation (including previous years if the instrument is the continuation of a series).

Instrument tables, including information on:

- satellites hosting the instrument (also if no longer active)

- status of development of the instrument and utilisation period

- addressed mission

- instrument type

- scanning technique

- time for global coverage (observing cycle)

- geometric resolution

- resources required to the platform (mass, power, data rate) (if the information is available)

- channels characteristics: spectral range, spectral resolution (or bandwidths), radiometric accuracy, polarisation, geometric resolution if changing with channel.

Areas of missing information are highlighted by “yellow” colour.

| List of satellites mentioned in the gap analysis text (sheet 1 of 3) |
| --- |
| Satellite | Launch | End of service | Height | LST/incl. | Status | Instruments mentioned in the text |
| ACRIMSat | 20 Dec 1999 | expected ( 2011 | 703 km | 10:50 d | Operational | ACRIM-III |
| ADM-Aeolus | Sep-2008 | expected ( 2011 | 400 km | 06.00 d | Being built | ALADIN |
| ALOS | 24 Jan 2006 | expected ( 2010 | 692 km | 10:30 d | Operational | PRISM, AVNIR-2, PALSAR |
| CALIPSO | 28 Apr 2006 | expected ( 2009 | 705 km | 13:30 a | Operational | CALIOP |
| CartoSat-1 | 5 May 2005 | expected ( 2010 | 618 km | 10:30 d | Operational | PAN-A, PAN-F |
| CartoSat-2 | 10 Jan 2007 | expected ( 2012 | 635 km | 10:30 d | Operational | PAN |
| CHAMP | 15 Jul 2000 | expected ( 2009 | 450 km | 87° | Operational | BlackJack |
| CloudSat | 28 Apr 2006 | expected ( 2008 | 705 km | 13:30 a | Operational | CPR |
| COMS-1 | 2008 | expected ( 2015 | GEO, 128°E | or 116°E | Being built | MI, GOCI |
| COMS-2 | 2014 | expected ( 2021 | GEO, 128°E | or 116°E | Being defined | IMAGER TBD, GOCI |
| Coriolis | 6 Jan 2003 | expected ( 2009 | 830 km | 06:00 d | Operational | WindSat |
| COSMIC (6 satellites) | 14 Apr 2006 | expected ( 2011 | 800 km | 71° | Operational | IGOS |
| COSMO-SkyMed-1 | 8 Jun 2007 | expected ( 2012 | 619 km | 06:00 d | Just launched | SAR-2000 |
| COSMO-SkyMed-2 | end-2007 | expected ( 2013 | 619 km | 06:00 d | Close to launch | SAR-2000 |
| COSMO-SkyMed-3 | mid-2008 | expected ( 2014 | 619 km | 06:00 d | Built | SAR-2000 |
| COSMO-SkyMed-4 | early-2009 | expected ( 2015 | 619 km | 06:00 d | Being built | SAR-2000 |
| CryoSat-2 | Mar-2009 | expected ( 2012 | 717 km | 92° | Being built | SIRAL |
| DMSP-F15 | 24 Mar 1995 | expected ( 2007 | 850 km | 06.30 d | Operational | SSM/I |
| DMSP-S16 | 18 Oct 2003 | expected ( 2008 | 833 km | 08.10 d | Operational | SSMIS |
| DMSP-S17 | 2007 | expected ( 2012 | 833 km | 05.30 d | Close to launch | SSMIS |
| DMSP-S18 | 2008 | expected ( 2013 | 833 km | 08.00 d | Being built | SSMIS |
| DMSP-S19 | 2010 | expected ( 2015 | 833 km | 05.30 d | Planned | SSMIS |
| DMSP-S20 | 2012 | expected ( 2017 | 833 km | 05.30 d | Planned | SSMIS |
| Earth-CARE | Dec-2012 | expected ( 2015 | 450 km | 10.30 d | Planned | ATLID, CPR |
| Elektro-L-1 | 2007 | expected ( 2014 | GEO, | 76°E | Close to launch | MSU-GS |
| Elektro-L-2 | 2010 | expected ( 2017 | GEO, 76°E | or 14.5°E | Planned | MSU-GS |
| Elektro-L-3 | 2015 | expected ( 2022 | GEO, 76°E | or 14.5°E | Planned | MSU-GS |
| Envisat | 1 Mar 2002 | expected ( 2010 | 800 km | 10.00 | Operational | ASAR, RA-2, AATSR, MWR, MERIS, MIPAS, GOMOS, SCIAMACHY |
| EOS-Aqua | 4 May 2002 | expected ( 2009 | 705 km | 13:30 a | Operational | MODIS, CERES, AIRS, AMSU-A, HSB, AMSR-E |
| EOS-Aura | 15 Jul 2004 | expected ( 2011 | 705 km | 13:45 a | Operational | HIRDLS, MLS, OMI, TES |
| EOS-Terra | 18 Dec 1999 | expected ( 2008 | 705 km | 10:30 d | Operational | ASTER, MODIS, CERES, MISR, MOPITT |
| ERS-2 | 21 Apr 1995 | expected ( 2009 | 785 km | 10.30 | Operational | AMI-SAR, AMI-SCAT, RA, ATSR-2, MWR, GOME |
| FY-1D | 15 May 2002 | expected ( 2007 | 866 km | 8.20 d | Operational | MVISR |
| FY-2D | 8 Dec 2006 | expected ( 2011 | GEO, | 86.5°E | Operational | S-VISSR |
| FY-2E | 2009 | expected ( 2014 | GEO, | 123°E | Planned | S-VISSR |
| FY-2F | 2011 | expected ( 2016 | GEO, | 86.5°E | Planned | S-VISSR |
| FY-2G | 2013 | expected ( 2018 | GEO, | 123°E | Planned | S-VISSR |
| FY-3A | 2007 | expected ( 2010 | 836 km | 10.00 d | Being built | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |
| FY-3B | 2009 | expected ( 2013 | 836 km | 14.00 a | Planned | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |
| FY-3C | 2012 | expected ( 2015 | 836 km | 10.00 d | Planned | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |
| FY-3D | 2014 | expected ( 2017 | 836 km | 14.00 a | Planned | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |
| FY-3E | 2016 | expected ( 2019 | 836 km | 10.00 d | Planned | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |

| List of satellites mentioned in the gap analysis text (sheet 2 of 3) |
| --- |
| Satellite | Launch | End of service | Height | LST/incl. | Status | Instruments mentioned in the text |
| FY-3F | 2018 | expected ( 2021 | 836 km | 14.00 a | Planned | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |
| FY-3G | 2020 | expected ( 2023 | 836 km | 10.00 d | Planned | VIRR, MERSI, MWRI, IRAS, MWTS, MWHS, TOU/SBUS, ERM |
| FY-4 O/A | 2012 | expected ( 2017 | GEO, 105°E | or 86.5°E | Being defined | IIR, LM, MCSI |
| FY-4 O/B | 2015 | expected ( 2020 | GEO, | 105°E | Being defined | IIR, LM, MCSI |
| FY-4 O/C | 2015 | expected ( 2020 | GEO, | 86.5°E | Being defined | IIR, LM, MCSI |
| FY-4 O/D | 2019 | expected ( 2024 | GEO, | 105°E | Being defined | IIR, LM, MCSI |
| FY-4 O/E | 2019 | expected ( 2024 | GEO, | 86.5°E | Being defined | IIR, LM, MCSI |
| FY-4 M/A | 2015 | expected ( 2020 | GEO, | 123.5°E | Being defined | GEO-MW |
| FY-4 M/B | 2018 | expected ( 2023 | GEO, | 123.5°E | Being defined | GEO-MW |
| FY-4 M/C | 2022 | expected ( 2027 | GEO, | 123.5°E | Being defined | GEO-MW |
| GCOM-C-1 | 2011 | expected ( 2016 | 798 km | 10:30 d | Planned | SGLI |
| GCOM-C-2 | 2015 | expected ( 2020 | 798 km | 10:30 d | Proposed | SGLI |
| GCOM-C-3 | 2019 | expected ( 2024 | 798 km | 10:30 d | Proposed | SGLI |
| GCOM-W-1 | 2010 | expected ( 2015 | 700 km | 13:30 a | Planned | AMSR-2 |
| GCOM-W-2 | 2014 | expected ( 2019 | 700 km | 13:30 a | Proposed | AMSR-2, SeaWinds |
| GCOM-W-3 | 2018 | expected ( 2023 | 700 km | 13:30 a | Proposed | AMSR-2, SeaWinds |
| Glory | 2009 | expected ( 2015 | 705 km | 13:30 a | Planned | APS, TIM |
| GMES-1 | 2011 | expected ( 2017 | 700 km | 06:00 d | Planned | SAR-C |
| GMES-2 | 2012 | expected ( 2017 | 700 km | 06:00 d | Planned | SAR-C |
| GOES-10 | 25 Apr 1997 | expected ( 2009 | GEO, | 60°W | Operational | IMAGER, SOUNDER |
| GOES-11 | 3 May 2000 | expected ( 2009 | GEO, | 135°W | Operational | IMAGER, SOUNDER |
| GOES-12 | 23 Jul 2001 | expected ( 2009 | GEO, | 75°W | Operational | IMAGER, SOUNDER |
| GOES-13 | 24 May 2006 | expected ( 2011 | GEO, | 105°W | Standby | IMAGER, SOUNDER |
| GOES-14 | Apr 2008 | expected ( 2015 | GEO, | TBD | Being built | IMAGER, SOUNDER |
| GOES-15 | Apr 2009 | expected ( 2016 | GEO, | TBD | Planned | IMAGER, SOUNDER |
| GOES-16 (R) | 2014 | expected ( 2021 | GEO, | TBD | Being defined | ABI, HES (to be confirmed), GML |
| GOES-17 | 2014 | expected ( 2021 | GEO, | TBD | Being defined | ABI, HES (to be confirmed), GML |
| GOSAT | Aug 2008 | expected ( 2013 | 666 km | 13:00 d | Planned | TANSO-FTS, TANSO-CAI |
| GPM “core” | 2012 | expected ( 2017 | 407 km | 65° | Planned | DPR, GMI |
| GRACE | 17 Mar 2002 | expected ( 2011 | 400 km | 89° | Operational | BlackJack |
| ICESat | 12 Jan 2003 | expected ( 2007 | 600 km | 94° | Operational | GLAS |
| INSAT-3A | 10 Apr 2003 | expected ( 2012 | GEO, | 93.5°E | Operational | VHRR, CCD |
| INSAT-3D | 2007 | expected ( 2014 | GEO, | 83°E | Close to launch | IMAGER, SOUNDER |
| JASON-1 | 7 Dec 2001 | expected ( 2008 | 1336 km | 66° | Operational | Poseidon-2, JMR |
| JASON-2 | 2008 | expected ( 2015 | 1334 km | 66° | Planned | Poseidon-3, AMR |
| Kalpana-1 | 12 Sep 2002 | expected ( 2010 | GEO, | 74°E | Operational | VHRR |
| LDCM | ( 2010 | N/A | TBD | TBD | Being studied | OLI |
| Landsat-5 | 1 Mar 1984 | expected ( 2008 | 705 km | 10:00 | Operational (partially) | MSS, TM |
| Landsat-7 | 15 Apr 1999 | expected ( 2009 | 705 km | 10:00 | Operational | ETM+ |
| Megha-Tropique | end-2009 | expected ( 2014 | 867 km | 20° | Planned | MADRAS, SAPHIR, ScaRaB |
| Meteor-M-1 | 2007 | expected ( 2011 | 830 km | 10:20 a | Close to launch | MSU-MR, KMSS, MTVZA, Severjanin |
| Meteor-M-2 | 2008 | expected ( 2012 | 830 km | 10:20 a | Planned | MSU-MR, KMSS, IRFS-2, MTVZA, Radiomet, Severjanin |
| Meteosat-7 | 3 Sep 1997 | expected ( 2008 | GEO, | 57.5°E | Operational | MVIRI |
| Meteosat-8 (MSG) | 28 Aug 2002 | expected ( 2009 | GEO, | 3.6°W | Hot standby | SEVIRI, GERB |
| Meteosat-9 | 22 Dec 2005 | expected ( 2013 | GEO, | 0° | Operational | SEVIRI, GERB |
| Meteosat-10 | 2011 | expected ( 2018 | GEO, | TBD | In storage | SEVIRI, GERB |
| Meteosat-11 | 2013 | expected ( 2019 | GEO, | TBD | Being built | SEVIRI, GERB |
| Meteosat-12 (MTG) | 2015 | expected ( 2020 | GEO, | TBD | Being defined | Being defined (FCI, IRS, LI) |

| List of satellites mentioned in the gap analysis text (sheet 3 of 3) |
| --- |
| Satellite | Launch | End of service | Height | LST/incl. | Status | Instruments mentioned in the text |
| MetOp-1 | 19 Oct 2006 | expected ( 2010 | 834 km | 09.30 d | Operational | AVHRR/3, HIRS/4, AMSU-A, MHS, IASI, GOME-2, GRAS, ASCAT |
| MetOp-2 | Oct 2010 | expected ( 2015 | 834 km | 09.30 d | In storage | AVHRR/3, HIRS/4, AMSU-A, MHS, IASI, GOME-2, GRAS, ASCAT |
| MetOp-3 | Apr 2015 | expected ( 2020 | 834 km | 09.30 d | Being built | AVHRR/3, AMSU-A, MHS, IASI, GOME-2, GRAS, ASCAT |
| Monitor-E | 26 Aug 2005 | expected ( 2008 | 540 km | 10:30 a | Operational | PAN, MS |
| MTSAT-1R | 26 Feb 2005 | expected ( 2010 | GEO, | 140°E | Operational | JAMI |
| MTSAT-2 | 18 Feb 2006 | expected ( 2015 | GEO, | 145°E | Standby | IMAGER |
| MTSAT-3 | 2013 | expected ( 2018 | GEO, | TBD | Being defined | IMAGER TBD, SOUNDER TBD |
| NMP EO-1 | 21 Nov 2000 | expected ( 2007 | 705 km | 10:15 d | Operational | ALI, LAC, Hyperion |
| NOAA-15 | 13 May 1998 | expected ( 2007 | 807 km | 05.30 d | Backup | AVHRR/3, HIRS/3, AMSU-A, AMSU-B |
| NOAA-16 | 21 Sep 2000 | expected ( 2007 | 849 km | 15.30 a | Backup | AVHRR/3, HIRS/3, AMSU-A, AMSU-B, SBUV/2 |
| NOAA-17 | 24 Jun 2002 | expected ( 2009 | 810 km | 10.20 d | Operational | AVHRR/3, HIRS/3, AMSU-A, AMSU-B, SBUV/2 |
| NOAA-18 | 20 May 2005 | expected ( 2010 | 854 km | 13.40 a | Operational | AVHRR/3, HIRS/4, AMSU-A, MHS, SBUV/2 |
| NOAA-19 | 2009 | expected ( 2014 | 840 km | 14.00 a | Being built | AVHRR/3, HIRS/4, AMSU-A, MHS, SBUV/2 |
| NPOESS-1 | 2013 | expected ( 2018 | 833 km | 13.30 a | Planned | VIIRS, CrIS, ATMS, OMPS-nadir, ERBS (OMPS-limb, APS in stanby list) |
| NPOESS-2 | 2016 | expected ( 2021 | 833 km | 5.30 d | Planned | VIIRS, CMIS (CrIS, ATMS, TSIS in standby list) |
| NPOESS-3 | 2020 | expected ( 2025 | 833 km | 13.30 a | Planned | VIIRS, CrIS, ATMS, CMIS, OMPS-nadir (ERBS, OMPS-limb, APS in standby list) |
| NPOESS-4 | 2022 | expected ( 2027 | 833 km | 5.30 d | Planned | VIIRS, CMIS (CrIS, ATMS, TSIS in standby list) |
| NPP | 2009 | expected ( 2014 | 833 km | 13.30 a | Being built | VIIRS, CrIS, ATMS, OMPS |
| OceanSat-1 | 26 May 1999 | expected ( 2007 | 720 km | 12:00 | Operational | OCM, MSMR |
| OceanSat-2 | 2008 | expected ( 2013 | 720 km | 12:00 | Planned | OCM. SCAT, ROSA |
| OCO | 2008 | expected ( 2010 | 705 km | 13:15 a | Being built | OCO |
| PARASOL | 18 Dec 2004 | expected ( 2008 | 705 km | 13:30 a | Operational | POLDER |
| Pléiades-1 | end-2008 | expected ( 2013 | 694 km | 10:15 d | Being built | HiRI |
| Pléiades-2 | early 2010 | expected ( 2015 | 694 km | 10:15 d | Planned | HiRI |
| QuikSCAT | 19 Jun 1999 | expected ( 2008 | 803 km | 06:00 d | Operational | SeaWinds |
| RadarSat-1 | 4 Nov 1995 | expected ( 2008 | 798 km | 06:00 d | Operational | SAR |
| RadarSat-2 | 2007 | expected ( 2014 | 798 km | 06:00 d | Close to launch | SAR |
| ResourceSat-1 | 17 Oct 2003 | expected ( 2009 | 817 km | 10:30 | Operational | LISS-3, LISS-4, AWiFS |
| ResourceSat-2 | 2009 | expected ( 2014 | 817 km | 10:30 | Planned | LISS-3, LISS-4, AWiFS |
| Resurs-DK | 15 Jun 2006 | expected ( 2009 | 350 km | 70° | Operational | Geoton |
| SAC-D | 2009 | expected ( 2012 | 657 km | 06:00 d | Being built | Aquarius, ROSA |
| SAOCom-1 | 2008 | expected ( 2014 | 629 km | 06:00 d | Being built | SAR-L |
| SAOCom-2 | 2009 | expected ( 2015 | 629 km | 06:00 d | Being built | SAR-L |
| SeaStar | 1 Aug 1997 | expected ( 2009 | 705 km | 12:00 d | Operational | SeaWiFS |
| Sentinel-2/1 | 2012 | expected ( 2019 | 800 km | 10:30 d | Planned | MSI |
| Sentinel-2/2 | 2013 | expected ( 2020 | 800 km | 10:30 d | Planned | MSI |
| Sentinel-3/1 | 2012 | expected ( 2018 | 815 km | 10.00 d | Planned | SRAL, OLCI, SLSTR |
| Sentinel-3/2 | 2014 | expected ( 2020 | 815 km | 10.00 d | Planned | SRAL, OLCI, SLSTR |
| Sentinel-4 | 2016 | expected ( 2023 | GEO, | 0° | Being defined | TBD (for chemistry) |
| Sentinel-5 | 2020 | expected ( 2025 | 834 km | 09.30 d | Being defined | TBD (for chemistry) |
| SMOS | Sep-2007 | expected ( 2010 | 763 km | 06.00 d | Close to launch | MIRAS |
| SORCE | 25 Jan 2003 | expected ( 2009 | 645 km | 40° | Operational | TIM |
| SPOT-2 | 22 Jan 1990 | expected ( 2007 | 822 km | 10:30 d | Partly operational | HRV |
| SPOT-4 | 24 Mar 1998 | expected ( 2008 | 822 km | 10:30 d | Operational | HRVIR, Vegetation, POAM-3 |
| SPOT-5 | 4 May 2002 | expected ( 2009 | 822 km | 10:30 d | Operational | HRG, HRS, Vegetation |
| TRMM | 27 Nov 1997 | expected ( 2009 | 402 km | 35° | Operational | PR, TMI, CERES, VIRS, LIS |

| List of instruments mentioned in the gap analysis text (sheet 1 of 3) |
| --- |
| Acronym | Full name | Satellites | Utilisation |
| AATSR | Advanced Along-Track Scanning Radiometer (= ATSR-2) | ERS-1/2, Envisat | 1991-2010 |
| ABI | Advanced Baseline Imager | GOES-R and follow-on | 2014 ( |
| ACRIM-III | Active Cavity Radiometer Irradiance Monitoring - III | SMM, UARS, ACRIMSat | 1980-2012 |
| AIRS | Atmospheric Infra-Red Sounder | EOS-Aqua | 2002-2009 |
| ALADIN | Atmospheric Laser Doppler Instrument | ADM-Aeolus | 2008-2011 |
| ALI | Advanced Land Imager | NMP-EO-1 | 2000-2008 |
| AMI-SAR | Active Microwave Instrument - SAR mode | ERS-1/2 | 1991-2009 |
| AMI-SCAT | Active Microwave Instrument - Scat mode | ERS-1/2 | 1991-2009 |
| AMR | Advanced Microwave Radiometer | Jason-2 | 2008-2015 |
| AMSR-2 | Advanced Microwave Scanning Radiometer - 2 | GCOM-W 1/2/3 | 2010-2023 |
| AMSR-E | Advanced Microwave Scanning Radiometer for EOS | EOS-Aqua | 2002-2009 |
| AMSU-A | Advanced Microwave Sounding Unit - A | NOAA 15 to 19 Metop 1 to 3 EOS-Aqua | 1998-2014 2006-2020 2002-2009 |
| AMSU-B | Advanced Microwave Sounding Unit - B | NOAA-15/16/17 | 1998-2009 |
| APS | Aerosol Polarimetry Sensor | Glory, NPOESS 1 & 3 | 2009-2025 |
| Aquarius | Aquarius | SAC-D | 2009-2012 |
| ASAR | Advanced Synthetic Aperture Radar – SAR mode | Envisat | 2002-2010 |
| ASCAT | Advanced Scatterometer | Metop 1 to 3 | 2006-2020 |
| ASTER | Advanced Spaceborne Thermal Emission and Reflection radiometer | EOS-Terra | 1999-2009 |
| ATLID | Atmospheric Lidar | Earth-CARE | 2013-2015 |
| ATMS | Advanced Technology Microwave Sounder | NPP, NPOESS 1 to 4 | 2009-2027 |
| AVHRR/3 | Advanced Very High Resolution Radiometer | TIROS-N, NOAA 6 to 19 Metop 1 to 3 | 1978-2014 2006-2020 |
| AVNIR 1/2 | Advanced Visible and Near-Infrared Radiometer 1 and 2 | ADEOS-1 ALOS | 1996-1997 2006-2010 |
| AWiFS | Advanced Wide Field Sensor | ResourceSat-1/2 | 2003-2014 |
| BlackJack | BlackJack | CHAMP, GRACE | 2000-2011 |
| CALIOP | Cloud-Aerosol Lidar with Orthogonal Polarisation | CALIPSO | 2006-2009 |
| CCD | Charge Coupled Device Camera | INSAT-2E, INSAT-3A | 1999-2012 |
| CERES | Clouds and the Earth’s Radiant Energy System | TRMM, Terra, Aqua | 1997-2009 |
| CMIS | Conical-scanning Microwave Imager/Sounder | NPOESS 2 to 4 | 2016-2027 |
| CPR | Cloud Profiling Radar | CloudSat | 2006-2008 |
| CPR | Cloud Profiling Radar | Earth-CARE | 2013-2015 |
| CrIS | Cross-track Infrared Sounder | NPP, NPOESS 1 to 4 | 2009-2027 |
| DPR | Dual-frequency Precipitation Radar | GPM-core | 2012-2017 |
| ERBS | Earth Radiation Budget Sensor | NPOESS-1/3 | 2013-2025 |
| ERM | Earth Radiation Measurement | FY-3 A to G | 2007-2023 |
| ETM+ | Enhanced Thematic Mapper + | Landsat-7 | 1999-2009 |
| FCI | Flexible Combined Imager | Meteosat Third Generation | 2015 ( |
| GEO-MW | Microwave Sounder in Geostationary Orbit | FY-4 M A/B and follow-on | 2015 ( |
| Geoton | Panchromatic and multispectral radiometer | Resurs-DK | 2006-2009 |
| GERB | Geostationary Earth Radiation Budget | Meteosat 8 to 11 (MSG) | 2002-2019 |
| GLAS | Geoscience Laser Altimeter System | ICESat | 2003-2008 |
| GLM | Geostationary Lightning Mapper | GOES-R and follow-on | 2014 ( |
| GMI | GPM Microwave Imager | GPM-core | 2012-2017 |
| GOCI | Geostationary Ocean Color Imager | COMS-1/2 | 2008-2021 |
| GOME | Global Ozone Monitoring Experiment | ERS-2 | 1995-2009 |
| GOME-2 | Global Ozone Monitoring Experiment - 2 | Metop 1 to 3 | 2006-2020 |
| GOMOS | Global Ozone Monitoring by Occultation of Stars | Envisat | 2002-2010 |
| GRAS | GNSS Receiver for Atmospheric Sounding | Metop 1 to 3 | 2006-2020 |
| HES | Hyperspectral Environmental Suite | GOES-R and follow-on | 2014 ( |
| HIRDLS | High-Resolution Dynamics Limb Sounder | EOS-Aura | 2004-2010 |
| HiRI | High-Resolution Imager | Pléiades-1/2 | 2008-2015 |
| HIRS-3/4 | High-resolution Infra Red Sounder | TIROS-N, NOAA 6 to 19 Metop-1/2 | 1978-2014 2006-2015 |

| List of instruments mentioned in the gap analysis text (sheet 2 of 3) |
| --- |
| Acronym | Full name | Satellites | Utilisation |
| HRG | Haut Résolution Géométrique | SPOT-5 | 2002-2009 |
| HRS | Haut Résolution Stéréoscopique | SPOT-5 | 2002-2009 |
| HRV | Haut Résolution dans le Visible | SPOT-1/2/3 | 1986-2007 |
| HRVIR | Haut Résolution dans le Visible et l’Infra-Rouge | SPOT-4 | 1998-2008 |
| HSB | Humidity Sounder for Brazil | EOS-Aqua | 2002-2009 |
| Hyperion | Hyperion | NMP EO-1 | 2000-2008 |
| IASI | Infrared Atmospheric Sounding Interferometer | Metop 1 to 3 | 2006-2020 |
| IGOS | Integrated GPS Occultation Receiver | COSMIC (6 satellites) | 2006-2011 |
| IIS | Interferometric Infrared Sounder | FY-4 O A/B and follow-on | 2012 ( |
| IMAGER | GOES Imager INSAT Imager MTSAT Imager | GOES 8 to 15 INSAT-3D MTSAT-2 | 1994-2015 2007-2014 2010-2015 |
| IMAGER TBD | COMS Imager MTSAT Imager | COMS-2 MTSAT-3 and follow-on | 2014-2021 2014 ( |
| IRAS | Infra Red Atmospheric Sounder | FY-3 A to G | 2007-2023 |
| IRFS-2 | IR Sounding Spectrometer | Meteor-M-2 | 2008-2012 |
| IRS | Infra Red Sounder | Meteosat Third Generation | 2015 ( |
| JAMI | Japanese Advanced Meteorological Imager | MTSAT-1R | 2005-2010 |
| JMR | Jason Microwave Radiometer | Jason-1 | 2001-2008 |
| KMSS | High-resolution VIS/IR Radiometer | Meteor-M 1/2 | 2007-2012 |
| LAC | LEISA (Linear Etalon Imaging Spectrometer Array) Atmospheric Corrector | NMP EO-1 | 2000-2008 |
| LI | Lightning Imager | Meteosat Third Generation | 2015 ( |
| LIS | Lightning Imaging Sensor | TRMM | 1997-2009 |
| LISS-3 | Linear Imaging Self-Scanning Sensor - 3 | IRS-1C/1D, ResourceSat-1/2 | 1995-2014 |
| LISS-4 | Linear Imaging Self-Scanning Sensor - 4 | ResourceSat 1/2 | 2003-2014 |
| LM | Lightning Mapper | FY-4 O A/B and follow-on | 2012 ( |
| MADRAS | Microwave Analysis & Detection of Rain & Atmospheric Structures | Megha-Tropiques | 2009-2014 |
| MCSI | Multiple Channel Scanning Imager | FY-4 O A/B and follow-on | 2012 ( |
| MERIS | Medium Resolution Imaging Spectrometer | Envisat | 2002-2010 |
| MERSI | Medium Resolution Spectral Imager | FY-3 A to G | 2007-2023 |
| MHS | Microwave Humidity Sounding | NOAA-18/19 Metop 1 to 3 | 2005-2014 2006-2020 |
| MI | Meteorological Imager | COMS-1 | 2008-2015 |
| MIPAS | Michelson Interferometer for Passive Atmospheric Sounding | Envisat | 2002-2010 |
| MIRAS | Microwave Imaging Radiometer using Aperture Synthesis | SMOS | 2007-2010 |
| MISR | Multi-angle Imaging Spectro-Radiometer | EOS-Terra | 1999-2008 |
| MLS | Microwave Limb Sounder | UARS, EOS-Aura | 1991-2011 |
| MODIS | Moderate-resolution Imaging Spectro-radiometer | EOS Terra/Aqua | 1999-2009 |
| MOPITT | Measurement Of Pollution In The Troposphere | EOS Terra | 1999-2008 |
| MSI | Multi-Spectral Imager | Sentinel-2 | 2012-2020 |
| MSMR | Multi-frequency Scanning Microwave Radiometer | OceanSat-1 | 1999-2008 |
| MSS | Multi-Spectral Scanner | Landsat 1 to 5 | 1972-2008 |
| MSU-GS | Elektro-GOMS Imager | Elektro-L and follow-on | 2007 ( |
| MSU-MR | VIS/IR Imaging Radiometer | Meteor-M 1/2 | 2007-2012 |
| MTVZA | Imaging/Sounding Microwave Radiometer | Meteor-M 1/2 | 2007-2012 |
| MVIRI | Meteosat Visible Infra-Red Imager | Meteosat 1 to 7 | 1977-2008 |
| MVISR | Multichannel Visible Infrared Scanning Radiometer | FY-1 A to D | 1988-2007 |
| MWHS | Micro-Wave Humidity Sounder | FY-3 A to G | 2007-2023 |
| MWR | Micro-Wave Radiometer | ERS-1/2, Envisat | 1991-2010 |
| MWR | Micro-Wave Radiometer | Sentinel-3 | 2012-2020 |
| MWRI | Micro-Wave Radiation Imager | FY-3 A to G | 2007-2023 |
| MWTS | Micro-Wave Temperature Sounder | FY-3 A to G | 2007-2023 |
| OCM | Ocean Color Monitor | OceanSat-1/2 | 1999-2013 |
| OCO | Orbiting Carbon Observatory | OCO | 2008-2010 |
| OLCI | Ocean and Land Colour Imager | Sentinel-3 | 2012-2020 |

| List of instruments mentioned in the gap analysis text (sheet 3 of 3) |
| --- |
| Acronym | Full name | Satellites | Utilisation |
| OLI | Operational Land Imager | LDCM | 2010 ( |
| OMI | Ozone Monitoring Instrument | EOS Aura | 2004-2011 |
| OMPS | Ozone Mapping and Profiler Suite | NPP, NPOESS 1 & 3 | 2009-2025 |
| PALSAR | Phased-Array L-band Synthetic Aperture Radar | ALOS | 2006-2010 |
| PAN | Panchromatic Camera | CartoSat-2 | 2007-2012 |
| PAN + MS | Panchromatic + Multispectral Radiometers | Monitor-E | 2005-2008 |
| PAN-A, PAN-F | Panchromatic Cameras | CartoSat-1 | 2005-2010 |
| POAM | Polar Ozone and Aerosol Measurement | SPOT-3/4 | 1993-2008 |
| POLDER | Polarization and Directionality of the Earth’s Reflectances | PARASOL | 2004-2008 |
| Poseidon 2/3 | Poseidon 2/3 | JASON 1/2 | 2001-2015 |
| PR | Precipitation Radar | TRMM | 1997-2009 |
| PRISM | Panchromatic Remote-sensing Instrument for Stereo Mapping | ALOS | 2006-2010 |
| RA, RA-2 | Radar Altimeter | ERS-1/2, Envisat | 1991-2010 |
| Radiomet | Radio-occultation sounder | Meteor-M 1/2 | 2007-2012 |
| ROSA | Radio Occultation Sounder of the Atmosphere | OceanSat-2, SAC-D | 2008-2013 |
| SAPHIR | Sondeur Atmospherique du Profil d’Humidite Intertropicale par Radiometrie | Megha-Tropiques | 2009-2014 |
| SAR | Synthetic Aperture Radar (C-band) | RadarSat 1/2 | 1995-2014 |
| SAR-2000 | Synthetic Aperture Radar 2000 (X-band) | COSMO-SkyMed | 2007-2015 |
| SAR-C | Synthetic Aperture Radar (C-band) | GMES-1 A/B | 2011-2018 |
| SAR-L | Synthetic Aperture Radar (L-band) | SAOCom 1/2 | 2008-2015 |
| SBUV/2 | Solar Backscatter Ultraviolet / 2 | NOAA 9 to 19 except 12/15 | 1984-2014 |
| ScaRaB | Scanner for Radiation Budget | Megha-Tropiques | 2009-2014 |
| SCAT | Scatterometer | OceanSat-2 | 2008-2013 |
| SCIAMACHY | Scanning Imaging Absorption Spectrometer for Atmospheric Cartography | Envisat | 2002-2010 |
| SeaWiFS | Sea-viewing Wide Field-of-view Sensor | SeaStar | 1997-2009 |
| SeaWinds | SeaWinds | QuickSCAT GCOM-W 2/3 | 1999-2008 2014-2023 |
| Severjanin | X-band Synthetic Aperture Radar | Meteor-M 1/2 | 2007-2012 |
| SEVIRI | Spinning Enhanced Visible Infra-Red Imager | Meteosat 8 to 11 (MSG) | 2002-2019 |
| SGLI | Second-generation Global Imager | GCOM-C 1/2/3 | 2011-2024 |
| SIRAL | SAR Interferometer Radar Altimeter | CryoSat-2 | 2009-2012 |
| SLSTR | Sea and Land Surface Temperature Radiometer | Sentinel-3 | 2012-2020 |
| SOUNDER | GOES Sounder INSAT Sounder | GOES 8 to 15 INSAT-3D | 1994-2015 2007-2014 |
| SOUNDER TBD | MTSAT Sounder | MTSAT-3 and follow-on | 2014 ( |
| SRAL | SAR Radar Altimeter | Sentinel-3 | 2012-2020 |
| SSM/I | Special Sensor Microwave – Imager | DMSP F-8/10/11/13/14/15 | 1987-2007 |
| SSMIS | Special Sensor Microwave – Imager/Sounder | DMSP F 16 to 20 | 2003-2017 |
| S-VISSR | Stretched Visible-Infrared Spin Scan Radiometer | FY-2 A to G | 1997-2018 |
| TANSO-CAI | Thermal And Near infrared Sensor for carbon Observations - Cloud and Aerosol Imager | GOSAT | 2008-2013 |
| TANSO-FTS | Thermal And Near infrared Sensor for carbon Observations - Fourier Transform Spectrometer | GOSAT | 2008-2013 |
| TES | Tropospheric Emission Spectrometer | EOS-Aura | 2004-2011 |
| TIM | Total Irradiance Monitoring | SORCE, Glory | 2003-2013 |
| TM | Thematic Mapper | Landsat-4/5 | 1982-2008 |
| TMI | TRMM Microwave Imager | TRMM | 1997-2009 |
| TOU/SBUS | Total Ozone Unit & Solar Backscatter Ultraviolet Sounder | FY-3 A to G | 2007-2023 |
| TSIS | Total Solar Irradiance Sensor | NPOESS 2 & 4 | 2016-2027 |
| Végétation | Végétation | SPOT-4/5 | 1998-2009 |
| VHRR (in GEO) | Very High Resolution Radiometer | INSAT-1A to 3A, Kalpana-1 | 1982-2012 |
| VIIRS | Visible/Infrared Imager Radiometer Suite | NPP, NPOESS 1 to 4 | 2009-2027 |
| VIRR | Visible and Infra Red Radiometer | FY-3 A to G | 2007-2023 |
| VIRS | Visible and Infra Red Scanner | TRMM | 1997-2009 |
| WindSat | WindSat | Coriolis | 2003-2009 |

INSTRUMENT TABLES

| AATSR | Advanced Along-Track Scanning Radiometer (same as ATSR-2) |
| --- | --- |
| Satellites | ERS-1 (ATSR), ERS-2 (ATSR-2) and Envisat (AATSR) |
| Status (Sept 2006) | Operational – Utilised in the period 1991 to ( 2010 |
| Mission | Multi-purpose VIS/IR imagery, with emphasis on very accurate sea surface temperature for climate |
| Instrument type | 7-channel VIS/IR radiometer with dual view for accurate atmospheric corrections (4 channels on ERS-1) |
| Scanning technique | Conical oblique (cross-nadir and 47° fore); 2000 pixel of 1 km ssp; swath 500 km; scan rate 400 rpm |
| Coverage/cycle | Global coverage in 3 days (IR) or 6 days (VIS) |
| Resolution (s.s.p.) | 1 km IFOV |
| Resources | Mass: 101 kg - Power: 100 W - Data rate: 625 kbps |

| Central wavelength | Bandwidth | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 550 nm (not on ERS-1 ATSR) | 20 nm | 20 @ 0.5 % albedo |
| 659 nm (not on ERS-1 ATSR) | 20 nm | 20 @ 0.5 % albedo |
| 865 nm (not on ERS-1 ATSR) | 20 nm | 20 @ 0.5 % albedo |
| 1610 nm | 300 nm | 20 @ 0.5 % albedo |
| 3.70 (m | 3.55-3.85 (m | 0.08 K @ 270 K |
| 10.85 (m | 10.35-11.35 (m | 0.05 K @ 270 K |
| 12.00 (m | 11.50-12.50 (m | 0.05 K @ 270 K |

| ABI | Advanced Baseline Imager |
| --- | --- |
| Satellites | GOES-R (to become GOES-16) and follow-on |
| Status (Sept 2006) | Being defined – To be utilised from 2014 onward |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 16-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 15 min, 3000x5000 km2 (“CONUS”, Continental U.S.) in 5 min, 1000x1000 km2 in 30 s |
| Resolution (s.s.p.) | 0.5 km at 0.64 (m, 1.0 km at 0.47, 0.86 and 1.61 (m, 2 km in the remaining 12 channels |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 470 nm | 40 nm | 300 @ 100 % albedo |
| 640 nm | 100 nm | 300 @ 100 % albedo |
| 860 nm | 40 nm | 300 @ 100 % albedo |
| 1380 nm | 30 nm | 300 @ 100 % albedo |
| 1610 nm | 60 nm | 300 @ 100 % albedo |
| 2260 nm | 50 nm | 300 @ 100 % albedo |
| 3.90 (m | 0.20 (m | 0.1 K @ 300 K |
| 6.15 (m | 0.90 (m | 0.1 K @ 300 K |
| 7.00 (m | 0.40 (m | 0.1 K @ 300 K |
| 7.40 (m | 0.20 (m | 0.1 K @ 300 K |
| 8.50 (m | 0.40 (m | 0.1 K @ 300 K |
| 9.70 (m | 0.20 (m | 0.1 K @ 300 K |
| 10.3 (m | 0.50 (m | 0.1 K @ 300 K |
| 11.2 (m | 0.80 (m | 0.1 K @ 300 K |
| 12.3 (m | 1.00 (m | 0.1 K @ 300 K |
| 13.3 (m | 0.60 (m | 0.3 K @ 300 K |

| ACRIM-III | Active Cavity Radiometer Irradiance Monitoring - III |
| --- | --- |
| Satellites | SMM (ACRIM-I), UARS (ACRIM-2), ACRIMSat (ACRIM-III) |
| Status (Sept 2006) | Operational – Utilised from 1980 until ~ 2012 |
| Mission | Total solar irradiance monitoring |
| Instrument type | Assemblage of 3 active cavity radiometers for total irradiance. Range: 0.15 – 5.0 (m |
| Scanning technique | Sun pointing during orbital movement, data sampled each 2 min |
| Coverage/cycle | One measurement after integration on all data taken during the diurnal orbit arc; thus 100 min |
| Resolution (s.s.p.) | N/A (sun pointing) |
| Resources | Mass: 13 kg - Power: 10 W - Data rate: 600 bps |

| AIRS | Atmospheric Infra-Red Sounder |
| --- | --- |
| Satellite | EOS-Aqua |
| Status (Sept 2006) | Operational – Utilised in the period 2002 to ( 2009 |
| Mission | Temperature/humidity sounding, ozone profile and total-column green-house gases |
| Instrument type | Grating spectrometer, 2378 channels, resolving power (/(( = 1200, 4 supporting channels in VIS/NIR |
| Scanning technique | Cross-track: 90 samples scanned, swath 1650 km - Along-track: one 13.5-km line each 2.67 s |
| Coverage/cycle | Global coverage once/day |
| Resolution (s.s.p.) | 13.5 km IFOV for the spectrometer; 2.3 km IFOV for VIS/NIR channels |
| Resources | Mass: 177 kg - Power: 220 W - Data rate: 1.27 Mbps |
| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution | Accuracy (NE(T or SNR) |
| 3.74 - 4.61 (m | 2170 - 2674 cm-1 | ~ 2.0 cm-1 | 0.14 K @ 280 K |
| 6.20 - 8.22 (m | 1216 - 1613 cm-1 | ~ 1.0 cm-1 | 0.20 K @ 280 K |
| 8.80 - 15.4 (m | 650 - 1136 cm-1 | ~ 0.5 cm-1 | 0.35 K @ 280 K |
| 0.41-0.44 (m | not relevant | 30 nm | > 100 @ 40 % albedo |
| 0.58-0.68 (m | not relevant | 100 nm | > 100 @ 40 % albedo |
| 0.71-0.92 (m | not relevant | 210 nm | > 100 @ 40 % albedo |
| 0.49-0.94 (m | not relevant | N/A (broadband) | > 100 @ 40 % albedo |

| ALADIN | Atmospheric Laser Doppler Instrument |
| --- | --- |
| Satellite | ADM-Aeolus |
| Status (Sept 2006) | Being developed – To be utilised in the period 2008 to ( 2011 |
| Mission | Wind profile in clear-air. Also aerosol profile, cloud top height |
| Instrument type | Single-wavelength lidar (355 nm) with Doppler capability, side-looking (35° off-nadir). High Spectral Resolution Laser (HSRL) to discriminate aerosol types |
| Scanning technique | No scanning. Pulse echoes averaged over 50 km FOV. FOV sampled at 200 km intervals |
| Coverage/cycle | Global coverage in 16 d for cells of 100 km side |
| Resolution | Horizontal: 50 km FOV sampled at 200 km intervals. Vertical: 250 m to 2 km with increasing height |
| Resources | Mass: 500 kg - Power: 840 W - Data rate: 11 kbps |

| ALI | Advanced Land Imager |
| --- | --- |
| Satellite | NMP EO-1 |
| Status (Sept 2006) | Technological demonstration running – To be utilised in the period 2000-2007 |
| Mission | Advanced technology for land and vegetation observation |
| Instrument type | VIS/NIR radiometer, 9 VIS/NIR narrow-band channels, one panchromatic (PAN) |
| Scanning technique | Pushbroom; 1230 pixel/line (9 narrow-band channels), 3700 pixel/line (PAN); swath 37 km [reduced configuration for demonstration purpose - there should be 5 such arrays, to cover a 185 km swath] |
| Coverage/cycle | Global coverage in 80 days, in daylight [for full configuration it would be 16 days] |
| Resolution (s.s.p.) | 30 m (9 narrow-band channels), 10 m (PAN) |
| Resources | Mass: 106 kg - Power: 100 W - Data rate: 300 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 443 nm | 433 - 453 nm | ………. @ ….. % albedo |
| 482 nm | 450 - 515 nm | ………. @ ….. % albedo |
| 565 nm | 525 - 605 nm | ………. @ ….. % albedo |
| 660 nm | 630 - 690 nm | ………. @ ….. % albedo |
| 790 nm | 775 - 805 nm | ………. @ ….. % albedo |
| 867 nm | 845 - 890 nm | ………. @ ….. % albedo |
| 1250 nm | 1200 - 1300 nm | ………. @ ….. % albedo |
| 1650 nm | 1550 - 1750 nm | ………. @ ….. % albedo |
| 2215 nm | 2080 - 2350 nm | ………. @ ….. % albedo |
| Panchromatic | 480 - 690 nm | ………. @ ….. % albedo |

| AMI-SAR | Active Microwave Instrument - SAR mode |
| --- | --- |
| Satellites | ERS-1 and ERS-2 |
| Status (Sept 2006) | Operational – Utilised in the period 1991 to ( 2008 |
| Mission | High-resolution all-weather multi-purpose imager for ocean, land and ice; wave spectra |
| Instrument type | C-band SAR, frequency 5.3 GHz, polarisation VV |
| Scanning technique | Side-looking, 23° off-nadir, swath 100 km. Wave spectra are achieved by processing 5 x 5 km2 30-m resolution SAR imagettes within the SAR swath, 350 km off-track, sampling at 200 or 300 km intervals. The AMI wave mode can be operated at the same time as the AMI-Scat mode |
| Coverage/cycle | Imagery: global coverage in 9 months average, depending on operation mode (duty cycle 12 %). Wave spectra: global coverage in 1.5 months (duty cycle 70 %) |
| Resolution | Imagiery: 30 m. Wave spectra: 5 km |
| Resources | Mass: 325.8 kg - Power: 4800 W (peak) - Data rate: 105 Mbps (imagery), 370 kbps (wave mode) |

| AMI-Scat | Active Microwave Instrument - Scat mode |
| --- | --- |
| Satellites | ERS-1 and ERS-2 |
| Status (Sept 2006) | Operational – Utilised in the period 1991 to ( 2009 |
| Mission | Sea surface wind vector. Also large-scale soil moisture |
| Instrument type | C-band radar scatterometer (5.3 GHz), 3 side looking antennas |
| Scanning technique | One 500-km swaths starting from 200 km off-track. 3 looks each pixel (45, 90 and 135° azimuth) |
| Coverage/cycle | Global coverage in 3 days average, depending on operation mode (alternative to AMI-SAR, thus duty cycle about 80 %) |
| Resolution | Best quality: 50 km; sampling: 25 km |
| Resources | Mass: 325.8 kg (AMI) - Power: 4800 W (peak) - Data rate: 500 kbps |

| AMR | JASON Microwave Radiometer |
| --- | --- |
| Satellite | Jason-2 |
| Status (Sept 2006) | Being built – To be utilised in the period 2008 to ( 2015 |
| Mission | Water vapour correction for the Poseidon-3 radar altimeter |
| Instrument type | 3-frequency MW radiometer, 18.7, 23.8 and 34 GHz |
| Scanning technique | Nadir-only viewing, associated to the Poseidon-3 radar altimeter |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution (s.s.p.) | 25 km |
| Resources | Mass: 27 kg - Power: 31 W - Data rate: 100 bps |

| AMSR-2 | Advanced Microwave Scanning Radiometer - 2 |
| --- | --- |
| Satellites | GCOM-W 1, 2 and 3 |
| Status (mid-2006) | Planned – To be utilised in the period: 2010 to ( 2023 |
| Mission | Multi-purpose MW imager |
| Instrument type | MW radiometer with 6 frequencies / 12 channels |
| Scanning technique | Conical: 55° zenith angle; swath: 1450 km - Scan rate: 40 scan/min = 10 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution | Changing with frequency, consistent with an antenna diameter of 2 m |
| Resources | Mass: 320 kg - Power: 400 W - Data rate: 130 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 6.925 | 350 | V, H | 0.3 K | 35 x 62 km | 10 x 10 km |
| 10.65 | 100 | V, H | 0.6 K | 24 x 42 km | 10 x 10 km |
| 18.7 | 200 | V, H | 0.6 K | 14 x 22 km | 10 x 10 km |
| 23.8 | 400 | V, H | 0.6 K | 15 x 26 km | 10 x 10 km |
| 36.5 | 1000 | V, H | 0.6 K | 7 x 12 km | 10 x 10 km |
| 89.0 | 3000 | V, H | 1.1 K | 3 x 5 km | 5 x 5 km |

| AMSR-E | Advanced Microwave Scanning Radiometer for EOS |
| --- | --- |
| Satellites | EOS-Aqua |
| Status (mid-2006) | Operational - Utilisation period: 2002 to ( 2009 |
| Mission | Multi-purpose MW imager |
| Instrument type | MW radiometer with 6 frequencies / 12 channels |
| Scanning technique | Conical: 55° zenith angle; swath: 1450 km - Scan rate: 40 scan/min = 10 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution | Changing with frequency, consistent with an antenna diameter of 1.6 m |
| Resources | Mass: 314 kg - Power: 350 W - Data rate: 87.4 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 6.925 | 350 | V, H | 0.3 K | 43 x 75 km | 10 x 10 km |
| 10.65 | 100 | V, H | 0.6 K | 29 x 51 km | 10 x 10 km |
| 18.7 | 200 | V, H | 0.6 K | 16 x 27 km | 10 x 10 km |
| 23.8 | 400 | V, H | 0.6 K | 14 x 21 km | 10 x 10 km |
| 36.5 | 1000 | V, H | 0.6 K | 9 x 14 km | 10 x 10 km |
| 89.0 | 3000 | V, H | 1.1 K | 4 x 6 km | 5 x 5 km |

| AMSU-A | Advanced Microwave Sounder Unit - A |
| --- | --- |
| Satellites | NOAA 15 to 19 - MetOp 1 to 3 - EOS-Aqua |
| Status (Sept 2006) | Operational – Utilisation period: 1998 to ( 2014 on NOAA, 2006 to ( 2020 on MetOp, 2002 to ( 2009 on EOS-Aqua |
| Mission | Temperature sounding in nearly-all-weather conditions |
| Instrument type | 15-channel MW radiometer |
| Scanning technique | Cross-track: 30 steps of 48 km ssp, swath 2250 km - Along-track: one 48-km line each 8 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 48 km IFOV |
| Resources | Mass: 104 kg - Power: 99 W - Data rate: 3.2 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisation | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 23.800 | 270 | V | 0.30 K |
| 31.400 | 180 | V | 0.30 K |
| 50.300 | 180 | V | 0.40 K |
| 52.800 | 400 | V | 0.25 K |
| 53.596 ( 0.115 | 170 | H | 0.25 K |
| 54.400 | 400 | H | 0.25 K |
| 54.940 | 400 | V | 0.25 K |
| 55.500 | 330 | H | 0.25 K |
| f0 = 57.290344 | 330 | H | 0.25 K |
| f0 ( 0.217 | 78 | H | 0.40 K |
| f0 ( 0.3222 ( 0.048 | 36 | H | 0.40 K |
| f0 ( 0.3222 ( 0.022 | 16 | H | 0.60 K |
| f0 ( 0.3222 ( 0.010 | 8 | H | 0.80 K |
| f0 ( 0.3222 ( 0.0045 | 3 | H | 1.20 K |
| 89.000 | 6000 | V | 0.50 K |

| AMSU-B | Advanced Microwave Sounder Unit - B |
| --- | --- |
| Satellites | NOAA 15 to 17 |
| Status (Sept 2006) | Operational – Utilisation period: 1998 to ( 2009 |
| Mission | Humidity sounding in nearly-all-weather conditions. Also precipitation |
| Instrument type | 5-channel MW radiometer |
| Scanning technique | Cross-track: 90 steps of 16 km ssp, swath 2250 km - Along-track: one 16-km line each 8/3 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 16 km IFOV |
| Resources | Mass: 50 kg - Power: 90 W - Data rate: 60 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisation | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 89.0 | 1000 | V | 0.37 K |
| 150.0 | 1000 | V | 0.84 K |
| 183.31 ( 7.0 | 2000 | V | 0.60 K |
| 183.31 ( 3.0 | 1000 | V | 0.70 K |
| 183.31 ( 1.0 | 500 | V | 1.06 K |

| APS | Aerosol Polarimetry Sensor |
| --- | --- |
| Satellites | Glory, NPOESS 1 and 3 |
| Status (Sept 2006) | Being built for Glory; currently not baselined for NPOESS - To be utilised in the period 2009 to ( 2013 on Glory, ( 2025 if also on NPOESS 1/3 |
| Mission | Aerosol optical thickness, size distribution and shape |
| Instrument type | 9-channel VIS/NIR/SWIR polarimeter with multi-angle capability |
| Scanning technique | Along-track viewing only, fore- and aft- ( 60° (250 steps of 8 mrad), one full measurement each 8.8.km |
| Coverage/cycle | 30000 measurements/day at 8.8 km intervals – Global coverage (25 km average spacing) in 30 days |
| Resolution s.s.p. | 5.6 IFOV |
| Resources | Mass: 58 kg - Power: 45 W - Data rate: 160 kbps |

| Central wavelength | Bandwidth | Polarisations | Radiometric accuracy (SNR) |
| --- | --- | --- | --- |
| 412 nm | 20 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 445 nm | 18 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 488 nm | 20 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 555 nm | 20 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 672 nm | 20 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 746 nm | 15 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 865 nm | 39 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 1240 nm | 20 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 1378 nm | 15 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 1610 nm | 60 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |
| 2250 nm | 50 nm | 0, 45, 90 and 135 degrees | ........ @ .... % albedo |

| Aquarius | Aquarius |
| --- | --- |
| Satellite | SAC-D |
| Status (Sept 2006) | Planned – To be utilised in the period: 2009 to ( 2012 |
| Mission | Ocean salinity, soil moisture |
| Instrument type | Co-aligned MW radiometer at 1.413 GHz + scatterometer at 1.26 GHz, both polarimetric |
| Scanning technique | Pushbroom. Three parallel cross-track beams: 76 km x 94 km, 84 km x 120 km, 96 km x 156 km implementing a swath of 390 km |
| Coverage/cycle | Global coverage in 4 days (soil moisture). Average over one month for accurate salinity measurements |
| Resolution | 100 km average in the 390 km swath |
| Resources | Mass: 247 kg - Power: 291 W - Data rate: 5 kbps |

| ASAR | Advanced Synthetic Aperture Radar - SAR mode |
| --- | --- |
| Satellite | Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 2002 to ( 2010 |
| Mission | High-resolution all-weather multi-purpose imager for ocean, land and ice |
| Instrument type | C-band SAR, frequency 5.331 GHz, multi-polarisation and variable pointing/resolution |
| Scanning technique | Side-looking, 15-45° off-nadir, swath 100 to 405 km, depending on operation mode – See table |
| Coverage/cycle | Global coverage in 5 day for the ‘global monitoring’ mode (if used for 70 % of the time); in longer periods for other operation modes, up to 3 months |
| Resolution | 30 m to 1 km, depending on operation mode – See table |
| Resources | Mass: 832 kg - Power: 1400 W - Data rate: 100 Mbps |

| Operation mode | Resolution | Swath | Polarisation |
| --- | --- | --- | --- |
| Stripmap | 30 m | 100 km selectable within a range of 485 km | HH or VV |
| ScanSAR alternating pol | 30 m | 100 km selectable within a range of 485 km | VV/HH, HH/HV, VV/VH |
| ScanSAR wide swath | 150 m | 405 km | HH or VV |
| ScanSAR wide swath | 150 m | 405 km | HH or VV |
| ScanSAR global monitoring | 1 km | 405 km | HH or VV |
| Wave | 30 m | 5 x 5 km2 imagettes sampled at 100 km intervals | HH or VV |

| ASCAT | Advanced Scatterometer |
| --- | --- |
| Satellites | MetOp 1 to 3 |
| Status (Sept 2006) | Being commissioned - To be utilised in the period: 2006 to ( 2020 |
| Mission | Sea surface wind vector. Also large-scale soil moisture |
| Instrument type | C-band radar scatterometer (5.255 GHz), side looking both left and right. 3 antennas on each side |
| Scanning technique | Two 550-km swaths separated by a 700-km gap along-track. 3 looks each pixel (45, 90 and 135° azimuth) |
| Coverage/cycle | Global coverage in 1.5 days |
| Resolution | Best quality: 50 km – standard quality: 25 km – basic sampling: 12.5 km |
| Resources | Mass: 260 kg - Power: 215 W - Data rate: 42 kbps |

| ASTER | Advanced Spaceborne Thermal Emission and Reflection radiometer |
| --- | --- |
| Satellite | EOS-Terra |
| Status (Sept 2006) | Operational – Utilised in the period 1999 to ( 2007 |
| Mission | Land and vegetation observation |
| Instrument type | 14-channel radiometer in three sub-systems, VIS/NIR (3 channels), SWIR (6 channels), TIR (5 channels) |
| Scanning technique | VNIR and SWIR pushbroom; 4000 pixel/line (VNIR), 2000 pixel/line (SWIR); TIR whiskbroom (670 pixel/line; swath 60 km ssp; cross-track pointing capability within a range of ( 318 km (VNIR) or ( 116 km (SWIR and TIR); along-track stereoscopic viewing in one NIR channel (0.81 (m) |
| Coverage/cycle | By exploiting strategic pointing, any place within 16 days, or within 5 days limited to VNIR in daylight |
| Resolution (s.s.p.) | 15 m (VNIR), 30 m (SWIR), 90 m (TIR) |
| Resources | Mass: 421 kg - Power: 463 W - Data rate: 8.3 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.56 (m | 0.52 - 0.60 (m | …... @ ….. % albedo |
| 0.66 (m | 0.63 - 0.69 (m | …... @ ….. % albedo |
| 0.81 (m | 0.76 - 0.86 (m | …... @ ….. % albedo |
| 1.65 (m | 1.60 - 1.70 (m | …... @ ….. % albedo |
| 2.165 (m | 2.145 - 2.185 (m | …... @ ….. % albedo |
| 2.205 (m | 2.185 - 2.225 (m | …... @ ….. % albedo |
| 2.260 (m | 2.235 - 2.285 (m | …... @ ….. % albedo |
| 2.330 (m | 2.295 - 2.365 (m | …... @ ….. % albedo |
| 2.395 (m | 2.360 - 2.430 (m | …... @ ….. % albedo |
| 8.30 (m | 8.125 - 8.475 (m | …... K @ ….. K |
| 8.65 (m | 8.475 - 8.825 (m | …... K @ ….. K |
| 9.10 (m | 8.925 - 9.275 (m | …... K @ ….. K |
| 10.60 (m | 10.25 - 10.95 (m | …... K @ ….. K |
| 11.30 (m | 10.95 - 11.65 (m | …... K @ ….. K |

| ATLID | Atmospheric Lidar |
| --- | --- |
| Satellite | Earth-CARE |
| Status (Sept 2006) | Being developed – To be utilised in the period 2013 to ( 2015 |
| Mission | Aerosol profile, cloud top height |
| Instrument type | Single-wavelength lidar (355 nm), High Spectral Resolution Laser (HSRL) to discriminate Mie and Rayleigh scattering components, thus improve aerosol type classification |
| Scanning technique | Near-nadir viewing 2° ahead along-track, sampling at 100 m intervals along track, near continuous profiling |
| Coverage/cycle | Global coverage in 16 d for cells of 100 km side |
| Resolution | Horizontal: 30 m IFOV sampled at 100 m intervals along track. Vertical: 100 m |
| Resources | Mass: 230 kg - Power: 310 W - Data rate: 822 kbps |

| ATMS | Advanced Technology Microwave Sounder |
| --- | --- |
| Satellites | NPP, NPOESS 1/3 and possibly 2/4 |
| Status (Sept 2006) | Being built – To be utilised in the period 2009 to ( 2025 (2027 if also on NPOESS 2/4) |
| Mission | Temperature and humidity sounding in nearly-all-weather conditions. Also precipitation |
| Instrument type | 22-channel MW radiometer |
| Scanning technique | Cross-track: 96 steps of 16 km ssp, swath 2200 km - Along-track: one 16-km line each 8/3 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 16 km for channels 165-183 GHz, 32 km for channels 50-90 GHz, 75 km for channels 23-32 GHz |
| Resources | Mass: 75.4 kg - Power: 93 W - Data rate: 20 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Quasi-polarisation | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 23.800 | 270 | QV | 0.90 K |
| 31.400 | 180 | QV | 0.90 K |
| 50.300 | 180 | QH | 1.20 K |
| 51.760 | 400 | QH | 0.75 K |
| 52.800 | 400 | QH | 0.75 K |
| 53.596 ( 0.115 | 170 | QH | 0.75 K |
| 54.400 | 400 | QH | 0.75 K |
| 54.940 | 400 | QH | 0.75 K |
| 55.500 | 330 | QH | 0.75 K |
| f0 = 57.290344 | 330 | QH | 0.75 K |
| f0 ( 0.217 | 78 | QH | 1.20 K |
| f0 ( 0.3222 ( 0.048 | 36 | QH | 1.20 K |
| f0 ( 0.3222 ( 0.022 | 16 | QH | 1.50 K |
| f0 ( 0.3222 ( 0.010 | 8 | QH | 2.40 K |
| f0 ( 0.3222 ( 0.0045 | 3 | QH | 3.60 K |
| 89.5 | 5000 | QV | 0.50 K |
| 165.5 | 3000 | QH | 0.60 K |
| 183.31 ( 7.0 | 2000 | QH | 0.80 K |
| 183.31 ( 4.5 | 2000 | QH | 0.80 K |
| 183.31 ( 3.0 | 1000 | QH | 0.80 K |
| 183.31 ( 1.8 | 1000 | QH | 0.80 K |
| 183.31 ( 1.0 | 500 | QH | 0.90 K |

| AVHRR/3 | Advanced Very High Resolution Radiometer / 3 |
| --- | --- |
| Satellites | TIROS-N, NOAA 6 to 19 - MetOp 1 to 3 |
| Status (Sept 2006) | Operational – Utilisation period: 1978 to ( 2014 on NOAA, 2006 to ( 2020 on MetOp |
| Mission | Multi-purpose VIS/IR imagery |
| Instrument type | 6-channel VIS/IR radiometer (channel 1.6 and 3.7 alternative) |
| Scanning technique | Cross-track: 2048 pixel of 800 m ssp, swath 2900 km - Along-track: six 1.1-km lines/s |
| Coverage/cycle | Global coverage twice/day (IR) or once/day (VIS) |
| Resolution (s.s.p.) | 1.1 km IFOV |
| Resources | Mass: 33 kg - Power: 27 W - Data rate: 621.3 kbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.630 (m | 0.58 - 0.68 (m | 9 @ 0.5 % albedo |
| 0.862 (m | 0.725 - 1.00 (m | 9 @ 0.5 % albedo |
| 1.61 (m | 1.58 - 1.64 (m | 20 @ 0.5 % albedo |
| 3.74 (m | 3.55 - 3.93 (m | 0.12 K @ 300 K |
| 10.80 (m | 10.3 - 11.3 (m | 0.12 K @ 300 K |
| 12.00 (m | 11.5 - 12.5 (m | 0.12 K @ 300 K |

| AVNIR 1/2 | Advanced Visible and Near-Infrared Radiometer - 2 |
| --- | --- |
| Satellites | ALOS and ADEOS-1 (AVNIR) |
| Status (Sept 2006) | Operational on ALOS – To be utilised in the period 2006 to ( 2010 (AVNIR: 2002-2003) |
| Mission | Vegetation observation |
| Instrument type | 4-channel VIS/NIR radiometer (AVNIR: 5 channels ) |
| Scanning technique | Bushbroom, 7000 pixel/line, swath 70 km ssp, possible to be pointed cross-track within a swath of 1400 km |
| Coverage/cycle | Global coverage in 46 days, in daylight. With strategic pointing, one place can be observed each 2 days. |
| Resolution (s.s.p.) | 10 m IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: 160 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.46 (m | 0.42 - 0.50 (m | 200 @ 25 % albedo |
| 0.56 (m | 0.52 – 0.60 (m | 200 @ 29 % albedo |
| 0.65 (m | 0.61 – 0.69 (m | 200 @ 41 % albedo |
| 0.825 (m | 0.76 – 0.89 (m | 200 @ 59 % albedo |
| 0.60 (m (AVNIR) | 0.52 – 0.69 (m | 100 @ 100 % albedo or 5 @ 3.3 % albedo |

| AWiFS | Advanced Wide Field Sensor |
| --- | --- |
| Satellite | IRS-P6 (ResourceSat-1) and ResourceSat-2 |
| Status (Sept 2006) | Operational - Utilisation period: 2003 to ( 2014 |
| Mission | Land and vegetation observation |
| Instrument type | Two parallel radiometers, 4 VIS/NIR/SWIR channels |
| Scanning technique | Bushbroom, 12000 pixel/line, swath 740 km (with two instruments) |
| Coverage/cycle | Global coverage in 5 days, in daylight |
| Resolution (s.s.p.) | 56 m IFOV |
| Resources | Mass: 103.6 kg - Power: 114 W - Data rate: 52.5 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.555 (m | 0.52 – 0.59 (m | …... @ ….. % albedo |
| 0.650 (m | 0.62 – 0.68 (m | …... @ ….. % albedo |
| 0.815 (m | 0.77 – 0.86 (m | …... @ ….. % albedo |
| 1.625 (m | 1.55 – 1.70 (m | …... @ ….. % albedo |

| BlackJack | BlackJack |
| --- | --- |
| Satellites | CHAMP, Microlab-1 (GPS/MET), SAC-C (GOLPE), GRACE |
| Status (Sept 2006) | Operational – Utilised in the period 1995 to ( 2011 |
| Mission | Temperature/humidity sounding with highest vertical resolution, space weather |
| Instrument type | GPS receiver measuring the phase delay due to refraction during occultation between GPS and LEO |
| Scanning technique | Limb scanning from 830 km to close-to-surface by time sampling – Azimuth: 90° sectors fore- and aft- |
| Coverage/cycle | About 500 soundings/day – Average spacing 1000 km – Global coverage (300 km spacing) in 10 days |
| Resolution | About 300 km horizontal, 0.5 km vertical |
| Resources | Mass: … kg - Power: … W - Data rate: 17 kbps |

| CALIOP | Cloud-Aerosol Lidar with Orthogonal Polarisation |
| --- | --- |
| Satellite | Calipso |
| Status (Sept 2006) | Operational – Utilised in the period 2006 to ( 2009 |
| Mission | Aerosol profile, cloud top height |
| Instrument type | Two-wavelengths lidar (532 and 1064 nm), measurements at two orthogonal polarisations |
| Scanning technique | Nadir-only viewing, sampling at 330 m intervals along track, near continuous profiling |
| Coverage/cycle | Global coverage in 16 d (orbit repeat cycle) for cells of 100 km side |
| Resolution | Horizontal: 70 m IFOV sampled at 333 m intervals along track. Vertical: 30 m |
| Resources | Mass: 156 kg - Power: 124 W - Data rate: 332 kbps |

| CCD | Charge-Coupled Device Camera |
| --- | --- |
| Satellites | INSAT-2E and INSAT-3A |
| Status (Sept 2006) | Operational – Utilisation period: 1999 to ( 2012 |
| Mission | Cloud imagery |
| Instrument type | 3-channel VIS camera |
| Coverage/cycle | 10° x 10° each 3 hours. More frequently on demand. Daylight operation only |
| Resolution (s.s.p.) | 1.0 km |
| Resources | Mass: 55 kg - Power: 50 W - Data rate: … kbps |

| Central wavelength | Spectral interval | Radiometric Accuracy (SNR) |
| --- | --- | --- |
| 0.71 (m | 0.63 - 0.79 m | 417 @ 100 % albedo |
| 0.81 (m | 0.77 - 0.86 (m | 336 @ 100 % albedo |
| 1.62 (m | 1.55 - 1.70 (m | 342 @ 100 % albedo |

| CERES | Clouds and the Earth’s Radiant Energy System |
| --- | --- |
| Satellites | TRMM, EOS-Terra and EOS-Aqua |
| Status (Sept 2006) | Operational – Utilised in the period 1997 to ( 2009 |
| Mission | Earth radiation budget |
| Instrument type | Two broad-band and one narrow-band channel radiometer |
| Scanning technique | Cross-track: 80 steps of 20 km ssp, swath 3000 km - Along-track: one 20-km line each 3 s |
| Coverage/cycle | Global coverage twice/day (IR and total radiance) or once/day (short-wave) |
| Resolution (s.s.p.) | 20 km |
| Resources | Mass: 100 kg - Power: 103 W - Data rate: 20 kbps |

| Channel | Spectral interval | Noise Equivalent Radiance | Absolute accuracy | SNR |
| --- | --- | --- | --- | --- |
| Narrow-band | 8 - 12 (m | ......... Wm-2sr-1 | ......... Wm-2sr-1 | .............. |
| Short-wave | 0.3 - 5.0 (m | ......... Wm-2sr-1 | ......... Wm-2sr-1 | ............. |
| Total radiance | 0.3 - 100 (m | ......... Wm-2sr-1 | ......... Wm-2sr-1 | ............. |

| CMIS | Conical-scanning Microwave Imager/Sounder |
| --- | --- |
| Satellites | NPOESS 2 to 4 |
| Status (Sept 2006) | Design being reconsidered in view of descoping – Utilisation period: 2016 to ( 2027 |
| Mission | Multi-purpose MW imager with temperature/humidity sounding channels for improved precipitation |
| Instrument type | 63-frequency, 77-channel MW radiometer |
| Scanning technique | Conical: 53.6- 58.1° zenith angle, swath 1700 km – Scan rate: 31.6 scan/min = 12.5 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution (constant) | Changing with frequency, consistent with antenna diameters of 2.2 m (6-90 GHz) and 0.7 m (> 90GHz) |
| Resources | Mass: 257 kg - Power: 291 W - Data rate: 280 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations (*) | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 6.625 | 350 | V, H | ........ K | 34 x 56 km | 40 x 12.5 km |
| 10.65 | 100 | V, H, R, L | ........ K | 21 x 35 km | 20 x 12.5 km |
| 18.7 | 200 | V, H, P, M, L, R | ........ K | 12 x 20 km | 10 x 12.5 km |
| 23.8 | 400 | V, H | ........ K | 9.5 x 17 km | 10 x 12.5 km |
| 36.5 | 1000 | V, H, P, M | ........ K | 6.2 x 10 km | 5 x 12.5 km |
| 50.3 | 134 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 52.240 | 1280 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 53.570 | 960 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 54.380 | 440 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 54.905 | 350 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 55.490 | 340 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 56.660 | 300 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 59.380 | 280 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 59.940 | 440 | V | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 60.3712 | 57.6 | L | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 60.4080 | 16 | L | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 60.4202 | 8.4 | L | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 60.5088 | 44.8 | L | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 60.43476 (**) | 20 (40 FFT channels) | H | ........ K | 4.5 x 7.5 km | 5 x 12.5 km |
| 89.0 | 4000 | V, H | ........ K | 2.5 x 4.2 | 2.5 x 6.25 km |
| 166 ( 0.7875 | 1425 | V | ........ K | 15 x 25 | 10 x 12.5 km |
| 183.31 ( 7.70 | 4500 | V | ........ K | 15 x 25 | 10 x 12.5 km |
| 183.31 ( 3.10 | 3500 | V | ........ K | 15 x 25 | 10 x 12.5 km |
| 183.31 ( 0.7125 | 1275 | V | ........ K | 15 x 25 | 10 x 12.5 km |
| (*) Polarisations: H = horizontal, V = vertical, P = + 45°, M = - 45°, L = left-hand circular, R = right-hand circular |
| (**) 20 MHz band centred on 60.43476 GHz (7+ line of O2) split in 40 channels by Fast Fourier Transform (FFT) |

| CPR | Cloud Profiling Radar |
| --- | --- |
| Satellite | CloudSat |
| Status (Sept 2006) | Operational – Utilised in the period 2006 to ( 2008 |
| Mission | Vertical profile of cloud water (liquid and ice) |
| Instrument type | Radar, frequency 94.05 GHz, |
| Scanning technique | None. Along-track sampling at 2 km intervals |
| Coverage/cycle | Global coverage in 16 days for cells of 100 km side |
| Resolution | Horizontal: 1.4 km (cross-track) x 3.5 km (along-track); vertical 500 m |
| Resources | Mass: 230 kg - Power: 270 W - Data rate: 15 kbps |

| CPR | Cloud Profiling Radar |
| --- | --- |
| Satellite | Earth-CARE |
| Status (Sept 2006) | Planned – To be utilised in the period 2013 to ( 2015 |
| Mission | Vertical profile of cloud water (liquid and ice), vertical velocity |
| Instrument type | Radar, frequency 94.05 GHz, Doppler capability |
| Scanning technique | None. Along-track sampling at 1 km intervals |
| Coverage/cycle | Global coverage in 16 days for cells of 100 km side |
| Resolution | Horizontal: 0.65 km (cross-track) x 1 km (along-track); vertical 400 m |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| CrIS | Cross-track Infrared Sounder |
| --- | --- |
| Satellites | NPP, NPOESS 1/3 and possibly 2/4 |
| Status (Sept 2006) | Being built – To be utilised in the period 2009 to ( 2025 (2027 if also on NPOESS 2/4) |
| Mission | Temperature/humidity sounding, ozone profile and total-column green-house gases |
| Instrument type | IR spectrometer/interferometer (1300 channels) |
| Scanning technique | Cross-track: 32 steps of 48 km ssp, swath 2200 km - Along-track: one 48-km line each 8 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 3 x 3 14 km IFOV covering a 48 x 48 km2 cell (average sampling distance: 16 km) |
| Resources | Mass: 87 kg - Power: 91 W - Data rate: 1.44 Mbps |

| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution (unapodised) | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 9.13 - 15.40 (m | 650 - 1095 cm-1 | 0.625 cm-1 | ......... K @ ...... K |
| 5.71 - 8.26 (m | 1210 - 1750 cm-1 | 1.25 cm-1 | ......... K @ ...... K |
| 3.92 – 4.64 (m | 2155 - 2550 cm-1 | 2.5 cm-1 | ......... K @ ...... K |

| DPR | Dual-frequency Precipitation Radar |
| --- | --- |
| Satellite | GPM-core |
| Status (Sept 2006) | Planned – To be utilised in the period 2012 to ( 2017 |
| Mission | Vertical profile of precipitation |
| Instrument type | Dual-frequency imaging radar, frequencies 13.6 GHz and 35.55 GHz |
| Scanning technique | Electronic scanning, planar array of 148 elements, swath 245 km at 13.6 GHz, 120 km at 35.55 GHz |
| Coverage/cycle | Nearly-global in 5 days, high-latitudes (> 65°) not covered |
| Resolution (s.s.p.) | Horizontal 5.0 km, vertical 250 m (blind to the lowest ~ 150 m) |
| Resources | Mass: 780 kg - Power: 710 W - Data rate: 190 kbps |

| ERBS | Earth Radiation Budget Sensor |
| --- | --- |
| Satellites | NPOESS 1 and possibly 3 |
| Status (Sept 2006) | Recurring model of CERES – To be utilised in the period 2013 to ( 2018 (possibly to ( 2025) |
| Mission | Earth radiation budget |
| Instrument type | Two broad-band and one narrow-band channel radiometer |
| Scanning technique | Cross-track: 80 steps of 20 km ssp, swath 3000 km - Along-track: one 20-km line each 3 s |
| Coverage/cycle | Global coverage twice/day (IR and total radiance) or once/day (short-wave) |
| Resolution (s.s.p.) | 20 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Channel | Spectral interval | Noise Equivalent Radiance | Absolute accuracy | SNR |
| --- | --- | --- | --- | --- |
| Narrow-band | 8 - 12 (m | 0.3 Wm-2sr-1 | ......... Wm-2sr-1 | .............. |
| Short-wave | 0.3 - 5.0 (m | 0.8 Wm-2sr-1 | ......... Wm-2sr-1 | ............. |
| Total radiance | 0.3 - 100 (m | 0.6 Wm-2sr-1 | ......... Wm-2sr-1 | ............. |

| ERM | Earth Radiation Measurement |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to launch – To be utilised in the period 2007 to ( 2023 |
| Mission | Earth radiation budget and Total solar irradiance |
| Instrument type | Two broad-band channels radiometer. Two units, one scanning, one non-scanning. In addition, 3 cavity radiometers for total solar irradiance |
| Scanning technique | Scanner: swath 2200 km; cross-track scanning,151 steps of 28 km ssp each 4 s; non-scanning: 120 degrees viewing angle, 8 samples each 4 s. Total solar irradiance: sun-pointing |
| Coverage/cycle | Global coverage twice/day (total radiance) or once/day (short-wave) |
| Resolution (s.s.p.) | Scanner: 28 km - Non-scanner: N/A - Total solar irradiance: N/A |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Channel | Spectral interval | Noise Equivalent Radiance | Absolute accuracy | SNR |
| --- | --- | --- | --- | --- |
| Short-wave (outgoing) | 0.2 – 3.8 (m | 0.4 W m-2 sr-1 | 1.5 W m-2 sr-1 | 900 |
| Total radiance (outgoing) | 0.2 - 50 (m | 0.4 W m-2 sr-1 | 1.1 W m-2 sr-1 | 1250 |
| Total solar irradiance (incoming) | 0.2 - 50 (m | 0.2 W m-2 | 0.5 % | ? |

| ETM+ | Enhanced Thematic Mapper + |
| --- | --- |
| Satellite | Landsat-7 |
| Status (Sept 2005) | Operational – Utilised in the period 1999 to ( 2006 |
| Mission | Land and vegetation observation |
| Instrument type | VIS/NIR radiometer, 6 VIS/NIR narrow-band channels, one panchromatic (PAN), one in TIR |
| Scanning technique | Wiskbroom; 6000 pixel/line (narrow-band), 12000 pixel/line (PAN), 3000 pixel/line (TIR); swath 185 km |
| Coverage/cycle | Global coverage in 16 days, in daylight. |
| Resolution (s.s.p.) | 30 m (6 narrow-band channels), 15 m (PAN), 60 m (TIR) |
| Resources | Mass: 441 kg - Power: 590 W - Data rate: 150 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.48 (m | 0.45 - 0.52 (m | 32 @ ….. % albedo |
| 0.56 (m | 0.53 - 0.61 (m | 35 @ ….. % albedo |
| 0.66 (m | 0.63 - 0.69 (m | 26 @ ….. % albedo |
| 0.83 (m | 0.78 - 0.90 (m | 32 @ ….. % albedo |
| 1.65 (m | 1.55 - 1.75 (m | 25 @ ….. % albedo |
| 2.20 (m | 2.09 - 2.35 (m | 17 @ ….. % albedo |
| Panchromatic | 0.50 - 0.90 (m | 15 @ ….. % albedo |
| 11.45 (m | 10.4 - 12.5 (m | 0.5 K @ 300 K |

| FCI | Flexible Combined Imager |
| --- | --- |
| Satellites | Meteosat-12 and follow-on (Meteosat Third Generation) |
| Status (Sept 2006) | Being defined - To be utilised from 2015 onward |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 16-channel VIS/IR radiometer |
| Coverage/cycle | Full disk in 10 min and 2.5 min over Europe; or alternating modes |
| Resolution (s.s.p.) | Sampling distance (pixel) of 0.5, 1.0 or 2.0 km (see table). IFOV ~ 1.2 times the sampling distance |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Channel no. | Central wavelength | Bandwidth | Radiometric accuracy (SNR or NE(T) | Pixel |
| --- | --- | --- | --- | --- |
| 1 | 444 nm | 60 nm | 25 @ 1 % albedo | 1.0 km |
| 2 | 510 nm | 50 nm | 25 @ 1 % albedo | 1.0 km |
| 3 | 645 nm | 80 nm | 30 @ 1 % albedo | 0.5 km |
| 4 | 860 nm | 70 nm | 30 @ 1 % albedo | 1.0 km |
| 5 | 960 nm | 60 nm | 12 @ 1 % albedo | 1.0 km |
| 6 | 1375 nm | 30 nm | 40 @ 1 % albedo | 1.0 km |
| 7 | 1610 nm | 60 nm | 30 @ 1 % albedo | 1.0 km |
| 8 | 2260 nm | 50 nm | 25 @ 1 % albedo | 0.5 km |
| 9 | 3.80 µm | 0.40 µm | 0.1 K @ 300 K | 1.0 km |
| 10 | 6.30 µm | 0.40 µm | 0.3 K @ 250 K | 2.0 km |
| 11 | 7.35 µm | 0.50 µm | 0.3 K @ 250 K | 2.0 km |
| 12 | 8.70 µm | 0.30 µm | 0.1 K @ 300 K | 2.0 km |
| 13 | 9.66 µm | 0.30 µm | 0.3 K @ 250 K | 2.0 km |
| 14 | 10.50 µm | 0.70 µm | 0.1 K @ 300 K | 1.0 km |
| 15 | 12.30 µm | 0.50 µm | 0.1 K @ 300 K | 2.0 km |
| 16 | 13.30 µm | 0.60 µm | 0.2 K @ 270 K | 2.0 km |

| GEO-MW | Microwave Sounder in Geostationary Orbit |
| --- | --- |
| Satellites | FY-4 M A/B and follow-on |
| Status (Sept 2006) | Being defined - To be utilised from 2015 onward |
| Mission | Precipitation, temperature/humidity sounding, cloud liquid and ice water |
| Instrument type |  |
| Coverage/cycle | TBD |
| Resolution (s.s.p.) |  |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Band central frequency | No. channels in band | Average bandwidth | Radiometric accuracy | Resolution |
| --- | --- | --- | --- | --- |
|  |  | TBD |  |  |

| Geoton | Panchromatic and multispectral radiometer |
| --- | --- |
| Satellite | Resurs-DK |
| Status (Sept 2006) | Operational – Utilisation period: 2006 to ( 2009 |
| Mission | Land and vegetation observation |
| Instrument type | 3-channel VIS/NIR radiometer (multispectral), 1 channel in panchromatic mode (0.58-0.8 (m) |
| Scanning technique | Bushbroom, 12000 pixel/line; swath 30 km addressable within an area of regard of 450 km |
| Coverage/cycle | Global coverage in 80 days, in daylight; locally more frequent by strategic pointing |
| Resolution (s.s.p.) | 2-3 m in multi-spectral mode, 1 m in panchromatic mode |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.55 (m | 0.5 – 0.6 (m | …... @ ….. % albedo |
| 0.65 (m | 0.6 – 0.7 (m | …... @ ….. % albedo |
| 0.75 (m | 0.7 – 0.8 (m | …... @ ….. % albedo |

| GERB | Geostationary Earth Radiation Budget |
| --- | --- |
| Satellites | Meteosat 8 to 11 (Meteosat Second Generation) |
| Status (Sept 2006) | Operational – Utilisation period: 2002 to ( 2019 |
| Mission | Earth radiation budget |
| Instrument type | Two broad-band channels radiometer |
| Coverage/cycle | Full disk each 5 min. Integration over three cycles (15 min) to comply with accuracy requirements |
| Resolution (s.s.p.) | 42 km |
| Resources | Mass: 25 kg - Power: 35 W - Data rate: 50.6 kbps |

| Channel | Spectral interval | Noise Equivalent Radiance | Absolute accuracy | SNR |
| --- | --- | --- | --- | --- |
| Short-wave | 0.32 - 4.0 (m | 0.8 Wm-2sr-1 | 2.4 Wm-2sr-1 | 1250 |
| Total radiance | 0.32 - 30 (m | 0.15 Wm-2sr-1 | 0.4 Wm-2sr-1 | 400 |

| GLAS | Geoscience Laser Altimeter System |
| --- | --- |
| Satellite | ICESat |
| Status (Sept 2006) | Operational – Utilised in the period 2003 to ( 2008 |
| Mission | Polar ice sheet thickness and topography. Also cloud top height and aerosol |
| Instrument type | Two-wavelengths lidar (532 and 1064 nm) |
| Scanning technique | Nadir-only viewing, sampling at 170 m intervals along track, near continuous profiling |
| Coverage/cycle | Global coverage in 183 d (orbit repeat cycle) leaving cross-track 2.5 km gaps at 80° latitude, 15 km at equator |
| Resolution | Horizontal: 66 m IFOV sampled at 170 m intervals along track. Vertical: 10 cm surface, 200 m cloud top |
| Resources | Mass: 298 kg - Power: 300 W - Data rate: 450 bps |

| GLM | Geostationary Lightning Mapper |
| --- | --- |
| Satellites | GOES-R and follow-on |
| Status (Sept 2006) | Proposed – To be utilised from 2014 onward |
| Mission | Proxy for convective precipitation, proxy for NOx generation, study of Earth electric field |
| Instrument type | CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity |
| Coverage/cycle | Large fraction of the disk continuously observed (time resolution 2 ms) |
| Resolution (s.s.p.) | 8 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| GMI | GPM Microwave Imager |
| --- | --- |
| Satellite | GPM-core |
| Status (Sept 2006) | Planned – To be utilised in the period 2012 to ( 2017 |
| Mission | Multi-purpose MW imager, with emphasis on precipitation |
| Instrument type | MW radiometer with 7 frequencies / 13 channels |
| Scanning technique | Conical: 53° zenith angle; useful swath: 850 km - Scan rate: 32 scan/min = 12.8 km/scan |
| Coverage/cycle | Global coverage in 2 days; high latitudes (> 70°) not covered |
| Resolution | Changing with frequency, consistent with an antenna diameter of 1.2 m |
| Resources | Mass: 80 kg - Power: 90 W - Data rate: 25 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 10.65 | 100 | V, H | 0.6 K | 19.4 x 32.2 km | 12.8 x 25.6 km |
| 18.7 | 200 | V, H | 0.7 K | 11.2 x 18.3 km | 6.4 x 12.8 km |
| 23.8 | 200 | V | 0.9 K | 9.2 x 15.0 km | 6.4 x 12.8 km |
| 36.5 | 1000 | V, H | 0.4 K | 8.6 x 14.4 km | 6.4 x 12.8 km |
| 89.0 | 6000 | V, H | 0.7 K | 4.4 x 7.2 km | 3.2 x 6.4 km |
| 165.5 | 3000 | V, H | 1.5 K | 4.4 x 7.2 km | 3.2 x 6.4 km |
| 183.31 | 3500 | V | 1.5 K | 4.4 x 7.2 km | 3.2 x 6.4 km |
| 183.31 | 4500 | V | 1.5 K | 4.4 x 7.2 km | 3.2 x 6.4 km |

| GOCI | Geostationary Ocean Color Imager |
| --- | --- |
| Satellites | COMS 1 and 2 |
| Status (Sept 2006) | Being designed – To be utilised in the period 2008 to ( 2021 |
| Mission | Ocean color and aerosol |
| Instrument type | 8-channel VIS/NIR radiometer |
| Scanning technique | Pushbroom, 6000 pixel/line (3700 useful), swath 1420 km |
| Coverage/cycle | Area of 2500 km x 2500 km, hourly in daylight |
| Resolution (s.s.p.) | 500 m IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR @ specified NE(L) |
| --- | --- | --- |
| 412 nm | 20 nm | 1000 @ | 0.100 W m-2 sr-1 (-1 |
| 443 nm | 20 nm | 1090 @ | 0.086 W m-2 sr-1 (-1 |
| 490 nm | 20 nm | 1170 @ | 0.067 W m-2 sr-1 (-1 |
| 555 nm | 20 nm | 1070 @ | 0.056 W m-2 sr-1 (-1 |
| 660 nm | 20 nm | 1010 @ | 0.032 W m-2 sr-1 (-1 |
| 680nm | 10 nm | 870 @ | 0.031 W m-2 sr-1 (-1 |
| 745 nm | 20 nm | 860 @ | 0.020 W m-2 sr-1 (-1 |
| 865 nm | 40 nm | 750 @ | 0.016 W m-2 sr-1 (-1 |

| GOME | Global Ozone Monitoring Experiment |
| --- | --- |
| Satellite | ERS-2 |
| Status (Sept 2006) | Operational – Utilised in the period 1995 to ( 2009 |
| Mission | Ozone profile and total-column or gross profile of other species. Tracked species: BrO, ClO, H2O, HCHO, NO, NO2, NO3, O2, O3, O4, OClO, SO2 and aerosol |
| Instrument type | UV/VIS grating spectrometer, four bands, 4096 channels, with 3 polarisation channels |
| Scanning technique | Cross-track: 3 steps of 40 km or 320 km ssp, swath 120 or 960 km - Along-track: one 40-km line each 6 s |
| Coverage/cycle | Global coverage each 24 days with high resolution or 3 days with low resolution. Daylight only |
| Resolution (s.s.p.) | 40 x 40 km2 associated to 120 km swath or 40 x 320 km2 associated to 960 km swath |
| Resources | Mass: 50 kg - Power: 50 W - Data rate: 40 kbps |

| Spectral range | Number of channels | Spectral resolution | SNR at specified input radiance |
| --- | --- | --- | --- |
| 240 - 295 nm | 1024 | 0.22 nm | ................. @ ......... W m-2 sr-1 nm-1 |
| 290 - 405 nm | 1024 | 0.24 nm | ................. @ ......... W m-2 sr-1 nm-1 |
| 400 - 605 nm | 1024 | 0.40 nm | ................. @ ......... W m-2 sr-1 nm-1 |
| 590 - 790 nm | 1024 | 0.40 nm | ................. @ ......... W m-2 sr-1 nm-1 |
| 290 - 790 nm | 3 | 292-402 nm, 402-597 nm, 597-790 nm | ................. @ ......... W m-2 sr-1 nm-1 |

| GOME-2 | Global Ozone Monitoring Experiment - 2 |
| --- | --- |
| Satellites | MetOp 1 to 3 |
| Status (Sept 2006) | Being commissioned - To be utilised in the period 2006 to ( 2020 |
| Mission | Ozone profile and total-column or gross profile of other species. Tracked species: BrO, ClO, H2O, HCHO, NO, NO2, NO3, O2, O3, O4, OClO, SO2 and aerosol |
| Instrument type | UV/VIS grating spectrometer, four bands, 4096 channels, with 200 polarisation channels |
| Scanning technique | Cross-track: 24 steps of 40 km or 80 km ssp, swath 960 or 1920 km - Along-track: one 40-km line each 6 s |
| Coverage/cycle | Global coverage each 3 days with high resolution or 1.5 days with low resolution. Daylight only |
| Resolution (s.s.p.) | 40 x 40 km2 associated to 960 km swath or 40 x 80 km2 associated to 1920 km swath |
| Resources | Mass: 73 kg - Power: 42 W - Data rate: 400 kbps |

| Spectral range | Number of channels | Spectral resolution | SNR at specified input radiance |
| --- | --- | --- | --- |
| 240 - 315 nm | 1024 | 0.24 - 0.29 nm | 7-177 @ 50 % albedo and 60° Solar Zenith Angle |
| 311 - 403 nm | 1024 | 0.26 - 0.28 nm | 372-3000 @ 50 % albedo and 60° SZA |
| 401 - 600 nm | 1024 | 0.44 - 0.53 nm | 4000 @ 50 % albedo and 60° SZA |
| 590 - 790 nm | 1024 | 0.44 - 0.53 nm | 2000-4000 @ 50 % albedo and 60° SZA |
| 312 - 790 nm | 200 | 2.8 nm at 312 nm to 40 nm at 790 nm | 100 for λ< 400 nm, 1000 for 400 nm < λ < 790 nm |

| GOMOS | Global Ozone Monitoring by Occultation of Stars |
| --- | --- |
| Satellite | Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 2002 to ( 2010 |
| Mission | Profiles of ozone and other species. Tracked species: O3, H2O, NO2, NO3, OClO, BrO, ClO and aerosol |
| Instrument type | UV/VIS/NIR grating spectrometer, three bands, ~ 1000 channels, two broadband channels for scintillations |
| Scanning technique | Limb sounding during occultation of 25-40 stars/orbit, i.e. average 500 occultations/day |
| Coverage/cycle | One global coverage/day with one measurement each 1000 x 1000 km2 cell in average |
| Resolution | Vertical: 1.7 km, in the altitude range 20-100 km. Horizontal effective resolution: ~ 300 km (limb geometry) |
| Resources | Mass: 163 kg - Power: 146 W - Data rate: 222 kbps |

| Spectral range | Number of channels | Spectral resolution | SNR at specified input radiance |
| --- | --- | --- | --- |
| 248 - 693 nm | ~ 500 | 0.89 nm | 12 @ …............ |
| 750 - 776 nm | ~ 200 | 0.12 nm | 6 @ ….......... |
| 915 - 956 nm | ~ 300 | 0.12 nm | 3 @ ….......... |
| 466 - 705 nm | 2 | 466-582 nm, 644-705 nm | 15 @ …….…… |

| GRAS | GNSS Receiver for Atmospheric Sounding |
| --- | --- |
| Satellites | MetOp 1 to 3 |
| Status (Sept 2006) | Being commissioned - To be utilised in the period 2006 to ( 2020 |
| Mission | Temperature/humidity sounding with highest vertical resolution, space weather |
| Instrument type | GPS receiver measuring the phase delay due to refraction during occultation between GPS and LEO |
| Scanning technique | Limb scanning from 830 km to close-to-surface by time sampling – Azimuth: 90° sectors fore- and aft- |
| Coverage/cycle | About 500 soundings/day – Average spacing 1000 km – Global coverage (300 km spacing) in 10 days |
| Resolution | About 300 km horizontal, 0.5 km vertical |
| Resources | Mass: 30 kg - Power: 30 W - Data rate: 27 kbps |

| HES | Hyperspectral Environmental Suite |
| --- | --- |
| Satellites | GOES-R (to become GOES-16) and follow-on |
| Status (Sept 2006) | Currently not baselined. Plan being revisited - In case, to be utilised from 2014 onward |
| Mission | Temperature/humidity sounding and wind profile derivation by tracking water vapour features |
| Instrument type | IR spectrometer (+ one VIS channel) for sounding, 14-19 channel radiometer for coastal waters |
| Coverage/cycle | Full disk in maximum 60 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 2-10 km for sounding (0.5-1.0 km for the VIS channel), 0.15-2.0 km for coastal waters |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution (goal and threshold) | Accuracy (variation in the range) |
| --- | --- | --- | --- |
| 15.0 - 15.4 (m | 650 - 665 cm-1 | 0.5 - 0.625 cm-1 | 0.30 - 1.00 K @ 250 K |
| 13.9 - 15.0 (m | 665 - 720 cm-1 | 0.5 - 0.625 cm-1 | 0.17 - 0.30 K @ 250 K |
| 13.0 - 13.9 (m | 720 - 770 cm-1 | 0.5 - 0.625 cm-1 | 0.15 - 0.17 K @ 250 K |
| 9.84 - 13.0 (m | 770 - 1016 cm-1 | 0.5 - 0.625 cm-1 | 0.15 - 0.20 K @ 250 K |
| 9.56 - 9.84 (m | 1016 - 1046 cm-1 | 0.5 - 0.625 cm-1 | 0.15 - 0.20 K @ 250 K |
| 8.33 – 9.56 (m | 1046 - 1200 cm-1 | 0.5 - 0.625 cm-1 | 0.20 - 0.90 K @ 250 K |
| 5.75 - 8.26 (m or | 1210 - 1740 cm-1 or | 0.625 - 1.25 cm-1 | 0.13 - 0.24 K @ 250 K |
| 4.65 - 6.06 (m | 1650 - 2150 cm-1 | 0.625 - 1.25 cm-1 | 0.60 - 1.60 K @ 250 K |
| 4.44 - 4.65 (m | 2150 - 2250 cm-1 | 2.5 cm-1 | 1.5 - 2.0 K @ 250 K |
| 3.68 - 4.44 (m (goal) | 2250 - 2720 cm-1 | 2.5 cm-1 | 0.4 - 3.0 K @ 250 K |
| 0.52 - 0.70 (m | N/A | 0.18 (m | 300 @ 100 % albedo |
| Channel designed for coastal water monitoring | Baseline channels for ocean colour Resolution 150 - 300 m | Central wavelength | Bandwidth | SNR at specified input radiance |
|  |  | 0.412 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.443 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.477 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.490 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.510 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.530 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.550 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.645 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.667 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.678 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.750 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.763 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.865 (m | 0.04 (m | 300 (threshold) to 600 (goal) |
|  |  | 0.905 (m | 0.02 (m | 300 (threshold) to 600 (goal) |
|  | Goal channels | Cloud detection Resolution 0.9 - 1.2 km | 1.38 (m | 0.03 (m | 300 (threshold) to 600 (goal) |
|  |  |  | 1.61 (m | 0.06 (m | 300 (threshold) to 600 (goal) |
|  |  |  | 2.26 (m | 0.05 (m | 300 (threshold) to 600 (goal) |
|  |  | Sea surface temperature Resolution 1.0 - 2.0 km | 11.2 (m | 0.8 (m | NE(T = 0.1 K @ 250 K |
|  |  |  | 12.3 (m | 1.0 (m | NE(T = 0.1 K @ 250 K |

| HIRDLS | High-Resolution Dynamics Limb Sounder |
| --- | --- |
| Satellite | EOS-Aura |
| Status (Sept 2006) | Operational – Utilised in the period 2004 to ( 2011 |
| Mission | Chemistry of the high atmosphere. Tracked species: CFC-11, CFC-12, CH4, ClONO2, H2O, HNO3, N2O, N2O5, NO2, O3, temperature and aerosol |
| Instrument type | 21-channel filter radiometer; range 6.12-17.76 (m |
| Scanning technique | Limb scanning, 6 azimuth angles, swath 2000-3000 km |
| Coverage/cycle | Global coverage each 12 hours for cells of 500 km side |
| Resolution | Vertical: 1 km, in the altitude range 10-100 km. Horizontal effective resolution: ~ 300 km (limb geometry) |
| Resources | Mass: 220 kg - Power: 220 W - Data rate: 65 kbps |

| HiRI | High Resolution Imager |
| --- | --- |
| Satellites | Pléiades 1 and 2 |
| Status (Sept 2006) | Under development - To be utilised in the period 2008 to ( 2015 |
| Mission | Land and vegetation observation. Digital Elevation Model (DEM) |
| Instrument type | Two parallel radiometers, 5 VNIR channels, 4 multi-spectral (MS), one panchromatic (PAN) |
| Scanning technique | Bushbroom, 7500 pixel/line (MS), 30000 pixel/line (PAN), swath 20 km ssp; cross-track and along-track pointing capability by up to ( 30° off-nadir. By combining cross- and along- track capabilities, composite images of 120 km x 120 km may be built. Stereoscopic capability in-orbit and between successive orbits |
| Coverage/cycle | Global coverage in 26 days, in daylight. With strategic pointing, one place can be observed each 2 days. |
| Resolution (s.s.p.) | 2.8 m (MS), 0.7 m (PAN) |
| Resources | Mass: 200 kg - Power: 400 W - Data rate: 465 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.49 (m | 0.45 – 0.53 (m | …... @ ….. % albedo |
| 0.55 (m | 0.52 – 0.58 (m | …... @ ….. % albedo |
| 0.66 (m | 0.62 – 0.70 (m | …... @ ….. % albedo |
| 0.83 (m | 0.78 – 0.89 (m | …... @ ….. % albedo |
| 0.69 (m (PAN) | 0.48 – 0.90 (m | …... @ ….. % albedo |

| HIRS 3/4 | High-resolution Infra Red Sounder 3 / 4 |
| --- | --- |
| Satellites | TIROS-N, NOAA 6 to 17, NOAA 18 and 19 (HIRS/4) - MetOp 1 and 2 (HIRS/4) |
| Status (Sept 2006) | Operational – Utilisation period: 1978 to ( 2014 on NOAA, 2006 to ( 2015 on MetOp |
| Mission | Temperature/humidity sounding |
| Instrument type | 20-channel IR radiometer (including one VIS) |
| Scanning technique | Cross-track: 56 steps of 26 km ssp, swath 2200 km - Along-track: one line each 42 km each 6.4 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 18 km for HIRS/3, 10 km IFOV for HIRS/4 |
| Resources | Mass: 35 kg - Power: 24 W - Data rate: 2.88 kbps |

| Wavelength | Wavenumber | Bandwidth | Radiometric accuracy (NE(N or SNR) | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- | --- | --- |
| 14.95 (m | 669 cm-1 | 3 cm-1 | 3.00 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 14.71 (m | 680 cm-1 | 10 cm-1 | 0.67 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 14.49 (m | 690 cm-1 | 12 cm-1 | 0.50 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 14.22 (m | 703 cm-1 | 16 cm-1 | 0.31 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 13.97 (m | 716 cm-1 | 16 cm-1 | 0.21 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 13.64 (m | 733 cm-1 | 16 cm-1 | 0.24 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 13.35 (m | 749 cm-1 | 16 cm-1 | 0.20 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 12.47 (m | 802 cm-1 | 16 cm-1 | 0.15 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 11.11 (m | 900 cm-1 | 35 cm-1 | 0.10 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 9.71 (m | 1030 cm-1 | 25 cm-1 | 0.15 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 7.33 (m | 1364 cm-1 | 40 cm-1 | 0.20 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 6.52 (m | 1534 cm-1 | 55 cm-1 | 0.20 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 4.57 (m | 2188 cm-1 | 23 cm-1 | 0.006 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 4.52 (m | 2210 cm-1 | 23 cm-1 | 0.003 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 4.47 (m | 2237 cm-1 | 23 cm-1 | 0.004 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 4.45 (m | 2247 cm-1 | 23 cm-1 | 0.004 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 4.13 (m | 2420 cm-1 | 28 cm-1 | 0.002 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 4.00 (m | 2500 cm-1 | 35 cm-1 | 0.002 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 3.76 (m | 2660 cm-1 | 100 cm-1 | 0.001 mW(m-2(sr-1(cm | ..... K @ ..... K |
| 0.69 (m | N/A | 0.05 (m | 0.10 % albedo | ....... @ .... % albedo |

| HRG | Haut Résolution Géométrique |
| --- | --- |
| Satellite | SPOT-5 |
| Status (Sept 2006) | Operational – Utilisation period: 2002 to ( 2009 |
| Mission | Land and vegetation observation. Digital Elevation Model (DEM) |
| Instrument type | Two parallel radiometers, 5 VIS/NIR/SWIR channels, 4 multi-spectral (MS), one panchromatic (PAN) |
| Scanning technique | Bushbroom, 6000 pixel/line (MS), 12000 pixel/line (PAN), swath 60 km ssp (117 km with two instruments), cross-track pointing capability within a range of ( 450 km. Stereoscopic capability between successive orbits |
| Coverage/cycle | Global coverage in 26 days, in daylight. With strategic pointing, one place can be observed each 3 days. |
| Resolution (s.s.p.) | 10 m (the three VNIR channels), 20 m (the SWIR channel), 5 m (PAN) with super-mode at 2.5 m |
| Resources | Mass: 356 kg - Power: 344 W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.545 (m | 0.49 – 0.61 (m | …... @ ….. % albedo |
| 0.645 (m | 0.61 – 0.68 (m | …... @ ….. % albedo |
| 0.835 (m | 0.78 – 0.89 (m | …... @ ….. % albedo |
| 1.645 (m | 1.58 – 1.75 (m | …... @ ….. % albedo |
| 0.59 (m (PAN) (2 shifted channels) | 0.49 – 0.69 (m | …... @ ….. % albedo |

| HRS | Haut Résolution Stéréoscopique |
| --- | --- |
| Satellite | SPOT-5 |
| Status (Sept 2006) | Operational – Utilisation period: 2002 to ( 2009 |
| Mission | Digital Elevation Model (DEM) by in-orbit stereoscopy |
| Instrument type | Single VIS channel (0.51-0.73 (m), SNR ….. @ ….. % albedo |
| Scanning technique | Bushbroom, 12000 pixel/line, swath 120 km ssp, along-track fore- and aft- pointing by ( 20° |
| Coverage/cycle | Global coverage in 26 days, in daylight |
| Resolution (s.s.p.) | 10 m IFOV cross-track, 5 m sampling along-track |
| Resources | Mass: 90 kg - Power: 128 W - Data rate: … Mbps |

| HRV | Haut Résolution dans le Visible |
| --- | --- |
| Satellites | SPOT-1, SPOT-2, SPOT-3 |
| Status (Sept 2006) | Operational (on SPOT-2) - Utilisation period: 1986 to ( 2007 |
| Mission | Land and vegetation observation. Digital Elevation Model (DEM) |
| Instrument type | Two parallel radiometers, 4 VIS/NIR channels, three multi-spectral (MS), one panchromatic (PAN) |
| Scanning technique | Bushbroom, 3000 pixel/line (MS), 6000 pixel/line (PAN), swath 60 km ssp (117 km with two instruments), cross-track pointing capability within a range of ( 450 km. Stereoscopic capability between successive orbits |
| Coverage/cycle | Global coverage in 26 days, in daylight. With strategic pointing, one place can be observed each 3 days. |
| Resolution (s.s.p.) | 20 m (MS), 10 (PAN) |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.545 (m | 0.50 – 0.59 (m | …... @ ….. % albedo |
| 0.645 (m | 0.61 – 0.68 (m | …... @ ….. % albedo |
| 0.84 (m | 0.79 – 0.89 (m | …... @ ….. % albedo |
| 0.62 (m (PAN) | 0.51 – 0.73 (m | …... @ ….. % albedo |

| HRVIR | Haut Résolution dans le Visible et l’Infra-Rouge |
| --- | --- |
| Satellite | SPOT-4 |
| Status (Sept 2006) | Operational - Utilisation period: 1998 to ( 2008 |
| Mission | Land and vegetation observation. Digital Elevation Model (DEM) |
| Instrument type | Two parallel radiometers, 4 VIS/NIR/SWIR multi-spectral (MS) channels, one also panchromatic (PAN) |
| Scanning technique | Bushbroom, 3000 pixel/line (MS), 6000 pixel/line (PAN), swath 60 km ssp (117 km with two instruments), cross-track pointing capability within a range of ( 450 km. Stereoscopic capability between successive orbits |
| Coverage/cycle | Global coverage in 26 days, in daylight. With strategic pointing, one place can be observed each 3 days. |
| Resolution (s.s.p.) | 20 m (MS), 10 (PAN) |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.545 (m | 0.50 – 0.59 (m | …... @ ….. % albedo |
| 0.645 (m (MS) | 0.61 – 0.68 (m | …... @ ….. % albedo |
| 0.645 (m (PAN) | 0.61 – 0.68 (m | …... @ ….. % albedo |
| 0.84 (m | 0.79 – 0.89 (m | …... @ ….. % albedo |
| 1.64 (m | 1.58 – 1.75 (m | …... @ ….. % albedo |

| HSB | Humidity Sounder for Brazil |
| --- | --- |
| Satellite | EOS-Aqua |
| Status (Sept 2006) | No longer operational – To be utilised in the period 2002 to ( 2009 – Actually failed in 2003. |
| Mission | Humidity sounding in almost all-weather conditions. Also precipitation rate |
| Instrument type | 5-channel MW radiometer |
| Scanning technique | Cross-track: 90 steps of 13.5 km ssp, swath 1650 km - Along-track: one 13.5-km line each 8/3 s |
| Coverage/cycle | Near-global coverage once/day |
| Resolution (s.s.p.) | 13.5 km IFOV |
| Resources | Mass: 51 kg - Power: 80 W - Data rate: 4.2 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisation | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 150.0 | 1000 | V | 1.0 K |
| 183.31 ( 7.0 | 2000 | V | 1.0 K |
| 183.31 ( 3.0 | 1000 | V | 1.0 K |
| 183.31 ( 1.0 | 500 | V | 1.0 K |

| Hyperion | Hyperion |
| --- | --- |
| Satellite | NMP EO-1 |
| Status (Sept 2006) | Technological demonstration running – To be utilised in the period 2000-2008 |
| Mission | Advanced technology for land and vegetation observation |
| Instrument type | VIS/NIR/SWIR grating spectrometer with 220 channels, in two groups covering the ranges 0.4-1.0 (m and 0.9-2.5 (m respectively; channels bandwidths 10 nm |
| Scanning technique | Pushbroom; 250 pixel/line; swath 7.5 km |
| Coverage/cycle | Global coverage in 1 year, in daylight. |
| Resolution (s.s.p.) | 30 m IFOV |
| Resources | Mass: 49 kg - Power: 51 W - Data rate: … Mbps |

| IASI | Infrared Atmospheric Sounding Interferometer |
| --- | --- |
| Satellites | Metop 1 to 3 |
| Status (Sept 2006) | Being commissioned - To be utilised in the period 2006 to ( 2020 |
| Mission | Temperature/humidity sounding, ozone profile and total-column green-house gases |
| Instrument type | IR spectrometer/interferometer (8461 channels) with one embedded IR imaging channel |
| Scanning technique | Cross-track: 30 steps of 48 km ssp, swath 2130 km - Along-track: one 48-km line each 8 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 4 x 12-km IFOV close to the centre of a 48 x 48 km2 cell (average sampling distance: 24 km) |
| Resources | Mass: 236 kg - Power: 210 W - Data rate: 1.5 Mbps (after onboard processing) |

| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution (unapodised) | Accuracy (for 0.25 cm-1 channels) (NE(T) |
| --- | --- | --- | --- |
| 8.26 - 15.50 (m | 645 - 1210 cm-1 | 0.25 cm-1 | 0.2-0.3 K @ 280 K |
| 5.00 - 8.26 (m | 1210 - 2000 cm-1 | 0.25 cm-1 | 0.2-0.5 K @ 280 K |
| 3.62 - 5.00 (m | 2000 - 2760 cm-1 | 0.25 cm-1 | 0.5-2.0 K @ 280 K |
| 10.3-12.5 (m | N/A | N/A | 0.8 K @ 280 K |

| IGOS | Integrated GPS Occultation Receiver |
| --- | --- |
| Satellites | COSMIC constellation (6 satellites) |
| Status (Sept 2006) | Operational – Utilised in the period 2006 to ( 2011 |
| Mission | Temperature/humidity sounding with highest vertical resolution, space weather |
| Instrument type | GPS receiver measuring the phase delay due to refraction during occultation between GPS and LEO |
| Scanning technique | Limb scanning from 830 km to close-to-surface by time sampling – Azimuth: 90° sectors fore- and aft- |
| Coverage/cycle | About 500 soundings/day – Average spacing 1000 km – Global coverage (300 km spacing) in 10 days |
| Resolution | About 300 km horizontal, 0.5 km vertical |
| Resources | Mass: … kg - Power: … W - Data rate: 17 kbps |

| IIS | Interferometric Infrared Sounder |
| --- | --- |
| Satellites | FY-4 O A/B and follow-on |
| Status (Sept 2006) | Being defined - To be utilised from 2012 onward |
| Mission | Temperature/humidity sounding and wind profile derivation by tracking water vapour features |
| Instrument type | IR spectrometer/interferometer with large detector arrays for simultaneous sounding of more pixels |
| Coverage/cycle | Full disk in 60 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | Prototype flight 8.0 km, follow-on 4.0 km |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Spectral range (cm-1) | Spectral range ((m) | Spectral resolution | Radiometric accuracy (NE(R) |
| --- | --- | --- | --- |
| 685 - 1130 cm-1 | 14.6 - 8.85 (m | 0.8 cm-1 (later: 0.3 cm-1) | 0.4 mW(m-2(sr-1(cm-1 (later: 0.2 mW(m-2(sr-1(cm-1 |
| 1650 - 2250 cm-1 | 6.06 - 4.44 (m | 0.2 cm-1 (later: 0.6 cm-1) | 0.1 mW(m-2(sr-1(cm-1 (later: 0.06 mW(m-2(sr-1(cm-1) |

| IMAGER | GOES Imager |
| --- | --- |
| Satellites | GOES 8 to 15 |
| Status (Sept 2006) | Operational – Utilisation period: 1994 to ( 2015 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 5-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 4.0 km for IR channels; 1.0 km for the VIS channel |
| Resources | Mass: … kg - Power: … W - Data rate: 2.62 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.65 (m | 0.55 - 0.75 m | ........ @ ... % albedo |
| 3.90 (m | 3.80 - 4.00 (m | 0.11 K @ 300 K |
| 6.55 (m | 5.80 - 7.30 (m | 0.14 K @ 300 K |
| 10.70 (m | 10.2 - 11.2 (m | 0.09 K @ 300 K |
| 13.35 (m | 13.0 - 13.7 (m | ...... K @ 300 K |

| IMAGER | INSAT Imager |
| --- | --- |
| Satellites | INSAT-3D |
| Status (Sept 2006) | Being built – To be utilised in the period 2007 to ( 2014 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 6-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 4.0 km for IR window channels; 1.0 km for VIS/SWIR channels; 8.0 km for water-vapour channel |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.65 (m | 0.52 - 0.72 m | 150 @ 1 % albedo |
| 1.625 (m | 1.55 - 1.70 (m | 150 @ 1 % albedo |
| 3.90 (m | 3.80 - 4.00 (m | 1.4 K @ 300 K |
| 6.8 (m | 6.50 - 7.10 (m | 1.0 K @ 230 K |
| 10.8 (m | 10.2 - 11.2 (m | 0.35 K @ 300 K |
| 12.0 (m | 11.5 - 12.5 (m | 0.35 K @ 300 K |

| IMAGER | MTSAT Imager |
| --- | --- |
| Satellites | MTSAT- 2 |
| Status (Sept 2006) | Standby (Operational utilisation period: 2010 to 2015) |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 5-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Half disk each 15 min. |
| Resolution (s.s.p.) | 4.0 km for IR channels; 1.0 km for the VIS channel |
| Resources | Mass: 163.7 kg - Power: 169 W - Data rate: 2.7 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.675 (m | 0.55 - 0.80 m | 6.5 @ 2.5 % albedo |
| 3.75 (m | 3.50 - 4.00 (m | 0.09 K @ 300 K |
| 6.75 (m | 6.50 - 7.00 (m | 0.12 K @ 300 K |
| 10.8 (m | 10.3 - 11.3 (m | 0.11 K @ 300 K |
| 12.0 (m | 11.5 - 12.5 (m | 0.20 K @ 300 K |

| IMAGER TBD | COMS Imager |
| --- | --- |
| Satellites | COMS-2 |
| Status (Sept 2006) | Being defined (Operational utilisation period: 2014 to 2021) |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | TBD |
| Coverage/cycle | TBD |
| Resolution (s.s.p.) | TBD |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| TBD | TBD | TBD |

| IMAGER TBD | MTSAT Imager |
| --- | --- |
| Satellites | MTSAT-3 and follow-on |
| Status (Sept 2006) | Being defined (Operational utilisation period: 2014 to 2030) |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | Channels to be added to current imager: finally to be similar to MTG/FCI and GOER-R/ABI |
| Coverage/cycle | Full disk in 10 min |
| Resolution (s.s.p.) | 0.5 km VIS channels, 2 km IR channels |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| TBD | TBD | TBD |

| IRAS | Infra Red Atmospheric Sounder |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to launch – To be utilised in the period 2007 to ( 2023 |
| Mission | Temperature/humidity sounding |
| Instrument type | 26-channel IR radiometer (including 6 in short-wave) |
| Scanning technique | Cross-track: 56 steps of 26 km ssp, swath 2250 km - Along-track: one line each 42 km each 6.4 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 17 km IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Wavelength | Wavenumber | Bandwidth | Radiometric accuracy (NE(T or NE(ρ) |
| --- | --- | --- | --- |
| 14.95 (m | 669 cm-1 | 3 cm-1 | 2.50 K @ 290 K |
| 14.71 (m | 680 cm-1 | 10 cm-1 | 0.50 K @ 290 K |
| 14.49 (m | 690 cm-1 | 12 cm-1 | 0.37 K @ 290 K |
| 14.22 (m | 703 cm-1 | 16 cm-1 | 0.22 K @ 290 K |
| 13.97 (m | 716 cm-1 | 16 cm-1 | 0.20 K @ 290 K |
| 13.64 (m | 733 cm-1 | 16 cm-1 | 0.22 K @ 290 K |
| 13.35 (m | 749 cm-1 | 16 cm-1 | 0.18 K @ 290 K |
| 12.47 (m | 802 cm-1 | 30 cm-1 | 0.12 K @ 290 K |
| 11.11 (m | 900 cm-1 | 35 cm-1 | 0.10 K @ 290 K |
| 9.71 (m | 1030 cm-1 | 25 cm-1 | 0.14 K @ 290 K |
| 7.43 (m | 1345 cm-1 | 50 cm-1 | 0.27 K @ 290 K |
| 7.33 (m | 1365 cm-1 | 40 cm-1 | 0.37 K @ 290 K |
| 6.52 (m | 1533 cm-1 | 55 cm-1 | 0.53 K @ 290 K |
| 4.57 (m | 2188 cm-1 | 23 cm-1 | 0.10 K @ 290 K |
| 4.52 (m | 2210 cm-1 | 23 cm-1 | 0.05 K @ 290 K |
| 4.47 (m | 2235 cm-1 | 23 cm-1 | 0.08 K @ 290 K |
| 4.45 (m | 2245 cm-1 | 23 cm-1 | 0.08 K @ 290 K |
| 4.19 (m | 2388 cm-1 | 25 cm-1 | 0.06 K @ 290 K |
| 3.98 (m | 2515 cm-1 | 35 cm-1 | 0.10 K @ 290 K |
| 3.76 (m | 2660 cm-1 | 100 cm-1 | 0.11 K @ 290 K |
| 1.64 (m | 6098 cm-1 | 450 cm-1 | 0.1 % |
| 1.24 (m | 8065 cm-1 | 650 cm-1 | 0.1 % |
| 0.94 (m | 10638 cm-1 | 200 cm-1 | 0.1 % |
| 0.94 (m | 10638 cm-1 | 550 cm-1 | 0.1 % |
| 0.885 (m | 11299 cm-1 | 385 cm-1 | 0.1 % |
| 0.69 (m | 14500 cm-1 | 1000 cm-1 | 0.1 % |

| IRFS-2 | Infrared Sounding Spectrometer |
| --- | --- |
| Satellites | Meteor-M-2 |
| Status (Sept 2006) | Being built – To be utilised in the period 2008 to ( 2012 |
| Mission | Temperature/humidity sounding, ozone profile and total-column green-house gases |
| Instrument type | IR spectrometer/interferometer, 4000 channels |
| Scanning technique | Cross-track: 30 steps to cover a swath of 1000 km if contiguous, up to 2500 km with gaps |
| Coverage/cycle | Near-global coverage twice/day (with gaps) or once/day (continuous) |
| Resolution (s.s.p.) | 35 km IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: 600 kbps |

| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution (unapodised) | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 5 – 15 (m | 667 – 2000 cm-1 | 0.5 cm-1 | 0.5 K @ 300 K |

| IRS | Infra-Red Sounder |
| --- | --- |
| Satellites | Meteosat-12 and follow-on (Meteosat Third Generation) |
| Status (Sept 2006) | Being defined - To be utilised from 2015 onward |
| Mission | Temperature/humidity sounding and wind profile derivation by tracking water vapour features |
| Instrument type | IR spectrometer/interferometer with large detector arrays for simultaneous sounding of more pixels |
| Coverage/cycle | Full disk in 30 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 4.0 km |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Spectral range (cm-1) | Spectral range ((m) | Spectral resolution | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 700 - 1210 cm-1 | 14.3 - 8.26 (m | 0.625 cm-1 | 0.2-0.5 K @ 280 K |
| 1600 - 2175 cm-1 | 6.25 – 4.6 (m | 0.625 cm-1 | 0.2-0.8 K @ 280 K |

| JAMI | Japanese Advanced Meteorological Imager |
| --- | --- |
| Satellites | MTSAT- 1R |
| Status (Sept 2006) | Operational (Utilisation period: 2005 to 2010) |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 5-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Half disk each 15 min. |
| Resolution (s.s.p.) | 4.0 km for IR channels; 1.0 km for the VIS channel |
| Resources | Mass: 163.7 kg - Power: 169 W - Data rate: 2.7 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.725 (m | 0.55 - 0.90 m | 6.5 @ 2.5 % albedo |
| 3.75 (m | 3.50 - 4.00 (m | 0.18 K @ 300 K |
| 6.75 (m | 6.50 - 7.00 (m | 0.18 K @ 300 K |
| 10.8 (m | 10.3 - 11.3 (m | 0.15 K @ 300 K |
| 12.0 (m | 11.5 - 12.5 (m | 0.18 K @ 300 K |

| JMR | JASON Microwave Radiometer |
| --- | --- |
| Satellite | Jason-1 |
| Status (Sept 2006) | Operational – Utilised in the period 2001 to ( 2008 |
| Mission | Water vapour correction for the Poseidon-2 radar altimeter |
| Instrument type | 3-frequency MW radiometer, 18.7, 23.8 and 34 GHz |
| Scanning technique | Nadir-only viewing, associated to the Poseidon-2 radar altimeter |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution (s.s.p.) | 25 km |
| Resources | Mass: 27 kg - Power: 31 W - Data rate: 100 bps |

| KMSS | High-resolution VIS/IR Radiometer |
| --- | --- |
| Satellites | Meteor-M-1/2 |
| Status (Sept 2006) | Being built – To be utilised in the period 2007 to ( 2012 |
| Mission | High-resolution imagery |
| Instrument type | 6-channel VIS/NIR radiometer implemented by 3 cameras, two side-to-side and one overlapping |
| Scanning technique | Cross-track: 8000 CCD/line; swath 960 km |
| Coverage/cycle | Global coverage in 3 days |
| Resolution (s.s.p.) | 60 - 120 m IFOV (see table) |
| Resources | Mass: 8.1 kg - Power: 20.4 W - Data rate: 60 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) | Resolution |
| --- | --- | --- | --- |
| 0.41 (m | 0.37 - 0.45 (m | 200 @ 100 % albedo | 120 m |
| 0.48 (m | 0.45 - 0.51 (m | 200 @ 100 % albedo | 120 m |
| 0.635 (m | 0.58 - 0.69 (m | 200 @ 100 % albedo | 120 m |
| 0.555 (m | 0.535 - 0.575 (m | 200 @ 100 % albedo | 60 m |
| 0.655 (m | 0.63 - 0.68 (m | 200 @ 100 % albedo | 60 m |
| 0.830 (m | 0.76 - 0.90 (m | 200 @ 100 % albedo | 60 m |

| LAC | LEISA (Linear Etalon Imaging Spectrometer Array) Atmospheric Corrector |
| --- | --- |
| Satellite | NMP EO-1 |
| Status (Sept 2006) | Technological demonstration running – To be utilised in the period 2000-2008 |
| Mission | Advanced technology for land and vegetation observation – To correct ALI data for atmospheric effects |
| Instrument type | NIR filter-wedge spectrometer with 256 channels covering the ranges 0.93-1.58 (m with spectral resolution ranging from 2 to 6 nm. In addition, a 1.38 (m channel enables cirrus detection |
| Scanning technique | Pushbroom; 768 pixel/line; swath 185 km |
| Coverage/cycle | Global coverage in 16 days, in daylight. |
| Resolution (s.s.p.) | 250 m IFOV |
| Resources | Mass: 10.5 kg - Power: 35 W - Data rate: 95 Mbps |

| LI | Lightning Imager |
| --- | --- |
| Satellites | Meteosat-12 and follow-on (Meteosat Third Generation) |
| Status (Sept 2006) | Being defined - To be utilised from 2015 onward |
| Mission | Proxy for convective precipitation, proxy for NOx generation, study of Earth electric field |
| Instrument type | CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity |
| Coverage/cycle | Full disk continuously observed (time resolution ~1 ms) |
| Resolution (s.s.p.) | 10 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| LIS | Lightning Imaging Sensor |
| --- | --- |
| Satellite | TRMM |
| Status (Sept 2006) | Operational – Utilised in the period 1997 to ( 2009 |
| Mission | Proxy for convective precipitation, proxy for NOx generation, study of Earth electric field |
| Instrument type | CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity |
| Scanning technique | Pushbroom, matrix array of 128 x 128 detectors, swath 600 km; each earth location observed continuously (each 2 ms) for about 90 s |
| Coverage/cycle | Intertropical coverage 1 to 2 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution (s.s.p.) | 4 km |
| Resources | Mass: 21 kg - Power: 33 W - Data rate: 6 kbps |

| LISS-3 | Linear Imaging Self-Scanning Sensor - 3 |
| --- | --- |
| Satellites | IRS-1C, IRS-1D, IRS-P6 (ResourceSat-1) and ResourceSat-2 |
| Status (Sept 2006) | Operational - Utilisation period: 1995 to ( 2014 |
| Mission | Land and vegetation observation |
| Instrument type | Two parallel radiometers, 4 VIS/NIR/SWIR channels |
| Scanning technique | Bushbroom, 6000 pixel/line (SWIR 2100 pixel/line on IRS-1C/1D), swath 140 km (with two instruments) |
| Coverage/cycle | Global coverage in 24 days, in daylight |
| Resolution (s.s.p.) | IRS-1C/1D: 23.5 m (three VNIR channels), 70 m (SWIR channel), ResourceSat-1/2: 23.5 m in all channels. |
| Resources | Mass: 106.1 kg - Power: 70 W - Data rate: 52.5 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.555 (m | 0.52 – 0.59 (m | …... @ ….. % albedo |
| 0.650 (m | 0.62 – 0.68 (m | …... @ ….. % albedo |
| 0.815 (m | 0.77 – 0.86 (m | …... @ ….. % albedo |
| 1.625 (m | 1.55 – 1.70 (m | …... @ ….. % albedo |

| LISS-4 | Linear Imaging Self-Scanning Sensor - 4 |
| --- | --- |
| Satellite | IRS-P6 (ResourceSat-1) and ResourceSat-2 |
| Status (Sept 2006) | Operational – Utilisation period: 2003 to ( 2014 |
| Mission | Land and vegetation observation |
| Instrument type | 3-channel VIS/NIR radiometer, one camera each channel |
| Scanning technique | Bushbroom, 4096 pixel/line per camera; swath 23.9 km if the 3 cameras are used each for 1 different channel (thus multi-spectral), or 70 km if all cameras are used for viewing parallel strips in the same channel (thus panchromatic). Cross-track pointing capability ( 26° for stereoscopy in between orbits |
| Coverage/cycle | Global coverage in 24 days, in daylight. 5 days for a target area by using cross-track pointing |
| Resolution (s.s.p.) | 5.8 m IFOV |
| Resources | Mass: 169.5 kg - Power: 216 W - Data rate: 105 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.555 (m | 0.52 – 0.59 (m | …... @ ….. % albedo |
| 0.650 (m | 0.62 – 0.68 (m | …... @ ….. % albedo |
| 0.815 (m | 0.77 – 0.86 (m | …... @ ….. % albedo |

| LM | Lightning MAPPER |
| --- | --- |
| Satellites | FY-4 O A/B and follow-on |
| Status (Sept 2006) | Being defined - To be utilised from 2014 onward |
| Mission | Proxy for convective precipitation, proxy for NOx generation, study of Earth electric field |
| Instrument type | CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity |
| Coverage/cycle | Full disk continuously observed (time resolution ~1 ms) |
| Resolution (s.s.p.) | 10 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| MADRAS | Microwave Analysis & Detection of Rain & Atmospheric Structures |
| --- | --- |
| Satellite | Megha-Tropiques |
| Status (Sept 2006) | Planned - To be utilised in the period 2009 to ( 2014 |
| Mission | Contribution to the Global Precipitation Measurement mission (GPM) |
| Instrument type | MW radiometer with 5 frequencies / 9 channels |
| Scanning technique | Conical: 56° zenith angle; swath: 1740 km - Scan rate: 24.6 scan/min = 16 km/scan |
| Coverage/cycle | Intertropical coverage 2 to 5 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution | IFOV ranging from 7 km at 157 GHz to 50 km at 18.7 GHz |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Radiometric accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 18.7 | 180 | V, H | 1.0 K | 40 x 60 km | 40 x 40 km |
| 23.8 | 360 | V | 0.86 K | 40 x 60 km | 40 x 40 km |
| 36.5 | 900 | V, H | 0.72 K | 40 x 60 km | 40 x 40 km |
| 89.0 | 1100 | V, H | 1.23 K | 11 x 16 km | 10 x 10 km |
| 157.0 | 1100 | V, H | 3.3 K | 6 x 9 km | 6 x 6 km |

| MCSI | Multiple Channel Scanning Imager |
| --- | --- |
| Satellites | FY-4 O A/B and follow-on |
| Status (Sept 2006) | Being defined (Operational utilisation period: 2014 to 2030) |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 12-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | From 1 to 4 km (see table) |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) | Resolution @ s.s.p. |
| --- | --- | --- | --- |
| 0.65 (m | 0.55 - 0.75 (m | 200 @ 100 % albedo | 1 km |
| 0.825 (m | 0.75 - 0.90 (m | 200 @ 100 % albedo | 1 km |
| 1.375 (m | 1.36 - 1.39 (m | 200 @ 100 % albedo | 2 km |
| 1.61 (m | 1.58 - 1.64 (m | 200 @ 100 % albedo | 2 km |
| 2.25 (m | 2.1 - 2.35 (m | 200 @ 100 % albedo | 2 km |
| 3.75 (m | 3.5 - 4.0 (m | 0.3 K @ 300 K | 4 km |
| 6.25 (m | 5.8 - 6.7 (m | 0.3 K @ 260 K | 4 km |
| 7.1 (m | 6.9 - 7.3 (m | 0.3 K @ 260 K | 4 km |
| 8.5 (m | 8.0 - 9.0 (m | 0.2 K @ 300 K | 4 km |
| 10.7 (m | 10.3 - 11.1 (m | 0.2 K @ 300 K | 4 km |
| 11.0 (m | 11.5 - 12.5 (m | 0.2 K @ 300 K | 4 km |
| 13.5 (m | 13.2 - 13.8 (m | 0.5 K @ 300 K | 4 km |

| MERIS | Medium Resolution Imaging Spectrometer |
| --- | --- |
| Satellite | Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 2002 to ( 2010 |
| Mission | Ocean colour, vegetation, aerosol, cloud properties |
| Instrument type | 15-channel VIS/NIR spectro-radiometer, channel positions and bandwidths selectable |
| Scanning technique | Bushbroom, 3700 pixel/line (split in 5 parallel optical systems), total swath 1150 km |
| Coverage/cycle | Global coverage in 3 days, in daylight |
| Resolution (s.s.p.) | Basic IFOV 300 m, reduced resolution for global data recording: 1200 km |
| Resources | Mass: 200 kg - Power: 175 W - Data rate: 24 Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR @ specified input radiance) |
| --- | --- | --- |
| 412.5 nm | 10 nm | ................. @ ................. |
| 442.5 nm | 10 nm | ................. @ ................. |
| 490 nm | 10 nm | ................. @ ................. |
| 510 nm | 10 nm | ................. @ ................. |
| 560 nm | 10 nm | ................. @ ................. |
| 620 nm | 10 nm | ................. @ ................. |
| 665 nm | 10 nm | ................. @ ................. |
| 681.25 nm | 7.5 nm | ................. @ ................. |
| 708.75 nm | 10 nm | ................. @ ................. |
| 753.75 nm | 7.5 nm | ................. @ ................. |
| 760.625 nm | 3.75 nm | ................. @ ................. |
| 778.75 nm | 15 nm | ................. @ ................. |
| 865 nm | 20 nm | ................. @ ................. |
| 885 nm | 10 nm | ................. @ ................. |
| 900 nm | 10 nm | ................. @ ................. |

| MERSI | Medium Resolution Spectral Imager |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to launch – To be utilised in the period: 2007 to ( 2023 |
| Mission | Vegetation indexes and ocean colour |
| Instrument type | 20-channel radiometer, 19 narrow-bandwidth in VIR/NIR/SWIR and one broadband in the Thermal IR |
| Scanning technique | Cross-track: 2048 (8192) pixels of 1 km (250 m) ssp, swath 2900 km - Along-track: ten 10-km lines each 1.5 s |
| Coverage/cycle | Global coverage in 1 day (in daylight) |
| Resolution (s.s.p.) | 250 m for broad-band channels, 1.0 km for narrow-band channels |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Channel set | Central wavelength | Spectral range or Bandwidth | Radiometric accuracy (NE(T or NE(ρ) |
| --- | --- | --- | --- |
| Broad-band channels with 250 m resolution, mostly for clouds, vegetation and surface temperature | 0.470 (m | 0.445 - 0.495 (m | 0.45 % |
|  | 0.550 (m | 0.525 - 0.575 (m | 0.4 % |
|  | 0.650 (m | 0.625 - 0.675 (m | 0.3 % |
|  | 0.865 (m | 0.840 - 0.890 (m | 0.3 % |
|  | 11.250 (m | 10.0 - 12.5 (m | 0.3 K @ 300 K |
| Narrow-band channels with 1000 m resolution, for ocean colour, vegetation, aerosol | 412 nm | 20 nm | 0.1 % |
|  | 443 nm | 20 nm | 0.1 % |
|  | 490 nm | 20 nm | 0.05 % |
|  | 520 nm | 20 nm | 0.05 % |
|  | 565 nm | 20 nm | 0.05 % |
|  | 650 nm | 20 nm | 0.05 % |
|  | 685 nm | 20 nm | 0.05 % |
|  | 765 nm | 20 nm | 0.05 % |
|  | 865 nm | 20 nm | 0.05 % |
|  | 905 nm | 20 nm | 0.10 % |
|  | 940 nm | 20 nm | 0.10 % |
|  | 980 nm | 20 nm | 0.10 % |
|  | 1030 nm | 20 nm | 0.10 % |
|  | 1640 nm | 50 nm | 0.05 % |
|  | 2130 nm | 50 nm | 0.05 % |

| MHS | Microwave Humidity Sounder Unit |
| --- | --- |
| Satellites | NOAA 18 to 19 - Metop 1 to 3 |
| Status (Sept 2006) | Operational - Utilisation period: 2005 to ( 2014 on NOAA, 2006 to ( 2020 on MetOp |
| Mission | Humidity sounding in almost all-weather conditions. Also precipitation rate |
| Instrument type | 5-channel MW radiometer |
| Scanning technique | Cross-track: 90 steps of 16 km ssp, swath 2180 km - Along-track: one 16-km line each 8/3 s |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution (s.s.p.) | 16 km IFOV |
| Resources | Mass: 63 kg - Power: 93 W - Data rate: 3.9 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisation | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 89.0 | 2800 | V | 0.22 K |
| 157.0 | 2800 | V | 0.38 K |
| 183.31 ( 3.0 | 2000 | H | 0.42 K |
| 183.31 ( 1.0 | 1000 | H | 0.57 K |
| 190.311 | 2000 | V | 0.45 K |

| MI | Meteorological Imager |
| --- | --- |
| Satellites | COMS-1 |
| Status (Sept 2006) | Being designed – To be utilised in the period 2008 to ( 2015 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 5-channel VIS/IR radiometer |
| Coverage/cycle | Full disk in 27 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 1 km IFOV in 1 VIS channel, 4 km IFOV in 4 IR channels |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.675 m | 0.55 - 0.8 m | 10 @ 5 % albedo, 170 @ 100 % albedo |
| 3.75 m | 3.50 - 4.0 m | 0.10 K @ 300 K |
| 6.75 m | 6.5 - 7.0 m | 0.12 K @ 300 K |
| 10.8 m | 10.3 - 11.3 m | 0.12 K @ 300 K |
| 12 m | 11.5 - 12.5 m | 0.20 K @ 300 K |

| MIPAS | Michelson Interferometer for Passive Atmospheric Sounding |
| --- | --- |
| Satellite | Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 2002 to ( 2010 |
| Mission | Chemistry of the high atmosphere. Tracked species: O3, NO, NO2, HNO3, HNO4, N2O5, ClONO2, COF2, HOCl, CH4, H2O, N2O, CFC’s (F11, F12, F22, CCl4, CF4), CO, OCS, C2H2, C2H6, SF6 and aerosol |
| Instrument type | Michelson interferometer; range 685-2410 cm-1 (4.15-14.6 (m); spectral resolution 0.035 cm-1 unapodised; 60000 channels/spectrum; NESR: 50 nW(cm-2(sr-1(cm @ 685 cm-1, 4.2 nW(cm-2(sr-1(cm @ 2410 cm-1 |
| Scanning technique | Limb scanning, fore- and side. 75 s for one vertical scan; 80 scans/orbit, 1145 profiles/day |
| Coverage/cycle | Global coverage each 3 days for one measurement in each 300 x 300 km2 cell |
| Resolution | Vertical: 3 km, in the altitude range 5-150 km. Horizontal effective resolution: ~ 300 km (limb geometry) |
| Resources | Mass: 320 kg - Power: 210 W - Data rate: 8 Mbps |

| MIRAS | Microwave Imaging Radiometer using Aperture Synthesis |
| --- | --- |
| Satellite | SMOS |
| Status (Sept 2006) | Close to launch – To be utilised in the period: 2008 to ( 2010 |
| Mission | Ocean salinity, soil moisture |
| Instrument type | MW radiometer at 1.413 GHz with synthetic-aperture antenna. Several polarimetric modes. |
| Scanning technique | Pushbroom. Correlation interferometry is implemented among receiver arrays deployed on the three arms of an “Y” shaped antenna. A swath of 1000 km is implemented |
| Coverage/cycle | Global coverage in 3 days (soil moisture). Average over more weeks is needed depending on the desired accuracy for salinity measurements |
| Resolution | 50 km basic, to be degraded depending on the desired accuracy for salinity measurements |
| Resources | Mass: 369 kg - Power: 375 W - Data rate: … kbps |

| MISR | Multi-angle Imaging Spectro-Radiometer |
| --- | --- |
| Satellite | EOS-Terra |
| Status (Sept 2006) | Operational – Utilised in the period 1999 to ( 2008 |
| Mission | Bidirectional Reflectance Distribution Function (BRDF), vegetation, aerosol |
| Instrument type | Assembly of 9 cameras, each one with 4 spectral VIS/NIR channels, each camera with different pointing |
| Scanning technique | Pushbroom; cross-track: 1500 pixels each camera, swath 360 km; along track: nine viewing angles: nadir, ( 26.1°, ( 45.6°, ( 60.0° and ( 70.5° |
| Coverage/cycle | Near-global coverage in one week, in daylight. |
| Resolution (s.s.p.) | Selectable: 275 m or 550 m or 1100 m |
| Resources | Mass: 148 kg - Power: 131 W - Data rate: 3.3 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 446 nm | ........... - ….. nm | …….. @ ….. % albedo |
| 558 nm | ........... - ….. nm | …….. @ ….. % albedo |
| 672 nm | ........... - ….. nm | …….. @ ….. % albedo |
| 866 nm | ........... - ….. nm | …….. @ ….. % albedo |

| MLS | Microwave Limb Sounder |
| --- | --- |
| Satellite | EOS-Aura |
| Status (Sept 2006) | Operational – Utilised in the period 2004 to ( 2011 |
| Mission | Chemistry of the high atmosphere. Tracked species: BrO, ClO, CO, H2O, HCl, HCN, HNO3, HO2, HOCl, N2O, O3, OH, SO2, temperature and pressure |
| Instrument type | 5-band / 36 sub-bands / 1000 channels millimetre-submillimetre heterodyne radiometer at frequencies 118 GHz (9 bands), 190 GHz (6 bands), 240 GHz (7 bands), 640 GHz (9 bands) and 2500 GHz (5 bands) |
| Scanning technique | Limb scanning |
| Coverage/cycle | Global coverage each 3 d for cells of 300 km side |
| Resolution | Vertical: 1.5 km, in the altitude range 5-120 km. Horizontal effective resolution: ~ 300 km (limb geometry) |
| Resources | Mass: 490 kg - Power: 550 W - Data rate: 100 kbps |

| MODIS | Moderate-resolution Imaging Spectro-radiometer |
| --- | --- |
| Satellites | EOS-Terra and EOS-Aqua |
| Status (Sept 2006) | Operational – Utilised in the period 1999 to ( 2009 |
| Mission | Multi-purpose VIS/IR imagery |
| Instrument type | 36-channel VIS/IR spectro-radiometer |
| Scanning technique | Swath 2230 km. Whiskbroom scanning: a strip of 19.7 km width along-track is cross-track scanned each 2.956 s. The strip includes 16 parallel lines sampled by 2048 pixel of 1000 m ssp, or 32 parallel lines sampled by 4096 pixel of 500 m ssp, or 64 parallel lines sampled by 8192 pixel of 250 m ssp |
| Coverage/cycle | Global coverage nearly twice/day (long-wave channels) or once/day (short-wave channels) |
| Resolution (s.s.p.) | IFOV: 0.25 km (two channels), 0.5 km (5 channels), 1.0 km (29 channels) |
| Resources | Mass: 250 kg - Power: 225 W - Data rate: 6.2 Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR or NET) at specified NESR | IFOV at ssp |
| --- | --- | --- | --- |
| 645 nm | 50 nm | 128 @ 21.8 Wm-2m-1sr-1 | 250 m |
| 858 nm | 35 nm | 201 @ 24.7 Wm-2m-1sr-1 | 250 m |
| 469 nm | 20 nm | 243 @ 35.3 Wm-2m-1sr-1 | 500 m |
| 555 nm | 20 nm | 228 @ 29.0 Wm-2m-1sr-1 | 500 m |
| 1240 nm | 20 nm | 74 @ 5.4 Wm-2m-1sr-1 | 500 m |
| 1640 nm | 24 nm | 275 @ 7.3 Wm-2m-1sr-1 | 500 m |
| 2130 nm | 50 nm | 110 @ 1.0 Wm-2m-1sr-1 | 500 m |
| 412 nm | 15 nm | 880 @ 44.9 Wm-2m-1sr-1 | 1000 m |
| 443 nm | 10 nm | 838 @ 41.9 Wm-2m-1sr-1 | 1000 m |
| 488 nm | 10 nm | 802 @ 32.1 Wm-2m-1sr-1 | 1000 m |
| 531 nm | 10 nm | 754 @ 27.9 Wm-2m-1sr-1 | 1000 m |
| 551 nm | 10 nm | 750 @ 21.0 Wm-2m-1sr-1 | 1000 m |
| 667 nm | 10 nm | 910 @ 9.5 Wm-2m-1sr-1 | 1000 m |
| 678 nm | 10 nm | 1087 @ 8.7 Wm-2m-1sr-1 | 1000 m |
| 748 nm | 10 nm | 586 @ 10.2 Wm-2m-1sr-1 | 1000 m |
| 870 nm | 15 nm | 516 @ 6.2 Wm-2m-1sr-1 | 1000 m |
| 905 nm | 30 nm | 167 @ 10.0 Wm-2m-1sr-1 | 1000 m |
| 936 nm | 10 nm | 57 @ 3.6 Wm-2m-1sr-1 | 1000 m |
| 940 nm | 50 nm | 250 @ 15.0 Wm-2m-1sr-1 | 1000 m |
| 1375 nm | 30 nm | 150 @ 6.0 Wm-2m-1sr-1 | 1000 m |
| 3.750 m | 0.180 m | 0.05 K @ 0.45 Wm-2m-1sr-1 | 1000 m |
| 3.959 m | 0.060 m | 2.00 K @ 2.38 Wm-2m-1sr-1 | 1000 m |
| 3.959 m | 0.060 m | 0.07 K @ 0.67 Wm-2m-1sr-1 | 1000 m |
| 4.050 m | 0.060 m | 0.07 K @ 0.79 Wm-2m-1sr-1 | 1000 m |
| 4.515 m | 0.165 m | 0.25 K @ 0.17 Wm-2m-1sr-1 | 1000 m |
| 4.515 m | 0.067 m | 0.25 K @ 0.59 Wm-2m-1sr-1 | 1000 m |
| 6.715 m | 0.360 m | 0.25 K @ 1.16 Wm-2m-1sr-1 | 1000 m |
| 7.325 m | 0.300 m | 0.25 K @ 2.18 Wm-2m-1sr-1 | 1000 m |
| 8.550 m | 0.300 m | 0.25 K @ 9.58 Wm-2m-1sr-1 | 1000 m |
| 9.730 m | 0.300 m | 0.25 K @ 3.69 Wm-2m-1sr-1 | 1000 m |
| 11.030 m | 0.500 m | 0.05 K @ 9.55 Wm-2m-1sr-1 | 1000 m |
| 12.020 m | 0.500 m | 0.05 K @ 8.94 Wm-2m-1sr-1 | 1000 m |
| 13.335 m | 0.300 m | 0.25 K @ 4.52 Wm-2m-1sr-1 | 1000 m |
| 13.635 m | 0.300 m | 0.25 K @ 3.76 Wm-2m-1sr-1 | 1000 m |
| 13.935 m | 0.300 m | 0.25 K @ 3.11 Wm-2m-1sr-1 | 1000 m |
| 14.235 m | 0.300 m | 0.35 K @ 2.08 Wm-2m-1sr-1 | 1000 m |

| MOPITT | Measurement Of Pollution In The Troposphere |
| --- | --- |
| Satellites | EOS-Terra |
| Status (Sept 2006) | Operational – Utilised in the period 1999 to ( 2008 |
| Mission | Atmospheric chemistry. Tracked species: CO (profile) and CH4 (total column) |
| Instrument type | Gas correlation spectrometer; 3 bands, 8 channels. For CO: 4.62 (m (four channels) and 2.33 (m (two channels); for CH4: 2.26 (m (two channels) |
| Scanning technique | Cross-track, 29 steps for a total swath of 640 km |
| Coverage/cycle | Global coverage in 5 days, in daylight |
| Resolution (s.s.p.) | 22 km IFOV |
| Resources | Mass: 182 kg - Power: 243 W - Data rate: 25 kbps |

| MSI | Multi-Spectral Imager |
| --- | --- |
| Satellite | Sentinel-2 1 and 2 |
| Status (Sept 2006) | Being defined – To be utilised in the period 2012 to ( 2020 |
| Mission | Land observation, vegetation, territory management and hazards mitigation |
| Instrument type | 12-channel VIS/NIR/SWIR spectro-radiometer |
| Scanning technique | Pushbroom, swath ( 200 km nominally close to nadir, pointable off-track for emergencies |
| Coverage/cycle | Global coverage in 2 weeks, in daylight. More frequent possible for emergencies |
| Resolution (s.s.p.) | IFOV: 10 to 60 m. depending on channel (see table) |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR @ specified input radiance) | IFOV at s.s.p. |
| --- | --- | --- | --- |
| 443 nm | 20 nm | 129 @ 129.11 W(m-2(sr-1((m-1 | 60 m |
| 490 nm | 65 nm | 154@ 128.00 W(m-2(sr-1((m-1 | 10 m |
| 560 nm | 35 nm | 168.4 @ 128.00 W(m-2(sr-1((m-1 | 10 m |
| 665 nm | 30 nm | 142.1 @ 108.00 W(m-2(sr-1((m-1 | 10 m |
| 705 nm | 15 nm | 117 @ 74.60 W(m-2(sr-1((m-1 | 20 m |
| 740 nm | 15 nm | 89 @ 68.23 W(m-2(sr-1((m-1 | 20 m |
| 775 nm | 20 nm | 105 @ 66.70 W(m-2(sr-1((m-1 | 20 m |
| 842 nm | 115 nm | 174.6 @ 103.00 W(m-2(sr-1((m-1 | 10 m |
| 865 nm | 20 nm | 72 @ 52.39 W(m-2(sr-1((m-1 | 20 m |
| 940 nm | 20 nm | 114 @ 8.77 W(m-2(sr-1((m-1 | 60 m |
| 1375 nm | 20 nm | 50 @ 6.00 W(m-2(sr-1((m-1 | 60 m |
| 1610 nm | 90 nm | 100 @ 4.00 W(m-2(sr-1((m-1 | 20 m |
| 2190 nm | 180 nm | 100 @ 1.70 W(m-2(sr-1((m-1 | 20 m |

| MSMR | Multi-frequency Scanning Microwave Radiometer |
| --- | --- |
| Satellite | IRS-P4 (OceanSat-1) |
| Status (Sept 2006) | Operational – Utilisation period: 1999 to ( 2008 |
| Mission | Sea-surface temperature, wind on sea-surface, total-column water vapour over the sea |
| Instrument type | MW radiometer with 4 frequencies / 8 channels |
| Scanning technique | Conical: 55° zenith angle; swath: 1360 km - Scan rate: 11.16 scan/min = 36 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution | Changing with frequency, consistent with an antenna diameter of 80 cm |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Central frequency | Bandwidth | Polarisations | Radiometric accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 6.6 GHz | 350 MHz | V, H | < 1.0 K | 68 x 105 km | 50 x 36 km |
| 10.65 GHz | 100 MHz | V, H | < 1.0 K | 43 x 66 km | 50 x 36 km |
| 18.0 GHz | 200 MHz | V, H | < 1.0 K | 26 x 40 km | 25 x 36 km |
| 21.0 GHz | 400 MHz | V, H | < 1.0 K | 22 x 34 km | 25 x 36 km |

| MSS | Multi-Spectral Scanner |
| --- | --- |
| Satellite | Landsat 1 to 5 |
| Status (Sept 2006) | Operational – Utilised in the period 1972 to ( 2008 |
| Mission | Land and vegetation observation |
| Instrument type | VIS/NIR radiometer, 6 short-wave channels, one in TIR |
| Scanning technique | Wiskbroom; 2300 pixel/line; swath 185 km |
| Coverage/cycle | Global coverage in 16 days, in daylight. |
| Resolution (s.s.p.) | 80 m IFOV |
| Resources | Mass: 64 kg - Power: 50 W - Data rate: 15 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.55 (m | 0.50 - 0.60 (m | …….. @ ….. % albedo |
| 0.65 (m | 0.60 - 0.70 (m | …….. @ ….. % albedo |
| 0.75 (m | 0.70 - 0.80 (m | …….. @ ….. % albedo |
| 0.95 (m | 0.80 - 1.10 (m | …….. @ ….. % albedo |

| MSU-GS | Elektro-GOMS Imager |
| --- | --- |
| Satellites | Elektro-L and follow on |
| Status (Sept 2006) | Being built -To be utilised from 2007 onward |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 10-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 15-30 min. |
| Resolution (s.s.p.) | 4.0 km for the IR channels, 1.0 km for the VNIR channels |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.57 (m | 0.50 - 0.65 m | 200 @ 100 % albedo |
| 0.72 m | 0.65 - 0.80 m | 200 @ 100 % albedo |
| 0.86 m | 0.80 - 0.90 m | 200 @ 100 % albedo |
| 3.75 m | 3.50 - 4.00 m | 0.35 K @ 300 K |
| 6.35 m | 5.70 - 7.00 m | 0.4 K @ 300 K |
| 8.00 m | 7.50 - 8.50 m | 0.1 K @ 300 K |
| 8.70 m | 8.20 - 9.20 m | 0.15 K @ 300 K |
| 9.70 m | 9.20 - 10.2 m | 0.15 K @ 300 K |
| 10.7 m | 10.2 - 11.2 m | 0.15 K @ 300 K |
| 11.7 m | 11.2 - 12.5 m | 0.25 K @ 300 K |

| MSU-MR | VIS/IR Imaging Radiometer |
| --- | --- |
| Satellites | Meteor-M-1/2 |
| Status (Sept 2006) | Being built – To be utilised in the period 2007 to ( 2012 |
| Mission | Multi-purpose VIS/IR imagery |
| Instrument type | 6-channel VIS/IR radiometer |
| Scanning technique | Cross-track: 1540 pixels in line, swath 2800 km - Along-track: six 1-km lines/s |
| Coverage/cycle | Global coverage twice/day (IR) or once/day (VIS) |
| Resolution (s.s.p.) | 1.0 km IFOV |
| Resources | Mass: 70 kg - Power: … W - Data rate: 660 kbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.60 (m | 0.50 - 0.70 (m | 1000 @ 80 % albedo |
| 0.95 (m | 0.80 - 1.10 (m | 1000 @ 80 % albedo |
| 1.70 (m | 1.60 - 1.80 (m | 1000 @ 80 % albedo |
| 3.80 (m | 3.50 – 4.10 (m | 0.5 K @ 300 K |
| 11.00 (m | 10.5 - 11.5 (m | 0.15 K @ 300 K |
| 12.00 (m | 11.5 - 12.5 (m | 0.15 K @ 300 K |

| MTVZA | Imaging/Sounding Microwave Radiometer |
| --- | --- |
| Satellites | Meteor-M-1/2 |
| Status (Sept 2006) | Being built – To be utilised in the period 2007 to ( 2012 |
| Mission | Multi-purpose MW imager with temperature/humidity sounding channels for improved precipitation |
| Instrument type | 21-frequency / 29-channel MW radiometer |
| Scanning technique | Conical: 53.3° zenith angle, swath 1500 km – Scan rate: 24.9 scan/min = 15.8 km/scan |
| Coverage/cycle | Near-global coverage twice/day |
| Resolution | From 10 km at 183 GHz to 200 km at 10.6 GHz; consistent with an antenna diameter of 65 cm |
| Resources | Mass: 80 kg - Power: 80 W - Data rate: 35 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 10.6 | 100 | V, H | 0.5 K | 89х198 km | 32х32 km |
| 18.7 | 200 | V, H | 0.4 K | 52x160 km | 32x32 km |
| 23.8 | 400 | V, H | 0.3 K | 42x94 km | 32x32 km |
| 31.5 | 400 | V, H | 0.3 K | 35x76 km | 32x32 km |
| 36.7 | 400 | V, H | 0.3 K | 30x67 km | 32x32 km |
| 42.0 | 400 | V, H | 0.4 K | 26x60 km | 32x32 km |
| 48.0 | 400 | V, H | 0.4 K | 24x43 km | 32x32 km |
| 52.80 | 400 | V | 0.4 K | 21x48 km | 48x48 km |
| 53.30 | 400 | V | 0.4 K | 21x48 km | 48x48 km |
| 53.80 | 400 | V | 0.4 K | 21x48 km | 48x48 km |
| 54.64 | 400 | V | 0.4 K | 21x48 km | 48x48 km |
| 55.63 | 400 | V | 0.4 K | 21x48 km | 48x48 km |
| 57.290344(0.3222(0.1 | 50 | H | 0.4 K | 21x48 km | 48x48 km |
| 57.290344(0.3222(0.05 | 20 | H | 0.7 K | 21x48 km | 48x48 km |
| 57.290344(0.3222(0.025 | 10 | H | 0.9 K | 21x48 km | 48x48 km |
| 57.290344(0.3222(0.01 | 5 | H | 1.3 K | 21x48 km | 48x48 km |
| 57.290344(0.3222(0.005 | 3 | H | 1.7 K | 21x48 km | 48x48 km |
| 91.655 | 2500 | V, H | 0.6 K | 14x30 km | 16x16 km |
| 183.31 ( 7.0 | 1500 | V | 0.5 K | 9x21 km | 32x32 km |
| 183.31 ( 3.0 | 1000 | V | 0.6 K | 9x21 km | 32x32 km |
| 183.31 ( 1.0 | 500 | V | 0.8 K | 9x21 km | 32x32 km |

| MVIRI | Meteosat Visible Infra-Red Imager |
| --- | --- |
| Satellites | Meteosat 1 to 7 |
| Status (Sept 2006) | Operational - Utilisation period: 1977 to ( 2008 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 3-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | IFOV: 5.0 km for IR channels, 2.5 km for the VIS channel |
| Resources | Mass: 65 kg - Power: 17 W - Data rate: 333 kbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.70 (m | 0.50 - 0.90 (m | 3 @ 1 % albedo |
| 6.40 (m | 5.70 - 7.10 (m | 1.0 K @ 250 K |
| 11.5 (m | 10.5 - 12.5 (m | 0.5 K @ 300 K |

| MVISR | Multichannel Visible Infrared Scanning Radiometer |
| --- | --- |
| Satellites | FY-1 A to D |
| Status (Sept 2006) | Operational – Utilisation period: 1988 to ( 2007 |
| Mission | Multi-purpose VIS/IR imagery with emphasis on vegetation and ocean colour |
| Instrument type | 10-channel VIS/IR radiometer |
| Scanning technique | Cross-track: 2048 pixel of 800 m ssp, swath 2800 km - Along-track: six 1.1-km lines/s |
| Coverage/cycle | Global coverage twice/day (IR) or once/day (VIS) |
| Resolution (s.s.p.) | 1.1 km |
| Resources | Mass: 55 kg - Power: 45 W - Data rate: 1.23 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.455 (m | 0.43 - 0.48 (m | 3.0 @ 0.5 % albedo |
| 0.505 (m | 0.48 - 0.53 (m | 3.0 @ 0.5 % albedo |
| 0.555 (m | 0.53 - 0.58 (m | 3.0 @ 0.5 % albedo |
| 0.630 (m | 0.58 - 0.68 (m | 3.0 @ 0.5 % albedo |
| 0.865 (m | 0.84 - 0.89 (m | 3.0 @ 0.5 % albedo |
| 0.932 (m | 0.90 - 0.965 (m | 3.0 @ 0.5 % albedo |
| 1.600 (m | 1.55 - 1.64 (m | 3.0 @ 0.5 % albedo |
| 3.740 (m | 3.55 - 3.93 (m | 0.40 K @ 300 K |
| 10.80 (m | 10.3 - 11.3 (m | 0.22 K @ 300 K |
| 12.00 (m | 11.5 - 12.5 (m | 0.22 K @ 300 K |

| MWHS | Micro-Wave Humidity Sounder |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to be launched – To be utilised in the period: 2007 to ( 2023 |
| Mission | Humidity sounding in nearly-all-weather conditions |
| Instrument type | 4-frequency / 5-channel MW radiometer |
| Scanning technique | Cross-track: 98 steps of 16 km ssp, swath 2700 km - Along-track: one 15-km line each 2.667 s |
| Coverage/cycle | Global coverage twice/day |
| Resolution (s.s.p.) | 15 km IFOV |
| Resources | Mass: 44 kg - Power: 60 W - Data rate: 7.5 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) |
| --- | --- | --- | --- |
| 150 | 1000 | V, H | 0.9 K |
| 183.31 ( 7.0 | 2000 | V | 0.9 K |
| 183.31 ( 3.0 | 1000 | V | 0.9 K |
| 183.31 ( 1.0 | 500 | V | 1.1 K |

| MWR | Micro-Wave Radiometer |
| --- | --- |
| Satellites | ERS-1, ERS-2 and Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 1991 to ( 2010 |
| Mission | Water vapour correction for the radar altimeter (RA on ERS-1/2, RA-2 on Envisat) |
| Instrument type | 2-frequency MW radiometer, 23.8 and 36.5 GHz |
| Scanning technique | Nadir-only viewing, associated to the supported radar altimeter |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution (s.s.p.) | 20 km |
| Resources | Mass: 25 kg - Power: 23 W - Data rate: 16.7 kbps |

| MWR | Micro-Wave Radiometer |
| --- | --- |
| Satellites | Sentinel-3 1 & 2 |
| Status (Sept 2006) | Being defined – To be utilised in the period 2012 to ( 2020 |
| Mission | Water vapour correction for the radar altimeter (SRAL) |
| Instrument type | 3-channel MW radiometer: 18.7, 23.8 and 36.5 GHz |
| Scanning technique | Nadir-only viewing, associated to the supported radar altimeter |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution (s.s.p.) | 20 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| MWRI | Micro-Wave Radiation Imager |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to be launched – To be utilised in the period 2007 to ( 2023 |
| Mission | Multi-purpose MW imager |
| Instrument type | 6-frequency, 12-channel MW radiometer |
| Scanning technique | Conical: 53.1° zenith angle, swath 1400 km – Scan rate: 35.3 scan/min = 10 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution (constant) | Changing with frequency, consistent with an antenna diameter of 90 cm |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 10.65 | 180 | V, H | 0.5 K | 51 x 85 km | 70 x 70 km |
| 18.7 | 200 | V, H | 0.5 K | 30 x 50 km | 40 x 40 km |
| 23.8 | 400 | V, H | 0.8 K | 27 x 45 km | 30 x 30 km |
| 36.5 | 900 | V, H | 0.5 K | 18 x 30 km | 25 x 25 km |
| 89 | 4600 | V, H | 1.0 K | 9 x 15 km | 12 x 12 km |
| 150 | 3000 | V, H | 1.3 K | 7.5 x 12 km | 10 x 10 km |

| MWTS | Micro-Wave Temperature Sounder |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to be launched – To be utilised in the period 2007 to ( 2023 |
| Mission | Temperature sounding in nearly-all-weather conditions |
| Instrument type | 4-frequency, 4-channel MW radiometer |
| Scanning technique | Cross-track: 15 steps of 62 km ssp, swath 2250 km - Along-track: one line of 118 km each 16 s |
| Coverage/cycle | Global coverage once/day |
| Resolution (s.s.p.) | 62 km IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisation | Accuracy |
| --- | --- | --- | --- |
| 50.30 | 180 | V | 0.5 K |
| 53.596 ( 0.115 | 340 | H | 0.4 K |
| 54.94 | 400 | V | 0.4 K |
| 57.290 | 330 | H | 0.4 K |

| OCM | Ocean Color Monitor |
| --- | --- |
| Satellite | IRS-P4 (OceanSat-1) and OceanSat-2 |
| Status (Sept 2006) | Operational – Utilisation period: 1999 to ( 2013 |
| Mission | Ocean colour and aerosol |
| Instrument type | 8-channel VIS/NIR radiometer |
| Scanning technique | Pushbroom, 6000 pixel/line (3700 useful), swath 1420 km |
| Coverage/cycle | Global coverage in 2 days, in daylight |
| Resolution (s.s.p.) | 360 m x 236 m IFOV |
| Resources | Mass: 78 kg - Power: 134 W - Data rate: 20.8 Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR @ specified NESR) |
| --- | --- | --- |
| 412 nm | 20 nm | 1300 @ 0.26 W m-2 sr-1 (-1 |
| 442 nm | 20 nm | 1300 @ 0.23 W m-2 sr-1 (-1 |
| 489 nm | 20 nm | 1300 @ 0.17 W m-2 sr-1 (-1 |
| 512 nm | 20 nm | 1500 @ 0.17 W m-2 sr-1 (-1 |
| 557 nm | 20 nm | 1500 @ 0.15 W m-2 sr-1 (-1 |
| 670 nm | 20 nm | 1800 @ 0.10 W m-2 sr-1 (-1 |
| 768 nm | 40 nm | 1800 @ 0.05 W m-2 sr-1 (-1 |
| 867 nm | 40 nm | 2000 @ 0.08 W m-2 sr-1 (-1 |

| OCO | Orbiting Carbon Observatory |
| --- | --- |
| Satellite | EOS-Aura |
| Status (Sept 2006) | Being built – To be utilised in the period 2008 to ( 2010 |
| Mission | CO2 profile. |
| Instrument type | 3 NIR/SWIR grating spectrometer, 3 bands, 0.76 (m (O2), 1.61 and 2.06 (m (CO2) - 3000 channels total |
| Scanning technique | Pushbroom, cross-track swath 10 km, 160 pixels/line binned to 10 super-pixels/line. Three pointing modes: nadir, towards sun glint and towards a specific target |
| Coverage/cycle | Global coverage in one month for cells of 100 km side, in daylight |
| Resolution (s.s.p.) | 1.29 km (cross-track), 2.25 km (along-track |
| Resources | Mass: 150 kg - Power: 165 W - Data rate: 1 Mbps |

| Spectral range | Number of channels | Spectral resolution | SNR at specified input radiance (NESR) |
| --- | --- | --- | --- |
| 758 - 772 nm | 1024 | 0.04 nm | …….. @ ……… mWm-2nm-1sr-1 |
| 1594 - 1619 nm | 1024 | 0.08 nm | …….. @ ……… mWm-2nm-1sr-1 |
| 2042 - 2082 nm | 1024 | 0.10 nm | …….. @ ……… mWm-2nm-1sr-1 |

| OLCI | Ocean and Land Colour Imager |
| --- | --- |
| Satellite | Sentinel-3 1 & 2 |
| Status (Sept 2006) | Planned – To be utilised in the period 2012 to ( 2020 |
| Mission | Ocean colour, vegetation, aerosol, cloud properties |
| Instrument type | 16-channel VIS/NIR spectro-radiometer, channel positions and bandwidths selectable |
| Scanning technique | Pushbroom, 5 side-to-side telescopes, total swath 1270 km. Off-nadir view to avoid sun glint |
| Coverage/cycle | Global coverage in 2 days, in daylight |
| Resolution (s.s.p.) | 250 to 500 m |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR @ expected input radiance) |
| --- | --- | --- |
| 413 nm | 10 nm | 2006 |
| 443 nm | 10 nm | 2087 |
| 490 nm | 10 nm | 1683 |
| 510 nm | 10 nm | 1629 |
| 560 nm | 10 nm | 1481 |
| 620 nm | 10 nm | 1131 |
| 665 nm | 10 nm | 1022 |
| 681 nm | 7.5 nm | 829 |
| 709 nm | 10 nm | 956 |
| 754 nm | 7.5 nm | 673 |
| 761 nm | 3.75 nm | 407 |
| 779 nm | 15 nm | 810 |
| 865 nm | 20 nm | 688 |
| 885 nm | 10 nm | 417 |
| 900 nm | 10 nm | 312 |
| 1020 nm | 40 nm | TBD |

| OLI | Operational Land Imager (current assumption: similar to ALI) |
| --- | --- |
| Satellites | LDCM |
| Status (Sept 2006) | Planned – To be utilised in the period 2010 onwards |
| Mission | Land and vegetation observation |
| Instrument type | VIS/NIR radiometer, 9 VIS/NIR narrow-band channels, one panchromatic (PAN) |
| Scanning technique | Pushbroom; 6000 pixel/line (9 narrow-band channels), 18000 pixel/line (PAN); swath 185 km |
| Coverage/cycle | Global coverage in 16 days, in daylight. |
| Resolution (s.s.p.) | 30 m (9 narrow-band channels), 10 m (PAN) |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 443 nm | 433 - 453 nm | ………. @ ….. % albedo |
| 482 nm | 450 - 515 nm | ………. @ ….. % albedo |
| 565 nm | 525 - 605 nm | ………. @ ….. % albedo |
| 660 nm | 630 - 690 nm | ………. @ ….. % albedo |
| 790 nm | 775 - 805 nm | ………. @ ….. % albedo |
| 867 nm | 845 - 890 nm | ………. @ ….. % albedo |
| 1250 nm | 1200 - 1300 nm | ………. @ ….. % albedo |
| 1650 nm | 1550 - 1750 nm | ………. @ ….. % albedo |
| 2215 nm | 2080 - 2350 nm | ………. @ ….. % albedo |
| Panchromatic | 480 - 690 nm | ………. @ ….. % albedo |

| OMI | Ozone Monitoring Instrument |
| --- | --- |
| Satellite | EOS-Aura |
| Status (Sept 2006) | Operational – Utilised in the period 2004 to ( 2011 |
| Mission | Ozone profile and total-column or gross profile of other species. Tracked species: BrO, NO2, O3, OClO, SO2 and aerosol |
| Instrument type | UV/VIS grating imaging spectrometer, three bands, 1560 channels total |
| Scanning technique | Pushbroom, cross-track swath 2600 km – Zoom mode available, with swath 725 km |
| Coverage/cycle | Global coverage each day, in daylight |
| Resolution (s.s.p.) | 13 x 24 km2 associated to 2600 km swath, reduced to 36 x 48 km2 for profiles. 13 x 12 km2 in zoom mode |
| Resources | Mass: 65 kg - Power: 66 W - Data rate: 800 kbps |

| Spectral range | Number of channels | Spectral resolution | SNR at specified input radiance (NESR) |
| --- | --- | --- | --- |
| 270 - 314 nm | 390 | 0.42 nm | …….. @ ……… mWm-2nm-1sr-1 |
| 306 - 380 nm | 390 | 0.45 nm | …….. @ ……… mWm-2nm-1sr-1 |
| 350 - 500 nm | 780 | 0.63 nm | …….. @ ……… mWm-2nm-1sr-1 |

| OMPS | Ozone Mapping and Profiler Suite |
| --- | --- |
| Satellites | NPP, NPOESS 1 and 3 |
| Status (Sept 2006) | Being built. Limb component currently not baselined on NPOESS – Utilisation period: 2009 to ( 2025 |
| Mission | Ozone profile and total-column or gross profile of other species. Tracked species: BrO, HCHO, NO2, O3, OClO, SO2 |
| Instrument type | Three UV/VIS/NIR grating spectrometers for mapping, nadir profiling and limb sounding respectively |
| Scanning technique | Mapper: cross-track swath 2800 km, along-track one 50-km line in 7.6 s. Nadir profiler: one along-track sounding each 38 s (250 km). Limb sounder: 1-km vertical steps between 10 and 60 km; three adjacent 250-km views, fore- and sides, for a 750 km swath |
| Coverage/cycle | Global coverage: mapper once/day, nadir profiler in 6 days, limb sounder in 4 days. Daylight only |
| Resolution (s.s.p.) | Mapper: 50 km. Nadir profiler: 250 km. Limb sounder: about 300 km |
| Resources | Mass: 56.2 kg - Power: 54 W - Data rate: 180 kbps |

| Subsystem | Spectral range | Spectral resolution | SNR at specified input radiance |
| --- | --- | --- | --- |
| Cross-track mapper for total ozone | 300 - 380 nm | 1 nm | 1000 |
| Nadir-viewing ozone profiler | 250 - 310 nm | 1 nm | 35 (at 250 nm) to 400 (at 310 nm) |
| Limb scanning | 290 - 1000 nm | 1.5 to 40 nm | 320 (at 290 nm) to 1200 (at 600 nm) |

| PALSAR | Phased-Array L-band Synthetic Aperture Radar |
| --- | --- |
| Satellite | ALOS |
| Status (Sept 2006) | Operational – To be utilised in the period 2006 to ( 2010 |
| Mission | High-resolution all-weather soil moisture and ocean surface features observation |
| Instrument type | L-band SAR, frequency 1.27 GHz, multi-polarisation and variable pointing/resolution |
| Scanning technique | Side-looking, 10-51° off-nadir, swath 40 to 350 km, depending on operation mode – See table |
| Coverage/cycle | Global coverage in minimum 2 weeks, depending on operation mode (duty cycle 17.5 min/orbit) |
| Resolution | 7 to 100 m, depending on operation mode – See table |
| Resources | Mass: … kg - Power: … W - Data rate: 240 Mbps |

| Operation mode | Resolution | Swath | Polarisation | Incidence angle |
| --- | --- | --- | --- | --- |
| Highest resolution | 7-44 m | 40-70 km | HH or VV | 8-60° |
| High resolution | 14-89 m | 40-70 km | HH/HV or VV/VH | 8-60° |
| ScanSAR | 100 m | 250-350 km | HH or VV | 18-43° |
| Polarimetry | 24-89 m | 30 km | HH/HV + VV/VH | 8-30° |

| PAN | Panchromatic Camera |
| --- | --- |
| Satellite | CartoSat-2 |
| Status (June 2007) | Operational – Utilisation period: 2007 to ( 2012 |
| Mission | Very-high resolution land imagery |
| Instrument type | Single VNIR channel (0.50-0.85 (m), SNR = … @ ….. % albedo |
| Scanning technique | Pushbroom, 12288 pixel/line, swath 9.6 km |
| Coverage/cycle | Global coverage in 1 year, in daylight |
| Resolution (s.s.p.) | < 1 m IFOV |
| Resources | Mass: 120 kg - Power: 60 W - Data rate: 336 Mbps |

| PAN + MS | Panchromatic + Multispectral Radiometers (also known as PSA + RDSA) |
| --- | --- |
| Satellite | Monitor-E |
| Status (Sept 2006) | Operational – Utilisation period: 2005 to ( 2008 |
| Mission | Land and vegetation monitoring, Digital Elevation Model (DEM) by in-orbit stereoscopy |
| Instrument type | Two VIS/NIR radiometers, one panchromatic, one multi-channel |
| Scanning technique | Pushbroom. PAN: 12000 pixel/line, swath 90 km addressable within an area of regard of 780 km. MS: MS: 8000 pixel/line; swath 160 km addressable within an area of regard of 890 km. Fore- and aft- pointing capability for stereoscopy (by satellite tilting) |
| Coverage/cycle | Global coverage in 26 days (PAN) or 14 days (MS), in daylight; locally more frequent by strategic pointing |
| Resolution (s.s.p.) | IFOV: 8 m (PAN), 20 m (MS) |
| Resources | Mass: 420 kg - Power: 450 W - Data rate: 123 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) | Resolution @ s.s.p. |
| --- | --- | --- | --- |
| 0.565 (m | 0.54 - 0.59 (m | …... @ ….. % albedo | 20 m |
| 0.660 (m | 0.63 - 0.68 (m | …... @ ….. % albedo | 20 m |
| 0.845 (m | 0.79 - 0.90 (m | …... @ ….. % albedo | 20 m |
| 0.68 (m (PAN) | 0.51 - 0.85 (m | …... @ ….. % albedo | 8 m |

| PAN-A, PAN-F | Panchromatic Cameras |
| --- | --- |
| Satellite | IRS-P5 (CartoSat-1) |
| Status (Sept 2006) | Operational – Utilisation period: 2005 to ( 2010 |
| Mission | Digital Elevation Model (DEM) by in-orbit stereoscopy |
| Instrument type | Single VNIR channel (0.50-0.85 (m), SNR = 345 @ 55 mW(cm-2(sr-1((m-1 |
| Scanning technique | Pushbroom, 12000 pixel/line, swath 30 km; PAN-A aft- view 10°, PAN-F fore- view 26° |
| Coverage/cycle | Global coverage in 126 days, in daylight |
| Resolution (s.s.p.) | 2.5 m IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: 340 Mbps |

| POAM | Polar Ozone and Aerosol Measurement |
| --- | --- |
| Satellites | SPOT-3 (POAM-2), SPOT-4 (POAM-3) |
| Status (Sept 2006) | Operational (on SPOT-4) - Utilisation period: 1993 to ( 2008 |
| Mission | Atmospheric chemistry in high troposphere and stratosphere. Species: H2O, NO2, O2, O3 and aerosol |
| Instrument type | 9-channel photometer operating in the range 350-1024 nm (POAM-3) or 350-1064 nm (POAM-2) |
| Scanning technique | Limb scanning in solar occultation; vertical range 10-60 km |
| Coverage/cycle | N/A (few tens of events/day limited to latitudes above ~ 60°) |
| Resolution | 300 km (horizontal), 0.6 km (vertical) |
| Resources | Mass: 24.9 kg - Power: … W - Data rate: … kbps |

| POLDER | Polarization and Directionality of the Earth’s Reflectances |
| --- | --- |
| Satellites | PARASOL, ADEOS-1, ADEOS-2 |
| Status (Sept 2006) | Operational (on PARASOL) - Utilisation period: 2004 to ( 2008 (ADEOS-1: 1996-97; ADEOS-2: 2002-03) |
| Mission | Aerosol, ocean colour, vegetation, Bidirectional Reflectance Distribution Function (BRDF) |
| Instrument type | 9-wavelength radiometer with 3 polarisations at 4 wavelengths (3 in ADEOS) - total: 17 channels |
| Scanning technique | 242 x 274 CCD arrays, 2200 km swath, each earth’s spot viewed from more directions as satellite moves |
| Coverage/cycle | Near-global coverage each day in daylight. |
| Resolution (s.s.p.) | 6 km IFOV (PARASOL), 6.5 km IFOV (ADEOS) |
| Resources | Mass: 32 kg - Power: 50 W - Data rate: 883 kbps |

| Central wavelength | Bandwidth | Polarisations | Radiometric accuracy (SNR) |
| --- | --- | --- | --- |
| 444.5 nm | 20 nm | three | …... @ ….. % albedo |
| 444.9 nm | 20 nm | none | …... @ ….. % albedo |
| 492.2 nm | 20 nm | three | …... @ ….. % albedo |
| 564.5 nm | 20 nm | none | …... @ ….. % albedo |
| 670.2 nm | 20 nm | three | …... @ ….. % albedo |
| 763.3 nm | 10 nm | none | …... @ ….. % albedo |
| 763.1 nm | 40 nm | none | …... @ ….. % albedo |
| 860.8 nm | 40 nm | three | …... @ ….. % albedo |
| 907.3 nm | 20 nm | none | …... @ ….. % albedo |

| Poseidon 2/3 | Poseidon 2/3 |
| --- | --- |
| Satellites | Jason-1 (Poseidon -2) and Jason-2 (Poseidon-3) |
| Status (Sept 2006) | Operational – Utilised in the period 2001 to ( 2015 |
| Mission | Ocean topography, significant wave height, wind speed |
| Instrument type | Two-frequency (5.3 and 13.58 GHz) radar altimeter |
| Scanning technique | Nadir-only viewing, sampling at 30 km intervals along track |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution | 30 km IFOV |
| Resources | Mass: 70 kg - Power: 78 W - Data rate: 22.5 kbps |

| PR | Precipitation Radar |
| --- | --- |
| Satellite | TRMM |
| Status (Sept 2006) | Operational – Utilised in the period 1997 to ( 2009 |
| Mission | Vertical profile of precipitation |
| Instrument type | Imaging radar, frequency 13.8 GHz, |
| Scanning technique | Electronic scanning, planar array of 128 elements, swath 215 km |
| Coverage/cycle | Intertropical coverage 1 to 2 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution (s.s.p.) | Horizontal 4.3 km, vertical 250 m (blind to the lowest ~ 150 m) |
| Resources | Mass: 465 kg - Power: 250 W - Data rate: 93.2 kbps |

| PRISM | Panchromatic Remote-sensing Instrument for Stereo Mapping |
| --- | --- |
| Satellite | ALOS |
| Status (Sept 2006) | Operational – To be utilised in the period 2006 to ( 2010 |
| Mission | Digital Elevation Model (DEM) by stereoscopy |
| Instrument type | Single-channel (0.52-0.77 (m) radiometer with three views, fore-, nadir and aft- (( 24° and nadir) |
| Scanning technique | Push-broom, nadir image 28000 pixel/line / 70 km swath, fore- and aft- 14000 pixel/line / 35 km swath |
| Coverage/cycle | Global coverage in 46 days for nadir imagery, 96 days for stereoscopy |
| Resolution (s.s.p.) | 2.5 m IFOV for the nadir image |
| Resources | Mass: … kg - Power: … W - Data rate: 960 Mbps |

| RA, RA-2 | Radar Altimeter |
| --- | --- |
| Satellites | ERS-1, ERS-2 and Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 1991 to ( 2010 |
| Mission | Ocean topography, significant wave height, wind speed on sea surface |
| Instrument type | Radar altimeter: RA-2 two-frequencies (3.2 and 13.6 GHz), ERS-1/2 RA single frequency (13.8 GHz) |
| Scanning technique | Nadir-only viewing, continuous sampling along track |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution | 20 km IFOV |
| Resources | Mass: 110 kg - Power: 161 W - Data rate: 100 kbps |

| Radiomet | Radio-occultation sounder |
| --- | --- |
| Satellites | Meteor-M-2 |
| Status (Sept 2006) | Being built – Utilisation period: 2008 to ( 2012 |
| Mission | Temperature/humidity sounding with highest vertical resolution, space weather |
| Instrument type | GPS receiver measuring the phase delay due to refraction during occultation between GPS and LEO |
| Scanning technique | Limb scanning from 830 km to close-to-surface by time sampling – Azimuth 90° fore- and aft- |
| Coverage/cycle | About 500 soundings/day – Average spacing 1000 km – Global coverage (300 km spacing) in 10 days |
| Resolution | 300 km (horizontal), 0.5-1.0 km (vertical) |
| Resources | Mass: … kg - Power: … W - Data rate: … bps |

| ROSA | Radio Occultation Sounder of the Atmosphere |
| --- | --- |
| Satellites | OceanSat-2 and SAC-D |
| Status (Sept 2006) | Being built - To be utilised in the period 2008 to ( 2013 |
| Mission | Temperature/humidity sounding with highest vertical resolution, space weather |
| Instrument type | GPS receiver measuring the phase delay due to refraction during occultation between GPS and LEO |
| Scanning technique | Limb scanning from 700 km to close-to-surface by time sampling – Azimuth: 90° sectors fore- and aft- |
| Coverage/cycle | About 500 soundings/day – Average spacing 1000 km – Global coverage (300 km spacing) in 10 days |
| Resolution | About 300 km horizontal, 0.5 km vertical |
| Resources | Mass: 17 kg - Power: 38 W - Data rate: … kbps |

| SAPHIR | Sondeur Atmospherique du Profil d’Humidite Intertropicale par Radiometrie |
| --- | --- |
| Satellite | Megha-Tropiques |
| Status (Sept 2006) | Planned - To be utilised in the period 2009 to ( 2014 |
| Mission | Humidity sounding in nearly-all-weather conditions. Also precipitation |
| Instrument type | 6-channel MW radiometer |
| Scanning technique | Cross-track: 127 steps of 10 km ssp, swath 1700 km - Along-track: one 10-km lines each 1.6 s |
| Coverage/cycle | Intertropical coverage 2 to 5 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution (s.s.p.) | 10 km IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisation | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 183.31 ± 0.2 | 200 | V | 2.35 K |
| 183.31 ± 1.1 | 350 | V | 1.45 K |
| 183.31 ± 2.8 | 500 | V | 1.36 K |
| 183.31 ± 4.2 | 700 | V | 1.38 K |
| 183.31 ± 6.8 | 1200 | V | 1.03 K |
| 183.31 ± 11 | 2000 | V | 1.10 K |

| SAR | Advanced Synthetic Aperture Radar (C-band) |
| --- | --- |
| Satellite | RadarSat 1/2 |
| Status (Sept 2006) | Operational – Utilised in the period 1995 to ( 2014 |
| Mission | High-resolution all-weather multi-purpose imager for ocean, land and ice |
| Instrument type | C-band SAR, frequency 5.405 GHz, multi-polarisation and variable pointing/resolution |
| Scanning technique | Side-looking, possible both to left- and right- end, (alternatively) 20-49° off-nadir, swath 25 to 500 km, depending on operation mode – See table |
| Coverage/cycle | Global coverage in 4 days for the ‘ScanSAR wide’ mode (if used 50 % of the time); in longer periods for other operation modes, up to 6 months |
| Resolution | 3 to 100 m, depending on operation mode – See table |
| Resources | Mass: 705 kg - Power: 1650 W - Data rate: 105 Mbps |

| Operation mode | Resolution | Swath | Polarisation |
| --- | --- | --- | --- |
| Standard | 25 x 28 m2 | 100 km selectable in the range 250-750 km | HH/HV or VV/VH |
| Fine | 10 x 9 m2 | 50 km selectable in the range 525-750 km | HH/HV or VV/VH |
| ScanSAR wide | 100 x 100 m2 | 500 km in the range 250-750 | HH/HV or VV/VH |
| ScanSAR narrow | 50 x 50 m2 | 300 km selectable in the range 300-720 km | HH/HV or VV/VH |
| Polarimetric standard | 25 x 28 m2 | 25 km selectable in the range 250-600 km | VV/HH, HH/HV, VV/VH |
| Polarimetric fine | 11 x 9 m2 | 25 km selectable in the range 400-600 km | VV/HH, HH/HV, VV/VH |
| Multi-look fine | 11 x 9 m2 | 50 km selectable in the range 400-750 km | HH or VV |
| Ultra-fine | 3 x 3 m2 | 20 km selectable in the range 400-550 km | HH or VV |

| SAR-2000 | Advanced Synthetic Aperture Radar - 2000 (X-band) |
| --- | --- |
| Satellite | COSMO-SkyMed 1 to 4 |
| Status (Sept 2006) | Just launched – To be utilised in the period 2007 to ( 2014 |
| Mission | High-resolution all-weather multi-purpose imager for ocean, land and ice |
| Instrument type | X-band SAR, frequency ~ 9.5 GHz, multi-polarisation and variable swath/resolution |
| Scanning technique | Side-looking, possible both to left- and right- end, (alternatively) 20-50° off-nadir, swath 30 to 200 km, depending on operation mode – See table |
| Coverage/cycle | Global coverage in 2 weeks for the ‘huge swath’ mode (if used 50 % of the time); in longer periods for other operation modes, up to 3 months. The constellation of four COSMO-SkyMed enables to address any selected target every 12 hours, for emergencies |
| Resolution | 1 to 100 m, depending on operation mode – See table |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Operation mode | Resolution | Swath | Polarisation |
| --- | --- | --- | --- |
| Spotlight | 1 m | frames of size 10 x 10 km2 | HH or VV or HV or VH |
| Stripmap | 3-15 m | 40 km | HH or VV or HV or VH |
| ScanSAR wide swath | 30 m | 100 km | HH or VV or HV or VH |
| ScanSAR huge swath | 100 m | 200 km | HH or VV or HV or VH |
| Stripmap ping-pong | 15 m | 30 km | HH/HV + VV/VH |

| SAR-C | Advanced Synthetic Aperture Radar (C-band) |
| --- | --- |
| Satellite | GMES 1 A/B (previous name: Sentinel 1) |
| Status (Sept 2006) | Being developed – To be utilised in the period 2011 to ( 2018 |
| Mission | High-resolution all-weather multi-purpose imager for ocean, land and ice |
| Instrument type | C-band SAR, frequency 5.405 GHz, multi-polarisation and variable swath/resolution |
| Scanning technique | Side-looking, 15-45° off-nadir, swath 80 to 400 km, depending on operation mode – See table |
| Coverage/cycle | Global coverage in 5 day for the ‘Extra-wide swath’ mode (duty cycle 70 %); in longer periods for other operation modes (duty cycle 30 %), up to 3 months |
| Resolution | 4 m to 80 m, depending on operation mode – See table |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Operation mode | Resolution | Swath | Polarisation |
| --- | --- | --- | --- |
| Stripmap (SM) | 4 x 5 m2 | 80 km | VV + VH or HH + HV |
| ScanSAR - Interferometric wide-swath (IW) | 5 x 20 m2 | 240 km | VV + VH or HH + HV |
| ScanSAR - Extra-wide swath (EW) | 25 x 80 m2 | 400 km | VV + VH or HH + HV |
| Wave (WV) | 20 x 5 m2 | 20 x 20 km2 each 100 km | HH or VV |

| SAR-L | Advanced Synthetic Aperture Radar (L-band) |
| --- | --- |
| Satellite | SAOCOM 1/2 |
| Status (Sept 2006) | Being developed – To be utilised in the period 2008 to ( 2015 |
| Mission | High-resolution all-weather multi-purpose imager for ocean, land (specifically soil moisture) and ice |
| Instrument type | L-band SAR, frequency 1.275 GHz, multi-polarisation and variable pointing/resolution |
| Scanning technique | Side-looking, 15-50° off-nadir, swath 30 to 320 km, depending on operation mode – See table |
| Coverage/cycle | Global coverage in 1 week for the ‘wide-swath’ mode (if used 50 % of the time); in longer periods for other operation modes, up to 3 months |
| Resolution | 10 to 100 m, depending on operation mode – See table |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Operation mode | Resolution | Swath | Polarisation |
| --- | --- | --- | --- |
| High resolution A | 10 m | 60 km selectable within a range of 320 km | HH or VV |
| High resolution B | 10 m | 30 km selectable within a range of 320 km | VV/HH, HH/HV, VV/VH |
| Medium resolution | 20 m | 60 km selectable within a range of 320 km | HH or VV |
| ScanSAR wide swath | 100 m | 320 km | HH or VV |
| ScanSAR narrow swath | 50 m | 120 km selectable within a range of 320 km | HH or VV |

| SBUV/2 | Solar Backscatter Ultraviolet / 2 |
| --- | --- |
| Satellites | NOAA 9 to 19 except 12 and 15 |
| Status (Sept 2006) | Operational – Utilisation period: 1984 to ( 2014 |
| Mission | Vertical profile of ozone and other species. Solar irradiance |
| Instrument type | UV spectro-radiometer. Either 12 discrete 1-nm bandwidth channels selectable in the interval 252 to 340 nm, or continuous sweep from 160 to 340 nm. |
| Scanning technique | Nadir view only |
| Coverage/cycle | About 1650 measurements/day. Global coverage (170 km spacing) in 10 days, in daylight |
| Resolution | 170 km |
| Resources | Mass: … kg - Power: … W - Data rate: … bps |

| ScaRaB | Scanner for Radiation Budget |
| --- | --- |
| Satellites | Megha-Tropiques (also Meteor-3-7 and Resurs-O1-4) |
| Status (Sept 2006) | Planned - To be utilised in the period 2009 to ( 2014 (1994-95 on Meteor-3-7, in 1998-99 on Resurs-O1-4) |
| Mission | Earth radiation budget at Top Of Atmosphere (TOA) |
| Instrument type | 4-channel radiometer, two broad-band, two narrow-band |
| Scanning technique | Cross-track: 51 pixel/scan, swath 3200 km - Along-track: 1 scan / 6 s |
| Coverage/cycle | Intertropical coverage 2 to 6 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution (s.s.p.) | 40 km IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Channel | Spectral interval | Noise Equivalent Radiance | Absolute accuracy | SNR |
| --- | --- | --- | --- | --- |
| Short-wave | 0.2 - 4.0 (m | < 0.5 W m-2 sr-1 | 1 to 2 % | 850 |
| Total radiance | 0.2 - 50 (m | < 0.5 W m-2 sr-1 | 1 to 2 % | 1000 |
| VIS | 0.55 – 0.65 (m | < 1.0 W m-2 sr-1 | 1 to 2 % | 120 |
| TIR | 10.5-12.5 (m | <0.5 W m-2 sr-1 | 1 to 2 % | 60 |

| SCAT | Scatterometer |
| --- | --- |
| Satellites | OceanSat-2 |
| Status (mid-2006) | Close to launch – To be utilised in the period 2008-2013 |
| Mission | Sea surface wind vector |
| Instrument type | Ku-band radar scatterometer (13.52 GHz) |
| Scanning technique | Conical scanning, two beams, to provide four views of each spot from different angles; swath > 1400 km |
| Coverage/cycle | Global coverage each day |
| Resolution | 50 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| SCIAMACHY | Scanning Imaging Absorption Spectrometer for Atmospheric Cartography |
| --- | --- |
| Satellite | Envisat |
| Status (Sept 2006) | Operational – Utilised in the period 2002 to ( 2010 |
| Mission | Atmospheric chemistry. Tracked species: O3, O2, O4, NO, NO2, NO3, N2O, CO, CO2, CH4, H2O, BrO, ClO, OClO, HCHO, SO2 and aerosol |
| Instrument type | UV/VIS/NIR/SWIR grating spectrometer, eight bands, 8192 channels, with 7 polarisation channels |
| Scanning technique | Cross-track: 16-km cross-track x 32-km along-track, for a swath of 1000 km - One scan line in 4.5 s Limb mode: in addition to vertical scanning, ( 500 km horizontal scanning across track is provided Solar and lunar occultation: in this mode the instrument is self-calibrating (DOAS principle) The three modes are alternative to each other |
| Coverage/cycle | Cross-track mode: if used full time, it would provide global coverage each 3 days (in daylight) Limb mode: if used full time, it would provide global coverage each 3 days (in daylight) Solar and lunar occultation: N/A |
| Resolution | Cross-track mode: 16 x 32 km2 s.s.p. Limb mode: 3 km, in the altitude range 10-100 km, horizontal effective resolution: ~ 300 km (limb geometry) Solar and lunar occultation: 1 km, in the altitude range 10-100 km, horizontal effective resolution: ~ 300 km |
| Resources | Mass: 198 kg - Power: 122 W - Data rate: 400 kbps |

| Spectral range | Number of channels | Spectral resolution | SNR at specified input radiance |
| --- | --- | --- | --- |
| 240-314 nm | 1024 | 0.24 nm | ................. @ ................. |
| 309-405 nm | 1024 | 0.26 nm | ................. @ ................. |
| 394-620 nm | 1024 | 0.44 nm | ................. @ ................. |
| 604-805 nm | 1024 | 0.48 nm | ................. @ ................. |
| 785-1050 nm | 1024 | 0.54 nm | ................. @ ................. |
| 1000-1750 nm | 1024 | 1.48 nm | ................. @ ................. |
| 1940-2040 nm | 1024 | 0.22 nm | ................. @ ................. |
| 2265-2380 nm | 1024 | 0.26 nm | ................. @ ................. |
| 310-2380 nm | 7 | 67 to 137 nm, depending on channel | ................. @ ................. |

| SeaWiFS | Sea-viewing Wide Field-of-view Sensor |
| --- | --- |
| Satellite | SeaStar (now called OrbView-2) |
| Status (Sept 2006) | Operational – Utilised in the period 1997 to ( 2009 |
| Mission | Ocean colour (chlorophyll, suspended sediments, yellow matter, ...) and aerosol |
| Instrument type | 8-channel VIS/NIR radiometer |
| Scanning technique | Cross-track: 2048 pixel of 800 m ssp, swath 2800 km - Along-track: six 1.1-km lines/s - Possibility to tilt the instrument to see aft- or fore- along track by 20 degrees to avoid sunglint |
| Coverage/cycle | Global coverage each day, in daylight |
| Resolution (s.s.p.) | 1.1 IFOV |
| Resources | Mass: 45 kg - Power: … W - Data rate: 2 Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR at specified input radiance) |
| --- | --- | --- |
| 412 nm | 20 nm | 499 @ 9.10 mW/cm2 |
| 443 nm | 20 nm | 674 @ 8.41 mW/cm2 |
| 490 nm | 20 nm | 667 @ 6.56 mW/cm2 |
| 510 nm | 20 nm | 640 @ 5.64 mW/cm2 |
| 555 nm | 20 nm | 596 @ 4.57 mW/cm2 |
| 670 nm | 20 nm | 442 @ 2.46 mW/cm2 |
| 765 nm | 40 nm | 455 @ 1.61 mW/cm2 |
| 865 nm | 40 nm | 467 @ 1.09 mW/cm2 |

| SeaWinds | SeaWinds |
| --- | --- |
| Satellites | QuikSCAT, ADEOS-2, GCOM-W 2/3 |
| Status (mid-2006) | Operational (on QuikSCAT) - Utilisation period: 1999 to ( 2008. If GCOM 2/3 approved, 2014 to ~ 2023 |
| Mission | Sea surface wind vector |
| Instrument type | Ku-band radar scatterometer (13.4 GHz) |
| Scanning technique | Conical scanning, two beams, to provide four views of each spot from different angles; swath 1800 km |
| Coverage/cycle | Global coverage each day |
| Resolution | Best quality: 50 km – standard quality: 25 km – basic sampling: 12.5 km |
| Resources | Mass: 200 kg - Power: 220 W - Data rate: 40 kbps |

| Severjanin | Onboard Radar Complex |
| --- | --- |
| Satellites | Meteor-M 1 and 2 |
| Status (Sept 2006) | Being built – Utilisation period: 2007 to ( 2012 |
| Mission | High-resolution all-weather land observation |
| Instrument type | X-band SAR, frequency 9.623 GHz |
| Scanning technique | Side-looking 25-48°, swath 600 km |
| Coverage/cycle | Global coverage in 1 month (duty cycle 10-20 %) |
| Resolution | Two modes: 400-500 m or 700-1000 m |
| Resources | Mass: … kg - Power: … W - Data rate: 10 Mbps |

| SEVIRI | Spinning Enhanced Visible Infra-Red Imager |
| --- | --- |
| Satellites | Meteosat 8 to 11 (Meteosat Second Generation) |
| Status (Sept 2006) | Operational - Utilisation period: 2002 to ( 2019 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 12-channel VIS/IR radiometer (11 narrow-bandwidth, 1 high-resolution broad-bandwidth VIS) |
| Coverage/cycle | Full disk each 15 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 4.8 km IFOV, 3 km sampling for narrow channels; 1.4 km IFOV, 1 km sampling for broad VIS channel |
| Resources | Mass: 260 kg - Power: 150 W - Data rate: 3.26 Mbps |

| Central wavelength | Spectral interval (99 % encircled energy) | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| N/A (broad bandwidth channel) | 0.6 – 0.9 m | 4.3 @ 1 % albedo |
| 0.635 m | 0.56 – 0.71 m | 10.1 @ 1 % albedo |
| 0.81 m | 0.74 – 0.88 m | 7.28 @ 1 % albedo |
| 1.64 m | 1.50 – 1.78 m | 3 @ 1 % albedo |
| 3.92 m | 3.48 – 4.36 m | 0.35 K @ 300 K |
| 6.25 m | 5.35 – 7.15 m | 0.75 K @ 250 K |
| 7.35 m | 6.85 – 7.85 m | 0.75 K @ 250 K |
| 8.70 m | 8.30 – 9.10 m | 0.28 K @ 300 K |
| 9.66 m | 9.38 – 9.94 m | 1.50 K @ 255 K |
| 10.8 m | 9.80 - 11.8 m | 0.25 K @ 300 K |
| 12.0 m | 11.0 - 13.0 m | 0.37 K @ 300 K |
| 13.4 m | 12.4 - 14.4 m | 1.80 K @ 270 K |

| SGLI | Second-generation Global Imager |
| --- | --- |
| Satellites | GCOM-C (3 satellites) |
| Status (Sept 2006) | Being designed – To be utilised in the period: 2011 to ( 2024 |
| Mission | Ocean colour, vegetation indexes, aerosol |
| Instrument type | 19-channel radiometer, 17 narrow-bandwidth in VIR/NIR/SWIR and two broadband in the Thermal IR. Two channels with three polarisations, with along-track tilting capability of ( 45° |
| Scanning technique | VNIR: pushbroom; SWIR/TIR: whiskbroom Swath 1100 km Cross-track: 3 CCD of 2000 pixels each of 250 m ssp (non polarimetric channels) and 1 CCD of 1000 pixels of 1 km ssp (polarimetric channels) |
| Coverage/cycle | Global coverage in 3 days (in daylight) |
| Resolution (s.s.p.) | 250 m to 1.0 km (see below) |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR or NET) at specified NESR | IFOV at ssp |
| --- | --- | --- | --- |
| 380 nm | 10 nm | ….. @ 60 Wm-2m-1sr-1 | 250 m |
| 412 nm | 10 nm | ….. @ 75 Wm-2m-1sr-1 | 250 m |
| 443 nm | 10 nm | ….. @ 64 Wm-2m-1sr-1 | 250 m |
| 490 nm | 10 nm | ….. @ 53 Wm-2m-1sr-1 | 250 m |
| 530 nm | 20 nm | ….. @ 41 Wm-2m-1sr-1 | 250 m |
| 565 nm | 20 nm | ….. @ 33 Wm-2m-1sr-1 | 250 m |
| 670 nm | 10 nm | ….. @ 23 Wm-2m-1sr-1 | 250 m |
| 670 nm | 20 nm | .…. @ 25 Wm-2m-1sr-1 | 250 m |
| 763 nm | 8 nm | ….. @ 40 Wm-2m-1sr-1 | 1000 m |
| 865 nm | 20 nm | …. @ 8 Wm-2m-1sr-1 | 250 m |
| 865 nm | 20 nm | ….. @ 30 Wm-2m-1sr-1 | 250 m |
| 670 nm 3 pol | 20 nm | ….. @ 25 Wm-2m-1sr-1 | 1000 m |
| 865 nm 3 pol | 20 nm | ….. @ 30 Wm-2m-1sr-1 | 1000 m |
| 1050 nm | 20 nm | ….. @ 57 Wm-2m-1sr-1 | 1000 m |
| 1380 nm | 20 nm | …. @ 8 Wm-2m-1sr-1 | 1000 m |
| 1640 nm | 200 nm | …. @ 3 Wm-2m-1sr-1 | 250 m |
| 2210 nm | 50 nm | ……. @ 1.9 Wm-2m-1sr-1 | 1000 m |
| 10.8 m | 0.7 m | …. K @ 300 K | 500 m |
| 12.0 m | 0.7 m | …. K @ 300 K | 500 m |

| SIRAL | SAR Interferometer Radar Altimeter |
| --- | --- |
| Satellite | CryoSat-2 |
| Status (Sept 2006) | Being built – To be utilised in the period 2009 to ( 2012 |
| Mission | Ice topography, ocean topography, significant wave height, wind speed on sea surface |
| Instrument type | Single frequency radar altimeter (13.56 GHz), with SAR capability along-track for high spatial resolution, and two cross-track aligned antennas implementing SAR interferometry to capture elevation changes |
| Scanning technique | No scanning. Several operating modes possible, depending on the target area |
| Coverage/cycle | Global coverage on high latitudes in 1 month |
| Resolution | 15 km IFOV. When used in SAR mode, the along-track resolution is 250 m |
| Resources | Mass: 70 kg - Power: 149 W - Data rate: 60 kbps, 12 Mbps (SAR), 24 Mbps (SAR interferometry) |

| SLSTR | Sea and Land Surface Temperature Radiometer |
| --- | --- |
| Satellites | Sentinel-3 1 & 2 |
| Status (Sept 2006) | Planned – To be utilised in the period 2012 to ( 2020 |
| Mission | Multi-purpose VIS/IR imagery, with emphasis on very accurate surface temperature for climate |
| Instrument type | 9-channel VIS/IR radiometer with dual viewing directions for accurate atmospheric corrections |
| Scanning technique | Conical oblique, with cross-nadir swath of 1675 km, fore-viewing swath of 750 km |
| Coverage/cycle | From 24 h (IR channels in cross-nadir swath, to 4 days (SW channels in dual viewing) |
| Resolution (s.s.p.) | IFOV: 0.5 km for short-wave channels, 1.0 km for thermal IR |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.555 (m | 20 nm | 20 @ 0.5 % albedo |
| 0.659 (m | 20 nm | 20 @ 0.5 % albedo |
| 0.865 (m | 20 nm | 20 @ 0.5 % albedo |
| 1.375 (m | 15 nm | 20 @ 0.5 % albedo |
| 1.61 (m | 60 nm | 20 @ 0.5 % albedo |
| 2.25 (m | 50 nm | 20 @ 0.5 % albedo |
| 3.74 (m | 380 nm | 0.08 K @ 270 K |
| 10.85 (m | 900 nm | 0.05 K @ 270 K |
| 12.0 (m | 1000 nm | 0.05 K @ 270 K |

| SOUNDER | GOES Sounder |
| --- | --- |
| Satellites | GOES 8 to 15 |
| Status (Sept 2006) | Operational – Utilisation period: 1994 to ( 2015 |
| Mission | Temperature/humidity sounding |
| Instrument type | 19-channel IR radiometer (including one VIS) |
| Coverage/cycle | Full disk in 8 h, 3000x3000 km2 in 42 min, 1000x1000 km2 in 5 min |
| Resolution (s.s.p.) | 8.0 km |
| Resources | Mass: … kg - Power: … W - Data rate: 40 kbps |

| Wavelength | Wavenumber | Bandwidth | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- | --- |
| 14.71 (m | 680 cm-1 | 13 cm-1 | 1.24 K @ 290 K |
| 14.37 (m | 696 cm-1 | 13 cm-1 | 0.79 K @ 290 K |
| 14.06 (m | 711 cm-1 | 13 cm-1 | 0.68 K @ 290 K |
| 13.64 (m | 733 cm-1 | 16 cm-1 | 0.55 K @ 290 K |
| 13.37 (m | 748 cm-1 | 16 cm-1 | 0.49 K @ 290 K |
| 12.66 (m | 790 cm-1 | 30 cm-1 | 0.23 K @ 290 K |
| 12.02 (m | 832 cm-1 | 50 cm-1 | 0.14 K @ 290 K |
| 11.03 (m | 907 cm-1 | 50 cm-1 | 0.10 K @ 290 K |
| 9.71 (m | 1030 cm-1 | 25 cm-1 | 0.12 K @ 290 K |
| 7.43 (m | 1345 cm-1 | 55 cm-1 | 0.06 K @ 290 K |
| 7.02 (m | 1425 cm-1 | 80 cm-1 | 0.06 K @ 290 K |
| 6.51 (m | 1535 cm-1 | 60 cm-1 | 0.15 K @ 290 K |
| 4.57 (m | 2188 cm-1 | 23 cm-1 | 0.20 K @ 290 K |
| 4.52 (m | 2210 cm-1 | 23 cm-1 | 0.17 K @ 290 K |
| 4.45 (m | 2248 cm-1 | 23 cm-1 | 0.20 K @ 290 K |
| 4.13 (m | 2420 cm-1 | 40 cm-1 | 0.14 K @ 290 K |
| 3.98 (m | 2513 cm-1 | 40 cm-1 | 0.22 K @ 290 K |
| 3.74 (m | 2671 cm-1 | 100 cm-1 | 0.14 K @ 290 K |
| 0.70 (m | N/A | 0.05 (m | ....... @ .... % albedo |

| SOUNDER | INSAT Sounder |
| --- | --- |
| Satellites | INSAT-3D |
| Status (Sept 2006) | Being built – To be utilised in the period 2007 to ( 2014 |
| Mission | Temperature/humidity sounding |
| Instrument type | 19-channel IR radiometer (including one VIS) |
| Coverage/cycle | 6000 km x 6000 km in 3 h. Smaller areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 10.0 km |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Wavelength | Wavenumber | Bandwidth | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- | --- |
| 14.71 (m | 680 cm-1 | 13 cm-1 | 1.50 K @ 320 K |
| 14.37 (m | 696 cm-1 | 13 cm-1 | 1.00 K @ 320 K |
| 14.06 (m | 711 cm-1 | 13 cm-1 | 0.50 K @ 320 K |
| 13.96 (m | 716 cm-1 | 16 cm-1 | 0.50 K @ 320 K |
| 13.37 (m | 748 cm-1 | 16 cm-1 | 0.50 K @ 320 K |
| 12.66 (m | 790 cm-1 | 30 cm-1 | 0.30 K @ 320 K |
| 12.02 (m | 832 cm-1 | 50 cm-1 | 0.15 K @ 320 K |
| 11.03 (m | 907 cm-1 | 50 cm-1 | 0.15 K @ 320 K |
| 9.71 (m | 1030 cm-1 | 25 cm-1 | 0.20 K @ 320 K |
| 7.43 (m | 1345 cm-1 | 55 cm-1 | 0.20 K @ 320 K |
| 7.02 (m | 1425 cm-1 | 80 cm-1 | 0.20 K @ 320 K |
| 6.51 (m | 1535 cm-1 | 60 cm-1 | 0.20 K @ 320 K |
| 4.57 (m | 2188 cm-1 | 23 cm-1 | 0.15 K @ 320 K |
| 4.52 (m | 2210 cm-1 | 23 cm-1 | 0.15 K @ 320 K |
| 4.45 (m | 2248 cm-1 | 23 cm-1 | 0.15 K @ 320 K |
| 4.13 (m | 2420 cm-1 | 40 cm-1 | 0.15 K @ 320 K |
| 3.98 (m | 2513 cm-1 | 40 cm-1 | 0.15 K @ 320 K |
| 3.74 (m | 2671 cm-1 | 100 cm-1 | 0.15 K @ 320 K |
| 0.695 (m | N/A | 0.05 (m | 1000 @ 100 % albedo |

| SOUNDER TBD | Infra-Red Sounder |
| --- | --- |
| Satellites | MTSAT-3 and follow-on |
| Status (Sept 2006) | Being defined - To be utilised from 2014 onward |
| Mission | Temperature/humidity sounding and wind profile derivation by tracking water vapour features |
| Instrument type | TBD - User requirement imply using a spectrometer. Feasibility not yet confirmed |
| Coverage/cycle | Full disk in 60 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | TBD |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Spectral range (cm-1) | Spectral range ((m) | Spectral resolution | Radiometric accuracy (NE(T) |
| --- | --- | --- | --- |
| 700 - 1210 cm-1 | 14.3 - 8.26 (m | 0.625 cm-1 | 0.2-0.5 K @ 280 K |
| 1600 - 2175 cm-1 | 6.25 – 4.6 (m | 0.625 cm-1 | 0.2-0.8 K @ 280 K |

| SRAL | SAR Radar Altimeter |
| --- | --- |
| Satellites | Sentinel-3 1 & 2 |
| Status (Sept 2006) | Planned – To be utilised in the period 2012 to ( 2020 |
| Mission | Ocean and ice topography, significant wave height, wind speed on sea surface |
| Instrument type | Dual-frequency radar altimeter (5.3 and 13.58 GHz); SAR capability along-track for high spatial resolution |
| Scanning technique | No scanning. SAR mode possible to be activated, depending on the target area |
| Coverage/cycle | Global coverage in 1 month for 30 km average spacing, or in 10 days for 100 km average spacing |
| Resolution | 20 km IFOV. When used in SAR mode, the along-track resolution is 300 m |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps, … Mbps (SAR) |

| SSM/I | Special Sensor Microwave - IMAGER |
| --- | --- |
| Satellites | DMSP F 8, 10, 11, 13, 14 and 15 |
| Status (Sept 2006) | Operational – Utilisation period: 1987 to ( 2007 |
| Mission | Multi-purpose MW imager |
| Instrument type | 4-frequency, 7-channel MW radiometer |
| Scanning technique | Conical: 53.1° zenith angle, swath 1400 km – Scan rate: 31.9 scan/min = 12.5 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution (constant) | Changing with frequency, consistent with an antenna diameter of 61 x 66 cm |
| Resources | Mass: 48.5 kg - Power: 45 W - Data rate: … kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 19.35 | 400 | V, H | 0.43 K | 45 x 68 km | 25.0 x 12.5 km |
| 22.235 | 400 | V | 0.73 K | 40 x 60 km | 25.0 x 12.5 km |
| 37.0 | 1500 | V, H | 0.38 K | 24 x 36 km | 25.0 x 12.5 km |
| 85.5 | 3000 | V, H | 0.71 K | 11 x 16 km | 12.5 x 12.5 km |

| SSMIS | Special Sensor Microwave – Imager/Sounder |
| --- | --- |
| Satellites | DMSP F 16 and DMSP S 17 to 20 |
| Status (Sept 2006) | Operational – Utilisation period: 2003 to ( 2017 |
| Mission | Multi-purpose MW imager with temperature/humidity sounding channels for improved precipitation |
| Instrument type | 21-frequency, 24-channel MW radiometer |
| Scanning technique | Conical: 53.1° zenith angle, swath 1700 km – Scan rate: 31.9 scan/min = 12.5 km/scan |
| Coverage/cycle | Global coverage once/day |
| Resolution (constant) | Changing with frequency, consistent with an antenna diameter of 61 x 66 cm |
| Resources | Mass: 96 kg - Power: 135 W - Data rate: 14.2 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 19.35 | 400 | V, H | 0.7 K | 45 x 68 km | 25.0 x 12.5 km |
| 22.235 | 400 | V | 0.7 K | 40 x 60 km | 25.0 x 12.5 km |
| 37.0 | 1500 | V, H | 0.5 K | 24 x 36 km | 25.0 x 12.5 km |
| 50.3 | 400 | H | 0.4 K | 18 x 27 km | 37.5 x 12.5 km |
| 52.8 | 400 | H | 0.4 K | 18 x 27 km | 37.5 x 12.5 km |
| 53.596 | 400 | H | 0.4 K | 18 x 27 km | 37.5 x 12.5 km |
| 54.4 | 400 | H | 0.4 K | 18 x 27 km | 37.5 x 12.5 km |
| 55.5 | 400 | H | 0.4 K | 18 x 27 km | 37.5 x 12.5 km |
| 57.29 | 350 | - | 0.5 K | 18 x 27 km | 37.5 x 12.5 km |
| 59.4 | 250 | - | 0.6 K | 18 x 27 km | 37.5 x 12.5 km |
| 60.792668 ( 0.357892 ( 0.050 | 120 | V + H | 0.7 K | 18 x 27 km | 37.5 x 12.5 km |
| 60.792668 ( 0.357892 ( 0.016 | 32 | V + H | 0.6 K | 18 x 27 km | 75.0 x 12.5 km |
| 60.792668 ( 0.357892 ( 0.006 | 12 | V + H | 1.0 K | 18 x 27 km | 75.0 x 12.5 km |
| 60.792668 ( 0.357892 ( 0.002 | 6 | V + H | 1.8 K | 18 x 27 km | 75.0 x 12.5 km |
| 60.792668 ( 0.357892 | 3 | V + H | 2.4 K | 18 x 27 km | 75.0 x 12.5 km |
| 63.283248 ( 0.285271 | 3 | V + H | 2.4 K | 18 x 27 km | 75.0 x 12.5 km |
| 91.655 | 3000 | V, H | 0.9 K | 10 x 15 km | 12.5 x 12.5 km |
| 150 | 1500 | H | 0.9 K | .... x .... km | 37.5 x 12.5 km |
| 183.31 ( 6.6 | 1500 | H | 1.2 K | .... x .... km | 37.5 x 12.5 km |
| 183.31 ( 3.0 | 1000 | H | 1.0 K | .... x .... km | 37.5 x 12.5 km |
| 183.31 ( 1.0 | 500 | H | 1.2 K | .... x .... km | 37.5 x 12.5 km |

| S-VISSR | Stretched Visible and Infrared Spin Scan Radiometer |
| --- | --- |
| Satellites | FY-2 A to G |
| Status (Sept 2006) | Operational – Utilisation period: 1997 to ( 2018 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 5-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 30 min. Limited areas in correspondingly shorter time intervals |
| Resolution (s.s.p.) | 5.0 km for IR channels; 1.25 km for the VIS channel |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.77 (m | 0.55 - 0.99 m | 1.5 @ 0.5 % albedo |
| 3.75 (m | 3.50 - 4.00 (m | 0.4 K @ 300 K |
| 6.95 (m | 6.30 - 7.60 (m | 0.5 K @ 300 K |
| 10.8 (m | 10.3 - 11.3 (m | 0.3 K @ 300 K |
| 12.0 (m | 11.5 - 12.5 (m | 0.3 K @ 300 K |

| TANSO-CAI | Thermal And Near infrared Sensor for carbon Observations - Cloud and Aerosol Imager |
| --- | --- |
| Satellite | GOSAT |
| Status (Sept 2006) | Under development – To be utilised in the period 2008 to ( 2013 |
| Mission | Cloud and aerosol observation |
| Instrument type | 4-channel UV/ VIS/NIR/SWIR radiometer |
| Scanning technique | Push-broom, 2000 pixel/line (three VNIR channels), 500 pixels/line (SWIR channel); 1000 km swath |
| Coverage/cycle | Global coverage in 3 days |
| Resolution (s.s.p.) | 0.5 km IFOV in VNIR, 1.5 km in SWIR |
| Resources | Mass: 40 kg - Power: 100 W - Data rate: … Mbps |

| Central wavelength | Bandwidth | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 380 nm | 20 nm | 200 @ 15 % albedo |
| 674 nm | 20 nm | 200 @ 11 % albedo |
| 870 nm | 20 nm | 200 @ 11 % albedo |
| 1600 nm | 90 nm | 200 @ 10 % albedo |

| TANSO-FTS | Thermal And Near infrared Sensor for carbon Observations - Fourier Transform Spectrometer |
| --- | --- |
| Satellite | GOSAT |
| Status (Sept 2006) | Under development – To be utilised in the period 2008 to ( 2013 |
| Mission | Measurements of CO2, CH4 and other species |
| Instrument type | 4–band SWIR/TIR interferometer |
| Scanning technique | Cross-track mechanical pointing, swath 790 km |
| Coverage/cycle | Global coverage in 3 days |
| Resolution (s.s.p.) | 10.5 km IFOV |
| Resources | Mass: 250 kg - Power: 310 W - Data rate: … Mbps |

| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution (unapodised) | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- | --- |
| 14.28 - 5.55 (m | 700 - 1800 cm-1 | 0.2 cm-1 | ….. K @ 280 K |
| 1.92 – 2.08 (m | 4800 - 5200 cm-1 | 0.2 cm-1 | 300 @ 30 % albedo |
| 1.56 – 1.72 (m | 5800 - 6400 cm-1 | 0.2 cm-1 | 300 @ 30 % albedo |
| 0.757 – 0.775 (m | 12900 - 13200 cm-1 | 0.5 cm-1 | 300 @ 30 % albedo |

| TES | Tropospheric Emission Spectrometer |
| --- | --- |
| Satellite | EOS-Aura |
| Status (Sept 2006) | Operational – Utilised in the period 2004 to ( 2011 |
| Mission | Atmospheric chemistry. Tracked species: CFC-11, CFC12, CH4, CO, CO2, H2O, HCl, HDO, HNO3, N2, N2O, NH3, NO, NO2, O3, OCS, SO2 and aerosol |
| Instrument type | IR imaging interferometer, four bands, 40540 channels (cross-track mode) or 162162 channels (limb mode) |
| Scanning technique | Cross-track mode: array of 16 detectors of 0.53 x 0.53 km2 IFOV s.s.p. moving in 10 steps to cover a FOV of 5.3 x 8.5 km2 that can be pointed everywhere within a cone of 45° aperture or a swath of 885 km. Limb mode: each detector subtends a 2.3 km IFOV at the lowest altitude (surface); the 16 detectors simultaneously observe a range of altitudes of 37 km; the 10 transverse steps cover 23 km (horizontal). The two modes are alternative to each other. |
| Coverage/cycle | Cross-track mode: if used full time and exploiting strategic pointing, in 16 days (the orbital repeat cycle) a global coverage could be obtained for cells of ~ 80-km side. Limb mode: if used full time, it would provide global coverage each 3 days (for cells of 300-km side). |
| Resolution | Cross-track mode: 0.53 x 0.53 km2 s.s.p. Limb mode: 2.3 km in the altitude range 0-37 km; horizontal effective resolution: ~ 300 km (limb geometry) |
| Resources | Mass: 385 kg - Power: 334 W - Data rate: 4.5 Mbps |

| Spectral range ((m) | Spectral range (cm-1) | Spectral resolution (unapodised) | Accuracy (NE(T) |
| --- | --- | --- | --- |
| 11.11 - 15.38 (m | 650 - 900 cm-1 | 0.059 cm-1 (nadir view), 0.015 cm-1 (limb mode) | ……… K @ 280 K |
| 8.70 - 12.20 (m | 820 - 1150 cm-1 | 0.059 cm-1 (nadir view), 0.015 cm-1 (limb mode) | ……… K @ 280 K |
| 5.13 - 9.09 (m | 1100 - 1950 cm-1 | 0.059 cm-1 (nadir view), 0.015 cm-1 (limb mode) | ……… K @ 280 K |
| 3.28 - 5.26 (m | 1900 - 3050 cm-1 | 0.059 cm-1 (nadir view), 0.015 cm-1 (limb mode) | ……… K @ 280 K |

| TIM | Total Irradiance Monitoring |
| --- | --- |
| Satellites | SORCE and Glory |
| Status (Sept 2006) | Operational (on SORCE); to be launched (on Glory) – Utilised from 2003 until ~ 2012 |
| Mission | Total solar irradiance monitoring |
| Instrument type | Assemblage of 4 active cavity radiometers. Range: 0.2-10 (m. |
| Scanning technique | Sun pointing during orbital movement, data sampled each 2 min |
| Coverage/cycle | One measurement after integration on all data taken during the diurnal orbit arc; thus 100 min |
| Resolution (s.s.p.) | N/A (sun pointing) |
| Resources | Mass: 7.9 kg - Power: 14 W - Data rate: 539 bps |

| TM | Thematic Mapper |
| --- | --- |
| Satellites | Landsat 4 and 5 |
| Status (Sept 2006) | Operational – Utilised in the period 1982 to ( 2008 |
| Mission | Land and vegetation observation |
| Instrument type | VIS/NIR radiometer, 6 short-wave channels, one in TIR |
| Scanning technique | Wiskbroom; 6000 pixel/line (6 short-wave channels), 1500 pixel/line (TIR); swath 185 km |
| Coverage/cycle | Global coverage in 16 days, in daylight. |
| Resolution (s.s.p.) | 30 m (6 short-wave channels), 120 m (TIR) |
| Resources | Mass: 258 kg - Power: 332 W - Data rate: 85 Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.48 (m | 0.45 - 0.52 (m | 60 @ ….. % albedo |
| 0.56 (m | 0.52 - 0.60 (m | 60 @ ….. % albedo |
| 0.66 (m | 0.63 - 0.69 (m | 46 @ ….. % albedo |
| 0.83 (m | 0.76 - 0.90 (m | 46 @ ….. % albedo |
| 1.65 (m | 1.55 - 1.75 (m | 36 @ ….. % albedo |
| 2.20 (m | 2.08 - 2.35 (m | 28 @ ….. % albedo |
| 11.45 (m | 10.4 - 12.5 (m | 0.5 K @ 300 K |

| TMI | TRMM Microwave Imager |
| --- | --- |
| Satellite | TRMM |
| Status (Sept 2006) | Operational – To be utilised in the period 1997 to ( 2009 |
| Mission | Multi-purpose MW imager, with emphasis on precipitation |
| Instrument type | MW radiometer with 5 frequencies / 9 channels |
| Scanning technique | Conical: 53° zenith angle; useful swath: 760 km - Scan rate: 32 scan/min = 12.8 km/scan |
| Coverage/cycle | Intertropical coverage 1 to 2 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution | Changing with frequency, consistent with an antenna diameter of 61 x 66 cm |
| Resources | Mass: 65 kg - Power: 50 W - Data rate: 8.8 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 10.65 | 100 | V, H | 0.6 K | 37 x 63 km | 24 x 25.6 km |
| 19.35 | 500 | V, H | 0.7 K | 18 x 30 km | 12 x 12.8 km |
| 21.3 | 200 | V | 0.9 K | 18 x 23 km | 12 x 12.8 km |
| 37.0 | 2000 | V, H | 0.4 K | 9 x 16 km | 6 x 12.8 km |
| 85.5 | 3000 | V, H | 0.7 K | 5 x 7 km | 3 x 6.4 km |

| TOU/SBUS | Total Ozone Unit and Solar Backscatter Ultraviolet Sounder |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to launch – Utilisation period: 2007 to ( 2023 |
| Mission | Ozone total column and vertical profile |
| Instrument type | Two UV spectro-radiometers. TOU with 6 channels of 1.2 nm bandwidth in the range 308-360 nm, SBUS with 12 discrete channels of 1.15 nm bandwidth in the range 252-340 nm |
| Scanning technique | TOU cross-track scanning, swath 3000 km, SBUS nadir view only |
| Coverage/cycle | TOU: global coverage once/day. SBUS: global coverage (200 km spacing) in 7 days. Daylight |
| Resolution | 50 km for total ozone from TOU, 200 km for ozone profile from SBUS |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| TSIS | Total Solar Irradiance Sensor |
| --- | --- |
| Satellites | NPOESS 2 & 4 |
| Status (Sept 2006) | Currently not baselined - If recovered, to be utilised from 2016 until ~ 2027 |
| Mission | Total solar irradiance monitoring, and also spectral solar irradiance in UV/VIS/NIR/SWIR |
| Instrument type | Assemblage of 4 active cavity radiometers for total irradiance (TIM, range 0.2-10 (m), plus a prism spectrometer for spectral irradiance (SIM, range 0.2-2.0 (m, spectral resolution from 0.25 to 33 nm) |
| Scanning technique | Sun pointing during orbital movement, data sampled each 2 min |
| Coverage/cycle | One measurement after integration on all data taken during the diurnal orbit arc; thus 100 min |
| Resolution (s.s.p.) | N/A (sun pointing) |
| Resources | TIM: mass 7.9 kg, power 14 W, data rate 539 bps – SIM: mass 22 kg, power 25.3 W, data rate …... kbps |

| Végétation | Végétation |
| --- | --- |
| Satellites | SPOT-4, SPOT-5 |
| Status (Sept 2006) | Operational - Utilisation period: 1998 to ( 2009 |
| Mission | Vegetation observation |
| Instrument type | 4-channel VIS/NIR/SWIR radiometer |
| Scanning technique | Bushbroom, 1728 pixel/line, swath 2200 km |
| Coverage/cycle | Near-global coverage in one day |
| Resolution (s.s.p.) | 1.15 km IFOV |
| Resources | Mass: 152 kg - Power: 200 W - Data rate: 510 kbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR) |
| --- | --- | --- |
| 0.450 (m | 0.43 – 0.47 (m | …... @ ….. % albedo |
| 0.645 (m | 0.61 – 0.68 (m | …... @ ….. % albedo |
| 0.835 (m | 0.78 – 0.89 (m | …... @ ….. % albedo |
| 1.645 (m | 1.58 – 1.75 (m | …... @ ….. % albedo |

| VHRR (in GEO) | Very High Resolution Radiometer |
| --- | --- |
| Satellites | INSAT-1 A/B/C/D, INSAT-2 A/B/D/E, INSAT-3A, Kalpana |
| Status (Sept 2006) | Operational – Utilisation period: 1982 to ( 2012 |
| Mission | Multi-purpose VIS/IR imagery and wind derivation by tracking clouds and water vapour features |
| Instrument type | 3-channel VIS/IR radiometer |
| Coverage/cycle | Full disk each 3 hours, more frequently on demand. Half-hourly triplets around 00 and 12 UT for winds |
| Resolution (s.s.p.) | 8.0 km for IR channels; 2 km for the VIS channel |
| Resources | Mass: … kg - Power: … W - Data rate: … kbps |

| Central wavelength | Spectral interval | Radiometric accuracy (SNR or NE(T) |
| --- | --- | --- |
| 0.65 (m | 0.55 - 0.75 m | > 6 @ 2.5 % albedo |
| 6.40 (m | 5.70 - 7.10 (m | 0.50 K @ 300 K |
| 11.5 (m | 10.5 - 12.5 (m | 0.25 K @ 300 K |

| VIIRS | Visible/Infrared Imager Radiometer Suite |
| --- | --- |
| Satellites | NPP, NPOESS 1 to 4 |
| Status (Sept 2006) | Being built – Utilisation period: 2009 to ( 2027 |
| Mission | Multi-purpose VIS/IR imagery, including ocean colour |
| Instrument type | 22-channel VIS/IR radiometer, including a day/night 0.7 (m channel |
| Scanning technique | Cross-track: 16 parallel lines sampled by 2048 pixel of 800 m ssp and 32 parallel lines sampled by 4096 pixel of 400 m ssp; swath 3000 km. Along-track: one 11.9-km strip of 16 or 32 lines in 1.786 s. |
| Coverage/cycle | Global coverage twice/day (IR) or once/day (VIS) |
| Resolution (s.s.p.) | 400 m for five AVHRR-like channels and the VIS day/night channel, 800 m for all other channels |
| Resources | Mass: 252 kg - Power: 186 W - Data rate: 5.9 Mbps |

| Channel set | Central | Bandwidth or | Radiometric accuracy | (SNR or NE(T) |
| --- | --- | --- | --- | --- |
| and resolution | wavelength | spectral interval | High or single gain | Low gain |
| High-quality radiometric channels, resolution 800 m | 412 nm | 20 nm | 352 @ 45 Wm-2m-1sr-1 | 316 @ 155 Wm-2m-1sr-1 |
|  | 445 nm | 18 nm | 380 @ 40 Wm-2m-1sr-1 | 409 @ 146 Wm-2m-1sr-1 |
|  | 488 nm | 20 nm | 416 @ 32 Wm-2m-1sr-1 | 414 @ 123 Wm-2m-1sr-1 |
|  | 555 nm | 20 nm | 362 @ 21 Wm-2m-1sr-1 | 315 @ 90 Wm-2m-1sr-1 |
|  | 672 nm | 20 nm | 242 @ 10 Wm-2m-1sr-1 | 360 @ 68 Wm-2m-1sr-1 |
|  | 746 nm | 15 nm | 199 @ 9.6 Wm-2m-1sr-1 |  |
|  | 865 nm | 39 nm | 215 @ 6.4 Wm-2m-1sr-1 | 340 @ 33.4 Wm-2m-1sr-1 |
|  | 1240 nm | 20 nm | 101 @ 5.4 Wm-2m-1sr-1 |  |
|  | 1378 nm | 15 nm | 83 @ 6.0 Wm-2m-1sr-1 |  |
|  | 1610 nm | 60 nm | 342 @ 7.3 Wm-2m-1sr-1 |  |
|  | 2250 nm | 50 nm | 10 @ 0.12 Wm-2m-1sr-1 |  |
|  | 3.70 (m | 0.18 (m | 0.40 K @ 270 K |  |
|  | 4.05 (m | 0.155 (m | 0.11 K @ 300 K | 0.42 K @ 380 K |
|  | 8.55 (m | 0.30 (m | 0.09 K @ 270 K |  |
|  | 10.763 (m | 1.00 (m | 0.07 K @ 300 K |  |
|  | 12.013 (m | 0.95 (m | 0.07 K @ 300 K |  |
| Day/night band, resolution 800 m | 0.7 (m | 0.5 - 0.9 (m | 5 @ 6.70 E-5 |  |
| High-resolution imaging channels, resolution 400 m | 0.64 (m | 0.60 - 0.68 (m | 119 @ 22 Wm-2m-1sr-1 |  |
|  | 0.865 (m | 0.845 - 0.884 (m | 150 @ 25 Wm-2m-1sr-1 |  |
|  | 1.61 (m | 1.58 - 1.64 (m | 6 @ 7.3 Wm-2m-1sr-1 |  |
|  | 3.74 (m | 3.55 - 3.93 (m | 2.50 K @ 270 K |  |
|  | 11.45 (m | 10.5 - 12.4 (m | 1.50 K @ 210 K |  |

| VIRR | Visible and Infra Red Radiometer |
| --- | --- |
| Satellites | FY-3 A to G |
| Status (Sept 2006) | Close to launch – Utilisation period: 2007 to ( 2023 |
| Mission | Multi-purpose VIS/IR imagery with emphasis on vegetation and ocean colour |
| Instrument type | 10-channel VIS/IR radiometer |
| Scanning technique | Cross-track: 2048 pixel of 800 m ssp, swath 2800 km - Along-track: six 1.1-km lines/s |
| Coverage/cycle | Global coverage twice/day (IR) or once/day (VIS) |
| Resolution (s.s.p.) | 1.1 km IFOV |
| Resources | Mass: … kg - Power: … W - Data rate: … Mbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(ρ or NE(T) |
| --- | --- | --- |
| 0.455 (m | 0.43 - 0.48 (m | 0.05 % |
| 0.505 (m | 0.48 - 0.53 (m | 0.05 % |
| 0.555 (m | 0.53 - 0.58 (m | 0.05 % |
| 0.630 (m | 0.58 - 0.68 (m | 0.10 % |
| 0.865 (m | 0.84 – 0.89 (m | 0.10 % |
| 1.360 (m | 1.325 - 1.395 (m | 0.19 % |
| 1.600 (m | 1.55 - 1.64 (m | 0.15 % |
| 3.740 (m | 3.55 - 3.93 (m | 0.3 K @ 300 K |
| 10.80 (m | 10.3 - 11.3 (m | 0.2 K @ 300 K |
| 12.00 (m | 11.5 - 12.5 (m | 0.2 K @ 300 K |

| VIRS | Visible and Infra-Red Scanner |
| --- | --- |
| Satellites | TRMM |
| Status (Sept 2006) | Operational – To be utilised in the period 1997 to ( 2009 |
| Mission | Multi-purpose VIS/IR imagery |
| Instrument type | 5-channel VIS/IR radiometer |
| Scanning technique | Cross-track: 256 pixel of 1.6 km s.s.p., swath 720 km - Along-track: 240 lines/min, 1.7 km/scan |
| Coverage/cycle | Intertropical coverage 1 to 2 times/day depending on latitude (best coverage at 15°N and 15°S) |
| Resolution (s.s.p.) | 2.0 km IFOV |
| Resources | Mass: 34.5 kg - Power: 40 W - Data rate: 50 kbps |

| Central wavelength | Spectral interval | Radiometric accuracy (NE(T or SNR) |
| --- | --- | --- |
| 0.630 (m | 0.58 - 0.68 (m | 9 @ 0.5 % albedo |
| 1.61 (m | 1.58 - 1.64 (m | 20 @ 0.5 % albedo |
| 3.74 (m | 3.55 - 3.93 (m | 0.12 K @ 300 K |
| 10.80 (m | 10.3 - 11.3 (m | 0.12 K @ 300 K |
| 12.00 (m | 11.5 - 12.5 (m | 0.12 K @ 300 K |

| WindSat | WindSat |
| --- | --- |
| Satellite | Coriolis |
| Status (Sept 2006) | Operational – Utilised in the period 2003 to ( 2009 |
| Mission | Demonstration of sea surface wind vector observation by polarimetric passive radiometry. Also sea-surface temperature, precipitation, ice, snow and soil moisture index |
| Instrument type | 5-frequency, 22-channel MW radiometer; three channels with full polarimetric capability |
| Scanning technique | Conical: 50-55° zenith angle, swath 1000 km – Scan rate: 31.6 scan/min = 12.5 km/scan |
| Coverage/cycle | Global in 1.5 days |
| Resolution (constant) | Changing with frequency, consistent with antenna diameters of 1.83 m |
| Resources | Mass: 341 kg - Power: 350 W - Data rate: 35 kbps |

| Central frequency (GHz) | Bandwidth (MHz) | Polarisations | Accuracy (NE(T) | IFOV | Pixel |
| --- | --- | --- | --- | --- | --- |
| 6.8 | 125 | V, H | ........ K | 40 x 60 km | 40 x 50 km |
| 10.7 | 300 | V, H, P, M, L, R | ........ K | 25 x 38 km | 20 x 25 km |
| 18.7 | 750 | V, H, P, M, L, R | ........ K | 16 x 27 km | 10 x 25 km |
| 23.8 | 500 | V, H | ........ K | 12 x 20 km | 10 x 12.5 km |
| 37.0 | 2000 | V, H, P, M, L, R | ........ K | 8 x 13 km | 5 x 12.5 km |
| (*) Polarisations: H = horizontal, V = vertical, P = + 45°, M = - 45°, L = left-hand circular, R = right-hand circular |

# Text boxes

LST: 13:30 a

LST: 9:30 d

LST: 5:30 d

LST: 9:30 d

LST: 13:30 a