| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON THE EVOLUTION OF GLOBAL OBSERVING SYSTEMS Sixth Session GENEVA, SWITZERLAND, 14 – 17 JUNE 2011 |  | CBS/OPAG-IOS/ET-EGOS-6/Doc. 8.3.2(10/3) rev. 1 (09.06.2011) _______ ITEM: 8.3.2 Original: ENGLISH |
| --- | --- | --- |

Rolling Review of Requirements and Statements of Guidance

Statements of Guidance (SoGs)

Global Cryosphere Watch (GCW) observing requirements

(Submitted by WMO Secretariat)

SUMMARY AND PURPOSE OF DOCUMENT The document provides information on how the observational requirements for the Global Cryosphere Watch (GCW) are currently taken into account within existing RRR process, and propose how these should be updated, under the new application area “Cryosphere” to address the observational requirements of the GCW not covered as part of existing application areas.

ACTION PROPOSED

The Meeting is invited to consider the information contained in this document when preparing its recommendations.

____________

References:

1. Current versions of the Statements of Guidance

http://www.wmo.int/pages/prog/sat/RRR-and-SOG.html

2.	IGOS, 2007. Integrated Global Observing Strategy Cryosphere Theme Report - For the Monitoring of our Environment from Space and from Earth. Geneva: World Meteorological Organization. WMO/TD-No. 1405. 100 pp.

(http://igos-cryosphere.org/docs/cryos_theme_report.pdf)

Appendix:

A.	Summary of Requirements for Cryosphere Variables Currently Included in the RRR

B.	IGOS Cryosphere Theme Report “CryOS”: Observational Capabilities and Requirements

C.	Satellite Missions in Support of Cryosphere Theme

DISCUSSION

Statements of Guidance (SoGs)

Global Cryosphere Watch (GCW) observing requirements

1. 	A complete set of observing requirements for the Global Cryosphere Watch (GCW) is currently not included in the Rolling Review of Requirements Data Base. A list, compiled from the current on-line RRR DB, of the cryospheric variables and their related application area(s) is given in Appendix A. The requirements for many of the applications listed in the WMO RRR DB likely extend back over a decade.

2.	An Integrated Global Observing Strategy (IGOS) Cryosphere Theme (“CryOS”) report was prepared and published by WMO in 2007. This document created a framework for improved coordination of cryospheric observations conducted by research, long-term scientific monitoring, and operational programmes, and to generate the data and information needed for both operational services and research. It was based on community input through workshops in North America, Asia and Europe and involving over 80 scientists. It was prepared under the auspices of WCRP/CliC and ICSU/SCAR as an IPY contribution to the IPY project on State and Fate of the Cryosphere. WMO’s GCW initiative has taken on the responsibility of implementing the CryOS recommendations.

3.	The objective of CryOS was to initiate a process that will ultimately result in a more comprehensive, coordinated, and integrated cryospheric observing system.  The report identified the major applications and societal benefits of cryospheric data, detailed our current measurement capabilities and requirements, and hence the shortcomings of the current observational systems, made recommendations in three timeframes on how to close those gaps, and presented an implementation plan to enhance the current systems so that the observational requirements are met. Appendix B provides the observational capabilities and requirements developed for the IGOS Cryosphere Theme report. Appendix C lists the satellite missions that support the Cryosphere Theme. GCW has identified the development of a comprehensive set of requirements as an important task. Its implementation strategy specifically states that it will meet evolving cryospheric observing requirements of WMO Members, partners, and the scientific community by making CryOS a living document and contributing to the WMO Rolling Review of Requirements (RRR) process.

4.	Appendix A lists the key cryospheric variables based on the CryOS report and then identifies the associated RRR application area(s) as identified in the current RRR online DB. It has to be noted that some cryospheric variables are required by a variety of applications but often with different requirements. Many others have not been identified in the RRR process. For example, lake and river ice are not considered while others have limited consideration, usually just referring to extent or cover of the variable rather than more detailed physical properties. These requirements should be expanded, merged (where appropriate), and updated in response to the IGOS Cryosphere Theme report recommendations, which form an integral part of the WMO GCW Implementation Strategy that was approved by Cg-XVI.

5.	There is a need to rationalize the CryOS requirements with those currently available in the WMO RRR DB. It is recommended that the WMO GCW (project office) takes on this task, including preparation of a draft Statement of Guidance for a new application area called “Cryosphere”. This new application area would allow all requirements to be harmonized, compiled together and inserted into the WMO RRR DB. It is recognized that there will be different requirements by different application areas. Having these compiled together would allow rationalization of requirements, as appropriate, while strengthening the guidance and rationale for improving cryospheric observing systems and developing new ones. It is recommended that existing applications would still include reference to the need for cryospheric observations which could be cross-referenced to the “cryosphere application area”. It would also provide guidance that would be useful for past, present and future analyses, including data rescue and re-analyses. The goal would be to have the first draft of a statement of guidance for the Cryosphere application area, including requirements, available for review by the next meeting of ET-EGOS.

Appendix A

Summary of Requirements for Cryosphere Variables Currently Included in the RRR

Snow

Snow Water Equivalent (SWE): AgroMet; Global NWP; HR NWP; Hydrology; S&IA; ACSYS; GEWEX; AOPC

Snow Depth linked to SWE through density (but snow depth is normal measurement for exchange)

Snow Extent(cover): AgroMet; Global NWP; HR NWP; Hydrology; Nowcasting (snowfall??); ACSYS;GEWEX; AOPC; TOPC

Density:

Snowfall:

Albedo: HR NWP;

Snow melting: Hydrology

Solid Precipitation
Amount (index): AgroMet; Global NWP; GEWEX; AOPC

Rate: Global NWP; HR NWP; Nowcasting; synoptic met; AOPC;

Lake and River Ice (not included)
 freeze-up/breakup:

Thickness:

Snow on ice:

Sea Ice
Extent (cover): Global NWP; HR NWP; ACSYS; CLIVAR; Global modelling/WCRP; GOOS; OOPC

Concentration:

Open water:

Type: Global NWP;

Thickness (sea-ice elevation as method to est.): Global NWP; HR NWP; ACSYS; GOOS; OOPC

Motion:

Icebergs: (height and fractional cover) Hydrology, ACSYS;

Snow on ice:

SST: Global NWP; HR NWP; ACSYS;

Type:

Glaciers, Ice Caps, Ice sheets

Mass balance (accumulation/ablation):

Thickness:

Area (cover): TOPC;

Length (geometry): ACSYS, TOPC (topography);

Firn temperature:

Snowline/equilibrium line:

Snow on ice:

Frozen Ground/Permafrost (permafrost)
Soil temperature/thermal state

Active layer thickness

Borehole temperature

Extent: Hydrology; TOPC

Snow cover:

_____________

Appendix B.  IGOS Cryosphere Theme Report “cryos” 	Observational Capabilities and Requirements

The following tables provide current measurement capabilities and observational requirements for each cryosphere domain (snow, sea ice, etc.).  In some cases observational requirements are listed separately for satellite and in situ observations because of different applications. Codes are as follows: C = Current Capability, T = Threshold Requirement (Minimum necessary), O= Objective Requirement (Target), L = Low end of measurement range, U = Unit, H = High end of measurement range, V = Value, cl = climate, op = operational.

Table B.1. Summary of current/planned capabilities and requirements for terrestrial snow parameters.

| Parameter | CT O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Snow Cover | C | 20 | 100 | % | 15-20 | % | 1 | km |  | day | e.g. MODIS |
|  | T | 0 | 100 | % | 10 | % | 0.5 | km | 1 | day | Hydromet |
|  | O | 0 | 100 | % | 5 | % | 0.1 | km | 12 | hr |  |
| Snow Water Equivalent, satellite (Shallow) | C | 0 | 0.2 | m | 2-10 | cm | 25 | km | 1 | day | e.g. AMSR-E |
|  | T | 0 | 0.3 | m | 3 | cm | 0.5 | km | 6 | day | Hydromet |
|  | O | 0 | 0.3 | m | 2 | cm | 0.1 | km | 12 | hr |  |
| Snow Water Equivalent, satellite (Deep) | C | None | --- | --- | --- | --- | --- | --- | --- | --- | Need HF SAR |
|  | T | 0.3 | 3 | m | 10 | % | 0.5 | km | 6 | day | Hydromet |
|  | O | 0.3 | 3 | m | 7 | % | 0.1 | km | 12 | hr |  |
| Snow Water Equivalent, in situ (Shallow) | C | 0 | 3 | m | 1 | cm | 1 | m | 30 | day | Hydromet |
|  | T | 0 | 3 | m | 1 | cm | 1 | m | 7 | day | Hydromet |
|  | O | 0 | 3 | m | 1 | cm | 1 | m | 1 | day |  |
| Snow Depth, satellite (Shallow) | C | 0 | ~0.7 | m | 6-35 | cm | 25 | km | 1 | day | e.g. AMSR-E |
|  | T | 0 | 1 | m | 10 | cm | 0.5 | km | 6 | day | Hydromet |
|  | O | 0 | 1 | m | 6 | cm | 0.1 | km | 1 | hr | Transportation |
| Snow Depth, satellite (Deep) | C | None | --- | --- | --- | --- | --- | --- | --- | --- | Need HF SAR |
|  | T | 1 | 10 | m | 10 | % | 0.5 | km | 6 | day | Hydromet |
|  | O | 1 | 10 | m | 6 | % | 0.1 | km | 1 | hr | Transportation |
| Snow Depth, in situ | C | 0 | 10 | m | 1 | cm | 1 | m | 1 | day | Hydromet |
|  | T | 0 | 10 | m | 1 | cm | 1 | m | 6 | hr | Hydromet |
|  | O | 0 | 10 | m | 1 | cm | 1 | m | 1 | hr |  |

Table B.2. Summary of current/planned capabilities and requirements for sea ice parameters.

| Parameter | C T O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Extent/Edge | Ccl Cop | NA | NA | km | 15 0.1 | km | 15 0.1 | km | 1 3 | day | AMSR VIR, SAR, AUV |
|  | T | NA | NA | km | 10 | km | 10 | km | 1 | day | CMIS |
|  | Ocl Oop | NA | NA | km | 5 0.1 | km | 1-5 0.1 | km | 1 1 | day | CMIS, SAR, AUV |
| Concentration | Ccl Cop | 15 0 | 100 | % | 5-20 | % | 15 | km | 1 | day | AMSR, VIR, SAR, AUV |
|  | T | 0 | 100 | % | <10 | % | 15 | km | 1 | day |  |
|  | O | 0 | 100 | % | <5 | % | 10 | km | 1 | day | CMIS, SAR, AUV |
| Leads/polynyas | Ccl Cop | 0 0 | 100 indet. | % km2 | 5-20 0.1 | % km2 | 15 0.5 | km | 1 1 | day week | AMSR, SAR, AUV |
|  | T |  |  |  |  |  |  |  |  |  |  |
|  | Ocl Oop | 0 0 | 100 indet. | % km2 | 5 0.1 | % km2 | 10 0.1 | km | 1 1 | day | MODIS, PM, AUV |
| Stage of Development (Ice Age) | Ccl Cop | 0 | 100 | % | 5-20 | % | 15 | km | 1 | day | SSMI, VIR, Scat, SAR |
|  | T | 0 | 100 | % | <10 | % | 15 | km | 1 | day | SAR |
|  | Ocl Oop | 0 | 100 | % | <5 | % | 10 | km | 1 | day | SAR |
| Motion1 | Ccl Cop | 0 | 100 | km day-1 | 5 0.5 | km day-1 | 25 1 | km | 1 3 | day | AMSR2 SAR2, buoys |
|  | T | 0 | 100 | km day-1 | 3 | km day-1 | 25 | km | 1 | day | SAR |
|  | Ocl Oop | 0 | 100 | km day-1 | 1 0.5 | km day-1 | 1 0.1 | km | 1 1 | day | More freq. SAR, improved MIZ performance |
| Thickness | Ccl Cop | 0 | 10 | m | 0.5 10 | m % | 0.5 0.5 | km | 0.5 1 | year week | ICESat op ice charts, mass balance buoys, AUV |
|  | T | 0 | 10 | m |  |  |  |  |  |  |  |
|  | Ocl Oop | 0 | 10 | m | 0.1 10 | m % | 25 0.5 | km | 1 1 | mnth day | sat. altimeter, mass balance buoys, AUV |
| Ridge Height, Concentration | Ccl Cop | 0 | 10 | m | - | m |  |  |  |  | SAR |
|  | T | 0 | 10 | m | 2 | m |  |  |  |  | SAR |
|  | Ocl Oop | 0 | 10 | m | 1 | m |  |  |  |  | SAR |
| Snow Depth on Ice | Ccl | 0 | 100 | cm | 10-20 | cm | 15 | km | 1 | day | AMSR |
|  | T | 0 | 100 | cm | 5 | cm | 10 | km | 1 | day | CMIS |
|  | Ocl | 0 | 100 | cm | 2 | cm | 5 | km | 1 | day | CMIS |
| Melt Onset, Duration of Melt | Ccl | 1 | 365 | doy | 4 | day | 15 | km | 1 | day | AMSR, Scat |
|  | T | 1 | 365 | doy | 2 | day | 15 | km | 1 | day |  |
|  | Ocl | 1 | 365 | doy | 1 | day | 10 | km | 1 | day |  |
| Surface Characteristics (albedo, meltpond, dust, snow properties, temperature)3 | Ccl | 0 | 100 | % | 10 | % | 1 | km | 1 | day | MODIS, but not currently produced, AUV |
|  | T | 0 | 100 | % | 10 | % | 1 | km | 1 | day |  |
|  | Ocl | 0 | 100 | % | 1-5 | % | 0.5 | km | 1 | day |  |
| Volume/Mass Flux | Ccl |  |  |  |  |  |  |  |  |  | Derived from motion, thickness, concentration |
|  | T |  |  |  |  |  |  |  |  |  |  |
|  | Ocl | 0 | indet. | km3 day-1 | 1 | km3 day-1 | 25 | km | 1 | day |  |

1Velocity measurement, range and errors are for each orthogonal component. 2Antarctic measurements are less robust than for the Arctic primarily due to the influence of weather. 3Range and errors for albedo and meltpond concentration.  Other parameters listed not yet regularly observed.  There is overlap of these products with products in snow chapter and albedo/temperature chapter.

Table B.3. Summary of current/planned capabilities and requirements for lake and river ice parameters.

| Parameter | CT O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Concentration | C |  |  | % |  | % | 100-1 | m- km | 1 | w | Radarsat, AVHRR, OLS |
|  | T | 0 | 100 | % | 10 | % | 100 | m | 1 | d | e.g. AMSR-E, SAR, optical |
|  | O | 0 | 100 | % | 5 | % | 30 | m | 1 | d | SAR, optical |
| Ice areal extent (and open water area)1 | C |  |  | km2 |  | % | 250-500 | m | 1 | d | MODIS |
|  | T |  |  | km2 | 10 | % | 100 | m | 1 | d | SAR, optical |
|  | O |  |  | km2 | 5 | % | 30 | m | 1 | d | SAR, optical |
| Freeze-up and break-up date /ice cover duration2 | C |  |  | JD/d | 1 | d | point |  |  | a | In situ obs. |
|  | T |  |  | JD/d | 2 | d | 100 | m | 1 | a | SAR, optical, |
|  | O |  |  | JD/d | 1 | d | 30 | m | 1 | a |  |
| Thickness | C | 0 | 5 | m | 2 | cm | point |  | 1-2 | w | In situ obs. |
|  | T | 0 | 3 | m | 5 | cm | 100 | m | 1 | w | SAR, passive mw |
|  | O | 0 | 5 | m | 2 | cm | 10 | m | 1 | d |  |
| Snow depth on ice | C | 0 | 1 | m | 2 | cm | point |  | 1-2 | w | In situ obs. |
|  | T | 0 | .8 | m | 5 | cm | 100 | m | 1 | w | SAR, passive mw |
|  | O | 0 | 1 | m | 2 | cm | 10 | m | 1 | d |  |
| Areal extent of floating and grounded ice1 | C |  |  | km2 |  | % | 10 | m | 1 | w | SAR |
|  | T |  |  | km2 | 10 | % | 5 | m | 1 | w | SAR |
|  | O |  |  | km2 | 5 | % | 3 | m | 1 | w |  |
| River ice jams and dams1 | C |  |  | km2 |  | % | 0.5 | m | 1 | h | Aerial survey |
|  | T |  |  | km2 | 10 | % | 10 | m | 1 | d | SAR, optical |
|  | O |  |  | km2 | 5 | % | 3 | m | 1 | d |  |
| Flooding extent caused by jams and dams1 | C |  |  | km2 |  | % | 10 | m | 1 | w | e.g. Radarsat |
|  | T |  |  | km2 | 10 | % | 5 | m | 1 | d | SAR, optical |
|  | O |  |  | km2 | 5 | % | 3 | m | 1 | d |  |
| River icings (aufeis) 1 | C |  |  | km2 |  | % | 15-30 | m | 2 | m | e.g. Landsat, ASTER, SAR |
|  | T |  |  | km2 | 10 | % | 10 | m | 1 | w | SAR, optical |
|  | O |  |  | km2 | 5 | % | 3 | m | 1 | w |  |

1 The measurement range is not specified because the size (km2) of the parameter can be very variable.  2 Freeze and break-up dates are expressed in Julian Days while ice duration is in days. The measurement range is not specified because the dates and number of days can be highly variable and some lakes at higher latitudes can have a perennially ice cover.

Table B.4. Summary of current/planned capabilities and requirements for ice sheet parameters.

| Parameter | CT O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Ice margin | C | 0 | 1000 | km | 2 | km | 2 | km | 5 | yr | AVHRR |
|  | T | 0 | 1000 | Km | 2 | Km | 2 | Km | 5 | yr | Hi res optical and SAR |
|  | O | 0 | 1000 | km | 25 | m | 25 | m | 1 | yr |  |
| Grounding Line | C | 0 | 1000 | km | 1 | km | 1 | km | 5 | yr |  |
|  | T | 0 | 1000 | Km | 1 | Km | 1 | Km | 5 | yr | Hi Res optical/InSAR |
|  | O | 0 | 1000 | Km | 100 | m | 1 | km | 1 | yr |  |
| Surface Accumulation | C | 0 | 50 | cm water eq/yr | 1 | cm water eq./yr | 25 | km | 1 | yr | Passive microwave, P/E/ models and in situ |
|  | T | 0 | 50 | Cm water eq/yr | 1 | Cm water eq/yr | 25 | km | 1 | yr | Active/Passive Microwave |
|  | O | 0 | 50 | Cm water eq/yr | 1 | Cm water eq/yr | 1 | km | 6 | mo |  |
| Basal Melt Magnitude | C | 0 | 20 | m/yr | 100 | cm/yr | 10 | km | 1 | yr | Inferred |
|  | T | 0 | 20 | m/yr | 100 | Cm/yr | 10 | km | 1 | yr |  |
|  | O | 0 | 20 | m/yr | 10 | Cm/yr | 1 | km | 6 | mo |  |
| Basal Melt Distribution | C | 0 | 104 | km2 | 1 | km | 50 | km | 1 | yr |  |
|  | T | 0 | 104 | km2 | 1 | km | 50 | km | 1 | yr | UHF/VHF radar |
|  | O | 0 | 104 | km2 | 1 | km | 10 | km | 1 | yr |  |
| Surface Elevation | C | 0 | 4 | km | 50 | cm | 1 | km | 1 | yr |  |
|  | T | 0 | 4 | km | 50 | cm | 1 | km | 1 | yr | Radar and laser altimeter |
|  | O | 0 | 4 | km | 50 | cm | 1 | km | 1 | yr |  |
| Surface Elevation Change | C | 0 | 5 | m/yr | 10 | cm/yr | 5 | km | 1 | yr |  |
|  | T | 0 | 5 | m/yr | 10 | cm/yr | 5 | km | 1 | yr | Radar and laser altimeter |
|  | O | 0 | 5 | m/yr | 10 | Cm/yr | 1 | km | 6 | Mo |  |
| Snow/Firn Density | C | 0 | 910 | kg/m3 | 50 | kg/m3 | 100 | km | 5 | yr |  |
|  | T | 0 | 910 | kg/m3 | 50 | kg/m3 | 100 | km | 5 | yr | In situ obs |
|  | O | 0 | 910 | kg/m3 | 10 | kg/m3 | 100 | km | 5 | yr |  |
| Snow Grain Size and Shape | C | 0.1 | 3 | mm | 0.25 | mm | 100 | km | 5 | yr | Optical and in situ |
|  | T | 0.1 | 3 | mm | 0.25 | mm | 100 | km | 5 | yr |  |
|  | O | 0.1 | 3 | mm | 0.25 | mm | 100 | km | 5 | yr |  |
| Surface Temperature | C | 173 | 278 | oK | 1 | oK | 10 | km | 1 | yr | In Situ |
|  | T | 173 | 278 | oK | 1 | oK | 10 | km | 1 | yr | Annual average THIR |
|  | O | 173 | 278 | oK | 1 | oK | 10 | km | 1 | mo |  |
| Internal Temperature | C | 173 | 273 | oK | 0.1 | oK | 500 | km | 5 | yr |  |
|  | T | 173 | 273 | oK | 0.1 | oK | 500 | km | 5 | yr | Borehole temp. |
|  | O | 173 | 273 | oK | 0.1 | oK | 500 | km | 5 | yr |  |
| Gravity Field | C |  |  |  | 2 | mgal | 1 | km | 1 | yr |  |
|  | T |  |  |  | 2 | mgal | 1 | km | 1 | yr | Airborne Gravity |
|  | O |  |  |  | 0.5 | mgal | 1 | km | 1 | yr |  |
| Surface Velocity Field | C | 0 | 15 | Km/yr | 10 | m/yr | 1 | km | 6 | mo |  |
|  | T | 0 | 15 | Km/yr | 10 | m/yr | 1 | km | 6 | mo | GPS and InSAR |
|  | O | 0 | 15 | Km/yr | 10 | m/yr | 1 | km | 6 | mo |  |
| Vertical Velocity Variation | C | 0 | 1 | m/yr | 10 | Cm/yr | 100 | km | 5 | yr |  |
|  | T | 0 | 1 | m/yr | 10 | Cm/yr | 100 | km | 5 | yr | Vertical strain gauges |
|  | O | 0 | 1 | m/yr | 10 | Cm/yr | 100 | km | 5 | yr |  |
| Ice thickness | C | .010 | 4 | km | 20 | m | 50 | km | 10 | yr | Ice sheet wide |
|  | T | .010 | 4 | km | 20 | m | 50 | km | 10 | yr | VHF and UHF Radar |
|  | O | .010 | 4 | km | 20 | m | 1 | km | 10 | yr |  |
| Internal Layer Depth | C | .010 | 4 | km | 20 | m | 50 | km | 10 | yr |  |
|  | T | .010 | 4 | km | 20 | m | 50 | km | 10 | yr | VHF and UHF radar |
|  | O | .010 | 4 | km | 20 | m | 1 | km | 10 | yr |  |
| Iceberg calving rate | C | 0 | 30 | Km/yr | 1 | Km/yr | 1 | km | 1 | yr | Inferred |
|  | T | 0 | 30 | Km/yr | 1 | Km/yr | 1 | km | 1 | yr |  |
|  | O | 0 | 30 | Km/yr | 1 | Km/yr | 1 | km | 6 | mo |  |
| Changes in ice sheet morphology (crevasses, shear margins) | C | 0 | 100 | m | 100 | m | 1 | km | 1 | yr |  |
|  | T | 0 | 100 | m | 100 | m | 1 | km | 1 | yr | Hi Res optical and InSAR |
|  | O | 0 | 100 | m | 100 | m | 1 | km | 1 | yr |  |
| Surface melt extent | C | 0 | 20 | 106sq km | 2500 | Sq km | 25 | km | 1 | day |  |
|  | T | 0 | 20 | 106sq km | 2500 | Sq km | 25 | km | 1 | day | Passive and active microwave |
|  | O | 0 | 20 | 106sq km | 400 | Sq km | 10 | km | 1 | day |  |
| Surface melt duration | C | 0 | 100 | Melt days | 1 | Melt day | 25 | km | 1 | day |  |
|  | T | 0 | 100 | Melt days | 1 | Melt day | 25 | km | 1 | day | Passive and active microwave |
|  | O | 0 | 100 | Melt days | 1 | Melt day | 1 | km | 1 | day |  |
| Ice Sheet Mass Change | C | 0 | 200 | Km3/yr | 50 | Km3/yr | 500 | km | 1 | yr | Flux approach not included in this category |
|  | T | 0 | 200 | Km3/yr | 50 | Km3/yr | 500 | km | 1 | yr | Satellite Gravity |
|  | O | 0 | 200 | Km3/yr | 10 | Km3/yr | 500 | km | 1 | yr |  |
| Geothermal Heat Flux | C | 0 | 1 | w/m2 | 1 | w/m2 | 1000 | km | 10 | yr |  |
|  | T | 0 | 1 | w/m2 | 1 | w/m2 | 1000 | km | 10 | yr | TBD approach |
|  | O | 0 | 1 | w/m2 | 1 | w/m2 | 100 | km | 10 | yr |  |

Table B.5. Summary of current/planned capabilities and requirements for iceberg parameters.

| Parameter | C T O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Limit of iceberg area | C | NA | NA | km | 10 | km | 10 | km | 1 | day | SAR, SLAR airborne reconnaissance |
|  | T | NA | NA | km | 10 | km | 10 | km | 2 | hour | same |
|  | O | NA | NA | km | 10 | km | 10 | km | 2 | hour | same |
| Concentration of icebergs | C | 0 | 100 | % | 10 | % | 1 | deg | 1 | day | same |
|  | T | 0 | 100 | % | <10 | % | 1 | deg | 1 | day | same |
|  | O | 0 | 100 | % | <5 | % | 1 | deg | 1 | day | same |
| Iceberg position | C | NA | NA |  | 10 | % | 1 | km | 1 | day | same |
|  | T | NA | NA |  | <10 | % | 1 | km | 1 | day | same |
|  | O | NA | NA |  | <5 | % | 1 | km | 2 | hour | same |
| Iceberg Size | C | 0.01 | 100 | km | 30 | % | .01 | km | 1 | day | same |
|  | T | .001 | 100 | km | 30 | % | .01 | km | 1 | day | same |
|  | O | .001 | 100 | km | 30 | % | .001 | km | 1 | hour | same |
| Iceberg Draft | C | 1 | 1000 | m | 30 | % | 10 | m | 1 | day | shipborne, modelling |
|  | T | 1 | 1000 | m | 30 | % | 1 | m | 1 | day | altimeter (for large bergs) |
|  | O | 1 | 1000 | m | 30 | % | 1 | m | 2 | hour | altimeter |
| Iceberg Mass | C | 0 | NA | kg | 30 | % | 15 | km | 1 | day | shipborne, modelling |
|  | T | 0 | NA | kg | 30 | % | 15 | km | 1 | day | altimeter (for large bergs) |
|  | O | 0 | NA | kg | 30 | % | 10 | km | 2 | hour | altimeter |
| Iceberg Velocity | C | 0 | 30 | km day-1 | 10 | % | 1 | km day-1 | 1 | day | SAR, SLAR, scatterometer, visible/IR |
|  | T | 0 | 30 | km day-1 | 10 | % | 1 | km day-1 | 1 | day | SAR, SLAR, scatterometer, visible/IR |
|  | O | 0 | 30 | km day-1 | 10 | % | 0.5 | km day-1 | 2 | hour | SAR, SLAR, scatterometer, visible/IR |

Table B.6. Summary of current/planned capabilities and requirements for glaciers and ice caps.

| Parameter | CT O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Area | C |  |  |  | 1 | % | 5 | m | 30 | a | airborne |
|  | O |  |  |  | 3 | % | 30 | m | 5 | a | Landsat etc. |
|  | T | 0.01 |  | Km2 | 3 | % | 50 | m | 5 | a | hi res. optical |
|  | O | 0.01 |  | Km2 | 1 | % | 15 | m | 1 | a |  |
| Topography | O |  |  |  |  |  |  |  |  |  | Airborne |
|  | C | 0 | 8500 | m sl. | 5 | m | 100 | m | 5 | a | For models |
|  | T | 0 | 8500 | m sl. | 0.1 | m | 30 | m | 1 | a | Mass balance |
| Velocity | O |  |  |  | 1 | % | point |  | 1 | a | In situ |
|  | C | 0 | 10 | Km/a | 5 | % | 10 | m | 1 | a | InSAR, hi res. optical, etc. |
|  | T | 0 | 10 | Km/a | 1 | % | 20 | m | 1 | m |  |
| Glacier dammed lakes | O |  |  |  | 1 | % | 1 | m | 1 | a | airborne |
|  | C | 0.05 | 10 | Km2 | 3 | % | 50 | m | 1 | m | SAR, hi res. optical |
|  | T | 0.01 | 10 | Km2 | 1 | % | 15 | m | 5 | d |  |
| Facies, snowline | C |  |  |  |  |  | point |  |  |  | In situ |
|  | T |  |  | class | 200 | m | 100 | m | 1 | m | Position of boundary |
|  | O |  |  | class | 30 | m | 30 | m | 10 | d |  |
| Accumulation | C |  |  |  | 5 | % | point |  |  |  | In situ |
|  | T | 0.05 | 8 | m | 10 | % | 500 | m | 1 | a | Ku-, X-SAR |
|  | O | 0.10 | 5 | m | 5 | % | 100 | m | 1 | m |  |
| Mass balance | C |  |  |  | 0.10 | m | point |  |  |  | In situ |
|  | T | 0 | (5 | m | 0.20 | m | 500 | m | 1 | m | process model & SAR |
|  | O | 0 | (5 | m | 0.05 | m | 100 | m | 1 | a |  |
| Ice thickness | C | 0 | 200 | m | 2-5 | m | 100 | M | 30 | Yr | In situ, airborne |

Table B.7. Summary of current/planned capabilities and requirements for snow/ice temperature and albedo.

| Parameter | CT O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Snow/ice Albedo (Broadband) | C | 30 | 100 | % | 7 | % | 1 | km | 1 | day | e.g. MODIS |
|  | T | 0 | 100 | % | 1 | % | 8 | km | 1 | hr | Hydromet |
|  | O | 0 | 100 | % | 0.5 | % | 5 | km | 30 | min |  |
| Snow/ice Surface Temperature | C | 190 | 290 | K | 2-3 | K | 1 | Km | 100 | min |  |
|  | T | 200 | 275 | K | 1 | K | 1 | km | 1 | hr | Hydromet |
|  | O | 200 | 275 | K | 0.1 | K | 0.1 | km | 30 | min |  |

Table B.8. Summary of current/planned capabilities and requirements for terrestrial permafrost and seasonally frozen ground parameters.

| Parameter | C T O | Measurement Range | Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  | L | H | U | V | U | Spatial | Temporal |  |
|  |  |  |  |  |  |  | V | U | V | U |  |
| Permafrost* |  |  |  |  |  |  |  |  |  |  |  |
| Permafrost thermal state | C | -20 | 0 | 0C | 0.05 | K | Vertical profile | 1 | a | Key parameter of the GTN-P; in situ measurements; (annual upper 20-100 m; deeper 5 a) |
|  | T | -20 | 0 | 0C | 0.01 | K |  | 1 | a |  |
|  | O | -20 | 0 | 0C | 0.01 | K |  | 1 | a |  |
| Permafrost thickness | C | 0 | 1600 | m | 1 | m | Point | 10-100 | a | Measured or interpolated from temperature profiles; inferred from geophysical logs or surface surveys; modeled parameter |
|  | T | 0 | 1600 | m | 0.5 | m |  | 10 | a |  |
|  | O | 0 | 1600 | m | 0.5 | m |  | 10 | a |  |
| Permafrost distribution (continental) | C | 0 | 100 | % |  | % | 10 | km | 10 | a | inferred from ground temperatures, photo terrain interpretation, geophysics |
|  | T | 0 | 100 | % | 2 | % | 1 | km | 10 | a |  |
|  | O | 0 | 100 | % | 1 | % | 1 | km | 1 | a |  |
| Permafrost distribution (mountain) | C | 0 | 100 | % |  | % | 25 | m | 1 | a | Distributed models, based on DEM, calibrated with BTS; distribution based on elevation (m) |
|  | T | 0 | 100 | % | 2 | % | 25 | m | 1 | a |  |
|  | O | 0 | 100 | % | 1 | % | 25 | m | 1 | a |  |
| Downslope velocity of creeping permafrost | C | 0.01 | 15 | m / yr | 1 | cm | Point | 1 | a | Survey transects, repeat high-resolution imagery, radar, InSAR |
|  | T | 0.01 | 15 | m / yr | 1 | cm | 10 | m | 1 | a | Same; InSAR |
|  | O | 0.01 | 15 | m / yr | 1 | cm | 10 | m | 1 | a | Same; InSAR |
| Annual surface elevation change | C | 0 | 1 | m | 1 | cm | Point | 1 | a | In situ survey transects, LIDAR maps, InSAR |
|  | T | 0 | 1 | m | 1 | cm | 10 | m | 1 | a |  |
|  | O | 0 | 1 | m | 1 | cm | 1 | m | 1 | a |  |
| Ground ice volume | C | 0 | 100 | Vol % | 5-10 | Vol % | Point | One time | In situ measurements (sampling during borehole drilling) |
|  | T | 0 | 100 | Vol % | 5 | Vol % | 1 | m |  | Geophysical investigations |
|  | O | 0 | 100 | Vol % | 5 | Vol % | 0.1 | m |  |  |
| Active Layer* |  |  |  |  |  |  |  |  |  |  | Areas underlain by permafrost |
| Active layer depth | C | 0 | 5 | m | 1 | cm | Point | 1 | a | In situ measurements (maximum value at end of summer, key GTN-P parameter) |
|  | T | 0 | 5 | m | 1 | cm |  | 7 | d |  |
|  | O | 0 | 5 | m | 1 | cm |  | 7 | d |  |
| Soil temperature** | C | -60 | 35 | 0C | 0.1 | K | Vertical profile | 1 | d | 10 cm interval to 1.2m on data recorder; GTOS TEM parameter |
|  | T | -60 | 35 | 0C | 0.05 | K |  | 6 | h |  |
|  | O | -60 | 35 | 0C | 0.05 | K |  | 6 | h |  |
| Surface temperature | C | -70 | 45 | 0C | 1 | K | 1 | km | 1 | d | MODIS |
|  | T | -70 | 45 | 0C | 1 | K | 100 | m | 1 | d |  |
|  | O | -70 | 45 | 0C | 1 | K | 10 | m | 0.5 | d |  |
| Soil moisture** | C | 0 |  | Vol % | 1-5 | Vol % | Point | 1 | d | Monitored continuously at some locations, or based on sampling during drilling or soil pits; GTOS TEM parameter |
|  | T | 0 |  | Vol % | 1-5 | Vol % | 1 | m |  |  | Same; SAR |
|  | O | 0 |  | Vol % | 1-5 | Vol % | 0.1 | m |  |  | Same; SAR |
| Duration of thaw | C | 0 | 365 | days | 14 | d | Point | 1 | d | Computed from weather records and inferred or measured from soil temperatures; sequential microwave |
|  | T | 0 | 365 | days | 7 | d | 1 | km |  |  |  |
|  | O | 0 | 365 | days | 7 | d | 100 | m |  |  |  |
| Seasonal frost heave / thaw subsidence | C | 0 | 100 | cm | 1 | cm | Point | 0.5 | a | In situ survey transects, LIDAR maps, InSAR |
|  | T | 0 | 100 | cm | 1 | cm | 10 | cm |  |  |  |
|  | O | 0 | 100 | cm | 1 | cm | 1 | cm |  |  |  |
| Seasonally Frozen Ground* |  |  |  |  |  |  |  |  |  |  | Areas not underlain by permafrost and beyond limits of permafrost |
| Onset of seasonal freezing | C | 0 | 365 | days | 14 | d | Point | 14 | d | determined from interpolation of soil temperature profiles or frost tubes; passive microwave |
|  | T | 0 | 365 | days | 7 | d | 1 | km | 7 | d |  |
|  | O | 0 | 365 | days | 7 | d | 100 | m | 7 | d |  |
| Depth of seasonal freezing | C | 0 | 4 | m | 1 | cm | Point | 1 | a | Determined from interpolation of soil temperature profiles or frost tubes; passive microwave |
|  | T | 0 | 4 | m | 1 | cm |  | 7 | d |  |
|  | O | 0 | 4 | m | 1 | cm |  | 7 | d |  |
| Duration of freeze | C | 0 | 365 | days | 14 | d | Point | 1 | d | Computed from weather records and inferred or measured from soil temperatures; sequential microwave |
|  | T | 0 | 365 | days | 7 | d | 1 | km |  |  |  |
|  | O | 0 | 365 | days | 7 | d | 100 | m |  |  |  |
| Distribution of seasonal freezing | C | 0 | 100 | % |  | % | 25 | km | 5 | d | Microwave (passive and active) sensors at regional scale; sequential microwave |
|  | T | 0 | 100 | % |  | % | 10 | km |  |  |  |
|  | O | 0 | 100 | % |  | % | 1 | km |  |  |  |
| Coastal Dynamics |  |  |  |  |  |  |  |  |  |  |  |
| Coastal retreat | C | 0 | 30 | m / yr | 0.5 | m / yr | Point | 1 | a | Ground surveys, DGPS, aerial photos, high-resolution satellite imagery, InSAR |
|  | T | 0 | 30 | m / yr | 0.25 | m / yr | 0.25 | m |  |  |  |
|  | O | 0 | 30 | m / yr | 0.25 | m / yr | 0.25 | m |  |  |  |
| Isostatic vertical motion | C | 0 | 15 | cm / yr | 1 | mm | Point | 1 | a | DGPS |
|  | T | 0 | 15 | cm / yr | 1 | mm | 1 | km |  |  | DGPS, LIDAR, Laser Altimetry, InSAR |
|  | O | 0 | 15 | cm / yr | 1 | mm | 1 | km |  |  |  |
| Wind speed and direction | C | 0 |  | m / s | 0.1 | m / s | Point | 1 | min | Anemometer |
|  | T | 0 |  | m / s | 0.1 | m / s |  |  |  |  |
|  | O | 0 |  | m / s | 0.1 | m / s |  |  |  |  |
| Storm surge | C | NA | NA | NA | NA | NA | NA |  | NA |  | NA |
|  | T |  |  |  |  |  | 25 | m | 1 | d | Time-lapse camera, tide gauge, Opportunistic SAR |
|  | O |  |  |  |  |  | 25 | m | 1 | h |  |
| Sediment transport | C | NA | NA | NA | NA | NA | NA |  | NA |  | NA |
|  | T |  |  |  |  |  | 250 | m | 7 | d | MODIS |
|  | O |  |  |  |  |  | 250 | m | 1 | d |  |
| Sea ice extent | see Sea Ice table |  |  |  |  |  |  |  |  |
| Ice scouring depth | C |  |  | cm | 10 | cm |  | m |  |  | Multi-beam sonar |
|  | T |  |  |  | 10 | cm |  | m |  |  |  |
|  | O |  |  |  | 10 | cm |  | m |  |  |  |
| Ice scouring area | C | 0 | 100 | % | 20 | % | 10 | m |  |  | Multi-beam sonar |
|  | T | 0 | 100 | % | 10 | % | 1 | m |  |  |  |
|  | O | 0 | 100 | % | 10 | % | 1 | m |  |  |  |
| Subsea permafrost distribution | C | 0 | 100 | % |  | % | 10 | km | 10 | a | Boreholes, multibeam sonar, shallow seismic |
|  | T | 0 | 100 | % |  | % | 1 | km | 10 | a |  |
|  | O | 0 | 100 | % |  | % | 1 | km | 1 | a |  |
| Subsea permafrost thickness | C | 0 | 500 | m | 1 | m | Point | 10-100 | a | Boreholes, multibeam sonar, shallow seismic |
|  | T | 0 | 500 | m | 1 | m |  | 10 | a |  |
|  | O | 0 | 500 | m | 1 | m |  | 10 | a |  |

* includes all aspects of snow cover.

** applies also to seasonally frozen ground

Table B.9. Summary of current/planned capabilities and requirements for snowfall parameters. (Adopted from http://www.nosa.noaa.gov/requirements.html)

| Parameter | CT O | Measurement Range | Measurement Accuracy | Resolution | Comment / Principal Driver |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Spatial | Temporal |  |
|  |  | L | H | U | V | U | V | U | V | U |  |
| Snowfall amount | C | 0 | 100 | mm | 1 | mm | 1 | km | 1 | day | MODIS/SSMI |
|  | T | 0 | 100 | mm | 1 | mm | 0.5 | km | 1 | day | Hydromet |
|  | O | 0 | 100 | mm | 1 | mm | 0.1 | km | 12 | hr |  |
| Precip/Snowfall rate | C | 0 | 100 | mm/hr | 2-10 | cm | 25 | km | 1 | day | AMSR-E/TRMM |
|  | T | 0 | 100 | mm/hr | 3 | cm | 0.5 | km | 1 | day | Hydromet Transportation |
|  | O | 0 | 100 | mm/hr | 2 | cm | 0.1 | km | 12 | hr |  |
| Precipitation type | C | N.A. | --- | --- | --- | --- | --- | --- | --- | --- | Need HF SAR |
|  | T | 0.3 | 3 |  | 10 | % | 0.5 | km | 1 | day | Hydromet |
|  | O | 0.3 | 3 |  | 7 | % | 0.1 | km | 12 | hr |  |
| Snow particle size | C | 0 | ~0.7 |  | 6-35 |  | 25 | km | 1 | day | e.g. AMSR-E |
|  | T | 0 | 1 |  | 10 |  | 0.5 | km | 1 | day | Hydromet |
|  | O | 0 | 1 |  | 6 |  | 0.1 | km | 1 | hr |  |

_____________

Appendix C.  Satellite Missions in Support of the Cryosphere Theme

Figure C.1 gives a timeline for current and future satellite sensors that can be used to estimate properties of the cryosphere.

_____________