| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON THE EVOLUTION OF GLOBAL OBSERVING SYSTEMS Sixth Session GENEVA, SWITZERLAND, 14 – 17 JUNE 2011 |  | CBS/OPAG-IOS/ET-EGOS-6/Doc. 9 (13.05.2011) _______ ITEM: 9 Original: ENGLISH |
| --- | --- | --- |

Observing System Studies

(Submitted by  Erik Andersson (ECMWF))

SUMMARY AND PURPOSE OF DOCUMENT The document provides for a review of the current activities with Observing System Experiments (OSEs) and Observing System Simulation Experiments (OSSEs) with emphasis on the design of the future of the GOS.

ACTION PROPOSED

The meeting is invited to note the information contained in this document for discussion under the appropriate agenda items.

____________

References:	n/a

Appendix A:	Proposed topics for NWP impact studies relevant to the evolution of global observing systems

Appendix B:	Workshop announcement (Draft)

Appendix C:	ECMWF study on the impact of future developments of the space-based observing system on Numerical Weather Prediction

Appendix D:	ECMWF study to quantify the interaction between terrestrial and space-based observing systems on Numerical Weather Prediction skill

9.1	UPDATE ON RECENT OSEs/OSSEs

      - Adjoint-based sensitivity to forecast error: The results obtained with these newly-developed tools are receiving significant attention. Bar charts showing the relative importance of each component of the GOS have been produced based on the observation sensitivity with respect to (typically) 24-hour forecast error measured in terms of vertically integrated total energy. Specific experiments have been conducted to compare the impacts of observations in three different NWP forecasting systems, and to assess the three different implementations of these tools and their usefulness (Gelaro et al., AMS 2011). The participating NWP centers were the NASA Global Modeling and Assimilation Office, the Naval Research Laboratory, and Environment Canada. With the adjoint technique, the impacts of all observations are computed simultaneously from one single execution of the system, for one chosen measure of forecast error, allowing results to be easily aggregated according to data type, location, satellite sounding channel, or other attributes. The technique is highly economical as compared with running multiple data denial OSEs, but its accuracy is generally limited to forecast ranges of 1-3 days.

      - Despite differences in the assimilation algorithms and forecast models, the impacts of the major observation types were found to be similar in each of the three forecasting systems in a global sense. However, regional details and other aspects of the results can differ substantially. Large forecast error reductions are provided by satellite radiances, geostationary satellite winds, radiosondes and aircraft. Other observation types provide smaller impacts individually, but their combined impact is also significant.

      - In all three NWP systems only a small majority (less than 55%) of the total number of observations assimilated actually improves the forecast, and most of the overall improvement comes from a large number of observations that have relatively small individual impacts. This is a consequence of the fact that the observation error often is greater than the background error that the assimilation system corrects.

      - Ensemble-based sensitivity to forecast error: An ensemble-based estimation method (Liu and Kalnay 2008), using the local ensemble transform Kalman filter (LETKF), has been applied to a global NWP model to assess the observation impact of simulated radiosondes, cloud drift wind, and satellite retrieved temperature and humidity profiles (Hong Li et al., AMS 2011). With this technique it is not necessary to add or remove observations from the assimilation as is done in the traditional OSEs. Results show that the procedure can successfully evaluate the forecast impact of observations. The impact values can be grouped and summed by various subsets of observations that may be of interest (as with adjoint sensitivity methods, above). It was found that the total observation impact in the N Hemisphere is bigger than that in the S Hemisphere. The largest impact in the N Hemisphere is produced by radiosondes, whereas it is produced by satellite retrieved profiles in the S Hemisphere. Cloud drift winds have the largest impact in the tropics.

      - The international Joint OSSSE: OSSEs are a powerful tool to assess the potential impact on the NWP forecast skill of planned or hypothetical future observing systems. Over the last several years an international Joint OSSE collaboration has emerged (Masutani et al. 2007 AMS 18th NWP conf. and Riishojgaard et al. 2011, AMS 15th IOAS/AOLS conf) centred on the use of NASA's and NOAA's data assimilation systems. A 13-month Nature Run provided by ECMWF (Andersson and Masutani 2010, ECMWF Newsletter No 123) has undergone extensive validation.

      - A first version of simulated observations has been generated from the Nature Run (Errico et al., AMS 2011). These observations include simulated errors of both instruments and representativeness. Validation is performed by comparing statistics of the results of assimilating these for one winter month compared with corresponding statistics obtained from assimilating real observations during an equivalent period using NCEPs GSI data assimilation system. In terms of the examined statistics, the OSSE validates remarkably well. In order to obtain this degree of success, it was found necessary to employ horizontally correlated observation errors for both.

      - AMVs (e.g., cloud-track winds) and radiances. The simulated observations with added observation errors are suitable for some initial OSSE applications.

      - One of the first candidate observing systems that is being assessed by this system is a wind lidar based on the GWOS concept developed by NASA in response to the NRC Decadal Survey. Results by Le Zhang et al. (AMS 2011) indicate that assimilating the DWL wind observations into the meso-scale numerical model (WRF) has significant potentials for improving the high-impact weather forecasting. However, the data impact much depends on the configuration (in terms of the area coverage of the data) and resolution of the DWL measurements. The European ADM-Aeolus instrument is subject to similar OSSE studies, based on DWL simulations carried out by KNMI.

      - This OSSE system has also been used to evaluate the potential benefit of unmanned airborne systems (UAS) for hurricane track forecasting. Experiments exploring the use of dropsondes deployed from high-altitude UAS near tropical cyclones in the Atlantic basin have been performed. OSSEs to evaluate the prospective Canadian PCW mission are being conducted at Environment Canada. The University of Utah, Florida State University, Mississippi State University and more institutes are starting OSSEs using the Joint OSSE Nature Run.

      - Radio occultation data: The Global Positioning System (GPS) radio occultation (RO) technique has emerged as a powerful and relatively inexpensive approach for sounding the global atmosphere in all weather. On average, COSMIC is providing 1,500 – 2,000 GPS RO soundings per day, uniformly distributed around the globe. RO sounding is able to penetrate clouds and precipitation with virtually no impact on its accuracy. With its ability to take measurements over the ocean, where there are few traditional observations, GPS RO soundings from COSMIC and other RO missions have demonstrated significant NWP impact. In particular, GPS RO soundings provide valuable information on the moisture in the tropical lower troposphere, which is crucial for the development of tropical storms (Ying-Hwa Kuo et al. AMS 2011). Taiwan and U.S. are planning for the COSMIC follow-on mission, (COSMIC-II), which promises to provide 8,000 to 10,000 GPS RO soundings per day.

      - Horizontal density of satellite radiance data: It has long been the practice at operational NWP centres to substantially thin satellite observations, particularly radiances, before assimilation. The reasons for such thinning include computational considerations (to meet operational timing requirements), the desire for a diverse “mix” of observations, and to avoid the effects of correlated observation errors which are not accounted for in current operational DA schemes (Baker and Langland, AMS 2011). However, it has recently been demonstrated that the spatial and inter-channel observation error correlations are small for AMSU-A and for the AIRS and IASI long-wave temperature sensitive channels that peak in the mid-troposphere to stratosphere. Several centres (ECMWF, NRL, NCEP and the Met Office) have therefore experimented with reduced thinning of these data, and found significant benefit

      - Use of the Chinese FY-3A data: Xiang Wang et al. (AMS 2011) compared measured radiances from FY-3A and AMSU-A against simulated radiances calculated from coincident profile measurements of temperature and humidity from COSMIC. Excellent agreement was found between FY-3A and COSMIC GPS RO data, similar to that between AMSU-A and COSMIC GPS data. It can therefore be concluded that FY-3A and AMSU-A data are of similar quality. This has been confirmed by William Bell and co-workers at ECMWF who have monitored the quality of FY-3A data within the operational 4D-Var system at ECMWF. The data is almost ready for operational assimilation at ECMWF.

      - Composite LEO/GEO Winds: The composite LEO/GEO winds are distributed by CIMSS. The data complements data gaps between GEO atmospheric motion vectors (AMV) and LEO polar AMV. The assimilation test was conducted with the JMA global 4D-Var and showed positive impact.

      - Accuracy of humidity observations from aircraft: R. A. Petersen et al. have studied the accuracy of the Water Vapour Sensing System (WVSS-II) currently being deployed and tested on commercial aircraft in the US and on three Lufthansa aircraft in Europe. The data was compared to radiosonde data. Following recent improvements to the instrument, the RMS fit to radiosondes is now < 0.5 g/kg for mixing ratio or <10% for relative humidity in most conditions.

      - Yongxin Zhang et al. (AMS 2011) and Feng Gao et al. (AMS 2011) have studied the impact of the Tropospheric Airborne Meteorological Data Reporting (TAMDAR) network, operated by AirDat LLC. TAMDAR measures humidity, pressure, temperature, winds, icing and turbulence by commercial airlines along the flight routes. The data is licensed by Airdat at a charge (EUMETNET is negotiating access for European NWP). The TAMDAR measurements have been assimilated into the WRF-based RTFDDA (4D-Var) system for the CONUS domain at 12-km and 4-km resolutions. Case studies focused on episodes of warm season rainfall, with positive results reported.

      - Impact of Radar reflectivity and ground based GPS: At JMA, relative humidity is retrieved from the 3D radar refractivity with Bayesian method. The RH data assimilation test was conducted with the JMA meso-scale 4D-Var. It makes the simulated echo position relocated appropriately. The global ground-based GPS data are acquired from IGS (International GNSS  Service).  The assimilation of GPS precipitable water data was tested in JMA - it reduced dry bias in the humidity analysis and showed positive impact on the forecast.

      - The impact of future developments of the space-based observing system on Numerical Weather Prediction impact of reduced ground-based observing systems on satellite data assimilation: The specific objectives of the present study are thus to estimate the impact of the key components of the current space-based observing system with a special focus on

        - temperature and humidity sounding from advanced sounders of the AIRS/IASI-type and conventional sounders of the HIRS/AMSU-A/MHS-type,

        - humidity imaging in clear skies and in areas affected by clouds and precipitation,

        - radio-occultation observations to support the estimation of the observation requirements of a radio-occultation observation constellation for the next decade,

        - indirect wind observations (through AMVs) with special focus on polar AMVs and

        - new observation types, in particular soil moisture derived from scatterometry (ASCAT).

Please see Appendix C.

      - Study to quantify the interaction between terrestrial and space-based observing systems: The aim was to investigate the impact of a thinned terrestrial observing system on radiance bias correction anchoring (OSEs with and without GPSRO and with full and less dense conventional observing system) with special focus on:

        - the synergy between radiosondes and GPSRO as anchors (with resepect to temperature);

        - the question of what radiosonde coverage is needed in the stratosphere, to which height, and for which latitude ranges;

        - the synergy between ships/buoys and GPSRO as anchors (with respect to surface pressure).

Please see Appendix D.

      - Impact of targeting: The emphasis of the THORPEX DAOS group has been on the evaluation of the impact of observations, including targeted observations, based on results from field experiments (ATReC, AMMA, IPY, T-PARC), OSEs and OSSEs. The main outcomes from these impact studies may be summarized as follows:

        - The value of extra-tropical targeted data has been found to be positive but small on average

        - Observations taken in sensitive areas have more value than observations deployed randomly

        - Past experiment do not provide evidence of major impact obtained from just a few observations (when averaged over a large sample of cases)

        - There are limitations to the current assimilation methods to be able to detect the small signal associated with precursors of meteorological systems

        - The methods employed to identify sensitive areas do not appear to be a major problem

        - Additional observations around tropical cyclones have proven to be useful

        - Benefit may be obtained from regional (versus highly localized) and systematic targeting during low predictability flow regimes on a continuous basis (days or weeks) and/or via adaptive processing and data selection of satellite data.

      - The EUCOS upper-air network design study: A set of upper-air network design studies had been carried out under the coordination of the EUCOS scientific advisory team (E-SAT): The study assessed the impact of several potential optimizations aimed at reducing the redundancy between aircraft and radiosondes where both systems report regularly and in close proximity. The OSE studies were conducted with the global model of ECMWF and the limited area models of OMSZ (Humgary) and several HIRLAM members. In general the experiments show similar results.

      - The conclusions from the EUCOS upper-air network redesign study are:

- (a)	In agreement with the previous Space-Terrestrial study the baseline scenario shows a significant and the strongest reduction in forecast skill.

- (b)	Scenarios 3a and 3b which removed radiosonde sites collocated to 3-hourly visited E-AMDAR airports show almost no degradation in forecast skill. Results from OMSZ’ regional model show better results for a scenario where 0 UTC radiosonde observations –in vicinity to airports- are kept.

- (c)	Further thinning of upper-air observations to 250 km or 500 km spacing show a significant degradation of forecast skill for most parameters, and for summer and winter periods.

- (d)	When thinning radiosonde observations the parameter most negatively affected is relative humidity in lower troposphere.

- (e)	Biases are observed between radiosonde and AMDAR temperature measurements. More investigations are needed to correct biases of AMDAR observations.

      - The recommendations derived from the EUCOS upper-air network redesign study are:

- (1)	A collocation of operational radiosonde observations and 3-hourly AMDAR profile measurements should be avoided..

- (2)	Humidity information in the lower troposphere should not be degraded, E-SAT therefore recommends to improve the coverage of lower tropospheric moisture observations.

- (3)	E-SAT recommends to work towards a horizontally more homogeneous distribution of upper-air observing sites.

9.2	PROPOSAL FOR NEW OSES/OSSEs TO BE PROMOTED BY ET-EGOS

      - The list of OSEs/OSSEs presented to CBS-Ext.(10) (2010) consisted of those specified in the Annex to paragraph 6.1.32 of the general summary of the Abridged Final Report with Resolutions and Recommendations of CBS-XIV (2009) and in addition the following OSEs/OSSEs which the ICT-IOS requested Members to conduct:

- (a)	In the presence of dense satellite observations of ocean surface wind, what is the requirement for the density of in-situ surface pressure observations?

- (b)	Guidance is needed on desirable coverage of Automated Ship-borne Aerological Programme (ASAP) soundings over oceans;

- (c)	In support of Regional NWP, what observations are needed for the planetary boundary layer - which variables, and what space/time resolution?

- (d)	Studies are needed to address identification of critical locations for surface-based stations.

      - Based on this list and subsequent new results, an updated proposal for OSEs and OSSEs of particular interest to ET-EGOS has been developed as part of the preparations for the fifth workshop on the Impact of Various Observing Systems on Numerical Weather Prediction. This new list of specific studies and science questions is shown here as Appendix A.

9.3	NEXT OSEs/OSSE WORKSHOP

      - CBS-Ext.(10) (2010) requested the OPAG-IOS to develop the scope of the fifth workshop as soon as possible, including exact dates for holding the Workshop in 2012. It welcomed the proposal from the USA representative to host this workshop.

      - The fifth workshop on the Impact of Various Observing Systems on Numerical Weather Prediction will be organised by the Expert Team on the Evolution of the Global Observing System in xxxxx, United States, from 22 to 25 May 2012. Participants are expected to come from all the major NWP centres which are active in the area of impact studies. The workshop will be conducted in English. As on the first four workshops it is planned to produce a workshop report to be published as a WMO Technical Report that will include the papers submitted by the participants.

      - The workshop will be organised in the following sessions:

- Session 1: Global forecast impact studies

- Session 2: Regional forecast impact studies

- Session 3: Specific scientific areas (including network design)

- Session 4: Workshop discussions and conclusions.

      - The draft workshop announcement is shown as Appendix B.

      - The committee has agreed on the following plan and time table for the organisation of the workshop (EA: Erik Andersson, LPR: Lars Peter Riishojgaard, MO: Miroslav Ondras)

| No. | Action | Responsible | Deadline |
| --- | --- | --- | --- |
| 1 | Invitation from the PR of USA with WMO | LPR | end Apr 2011 |
| 2 | 1st unofficial invitation, including preliminary speakers and draft programme) | EA | mid May 2011 |
| 3 | Preliminary programme | EA | mid Nov 2011 |
| 4 | Information on Local arrangements (Venue, transport, accommodation, etc.) | LPR | mid Nov 2011 |
| 5 | List of participants, Country, institution | EA | mid Nov 2011 |
| 6 | List of participants to be fin. supported, (Country, Town, Institution, contact address) | EA | mid Nov 2011 |
| 7 | Costing | MO | end Nov 2011 |
| 8 | Resource mobilization | All | end Nov 2011 |
| 9 | Preparation & approval of Meeting Form | MO | mid Dec 2011 |
| 10 | Invitation participants | MO | end Jan 2012 |
| 11 | Invitation participants to be fin supported, concurrence from respective PRs | MO | mid March 2012 |
| 12 | Travel arrangements | MO | mid May 2012 |
| 13 | Final programme, speakers, participants, panel chairs, etc.. | EA | mid May 2012 |

Appendix A

# Proposed topics for NWP impact studies relevant to the evolution of global observing systems

| Short name: Full name | Science question |
| --- | --- |
| Surface-based |
| S1MarinePs: Surface pressure over ocean | What density of surface pressure observations over ocean is needed to complement high-density surface wind observations from satellites? Suggestions: (a) network density reduction OSE in N.Atlantic, (b) southern oceans OSSE. |
| S2Strat: In situ observations of the stratosphere | What network of in situ observations is needed in the stratosphere to complement current satellite observations (including radio occultation)? What about the tropics? |
| S3AMDAR: Coverage of AMDAR | What is the impact of current AMDAR observations? What are the priorities for expansion of the network? |
| S4ASAP: Coverage of ASAP | What is the impact of current coverage of profiles from the Automated Shipboard Aerological Programme (ASAP)? How might coverage be optimised for a given level of resources? |
| S5Radar: Radar observations | What are the impacts of current radar observations, including radial winds and reflectivities? |
| Space-based |
| S6RO: Radio occultation saturation | At what level, in terms of profiles per day, does the impact of radio occultation observations start to saturate? |
| S7SatLand: Satellite radiances over land | What is the impact of new developments in the assimilation of radiance data over land? |
| S8Sounders: Impact of multiple satellite sounders | What benefits are found when data from more than one passive sounder are available from satellite in complementary orbits, e.g. multiple AMSU-As, AIRS + IASI ? |
| S9AMVs: AMVs | What impacts are currently found from AMVs? |
| General |
| S10Thinning: Data density and data thinning | What impacts/benefits are found from data density/thinning strategies from various observation types? |
| S11PBL: Observations of the PBL for regional / high-resolution NWP | What should be the focus of improvements for observations of the PBL in support of regional/high-resolution NWP? Which variables and what space-time resolution? |
| S12UA: EUCOS-like upper air OSEs | Can EUCOS-like upper air studies be performed for other regions? |
| S13AdjEns: Regional application and adjoint and ensemble methods | What insights can be gained from more tailored use of adjoint- and ensemble-based measures of observation impact, for example, in the tropics or at the meso-scale where metrics other than global energy may be appropriate? |

| S14ExtRange: Impact of observations on extended range forecasts | Which observations are particularly important for the 7-14 day forecast range? |
| --- | --- |
| S15Targeting: Targeted observations | What do experiments on targeted observations tell us about observing system design? |
| S16aAMMA, S16bIPY: AMMA and IPY legacy | What impacts/benefits could be expected by sustained components of the AMMA and IPY special observing systems? |

_______________

APPENDIX b

## Workshop Announcement (Draft)

1.	The WMO and THORPEX co-sponsored fifth Workshop on the Impact of Various Observing Systems on Numerical Weather Prediction will be organised by the Expert Team on the Evolution of the Global Observing System in xxxxx, United States, from 22 to 25 May 2012. Participants are expected to come from all the major NWP centres which are active in the area of impact studies. The workshop will be conducted in English. As on the first four workshops it is planned to produce a workshop report to be published as a WMO Technical Report that will include the papers submitted by the participants.

2.	The previous four workshops in this series took place in Geneva (April 1997), Toulouse (March 2000), Alpbach (March 2004) and Geneva (May 2008). Results from Observing System Experiments (OSEs), both with global and regional aspects were presented and conclusions were drawn concerning the contributions of the various components of the observing system to the large scale forecast skill at short and medium range (Workshop Proceedings published as WMO World Weather Watch Technical Reports TD No. 868, 1034, 1228 and 1450, respectively).

3.	Since then, some significant changes and developments have affected the global observing system and more efforts have been devoted to meso-scale observing and assimilation systems. There has also been a trend toward using other techniques than OSEs to document data impact, such as adjoint-based sensitivity to observations or ensemble-based sensitivity. Field experiments have been carried out, in particular through the THORPEX project, and the use of targeted data has been assessed. You may wish to contribute to the workshop on any of these general topics, or address one or several of the specific studies and science questions listed in the attachment. Those who are interested to contribute to this workshop are asked to submit a short abstract and request an invitation from the organisers by e-mail as detailed below.

4.	At the Fifth workshop, the results will be reviewed in plenary discussion sessions and a consensus view will be formed. Conclusions to help guide the design of an optimised Global Observing System for NWP will be drawn.

5.	The workshop will be organised in the following sessions:

Session 1: Global forecast impact studies

Session 2: Regional forecast impact studies

Session 3: Specific scientific areas (including network design)

Session 4: Workshop discussions and conclusions.

6.	To receive an invitation to participate, please submit abstract and title to the organising committee via email to Karen.Clarke@ecmwf.int, by 31 January 2011. The full papers for the workshop report will be required at the time of the meeting and should be sent in electronic form. Information on hotel accommodation and local transport will be posted in a subsequent announcement. There will be the possibility of financial support for a limited few upon request to the Chairman of the organizing committee via e-mail to the address given above.

7.	The Organizing Committee, chaired by Erik Andersson (ECMWF), comprises Carla Cardinali (ECMWF), John Eyre (Met Office, UK), Ron Gelaro (NOAA/GMAO, the US), Florence Rabier (Meteo-France), Lars-Peter Riishojgaard (NOAA/JCSDA, the US) and Yoshiako Sato (JMA, Japan).

8.	The local organizing committee is chaired by Lars-Peter Riishojgaard (NOAA/JCSDA, the US). Local information about xxxxx and local arrangements can be found at www.xxx.xx. The local organisers will coordinate hotel arrangements for the attendees.

_______________

appendix c

appendix d