| WORLD METEOROLOGICAL ORGANIZATION ____________________ COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS EXPERT TEAM ON THE EVOLUTION OF GLOBAL OBSERVING SYSTEMS Seventh Session GENEVA, SWITZERLAND, 7-11 MAY 2012 |  | CBS/OPAG-IOS/ET-EGOS-7/ Doc. 8.3.2(3) (03.04.2012) _______ ITEM: 8.3.2 Original: ENGLISH |
| --- | --- | --- |

Review of Statements of Guidance

Nowcasting and Very Short Range Forecasting (VSRF)

(Submitted by  Aurora Bell, Romania)

SUMMARY AND PURPOSE OF DOCUMENT The document provides information on the current status of the Statement of Guidance for Nowcasting and Very Short Range Forecasting (VSRF).

ACTION PROPOSED

The Meeting is invited to consider the current version of the Statement of Guidance and to suggest updates as appropriate.

____________

References:	Current versions of the Statements of Guidance

http://www.wmo.int/pages/prog/sat/RRR-and-SOG.html

Appendix A:	Statement of Guidance for Nowcasting and Very Short Range Forecasting (VSRF)

DISCUSSION

The new version of the Statement of Guidance for Nowcasting, Very Short Range and short range Forecasting (NVSRF) as detailed in Appendix A, includes the following changes:

1) Changes requested by ET-EGOS-6, i.e.

- The SoG will be reorganized as following: (i) Gaps in quantity and quality; (ii) New developments; and (iii) Gaps in Capacity Building;

- Duplication to be removed;

- Meteorological concepts/features to be considered;

- Encouraging met services to be more open regarding data policy for cross-border data exchange (not only global data exchange);

- Adding new variables: e.g. fresh deposit of snow;

- New issues as proposed by the PoC to be added.

2) Some changes proposed by the ET-EGOS chair in February 2012, and comments/questions added for the PoC to address.

3) Changes per the review of Dominique Ruffieux (Switzerland) and the Point of contact in March/April 2012.

The Team needs to review and comment the SoG for NVSRF with the view to post an updated version of the SoG on the web with the Chair’s approval.

__________

Appendix A

Statement of Guidance for

Nowcasting, Very Short Range  and short range Forecasting

(Point of contact: Ms Aurora Bell, Romania)

(Version updated January 2009 by Ms Aurora Bell, Romania, merged with Statement of Guidance for Synoptic Meteorology- version July 2008, Nick Grahame, UK and approved by ET-EGOS-5, December 200 and reviewed by Dominique Ruffieux, Switzerland, and Aurora Bell, February 2012 taking into account ET-EGOS-6 and John Eyre’s comments)

Nowcasting is carried out in regional or national forecast centres.  At this time,  extrapolation of observations, using heuristic rules to modify these observations into the future and using numerical weather prediction models (NWP) forecasts are made from zero to 2 hours.  Very Short Range Forecasting (VSRF) is defined as when meteorologists analyse observations to diagnose the atmospheric state and then forecast the atmosphere up to 12 hours.  Depending on the phenomena, nowcasting and VSRF cover spatial scales from the micro-alpha (hundreds of metres to 2 km) to the meso-alpha (200-2000 km).  Temporal scales are from a few minutes to 12 or more hours.  At the larger end of the spatial and temporal scales, there is a transition to synoptic scale with phenomena such as extratropical and tropical cyclones.

While nowcasting is largely based on observational data, VSRFs are now being generated based on high-resolution local area and regional numerical weather prediction models.  These models will increasingly be used to provide guidance to meteorologists making detailed nowcasts and VSRFs. It has meanwhile  to be mentioned that those models will still be driven by a number of 3D observations increasing with an increase of the model spatial and temporal resolutions.

While nowcasting can be done over any region, it is more frequently practised over populated areas having, for example, cities, airports, marine and lakes recreation areas or for special events and large venues such as the Olympic Games or other sporting events, or for special missions like interventions in wild fires, floods, polluted or contaminated areas, or for regions where emergency forces have to act.

Nowcasting and VSRF were first practiced and developed due to the needs of the aeronautical community.  The data requirements of aeronautical meteorology include and expand upon those of nowcasting and VSRF. An important step to bridge the data gaps in aeronautical meteorology is to use of observations from “hybrid systems”.   For example, the wind profile can be derived also from Doppler weather radar (Velocity Azimuth Display products), or rain can be estimated in remote areas from satellite and radar.

Sophisticated nowcasting techniques are now routinely used in developed countries where  radar systems are mature and robust.  However, in less developed countries the required operational radar systems needed for nowcasting are still missing. There are efforts to encourage developed countries to extend and adapt their existing Nowcasting systems mainly to developing countries, where observational data is generally very sparse and also less frequently received (e.g. satellite data). Developing countries should be encouraged to develop - “low cost” Nowcasting systems based on satellite data and NWP since radar data is often non-existent.

Nowcasting and VSRF techniques can be applied to many phenomena.  They are most frequently used to forecast: (1) convective storms with attendant phenomena; (2) mesoscale features associated with extra-tropical and tropical storms; (3) fog and low clouds; (4) locally forced precipitation events; (5) sand and dust storms; (6) wintertime weather (ice, glazed frost, blizzards, avalanches), and, (7) wild fires and (8) contaminated areas.  While there is some commonality with synoptic meteorology in forecasting these phenomena, nowcasting focuses greater attention on short time scales and fine spatial resolution covering small geographic areas.  In recent years, there is a clear tendency to develop the nowcasting of “severe” weather.   This also requires a special operational routine for the issue of warnings.  These warnings are, based on specific regional needs but also follow specific national or administrative regulations and thresholds.

Nowcasting and VSRF observational requirements are best satisfied by frequent monitoring of the location, intensity, movement and evolution of the phenomena of interest.  Important weather elements are: (1) clouds and precipitation; (2) surface meteorological variables of pressure, wind, temperature, moisture, present weather and precipitation accumulation (or snow layer) and recently, land cover and structure; (3) 3-dimensional (3-D) wind field; (4) 3-D humidity field and, (5) 3-D temperature field.  Each variable, listed above, is assessed in the sections below as to how well the observational requirements are met by existing or planned observing systems.

Short Range Forecasting (known as synoptic forecasting) could be defined as the activity performed by a forecaster when predicting the weather at time scales from 12 hours to several days, and at related space scales.  Numerical Weather Prediction (NWP) output (global, regional and ensembles) play a vital role in forecasting; and information benefiting these models benefits synoptic forecasting.  Many uses of the observations in synoptic forecasting and meteorology are thus related to numerical models:

- to evaluate the value of model output by comparing the analysis and early frames of a forecast (regarding timing, location and intensity of synoptic-scale features);

- to take appropriate mitigating action if a mismatch exists between model output and observations;

- to capture smaller-scale details that are unresolved by the models; and,

- to verify forecasts a posteriori.

This statement of guidance concentrates on uses other than data assimilation and model forecasting, which are already covered in the SOGs for global NWP and high-resolution NWP.

Contrary to a NWP data assimilation system, where the goal is to estimate each atmospheric variable on a more or less regular grid, synoptic meteorologists attempt to depict meteorological phenomena in an object-oriented way.  Forecasting methods evolve from looking at individual observing systems separately to integrating different data sources to infer meteorological parameters and phenomena, so that the impact of the different observing systems discussed in this SOG is both by objects and by data source.

- Clouds and precipitation

- Satellites

Geostationary satellites imagery is the prime source for locating synoptic-scale features and objects in real-time, allowing them to detect any incipient discrepancies between model forecasts and reality at an early stage.  This is particularly true over oceanic areas, where conventional data are typically very sparse.  Model fields and satellite imagery may be superposed on a workstation screen; a good example is given by the potential vorticity field of the upper-level flow correlated with water vapour satellite images.  The horizontal resolution and coverage are good, except over the Polar Regions (60-90N and 60-90S).  The vertical resolution is improving with the new generation of geostationary satellites GOES and Meteosat.

The steadily improving horizontal and spectral resolution of geostationary satellite instruments leads to improved detection and classification of clouds.  Progress has been made on night-time detection of low clouds, which used to be marginal, and on distinction between high-thin and high-thick clouds (e.g., cirrus versus cumulonimbus).  Many of the derived products are very useful for nowcasting purposes, and the recently enhanced rapid-scan facility on Meteosat 8 is also beneficial.

Quantitative precipitation estimates from geostationary satellites are improving, but are still considered marginal.

Meteorological satellite data are well suited to monitoring in a qualitative way the initiation and rapid development of precipitation generating systems both in space and time.  Rapid imaging (on the order of minutes) is critical to nowcasting, but it is not yet provided by all geostationary satellites.  With some satellite systems, the rapid scan of small areas competes with broader coverage requirements.  Frequent images from geostationary satellites provide good to adequate horizontal resolution for identifying the initiation, evolution and movement of synoptic and mesoscale cloud systems or of local circulations over most of the tropics and temperate zones.

The more frequent and more comprehensive data collected by latest satellites will also aid the weather forecasters in the fast recognition and accurate prediction of dangerous weather phenomena such as thunderstorms, thus forming  an important contribution to nowcasting.

Air mass parameters (moisture, temperature at different tropospheric levels) derived from satellite data can also be used to issue severe weather warnings, if a derived severe weather index exceeds a certain threshold.  These thresholds are usually determined empirically and should not be regarded as fixed values.  A skilled local forecaster is absolutely necessary for a correct interpretation.

An operational satellite-based retrieval of these derived parameters provides good potential for the identification of pre-convective conditions.

Polar orbiting satellite infrared and visible images continue to deliver excellent horizontal and spectral resolution, with their use being limited only by the infrequent availability of the data.  However, for the high latitudes, where geostationary satellite data are missing, the polar orbiting satellites provide valuable observations with acceptable frequency due to the convergence of tracks.

Surface winds over oceans provided either by microwave imagers (wind speed) or scatterometers (speed and direction) are considered accurate, and are widely used, particularly for marine forecasts.  The horizontal resolution is good at synoptic scales, while the temporal resolution is marginal to acceptable depending on the swath width of the instrument.

The detection of precipitation is marginal for microwave imagers and depending on the wavelength of the instrument good to poor for scatterometers.  Precipitation estimates derived from satellite measurements are improving.  Microwave radiometers, and precipitation radars are capable of estimating precipitation with acceptable accuracy and horizontal resolution.  The nature of the phenomenon (short-lived convective cells and rain bands) limits the use of data for quantitative assessments of accumulated precipitation.

The satellite-based products developed for nowcasting use can also provide new information about the relative probability of precipitation intensity categories in pre-defined intervals.

Using the polar orbiting satellites, the combined analysis of two different types of observations (high-resolution multi-spectral imagery and microwave observations) allows for a higher quality of the precipitating cloud product.

There are products for rainfall rate estimated specifically from convective clouds (in millimeters per hour).  The are complementary Nowcasting products which provide information on the characteristics of precipitating clouds and cloud type.

Data collected by satellites in clear air can be used for quantitative studies.  Water vapour and thermodynamic stability can be estimated in the non-cloudy pre-convective areas and can therefore help to classify the air mass in terms of severe weather potential.  Moisture features in the troposphere, like the presence and position of the jet stream, - are related to the dynamics of the upper troposphere and provide information on the future development of weather systems.

Total precipitable water provides information about the vertically integrated humidity in the atmosphere.  It is given as the total amount of liquid water (mm) and is defined as, if all the atmospheric water vapour in the column from the Earth's surface to the "top" of the atmosphere were condensed.  High values in clear air often create conditions for the development of heavy precipitation and thus flash floods. Precipitable water can also be measured with ground-based microwave radiometers.

Stability Analysis Imagery provides estimations of the atmospheric thermodynamic stability in cloud-free areas.

Air Mass Analysis products provides basic properties of air masses such as upper and mid- level humidity, mean temperature, atmospheric stability, cloud, etc.  Previously, these properties evaluated manually from radiosonde soundings, but MSG data now makes it possible to perform them automatically every 15 minutes and with 5 kilometer horizontal resolution.

The High-Resolution Wind product supports Nowcasting by providing atmospheric dynamics information at a scale much finer than the synoptic scale.  Of particular interest is the information associated with the derivative of this product, i.e., wind shear and wind convergence.  The product can also be used for aviation support and as input to regional NWP models.

The Rapidly Developing Thunderstorms product monitors thunderstorms from MSG data.  It automatically identifies, monitors and tracks intense convective systems so detects of the existence of  rapidly developing convective cells.  These highlight the most active cells, and can be therefore be used for the automated convection detection needed in aviation meteorology.

Automatic Satellite Image Interpretation is an automatic diagnosis of typical cloud structures based on  conceptual models.  It identifies complex meteorological phenomena like fronts, wave structures, areas of intensification at fronts, positions of the jet stream axis, comma clouds and enhanced convection areas, etc.

While coverage is good over mid-latitudes and tropical areas, coverage over polar areas is marginal or absent.  Satellite microwave imagers and sounders offer information on liquid water and precipitation with good horizontal resolution but marginal temporal resolution.  It has acceptable accuracy (though validation is difficult) only if other precipitation data (radar or rain gauge) are missing.

- Weather radars

Weather radars are essential for the detection of precipitation in real-time at high-spatial resolution.  In areas where radar networks are installed, the horizontal and temporal resolution are excellent, and the accuracy of the quantitative estimation of precipitation is acceptable to good except for complex topography, where obscuration of low-lying areas hidden by higher topography is a limiting factor.

Doppler radars are now becoming the standard, so that VAD winds and the identification of line squalls and outflow boundaries are an essential element of the data.  Increasingly, polarimetric radars are being used to discern between liquid and solid precipitation, which is highly relevant for all types of traffic and infrastructure forecasts (i.e., aviation, road and rail weather, building industry, etc...).

Conventional scanning weather radars can detect and track the movement and intensity of convective and non-convective systems over many populated areas where nowcasting techniques are primarily practiced.  Radar data are valuable in precise quantitative measurements, identifying heavy rain, severe hail, high straight-line winds and tornadoes (if Doppler capability is available) in single cellular convective storms as well as in more organized convection, like linear or clustered multi-cellular storms, associated with extratropical and tropical storms. The use of weather radars precipitation cells trajectories is also a tool commonly used for nowcasting The location and intensity of locally forced precipitation events such as those found downwind of large water bodies, or with upslope enhancement, can be monitored.  Radars can  also identify changes in precipitation type if polarimetry is used.  Polarimetric radar systems provide information on the temporal and spatial distribution of hydrometeors in the atmosphere and so are able, in contrast to conventional radar, to classify the hydrometeors such as rain, hail, graupel, and snow.

Clear air detection by radars can help identify the regions where lifting mechanisms develop giving a good precursor to convection initiation.  Coverage over many populated areas is marginal to acceptable, but over oceanic and sparsely inhabited land areas coverage is marginal or absent since it is a low level phenomena.  Where available, the time resolution of radar scans is about 5 -10 minutes at regional level.  The coverage, in well sited radars where orography does not block the beam , is circular regions of several hundred kilometre in diameter.  Due to the strong societal impact of severe weather in recent years, there is a general increase in the interest of many nations to develop radar networks, and even to join existing networks.  These large cross-border composite radar networks provide information at a lower resolution than the local radar data, but are of great value for regional monitoring. A gap that can be addressed is the lack of availability of the radar data collected by private companies that could be integrated into the composite networks - at least in severe weather situations. There are also private companies, agencies and utilities that have their own radars or lightning detectors  that can be integrated with national or regional public networks.

Disdrometers are used to measure the drop size distribution and velocity of falling hydrometeors. Some disdrometers can distinguish between rain, graupel and hail. Disdrometers are not used operational but the uses for disdrometers are numerous. They can be used for traffic control, scientific examination, airport observation systems, and hydrology in enhancing the observation of precipitation.

- Lightning detection

Ground-based (total or only cloud-to–ground) real-time lightning detection and tracking systems have demonstrated their value as an early indicator of the location and intensity of developing convection, and also of the movement of thunderstorms.  By identifying electrically active storms in space and time, these systems increase warning lead times for dangerous thunderstorms which may have major impacts on aviation, the electric power grid, mobile phones companies, satellite transmissions, oil and gas companies, forest management, fires control, marine and recreational activities.  The horizontal resolution of these systems is marginal to acceptable over populated land and adjacent ocean areas; however major progress have been achieved these recent years to improve accuracy and resolution of these systems.

Over most oceanic, sparsely settled land and polar areas, coverage is marginal to acceptable, but in some areas, totally absent.  Cycle time and delay is acceptable to good.  In some countries  efforts are under way to expand lightning detection systems to cover more oceanic areas.  Advanced lightning systems also provide the 3-D structure of the electrical activity.   As exploited by NSSL (Oklahoma Lightning Mapping Array), under such technique, up to thousands of points can be mapped for an individual lightning flash, to reveal its location and the development of its structure. Scientists hope to learn more about how storms produce intra-cloud and cloud-to-ground flashes and how each type is related to tornadoes and other severe weather. Better lightning mapping techniques show that some supercell thunderstorms have "lightning holes" where updrafts are located and precipitation is scarce. If these holes form, as suspected, just before a storm becomes severe, this information could alert forecasters to developing severe conditions. This has particular special value for aeronautical purposes.

The strength of the lighting information is provided by the almost real-time sampling of the atmosphere, and provides added value to radar and satellite data.  The ‘satellite-radar-lightning’ trio is the basic building block for a good nowcasting observation system over populated areas.

- Surface Variables

Aviation and synoptic surface observing stations, both automatic and manual, measure pressure, wind, temperature, humidity, present weather, visibility and accumulated precipitation at many locations where nowcasting and VSRF is practiced.  The sites are often at or near airports and population centres and provide a comprehensive description of meteorological variables.  For most variables, the accuracy of the data is adequate to good.  For present weather however, there are important gaps in the networks, and phenomena like hail, tornadic winds, downbursts, and local maximum of precipitations are not well sampled.  In some regions, volunteers provide reports of these phenomena.

Over populated areas, the horizontal resolution of most surface variables is marginal to acceptable for nowcasting for most phenomena.  For a few small scale phenomena, which are highly variable in distribution and intensity, such as fog, low cloud, dust and sand storms, the measurable horizontal resolution of visibility and cloud base/top data is less than marginal even in populated areas.  Over oceanic and sparsely populated areas, the horizontal resolution is marginal or absent.

Surface data are quite essential in synoptic meteorology.  Their horizontal coverage is generally good over populated land, and marginal to poor over oceanic or desert areas, although oceanic buoys are being deployed in large numbers and improving the situation there.  Measurement frequency and data accuracy are good.  In addition, forecasters are very familiar with these data and can make best use of them.

Over land surface, data from an increasing number of automated stations contains, as a minimum, information on wind, temperature, moisture and mean sea-level pressure, with weather elements such as cloud cover or visibility mostly available from manned and aeronautical stations.  Regional efforts are underway to collect, standardize, and quality control data from observing networks from non-NMHS sources such as hydrological services, road networks and private and industrial operators.

Over the oceans, fewer parameters are available.  Mean sea-level pressure, measured on ships, buoys, and islands is a key tracer of synoptic activity.  Even very isolated stations may play an important role in synoptic forecasting, especially when they point out differences with NWP model output.

Satellites do not observe surface pressure nor horizontal visibility, but some research polar satellites provide information on the global coverage of oceanic surface winds with acceptable horizontal resolution and accuracy, taken into account the lack of available information on these regions. Passive microwave imagers already provide information of acceptable temporal resolution, but of wind speed only.  The temporal cycle of data from polar satellites and the delay in their availability makes the data marginal or not very useful for nowcasting / VSRF.

The coverage of the radar observations has gaps due to  the geometry of the radar observations (overshooting of the radar beam above low level precipitation cores) but also due to orographic blocking, making it difficult to provide complete azimuthal coverage out to the full range of the radar.   Good coverage is required in weather sensitive areas, such as airports, harbours and cities.

- 3-D Wind Field

To be able to make nowcasts or VSRF predictions several hours in advance, the wind field needs to be known within the area of interest and for a few hundred kilometres beyond.  The wind shear is a crucial element in determining the organization of the convection (severe vs. non-severe). In addition, NWP outputs are essential.

There are four types of measurement technologies

- Radiosounding : precise but low temporal resolution

- Wind profiler : precise and good temporal resolution, but possible contamination, in populated areas

- Weather radar winds : sort of precise and only during precipitation (+ maginally when insects). No wind data in clear air, in populated areas

- AMDARs : precise, but at some locations (airports) and at some times (little during nighttime)

Radiosondes remain the reference observing system for determination of detailed vertical structure in the atmosphere.  This is due to their excellent vertical resolution (provided full resolution data are being transmitted instead of standard / significant eel data only) and second to the simultaneous presence of temperature, wind, moisture and pressure measurements (moisture with marginal accuracy, all other parameters with good accuracy).  Vertical stability analyses, seeking details which are not necessarily captured by the NWP models, are based mostly on the radiosondes. Moreover, radiosondes remain one of the key observing systems in NWP analyses; the model assessment made by the forecasters relies to a large extent on them.  Thus, despite the poor temporal resolution and uneven geographical coverage, radiosondes are of primary importance in synoptic meteorology.

Wind profiles are available from radiosondes in specific locations over populated land areas and from aircraft (ascent / descent) profiles over limited areas (airports).  The temporal resolution of wind profiles from radiosondes is marginal to acceptable.  Except for a few radiosonde stations and infrequent single level aircraft reports, wind coverage in Polar Regions is essentially absent.

Single-level satellite winds are available over low and mid-latitudes and provide acceptable horizontal and temporal coverage, but vertical coverage is marginal.  Satellite winds are of acceptable to marginal accuracy.

Wind profilers (boundary layer and tropospheric) are still widely regarded as research tools, despite the fact that operational networks have been established in the United States of America, and in Europe. The good temporal resolution of wind profilers and the generally adequate data quality is making them quite useful.  However, their geographical coverage is expected to remain marginal to poor except in a few regions of the world.  Moreover, the cost of technical maintenance and the difficulty to obtain the necessary frequency bands are limiting their operational implementation.

Except for a few radiosonde stations and infrequent single level aircraft reports, wind coverage in Polar Regions is essentially absent.  Volumetric vertical profiles of winds usually within 1 - 5 km of the ground are provided by Velocity Azimuth Displays (VAD) generated from scanning Doppler radars when sufficient atmospheric reflectors are available – normally, with precipitating systems, but also in clear air on dust and insects.  In clear air, the VAD data can be contaminated by birds, so this information requires careful treatment.

Data available from either isolated radars or radar networks have good time resolution, of the order of a few minutes, but this happens only over populated areas. Overall horizontal and vertical coverage is generally acceptable and the vertical resolution is good, but it is confined to a small region around the radar (up to 50 km).  Important information about the storm scale winds or local wind maxima, are provided by the Radial Doppler Velocity field, or by the Storm Relative Velocity field.  These data are critical in determining the internal structure of the severe storms, and in the manner in which a storm can modify the environmental winds.

Near or just below the tropopause, single level aircraft winds are often available along primary air routes over certain areas in the temperate and tropical zones.  At major airports, especially in populated areas, AMDAR data are providing an increasing number of high quality soundings.

Single-level satellite winds are available over low and mid-latitudes and provide acceptable horizontal and temporal coverage, but vertical coverage is marginal.  Satellite winds are of acceptable to marginal accuracy.

Doppler wind profilers have been deployed over limited areas like USA, Europe, and Japan and are in strong development in countries like China and South Korea.  Tropospheric profilers provide high vertical resolution and accurate winds at sub-hourly intervals from 0.5 to 17 km.  Boundary layer profilers produce winds with similar attributes at altitudes from 0.1 to 8 km, depending on the weather conditions.  Accuracy, vertical resolution, cycle time and delay are good.  However, the limited deployment over a few populated areas results in marginal, or even worse, horizontal resolution.  Wind profiler data over oceanic, sparsely populated and Polar Regions is nearly absent.  An expansion of boundary layer profilers in combination with AMDAR profiles and VAD weather radars wind profiles may provide a mean of improving upper air coverage over selected land areas.

The increasing availability of display software for ADMAR data, particularly for ascent / descent profiles is making these data a highly useful tool for forecasters, particularly in data sparse regions of developing countries.  Data quality is generally good, and quality control measures are being put in place to ensure adequate data integrity.

An expansion of the use of AMDAR technology over the next few years provides the best opportunity for increasing wind observations. While AMDAR vertical profiles of wind and temperature are limited to airports having suitably equipped aircraft, additional single-level data will be given by AMDAR aircraft when flying at cruise altitudes.  In addition to ingesting AMDAR data into numerical models, it is also important that the profile data be routed to local forecast offices for display on thermodynamic diagrams and on plan views of the atmosphere.

- 3-D Temperature and Humidity Fields

In nowcasting, the temperature and humidity fields are particularly useful for determining atmospheric stability for predicting convective storms initiation, precipitation type, the possibility of hail and the amount of frozen precipitation.  The vertical profiles of temperature, moisture and winds provide the basic information for convective nowcasting.

Radiosondes and some aircraft provide profiles of temperature and humidity over populated land areas.  Over these areas, the horizontal and temporal resolution is marginal to acceptable and the vertical resolution and accuracy are good.  However, over most of the Earth - ocean and sparsely inhabited land - coverage is marginal or absent.  Temperature profile data are supplemented by single-level aircraft data along major air routes. Also, some aircraft are beginning to carry humidity sensors, as well.  This yields acceptable to good horizontal and temporal resolution and accuracy.  A few sites have radio acoustic sounders (RASS) associated with wind profilers in several populated areas.  They provide profiles of virtual temperature from near the surface to up to from 1 to 4 km depending on the type of system wind conditions.  Their vertical resolution and accuracy are good, but horizontal resolution is less than marginal.

Infra-red soundings from geostationary satellite (only in cloud-free areas), also help to expand coverage in some regions by providing hourly measurements.  Vertical resolution has been  substantially improved with AIRS on EOS-Aqua and IASI on Metop.  Also data from CrIS on Suomi-NPP is expected soon.  Satellite sounding data are currently under-utilised over land;  progress has already happened, but it is true that much remains to be done in the near future.  In the future, radio-occultation measurements from satellites will complement other systems and provide high accuracy and high vertical resolution in the stratosphere and upper troposphere, thus helping to improve analyses around the tropopause. Moreover, a strong tendency to push ground-based remote sensing microwave radiometer into operational status can be observed.

Similar to the 3-D wind field, the greatest opportunity for improving the temperature and humidity field by in situ instruments is from an expansion of AMDAR to more airlines and aircraft.  
If there is an eventual wider deployment of tropospheric and boundary layer wind profilers, additional vertical profiles may be obtained from RASS over limited populated areas.

The future is not only in developing one method of measurement, but  by combining existing and future sources (AMDARs, radiosoundings, wind profilers, Weather radars, satellites, ..) in order to get the best possible view of the phenomena and their evolution in the short term.

- Precipitation

Precipitation is measured with adequate accuracy by automated and manual rain gauges, except for frozen precipitation or small scale convection.  Advanced scanning radars can estimate accumulated precipitation to within about 50% accuracy, but this can be substantially improved through real-time calibration with rain-gauge networks.  Supplemental reports of accumulated precipitation are often provided on an event-driven basis by large numbers of non-professional cooperative observers reporting to nearby meteorological offices.  This near real-time reporting can fill horizontal resolution gaps and be helpful in flash-flood forecasting.

#### - The special case of tropical cyclones

Geostationary satellites provide vital information on the location of a tropical cyclone with a good temporal resolution and a good horizontal coverage; the availability of such information all over the tropical belt is essential.  Polar orbiting satellites provide more detailed information on tropical cyclones, but at a coarser temporal resolution.  For the surface, wind scatterometers are most useful.  They also provide some capability for detecting precipitation.

Ground-based precipitation radars have a good horizontal and temporal coverage around land (including islands) areas, but are absent over most oceanic regions.  They allow good monitoring of tropical cyclones and landfall, and they contribute quite significantly to nowcasting and very short range forecast, but not to their longer-term forecast.

Conventional in situ data provide marginal coverage over tropical cyclones, but measure MSLP with a good accuracy (one of the essential parameters of a tropical cyclone); they also provide measurements of wind with good accuracy.

Targeted observations like dropsondes have been used for tropical cyclones, and have proved to be very useful not only for NWP usage but also for direct use by forecasters.

Summary of Statement of Guidance for Nowcasting and VSRF

Nowcasting primarily consists of analyzing observational data to make diagnoses and mostly extrapolative-based forecasts from a few minutes to 2 hours.  VSRFs are now often generated by regional NWP models and have a validity period up to 12 hours.  Nowcasting and VSRF cover scales from hundreds of metres to as large as 2000 km.

Nowcasting and VSRF can be applied to many phenomena including severe weather, but is most frequently used to forecast and monitor:

- 	convective storms with attendant phenomena (gust fronts, hail, intense precipitation, intense electrical activity, tornadoes);

- 	wintertime severe weather (blizzards, snowstorms, ice, avalanches, etc.);

-	mesoscale features associated with extratropical and tropical storms;

- local flows or circulations (breeze, foehn, low level jets, convergence lines, dry lines, boundaries, intersection of boundaries, etc.);

- fog and low clouds;

- locally forced precipitation events;

- sand and dust storms;

- wild fires.

Key nowcasting and VSRF parameters for which observational data are required are:

- clouds and precipitation;

- 3-D wind field;

- 3-D humidity field;

- 3-D temperature field;

- surface variables: pressure, wind, temperature, humidity, present weather, visibility and precipitation accumulation, snow layer, land cover or structure;

- dust;

Well-defined high spatial and temporal resolution multi-spectral imagery from space is providing important immediate benefits to nowcasting phenomena such as areas of cloud, fog, dust, fires, and severe convective weather.

While few in number, scanning weather radars (especially Doppler) provide excellent information critical to improving nowcasting and VSRF of convective and stratiform precipitation with their potential for localised flash floods, tornadoes, hail, and high winds.

The resolution of the radar data depends on the density of the networks, but also on the frequency of the scanning observations and the volume coverage pattern chosen. The resolution of the radar and nowcasting products displayed to the user depends on the telecommunications and computing capacities. So, even if high resolution data and detailed products are available or possible at the acquisition and data processing level, in general and particularly in developing countries,  there are insufficient computing and communication resources to transmit and display these products in real-time to the end- user.

For frequently updated fields of 3-D wind and temperature important for nowcasting and VSRF, the increasing number of AMDAR observations provide high resolution wind and temperature data at the tropopause level, and composites of radio-soundings, wind profilers, weather radars VAD and AMDARS provide tropospheric wind observation over populated regions.

Doppler wind profilers have proven valuable for nowcasting and VSRF because they provide high vertical and temporal resolution as a complement to other upper-air observing systems.

Lightning detection systems, for cloud-to-cloud and / or cloud-to-ground lighting, are important for convective electrical activity monitoring and bring unique information about storms structure and evolution.

Rapid imaging (on the order of minutes) is critical for nowcasting, and is increasingly available from geostationary satellites.  With some systems, the rapid scan for small areas competes with the scanning requirements for broad coverage.

Reliable and accurate precipitation estimates still pose problems; however, they will benefit from continuing enhancements to satellite measurement capabilities over unpopulated regions.

NWP models are the most important tool for short range prediction, leading to a strong dependence on the same data as identified as sources for NWP.  Thus, the SOG for global and regional NWP applies for SRP as well.  Information that best complements these data is found in satellite imagery and weather radar data; their usage is further supported by their good temporal and spatial resolution.  Surface data, because of their good representation of the conditions where people are living, are also essential.  There still is concern for oceanic areas, where significant phenomena such as cyclogenesis occur, but surface-based data are sparse.  Another concern is the quality of cloud cover and base height estimates in remote areas, and especially during the night, some progress is expected in this area from new satellite sensors over the next decade.

Summary of gaps

Wind field and wind shear data do not have yet the needed resolution for aeronautical meteorology in all places but use of composite systems could overcome this gap. In some locations the coverage of the radar observations can have gaps due to  the geometry of the radar observations (overshooting of the radar beam above low level precipitation cores) but also due to orographic blocking, making it difficult to provide complete azimuthal coverage out to the full range of the radar.   Good coverage is required in weather sensitive areas, such as airports, harbours and cities.

Snow depth data and fresh snow layer spatial and temporal resolution are not sufficient for urban areas. Snow profile of the snow-pack is done only in few mountain stations.

The horizontal resolution of most surface variables and phenomena needed for nowcasting and VSRF is acceptable in populated area but marginal to absent in unpopulated areas and above seas.

Operational radar systems needed for nowcasting are still missing in less developed and developing countries; low cost nowcasting systems and technologies based on satellite data could be applied to these countries from developed ones.

Cross border radar and lightning data exchange is difficult for some countries that do not have a memorandum of understanding or protocols for these exchanges.

Radar data and lightning data belonging to other bodies than met services (private companies, agencies, utilities etc) are missing from the national or regional public integrated products.

Developing parallel exclusive networks for electrical activity and radar monitoring is not an efficient way to use national resources; these networks should be integrated for better monitoring of severe weather.

Additional meteorological data can be obtained from wind farms poles.

Rapid imaging is not yet fully available for all geostationary satellites. Some of the derived satellite parameters relevant for severe weather monitoring (like air mass instability) are not yet calibrated for specific regions and thus have only qualitative value.

Data resolution in polar areas is marginal. The temporal resolution of satellite microwave imagers needed for liquid water and precipitation is marginal. The accuracy of these data can be validated only over populated areas where radar data and rain gauges are available.

Non-professional cooperative observers of high impact meteorological events (like mesurements of rain accumulation in flash floods cases, or spotters of tornadoes, strong winds, or large hail fall) exists only in some developed countries.

Wind data coverage in polar regions is in general absent.

Actions to fill the gaps

- Data Quality and Quantity

  - The resolution of the radar data depends on the density of the networks, but also on the frequency of the scanning observations and the volume coverage pattern chosen, and also the resolution of the products displayed depends on the telecommunications and computing capacities; improving the density of these networks and enhancing the capacities for telecommunications and computing is recommended.

  - More radars should be installed mainly in the sensitive areas (airports, harbours and cities). The coverage of the radar observations: the geometry of the radar observations (overshooting of the radar beam above the precipitation cores) and also the limitations due to the orography blocking make it difficult to provide complete low level coverage.

  - Use of QC/QA techniques and recording metadata ( with reference to the WMO WIGOS and RRR tables currently under construction: www.wmo-sat.info/db )

  - To recommend “opening” of data if the data belong to private companies, at least in case of “significant events”.

  - To make a larger use of specific observation networks data (pollution, military, wind farms, forest etc).

- Future Development

  - To extend the use of hybrid systems to derive values of important parameters (e.g., the wind can be derived also from Doppler weather radar - VAD radar products, or rain can be estimated with satellite in remote areas);

  - To develop non-professional alternative observations networks like trained spotters network, meteorological observations performed in schools, cell phones, web cameras, etc.

  - To avoid the spread of national resources in development of parallel exclusive radar and lightning networks instead of integration and enhance of the current ones.

  - To support the cross-border exchange of radar and lightning data and meteorological observation stations data in the vicinity of the borders.

  - To archive high resolution radar data for climatological studies of severe weather based on “radar objects” (i.e. climatology of supercells).

- Capacity Building for Cross Border Severe Weather Management

For public benefit and for developing countries:

k)      To install low-cost nowcasting systems  (based on satellite and NWP in regions with lack or radar data; to organize regional virtual centres of guidance in observation and forecasting severe weather and to provide free access of developing countries to severe weather products displayed on Internet.

l)       To urge state members to adopt Memorandum of Understanding and Protocols  on

regional radar data (and observational data) exchange, and to organize enhanced exchange of data during severe weather events.

_______________

# Footnotes

The retrieval of refractivity fields from Doppler weather radar using ground clutter targets is an innovative development in recent years.  It provides acceptable temporal and horizontal resolution but coverage is marginal since it relies on ground clutter targets (available only near the radar) and only over populated land areas.  Development of high density networks of small radars may improve the coverage over land.

In recent years, the extrapolation techniques have been extended with heuristic approaches to account for decay and growth of precipitation systems and also include blending with high resolution NWP.