| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS OPEN PROGRAMME AREA GROUP ON INTEGRATED OBSERVING SYSTEMS IMPLEMENTATION/COORDINATION TEAM ON INTEGRATED OBSERVING SYSTEMS Fourth Session GENEVA, 11-15 SEPTEMBER 2006 |  | CBS/OPAG-IOS/ICT-IOS-4/Doc.4.1 (11.IX.2006) Add.1 ____________ ITEM: 4.1 Original: ENGLISH |
| --- | --- | --- |

REVIEW OF THE STATUS OF THE SPACE-BASED COMPONENT OF THE GOS

(Submitted by the WMO Secretariat)

Summary and Purpose of Document

This addendum provides an update on the status of the space-based component of the Global Observing System, extracted from the report of the second meeting of the Expert Team on Satellite Systems (ET-SAT-2), as well as an updated version of the tables summarizing satellite launch dates and status.

EXTRACT FROM ET-SAT 2 REPORT

Item 4: STATUS OF THE SPACE-BASED COMPONENT OF THE GOS

4.1	Mr Lu Naimeng presented an update on the status and plans of FY-1, -2, -3 and FY-4 series of meteorological satellites of CMA.  The currently operational satellites are FY-1D, a polar-orbiting spacecraft on a morning orbit (08:20 D) with a 10 channel Visible-Infrared radiometer, and FY-2C, a geostationary spacecraft located at 105°E with a 5-channel Visible-Infrared radiometer.  The future generation of polar-orbiting satellites will start with the satellites FY-3A, planned for launch in 2007, and FY-3B, in 2009, that would be flying on a morning and afternoon orbit respectively, and would include 11 instruments.  They would be followed by an operational series with improved sounding and imaging capabilities.  On the geostationary orbit, the operational configuration will soon include 2 satellites with FY-2C at 105°E and FY-2D at 86.5°E  providing a back-up capability.  The next generation of geostationary satellites will include an optical series starting with FY-4A to be launched in 2012 and a microwave series starting with FY-4B to be launched after 2015.  In addition to Direct broadcast, data dissemination is supported by a  DVB-S service over China and there are plans for extending the coverage of this service at the regional scale.

  - Mr Gao Jun reported on the status of current and approved satellites of the Chinese National Space Administration (CNSA) contributing to the GOS.  This included:

- the Chinese-Brazilian CBERS series with CBERS-02 being currently operational and follow-on satellites planned for launch in 2007 and 2009,

- the HY-1B satellite to be launched in 2006 to monitor ocean colour and temperature and coastal environment,	
- the HJ environment and disaster monitoring satellite constellation  HJ-1 (-A,-B,-C) to be launched in 2007/2008.

4.3	Mr A.S. Kiran Kumar gave a presentation on the Earth Observation programme of the Indian Space Research Organization (ISRO) in support of weather and climate studies.  On the geostationary orbit, after the INSAT-1 and INSAT-2 series, the currently operational satellites are INSAT-3A and Kalpana1.  The future INSAT-3D, to be launched in 2007, will include an 18-channel IR sounder.  As concerns the Low Earth Orbit satellites, ISRO currently operates Oceansat-1 for ocean monitoring, Resourcesat-1 for land monitoring, and Cartosat-1 for high-resolution stereo imagery.  Oceansat-2 is planned for launch in 2007/2008, and will include an ocean colour sensor, a radio-occultation sounder and a scatterometer. Resourcesat-2 is planned for 2008/2009. The ISRO-CNES Megha-tropiques satellite would be launched in 2009 on a low-inclination orbit to contribute to monitor water cycle and energy budget in tropical regions.

4.4	Mr T. Hashimoto summarized the status and plans of JMA for geostationary satellites.  MTSAT-1R is fully operational and provide geostationary coverage at 140°E with full-disc 5-channel imagery every hour and additional half disc images.  MTSAT- 2 is now available at 140° E with the capability to provide back-up for MTSAT-1R and to replace it in 2010.  In the meantime, this capability can be used for supplementary observations in support of scientific campaigns.  ET-SAT could view the development of a typhoon with a 1-minute time step rapid-scan obtained from MTSAT-2.  Dissemination in HRID and WEFAX  will be maintained in parallel with HRIT/LRIT until 2007 to facilitate transition for the users.  MTSAT follow-on is being prepared for 2013/2015.

4.5	The Chairman invited Mr Jérôme Lafeuille to present the information provided by NOAA on the Nunn-Mc Murdy certification process that had determined a revision of the NPOESS programme.  The revised NPOESS baseline would include in total 4 satellites, two of them ensuring continuity on a 13:30 (A) afternoon orbit, and the other two on a 17:30 (A) early morning orbit.  In terms of meteorological payload, the first afternoon spacecraft would include advanced imagery and sounding package, plus one Earth Radiation Budget and one Ozone monitoring instrument.  The early-morning one would include a Visible-Infrared Imager and a Multi-polarisation microwave imager.  Furthermore, the risk reduction mission NPP satellite would be launched at the end the 2009 on an afternoon orbit.

4.6	All these updates, together with the input received from ESA, EUMETSAT and NASA prior to the meeting, allowed ET-SAT to update the Tables of current and future LEO/GEO/R&D satellites  […].

SUMMARY TABLES ON CURRENT AND PLANNED SATELLITE MISSIONS 
CONTRIBUTING TO THE GLOBAL OBSERVING SYSTEM

(updated as of  8 September 2006)

The following tables are included:

- Current Operational Low Earth Orbit Satellites within the WMO Global Observing System

- Current Operational Geostationary Satellites within the WMO Global Observing System

- Current R & D satellites within the WMO Global Observing System

- Future Operational Low Earth Orbit Satellites within the WMO Global Observing System

- Future Operational Geostationary Satellites within the WMO Global Observing System

- Future R & D satellites within the WMO Global Observing System

Current Operational Low Earth Orbit Satellites within the WMO Global Observing System

Equator Crossing Time (if sun-synchronous orbit):  A= ascending (Northward), D=descending (Southward)

Updated on 8 September 2006

| Orbit type | Satellites (+operation mode) P=Pre-operational Op=operational B=back-up L=limited availability | Operator | Equator Crossing Time (ECT) | Mean Altitude | Launch date | Status |
| --- | --- | --- | --- | --- | --- | --- |
| Sun-synchronous “Morning” orbit E.C.T. between (6:00 – 12:00) and (18:00 – 24:00) | NOAA-17 (Op) | USA/NOAA | 10:24 (D) | 810 km | 6/02 | Functional. AMSU-A1 Failed. |
|  | NOAA-15 (B) | USA/NOAA | 05:58 (D) | 807 km | 05/98 | Functional (intermittent problems with AVHRR, AMSU-B & HIRS) |
|  | NOAA-12 (L) | USA/NOAA | 04:55 (D) | 804 km | 05/91 | Functional (except sounding). |
|  | DMSP-F16 (Op) | USA/NOAA | 20 :13 (A) |  | 10/03 | Defense satellite. SSMIS Data available to civilian users through NOAA. |
|  | DMSP-F15 (B) | USA/NOAA | 20:41 (A) | 850 km | 12/99 | Defense satellite. SSMT2 non-functional. Data available to civilian users through NOAA. |
|  | DMSP-F14 (B) | USA/NOAA | 18:36 (A) | 852 km | 04/97 | Defense satellite. SSMT1and SSMT2 (microwave temperature and humidity sounder) non-functional. Only 1 functional onboard recorder. Data available to civilian users through NOAA. |
| Sun-synchronous “Afternoon” (12:00 –16:00) and (00:00 – 04:00) | NOAA-18 (Op) | USA/NOAA | 13:55 (A) | 854 km | 5/05 | Functional. Noise on HIRS long wave channels |
|  | NOAA-16 (B) | USA/NOAA | 14:11 (A) | 850 km | 09/00 | Functional, no APT. Intermittent problems with AVHRR. |
|  | NOAA-14 (B) | USA/NOAA | 19:30 (A) | 845 km | 12/94 | Functional. AVHRR and SBUV degraded. |
| Sun-synchr. “Early morning” (4:00 - 6:00) and (16:00 – 18:00) | DMSP-F13 (Op) | USA/NOAA | 18:33 (A) | 850 km | 03/95 | Defense satellite. On orbit 125 months – estimate 7 months of mission life remaining. Data available to civilian users through NOAA. |
|  | FY-1D (Op) | China/CMA | 08:20 (D) | 866 km | 5/02 | Functional. CHRPT |

#### Current Operational Geostationary Satellites within the WMO Global Observing System

#### Updated 8 September 2006

| Sector | Satellites currently in orbit (+mode) P: Pre-operational Op: Operational B: Back-up L: Limited availability | Operator | Location | Launch date | Status |
| --- | --- | --- | --- | --- | --- |
| West –Pacific (108° E-180° E) | MTSAT-1R (Op) | JAPAN | 140°E | 26/02/05 | Fully Functional |
|  | MTSAT-2 (B) | JAPAN | 145° E | 18/02/06 | Back-up to MTSAT-1R until 2010, then operational |
|  | GOES-9 (B) | USA/NOAA | 160°E | 05/95 | Dissemination is not activated |
| east -pacific (180°W-108°W) | GOES-11 (Op) | USA/NOAA | 135°W | 05/00 | Operational GOES-West position |
|  | GOES-10 (B) | USA/NOAA | 120°W | 04/97 | Inverted, solar array anomaly, DCP interrogator on back-up Plan to move to 60°W for South-America coverage by October 2006 |
| west-atlantic (108°W-36°W) | GOES-12 (Op) | USA/NOAA | 75°W | 7/ 01 | Solar X-Ray Imager anomaly 9/05 under investigation |
|  | GOES-13 (P) | USA/NOAA | 89.5°W | 05/06 | In commissioning |
| East Atlantic (36°W-36°E) | Meteosat-6 (B) | EUMETSAT | 10°E | 11/93 | Rapid Scanning Service. Minor gain anomaly on IR imager |
|  | Meteosat-7 (B) | EUMETSAT | 0° | 02/97 | To be relocated at 57.5°E |
|  | Meteosat-8 (Op) | EUMETSAT | 3.4°W | 28/08/02 | EUMETCast, no LRIT |
|  | Meteosat-9 (P) | EUMETSAT | 6.5°W | 21/12/05 | In commissioning, then at 0° |
| Indian Ocean (36°E-108°E) | Meteosat-5 (Op) | EUMETSAT | 63°E | 03/91 | IODC, functional but high inclination mode |
|  | GOMS-N1 (B) | RUSSIA | 76°E | 11/94 | Since 9/98 in stand-by |
|  | FY-2C (Op) | CHINA/CMA | 105(E | 19/10/04 | Functional |
|  | INSAT 3-C | INDIA | 74°E | 24/01/02 | No meteorological payload. Used for dissemination of processed meteorological data in broadcast mode in S-Band only over India and neighbouring countries. No WEFAX broadcast capability in L-band. |
|  | Kalpana-1 (Op) (METSAT) | INDIA | 74°E | 12/09/02 | Dedicated meteorological satellite. |
|  | INSAT-3A (Op) | INDIA | 93.5°E | 10/04/03 | Operationalisation date: 24/04/03. A 3 channel VHRR imager and CCD payload available for use similar to INSAT-2-E. |

Current R & D satellites within the WMO Global Observing System

sorted in alphabetical space agency order

Equator Crossing Time (if sun-synchronous orbit):  A= ascending (Northward), D=descending (Southward)

Updated 8 September 2006

| Satellites | Space Agency | Equator Crossing Time + Altitude | Launch date | Instruments | Status, applications and other information |
| --- | --- | --- | --- | --- | --- |
| CBERS-02 | CNSA + AEB | 10:30 (D) 778 km | 10/2003 | CCD camera, IRMSS, WFI | China-Brazil cooperation satellite for land monitoring |
| PARASOL | CNES | 13 :32 (A) 705 km | 18/12/04 | POLDER | Characterisation of clouds and aerosols microphysical and radiative properties. Data can be accessed for level 1 at <http://parasol-polder.cnes.fr/> and for level 2 and more at <http://www-icare.univ-lille1.fr/> |
| SPOT-5 | CNES | 10:30 (D) 832 km | 05/2002 | DORIS, HRG, HRS, VEGETATION | Cartography, land surface, agriculture and forestry, civil planning and mapping, digital terrain models, environmental monitoring |
| ERS-2 | ESA | 10:30 (D) 785 km | 04/95 | Altimeter, SAR, SAR-wave, ATSR, Scatterometer, GOME | Due to OB recorder problems in 06/03, the LBR mission is ensured over ESA agreed acquisition stations Operations extended till 2008. |
| ENVISAT | ESA | 10:00 (D) 800 km | 03/2002 | ASAR, RA-2 AATSR, MERIS GOMOS, MIPAS MWR, SCHIAMACHY | MIPAS is operated in discontinuous scenario. GOMOS performs regularly with reduced azimuth range since 29 august 2005. RA has experienced some anomalies since Feb 2006 Operations extended 3 years (till 2010) |
| PROBA | ESA | 10: 30 ( D) 615 km | 10/2001 | CHRIS | Drifting orbit. Technology experiment. AO Science mission since 2003. |
| Oceansat-1 | ISRO | 12:00am D 723 km | 05/1999 | OCM, | Ocean and land monitoring + MSMR operational in 1999-2002 |
| Resourcesat-1 | ISRO | 10:30 (D) 817 km | 10/2003 | AWIFS | Land monitoring 4 channel camera |
| Cartosat-1 | ISRO | 10:30 (D) 618 km | 05/2005 | Carto-dem | High resolution stereo imagery 2 Panchromatic cameras |
| ALOS | JAXA | 10:30 (D) 700km | 24/01/06 | ALOS | Advanced Land Observing Satellite (mapping, precise land coverage observation, disaster monitoring, resource surveying) |
| TRMM | JAXA/ NASA | non-sun-synchronous (35° incl) 402 km | 28/11/97 | PR (Precipitation Radar) TMI (TRMM MW Imager) CERES, VIRS LIS (Lightning Imaging Sensor) | Measures tropical rainfall/precipitation and radiation energy Precipitation Radar (PR) provided by JAXA Satellite bus and other instruments provided by NASA CERES no longer functional |
| EP-TOMS | NASA | 12 :00am(D) 740 km | 02/07/96 | Total Ozone Mapping Spectrometer | (Total Ozone Mapping Spectrometer - Earth Probe) measures total column ozone and its variation on a daily basis |
| Landsat 7 | NASA | 10:05 (D) 705 km | 15/04/99 | ETM+ (Enhanced Thematic Mapper Plus ) | well-calibrated, multispectral, moderate resolution, substantially cloud-free, sunlit digital images of the Earth's continental and coastal areas and selected coral reefs |
| QuikSCAT (Quick Scatterometer) | NASA | 06:00 (A) 803 km | 19/06/99 | SeaWinds | Sea surface wind speed and direction data for global climate research and operational weather forecasting and storm warning |
| Terra | NASA | 10 :30 (D) 705 km | 18/12/99 | CERES, MISR, MODIS, MOPITT, ASTER | Measurement of Earth' climate system, atmosphere, land, oceans and interactions with solar radiation |
| ACRIMSAT | NASA | 10 :50 (D) 720 km | 20/12/99 | ACRIM 3 | Active Cavity Radiometer Irradiance Monitor Satellite measures total solar irradiance |
| NMP EO-1 (New Millennium Program Earth Observing-1) | NASA | 10 :01 (D) 705 km | 21/11/00 | Advanced Land Imager, Hyperion, LAC(atmospheric corrector) | demonstrates and validates advanced technology instruments (multi and hyperspectral), spacecraft systems, and mission concepts in flight |
| Jason-1 | NASA/ CNES | non-sun-synchronous (66° incl) 1336 km | 07/12/01 | LRA (Laser retroreflector array) Poseidon-2 solid state radar altimeter, DORIS receiver , Jason Microwave Radiometer , BlackJack GPS Receiver | Ocean surface topography follow-on mission to TOPEX/Poseidon. Monitors global ocean circulation for global climate prediction |
| GRACE (Gravity Recovery and Climate Experiment) | NASA/ DRL | non-sun-synchronous (89°incl) 485 km | 17/03/02 | - Star Camera Assembly - GPS BlackJack Receiver - Instruments Processing Unit - Laser Retro-Reflector Assembly - K-Band Ranging Instruments - SuperSTAR Accelerometers | accurate global and high-resolution determination of static and time-variable components of Earth's gravity field measurement of: Gravitational field GPS atmospheric and ionospheric limb sounding |
| Aqua | NASA | 13:30 (A) 705 km | 04/05/02 | AMSR-E, AIRS, HSB, AMSU-A, CERES, MODIS | collects data on Earth's water cycle, precise atmospheric, land and oceanic measurements, and interaction with solar radiation AMSR-E provided by JAXA. HSB provided by INPE (no longer functional) |
| ICESat (Ice, Cloud, and Land Elevation Satellite) | NASA | Circular non sun-synchronous (94° incl) 600 km | 12/01/03 | GLAS (Geo-science Laser Altimeter System), GPS BlackJack receiver | measures ice sheet topography, ice sheet elevation changes, cloud and aerosol heights, land topography and vegetation characteristics. |
| SORCE (Solar Radiation and Climate Experiment) | NASA | non-sun-synchronous (40° incl) 640 km | 25/01/03 | - XPS (Extreme Ultraviolet (XUV) Photometer System) - TIM (Total Irradiance Monitor) - SIM (Spectral Irradiance Monitor A&B) - SOLSTICE (Solar Stellar Irradiance Comparison Experiment A&B) | Provides total solar irradiance measurements and full solar spectral irradiance measurements. Continuation of ACRIMSAT total solar irradiance measurements. |
| Aura | NASA | 13:45 (A) 705 km | 15/07/04 | HIRDLS, MLS (Microwave Limb Sounder), OMI (Ozone Monitoring Instrument), TES | Comprehensive measurements of atmospheric chemistry and trace gasses : HIRDLS = High Resolution Dynamic Limb Sounder (IR) TES = Tropospheric Emission Spectrometer |
| CALIPSO | NASA/ CNES | 13 :30 (A) 705 km | 28/04/06 | CALIOP, WFC, IIR | Cloud-Aerosol Lidar and Infrared Pathfinder Satellite Observations for climate predictions |
| CloudSat | NASA/ CSA | 13:30 (A) 705 km | 28/04/06 | Cloudsat Profiling Radar (CPR) | global cloud properties (applications: air quality, aviation safety, disaster management, energy and water management) |
| Monitor-E | Russia | 10:30 550 km | 27/08/05 | Land Observing Satellite | Surface mapping, support to disaster management and monitoring the effects of pollution. Two optical cameras. |

Future Operational Low Earth Orbit Satellites within the WMO Global Observing System

Updated 8 September 2006

| Orbit type | Future Satellites | Operator | Equator Crossing Time | Altitude | Planned launch date | Other information |
| --- | --- | --- | --- | --- | --- | --- |
| Sun-synchronous Morning ECT in (6:00 – 12:00) and (18:00 – 24:00) | METOP-A | EUMETSAT | 09:30 D | 837 km | 10/2006 | AHRPT |
|  | METOP-B | EUMETSAT | 09:30 D | 837 km | 2011 | AHRPT |
|  | METOP-C | EUMETSAT | 09:30 D | 837 km | 2015 | AHRPT |
|  | FY-3A | CHINA/CMA | 10:20 D | 836 km | 2007 | AHRPT/MPT |
|  | METEOR M-N1 | RUSSIA | 10:20 A | 830 km | 2006 | AHRPT |
|  | METEOR M-N2 | RUSSIA | 10:20 | 830 km | 2008 | AHRPT |
|  | DMSP F-18 | USA/NOAA | 08:00 (D) | 833 km | 03/2008 | SSMI/S |
| Sun-synchr. Afternoon (12:00 – 16:00) (00:00 – 04:00) | FY-3B | CHINA/CMA | 14:00 A | 836 km | 2009 | AHRPT/MPT |
|  | NOAA-N’ | USA/NOAA | 14:00 A | 850 km | 2009 |  |
|  | NPP (NPOESS Preparatory Project) | USA NOAA/NASA | 13:30 A | 833 km | 2009 | VIIRS, CrIS, ATMS, OMPS/Nadir |
|  | NPOESS-C1 | USA/NOAA | 13:30 A | 833 km | 2013 | VIIRS, CrIS, ATMS, CERES,OMPS/N |
|  | NPOESS-C3 | USA/NOAA | 13:30 A | 833 km | 2020 | VIIRS, CrIS, ATMS, Mw imager OMPS/N |
| Sun-synchr. Early morning (4:00 - 6:00) (16:00 – 18:00) | DMSP-S17 | USA/NOAA | 17:30 (A) | 833 km | 2006 | (SSMI/S) |
|  | DMSP-S19 | USA/NOAA | 17:30 (A) | 833 km | 10/2010 | (SSMI/S) |
|  | DMSP-S20 | USA/NOAA | 17:30 (A) | 833 km | 10/2012 | (SSMI/S) |
|  | NPOESS-C2 | USA/NOAA | 17:30 A | 833 km | 2016 | VIIRS, Mwimager |
|  | NPOESS-C4 | USA/NOAA | 17:30 A | 833 km | 2022 | VIIRS, Mwimager |
| Non sun-synchr. | JASON-2 (Ocean Surface Topography Mission) | NASA/NOAA/ EUMETSAT/ CNES | (66° inclin.) | 1336 km | 06/2008 | follow-on of Jason-1 sea surface topography measurement |

Future Operational Geostationary Satellites within the WMO Global Observing System

Updated 8 September 2006

| Sector | Future additional satellites | Operator | Planned location | Planned launch | Other remarks |
| --- | --- | --- | --- | --- | --- |
| East Pacific (180°W-108°W) and West Atlantic (108°W-36°W) | GOES-O | USA/NOAA | 135° W or 75° W | 2007 (TBC) |  |
|  | GOES-P | USA/NOAA | 135° W or 75° W | 2008 |  |
|  | GOES-R | USA/NOAA | 135° W or 75° W | 2014 | ABI,GLM, SIS, SEISS Advanced Baseline Imager Geostationary Lightning Mapper Solar Imaging Suite Space Environment In-Situ Suite |
|  | MSG-3 | EUMETSAT | 0° | 2011 |  |
|  | MSG-4 | EUMETSAT | 0° | 2012 |  |
| Indian Ocean (36°E-108°E) | Electro-L N1 | Russia | 76°E | 2007 |  |
|  | Electro-L N2 | Russia | 76°E or 14.5°E (TBC) | 2010 |  |
|  | Electro-L N3 | Russia | 76°E or 14.5°E (TBC) | 2015 |  |
|  | INSAT-3D | India | TBD | Q4 2007 | Dedicated Meteorological mission with improved 6-channel Imager and 19-channel Sounder. |
|  | FY-2D | China/CMA | 86.5 E | 2006 | 5 channel VISSR, LRIT |
|  | FY-2E | China/CMA | 123 E | 2009 | 5 channel VISSR, LRIT |
|  | FY-2F | China/CMA | 86.5 E | 2011 | 5 channel VISSR, LRIT |
|  | FY-2G | China/CMA | 123 E | 2013 | 5 channel VISSR, LRIT |
| West Pacific (108°E- 180°E) | COMS | Korea/KMA | 128.2° E | 2008 | 5 channel HRIT/LRIT |
|  | MTSAT follow-on | JAPAN | 140° E | 2015 |  |

Future R & D satellites within the WMO Global Observing System

(Updated 8 September 2006)

(by planned launch dates. Equator Crossing Time:  A= ascending (Northward), D=descending (Southward))

| Satellites | Space Agency | Equator Crossing Time + Altitude | Launch date | Status, applications and other information |
| --- | --- | --- | --- | --- |
| Kompas-2 | Russia | 400-550 km 79( incl | Q2 / 2006 | Monitoring of anomaly phenomena in the Earth ionosphere |
| Baumanets | Russia | (11:30) 490-500 km | 2006 | Land observing satellite |
| Resurs-DK | Russia | 350 km | 2006 | Land Observing Satellite |
| GOCE | ESA | 250 km (dawn-dusk) | 05/2007 | Gravity mission |
| SMOS | ESA | 6:00 (A) 755 km | 09/2007 | Salinity & Soil moisture |
| CBERS-2B | CNSA + AEB | 10:30 (D) 778 km | 2007 | China-Brazil cooperation Land monitoring CCD camera, WFI |
| HY-1B | CNSA | 10:30 (D) 798 km | 2006 | Ocean monitoring CCD camera, OCTS |
| HJ-1A | CNSA | 10:30 (D) 650 km | 2007/ 2008 | Land monitoring CCD camera Hyperspectral camera |
| HJ-1B | CNSA | 10:30 (D) 650 km | 2007/ 2008 | Land monitoring CCD camera IR camera |
| HJ-1C | CNSA | 6:00 (D) 500 km | 2007/ 2008 | Land monitoring S-band SAR |
| Oceansat-2 | ISRO | 12:00 am (D) | 2007/ 2008 | OCM(ocean colour), ROSA (Radio-occultation) , Scatterometer |
| GOSAT | JAXA & Japan’s Ministry of Environment | 13:00 666km | 08/2008 | Greenhouse Gases Observing Satellite monitoring the distribution of the density of carbon dioxide |
| ADM-Aeolus | ESA | 18:00 (A) 405 km | 09/2008 | Wind profile by Lidar |
| OCO | NASA | 13 :15 (A) 705 km | 09/2008 | Orbiting Carbon Observatory (observations of atmospheric carbon dioxide) 3 grating spectrometers |
| Glory | NASA | 13:30 (A) 705 km | 12/2008 | in framework of Climate Change Research Initiative (CCRI) global distribution of natural and anthropogenic aerosols Airborne Polarimeter Sensor (APS) Total Irradiance Monitor (TIM) |
| Resourcesat-2 | ISRO | 10:30 (D) 817 km | 2008/ 2009 | Land monitoring AWIFS 4-channel camera |
| Aquarius | NASA/ CONAE | 6:00 657 km | 03/2009 | Global sea surface salinity (SSS): L-band Radiometer (LBR) and Scatterometer (LBS) |

| Satellites | Space Agency | Equator Crossing Time + Altitude | Launch date | Status, applications and other information |
| --- | --- | --- | --- | --- |
| Megha-Tropiques | ISRO (+CNES) | Non sun-synchronous (20° incl) 870 km | 2009 | Monitoring convective systems, water cycle and energy budget in tropical atmosphere MADRAS (microwave imager), SAPHIR (humidity microwave sounder) 183 GHz, SCARAB (outgoing radiative flux at TOA) |
| CRYOSAT-2 | ESA | 717 km (92° incl) | 03/2009 | Polar ice monitoring (replacing CRYOSAT-1 lost on launch failure in October 2005) |
| CBERS-3 | CNSA + AEB | 10:30 (D) 778 km | 2009 | Land monitoring CCD camera, IRMSS, WFI |
| LDCM Landsat Data Continuity Mission | NASA/US Geological Survey | 828 km (at equator) sun-synchronous | 07/2010 | Extension of Landsat record of multispectral 30m resolution |
| GPM (core-satellite) | NASA/ JAXA | 407 km Non sun-synchronous (65° incl) | 12/2012 | Global Precipitation Measurement, follow-on and expanded mission of the current TRMM |
| EarthCare | ESA-JAXA | 10:30 (D) 450 km | 12/2012 | ATLID, BBR, CPR, MSI . Cloud, radiation and aerosol interaction processes |