| WORLD METEOROLOGICAL ORGANIZATION _____________________________ WMO INTEGRATED GLOBAL OBSERVING SYSTEMS (WIGOS) PILOT PROJECT FOR AMDAR, Fifth Session & AMDAR Panel Management Group Meeting DE BILT, THE NETHERLANDS, 28 FEBRUARY – 4 MARCH 2011 |  | WIGOS-PP-5-AMDAR-MG/Doc.2.1(1) (21.II.2011) __________ ITEM: 2.1 Original: ENGLISH ONLY |
| --- | --- | --- |

STATUS OF THE WIGOS PILOT PROJECT FOR AMDAR

AMDAR BUFR Template

(Submitted by Stewart Taylor)

Summary and Purpose of Document This document presents the current status of the AMDAR BUFR Template.

ACTION PROPOSED

The Meeting is invited to:

(a)	Note the current status of the AMDAR BUFR Template; and,

(b)	Comment and make recommendations as appropriate.

___________________

AMDAR BUFR Template

- The Joint Meeting of the Thirteenth Session of the AMDAR Panel Meeting and the Second Session of the Expert Team of Aircraft-Based Observations discussed the outcomes from the WIGOS Ad-Hoc Meeting in Geneva, Switzerland in August 2010 that was tasked with revising the ARINC620v4 Specification; see Appendix A for the revised Downlink and Appendix B for Uplink Message Formats. The joint Meeting decided that following the recommendations from the 5th WIGOS PP for AMDAR that the newly developed standardized AMDAR BUFR Template version 4, see Appendix C, will require some additional modification before it can again be passed to the Inter-Programme Expert Team on Data Representation and Codes (IPET-DRC). One of the major recommendations from the 5th WIGOS PP for AMDAR Meeting was that the new AMDAR BUFR Template should revert back to PALT rather than use Pressure as the primary height field.

- Following the finalization of the newly developed standardized AMDAR BUFR Template version 5 the template would go through a validation process by two operational AMDAR Programs and two independent processing centers. Approval would then be sought from the IPET-DRC, the Chairperson of the OPAG-ISS and the president of the CBS before the new BUFR Template would be declared preoperational (it is expected to be accomplished by mid 2011).

- Following on from the WMO AMDAR Panel and E-AMDAR representation to AEEC DataLink Systems Sub-Committee in July 2010, revision of the ARINC620v4 Specification has been initiated. This takes the form of an amendment request under an AEEC process called API/M (ARINC Project Initiation/Modification). An example of the API/M Form is included in Appendix D. Once the API/M has been received by AEEC DataLink Systems, it is forwarded to AEEC General Session for approval. The opportunity to present the revision to AEEC General Session did not arise in 2010 and the Mid Term Session for 2011 was also missed due to timings of meetings. The next opportunity to put forward an API/M will be the 2011 General Session scheduled for April 18-21st at FedEx Memphis.

_________

DOWNLINK MESSAGE TEXT FORMATS

Format of the Meteorological Report Messages should be as follows:

ARINC 620, Table 5.3.13.2-1 — Ascent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Message Header |  |  |
| 11-12 | 2 | Version Number | 02 |  |
| 13 | 1 | Type of Met Format | A, E, D | 2 |
| 14-15 | 2 | Date Message Assembled | dd |  |
| 16-19 | 4 | Time Message Assembled | hhmm |  |
| 20-23 | 4 | Departure Station | xxxx |  |
| 24-27 | 4 | Destination Station | xxxx |  |
| 28-29 | 2 | Parameter configuration | nn |  |
| Initial report: |  |  |  |  |
|  | 7 | Latitude | ADDMM ss | 3 |
|  | 8 | Longitude | ADDDMMss | 4 |
|  | 2 | Date of Observation |  | dd |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | GNSS Altitude | nnnn |  |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 5 | WV Mixing Ratio | nnnnQ | 9 |
| Series #1 |  |  |  |  |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | GNSS | nnnn |  |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 5 | WV Mixing Ratio | nnnnQ | 9 |
|  | 4 | True air speed vector | nnnn |  |
|  | 4 | True heading | nnnn |  |
|  | 1 | De-icing | n |  |
|  | 1 | Aircraft configuration | n |  |
|  | 62 | Aerosols (Volcanic Ash) | Base 36 |  |
|  | 4 | Aerosols (Weather) | Base 36 |  |
|  | 10 | Clouds (Weather Forecast) | Base 36 |  |
|  | 14 | Airborne Chemistry | Base 36 |  |
| Delimiter | 1 | Slash </> | / | Indicates end of Series #1 data! beginning of Series #2 data |
| Series #2 |  |  |  |  |
|  | 7 | Latitude | ADDMMss | 3 |
|  | 8 | Longitude | ADDDMMss | 4 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | GNSS | nnnn |  |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 5 | WV Mixing Ratio | nnnnQ | 9 |
|  | 4 | True air speed vector | nnnn |  |
|  | 4 | True heading | nnnn |  |
|  | 1 | De-icing | n |  |
|  | 1 | Aircraft configuration | n |  |
|  | 62 | Aerosols (Volcanic Ash) | Base 36 |  |
|  | 4 | Aerosols (Weather) | Base 36 |  |
|  | 10 | Clouds (Weather Forecast) | Base 36 |  |
|  | 14 | Airborne Chemistry | Base 36 |  |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.2-2 — Enroute Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Header |  | 1 |
| 11-12 | 2 | Version Number | 02 |  |
| 13 | 1 | Type of Met Format | A, E, D | 2 |
| 14-15 | 2 | Date of Message Assembly | dd |  |
| 16-19 | 4 | Departure Station | xxxx |  |
| 20-23 | 4 | Destination Station | xxxx |  |
| Series #1 |  |  |  |  |
|  | 7 | Latitude | ADDMMss | 3 |
|  | 8 | Longitude | ADDDMMss | 4 |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 4 | Pressure Altitude | nnnn | 6 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | Roll Angle Flag | n | 8 |
|  | 5 | WV Mixing Ratio | nnnnQ | 9 |
|  | 4 | GNSS | nnnn |  |
|  | 4 | True air speed vector | nnnn |  |
|  | 4 | True heading | nnnn |  |
|  | 1 | De-icing | n |  |
|  | 62 | Aerosols (Volcanic Ash) | Base 36 |  |
|  | 4 | Aerosols (Weather) | Base 36 |  |
|  | 10 | Clouds (Weather Forecast) | Base 36 |  |
|  | 14 | Airborne Chemistry | Base 36 |  |
|  |  | End of Text | <ETX> |  |

Table 5.3.13.2-3 – Descent Weather Report Format

| Character Number | # of Char | Character Content | Format | Notes |
| --- | --- | --- | --- | --- |
| 1-10 | 10 | Standard Header |  | 1 |
|  | 2 | Version Number | 02 |  |
|  | 1 | Type of Met Format | A, E, D | 2 |
|  | 2 | Date of Message Assembly | dd |  |
|  | 4 | Departure Station | xxxx |  |
|  | 4 | Destination Stat ion | xxxx |  |
| Series #1 |
|  | 7 | Latitude | ADDMMss | 3 |
|  | 8 | Longitude | ADDDMss | 4 |
|  | 6 | Time of Observation | hhmmss | 5 |
|  | 4 | Pressure Altitude | nnnn | 4 |
|  | 4 | Static Air Temperature | annn | 7 |
|  | 3 | Wind Direction | nnn | Degrees true |
|  | 3 | Wind Speed | nnn | Knots |
|  | 1 | RolI Angle Flag | n | 8 |
|  | 5 | WV Mixing Ratio | nnnnQ | 9 |
|  | 4 | Turbulence | nnnn | 11 |
|  | 4 | GNSS | nnnn |  |
|  | 4 | True air speed vector | nnnn |  |
|  | 4 | True heading | nnnn |  |
|  | 1 | De-icing | n |  |
|  | 1 | Aircraft configuration | n |  |
|  | 62 | Aerosols (Volcanic Ash) | Base 36 |  |
|  | 4 | Aerosols (Weather) | Base 36 |  |
|  | 10 | Clouds (Weather Forecast) | Base 36 |  |
|  | 14 | Airborne Chemistry | Base 36 |  |
|  |  | End of Text | <ETX> |  |

Notes:

- See ARINC Specification 618.

- (A = Ascent, E = Enroute, D = Descent). Each type has the same order of relevant meteorological information (latitude, longitude, time, pressure (or altitude), wind direction, wind speed, roll angle flag, water vapor, turbulence) but actual information and frequency of reporting levels varies with type.

- A = N (North) or S (South), D = degrees, M = minutes, T = tenths of minutes.

- A = E (East) or W (West), D = degrees, M = minutes, T = tenths of minutes.

- h = hours, m = minutes

- Resolution in tens of feet

- The value of a is encoded either P (plus) or M (minus), un0069ts are tens, ones, tenths of a degree centigrade

- If RolI angle exceeds 5 degrees set to [B], otherwise set to [G]

- nnn = n1 n2 n3 which implies n1 . n2 x 10 ; e.g., 123 = 1.2x10-3. Q is a quality control character to be determined after contract award for WJSS.

- C is a code where if C = Z then no turbulence above threshold and no data (characters) follow; if C = Q then some data problem exists and no data (characters) follow; if C = an integer n = 0 to 9, then 4n hexadecimal characters follow where the first two characters in a group of four are the average values of the turbulence metric and the last two characters are the peak values of the turbulence metric over a one-minute period.

- nnnn: First two hexadecimal characters represent the average turbulence metric. The last two hexadecimal characters represent the peak turbulence metric.

____________

UPLINK MESSAGE TEXT FORMATS 

Table 4.3.10.1 -1 — Basic Configuration Data

| Number of characters | Data | Description | Default value | Remarks |
| --- | --- | --- | --- | --- |
| 1 | A | IMI |  |  |
| i | W | IMI |  |  |
| 1 | R | IMI |  |  |
| 2 | 04 | Version number |  |  |
| 1 | 0, 1, 9 | Enable AMDAR | 1 | 0 = disable, 1 = enable, 9 = no change |
| 1 | 0 1 9 ‘ | Inhibit reporting in selected time interval See Note 2. | 0 | 0 = disable (report through 24hrs every day), 1 = enable, 9 = no change. If enabled see Table 4.3.10-9. |
| 1 | 0, 1, 9 | Report in designated region See Note 3. | O | 0 = disable, 1 = enable, 9 = no change, If enabled see Table 4.3.10-2. |
| 1 | 0 1 9 ‘ | Airport selection See Note 4. |  | O = disable, 1 = enable, 9 = no change. If enabled see Table 4.3.10-3. |
| 1 | 0 1 9 , | Ascent selection See Note 5. | 1 | O = disable, 1 = enable. If enabled see Tables 4.3.10-5 and 4.3.10-3. If disabled and airport selection is disabled see Tables 4.3.10-6 and 4.3.10-4. 9 = no change |
| 1 | OA 9 | Enroute selection See Note 6. | 1 | = disable, 1 = enable, 9 = no change. If enabled see Tables 4-3.10-4 and 4.3.10-3. |
| 1 | 0 1 9 , | Descent selection See Note 7. | 1 | O = disable, 1 = enable. If enabled see Tables 4.3.10-7 and 4.3.10-3. If disabled see Tables 4.3.10-8 and 4.3.10-4. 9 = no change |
| 1 | 0-2 | Downlink configuration tables See Note 8. | 0 | O = do nothing, 1 = downlink Table l, 2 = downlink Tables 4.3.10-1, 4.3.10-2, 4.3.10- 3, 4.3.10-4, 4.3.10-5, 4.3.10-6 4.3.10-7, 4.3.10-8 and 4.3.10-9 (see downlink report Label H4) |
| 8 | E2 E3 E4 E5 E6 E7 E8 E9 | Extended message indicator See Note 9. | 00000000 | E2= 2 means Table 4.3.10-2 follows, O means not included (and unchanged). E.g., 03450700 means Tables 4.3.10-3, 4.3.10-4, 4.3.10-5 and 4.3.10-7 follow in that order. |
|  |  | Parameter configurationParameter configuration |  |  |
| 1 | I | Delimiter |  | End of Table 4.3.10-1 (this table) commands |

Notes:

- This table is the basic configuration table. It is the smallest message that can be uplinked and the information content is stored on board as Table 4.3.10-1. The information actually stored is determined by the commands contained in characters 6— 12. Following a complete system reset and/or initialization, Table 4.3.10-1 contains the default characters (0 or 1) corresponding to characters 6 to 12. These can be changed by the uplinked message as necessary. Uplinked commands can be made to enable or disable the appropriate functions or leave the previous command unchanged. Each character gives links to further on board data that affects the downlinked message required and, as necessary, updates to these data can be appended. Further explanation of each command follows.

- Inhibit reporting in selected time interval, if enabled, points to Table 4.3.10-9. This command allows reporting to be inhibited for a selected period in any consecutive 24-hour period. When disabled, reporting is continuous unless inhibited by subsequent commands.

- Report in designated region, if enabled, points to 
Table 4.3.10-2. Table 4.3.10-2 allows specific regions to be designated for enabling reporting or inhibiting reporting. When disabled, reports are to be made globally unless inhibited by subsequent commands.

- Airport selection, if enabled, points to Table 4.3.10-3 which allows specific airfields to be selected for enabling ascent and/or descent reports or inhibiting ascent and/or descent reporting from specific airfields. If disabled, ascent and descent reports are required in ail regions where AMDAR is enabled.

- If Ascent selection is enabled, it points to Table 4.3.10-5 that specifies the ascent reporting scheme to be followed. If disabled, it overrides ail previous commands and inhibits ail ascent reporting. However, if Airport selection is disabled also, routine, timed reports can be enabled by reference to Table 4.3.10-6 using time intervals designated in Table 4.3.10-4. if Ascent selection is disabled and Airport selection is enabled it points to Table 4.3.10-3 to determine if routine reports are required during ascent from designated airfields.

- Enroute selection, if disabled, overrides ail previous 
commands and disables all enroute reporting. If enabled, enroute reporting is determined according to the commands linked to characters 6,7 and 8.

- Descent selection is enabled, it points to Table 4.3.10-7 that specifies the descent reporting scheme to be followed. If disabled, it overrides ail previous commands and inhibits ail descent reporting. However, if Airport selection is disabled also, routine, timed reports can be enabled by reference to Table 4.3.10-8 using time intervals designated in Table 4.3.10-4. If Descent selection is disabled and Airport selection is enabled it points to Table 4.3.10-3 to determine if routine reports are required during descent from designated airfields.

- Downlink configuration tables, if set to O is ignored. If set to 1 the basic configuration (Table 4.3.10-1), as amended by the current message, is to be downlinked after the current uplink message has been processed. If set to 2 all configuration tables are to be downlinked after the current uplink message has been processed.

- The Extended message indicator indicates which updated configuration table data to be uplinked follows, as necessary.

Table 4.3.10.4-1 — Interval and Wind Reporting Status

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 2 | mm | Routine-level flight observing interval (mm) | Default = 07 Range = 01 —60 |
| 1 | w | Enable or disable maximum wind reporting | Default = 1 (enable) Disable = O |
| 1 | I | Delimiter | End of Table 4.3.10-4 data |

Note: This table sets the routine/enroute reporting interval. The third character (w), 
if set to the default value 1 enables maximum wind reporting during the enroute phase. If set to 0, this function is disabled.

Table 4.3.10.5-1 — Ascent Data

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | Don | Pressure level (0) or Time interval (1) selection | Ascent sampling mode Default = 1 |
| 2 | ss | Series 1 intervals (seconds) | Default = 06 (seconds) Range = 03 - 20 |
| 3 | sss | Series 1 duration (seconds) | Default = 090 Range = 030—600 |
| 2 | ss | Series 2 intervals (seconds) | Default = 20 Range = 03—60 |
| 3 | 555 | Total duration (secondsx10) | Default = 051 Range= 051 —111 |
| 3 | hhh | Top of climb (ftx100) | Default = 200 Range= 150—350 |
| 1 | 1 or 2 | Pressure target list selection | 1 = List 1, 2 = List 2 (Table 4.3.10-1 0) Default = 2 |
| 1 | 0 or 1 | Additional level flight timer for pressure-based sampling: enabled = (1), disabled = (0) | Default = 1 (Routine timer interval as defined in Table 4.3.10-4) |
| 1 | I | Delimiter | End of Table 4.3.10-5 data |

Note: This table is used when ascent reports are made. (This will be established by reference to Tables 4.3.10-1, 4.3.10-2 and 4.3.10-3). Following a complete system reset and/or initialization, the table holds the default values as given (ail of which must be stored onboard). The first character indicates whether interval selection is by time or pressure intervals. The next 4 fields (Series 1 int. etc) give the required time interval parameters. If pressure is used, sampling commences using Series 2 format immediately. The next 3 characters set the top of climb defining the end of the ascent phase. This is followed by a single character that defines which of the two pre-stored lists of pressure altitude target heights are to be used (Table 4.3.1-0-10, List 1 or 2) when pressure level is selected by the first field. The next character selects whether a default timer is used in conjunction with pressure level selection to ensure that samples are still obtained if there is a pause during the ascent phase for periods of level flight. The additional interval timer resets and commences following each observation, If no pressure level is encountered during the pre-set time interval, a sample is taken and the timer is reset. The pre-set time interval is the same as selected in field 1 of Table 4.3.10-4 for routine/level flight. This technique also automatically commences the enroute phase of level flight if the top of climb is not reached. The function is disabled if Ascent selection is disabled in Table 4.3.10-1. 

Table 4.3.10.7-1 — Descent Data (I)

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Pressure interval (0) or Time interval (1) selection | Descent sampling mode selection Default = 1 |
| 3 | sss | Descent interval (seconds) | Default = 040 Range = 010 —300 |
| 3 | hhh | Top of descent (PALT) (ft X 100) | Default = 200 Range = 150-350 |
| 1 | 1-2 | Pressure target list selection | 1 = list 1, 2 = list 2 (43.10 Table A), Default = 2 |
| 1 | 0 or 1 | Additional level flight timer for pressure-based sampling: enabled = (1), disabled = (0) | Default = 1 (Routine timer interval as defined in Table 4.3.10-4) |
| 1 | I | Delimiter | End of Table 4.3.10-7 data |

Note: This table is used if descent reports are made. (This will be established by reference to Tables 4.3.10-1, 4.3.10-2 and 4.3.10-3.) The first character indicates whether interval selection is by time or pressure intervals. The next 3 characters give the required time interval and must be included even if the pressure sampling mode is selected. The following 3 characters set the top of descent. The next character indicates which of two pre-stored pressure altitude target heights lists are to be used (Table 4.3.10-1 0, List 1 or List 2). The second last character determines whether a default timer is used in conjunction the pressure level selection to ensure that samples are still obtained if there is a pause during the descent phase for periods of level flight. The additional interval timer resets and commences following each observation. If no pressure level is encountered during the pre-set time interval, a sample is taken and the timer is reset. The pre-set time interval is the same as selected in field 1 of Table 4.3.10-4 for routine/level flight. The function is disabled if Descent selection is disabled through Table 4.3.10-1 command.

Table 4.3.10.8-1 — Descent Data (2)

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 1 | 0 or 1 | Routine observations: enabled = (1), disabled = (0) | Enables or disables routine observations when both descent and airport selection are disabled in 4.3.10-1. Default = 1 |
| 1 | / | Delimiter | End of Table 4.3.10-8 data |

Note: This Table is used only if Descent selection and Airport selection are disabled through Table 4.3.10-1 command. If the first character is set to 1 (default) then routine observations at the time intervals given in Table 4.3.10-4 will be made during descent whenever AMDAR reporting is enabled through previous Table 4.3.10-1 commands. If set to 0 no reports will be made anywhere during the descent phase. If Descent selection is disabled and Airport selection enabled this table is ignored and routine reporting requirements are determined from Table 4.3.10-3. Table 4.3.10-2 has no influence on this function.

Table 4.3.10.9-1 — Reporting Disabled Status

| Number of Characters | Data | Description | Remarks |
| --- | --- | --- | --- |
| 4 | H1H1H2H2 | Disable observations between selected hours (00-23) UTO, every day | H1H1 = start of inhibit period H2H2 = end of inhibit period Default = 0000 |
| 1 | I | Delimiter | End of Table 4.3.10-9 data |

Note: This table is used if Inhibit reporting in selected time interval (Table 4.3.10-1) is selected. It allows observations to be inhibited between selected hours UTC, each 24 hours it is enabled. The default value is interpreted as no interval selected. The inhibit period starts at the first designated hour in the day and ends when the next designated hour is reached the same or next day. Thus 2301 means inhibit between 2300 hours and 0100 hours the next day, every day. (two hours spanning midnight UTC). 0000 means report though all 24 hour periods.

Additional notes: Default data for Tables 4.3.10-1 through to 4.3.10-9 are stored onboard as part of the basic software but can only be altered through software re-programming. Following a complete system reset and/or initialization, the default table variables from non-volatile memory are loaded and then retained in volatile memory until altered by uplink command. Default values can only be altered through software re-programming. Any subsequent uplinked changes are retained in volatile memory until the next system reset and/or initialization. The uplink command can be used to change any of the system control parameters or simply to downlink an existing configuration for data management purposes.

Table 4.3.10.10-1 — Preset Target Heights based on Pressure Level Selection

| Pressure (hPa) | Height (ft) | List I | List 2 | Height No (nn) |
| --- | --- | --- | --- | --- |
| 1050 | -989 | 1 | 1 | 01 |
| 1045 | -856 | 2 |  | 02 |
| 1040 | -723 | 3 | 2 | 03 |
| 1035 | -589 | 4 |  | 04 |
| 1030 | -454 | 5 | 3 | 05 |
| 1025 | -319 | 6 |  | 06 |
| 1020 | -184 | 7 | 4 | 07 |
| 1015 | -48 | 8 |  | 08 |
| 1010 | 89 | 9 | 5 | 09 |
| 1005 | 226 | 10 |  | 10 |
| 1000 | 364 | 11 | 6 | 11 |
| 995 | 502 | 12 |  | 12 |
| 990 | 641 | 13 | 7 | 13 |
| 985 | 780 | 14 |  | 14 |
| 980 | 920 | 15 | 8 | 15 |
| 975 | 1061 | 16 |  | 16 |
| 970 | 1202 | 17 | 9 | 17 |
| 965 | 1344 | 18 |  | 18 |
| 960 | 1486 | 19 | 10 | 19 |
| 955 | 1629 | 20 |  | 20 |
| 950 | 1773 | 21 | 11 | 21 |
| 945 | 1917 | 22 |  | 22 |
| 940 | 2062 | 23 | 12 | 23 |
| 935 | 2207 | 24 |  | 24 |
| 930 | 2353 | 25 | 13 | 25 |
| 925 | 2500 | 26 |  | 26 |
| 920 | 2647 | 27 | 14 | 27 |
| 915 | 2795 | 28 |  | 28 |
| 910 | 2944 | 29 | 15 | 29 |
| 905 | 3093 | 30 |  | 30 |
| 900 | 3243 | 31 | 16 | 31 |
| 895 | 3394 | 32 |  | 32 |
| 890 | 3545 | 33 | 17 | 33 |
| 885 | 3697 | 34 |  | 34 |
| 880 | 3850 | 35 | 18 | 35 |
| 875 | 4003 | 36 |  | 36 |
| 870 | 4157 | 37 | 19 | 37 |
| 865 | 4312 | 38 |  | 38 |
| 860 | 4468 | 39 | 20 | 39 |
| 855 | 4624 | 40 |  | 40 |
| 850 | 4781 | 41 | 21 | 41 |
| 845 | 4939 | 42 |  | 42 |
| 840 | 5098 | 43 | 22 | 43 |
| 835 | 5257 | 44 |  | 44 |
| 830 | 5417 | 45 | 23 | 45 |
| 825 | 5578 | 46 |  | 46 |
| 820 | 5739 | 47 | 24 | 47 |
| 815 | 5902 | 48 |  | 48 |
| 810 | 6065 | 49 | 25 | 49 |
| 805 | 6229 | 50 |  | 50 |
| 800 | 6394 | 51 | 26 | 51 |
| 795 | 6560 | 52 |  | 52 |
| 790 | 6727 | 53 | 27 | 53 |
| 785 | 6894 | 54 |  | 54 |
| 780 | 7062 | 55 | 28 | 55 |
| 775 | 7232 | 56 |  | 56 |
| 770 | 7402 | 57 | 29 | 57 |
| 765 | 7573 | 58 |  | 58 |
| 760 | 7745 | 59 | 30 | 59 |
| 755 | 7917 | 60 |  | 60 |
| 750 | 8091 | 61 | 31 | 61 |
| 745 | 8266 | 62 |  | 62 |
| 740 | 8442 | 63 | 32 | 63 |
| 735 | 8618 | 64 |  | 64 |
| 730 | 8796 | 65 | 33 | 65 |
| 725 | 8974 | 66 |  | 66 |
| 720 | 9154 | 67 | 34 | 67 |
| 715 | 9334 | 68 |  | 68 |
| 710 | 9516 | 69 | 35 | 69 |
| 705 | 9699 | 70 |  | 70 |
| 700 | 9882 | 71 | 36 | 71 |
| 675 | 10817 | 72 |  | 72 |
| 650 | 11780 | 73 | 37 | 73 |
| 625 | 12774 | 74 |  | 74 |
| 600 | 13801 | 75 | 38 | 75 |
| 575 | 14862 | 76 |  | 76 |
| 550 | 15962 | 77 | 39 | 77 |
| 525 | 17103 | 78 |  | 78 |
| 500 | 18289 | 79 | 40 | 79 |
| 475 | 19524 | 80 |  | 80 |
| 450 | 20812 | 81 | 41 | 81 |
| 425 | 22160 | 82 |  | 82 |
| 400 | 23574 | 83 | 42 | 83 |
| 375 | 25061 | 84 |  | 84 |

Notes:

- The contents of this table are the same as in Table 5.3.13.4-4 and Table 10 in Appendix G. If changes are necessary, please change all three tables.

- The following two equations are used in the process to calculate pressure (P(hPa)) from pressure altitude (PALT) and pressure altitude from pressure if Table 4.3.10-10 is not used to determine pressure target heights.

Computation of pressure, P(hPa) in ICAO Standard Atmosphere from pressure altitude, PALT:

P(hPa) = 1013.25[1 – 10-6x6.8756(PALT)] 5.2559 -------(1)

Computation of pressure altitude, PALT from pressure, P(hPa) in ICAO Standard Atmosphere:

PALT = 1.4544x105[1 - (P(hPa)/1013.25) 0.19026] --------(2)

For pressure-based observations during ascent and descent phases of flight, all sampling takes place at multiples of 10 or 50 hPa if List 2 is selected (5 and 25 hPa if List 1 is selected) except for the initial observation following the Off event and predefined tops of ascent and descent both of which are defined in thousands of feet.

BUFR TEMPLATE FOR AMDAR, 3 11 010, version 4

| 0 | 01 | 008 |  | Aircraft identification (1) |
| --- | --- | --- | --- | --- |
| 0 | 01 | 023 | Optional | Sequence number (2) |
| 0 | 01 | 006 | Optional | Flight number (3) |
| 0 | 01 | 110 | Optional | Aircraft tail number (4) |
| 0 | 01 | 111 | Optional | Origination airport (4) |
| 0 | 01 | 112 | Optional | Destination airport (4) |
| 2 | 04 | 002 |  | Add associated field (of 2 bits) (19) (20) |
| 0 | 31 | 021 |  | Associated field significance (19) (20) (= 8 Two bits quality information) |
| 3 | 01 | 011 |  | Year, month and day |
| 3 | 01 | 013 |  | Hour, minute and second |
| 3 | 01 | 021 |  | Latitude and longitude (high accuracy) |
| 0 | 07 | 004 |  | Pressure (5) |
| 0 | 10 | 053 |  | GNSS Altitude (4) |
| 0 | 08 | 009 |  | Detailed phase of flight (6) |
| 0 | 11 | 001 |  | Wind direction |
| 0 | 11 | 002 |  | Wind speed |
| 0 | 02 | 064 |  | Aircraft roll angle quality |
| 0 | 11 | 100 | Optional | True aircraft speed (7) |
| 0 | 11 | 101 | Optional | Aircraft ground velocity (u-component) (4) |
| 0 | 11 | 102 | Optional | Aircraft ground velocity (v-component) (4) |
| 0 | 11 | 103 | Optional | Aircraft ground velocity (w-component) (4) |
| 0 | 11 | 104 | Optional | Aircraft true heading (4) |
| 0 | 12 | 101 |  | Temperature/air temperature (8) |
| 0 | 13 | 002 |  | Mixing ratio |
| 0 | 13 | 003 |  | Relative humidity |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 12 | 103 | Optional | Dew-point temperature (9) |
| 0 | 33 | 026 |  | Moisture quality |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 042 | Optional | Airframe icing (10) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 20 | 043 | Optional | Peak liquid water content (11) |
| 0 | 20 | 044 | Optional | Average liquid water content (11) |
| 0 | 20 | 045 | Optional | Supercooled large droplet (SLD) conditions (11) |
| 1 | 01 | 000 |  | Delayed replication of 1 descriptor |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 33 | 025 | Optional | ACARS interpolated values indicator (12) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors (13) |
| 0 | 31 | 001 |  | Delayed descriptor replication factor (14) |
| 0 | 11 | 075 | Optional | Mean turbulence intensity (EDR) |
| 0 | 11 | 076 | Optional | Peak turbulence intensity (EDR) |
| 0 | 11 | 039 | Optional | Extended time of occurrence of peak EDR (15) |
| 1 | 02 | 000 |  | Delayed replication of 2 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 037 | Optional | Turbulence index (EDR) |
| 0 | 11 | 077 | Optional | Reporting interval or averaging time for EDR (16) |
| 1 | 03 | 000 |  | Delayed replication of 3 descriptors |
| 0 | 31 | 000 |  | Short delayed descriptor replication factor |
| 0 | 11 | 034 | Optional | Vertical gust velocity (17) |
| 0 | 11 | 035 | Optional | Vertical gust acceleration (17) |
| 0 | 11 | 036 | Optional | Maximum derived equivalent vertical gust speed (17) |
| 2 | 04 | 000 |  | Cancel add associated field (19) (20) |
| 1 | 18 | 000 |  | Delayed replication of 18 descriptors (18) |
| 0 | 31 | 001 |  | Delayed descriptor replication factor (18) |
| 3 | 01 | 021 | Optional | Latitude and longitude (high accuracy) |
| 0 | 07 | 007 | Optional | Height |
| 3 | 01 | 013 | Optional | Hour, minute and second |
| 0 | 11 | 105 | Optional | EDR algorithm version (4) |
| 2 | 04 | 007 |  | Add associated field (of 7 bits) (21) |
| 0 | 31 | 021 |  | Associated field significance (21) (= 7 Percentage confidence) |
| 0 | 11 | 076 | Optional | Peak turbulence intensity (EDR) |
| 0 | 11 | 075 | Optional | Mean turbulence intensity (EDR) |
| 2 | 04 | 000 |  | Cancel add associated field(21) |
| 0 | 11 | 106 | Optional | Running minimum confidence (4) |
| 0 | 11 | 107 | Optional | Maximum number bad inputs (4) |
| 0 | 11 | 108 | Optional | Peak Location (4) |
| 0 | 11 | 109 | Optional | Number of good EDR (4) |
| 0 | 12 | 101 | Optional | Temperature/air temperature |
| 0 | 11 | 001 | Optional | Wind direction |
| 2 | 01 | 130 | Optional | Change data width |
| 0 | 11 | 084 | Optional | Wind speed |
| 2 | 01 | 000 | Optional | Cancel change data width |

Table 1. Standardized BUFR Template for AMDAR 3 11 010 version 4.

Notes for Standardized BUFR Template for AMDAR data 3 11 010, version 4:

- Aircraft identifier 0 01 008 can cope with ASDAR, ADS and other AMDAR identities. ADS reports use a 24-bit ICAO airframe identifier, equating to an 8-character BCD number. Look at developing a standard naming convention for the various AMDAR regions and/or programmes. The WIGOS meeting agreed that additional information such aircraft type and navigation systems would be part of the Meta data, not part of the Standardized BUFR Template for AMDAR. It was noted that AMDAR Meta data would be addressed by the WIGOS Pilot Project for AMDAR.

- The sequence number is a simple observation count to be included in the down-linked message.  It should be reset at 0000 UTC each day and can be useful for quality control, data management and archiving purposes. The WIGOS meeting has made the recommendation that if this parameter is not used by an operational AMDAR programme or NWP Centre then this parameter be removed from the new Standardized BUFR Template for AMDAR.

- 0 01 006 (Flight number) will assist with the quality control of aircraft track data, by providing information on the route the aircraft is expected to take, including information on the departure airport and the expected arrival airports. Presently 8 characters has been used as an estimate as the maximum length for any given flight number.

- Refer to Table 2 for the required BUFR and CREX descriptors for the new elements, including the units, scale, reference value and data width.

| Table reference |  | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y | Element name | Unit | Scale | Reference value | Data width | Unit | Scale | Data width |
| 0 11 100 | True aircraft speed | m s-1 | 1 | 0 | 12 | m s-1 | 1 | 4 |
| 0 11 101 | Aircraft velocity u-component | m s-1 | 1 | –4096 | 13 | m s-1 | 1 | 4 |
| 0 11 102 | Aircraft velocity v-component | m s-1 | 1 | –4096 | 13 | m s-1 | 1 | 4 |
| 0 11 103 | Aircraft velocity w-component | m s-1 | 1 | –512 | 10 | m s-1 | 1 | 4 |
| 0 11 104 | Aircraft true heading | Degree true | 0 | 0 | 9 | Degree true | 0 | 3 |
| 0 10 053 | Global Navigation Satellite System Altitude | m | 0 | -1000 | 17 | m | 0 | 5 |
| 0 01 110 | Aircraft tail number | CCITT IA5 | 0 | 0 | 48 | character | 0 | 6 |
| 0 01 111 | Origination airport | CCITT IA5 | 0 | 0 | 24 | character | 0 | 3 |
| 0 01 112 | Destination airport | CCITT IA5 | 0 | 0 | 24 | character | 0 | 3 |
| 0 11 105 | EDR algorithm version | numeric | 0 | 0 | 6 | numeric | 0 | 2 |
| 0 11 106 | Running minimum confidence | numeric | 1 | 0 | 4 | numeric | 1 | 2 |
| 0 11 107 | Maximum number bad inputs | numeric | 0 | 0 | 5 | numeric | 0 | 2 |
| 0 11 108 | Peak Location | numeric | 1 | 0 | 4 | numeric | 1 | 2 |
| 0 11 109 | Number of good EDR | numeric | 0 | 0 | 4 | numeric | 0 | 2 |

Table 2. Proposal for new AMDAR descriptors in 3 11 010, version 4.

- The AMDAR Science and Technical Sub-Group requested that Flight level (0 07 010) be replaced with static pressure (0 07 004) as this value is primarily there before any altitude value is calculated by the aircrafts on-board algorithms. Only the left-over of the so-called built-in error remain any other effect of calculation methods, rounding, or formatting are avoided. For any meteorological application of the AMDAR data the pressure value is needed but not the flight level.

- This phase of flight table is expanded to indicate wind quality from roll angle, or roll and pitch combined and also to indicate the method of ascent and descent observation interval selection either by time or pressure increments. The WIGOS meeting agreed that the Phase of flight 0 08 004 would not be included in the new Standardized BUFR Template for AMDAR as the required level of detail has been incorporated in the detailed phase of flight 0 08 009. The WIGOS meeting also discussed whether there is a requirement for adding a new condition to the detailed phase of flight 0 08 009 that would cover an aircraft being placed in a holding pattern.

- Refer to AMDAR Reference Manual for definition.

- This parameter has been renamed Temperature/air temperature.

- 0 12 103 Dew-point temperature had been introduced in the templates for AMDAR profile data to simulate radiosonding data.

- The old ACARS airframe icing code table 0 20 041 is not included.

- A special automatic icing report, including these elements, is expected to become available from some aircraft and a down-link code has been published.

- 0 33 025 ACARS interpolated values was primarily used in the USA AMDAR Programme to indicate time and position being reported or interpolated. The name for this element has been changed to ACARS interpolated values indicator.

- Delayed replication 1 03 000 refers to the following three descriptors 0 11 075, 0 11 076 and 0 11 039 to allow reporting of the Extended time of occurrence of peak EDR of all included values of 0 11 076 (Peak (EDR)). This allows each turbulence peak to be reported.

Explanatory remarks to Note (13):

According to Note (14), up to ten values of 0 11 076 (Peak (EDR)) may be reported.  However, 0 11 039 (Extended time of occurrence of peak EDR) was included only once in the template 3 11 010, version 0.  Therefore, it was not clear to which out of those ten values of 0 11 076, the time specification 0 11 039 referred.  If it had been the maximum value, the name of 0 11 039 should have been modified to read “Extended time of occurrence of maximum peak EDR”.  If the time information on all the reported values of 0 11 076 (Peak (EDR)) is required, then 0 11 039 (Extended time of occurrence of peak EDR) should be included under the delayed replication as shown in the proposed template 3 11 010, version 4.

- Some aircraft report up to 10 pairs of (EDR) values per observation.  The corresponding times and position could be found by interpolation from the previous report. If the aircraft does not report it the number of replication 0 31 001 is set to zero.

- 0 11 039 allows observation intervals up to one hour.  0 11 038 allows up to 15 minutes only whereas observation intervals of 30 minutes or more are commonly used, hence 0 11 038 had been replaced by 0 11 039.

- The EDR observing interval and associated averaging time differs according to individual observing schedule and cannot be assumed to be identical to the observation interval for the main elements.  It is desirable to include this information in the coded data.

- Vertical gust velocity 0 11 034, Vertical gust acceleration 0 11 035 and Maximum derived equivalent vertical gust speed 0 11 036 have been added to meet the request for reflecting all entries of 3 11 004 in the Standardized BUFR template for AMDAR. The current ICAO standard for automated turbulence reporting is EDR.

- Up to 254 EDR reports may be included in a BUFR message. If the aircraft does not report them, the number of replication 0 31 001 is set to zero.

- Operator descriptor 2 04 Y has been introduced for representation of AMDAR quality information instead of flag table 0 33 079 (AMDAR quality information) used in the previous versions of the AMDAR template 3 11 010. Some elements (such as Wind Speed, Wind Direction, Air Temperature) may appear more than once in the data described by 3 11 010.  Operator descriptor 2 04 Y allows to assign unambiguously the required quality information to the element to which it refers.

- Each of the following elements, apart from delayed replication factors 0 31 000 and 0 31 001, shall be preceded by two bits providing information on the element being suspected or not. If the quality information on the element is not required, the associated field shall be set to 3. For this purpose, a new code figure 8 (Two bit quality information) is proposed in the Code table 0 31 021 (Associated field significance)  as follows:

0 31 021

| Code figure |  |
| --- | --- |
| 8 | 0 - Not suspected |
|  | 1 - Suspected |
|  | 2 - Reserved |
|  | 3 - Information not required |

- Peak turbulence intensity (EDR) and Mean turbulence intensity (EDR) shall be preceded by seven bit information containing percentage confidence of Peak turbulence intensity (EDR) and Mean turbulence intensity (EDR), respectively.

ARINC IA Project Initiation/Modification (APIM)

# Name of Proposed Project	APIM #:  _____

(Insert name of proposed project.)

## Name of Originator & Organization

(Insert name of individual and their organization)

# Subcommittee Assignment and Project Support

## Suggested AEEC Group and Chairman

(Identify an existing or new AEEC group.)

## Support for the activity (as verified)

Airlines: (Identify each company by name.)

Airframe Manufacturers:

Suppliers:

Others:

## Commitment for Drafting and Meeting Participation (as verified)

Airlines:

Airframe Manufacturers:

Suppliers:

Others:

## Recommended Coordination with other groups

(List other AEEC subcommittees or other groups.)

# Project Scope (why and when standard is needed)

## Description

(Insert description of the scope of the project.

## Planned usage of the envisioned specification

Use the following symbol to check yes or no below. (

New aircraft developments planned to use this specification

yes 	no 

Airbus:	(aircraft & date)

Boeing:	(aircraft & date)

Other:	(manufacturer, aircraft & date)

Modification/retrofit requirement	yes 	no 

Specify:	(aircraft & date)

Needed for airframe manufacturer or airline project

yes 	no 

Specify:	(aircraft & date)

Mandate/regulatory requirement 	yes 	no 

Program and date: 	(program & date)

Is the activity defining/changing an infrastructure standard?

yes 	no 

Specify	 (e.g., ARINC 429)

When is the ARINC standard required? 	______(month/year)__________

What is driving this date? _______(state reason)_____________________

Are 18 months (min) available for standardization work?

yes 	no 

If NO please specify solution:     _________________

Are Patent(s) involved?

yes 	no 

If YES please describe, identify patent holder:     _________________

## Issues to be worked

(Describe the major issues to be addressed.)

# Benefits

## Basic benefits

Operational enhancements	yes 	no 

For equipment standards:

a. Is this a hardware characteristic?	yes 	no 

b. Is this a software characteristic?	yes 	no 

c. Interchangeable interface definition?	yes 	no 

d. Interchangeable function definition?	yes 	no 

If not fully interchangeable, please explain:     _________________

Is this a software interface and protocol standard?

yes 	no 

Specify:     _________________

Product offered by more than one supplier	yes 	no 

Identify:    	(company name)

## Specific project benefits (Describe overall project benefits.)

### Benefits for Airlines

(Describe the benefits unique to the airline point of view.)

### Benefits for Airframe Manufacturers

(Describe the benefits unique to the airframe manufacturer’s point of view.)

### Benefits for Avionics Equipment Suppliers

(Describe the benefit unique to the equipment supplier’s point of view.)

# Documents to be Produced and Date of Expected Result

One/two/ Project Papers are expected to be completed per the table below.

## Meetings and Expected Document Completion

The following table identifies the number of meetings and proposed meeting days needed to produce the documents described above.

| Activity | Mtgs | Mtg-Days (Total) | Expected Start Date | Expected Completion Date |
| --- | --- | --- | --- | --- |
| Document a | # of mtgs | # of mtg days | mm/yyyy | mm/yyyy |
|  | # of mtgs * | # of mtg days * |  |  |
| Document b | # of mtgs | # of mtg days | mm/yyyy | mm/yyyy |
|  | # of mtgs * | # of mtg days * |  |  |

* Indicate unsupported meetings and meeting days, i.e., technical working group or other ad hoc meetings that do not requiring IA staff support.

# Comments

(Insert any other information deemed useful to the committee for managing this work.)

6.1 		Expiration Date for this APIM

April/October 20XX

# Comments

Will be integrated in to the new configuration table.

Will be integrated in to the new configuration table.

Not required

Will be integrated in to the new configuration table.

Will be integrated in to the new configuration table.

Not required

Not required.

Not required

A new table for uplink will be required.

Due to NWP data visualization this parameter is no longer required.

Table not required. When airport is deselected airport and decent then this data is not longer required.

Based on the above table, Decent Data, this table is no longer required. If this information is not required then this table would override the request.

This table must be expanded to flight level 35,000ft.

# Text boxes

For IA staff use only

Date Received:  Jan 15, 2010			Assigned to:

Potential impact:

(A. Safety	B.  Regulatory		C.  New aircraft/system	D.  Other)

Resolution:

Authorized, Deferred, Withdrawn, More Detail Needed, Rejected)

Assigned to SC/WG: