| WORLD METEOROLOGICAL ORGANIZATION ----------------------------- REGIONAL ASSOCIATION I FIFTH SESSION OF THE REGIONAL ASSOCIATION I WORKING GROUP ON PLANNING AND IMPLEMENTATION OF THE WWW NAIROBI, KENYA, 25-29 September 2006 |  | RA I/WG-PIW/Doc. 5.2(7) (21.IX.2006) --------------------- ENGLISH only |
| --- | --- | --- |

# Proposal for common sequence descriptors for representation

of SYNOP data manually encoded in CREX

Submitted by Eva Červená (Czech Republic)

_______________________________________________________________

Summary and Purpose of Document

This document contains a proposal for common sequence descriptors

for representation of SYNOP data manually encoded in CREX.

ACTION PROPOSED

The meeting is invited to take the content of this document into consideration

in view of the implementation of Migration to TDCF in RA I.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2

[2] Final Report, ET DR&C, Muscat, 5 – 8 December 2005

[3] Final Report, ET DR&C and CT MTDCF, Montreal, 8 – 12 May 2006

[4] Doc. 5.2(5), RA I WG-PIW, Nairobi, 25 – 29 September 2006

Introduction

Significant work has been done by some RA I National Meteorological Services, in particular by Tanzania Meteorological Agency (TMA), to achieve progress in implementation of Migration to TDCF as reported by Mr. William Amos Chillambo, the Rapporteur on Codes for RA I.

The manual encoding of observations in CREX is not a simple task, especially in the period of dual transmission, i.e. when the data are to be produced in the traditional as well as in the CREX format. It is to be appreciated that TMA has developed a detailed procedure for encoding SYNOP data in CREX to ease this process.

Proposal for sequence descriptors for SYNOP data manually encoded in CREX

The BUFR/CREX template TM 307080 developed for data representation of SYNOP data is capable to express practically the whole extent of SYNOP data as defined in Manual on Codes, Volume I.1. It is suitable for reporting of the synoptic data in both BUFR and CREX, provided that the reports are generated by software. This extent of data, however, would not be feasible to manage by manual encoding.

In the Annex to this document, there is a proposal for the template TM D07089 for SYNOP data manually encoded in CREX and the corresponding sequence descriptors. By introducing of these sequence descriptors, the template would obtain a “standard status” and the data description section in the CREX messages could be expressed in much more concise way.

The proposed template TM D07089 nearly corresponds to the template used by TMA in their CREX messages. The station identification is, however, represented only by WMO block and station number in the proposed template; the name of the station is not included (and the example CREX message from Dar Es Salaam has been modified accordingly to be in compliance with the proposed template). The reason of this reduction consists in the potential difficulty in including the correct number of space characters if the data are encoded manually.

Compared with the complex template TM 307080, the proposed template TM D07089 is of somewhat reduced extent, e.g. radiation data or wind gust data are not included there. If a NMS wishes to report these or other additional data, the corresponding descriptors are to be added as it is recommended in Notes (2) and (3) under the template (please see page 5). This addition might be preferably done in consultation with the Rapporteur on Codes for RA I and other Members of the ET on Data Representation and Codes (ET DR&C) or the WMO Secretariat.

It is to be taken into consideration that this proposal has not yet been approved by a meeting of ET DR&C and that the proposed descriptors have to be validated to which the NMS of RA I might be invited to contribute.

ANNEX

TM D07089 - Template for synoptic reports from fixed land stations suitable

for SYNOP data manually encoded in CREX

| D 07 089 |  | Sequence for representation of synoptic reports from a fixed land station suitable for SYNOP data manually encoded in CREX |
| --- | --- | --- |
|  | D 07 087 | “Instantaneous” parameters of sequence D07089 |
|  | D 07 088 | “Period” parameters of sequence D07089 |

Notes:

- “Instantaneous” parameter is a parameter that is not coupled to a time period descriptor, e.g. B04024.

- “Period” parameter is a parameter that is coupled to a time period descriptor, e.g. B04024.

This CREX template for synoptic reports from fixed land stations further expands as follows:

| D 07 087 |  |  | “Instantaneous” parameters of sequence D07089 |  |
| --- | --- | --- | --- | --- |
|  |  |  | Surface station identification, time, horizontal and vertical coordinates | in CREX |
|  | D 01 001 | B 01 001 | WMO block number II | Numeric, 0, 2 |
|  |  | B 01 002 | WMO station number iii | Numeric, 0, 3 |
|  | B 02 001 |  | Type of station (ix) | Code table, 0, 1 |
|  | D 01 011 | B 04 001 | Year | Year, 0, 4 |
|  |  | B 04 002 | Month | Month, 0, 2 |
|  |  | B 04 003 | Day YY | Day, 0, 2 |
|  | D 01 012 | B 04 004 | Hour GG | Hour, 0, 2 |
|  |  | B 04 005 | Minute gg | Minute, 0, 2 |
|  | D 01 023 | B 05 002 | Latitude (course accuracy) | Degree, 2, 4 |
|  |  | B 06 002 | Longitude (course accuracy) | Degree, 2, 5 |
|  | B 07 030 |  | Height of station ground above msl | m, 1, 5 |
|  | B 07 031 |  | Height of barometer above msl | m, 1, 5 |
|  |  |  | Pressure data |  |
|  | D 02 001 | B 10 004 | Pressure PoPoPoPo | Pa, –1, 5 |
|  |  | B 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1, 5 |
|  |  | B 10 061 | 3-hour pressure change ppp | Pa, –1, 4 |
|  |  | B 10 063 | Characteristic of pressure tendency a | Code table, 0, 2 |
|  | B 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1, 4 |
|  | B 07 004 |  | Pressure (standard level) a3 = 925, 850, 700, ..hPa = missing for lowland stations | Pa, –1, 5 |
|  | B 10 009 |  | Geopotential height of the standard level hhh = missing for lowland stations | gpm, 0, 5 |
|  |  |  | Temperature and humidity |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 12 101 |  | Temperature/dry-bulb temperature (sc. 2) snTTT | °C, 2, 4 |
|  | B 12 103 |  | Dew-point temperature (sc. 2) snTdTdTd | °C, 2, 4 |
|  | B 13 003 |  | Relative humidity | %, 0, 3 |
|  | B 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2, 5 |
|  |  |  | Visibility |  |
|  | B 20 001 |  | Horizontal visibility VV | m, –1, 4 |
|  |  |  | Cloud data |  |
|  | D 02 004 | B 20 010 | Cloud cover (total) N If N = 9, then B 20 010 = 113 %, if N = /, then B 20 010 = missing. | %, 0, 3 |
|  |  | B 08 002 | Vertical significance if CL are observed, then B 08 002 = 7 (low cloud), if CL are not observed and CM are observed, then B 08 002 = 8 (middle cloud), if only CH are observed, B 08 002 = 0, if N = 9, then B 08 002 = 5, if N = 0, then B 08 002 = 62, if N = /, then B 08 002 = missing. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount (of low or middle clouds) Nh If N = 0, then B 20 011 = 0, if N = 9, then B 20 011 = 9, if N = /, then B 20 011 = missing. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud h If N = 0 or /, then B 20 013 = missing. | m, –1, 4 |
|  |  | B 20 012 | Cloud type (low clouds) CL B 20 012 = CL + 30, if N = 0, then B 20 012 = 30, if N = 9 or /, then B 20 012 = 62. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (middle clouds) CM B 20 012 = CM + 20, if N = 0, then B 20 012 = 20, if N = 9 or / or CM = /, then B 20 012 = 61. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type (high clouds) CH 0 20 012 = CH + 10, if N = 0, then B 20 012 = 10, if N = 9 or / or CH = /, then B 20 012 = 60. | Code table, 0, 2 |
|  | R 01 000 |  | Delayed replication of the next 1 descriptor |  |
|  | D 02 005 | B 08 002 | Vertical significance In any Cb layer, B 08 002 = 4 , else: in the first replication: if N = 9, then B 08 002 = 5, if N = /, then B 08 002 = missing, else B 08 002 = 1; in the other replications B 08 002 = 2, 3, 4. | Code table, 0, 2 |
|  |  | B 20 011 | Cloud amount Ns In the first replication: If N = /, then B 20 011 = missing, else B 20 011 = Ns; in the other replications B 20 011 = Ns. | Code table, 0, 2 |
|  |  | B 20 012 | Cloud type C if N = 9 or /, then B 20 012 = missing, else B 20 012 = C. | Code table, 0, 2 |
|  |  | B 20 013 | Height of base of cloud hshs | m, -1, 4 |
| D 07 088 |  |  | “Period” parameters of sequence D 07 089 |  |
|  |  |  | Present and past weather |  |
|  | B 20 003 |  | Present weather ww | Code table, 0, 3 |
|  | B 04 024 |  | Time period At 00, 06, 12, 18 UTC = - 6. At 03, 09,15, 21 UTC = - 3. | Hour, 0, 4 |
|  | B 20 004 |  | Past weather (1) W1 | Code table, 0, 2 |
|  | B 20 005 |  | Past weather (2) W2 | Code table, 0, 2 |
|  |  |  | Evaporation |  |
|  | B 04 024 |  | Time period in hours = - 24 | Hour, 0, 4 |
|  | B 02 004 |  | Type of instrument for evaporation or iE crop type for evapotranspiration | Code table, 0, 2 |
|  | B 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1, 4 |
|  |  |  | Sunshine |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours In the first replication = - 24, in the second replication = - 1. | Hour, 0, 4 |
|  | B 14 031 |  | Total sunshine in minutes In the first replication SSS in the second replication SS | Minute, 0, 4 |
|  |  |  | Precipitation |  |
|  | R 02 002 |  | Replicate next 2 descriptors 2 times |  |
|  | B 04 024 |  | Time period in hours tR | Hour, 0, 4 |
|  | B 13 011 |  | Total precipitation RRR no precipitation = 0 trace = - 0.1 | kg m-2, 1, 5 Encoded as: -00001 |
|  |  |  | Extreme temperatures |  |
|  | B 07 032 |  | Height of sensor above local ground (for temperature measurement) | m, 2, 5 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 111 |  | Maximum temperature at height and over period specified snTxTxTx | °C, 2, 4 |
|  | B 04 024 |  | Time period in hours = - 12 | Hour, 0, 4 |
|  | B 12 112 |  | Minimum temperature at height and over period specified snTnTnTn | °C, 2, 4 |
|  |  |  | Wind data |  |
|  | B 07 032 |  | Height of sensor above local ground (for wind measurement) | m, 2, 5 |
|  | B 02 002 |  | Type for instrumentation for wind measurement iw | Flag table, 0, 2 |
|  | B 08 021 |  | Time significance = 2 (time averaged) | Code table, 0, 2 |
|  | B 04 025 |  | Time period = - 10 (or number of minutes after a significant change of wind, if any) | Minute, 0, 4 |
|  | B 11 001 |  | Wind direction dd If dd = 00 (calm) or dd = 99 (variable), B 11 001 = 0. | Degree true, 0, 3 |
|  | B 11 002 |  | Wind speed ff | m s-1, 1, 4 |
|  | B 08 021 |  | Time significance (set to missing to cancel the previous value) | Code table, 0, 2 |

Notes:

- CREX Edition 1 is recommended for manual encoding of data.

- If the addition of another “instantaneous” parameter is required, the sequence descriptor D07089 shall be replaced by D07087 D07088, and the B-descriptor for this parameter shall be placed between D07087 and D07088.

- If the addition of another “period” parameter is required, the sequence D 07 089 shall be supplemented by the relevant B-descriptor provided no additional “instantaneous” parameter is needed.

Example

CREX++

T000103 A000 D07089++

63 894 1 2006 02 22 06 00 -0687 03920 00552 00564 10062 10122 //// // 0000 ///// ///// 00125  2900 2320 071 ///// 2500 038 07 03 0073 31 20 10 0001 01 03 08 0073 005 -0006 00 00 -0024 01 0085 -0024 0690 -0001 0060 -0024 00000 //// ///// 00125 //// //// -0012 2210 01000 14 02 -0010 060 0025 //++
7777

Example with optional check digits:

CREX++

T000103 A000 D07089 E++

063 1894 21 32006 402 522 606 700 8-0687 903920 000552 100564 210062 310122 4//// 5// 60000 7///// 8///// 900125 02900 12320 2071 3///// 42500 5038 607 703 80073 931 020 110 20001 301 403 508 60073 7005 8-0006 900 000 1-0024 201 30085 4-0024 50690

6-0001 70060 8-0024 900000 0//// 1///// 200125 3//// 4////  5-0012 62210 701000 814 902

0-0010 1060 20025 3//++
7777