| WORLD METEOROLOGICAL ORGANIZATION ____________________ RA VI MEETING OF THE WORKING GROUP ON PLANNING AND IMPLEMENTATION OF WWW CO-ORDINATORS Offenbach, Germany, 13-17 October 2003 |  | RAVI/WG/PIW/Doc. 3.2(2) (12.IX.2003) _________ ITEM: 3.2 Original: ENGLISH |
| --- | --- | --- |

### OBSERVING SYSTEMS

AMDAR status

(Submitted by the Secretariat)

#### Summary and Purpose of the Document

# The document contains a report on the AMDAR status prepared by the AMDAR Panel Technical Co-ordinator.

##### ACTION PROPOSED

# The meeting is invited to consider the report on the AMDAR status prepared by the AMDAR Panel Technical Co-ordinator.

__________________

AMDAR STATUS AT SEPTEMBER 2003

By J. J. Stickland

AMDAR Panel Technical Coordinator

Report to RAVI Working Group on

Planning and Implementation of WWW Coordinators

1.	Introduction

  - The work of the AMDAR Panel over the past 12 months has continued to consolidate AMDAR as a cost effective observing system for upper air observations.  Significant achievements have been made in the 4 high priority projects and new development projects were commenced, namely:

- Coordination of National and Regional Programmes;

- Improvement in Data Exchange and Quality Control;

- Southern Africa Project; and,

- Middle East Project

Of significance is the commencement of a targeted observations programme in the ASECNA group of countries in Central and Eastern Africa in collaboration with the E-AMDAR regional programme.   There was a modest increase in the daily number of AMDAR observations exchanged on the GTS despite difficulties being experienced by 2 national programmes.  A number of administrative changes have taken place with responsibility for project management of E-AMDAR passing from the UK to Sweden and the relocation of the AMDAR Panel Technical Coordinator from UK to Australia.  Work with the various WMO OPAGs, Expert Teams, ICAO and other government and intergovernmental agencies continued as did extensive collaboration with the aviation industry.

1.2	Of special interest to the Panel has been the recognition by various WMO bodies including the Fourth Session of ET-ODRRGOS (Jan 2002), the Second Session of ICT/IOS (Oct. 2002), and more recently the Fourteenth Congress (May 2003), the Fifty-Fifth Session of Executive Council (May 2003) and the 2 Technical Commissions CBS and CAeM, that AMDAR is an important component of the Global Observing System and that it should be more fully integrated into the WWW Programme.  Plans are being developed to implement changes that will ensure ongoing support for AMDAR activities, their sustainability in the future and the desirability of funding these activities.  Initial steps are expected to be taken at a meeting of the CBS Management Group in October 2003 to address Congress and EC directives on the AMDAR Programme.  A discussion paper for the meeting has been prepared jointly by the President of CAeM and the Chairman of the AMDAR Panel in which a number of possible mechanisms are proposed to more fully integrate AMDAR activities into the WWW Programme.

2.	Items of Interest to RAVI

The following items relate directly to AMDAR activities of interest to RAVI:

- E-AMDAR became an operational component of EUCOS on 1 January 2003;

- Improvements to the E-AMDAR system continue with additional functionality included in the various operational systems for data acquisition, quality evaluation, and data optimisation;

- Aircraft fleets expanded from around 300 to 500 aircraft over the past 12 months;

- The number of daily observations declined from 25,000 to 23,000 in line with budget controls;

- However, data coverage improved with more airports meeting the required number of profiles even though the total number of observations declined.  This was made possible through close monitoring and network control now available with the optimisation system and skills of the Technical Coordinator;

- A new manual to specifically address requirements of airlines is being prepared;

- Upgrade of the AAA software was completed and is being introduced on appropriate aircraft.  The software provides significantly improved onboard control functionality and reduces communications costs through data compression;

- E-AMDAR participated in 2 intense observation periods (April and August 2003) as part of a high frequency trial to evaluate the impact of much more frequent observations (hourly and sub-hourly profiles at many airports) versus current 3-hourly profiles;

- E-AMDAR is preparing to participate in THORPEX;

- The Canadian national programme has begun to receive test data from recently equipped aircraft.  It is expected that data will be available for exchange on the GTS in the near future;

- Additional E-AMDAR data is now available over the central Atlantic, parts of the Caribbean, northern parts of South America, North Africa, Eastern Europe and the Middle East through careful data management using the optimisation system;

- E-AMDAR has agreed to provide targeted data for 14 countries in Central and Western Africa and Madagascar as part of a collaborative programme with the ASECNA organisation that is paying for the additional data.  This is the first substantial targeted programme in the world where one regional programme provides data for another region;

- E-AMDAR is preparing to evaluate a new alternative AMDAR system (TAMDAR) that will equip smaller regional aircraft and provide profiles at regional airports that are not serviced by regular AMDAR aircraft.  Lower level en-route data (10,000 to 20,000 ft) will also be provided;

- E-AMDAR is monitoring 2 programmes to develop humidity sensors in Europe (UK and Germany) as well as the ongoing work in the US.

3.	Major Projects

3.1	The AMDAR Reference Manual was published by WMO as WMO 958 in English only, after a delay of several months.  This completes a substantial effort by a number of people within the Panel and the WMO Secretariat and provides a wide range of information.

3.2	Following some unexpected delays, testing of new onboard software developed using the AAA Ver.2 specification was completed on KLM aircraft and initial trials on BA aircraft are due to commence soon.  Continuing assessment of the improved DEVG turbulence algorithm selected by E-AMDAR, is ongoing.

3.3	The Panel has continued its valuable collaboration with the Airlines Electronic Engineering Committee (AEEC) through the Data Link Systems Sub-committee.  A number of minor modifications, mostly of an editorial-presentation nature, have been made to the new ARINC 620 Ver. 4 onboard software specification.  It is expected to be formally approved by the end of 2003, a year later than originally planned.  The delay was caused by substantial new work in other unrelated parts of the ARINC 620 document.   ARINC 20 Ver. 4 is based on the upgraded E-AMDAR AAA Ver.2 specification and effectively becomes a new international standard.

3.4	The AMDAR Panel has commenced another project that proposes to convert the new broadly based ARINC 620 specification into a universal onboard software package that will be licensed by WMO to all major avionics hardware providers.  It is proposed that the avionics companies will adapt the package to suit many different types of aircraft ranging from the largest long haul models to small regional aircraft.   The project replaces several smaller projects that were targeted at a small number of specific types of aircraft.  It is expected to take several years to implement.

3.5	Proposed changes to the AMDAR BUFR code were accepted by CBS in 2002 and recommended for operational use in November 2003 subject to satisfactory testing by 2 WMO Members.  A testing programme will be conducted in August 2003 between DWD, KNMI and Canada.   New regional bulletins of FM42 AMDAR reports in text format have also been approved and are being implemented operationally by most originating AMDAR centres.  These bulletins will make it easier for countries with basic GTS message processing capability to handle data that is relevant to their specific area of interest.

4.	Existing AMDAR Systems

4.1	The number of daily observations exchanged on the GTS has increased from around 140,000 in 2002 to about 150,000 in mid 2003.  This is despite a reduction in the number of observations from E-AMDAR due to improvements to the very effective data optimisation system.  A small reduction also resulted from a further decrease in the number of operational ASDAR aircraft.

4.2	Australia’s attempts to rebuild its domestic AMDAR programme following the demise of Ansett Airlines have been slowed by a variety of technical and business reasons.  New Zealand has increased the number of equipped aircraft but carefully controls the number reporting because of budget constraints.

4.3	Although E-AMDAR has continued to expand its aircraft fleet equipped with AMDAR from approximately 300 aircraft a year ago to about 500 aircraft in mid 2003, the number of daily reports has declined from about 25,000 to 23,000 per day as mentioned above.  This has resulted in a much better controlled programme governed by the competing components of budget constraints and the need to provide more data.  It is now technically feasible to fine-tune the programme on a daily basis.  The various participating airlines have undergone substantial changes to their operational fleets following the down turn in the aviation industry.  New components have been added to the data acquisition system including a financial package that allows for micro-management of costs for each individual airline, and the ability to inhibit selected measured elements from being reported in the data message on the GTS.  Selection is based on data quality information.  It was mentioned earlier that E-AMDAR has changed the EUCOS member responsible for management in line with normal EUCOS procedures requiring the rotation of major tasks amongst members.  Improvements have also been made to the various targeting systems within the E-AMDAR programme making it easier to control data from aircraft involved in specific targeted programmes.

4.4	The US has begun a major overhaul of its MDCRS/ACARS programme.  Changes to the funding base have been implemented following the very serious financial positions of the larger participating airlines.  Plans are being prepared to develop the programme along similar lines to E-AMDAR.

4.5	The operational ASDAR programme has also undergone a further change with the closure of the maintenance support infrastructure provided by the UK Met Office and a repair/maintenance contractor.  No further repairs are possible.  Changes have also been made to the data quality monitoring system with the Met Office closing the ASDAR Centre in March 2003.  KNMI has offered to take over part of the monitoring service.

4.6	The number of reporting ASDAR aircraft has continued to decline.  At the time of writing, only 3 aircraft are reporting on a reasonably regular basis.  Despite earlier advice by SAA that it would decommission its 2 units, one has continued for more than a year longer than suggested and continues to report on an irregular basis.  Data quality problems in temperature observations remain on several aircraft.

5.	Developing Programmes

5.1	The past year has seen significant progress being made by members in either developing and testing new programmes, or planning new AMDAR programmes.  Although no new systems have reached the stage of being able to exchange data on the GTS during that time, several systems are very close to doing so and it is only a matter of time before this will happen.  Of special note are the 4 new national programmes currently under test in East Asia, and the progress being made by potential new programmes in the Middle East and South America.  Also, the first large collaborative programme of targeted observations is under development in the data sparse areas of Central and West Africa through the leadership of ASECNA.

Canada

5.2	The comprehensive Canadian programme that was about to go operational a year ago struck a major problem with the quality of temperature data that also impacted on wind data quality.  The cause was traced to inappropriate sensor exposure on the Dash 8 100 aircraft.  The participating airline (Air Canada Jazz) has undertaken to replace the sensors.  Data from new Canadian aircraft currently under test is expected in the next few months that should not be affected by this problem.

Japan

5.3	Japan has established a successful and substantial trial operational programme in collaboration with 2 national airlines, JAL and ANA.  Data impact evaluation trials are being undertaken by JMA but data are not being exchanged on the GTS during the trial period in accordance with an agreement with the airlines.

Hong Kong, China

5.4	Hong Kong, China is beginning to see the benefits of its efforts over the past 2 years in pursuing the development of an AMDAR programme with its national airline Cathay Pacific.  Data being produced as part of a trial phase are being evaluated for quality and impact.  A second component is also being developed in collaboration with the Government Flying Services agency.

China

5.5	Advice has been received recently that China is developing a substantial AMDAR programme and is producing up to 10,000 observations daily.  Data are being assessed and used operationally in a limited capacity and will be exchanged on the GTS in the near future.  China has requested the assistance of the UK Met Office with conducting a user-training programme.

Republic of Korea

5.6	The Republic of Korea has made much progress in less than 12 months in developing its AMDAR programme in collaboration with Korean Air.  It was expected that the first test data would be received during the third quarter of 2003.  Noting that many aircraft are already configured with software, further rapid progress is anticipated over the next year including the exchange of data on the GTS.

Saudi Arabia

5.7	The Middle East programme continues to advance slowly.  Saudi Arabia continues to evaluate data being transmitted from several Saudia MD90 aircraft that are being received by PMA.  Data will be exchanged on the GTS once some minor encoding issues have been resolved and quality has been established.  E-AMDAR has offered to conduct routine data quality monitoring and advise on follow up activities.  The programme will then be extended to the entire MD90 fleet.

6.	Planned New Systems

6.1	The Russian Federation and Morocco continue to express interest in developing national programmes as they prepare basic infrastructure in their respective meteorological services.  E-AMDAR provides en-route data and a limited number of profiles in cities of both countries as part of its normal programme.  Of special interest are the expressions of interest and activities being undertaken in South America and the Middle East.

6.2	Activity has recently increased in the Middle East with Saudi Arabia continuing system development as the project leader and Oman expressing strong interest in developing a programme.  Discussions are taking place with local and regional airlines exploring potential collaboration.  The United Arab Emirates (UAE) is now actively working to develop a programme.  The airline and the meteorological service are in discussions with the AMDAR Panel as well as Lufthansa/Lido on the initial steps that need to be taken.  Iran has requested programme information and has informally indicated its desire to develop a programme.  However, current international relations are preventing any concrete steps being taken.  A number of coalition countries are working to re-establish meteorological services in Iraq.  Initial planning included AMDAR and it is known that the ACARS communications infrastructure will be improved in 2004 with the establishment of 2 ground stations, one each in Basra and Baghdad.  E-AMDAR provides targeted profiles in many of the cities in the region as part of its basic programme.

6.3	Poland and Hungary have indicated their intention to develop programmes and have been consulting with E-AMDAR, but recent changes in government situations have slowed progress.  E-AMDAR keeps a monitoring watch on and provides encouragement to several countries in the region who have indicated interest in the past including Finland, Ireland, Spain, Portugal, Switzerland, Austria, Italy, Iceland and Belgium.

7.	Workshops

7.1	The AMDAR Panel has been offering to assist countries considering the development of new programmes by holding national or preferably, regional workshops.  Formal invitations to conduct workshops have been received from the following countries:

-	Morocco (national programme);

-	Argentina (South America regional programme); and

-	Hungary (East European regional programme).

7.2	Other countries have informally indicated interest in holding workshops including:

-	Saudi Arabia and Oman (Middle East regional programme)

-	The Russian Federation (national programme)

-	China (East Asia regional programme)

8.	Targeted Programmes

8.1	Development of an extensive collaborative programme of targeted observations is well under way between E-AMDAR and ASECNA, an intergovernmental agency representing 14 Central and West African countries plus Madagascar.  This follows a very successful 2-day workshop conducted by the AMDAR Panel in Dakar, Senegal in November 2002.  E-AMDAR will provide controlled data from appropriate aircraft from 3 of its airlines that operate into the region.  Data is being provided already for a small number of countries on a daily basis.  Ghana and Nigeria although not part of the ASECNA, will also be included.  ASECNA will in turn reimburse E-AMDAR for the marginal costs of providing the data.  Once the targeted programme is fully operational, the next stage will commence to explore opportunities to develop AMDAR programmes in collaboration with local airlines.

8.2	E-AMDAR continues to provide data in a small demonstration targeted programme in the Caribbean region.  This is controlled remotely by Météo-France as a further demonstration of how cost effective and easy targeting can be.

8.3	With the completion of a financial package and new data control elements in its data acquisition system, E-AMDAR now has the infrastructure to provide similar targeted programme services any where in the world, provided the data are either exchanged on the GTS or sent direct.

9.	Data Optimisation

9.1	Improvements to the E-AMDAR automated optimisation system have continued that further enhance this very sophisticated and powerful system.  It was used on several occasions to quickly adjust regional coverage taking advantage of built-in redundancy when short, unexpected circumstances (such as airline strikes) caused large blocks of AMDAR reporting aircraft from flying.

9.2	Canada has also developed an optimisation system and the US and Australia are also planning the development of similar control systems.

10.	Other AMDAR Systems

Significant progress has been made in several alternative forms of AMDAR systems.  Design of the US Tropospheric Airborne Meteorological Data Relay (TAMDAR) system has been finalised and prototype testing has been completed.  Various versions are being developed for the first operational trials.  In addition to those being undertaken by the company, an extensive operational trial is due to commence in the north central US early in 2004 with 62 systems being installed on SAAB 340 regional aircraft.  Data impact studies as well as detailed system performance will be studied by a number of NOAA and NASA agencies.  Additionally, Météo-France will commence testing a system on behalf of the E-AMDAR group later this year.

11.	Sensors

11.1	As mentioned earlier, initial testing of the TAMDAR system has been completed and the first operational trials will take place later this year.  A great deal of interest has been shown by a number of countries in different parts of the world in this system as a potential provider of humidity data in the boundary layer and lower troposphere.  It will not have the capability of humidity measurements in the mid to upper troposphere.  Work continues in the US and UK on development of aviation humidity sensors.  Interest in accelerating work on the UK sensor being developed by Cambridge University has increased with several groups indicating interest in deploying it.

11.2	Testing of the Eddy Dissipation rate algorithm continues in the US by NCAR for the FAA and ICAO and new work has commenced in an alternative method at NOAA Forecast Systems Laboratory at a low level.  The technique using pressure fluctuations in the Pilot static Tube is similar to the one adopted by TAMDAR.

11.3	Development and testing of icing sensors continue in several companies in the US with a reporting and operational evaluation trial under way.  Canada is also planning to conduct its own evaluation programme.  Changes have been introduced to the WMO FM94 BUFR code to be able to report basic icing “on/off” situations.

12.	Data Impact

12.1	Evaluation work is continuing to better determine the impact AMDAR data has on NWP products and routine operational forecasting services.  However, of interest is the work to relate improved forecasts to concrete benefits to recipients and users of forecasts.  Several studies have been completed that produce hard numbers showing impacts on different aspects of aviation operations.

# Comments

2196 words