| WORLD METEOROLOGICAL ORGANIZATION _________________________ REGIONAL ASSOCIATION VI (EUROPA) MEETING OF THE COORDINATORS/RAPPORTEUR OF THE WORKING GROUP ON PLAnning and implementation of the www in region vi langen, germany, 23-25 January 2007 |  | Ravi/wg-piw-2007/Doc. 3(4) (22.1/2007) ITEM 2.2 ENGLISH only |
| --- | --- | --- |

Status report of the Coordinator of the Sub-group

on Regional Aspects of the ISS for Central

and Eastern  Europe

Submitted by Leonid Bezruk (Russian Federation)

________________________________________________________________

Summary and Purpose of Document

The document contains information on the current status ISS

In RA VI and the activities of the Coordinator on the Action Plan.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to take the content of this document into consideration.

References:

[1] Regional Association VI (Europe), Fourteenth Session, Heidelberg, 7-15 September 2005.

[2] Action Plan.

1. Background

The RA VI session (Heidelberg, Germany, &-15 September, 2005) set 13 tasks before the support on regional aspects of information systems and services (Global Telecommunication System and Data Management) and accepted Action Plan for which a form of monitoring was designed by the RA VI Steering Group on Strategic Plan an Action Plan. The status of implementation of the ISS in the South-Eastern and Eastern parts of Region VI gave the Association the greatest concern.

2. The current status of implementation in Region VI

The status of the ISS is described in detail in doc. 2.2(6), represented by co-coordinators on the ISS in RA VI to the ICT-ISS meeting (18-22 September, 2006).

The extracts from the document with some refinements and updates are given below.

2.1 Status of the RMTN in Regional Association VI

The majority of the RMTN links within the Western part of Region VI now run over RMDCN and use TCP/IP as the data transport protocol, with almost all the GTS links that use RMDCN now capable of operating at 64 kbps or greater.

The status of the RMTN in the south-east part of Region VI still remains not quite satisfactory. This is demonstrated by the status of the centres and telecommunication circuits in this part of Region as well as by the status of national observation data collection systems in the surface observational network.

7 of the circuits, that are specified in the plan for the RMTN as being in the eastern part of the region, still do not exist. It is proposed that 3 of these circuits be excluded from the RMTN plan but  it is planned to implement the remaining 4 circuits. Most of the circuits in this part of Region use leased analogue/digital channels or the Internet and a significant number of them are expected to migrate to the RMDCN.

The delay, or lack of plans, by NMCs in moving the circuits to the RMDCN is attributable to the fact that, for these NMCs,  the cost of leased lines is still much lower than the cost of leasing a PVC or MPLS from EQUANT. However  the difference between these costs is gradually reducing. Several of the RMTN circuits, namely the Moscow-Baku , Sofia-Tirana circuits either already operate over the Internet. The NMC Damask is not connected to the GTS.

The status of the circuits in the Central and Eastern half of the region is given at Table 1. A diagram showing the current status of the RMTN in Region VI is given at  Figure 1

2.2 Regional Meteorological Data Communications Network (RMDCN)

There are now 36 members of RA VI connected directly to the RMDCN. ECMWF and EUMETSAT are also connected. Five centres have duplicated access lines to the network for resilience. A list of the centres connected to the RMDCN is given at Table 2. Those not connected are listed at Table 3.

Following from decisions made by the 13th session of the RA VI in 2002, four other RTHs outside RA VI are also connected to form the GTS and IMTN: China, India, Japan and Saudi Arabia. See Figure 2.

The RMDCN has proved to be a reliable and effective means of providing an RMTN within RA VI. Some sample performance statistics are at Figures 3, 4 & 5.

The access lines from the centres to the network range in speed from 64Kb/s to 2Mb/s for NHMSs. ECWMF accesses at 34Mb/s. PVC (Permanent Virtual Circuits) are established between centres and will support traffic at the contracted CIR (Committed Information Rate). This may be different in each direction. The network allows the CIR to be exceeded in short bursts, and this is illustrated for one particular PVC by Figure 3. Details of the PVCs between the RTHs and the NHMSs are in Table 4.

The RMDCN is supplied by OBS (Orange Business Services, formerly known as Equant). The RMDCN contract is managed by ECMWF on behalf of RA VI.

A modification to the RMDCN contract in 2003 gave improved basic connections to member states that were completed in 2004. Since then, various centres improved their links and back-up arrangements.

Satellite broadcasting systems in Europe transferred to the DVB channels allowing to significantly increase their capacity and reliability.

2.3 Use of the Internet

All the RTHs and NMSs have access to the Internet,  with several centres enabling access to their servers for provision of data and products. A Virtual Private Network (VPN) over the Internet is being used between some centres.

The Internet in Region VI is used for:

- Reception of additional information which does not come over the GTS;

- Provision of information within countries as well as for other NMCs;

- Arrangement of the GTS circuits or their backing up;

- Observation data collection in the national network.

2.4 Revision of the RMTN plan

Following a joint meeting of the RMDCN Operations Committee and the RMDCN Steering Group in Moscow in 2004, approval was given to ECMWF to pursue the option of migrating the underlying network structure of the RMDCN from Frame Relay protocols to one based on the Multi Layer Packet Switching Protocol (MLPS). Pilot testing of this protocol took place during 2005 and 2006.

There is now a project in progress to migrate all of the RMDCN network to the new protocol. This project is covered by the fourth Supplement to the contract which was agreed and signed by ECMWF on 8 May 2006. Lines and routers have been ordered for the 40 NHMSs and two international organisations and most delivered before the end of 2006. The new network will be built in parallel to the existing RMDCN and the switch-over to the new network will be done in a few days, with operational acceptance completed at the middle of 2007.

The new network will have a higher basic bandwidth for all members, with improved back-up facilities. Many centres will also upgrade their access connections to increase resilience.

Initially, the new network will mirror the existing structure of specific PVCs between NHMSs, which in turn mirrored the original point-to-point links of dedicated lines in the original RMTN with inter-connected RTHs supporting NHMS in their area of responsibility.

The migration to the new protocol will eventually allow any-to-any connections, greatly increasing the flexibility of the network, as there will be no requirement within MLPS to pre-define PVCs, as with Frame Relay. However it will increase the day-to-day traffic management challenges. Currently, the traffic volume is controlled in the current network by the CIR (Committed Information Rate) on each of the PVCs.

MLPS as the underlying network protocol for RMDCN could also potentially provide solutions for back-up connections in the event of an outage of an RTH.

An Ad-Hoc working group was set up to look into the content of the RA VI EUMETCast/WWW broadcast.

2.5 Data Management

In the majority of Eastern Europe countries, the national observation data collection systems are either being upgraded, or are planned to be upgraded in the near future. These upgraded networks will employ modern technologies which will enable the cost of data collection to be reduced and  will also increase reliability and timeliness. All the countries concerned require support on the part of the WMO to enable them to realise their plans within acceptable timescales. The move from the existing, expensive and inefficient, data collection methods to the new ways of data transmission from stations to telecommunication centres will require appropriate refitting of the stations within in these countries. In addition older methods of communications, such as radio telegraphy, as currently used by some countries within the Region, need replacing with more modern communications (packet radio communication, satellites, cellular communications, data communication networks). Moreover, in some countries (Georgia, Kazakhstan, Azerbaijan, Armenia) there are problems with power supply on the stations and at telecommunication centres which does not enable timely transmission of data.

The collection of SYNOP data in Eastern and Central Europe was improved and is at the level of 95 per cent and can be considered as satisfactory. However reliability and timeliness of data collection of some countries is at a much lower level (Azerbaijan – SM 58.3%). The reasons for this situation are the inadequate status of observation/data collection systems as described above and the MSS technical status.  As emphasized above, the data collection systems, especially in Eastern part of Europe, are obsolete and require or are in the process of major change.

The TEMP data collection in this part of Europe is lower than in the rest of Europe (90%) and can be blamed on a lack of consumables and the ageing of technical observation equipment. Moreover, actual plans of observations sometimes disagree widely from those announced in Volume C1. The reason for the disagreement is late reporting of changes in sounding plans to a regional centre on the MTN and to the WMO Secretariat.

The CLIMAT/CLIMAT-TEMP data collection is at a slightly lower level as compared with required data. One of the reasons for such a situation is a discrepancy between actual observations and information transmitted in the GTS represented in Volumes A, C1, RBSN, RBCN. Due to the actions taken by the WMO Secretariat and RTHs this situation has recently improved. Nevertheless, it is necessary to continue this work on monitoring data arrival and to make contact with those NMCs where problems with data transmission emerge. It should be noted that in fact CLIMAT-TEMP data is transmitted in the WMO GTS on the area of responsibility of the RTHs Moscow and Sofia only by the following centres: RUMS, UMMN, LZSO, YRBK, LYBM. The rest do not transmit the data specified.

Day to day experience in Western Europe suggests that there still many badly formatted messages and bulletins causing unnecessary overheads. Also, the use of more highly automated systems seems to occasionally exacerbate the problem. These points are highlighted by a simple investigation carried out at RTH Exeter, counting the number of international rejected bulletins. See Figure 6, indicating the great variability from day to day. Further work is required to identify the root cause of these problems.

2.6 Future WMO Information System

The future WMO Information System, as agreed by CBS, includes the concepts of  Global Information System Centres to replace the roles of the RTHs, and an improved MTN to distribute the information held by the GISCs. RA VI has been involved in both the improved MTN and the development of a GISC to be sited within RA VI.

GISC

Centres such as Moscow and Sofia are planning changes to their telecommunications and information systems to enable them to be ready for the introduction of FWIS. The Russian Federation plans as the first step to deploy GISC in Moscow and CDPC in Obninsk. Also, pilot projects to test different ways of improving the operational and future WMO information system are being conducted

The United Kingdom, France and Germany, in co-operation with EUMETSAT and ECMWF, are developing the concept of a virtual GISC (V-GISC). An ad-hoc group comprising representatives from the 3 countries and the 2 organisations is involved in a European Community sponsored project called SIMDAT to demonstrate a prototype system using various modern technologies including XML, Web Services and the WMO Core Metadata Profile. A variety of data types are being demonstrated in the system, such as synoptic, aviation, ATD and climate. The prototype will be demonstrated at CBS in Korea in November 2006, connecting to data servers in France, Germany, UK and ECMWF.

DWD have proposed the use of XML to implement the WMO Bulletin Catalogue. The related XML schemas use the proposed WMO Core Metadata Profile.

2.7 Improved MTN

The Improved MTN (IMTN) comprises 2 interconnected telecommunications clouds. The RMDCN is one of these Clouds, the other is the ‘Pacific Cloud’ network currently comprising links between Australia, the United Kingdom, Japan and the United States of America. A diagram showing the proposed configuration of the IMTN is given at Figure 2.

To accommodate this proposed structure, approval was given in 2002, for centres outside RA VI to be allowed to connect into the RMDCN, for the purpose of establishing direct GTS connections to centres within RA VI. As a consequence, Japan, India and China and Saudi Arabia are now connected into RMDCN. No further progress has been made with Kenya, Senegal, Algeria and Egypt joining the RMDCN.

Within the ‘Pacific Cloud’ (Network 1 in Figure 3), links have already been established between Australia-UK, Australia – Japan, USA - UK and USA – Japan. It is not clear whether or not the links Brasilia-Washington and Buenos Aries-Washington will be established over this network. This will depend upon the future development of the RMTN within RA III.

3. The activity of Co-Coordinator related to the implementation of the tasks set by the Regional Association

- Coordinator conducted meetings or conversations with representatives of all the centres of the area of responsibility of RTH Moscow and RTH Sofia for the purpose of the clarification of the status of ISS and plans on their improvement;

- With the support of Coordinator a number of centres (Tbilisi, Alma-Ata, Yerevan) refined the Catalogue of Meteorological Data – Volume C1 and ;

- Along with NMC Minsk, the tests on backing the Moscow-Minsk circuit via VPN Internet were successfully executed. Currently this technology is used in real-time practice in this and other circuits. It is planned to extend it over the whole circuits.

- Prices on the connection to the RMDCN for the states not acceded to it were requested.

- The prices were slightly reduced but they still remain unacceptably high for the majority of them. Only some of them are considering the possibility of accepting them (Azerbaijan, Georgia);

- Inadequate factors of data collection from observation stations and their input to the GTS were discussed with the governing body of Meteo Service of Azerbaijan. The Meteo Service contemplated some arrangements to rectify those deficiencies and to establish a more reliable circuit between NMC Baku and RTH Moscow;

- Participation in generating the requirements for GISCs and DCPCs within the framework of CBS ET on WIS GISCs and DCPCs (ET-WISC);

- Fostering the works on testing the technologies for collection and dissemination of information, GISCs, DCPCs;

- Participation in the preparation of documents of the meeting ICT-ISS, CBS/ISS goiut meeting ICT-MTN and ET-0I;

- Radar data exchange in BUFR between NMCs Kiev, Minsk, RTH Moscow was arranged. Provision has been made for arranging the data exchange with NMC Warsaw;

- Participation in conducting the tests on the migration to the MPLS, preparation of Migration Plan;

- Monitoring of SINOP, TEMP, CLIMAT data arrival from Region VI for the compliance with the Catalogue of Meteorological Bulletins, Volume C1, clarification of problems with data arrival when data arrival is less than 90 per cent.

Figure 2

Table 1

| № | Circuit | Status | Speed (Kbps) | Protocol | Data type | Future (2006-2007) |
| --- | --- | --- | --- | --- | --- | --- |
|  | Moscow – Exeter | MTN | FR RMDCN (Equant) CIR: Rx-64, Tx-8 Access line (backup): Mos–256 (256 ISDN) Exeter–512 (384 ISDN) | FTP WMO | A/N, BIN FAX | IP/VPN MPLS (OBS) Mos – 512 Kbps |
|  | Moscow – Prague | MTN | FR RMDCN (Equant) CIR: Rx-16, Tx-8 Access (ISDN backup): Mos–256 (256 ISDN) Prag–512 (384 ISDN) | FTP WMO | A/N, BIN FAX | IP/VPN MPLS (OBS) Mos – 512 Kbps |
|  | Moscow – Sofia | MTN | FR RMDCN (Equant) CIR: Rx/Tx –16/16 Access (ISDN backup): Mos–256 (256 ISDN) Sofia–256 (128 ISDN) | FTP WMO | A/N, BIN FAX | IP/VPN MPLS (OBS) Mos – 512 Kbps Sofia – 512 kbps |
|  | Moscow – New-Delhi | MTN | FR RMDCN (Equant) CIR: Rx/Tx –16/16 Access (ISDN backup): Mos–256 (256 ISDN) ND–64 (64 ISDN) | FTP WMO | A/N, BIN | IP/VPN MPLS (OBS) Mos – 512 Kbps |
|  | Moscow – Cairo | MTN | Digital line Tx/ Rx – 64 | FTP WMO | A/N |  |
|  | Moscow – Norkkoping | RMTN | FR RMDCN (Equant) CIR: Rx/Tx –16/16 Access (ISDN backup): Mos–256 (256 ISDN) Nork–1536 (384 ISDN) | FTP WMO | A/N, FAX BIN | IP/VPN MPLS (OBS) Mos – 512 Kbps |
|  | Moscow – Minsk | RMTN | Digital line Tx/Rx – 64 (Internet back-up) | TCP/IP-Socket (Special) | A/N, BIN FAX |  |
|  | Moscow – Kiev | RMTN | Digital line Tx, Rx – 64 (Internet back-up) | FTP WMO | A/N, FAX BIN |  |
|  | Moscow – Tbilisi | RMTN | Telephone leased line V.34 ITU Tx/Rx – 9,6 | TCP/IP-Socket (Special) | A/N, FAX | IP/VPN MPLS (OBS) CIR: Rx-8 Kbps Tx-16 Kbps Access line: Mos – 512 Kbps TCP/IP-Socket or FTP WMO |
|  | Moscow – Baku | RMTN | Through Internet |  | A/N, FAX | IP/VPN MPLS (OBS) CIR: Rx-8 Kbps Tx-16 Kbps Access line: Mos – 512 Kbps TCP/IP-Socket or FTP WMO |
|  | Moscow – Erevan | RMTN | Telegraphic adapter 200 bod (via Rostov), Through Internet | Async Email, Web-access | A/N, FAX | Telephone leased line TCP/IP-Socket or FTP WMO |
|  | Moscow – Kishinev | RMTN | Telephone leased line V.34 ITU Tx/ Rx – 21.6 | TCP/IP-Socket (Special) | A/N, FAX |  |
|  | Moscow – Beijing | Inter-regional | FR RMDCN (Equant) CIR: Rx/Tx –8/8 Access (ISDN backup): Mos–256 (256 ISDN) BJ–256 (256 LL) | FTP WMO | A/N, FAX BIN | IP/VPN MPLS (OBS) Mos – 512 Kbps |
|  | Moscow – Novosibirsk | Inter-regional | Digital line Tx/ Rx – 64 (Internet back-up) | TCP/IP-Socket (Special) | A/N, BIN FAX | Digital line Tx/ Rx – 512 (Internet back-up) |
|  | Moscow – Khabarovsk | Inter-regional | Digital line Tx/ Rx – 64 (Internet back-up) | TCP/IP-Socket (Special) | A/N, BIN, FAX, Satellite images | Digital line Tx/ Rx – 512 (Internet back-up) |
|  | Moscow – Tashkent | Inter-regional | Telephone leased line V.34 ITU Tx/Rx –19,2 (Internet back-up) | TCP/IP-Socket (Special) | A/N, BIN FAX | Digital line Tx/ Rx – 64 Kbps |
|  | Moscow – Almaty | Inter-regional | Telephone leased line V.34 ITU Tx, Rx –19,2 (Internet back-up) | TCP/IP-Socket (Special) | A/N, BIN, FAX | Digital line Tx/ Rx – 64 Kbps |
|  | Moscow – Hanoi | Inter-regional | Satellite Telegraphic adapter 100 bod | Async | A/N |  |
|  | Moscow – Tehran (NO) | Inter-regional | Telegraphic adapter 100 bod | Async | A/N | Telephone leased line TCP/IP FTP WMO (A/N, BIN) |
|  | Moscow – Bucharest | bilateral | FR RMDCN (Equant) CIR: Rx/Tx –8/16 Access line(backup): Mos–256(256 ISDN) Buch-128 kbps (-) | FTP WMO | All (ASCII, Binary) | RMTN IP/VPN MPLS (OBS) Mos – 512 Kbps |
|  | Moscow – Melbourne | bilateral | Through Internet | FTP WMO | A/N, BIN | via Internet |
|  | Moscow – - Helsinki (NO) | RMTN |  |  |  |  |
|  | Kiev – Kishinev (NO) | RMTN |  |  |  |  |
|  | Tbilisi – Baku (NO) | RMTN |  |  |  |  |
|  | Baku - Ankara | RMTN | Through Internet |  |  |  |
|  | Sofia - Prague | MTN | FR RMDCN (Equant) CIR: Rx/Tx – 16/8 Access line (backup): Sof–256(128 ISDN) Prag–512 (384 ISDN) | FTP WMO | A/N, BIN FAX | IP/VPN MPLS (OBS) Sofia – Access line (NAS backup): 512 kbps (256 Kbps) |
|  | Sofia - Toulouse | RMTN | FR RMDCN (Equant) CIR: Rx/Tx – 64/8 Access line(backup): Sof–256(128 ISDN) Toul-1M (1 M Mis Cr) | FTP WMO | A/N, BIN FAX | IP/VPN MPLS (OBS) Sofia – Access line (NAS backup): 512 kbps (256 Kbps) |
|  | Sofia - Bucharest | RMTN | FR RMDCN (Equant) CIR: Rx/Tx – 8/32 Access line (backup): Sof-256 Kbps(128 ISDN) Buch: 128 kbps (-) | FTP WMO | All (ASCII, Binary) | IP/VPN MPLS (OBS) Sofia – 512 kbps |
|  | Sofia – Skopje | RMTN | FR RMDCN (Equant) CIR: Rx/Tx – 8/16 Access line(backup): Sof–256(128 ISDN) Skopje-64 (64 ISDN) | FTP WMO | All (ASCII, Binary) | IP/VPN MPLS (OBS) Sofia – 512 kbps |
|  | Sofia - Belgrade | RMTN | Telephone leased line V.34 ITU Tx, Rx – 9,6 Kbps | FTP WMO | All (ASCII, Binary) |  |
|  | Bucharest – Kishinev | RMTN | Telephone leased line Async,PPP, 19,2 kbps (min.) | FTP | ASCII, Binary |  |
|  | Sofia - Tirana (NO) | RMTN | IPSec VPN on Internet | FTP WMO | All (ASCII, Binary) |  |
|  | Sofia – Larnaca (NO) | RMTN |  |  |  | Should be a Project for a connection of NMC Larnaca to RTH Sofia by VPN/Internet. |
|  | Sofia – Damascus (NO) | RMTN |  |  |  | NMC Damascus is not connected to GTS. It’s connected to AFTN (V.35). Should be a Project for a connection of NMC Damascus to RTH Sofia by VPN/Internet. |
|  | Larnaca – Athens | bilateral | Telephone leased line 21,6 Kbps | FTP |  |  |
|  | Belgrade – Vienna | bilateral | FR RMDCN (Equant) CIR: Rx/Tx – 8/8 Access line (backup): Belgrade -128 Kbps (-) | FTP | ASCII, Binary |  |
|  | Belgrade - Offenbach | bilateral | FR RMDCN (Equant) CIR: Rx/Tx – 32/16 Access line (backup): Belgrade -128 Kbps (-) | FTP | ASCII, Binary |  |
|  | Belgrade - Budapest | bilateral | FR RMDCN (Equant) CIR: Rx/Tx – 16/8 Access line (backup): Belgrade -128 Kbps (-) | FTP | ASCII, Binary |  |

Table 2

| Country/Site connected to RMDCN (* outside RA-VI) |  | Access line (bits per sec) |
| --- | --- | --- |
| Austria (Vienna) | RTH | 512k |
| Belgium (Brussels) |  | 512k |
| Bulgaria (Sofia) | RTH | 256k |
| *China (Beijing) | *RTH | 256k x 2 |
| Croatia (Zagreb) |  | 64k |
| Czech Republic (Prague) | RTH | 512k |
| Denmark (Copenhagen) |  | 1M |
| Estonia (Tallinn) |  | 64k |
| Finland (Helsinki) |  | 384k |
| France (Toulouse) | RTH | 2M x2 |
| Germany (Offenbach) | RTH | 1M x2 |
| Greece (Athens) |  | 384k |
| Hungary (Budapest) |  | 256k |
| Iceland (Reykjavik) |  | 64k |
| *India (New Delhi) | *RTH | 64k |
| Ireland (Dublin) |  | 384k |
| Italy (Rome) | RTH | 768k |
| *Japan (Tokyo) | *RTH | 128k |
| Jordan (Amman) |  | 64k |
| Latvia (Riga) |  | 128k |
| Lebanon (Beirut) |  | 64k |
| Lithuania (Vilnius) |  | 64k |
| Luxembourg (Luxembourg) |  | 384k |
| FYR of Macedonia (Skopje) |  | 64k |
| The Netherlands (De Bilt) |  | 384k |
| Norway (Oslo) |  | 384k |
| Poland (Warsaw) |  | 64k |
| Portugal (Lisbon) |  | 384k |
| Romania (Bucharest) |  | 64k |
| Russian Federation (Moscow) | RTH | 256k |
| *Saudi Arabia (Jeddah) | *RTH | 64k |
| Serbia-Montenegro (Belgrade) |  | 128k |
| Slovakia (Bratislava) |  | 128k |
| Slovenia (Ljubljana) |  | 128k |
| Spain (Madrid) |  | 2M |
| Sweden (Norrköping) | RTH | 1.5M |
| Switzerland (Zurich) |  | 512k |
| Turkey (Ankara) |  | 384k |
| *United Arab Emirates (Abu Dhabi) |  | 64k |
| United Kingdom (Exeter) | RTH | 512k |
| ECMWF (Reading) |  | 34MB x 2 |
| EUMETSAT (Darmstadt) |  | 512k x 2 |

Table 3

RA-VI Members not connected to RMDCN

Albania

Armenia

Azerbaijan

Belarus

Bosnia-Herzegovina

Cyprus

Georgia

Israel

Kazakhstan

Malta

Moldova

Monaco

Syria

Ukraine

Table 4: RTH PVC connections to NHMSs

| * Outside RA-VI | RTH | PVC In (Kb/s) | PVC Out (Kb/s) |
| --- | --- | --- | --- |
| Austria |  |  |  |
| Croatia (Zagreb) |  | 64 | 8 |
| Czech Republic (Prague) | RTH | 8 | 16 |
| Germany (Offenbach) | RTH | 64 | 64 |
| Hungary (Budapest) |  | 32 | 8 |
| Serbia-Montenegro (Belgrade) |  | 8 | 8 |
| Slovakia (Bratislava) |  | 48 | 16 |
| Slovenia (Ljubljana) |  | 64 | 8 |
| Bulgaria |  |  |  |
| Czech Republic (Prague) | RTH | 8 | 16 |
| France (Toulouse) | RTH | 8 | 64 |
| FYR of Macedonia (Skopje) |  | 16 | 8 |
| Romania (Bucharest) |  | 32 | 8 |
| Russian Federation (Moscow) | RTH | 16 | 16 |
| China |  |  |  |
| Germany (Offenbach) | RTH | 48 | 48 |
| *India (New Delhi) | *RTH | 8 | 8 |
| *Japan (Tokyo) | *RTH | 42 | 96 |
| Russian Federation (Moscow) | RTH | 8 | 8 |
| Czech Republic |  |  |  |
| Austria (Vienna) | RTH | 16 | 8 |
| Bulgaria (Sofia) | RTH | 16 | 8 |
| France (Toulouse) | RTH | 16 | 128 |
| Germany (Offenbach) | RTH | 32 | 32 |
| Poland (Warsaw) |  | 16 | 8 |
| Russian Federation (Moscow) | RTH | 16 | 8 |
| France |  |  |  |
| Belgium (Brussels) |  | 92 | 48 |
| Bulgaria (Sofia) | RTH | 64 | 8 |
| Czech Republic (Prague) | RTH | 128 | 16 |
| Germany (Offenbach) | RTH | 64 | 64 |
| Italy (Rome) | RTH | 32 | 32 |
| Portugal (Lisbon) |  | 64 | 32 |
| Spain (Madrid) |  | 32 | 32 |
| Switzerland (Zurich) |  | 32 | 32 |
| United Kingdom (Exeter) | RTH | 128 | 384 |
| Germany |  |  |  |
| Austria (Vienna) | RTH | 64 | 64 |
| *China (Beijing) | *RTH | 48 | 48 |
| Czech Republic (Prague) | RTH | 32 | 32 |
| France (Toulouse) | RTH | 64 | 64 |
| Greece (Athens) |  | 32 | 32 |
| Italy (Rome) | RTH | 32 | 32 |
| Jordan (Amman) |  | 16 | 8 |
| Poland (Warsaw) |  | 16 | 8 |
| *Saudi Arabia (Jeddah) | *RTH | 16 | 8 |
| Serbia-Montenegro (Belgrade) |  | 32 | 16 |
| Spain (Madrid) |  | 16 | 16 |
| Sweden (Norrköping) | RTH | 64 | 64 |
| Switzerland (Zurich) |  | 128 | 64 |
| Turkey (Ankara) |  | 32 | 32 |
| *United Arab Emirates (Abu Dhabi) |  | 16 | 16 |
| United Kingdom (Exeter) | RTH | 64 | 64 |
| EUMETSAT (Darmstadt) |  | 128 | 128 |
| India |  |  |  |
| *China (Beijing) | *RTH | 8 | 8 |
| *Japan (Tokyo) | *RTH | 32 | 32 |
| Russian Federation (Moscow) | RTH | 16 | 16 |
| Italy |  |  |  |
| France (Toulouse) | RTH | 32 | 32 |
| Germany (Offenbach) | RTH | 32 | 32 |
| Greece (Athens) |  | 32 | 32 |
| Lebanon (Beirut) |  | 16 | 16 |
| Turkey (Ankara) |  | 32 | 32 |
| United Kingdom (Exeter) | RTH | 16 | 16 |
| Japan |  |  |  |
| *China (Beijing) | *RTH | 96 | 48 |
| *India (New Delhi) | *RTH | 32 | 32 |
| Russia |  |  |  |
| Bulgaria (Sofia) | RTH | 16 | 16 |
| *China (Beijing) | *RTH | 8 | 8 |
| Czech Republic (Prague) | RTH | 8 | 16 |
| *India (New Delhi) | *RTH | 16 | 16 |
| Romania (Bucharest) |  | 16 | 8 |
| Sweden (Norrköping) | RTH | 16 | 16 |
| United Kingdom (Exeter | RTH | 8 | 64 |
| Saudi Arabia |  |  |  |
| Germany (Offenbach) | RTH | 8 | 16 |
| Sweden |  |  |  |
| Denmark (Copenhagen) |  | 32 | 32 |
| Finland (Helsinki) |  | 64 | 64 |
| Germany (Offenbach) | RTH | 64 | 64 |
| Latvia (Riga) |  | 64 | 16 |
| Lithuania (Vilnius) |  | 16 | 8 |
| Norway (Oslo) |  | 64 | 64 |
| Russian Federation (Moscow) | RTH | 16 | 16 |
| United Kingdom |  |  |  |
| Belgium (Brussels) |  | 32 | 32 |
| Denmark (Copenhagen) |  | 32 | 32 |
| France (Toulouse) | RTH | 384 | 128 |
| Germany (Offenbach) | RTH | 64 | 64 |
| Iceland (Reykjavik) |  | 16 | 16 |
| Ireland (Dublin) |  | 64 | 64 |
| Italy (Rome) | RTH | 16 | 16 |
| The Netherlands (De Bilt) |  | 64 | 64 |
| Norway (Oslo) |  | 32 | 32 |
| Portugal (Lisbon) |  | 32 | 32 |
| Russian Federation (Moscow) | RTH | 64 | 8 |
| Spain (Madrid) |  | 32 | 32 |

Figure 3: Example of traffic over PVC with CIR occasionally exceeded

Figures 4 & 5

# Text boxes

Network II

(RA VI RMDCN Ext.)

Moscow

New Delhi

Managed

data communication network

Cairo

Brasilia

Offenbach

Algiers

Dakar

Toulouse

Prague

Jeddah

Network I

Washington

Nairobi

Beijing

Tokyo

Buenos Aires

Melbourne

Sofia

Exeter