| WORLD METEOROLOGICAL ORGANIZATION _________________________ EXPERT MEETING ON ENHANCED UTILIZATION OF DATA COMMUNICATION SERVICES, ESP. INTERNET WELLINGTON, 11-16 DECEMBER 2003 |  | EM-DCS-INT 2003/Doc. 2.1(4) (5.XII.2003) ____________ ITEM 2.1 ENGLISH only |
| --- | --- | --- |

## An example of progress in data serving through the Internet

(Submitted by Hiroyuki ICHIJO (Japan) )

Summary and purpose of document This document introduces an outline of the RSMC Data Serving System operated by JMA as an example of data serving systems through the Internet.

ANNEX :   Guidance to the RSMC Data Serving System (the latest version)

1.  RSMC Data Serving System and JMA Internet connectivity

The RSMC Data Serving System (DSS) operated by JMA has been providing NWP products and global observational data to NMCs mainly in the Asian region through the Internet since 1995.  To meet user requirements in expanding data services the DSS was upgraded by the new one in April 2002.  The new DSS is a cluster system consists of three PC servers (see Figure 1) in DMZ (De-Militarized Zone).  It has sufficient capability and reliability to handle 90 ftp sessions simultaneously with necessary performance. Users are able to access to the DSS by standard ftp commands with authentication procedures.  The DSS identifies accessing from an authenticated user by a user ID, a user password and an IP address of a client host.

There are two permanent connections to the Internet Service Providers (ISPs) for multi-homed connectivity which provides more reliability than the case of only one ISP.  Total bandwidth of 18Mbps is enough to meet recent requirements in providing data to users at present.

2.  Access throughput to the RSMC DSS of JMA

As Figure 2 shows, generally throughputs have been increased for the last three years thanks to improvement of each user’s Internet environment.  However the throughput fluctuated from day to day.  The reasons seem to be quite complex, that is, impact factors are not only unexpected Internet traffic condition but also bottleneck of access circuits at both ends, tentative performance deterioration of server, client and/or ISP’s facilities, inappropriateness of the active session number and so on.

Hong Kong, Australia, Malaysia, Singapore and Brunei keep enough throughputs to retrieve the whole of NWP products routinely.

- Guide to access to the RSMC DSS

Only registered uses are able to access the RSMC DSS by the passwords and User Identifications (UIDs) assigned by JMA with permitted IP addresses of client hosts which are registered beforehand.  For security reason, each user is requested to change the passwords once a month.

The guidance to access to the RSMC DSS (see ANNEX) is prepared for NMCs to carry technical information and to show procedures in access with appropriate security.  Individual NMCs are able to access the RSMC DSS of JMA under the guidance.

### ANNEX

August 2003

Japan Meteorological Agency

Guidance to the RSMC Data Serving System

This Guidance was compiled by the Japan Meteorological Agency who operates the RSMC Data Serving System (referred to as DSS hereinafter) with intent to:

(a) Give users technical information on DSS, and

(b) Request users to follow procedures to keep the security of DSS.

DSS users are invited to peruse this Guidance before they first connect DSS.

__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/__/

TABLE of CONTENTS

Pages

1. How to obtain the data and products from the data server ...............................................................	2

(1) Hardware/software requirements to access the data server ....................................................	2

(2) Client registration ...................................................................................................................	2

(3) Procedures to obtain data and products ..................................................................................	2

(4) An example of ftp procedures ................................................................................................	2

a) Log in ................................................................................................................................	2

b) Changing directory ..........................................................................................................	3

c) File list of the directory ...................................................................................................	3

d) Setting file transfer type ..................................................................................................	3

e) Obtaining files .................................................................................................................	3

f) Log out ..............................................................................................................................	4

2. Exchange of operational information ..............................................................................................	4

(1) Possible contents of operational information ........................................................................	4

a) From the User to the Administrator ................................................................................	4

b) From the Administrator to the User ................................................................................	4

(2) Communication means ...........................................................................................................	4

3. Contents and formats of data and products ......................................................................................	5

(1) Kinds of data and products ....................................................................................................	5

a) Numerical prediction products produced by JMA ..........................................................	5

b) Observational data ...........................................................................................................	5

c) Satellite derived data .......................................................................................................	5

d) Miscellaneous ...................................................................................................................	5

(2) Period .....................................................................................................................................	5

(3) File format ..............................................................................................................................	5

a) Individual file ...................................................................................................................	5

b) Archived file ....................................................................................................................	5

c) Compressed file ...............................................................................................................	5

(4) Structure of directories and filenames ...................................................................................	6

a) Structure of directories ....................................................................................................	6

b) Filename ..........................................................................................................................	6

(5) Storage time of numerical prediction products ......................................................................	7

(6) Overview of data storage in the Server ..................................................................................	7

APPENDIX 1:  PASSWORDS MANAGEMENT ............................................................................	10

APPENDIX 2:  Usage of the ftp commands .....................................................................	12

1. How to obtain the data and products from the data server

(1) Hardware/software requirements to access the data server

A computer system connected to the Internet is required to obtain the data and/or products for each user country (referred to as User hereinafter).  Software required should have a function to support the 'ftp' commands.  Software for decompressing and extracting files from an archived file with compression may also be required.  In addition, it is necessary that User has a circumstance which allows exchange of Internet mails (e-mails) to communicate with RSMC/DSS Administrator (referred to as Administrator hereinafter) to exchange operational information.

(2) Client registration

The HOST machine or its network equipment (referred to as Client hereinafter) of each User should be registered to the RSMC data server (referred to as Server hereinafter) for logging into it beforehand.  One Client is allowed registration for one User.  The following items should be registered in the Server for each Client:

a)	IP address of the Client (Source IP address to be used for accesses to the Server)

b)	User ID

c)	User Password

Items a) should be notified to the Administrator prior to commencement of access to the Server.  Then the Administrator will provide the User ID and Password that allow each Client to access the Server.  Each User is requested to change the Password once a month in order to properly maintain the security of DSS.  Detailed procedures for Password management are shown in Appendix 1.

(3) Procedures to obtain data and products

The Server stores data and products in the UNIX file formats.  Each file is stored in an appropriate directory which is classified by date-time and data/product type.  Since the files are updated whenever new data or products become available at the Server, Users are suggested to log in after the objective data or products are supposed to be available.

Access to the Server starts with establishment of an ftp session targeting the Server’s symbolic name “rsmc.kishou.go.jp”.  Please note that the IP address will not be used as a target for access to the Server.  After receiving a proper response from the Server, User may log in the session with registered User ID and Password and then files can be obtained using ftp commands.

(4) An example of ftp procedures

Procedures for obtaining NWP products in the GRIB form for 12 UTC 15th April 2002 is presented below as an example.  Further information about usage of ftp commands is shown in Appendix 2.

a) Login

Access to the Server by ftp command

|  | % ftp rsmc.kishou.go.jp <= establishing a sesssion by ftp command Connected to rsmc <= connection message from the Server : <= message from the Server Name : yyyyyy <= key in the user ID 331 Password required for yyyyyy. <= message from the Server Password:ZZZZZZZZ <= key in the user password 230 User yyyyyy logged in. <= login message from the Server |
| --- | --- |

where,	rsmc.kishou.go.jp	:	host name of the Server

yyyyyy	:	user ID

ZZZZZZZZ	:	user password

underlined parts	:	keying-in by the Client

b) Changing directory

Just after the login User is at the root directory (/) of the Server.  User should move to an appropriate directory where the objective files are stored, by using 'cd' command.  Relative path shall be used to indicate the target directory.

In this example, target files are supposed to be stored in the directory /jp034/200204/1512/g02.

|  | ftp> cd jp034/200204/1512/g02 <= change directory command 250 CWD command successful. <= message from the Server |
| --- | --- |

c) File list of the directory

User may wish to know what files are stored in the current directory by 'dir' or 'ls' command.

|  | ftp> dir (or ls) <= file list command 227 Entering Passive Mode <= message from the Server 150 Opening ACSII mode data connection for file list <= message from the Server -rw-rw-rw- 1 TOKYO JMA 11123 Apr 15 16:52 heca88 -rw-rw-rw- 1 TOKYO JMA 11123 Apr 15 16:52 hecb88 ··············· file list from the Server -rw-rw-rw- 1 TOKYO JMA 11123 Apr 15 16:52 hzcy50 -rw-rw-rw- 1 TOKYO JMA 11123 Apr 15 16:52 hzcz50 226 Transfer complete. <= message from the Server |
| --- | --- |

d) Setting file transfer type

User is requested to set the file transfer type by 'binary' or 'ascii' command as necessary.  User is requested to set the binary type if the user wants to get data or product files.  In case of information files (ASCII text files), User is requested to set the ascii type.  The default transfer type when User logs into the Server is the binary type.

|  | ftp> binary <= setting the binary type 200 Type set to I. <= message from the Server |
| --- | --- |

or

|  | ftp> ascii <= setting the ascii type 200 Type set to A. <= message from the Server |
| --- | --- |

e) Obtaining files

To obtain objective files, User should use 'get' or 'mget' command.  The following example shows how to obtain the file of 6-hour prediction of temperature for 850 hPa.

|  | ftp> get htcb85 <= obtaining command local: htcb85 remote: htcb85 227 Entering Passive Mode 150 Opening BINARY mode data connection for htcb85 (11123 bytes). messages from the Server 226 Transfer complete. 11123 bytes received in 0.9107 secs (1.2e+01 Kbytes/sec) |
| --- | --- |

In addition to the above example, the following functions are available which may help users to obtain files efficiently.

- Obtaining files stored in a different directory

The following example shows how to obtain the file containing 6-hour prediction of temperature for 850 hPa stored in the directory '/jp034/200204/1512/g02' in case that User is in the root directory.

|  | ftp> get /jp034/200204/1512/g02/htcb85 |
| --- | --- |

Note:	In this case, it is assumed that User has prepared the same directories on the harddisk of the Client.

- Obtaining multiple files

This example shows how to obtain plural files by a single command.

|  | ftp> mget hhcc85 hhcc70 hhcc50 hhcc30 hhcc20 |
| --- | --- |

- Obtaining multiple files with the 'Wild card'

'Wild cards' can be used in the filename and are represented by an asterisc (*).  The following example shows how to obtain the same files as the above example using the wild cards.

|  | ftp> mget hhcc* |
| --- | --- |

f) Logout

User may repeat above procedures b), c), d) and e) as necessary until obtain all objective files.  After completion, User should log out from the Server by using 'bye' command.

|  | ftp> bye <= logout command 221 Goodbye. <= message from the Server |
| --- | --- |

2. Exchange of operational information

(1) Possible contents of operational information

The following are common candidates of operational information to be exchanged between User and the Administrator.  The Administrator will act as the focal point for operational aspects of the DSS.

a) From the User to the Administrator

- Notification of changing IP address for the Client

- Inquiry to RSMC Tokyo

- Others

b) From the Administrator to the User

Common information for all Users

- Notification about change of data and/or products

(e.g. structures of directories, file names, types of data, etc.)

- Notification about change of operational procedures

(e.g. store times of data and products, procedures to obtain data files, etc.)

- Notification about password change

- Notification about temporary suspension of service (only when it is foreseeable)

Information for each User

- Reminder to change User’s Password

- Advices on operational problems

(2) Communication means

E-mails are used to exchange operational information between User and the Administrator.  Every User is requested to have an e-mail address for this purpose and keep the Administrator informed when it is changed.  E-mail address for the Administrator is rsmc-jma@hq.kishou.go.jp .

3. Contents and formats of data and products

(1) Kinds of data and products

a) Numerical prediction products produced by JMA

- Global Spectral Model (GSM) products in the GRIB code form for the global area at both 1.25 and 2.5-degree resolutions with forecast hour up to 192 hours

- Global Wave Model (GWM) products in the GRIB code form for the ocean areas of the globe at both 1.25 and 2.5-degree resolutions with forecast hour up to 192 hours

- GSM Weekly Ensemble Forecast products (ensemble mean and standard deviation) in the GRIB code form for the global area at 2.5-degrees resolution

b) Observational data

SYNOP, SHIP, BUOY, TEMP and PILOT bulletins exchanged over the GTS

c) Satellite derived data

- Cloud amount and equivalent blackbody temperature (GRIB code form)

- High density cloud motion vectors around the center of a tropical cyclone (BUFR code form)

d) Miscellaneous

Tropical cyclone related information (BUFR code form)

(2) Period

Period of data/product files kept on the Server is 24 hours.

(3) File format

a) Individual file

Data and products on the Server usually have a format of a GTS bulletin and each bulletin forms an individual UNIX file.  Some of GSM products are stored as archived files (see b below) in addition to individual files in the same directory.

Contents of the file start with a WMO heading followed by text of the bulletin as shown below.

|  | WMO heading | Text |
| --- | --- | --- |

b) Archived file

Observational data and some products are stored as archived UNIX files (so-called tar files) which consist of a number of individual files.  For observational data, files containing GTS bulletins for the same time, same region and same type of obsevations are included in an archived file.  GSM products (except for 2.5-degree resolution for the Asian area) are combined into an archived file according to series of forecast hours or levels in the atmosphere.  The structure of a tar archived file is as follows:

|  | Tar control word | File 1 (bulletin 1) | Tar control word | File 2 (bulletin 2) | ..... |
| --- | --- | --- | --- | --- | --- |
|  |  | WMO heading | Text |  | WMO heading | Text |  |

|  | ..... | Tar control word | File n (bulletin n) |
| --- | --- | --- | --- |
|  |  |  | WMO heading | Text |

c) Compressed file

Files containing observational data are compressed by the 'gzip' command and the compressed files are stored in addtition to original ones in the same directory of the Server.  User may retrieve whichever type of files.  Retrieval of compressed files is expected to make best use of transmission capacity between the Server and the Client.

(4) Structure of directories and filenames

# a) Structure of directories

jp034 / yyyymm / YYGG / type / file

1st directory (jp034)	:   jp034 (fixed)

2nd directory (yyyymm)	:   yyyy : year	  mm : month

3rd directory (YYGG)	:   YY : day	  GG : hour (in UTC)

4th directory (type)	:   Type of data/products is defined by the following directory names:

# For GSM products at 1.25-degree resolution in thinned grid for the global area

# GI	: analyses and prognoses for the area 0-90N, 30W-60E

# GJ	: analyses and prognoses for the area 0-90N, 60E-150E

# GK	: analyses and prognoses for the area 0-90N, 150E-120W

# GL	: analyses and prognoses for the area 0-90N, 120W-30W

# GM	: analyses and prognoses for the area 90S-0, 30W-60E

# GN	: analyses and prognoses for the area 90S-0, 60E-150E

# GO	: analyses and prognoses for the area 90S-0, 150E-120W

# GP	: analyses and prognoses for the area 90S-0, 120W-30W

# For GSM products at 1.25-degree resolution for the Asian area (20S-60N, 60E-160W)

# g02	: analyses and prognoses up to 84 hours for levels below 100 hPa

# g12	: analyses and prognoses up to 84 hours for levels over 100 hPa

# g22	: prognoses beyond 84 hours for all levels

# For GSM products at 2.5-degree resolution for the global area

# g03	: analyses and prognoses up to 120 hours for Northern hemisphere

# g04	: analyses and prognoses up to 120 hours for Southern hemisphere

# g23	: prognoses beyond 120 hours for Northern hemisphere

# g24	: prognoses beyond 120 hours for Southern hemisphere

# For GSM products at 2.5-degree resolution for the Asian area (20S-60N, 80E-160W)

# ga01	: analyses

# gf01	: prognoses

# For GSM Weekly Ensemble Forecast products at 2.5-degree resolution for the global area

# wef	: ensemble mean and standard deviation

# For other types of products and observational data

# gms	: cloud amount, equivalent blackbody temperature

# obsr	: surface and upper-air observations

# typhoon : high density cloud motion vectors, tropical cyclone related information

# hwave : sea-wave prediction products from the Global Wave Model at 1.25 degree-

# resolution

# wave	: sea-wave prediction products from the Global Wave Model in 2.5 degree-

# resolution

# b) Filename

# (i) Filename of an individual file containing a GTS bulletin

ttaaii

ttaaii 	: T1T2A1A2ii of the WMO heading (lowercase letters)

# (ii) Filename of an archived file

For GSM products

aattth.tar

aa (or a)	: area or data type identifier (e.g.  as = Asia; gi = 0-90N, 30W-60E; we = Weekly Ensemble Forecast)

ttt (or tt)	: maximum forecast hour of prognoses included in the file

h	: fixed letter indicating that the file contains products for upper-air levels, attached as necessary

tar	: file descriptor indicating that the file is archived by the 'tar' command

For surface and upper-air observations

ttrnddhh.tar

tt	: identifier of the data contained in the file (lowercase letters)

(i.e. T1T2 of the WMO heading)

r	: fixed letter

n	: WMO Region (1 to 6 and 7 for Antarctica)

ddhh	: day and time of observation (i.e. YYGG of the WMO heading)

tar	: file descriptor indicating that the file is archived by the 'tar' command

For cloud amount and equivalent blackbody temperature data derived from satellite observations

ttaaii.tar

ttaaii	: T1T2A1A2ii of the WMO heading (lowercase letters)

tar	: file descriptor indicating that the file is archived by the 'tar' command

# (iii) Filename of a compressed file

ttrnddhh.tar.gz

ttmddhh.tar	: see (ii) above

gz	: file descriptor indicating that the file is compressed by the 'gzip' command

# (5) Storage time of numerical prediction products

The products (analyses and prognoses up to 72 (or 84) hours) are expected to be stored on the Server around the following placing times:

| Product | Placing time |
| --- | --- |
|  | 00 UTC initial | 12 UTC initial |
| GSM global area products ( 1.25 deg. resolution) | 0550 UTC | 1750 UTC |
| GSM global area products ( 2.5 deg. resolution) | 0450 UTC | 1650 UTC |
| GSM Asian area products ( 1.25 deg. resolution) | 0450 UTC | 1650 UTC |
| GSM Asian area products (2.5 deg. resolution) | 0450 UTC | 1650 UTC |
| GWM sea-wave products | 0500 UTC | 1700 UTC |

(6) Overview of data storage in the Server (an example for 12 UTC, April 15, 2003)

Year/month Day/hour	Type	File

jp034	200304	1512	GI	heia88

• • • • •	1.25° GSM products in thinned grid for the area

gi72.tar	0-90N, 30W-60E

gi192.tar

GJ	heja88

• • • • •	1.25° GSM products in thinned grid for the area

gj72.tar	0-90N, 60E-150E

gj192.tar

GK	heka88

• • • • •	1.25° GSM products in thinned grid for the area

gk72.tar	0-90N, 150E-120W

gk192.tar

(continued)

GL	hela88

• • • • •	1.25° GSM products in thinned grid for the area

gl72.tar	0-90N, 120W-30W

gl192.tar

GM	hema88

• • • • •	1.25° GSM products in thinned grid for the area

gm72.tar	90S-0, 30W-60E

gm192.tar

GN	hena88

• • • • •	1.25° GSM products in thinned grid for the area

gn72.tar	90S-0, 60E-150E

gn192.tar

GO	heoa88

• • • • •	1.25° GSM products in thinned grid for the area

go72.tar	90S-0, 150E-120W

go192.tar

GP	hepa88

• • • • •	1.25° GSM products in thinned grid for the area

gp72.tar	90S-0, 120W-30W

gp192.tar

g02	hhca89

• • • • •

as84.tar	1.25° GSM products for the Asian area

g12	as84h.tar

g22	as192.tar

as192h.tar

g03	hhxa70

• • • • •	2.5° GSM products for Northern hemisphere

gn120.tar

g23	gn192.tar

g04	hhya70

• • • • •	2.5° GSM products for Southern hemisphere

gs120.tar

g24	gs192.tar

ga01	hpda89

• • • • •	2.5° GSM products for the Asian area

gf01	hpdb89

• • • • •

wef	yexa89

• • • • • 	GSM Weekly Ensemble Forecast products

we192.tar

gms	hbxa40.tar	Cloud amount

htta40.tar	Equivalent blackbody temperature

• • • • •

typhoon	iutc41	High density cloud motion vectors

• • • • •

isxc41	Tropical cyclone related information

• • • • •

hwave	hjna88	1.25° wave height from GWM for Northern hemisphere

hmna88	1.25° wave period from GWM for Northern hemisphere

hzna88	1.25° prevailing wave direction from GWM for 						Northern hemisphere

• • • • •

hjsa88	1.25° wave height from GWM for Southern hemisphere

hmsa88	1.25° wave period from GWM for Southern hemisphere

hzsa88	1.25° prevailing wave direction from GWM for 						Southern hemisphere

• • • • •

(continued)

wave	hjxa88	2.5° wave height from GWM

hmxa88	2.5° wave period from GWM

hzxa88	2.5° prevailing wave direction from GWM

• • • • •

obsr	smr21512.tar

usr21512.tar	Surface and upper-air observations

• • • • •

smr21512.tar.gz

usr21512.tar.gz	Surface and upper-air observations (compressed files)

• • • • •

1513

APPENDIX 1

PASSWORDS MANAGEMENT

The procedures for assigning and changing the User Password indispensable for each Client to accesses to the Server are described below.

1. Introduction

In order to maintain security of the Server at a proper level, the User Passwords should be changed periodically (usually at 00 UTC on the first day of each month).  The Password should be changed both the User side and the Administrator side synchronously.  The old Password should expire at the time when the Administrator updates its Password File.  Then, User will be rejected to access to the Server until they renew the Password.  Therefore each User is requested to keep close contact with the Administrator for smooth change of Passwords and continuous accessibility to the Server.

2. Assignment of password

The attached table contains 99 different Passwords.  Once a month, the Administrator selects a Password for each User randomly from the list and notifies the relevant User of the reference number for the selected Password by e-mail.  Since the Password itself will not be informed by e-mail from the viewpoint of security, each User will identify the new Password by only the reference number in the attached table.

Planned date/time for the Password change is also notified by the e-mail.  After that date/time, the selected Password will become effective and the old one will expire.  This notification will be made about a week before the change.

In order to keep close and secure contact with the Administrator, User may wish to register two different e-mail addresses for the Administrator’s notification.

3. Change of password

The Administrator will update the Password File on the Server according to the schedule notified by the e-mail as in item 2 above.  User will also change the Password at the scheduled date/time.

ATTACHMENT to the APPENDIX 1

Password Table for                (ver. 1)

(Electric version of the Guidance does not contain the Password Table.)

APPENDIX 2

Usage of the ftp commands

|  | get remote-file [local-file] |  |
| --- | --- | --- |

Retrieve the remote-file and store it on the local machine.  If the local file name is not specified, it is given the same name it has on the remote machine.

|  | mget remote-files |  |
| --- | --- | --- |

Expand the remote-files on the remote machine and do a get for each file name thus produced.

|  | prompt |  |
| --- | --- | --- |

Toggle interactive prompting.  Interactive prompting occurs during multiple file transfers to allow the user to selectively retrieve or store files.  If prompting is turned off (default is on), any mget or mput will transfer all files, and any mdelete will delete all files.

|  | ascii |  |
| --- | --- | --- |

Set the file transfer type to network ASCII.

|  | binary |  |
| --- | --- | --- |

Set the file transfer type to support binary image transfer.

|  | dir [remote-directory] [local-file] |  |
| --- | --- | --- |

Print a listing of the directory contents in the directory, remote-directory, and, optionally, placing the output in local-file. If interactive prompting is on, ftp will prompt the user to verify that the last argument is indeed the target local file for receiving dir output.  If no directory is specified, the current working directory on the remote machine is used.  If no local file is specified, or localfile is -, output comes to the terminal.

|  | ls [remote-directory] [local-file] |  |
| --- | --- | --- |

Print a listing of the contents of a directory on the remote machine.  The listing includes any system-dependent information that the server chooses to include; for example, most UNIX systems will produce output from the command 'ls -l'.

If remote-directory is left unspecified, the current working directory is used.  If interactive prompting is on, ftp will prompt the user to verify that the last argument is indeed the target local file for receiving ls output.  If no local file is specified, or if local-file is '-', the output is sent to the terminal.

|  | pwd |  |
| --- | --- | --- |

Print the name of the current working directory on the remote machine.

|  | bye |  |
| --- | --- | --- |

Terminate the FTP session with the remote server and exit ftp. An end of file will also terminate the session and exit.

# Text boxes

8Mbps

10Mbps

Load Balancer

JMA

Secure Zone

Packet Shapers

FireWalls

Router Controllers

ISP #2 (C&W)

ISP #1 (IIJ)

Internet

Other servers

RSMC

Data Serving System

DMZ

Figure 1   RSMC Data Serving System in JMA Internet environment

1624

1633

2657

1400

[kbps]

0

1200

1000

800

600

400

200

JAN      FEB        MAR        APR        MAY        JUN         JUL       AUG        SEP         OCT      NOV

Australia

China

Macau

Malaysia

Brunei

Hong Kong

Vietnam

Philippines

Singapore

Hong Kong

Vietnam

Philippines

Singapore

[kbps]

0

600

500

400

300

200

100

1996            1997           1998           1999           2000           2001           2002          2003

Monthly average

Maximum daily average

Minimum daily average

Notes)   Hong Kong had accessed to the RSMC DSS through ISDN till November 2001.

The upper graph shows monthly averages of continuous ftp access over 10 seconds

2003

Figure 2  transition of ftp throughput  from the RSMC DSS to each access user