| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on WIS-GTS Communication Techniques and Structure Tokyo, Japan, 25-28 April 2006 |  | ISS/ET-CTS 2006/Doc. 2(3) (18.Ⅳ.2006) Agenda item 2 ENGLISH only |
| --- | --- | --- |

STATUS OF IMPLEMENTATION of TCP/IP PROCEDURES AT NMC ANKARA

(Submitted by OKTAR Cemal (Turkey))

Summary and purpose of document This document includes the report on the status of implementation of TCP/IP procedures and applications at NMC Ankara.

1. GTS facilities

TSMS have been using MESSIR MSS system since 2000. It consists of 2 Compaq Proliant 1850 Servers with PII 400 MHz processor. It has TCP/IP capabilities, in addition to PSTN connections, asynchronous lines, telex interfaces, SADIS connections, and ACOWEX connection. It does not support TDCF. TSMS will replace MSS system this year. A contract has been signed by IBL Company. New system will consist of 2 Fujitsu-Siemens RX600S2 servers. Each one will have 2 Intel Xeon 3.2 GHz processors with 64 bits support, 1MB cache, 667 MHz bus speed, and 4 GB RAM. Operating System will be LINUX. MSS software will be based on TCP/IP procedure. In addition, there will be a limited number of asynchronous lines for dial-up connections. It will have TDCF capabilities. SADIS2G will be also integrated to the system.

2.   Current Status of the International circuits connected with NMC Ankara

| Circuits (between Ankara and …) | Connection Type | Speed | Procedures Applications | Exchange data type |
| --- | --- | --- | --- | --- |
| Reading-UK ECWMF | RMDCN TCP/IP | F/R Equant Network CIR: 128K/256K | FTP, SSH, TCP 9000-9005 TCP 6001 | File (Model data) |
| Offenbach-Germany (RTH) | RMDCN TCP/IP | F/R Equant Network CIR: 32K/32K | FTP socket | File (OPMET, GRIB-Forecast, BUFR-Uemetsat) |
| Rome-Italy (RTH) | RMDCN TCP/IP | F/R Equant Network CIR: 32K/32K | FTP | File (OPMET, GRIB-Forecast) |
| UK | SADIS-Satellite Asynchronous | 9.6K |  | Asynchronous OPMET, GRIB, BUFR |
| Germany | Acowex-Satellite Asynchronous | 9.6K |  | Asynchronous OPMET, GRIB-FORECAST, BINARY-RADAR |
| Baku-Azerbaijan | VSAT TCP/IP | 64K | FTP, HTTP | File |
| Lefkoşa Northern Cyprus | VSAT TCP/IP | 64K | FTP, HTTP | File |
| Ercan-Northern Cyprus | VSAT TCP/IP | 64K | FTP, HTTP | File |
| Sarejova-Bosnia | Internet TCP/IP |  | FTP | File |
| Domestic Lines | TCP/IP | 9.6-64K | FTP | File |

3. Current Status of Domestic circuits connected with NMC Ankara

| Circuits | Communi-cation Type | Procedures Applications | Exchange data type | Explanations |
| --- | --- | --- | --- | --- |
| Airports (50) | VSAT TCP/IP (64K) | FTP, HTTP | File OPMET, GRIB | * Backup: ADSL-Internet, Dial-up *OPMET and GRIB data are sent via FTP. All have HTTP access to Intranet. *CLIMATOLOGICAL, SYNOP, METAR, SPECI, AND TAF Bulletins are received |
| Leased Lines(2) | Asynchronous | Asynchronous | OPMET, GRIB |  |
| Leased Lines(2) | Leased Line | FTP | File OPMET, GRIB |  |
| Dial-in Lines (10) | PSTN Asynchronous | Asynchronous | SYNOP, CLIMATOLOGICAL | SYNOP, CLIMATOGICAL Bulletins are received |
| MeteoSQL-1 | LAN, TCP/IP | FTP | File OPMET | Bulletins are decoded to put WEB |
| MeteoSQL-2 | LAN, TCP/IP | FTP | File OPMET | Bulletins are decoded to put WEB |
| GTSWEB(260) | LAN, TCP/IP | FTP | File SYNOP, CLIMATOLOGICAL | 260 stations can access web interface to send observations |
| GTSFTP(260) | LAN, TCP/IP | FTP | File SYNOP, CLIMATOLOGICAL | 260 stations can access web interface to send observations |
| Military | F/R TCP/IP | FTP | File OPMET, GRIB |  |
| Aviation Division(3) | LAN, TCP/IP | FTP | File OPMET | Especially to check aviation bulletins. |
| Agriculture Division | LAN, TCP/IP | FTP | File CLIMATOLOGICAL | For Agricultural purpose |
| Radar Div.-1 | LAN, TCP/IP | FTP | File RADAR Images | To put Radar images |
| Radar Div.-2 | LAN, TCP/IP | FTP | File Precipitation data | To get precipitation data for calibration of radars |
| METCAP Server-WAN | LAN, TCP/IP | FTP | File OPMET, GRIB | Used to send bulletins via Internet |
| METCAP Server-LAN | LAN, TCP/IP | FTP | File OPMET, GRIB | Used to map disk for LAN (MetCAP)Users |
| AWOS-Collection(2) | LAN, TCP/IP | FTP | File SYNOP | Used to put bulletins of 206 AWOS stations |

| Circuits | Communi-cation Type | Procedures Applications | Exchange data type | Explanations |
| --- | --- | --- | --- | --- |
| NWP | LAN, TCP/IP | FTP | File Model Products | Used to put Model Products |
| Forecasters(7) | LAN, TCP/IP | FTP | File OPMET, GRIB | Used for forecaster’s applications |
| MediaServer | LAN, TCP/IP | FTP | File OPMET, GRIB | Used to send decoded bulletins and images to media and other customers using e-mail or FTP |
| SYNOP (2) | LAN, TCP/IP | FTP | File OPMET | Especially to check SYNOP and RADIOSONDE bulletins. |
| RADIOSONDE | LAN, TCP/IP | FTP | File TEMP Data | Used to put TEMP data |
| DSİ | LAN, TCP/IP | FTP | File SYNOP | Used to send SYNOP data to NHS |
| Storage (2) | LAN, TCP/IP | FTP | File National bulletins | Used to store national bulletins in file structure |
| Archive | LAN, TCP/IP | FTP | File National Bulletins | Used to send National Bulletins. Bulletins are decoded and imported into DataBase. |

4. VSAT System of NMC Ankara

5. TURKSAT 1C Coverage Area