| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on WIS-GTS Communication Techniques and Structure Tokyo,Japan, 25-28 April 2006 |  | ISS/ET-CTS 2006/Doc. 2(1) (14.Ⅳ.2006) Agenda item 2 ENGLISH only |
| --- | --- | --- |

STATUS OF IMPLEMENTATION AT RTH TOKYO

(Submitted by NAKANO Hisashi (Japan) )

Summary and purpose of document This document includes the report on the status of implementation of TCP/IP procedures and applications at RTH Tokyo.

1.  GTS facilities

JMA central telecommunication system was replaced by new one in October 2005.  The new system is fully adopted GTS TCP/IP strategy.  All GTS circuits connect to the system by TCP/IP procedure. The new system is also capable of the data exchange through the Internet  using gateway system at headquarters.

2.  Current status of implementation of the GTS circuits

Table 1   Status of the GTS circuits connected with RTH Tokyo (as of April 2006)

| Circuit | Speed | Procedures Applications | Routing protocol | Exchange data type |
| --- | --- | --- | --- | --- |
| Washington Tokyo | MTN | FR (IMTN cloud I) CIR: WT ( 32/768kbps ( TK Port: WT=1.5Mbps,TK=1.5Mbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary, fax), File (Satellite data) |
| Melbourne Tokyo | MTN | FR (IMTN cloud I) CIR: MB ( 16/32kbps ( TK Port: MB=256kbps,TK=1.5Mbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary, fax), File (Satellite data) |
| Beijing Tokyo | MTN | FR (IMTN cloud II) CIR: BJ (48(*1)/48kbps( TK Port: BJ=256kbps,TK=128kbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary, fax), File (Satellite data) |
| New Delhi Tokyo | MTN | FR (IMTN cloud II) CIR: ND (16/16kbps( TK Port: ND=64kbps,TK=128kbps | TCP Socket | BGP-4 | Message (A/N, binary) |
| Khabarovsk Tokyo | RMTN | 14.4kbps (auto fall back V.34 modem ) | TCP Socket | Static | Message (A/N, binary, fax) |
| Bangkok Tokyo | RMTN | FR (NNI basis) CIR: BK (16/16kbps( TK Port: BK=128kbps,TK=192kbps | TCP Socket | BGP-4 | Message (A/N, binary) |
| Hong Kong Tokyo | RMTN | FR (NNI basis) CIR: HK (16/16kbps( TK Port: HK=64kbps,TK=192kbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary), File (Satellite data,GPV) |
| Seoul Tokyo | RMTN | FR (NNI basis) CIR: SL (16/16kbps( TK Port: SL=64kbps,TK=192kbps | TCP Socket | BGP-4 | Message (A/N, binary, fax) |
| Manila Tokyo | Inter-regional | FR (NNI basis) CIR: MN (16/16kbps( TK Port: MN=64kbps,TK=192kbps | TCP Socket | Static | Message (A/N, binary) |

FR: Frame Relay;     CIR: Committed Information Rate;     NNI: Network-to-Network Interconnection

Note (*1) : upgrade to 96kbps being under process

3.   Implementation status of TCP/IP protocols and applications

3.1  TCP/IP

TCP/IP protocols are used on all of GTS circuits connected with RTH Tokyo.  Meteorological messages including T4 charts are currently exchanged through the standard WMO sockets. They would be migrated to FTP of accumulated messages upon necessary arrangements with adjacent centers. The new Message Switching System of RTH Tokyo is applied to batched FTP procedure, which is already used for internal massage switching between servers.

Simple FTP is also used to receive satellite data from Washington ,Melbourne and Beijing and to relay some part of them to Beijing and Hong Kong.  GPVs of JMA one week ensemble forecast model are also transmitted to Hong Kong by simple FTP. The following manners are currently applied.

Data from Washington:	GET by Tokyo

Data from Melbourne:	PUT by Melbourne with renaming

Data from Beijing:	PUT by Beijing  with renaming

Data to Beijing:	GET by Beijing

Data to Hong Kong:	PUT by Tokyo with renaming

Satellite data exchange using  simple FTP is to expand to other GTS circuits such as Seoul-Tokyo near future. GTS file naming convention is used in these file exchange.

The new MSS is also able to receive meteorological messages via E-mail, which is under testing.

3.2  Routing protocols

BGP-4 is applied over almost all the TCP/IP circuits connected with Tokyo except Khabarovsk-Tokyo and Manila-Tokyo where static routing is applied.  In principal Tokyo advertises all available routing information to BGP neighbours without filtering, while exchange of BGP routes with the Equant router, which interconnects both Tokyo - Beijing and Tokyo – New Delhi as well as RA VI－RMDCN, is limited to a minimum that is necessary for establishing IP connectivity among these two centres and Seoul where re-routing operation is applied.

With growing IP connectivity among GTS centres, there would be a bypass route(s) through a third centre in addition to the direct one.  For making practical use of this feature, Tokyo, Washington and Melbourne started re-routing via the bypass route in case of a failure of the direct link on a triangle of circuits interconnecting these three centers established within IMTN could I in February 2003. On September 2003 Brisbane joined to the triangle as a Disaster Recovery Site for Melbourne. Besides, Tokyo, Beijing and Seoul also have re-routing connection among them.

4.  Traffic status of IP links

(a) Wahington-Tokyo

(b) Melbourne-Tokyo

(c)  Beijing-Tokyo

(d) New Delhi-Tokyo

(e) Khabarovsk-Tokyo

(f)  Bangkok-Tokyo

(g)  Hong Kong-Tokyo

(h)  Seoul-Tokyo

- Manila-Tokyo

# Text boxes

INTERNET

ISP

Domestic network

24 Mbytes/day

Private

network in headquarters

RSMC

Data

Serving

System

Servers for

Domestic data exchange

Servers for

International data exchange

Router for GTS connections

NAT (Network Address Translation) Router

Other

Data

Distribution

Serveres

DMZ

Servers for

Application

0.04 Mbytes/day

Figure 1   GTS facilities and Internet accessing system

1134 Mbytes/day

PLDT

Frame Relay

Network

64kbps

64kbps

128kbps

Equant Frame Relay Network

IMTN cloud II

New Delhi

Beijing

1.5Mbps

256kbps

Internet accessing system at JMA headquarters

t

Main components of Operational Telecommunication System

at Kiyose operation Office

AS 64520

Pure IP circuits

circuits

Manila

Private IP address

Frame Relay Networks

s

202.245.39.0/24

1.5Mbps

BT Frame Relay

Network

IMTN cloud I

Dedicated line connection

(analogue)

26 Mbytes/day

Figure 2   Configuration of the GTS circuits connected with RTH Tokyo

Valiable (normally 14.4kbps)

Khabarovsk

32 Mbytes/day

3.8 Mbytes/day

60 Mbytes/day

CAT

Frame Relay

Network

HKT

Frame Relay

Network

DACOM

Frame Relay

Network

103 Mbytes/day

1.3 Mbytes/day

Seoul

256kbps

128 Mbytes/day

KDDI

Frame Relay Network

128kbps

NNI basis Frame Relay connections

0.5 Mbytes/day

64kbps

64kbps

192kbps

Hong Kong

Bangkok

Melbourne

### Tokyo

197 Mbytes/day

0.4 Mbytes/day

32 Mbytes/day

2.3 Mbytes/day

18 Mbytes/day

1.0 Mbytes/day

39 Mbytes/day

Washington