| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on Enhanced Use of Data Communication Systems EXPERT TEAM ON THE IMPROVED MAIN TELECOMMUNICATIONS NETWORK AND GTS Montreal, Canada, 27-31 May 2002 |  | ISS/ET-EUDCS 2002/Doc. 3.2(1) (24.V.2002) ____________ ITEM 3.2 ENGLISH only |
| --- | --- | --- |

### The use of FTP procedures on the GTS

(Submitted by Hiroyuki Ichijo (Japan) )

Summary and purpose of document This document includes the outcome of a survey on the use of ftp procedures on the GTS, and provides some discussion points to promote the ftp use and its standardisation.

# ACTION PROPOSED

The session is invited to review the discussion points from the outcome of the survey and to clarify things to recommend as a guideline.

1.  An outline of the survey

The TCP/IP migration is progressing in the GTS community.   There are many Centres to have introduced TCP socket links as the initial step and then to study the possibility of migration to ftp based links as a goal.  However most of NMCs, especially in RA II, hesitate to move forward because of lack of actual information about ftp procedures on the GTS.

To promote the use of ftp procedures on the GTS, a questionnaire was distributed to 22 Centres, which had already implemented ftp and were interested in ftp implementation, in 2001 and 2002.   The 15 replies are summarised in Attachment of this document.

2.  Outcome of the survey and discussion points

2.1  For existing message types with AHL (batched ftp)

- File naming convention (CCCCNNNNNNNN.ext)

- About half of the Centres use the convention in the Attachment II-15 of the Manual on the GTS.  The others use their own conventions,   Most of the latter half include a time group in their file names.  There are specific cases without any cyclic number to indicate continuity of transferring files.

- The ext for urgent messages (i.e. “ua” or “ub”) is not used so far.

- In most cases, the file sequence number (NNNNNNNN) of zero is not dealt with system initialisation.

Discussion points Can the file naming convention in the Attachment II-15 be a true standard on the GTS? If Yes, we should encourage that Centres would introduce the convention in the Attachment II-15 at their appropriate timing/opportunity such as system replacement. If No, we should reconsider to revise the convention. A Centre having links with different file naming conventions could desire a true standard . Isn’t it problem to use a specific convention without any cyclic number in the view of request for retransmission? To clarify interpretation of “a sequential number from 0 to 99999999” Interpretation 1: regular cyclic from 1 to 99999999 with 0 for initialisation Interpretation 2: regular cyclic from 0 to 99999999 Even interpretation 2, the system would set 0 inevitably at its initialisation. Thus a receiver should regard a skip to 0 as the sender’s initialisation and not request for repetition.

- Message accumulation and retransmission rules

- The option 1 (format identifier=00, SOH to ETX) for the message structure in a file is used predominantly. The option 2 (format identifier=01, bulletin without starting and end lines) is rarely used.

- There are not many Centres having a rule and/or functions for retransmission by request in the message sequence number.

- There are a few Centres having a rule and/or functions for retransmission by request in the file.

- There are a few Centres to insert a dummy message of zero length after the last real message in a file.

- According to the Attachment II-15, cutoff time and maximum number of messages should be 60 seconds and 100, respectively.   In most cases, the limits are kept operationally except for a specific condition.  Furthermore these parameters are easily changeable in several systems.

Discussion points In the option 2, it is impossible to request a message by the message sequence number. Is the option 2 appropriate for message switching on the GTS in the practical view? Retransmission rules are required on either message or file basis. Because a receiver possibly loses some data already received internally. Should we head for a file based retransmission manner? The Attachment II-15 says “a 'dummy' message of zero length shall be inserted after the last real message, to assist with end of file detection in certain MSS systems;”. Isn’t it an option? Are the current limits allowable in transmission delays in the global-wide WWW operation?

- Ftp session procedures

- There are Centres not using any renaming method.

- To enable renaming and recovery, the “delete/overwrite/rename”  are normally permitted for a remote sender.

- Implementation details of ftp session handling are quite different among systems.  Especially a range of idle timer is 10 seconds to 10 minutes!

- Both of anonymous and real account are used.

- It seems that most systems implement a function of automatic recovery on ftp daemon level when an ftp transfer  is interrupted or aborted.  Sophisticated append command is used for effective recovery at RTH Offenbach.

- File compression is optionally used.

Discussion points The Attachment II-15 says “To avoid problems with the receiving centre processing a file before it has completely arrived, all sending centres must be able to remotely rename the files they send.” We should encourage that every Centre would introduce the renaming method. In a sense, the idle timer should be settled carefully considering statistics on data exchange, link capacity and the relation between system resources and session overhead. Any guidelines are desirable for NMCs studying ftp implementation. To specify comparison in the view of merit/demerit between anonymous and real account.

- Miscellaneous

  - Some types of ftp products are used in compliance with each platform.

  - Operator-interfaces to see the ftp status and logging are generally simple.

  - Tips based on actual operations are useful.

Discussion point To review the issues pointed out as tips, e.g. security risk, performance in multi-sessions, necessity of making an error report visible, and effective solution on low speed circuits

2.2  For new message type without AHL

- Ftp of a pair of information and metadata files

  - Only Toulouse has implemented the paired file method.  However Toulouse and Melbourne pointed out incompletion of the WMO specification.

  - Implementation plans might arise as long as the specification would be complete.

Discussion point Everybody knows the incompletion of the specification for the paired file method. For example, there seems be no switching keyword in contents and file name of information and metadata files.

- Simple ftp

  - Many Centres are already exchanging and switching large files such as satellite data by simple ftp.

(Attachment)

1.  For existing message types with AHL (batched ftp)

|  | 1. File naming conventions (CCCCNNNNNNNN.ext) |
| --- | --- |
|  | (1a) Do you use the file naming conventions in Attachment II-15 of the Manual on the GTS? If NO, please specify yours. | (1b) Is the file sequence number (NNNNNNNN) of zero used for the special meaning such as system initialization? |
| Bangkok | Yes CCCCNNNNNNNN.a for alphanumeric CCCCNNNNNNNN.b for binary | On receive, sequence of 0 will not cause report of missing sequence numbers. On transmit, sequence number is set to 0 at midnight (considered to be system initialization). |
| Beijing | Yes (Beijing-Moscow bilateral rule) CCCCNNNNNNNN.b for alpha numeric and binary data CCCCNNNNNNNN.f for facsimile information | No |
| Bracknell | Our Output files for GTS are named EGRRnnnnnnnn.ext. We use a, b and f only for the ext, chosen after bilateral agreement. The input files have to comply with the Tandem requirement of file names being no more than 8 characters long. | No |
| Brasilia | I´m not using it, but I have. I use another one where I have the channel number and the date/time | No |
| Hong Kong | No TTddhhmm.CFF where TT=Identifier of centre for messages switching to ddhhmm=day/hour/minute in 2 digits FF=Identifier of centre for messages switching from | No |
| Melbourne | Yes | No |
| Montreal | No batched FTP with AHL messages at this time. Requirement has been identified for alphanumeric messages for future development. |  |
| Nairobi | No Our MSS produces files with names "%u%H%M%S.%C". where: %u is a one letter machine indicator (e.g T is host TMSS and U is host UMSS) %H hour in two digits %M minutes in two digits %S is seconds in two digits %C is a two digit cyclic number (00 to 99) Thus a typical files might have the names T235826.63 or U111559.51 |  |
| Offenbach | Yes we do, but bilateral we often arrange another convention, we have developed ourselves. The DWD presented it to WMO five years ago (Dr. Dunke CBS-Meeting). | No, it is not. |
| Seoul | Yes | Yes |
| Sofia | Yes. RTH Sofia use CCCCNNNNNNNN.ext | RTH Sofia use (NNNNNNNN) for system initialization. |
| Tehran | No, Alpbhabet No.2 | No |
| Tokyo | We plan to use the conventions in our new MSS. Necessity of urgent connections (ext is "ua" or "ub") is under consideration. | We plan and hope so but we would like to make a decision through the discussion with other centers. |
| Toulouse | Yes | No |
| Washington | The format of the file name is a combination of WMO Recommendation 2, FTP procedures (described in CBS-ext.98; WMO-No. 893; page 64) and the U.S. Telecommunication Gateway TOC Directory and File Name Standard. cccc[_si.aaaa(aaaaaa)]_dt.hhnnss where: cccc = four letter ID of transmitting NMC or center "_si." = constant to indicate "data supplier" [_si.aaaa(aaaaaa)] = an optional group to allow additional file name definition for multiple data processes within a providing data supplier ( Length of definition aaaaaaaaaa is a variable field up to 10 characters as needed. ) "_dt." = constant to indicate "data time" hhnnss = hour-minute-second the file was generated for transfer Example) "ammc_dt.211515" | The file sequence number is not used. |

|  | 2. Message accumulation and retransmission rules |
| --- | --- |
|  | (2a) Please indicate names of the option1 (format identifier=00) and the option2 (format identifier=01) circuits, respectively. | (2b) In case of the option1, do you have any rules on retransmission by request in the message sequence number (nnn or nnnnn)? | (2c) Do you have any rules on retransmission in file, or get based recovery from receiver? |
| Bangkok | The system uses the option1 Circuit names : Bangkok-Vientiane (FTPA_VNO : alphanumeric outgoing FTPB_VNO : alphanumeric incoming FTPA_VNI : binary outgoing) | No | No |
| Bracknell | EDZW, LIIB, EBBR and LFPW receive option 1 format files. EIDB receives option 2 format files. Other GTS links are by sockets or X25. | We can retransmit by AHL, time or message sequence number but retransmits use a new message sequence number. We only use three figure message sequence numbers. | If a batched file is interrupted during an FTP transfer the whole file is FTPd again. |
| Hong Kong | Hong Kong – Beijing circuit (Only for the portion between Hong Kong and Guangzhou, see Notes) | Manual Intervention | Manual Intervention |
| Melbourne |  | No. There are no WMO rules. |  |
| Nairobi | Nairobi - Toulouse Nairobi - Dar-es-Salaam Nairobi- Entebbe |  |  |
| Offenbach | Option 1 is most used between EDZW and its international partners: EDZWnnnnnnnn.a or .b or .f edzwnnnnnnnn.a or .b with ECMWF, EUMETSAT, BABJ, LFPW, OMAE, EHDB Dnnnnnnn.a with EGRR Option 2 is not used at all Nationallly and Local we are using a lot of other filestructures (about eight) with special syntax and special namings, for example "one file with one mesage" where the name is equal to the bulletin header. Likewise we use the WMO-Format (option1) but another naming because of the better assigning (name/content). | No, we do request on bulletin base only; that is done on lines we use the x.25- or TCP-Socket-procedure | No automatic recovery but manual recovery is possible. |
| Seoul | Option1 | nnnnn | keeping the files during determined period from the sender side, and get based recovery from receiver. |
| Sofia | Option1 (SOH – ETX) Sofia - Toulouse (RMDCN) Sofia - Prague (RMDCN) Sofia - Bucharest (RMDCN) Sofia - Skopje (RMDCN) Sofia - Belgrade (direct telephone line) | RTH Sofia checks for errors and retransmit. | RTH Sofia has some rules of retransmission. |
| Tehran | Neither option1 nor option2 is used |  |  |
| Tokyo | Currently we have not batched ftp but TCP socket links. We plan to support the option1 only similar to the current socket streaming. | Under consideration | Under consideration |
| Toulouse | We can do the twice | Case1) NNN from 000 (or 001) to 999 Case2) NNNNN from 00000 (or 00001) to 09999 |  |

|  | 2. Message accumulation and retransmission rules |
| --- | --- |
|  | (2d) Do you insert a dummy message of zero length after the last real message, to assist with end of file detection? | (2e) Please show your parameters to combine messages into a file: |
| Bangkok | No | Cutoff time 30 seconds, max-number-of-message is 10, max file size is not configured (limited only by disk space available). |
| Beijing |  | (Beijing-Moscow bilateral rule) 10 messages in a file for alpha numeric and binary data 1 chart T4 in a file for facsimile information |
| Bracknell | On output we add a dummy message of zero length. On input we can handle a file with or without a dummy message. | All parameters negotiable. The standard parameters are cutoff time of 60 seconds, a max of 100 messages with a max file size of 2,000000. |
| Brasilia |  | Yes. We have 3 triggers that are basically negotiable. Time: specify how many seconds a file must be open to collect bulletins Size: e.g. 50,000bytes Number: e.g. 20 bulletin |
| Hong Kong | No | Cutoff time = 10 minutes Maximum number of messages = no limit Maximum file size = no limit |
| Melbourne | Optional – default is no. | Configurable on a per circuit basis |
| Nairobi |  | For alphanumeric and binary messages we we put up to 30 messages in a file but we have a timeout (30 seconds). For T4 charts we put 1 chart per file |
| Offenbach | Yes, we do terminate the files by help of a "NULL-header" 0000000000. | 20 .... 600 s 1 .... 500 messages 200 ..... 2500 kbytes |
| Seoul | Yes | Cutoff time-60sec, Maximum number of messages-100, Maximum file size-1500octets x 100 = 150KB |
| Sofia | No | 20 – 300 s 20 messages no max size |
| Tokyo | We plan not to use a dummy message. | Under consideration |
| Toulouse | Yes | Timeout send file: 10s Max number of messages: 100 Max file size: 150 Kbytes |
| Washington |  | Within a total length of 999999 octets |

|  | 3. Ftp session procedures |
| --- | --- |
|  | (3a) Do you use the file renaming method in Attachment II-15 of the Manual on the GTS? (.tmp) | (3b) Which do you use, anonymous ftp or real account ftp? | (3c) Is changing password from sender allowable? |
| Bangkok | Yes | Real account ftp. | Yes |
| Beijing |  | Anonymous ftp (Beijing-Offenbach) Real account ftp (Beijing-Moscow) | No |
| Bracknell | Adapted to be .TMPnn where nn=01 for first PUT but is incremented for repeated PUTs after a failure in the FTP. For example .TMP01 then .TMP02. We found there could be difficulties if an acknowledgement had not been received, due to an FTP failure, by the local host for a file successfully received on the remote host and then the same file name was used again. | Both on Output, chosen by bilateral agreement. On Input all FTPs set up as real accounts. | Only if co-ordinated with a change here. |
| Brasilia | No | Real account | No |
| Hong Kong | No | Normally anonymous FTP | No |
| Melbourne | Yes |  | No |
| Nairobi | After the transfer we might do some renaming depending on what is needed at the remote end. |  |  |
| Offenbach | Yes, but we prefer to do it by sending the filename with a leading dot first and then rename it. | Real. | No. |
| Seoul | Yes | anonymous ftp | Yes |
| Sofia | Yes .We rename then send and return. | Receive - from anonymous. Send - with user and pass. |  |
| Tehran | No | None |  |
| Tokyo | We plan and hope so. Currently the renaming method is introduced in a single ftp links with Melbourne, Hong Kong and so on. | We hope normally anonymous FTP | No |
| Toulouse | Yes | Anonymous in reception, real or anonymous when sending | No |

|  | 3. Ftp session procedures |
| --- | --- |
|  | (3d) Please show the mode (sticky bit, access permission) of specific sub-directory for placing files. | (3e) Please show details of ftp session handling, e.g. maximum number, idle timer, prioritizing and so on. | (3f) Please indicate delete/overwrite/rename/chmod/umask permissions in ftpaccess level (wu-ftp example) of receiver. |
| Bangkok | Ls –l /usr/users/FTPA_VNO Drwxrwxrwx 3 FTPA_VNO users 512 Jul 8 2001 FTPA_VNO | Maximum number=99999999 (number is assigned to ftp file on transmission) idle timer=10 (program polls each 10 seconds for more messages to transmit). Prioritizing, each message routed by the system is given a priority based on its header and the routing table entry used to router. If a message has a higher priority, it will be sent before one of lower priority if both messages are queued to the same circuit simultaneously. | All are allowed. |
| Beijing | rwxr-xr-x |  |  |
| Bracknell | Not applicable on our Tandems (Compaq). A sub-directory for each user is set up by us with Read, Write and Purge permissions and accessed using the correct username and password. | One session per route. The idle timer is configurable with the standard being 240 seconds. We prioritize within our message switch by AHL not route. | We can set all permissions quoted on output by bilateral agreement. |
| Hong Kong | Unix platform: rwxr-sr-x Umask: 01755 | Maximum number = 40 Idle timer = 5 minutes Priority: Controlled by operating system | Delete = yes Overwrite = yes Rename = yes Chmod = no Umask = no |
| Offenbach | rwxrwxr-x | We use our own FTP client that handles a session as follows: - Connect to remote partner - Login - Send password - Set remote idle time - Set type ascii or binary - Change directory - For each file open data port, transmitt file, rename and close data port. - Logout We allow up to five parrallel transfers with priorities ranging from 0 to 9. | Our FTP-server does not support this. |
| Seoul | sticky bit-1777, Access permission-777 | Maximum number-5, idle time-600sec, Give higher priority to principal ID when simultaneously session. | Not permit on anonymous ftp limit permit on wu-ftp |
| Sofia | The mod is 755 on subdirectory. | The session tries 5 times to send, no priority, time to send 20 – 300s and can retransmit again. | 755 delete , overwrite and rename |
| Tokyo |  | In our estimation, the maximum number of sessions is about 50 in total for both ways of the nine GTS links, We are considering that an idle timer would be long for mostly permanent connections. If necessary, we will prioritize batched ftp sessions over other single ftp sessions (e.g. satellite data). | Normally "delete/overwrite/rename" would be allowed for put-based partners. |
| Toulouse | 666 |  | Delete / overwrite / rename |

|  | 3. Ftp session procedures | 4. Miscellaneous |
| --- | --- | --- |
|  | (3g) Do you have any recovery mechanisms in session abort, e.g. resuming transfer function? | (3h) Do you use file compression? If YES, please show your compression method. | (4a) What type do you implement, wu-ftp, pro-ftp or others? |
| Bangkok | If the ftp transfer fails (transmit) then it will be retried forever. | No compression is used. | The ftpd command is the DARPA (Defense Advanced Research Projects Agency) Internet File Transfer Protocol server process. The server uses the TCP protocol and listens at the port specified in the FTP service specification. |
| Beijing |  | No (Beijing-Moscow bilateral rule) File compression (UNIX "compress") for alpha numeric and binary data: both modes are supported and will be tested. for facsimile information: mode without compression |  |
| Bracknell | There is an automatic resend within our FTP process. |  | Tandem (now Compaq) Specific |
| Brasilia | No | No | Internal |
| Hong Kong | No | No | wu-ftp |
| Melbourne |  | Optional |  |
| Offenbach | Yes, partly transmitted files are being appended via the FTP APPE command. | Yes, we use gzip. | We use the default FTP-server from FTX. |
| Seoul | Recognize session break by figure response using the verbose mode, and retranmission by sequence number. | Yes, gzip | wu-ftp |
| Sofia | Yes, if no ACK the sender try again . | No, RTH-Sofia doesn’t use compression. | RTH-Sofia works with standard ftp with some new feathers implement in. |
| Tehran | No | No |  |
| Tokyo | Under study, especially in the use of sophisticated append command for effective recovery | We will support both of "Gzip" and "Unix based Compress", but whether file compression would be used is depend on the link characteristics. | Lately we are very interested in pro-ftp from the views of security and programmable functionality. |
| Toulouse | No | Gzip (.gz) or compress | Wu-ftpd2.6.1 |

|  | 4. Miscellaneous |
| --- | --- |
|  | (4b) Have you developed any operator-friendly logging applications? If YES, please show your logging example. | (4c) Please show actual daily traffic on each circuit, e.g. Mbytes and the number of files. |
| Bangkok | No | No statistics of number of files but can viewing by the channel statistics. |
| Bracknell | Client automatic log file and our development of logging files are all readable text files. Example Client Log file. (GTS customer) 230 Guest login ok, access restrictions apply. ---> CWD /entree.alpha/UKMO9RgT678Ert/BRK.FA 250 CWD command successful. ---> TYPE I 200 Type set to I. ---> PORT 151,170,49,9,18,168 200 PORT command successful. ---> STOR EGRR01091946.tmp01 150 Opening BINARY mode data connection for EGRR01091946.tmp01. 226 Transfer complete. local: $data11.batlfpw.batfile1 remote: EGRR01091946.tmp01 68245 bytes sent in 1.73 seconds (38.52 Kbytes/s) ---> DELE EGRR01091946.a 550 EGRR01091946.a: No such file or directory. ---> RNFR EGRR01091946.tmp01 350 File exists, ready for destination name ---> RNTO EGRR01091946.a 250 RNTO command successful. Example Logging files. (Non GTS customer, alternative filename) Batfile1 contains 364 SNUK64 EGRR 191400 **MET20010919143027A.dat batch end *** -- FTPclient started \ORAC.$Z7MM -- 19 Sep 14:30:39 *PUT TRACE* 19 Sep 14:30:41 *ACK TRACE* +++ $data4.batngc.batfile1 local to remote host NGC MET20010919143027A.dat FTP put successful. +++ --idle_timeout cancelled in stop_ftp---- FTPclient stopped \ORAC.$Z7MM in stop_ftp---- | LFPW GTS data Input 12012846 bytes messages 10284 LFPW GTS data Output 134009340 bytes messages 64216 files 1342 LFPW charts & radar Input 11338333 bytes messages 1269 LFPW charts & radar Output 51691847 bytes messages 1298 files 1298 EIDB Input 434639 messages 382 EIDB Output 45202834 bytes messages 21245 files 1238 EDZW GTS data Input 2838097 bytes messages 6663 EDZW GTS data Output 60770439 bytes messages 29292 files 1040 EDZW Grib and T4 Input 30358227 bytes messages 2992 EDZW Grib and T4 Output 44655035 bytes messages 8882 files 248 LIIB Input 2371244 bytes messages 3688 LIIB Output 1668156 bytes messages 2167 files 715 EBBR GTS data Input 519644 bytes messages 93 EBBR GTS data Output 12726974 bytes messages 5649 files 1188 EBBR Grib Output 13996184 bytes messages 4411 files 963 EBBR T4 Output 22277046 bytes messages 349 files 349 |
| Brasilia | Yes |  |
| Hong Kong | No | Hong Kong – Beijing : 2.5 MB |
| Melbourne | Yes |  |
| Offenbach | Time Interval : 04.25. 02:43 - 04.25. 02:55 File name : File size : Directory : Host name : bras_i Protocol : FTP, SMTP, FILE, SCP1, WMO, MAP Date Time File name Hostname Type File size TT A =================================================== 04.25. 02:43:13 gme_new.bz2 bras_i FTP 44 1.27 N 04.25. 02:48:43 giff00000000.bz2 bras_i FTP 5803096 68.95 N 04.25. 02:51:58 gfff00030000.bz2 bras_i FTP 5743443 67.02 N 04.25. 02:54:07 gfff00060000.bz2 bras_i FTP 5720859 67.40 N =================================================== 0 00:10:54 4 Files (82.40 KB/s 22.02 Files/h) 16.47 MB 3m 24s | ECMWF 85.71 MB 571 files Toulouse 55.40 MB 3507 files Bracknell 62.92 MB 1664 files Bet Dagan 106.11 MB 565 files Rom 31.02 MB 1011 files Nairobi 9.36 MB 1364 files Denmark 228.30 KB 96 files Eumetsat 763.04 KB 349 files |
| Seoul | Using logging banner and README |  |
| Sofia | No | Our traffic is so various from 2MB to 500Mb and more |
| Tehran | No | Jeddah Circuit 7Mbytes and 110000 Files Delhi Circuit 1Mbytes and 100000 Files Kirachi Circuit 2Mbytes and 60000 Files |
| Tokyo | Under consideration | Currently none |
| Toulouse | Xferlog + owner log system | Circuit Toulouse-Offenbach: IN alpha: 47Mbytes and 15000 files OUT alpha: 27 Mbytes and 30000 files Circuit Toulouse-Bracknell: IN alpha: 138 Mbytes and 70000 files IN graphical: 49 Mbytes and 1000 files OUT alpha: 14 Mbytes and 12000 files OUT graphical: 12 Mbytes and 1200 files |

|  | 4. Miscellaneous | Notes |
| --- | --- | --- |
|  | (4d) Please advise tips on ftp implementation. |  |
| Bangkok | The WMO sockets is preferable. Because ftp is believed to be a security risk. |  |
| Beijing |  | In spite of FTP being widely employed in our internal data exchange, we currently have no practical experience in using FTP on GTS except that some FTP tests have been done on Beijing-Moscow circuit since last year. In the test, the rules of file naming are bilateral agreed. However, CMA and DWD are planning to upgrade the Beijing-Offenbach circuit. And, FTP will be used on the new link. In addition, the Internet is being used as a backup link for Beijing-Offenbach GTS circuit. Once Beijing-Offenbach GTS circuit interrupted, RTH Offenbach will send GTS data and its products to RTH Beijing by anonymous ftp. Some information about this application was filled in the questionnaire. |
| Bracknell | We have found FTP to be very disk intensive. Although using 2 batch files concurrently FTP seems very slow compared to X25. It is helpful to make error reporting as visible as possible. Routeing missing from remote end and full directories at remote end are a frequent cause of problems. | This questionnaire has been completed using the procedures that we follow at present. From early next year (2002) our Message Switch will be changing to Corobor's MESSIR.COMM on HP Unix machines and therefore the procedures may change. Tropics team Bracknell UK. |
| Brasilia |  | The Brasilia's system is the same one running at DWD Offenbach which was developed by IBL. The system provides flexible functions in ftp configuration, management and monitoring. |
| Hong Kong |  | Currently, Hong Kong, China has two GTS connections : Hong Kong – Tokyo circuit and Hong Kong – Beijing circuit. The Hong Kong – Tokyo circuit is an IP based circuit and AHLs are exchanged using sockets. FTP is used for the exchange of satellite data files. For the Hong Kong – Beijing circuit, an IP-based DDN link has been set up between Hong Kong and Guangzhou. Exchange of AHLs between Hong Kong and Beijing goes through Guangzhou. For the link between Hong Kong and Guangzhou, FTP is used for the exchange of AHLs as well as other data. In the questionairre regarding batched FTP, it refers to the link between Hong Kong and Guangzhou only. The link is also used for other regional data exchange between Hong Kong and Guangzhou. |
| Nairobi |  | The above information was provided by deceased Mr. James Abongo in June 1999. |
| Offenbach | Due to the high overhead of creating a data connection for each file it is recommended to send files in parallel especially on slow lines when lots of small files are being send. This has the additional advantage that one can send them with priorities. |  |
| Sofia | Error correction |  |
| Tehran |  | It seems that Teheran would use the ftp procedures not at present but in future. |
| Tokyo | A wise man says "fundamental ftp could be standard, but ftp implementation should be standard". | The batched ftp is not implemented in the current MSS. The MSS will be replaced by new one with the batched ftp in March 2005. |
| Washington |  | RTH Washington has implemented a portal for the delivery of WMO bulletins directly to the RTH by FTP through dedicated circuits or the Internet. This portal can receive observational and forecast WMO bulletins as contents of a file. All uploaded files are automatically processed by RTH Washington, and then the bulletins in the files are deliverd on the GTS. The bulletins received from the portal are handled just like they were received from any GTS circuits. The data is received by special servers open to the Internet with wrappers installed for security. The data providers must coordinate an ID and password with RTH Washington and they must use a specific IP address or range of addresses. The above information is about the portal named "FTP Input Service". The details are at "http://www.nws.noaa.gov/tg/circuit.shtml". |

For new message type without AHL

| Questions | Answers |
| --- | --- |
|  | Bangkok | Beijing | Brasilia | Montreal | Hong Kong | Melbourne | Offenbach | Seoul | Sofia | Tehran | Tokyo | Toulouse |
| Ftp of a pair of information and metadata files |
| Have you experienced the method of file pair transmission in Attachment II-15 of the Manual on the GTS? If YES, please show an outline. | No | No | No | No | No | No. The WMO specification is incomplete. We use similar methods internally | No. | No | No | No | No | Only suffixe ".ua", ".ub", ".a", ".b" and ".f" are implemented. WMO specification is incomplete. |
| Do you have any plans of the method of file pair transmission? | No |  |  | Possible requirement has been identified for future development | No | Yes – when the WMO spec is complete. | No, we do not plan to do this because the overhead is to high. It is much simpler and more effective to put additional information into the filename. | Yes | Yes, but we should buy some extra traffic channel and additional hardware. | No | No | No |
| Simple ftp |
| Do you exchange any data files by ftp? If YES, please show an outline, e.g. data name, volume, file naming, “get” or “put” basis, anonymous ftp or real account ftp, and compression? | No |  | Yes | Data exchanged with Bracknell: . satellite data (such as Meteosat, HRPT) . needs being revised now Data exchanged with US NESDIS: . NESDIS satellite data . some via TCP/IP part of GTS link for data available at NWS OOS . most via Internet (directly from NESDIS) . standard user based FTP . Pull procedure initiated automatically from Canada side . Data includes SSM/I, AMSUA, AMSUB, HIRS, QUIKSCAT, AIRS . No standard directory structure . No metadata . Access by permission only . NESDIS formats (TDR, Level 1B, BUFR, others) Data Exchanged with US NCEP: . US NCEP and Canadian model data . GRIB format . Standard user based FTP and Anonymous FTP . Pull procedure initiated automatically from requesting country Data Exchanged with US National Ice Center: . Satellite imagery for Ice Forecasting . Pull procedure initiated automatically from both Canadian and American side . Uses standard user based FTP . Although private line exists (256Kbps), it is considered as public (outside firewalls) Data Exchanged via Other TCP/IP: . Data for specific clients . Product Distribution System (PDS) - homebrew FTP pusher . Based on standard user based FTP . SSH and Sockets in future version . Handles retries, data conversions, logging . Used for national and international uses | [Hong Kong – Tokyo Circuit] Data type: satellite (SSM/I) File name: tp.hhmm1-hhmm2_ar.nnnnnnn where: "tp."= constant to indicate "time period" hhmm1-hhmm2 = hour/minute "_ar." = constant to indicate "area of data" nnnnnnn = oribit number ftp account : real Compression : no Put/get : put from Tokyo to Hong Kong Daily volume : 140Mbytes | Yes | Yes, we have many partners where we transmitt data on a 'put' basis. Volume is about 850 files per day with approximatly 1.3 Gigabyte of data. Compression used is either gzip or bzip2. Datatype is mostly binary. | Data type: SSM/I Account: anonymous Get/put: get Compression: gzip | We use anonymous and real account ftp , without compression. | No | (a) Meteosat data [20Mbytes/day] Bracknell --(get) --> Melbourne --(anonymous put) --> Tokyo (b) SSM/I data [150Mbytes/day] Washington --(anonymous get) --> Tokyo --(real-account put) --> Hong Kong | Yes |
| Do you switch data files to other GTS centres? If YES, please indicate the switching type (e.g. “put-put”, “get-put”). | No |  | Not GTS center, but with NMC |  | No | Yes – put to Tokyo. Get from Bracknell and receive routine puts from Bracknell | No. | “put-put” | Yes, we switch date get - put | No |  | Yes, put-put |
| Do you set a limit to exchange file size? If YES, please show the limit and possibility of segmentation of a large file in transmission. | No |  |  | No, but file sizes are set at time of procedure setup in consideration of link speeds. | No | No | No. | No | We sort by numbers of messages in file not by size. | No | No | Yes for WMO alpha data in output No for graphical data |