NAIROBI RTH - MAY   2002

THE STATUS  OF THE MAIN TELECOMMUNICATIONS NETWORK (MTN) AND REGIONAL METEOROLOGICAL TELECOMMUNICATION NETWORKS.

- RTH OFFENBACH – RTH NAIROBI CIRCUIT.

This MTN circuit is a 64 kbps digital leased circuit  using IP/OX and FTP protocols for exchange of data.

This circuit  has worked very well since it was implemented in October 1998.

- RTH TOULOUSE – RTH NAIROBI CIRCUIT.

This Bilateral circuit is a 64 kbps digital leased circuit  using IP/OX and  FTP protocols for exchange of data. This circuit has worked well with minimal interruptions since it was implemented.

RTH Nairobi also uses the link for Internet Access.

- CAIRO –NAIROBI CIRCUIT

The Nairobi-Cairo MTN link is a leased Analogue Telephone type of circuit using X.25 protocol for exchange of data.

This circuit has worked well with little interruption.

- RTH PRETORIA – RTH NAIROBI CIRCUIT

This REGIONAL circuit is a leased Analogue- Telephone- using IP for exchange of data and T4 charts. The link has worked well since it was revived in February 2001 after having been unserviceable for along time.

- NMC ADDIS-ABABA – RTH NAIROBI CIRCUIT

The circuit is a Leased Analogue Telephone type of circuit  using IP protocol for exchange of  both alphanumeric data and T4 charts. This circuit has not been operational  until recently when the line was revived and even after revival we can only send data to Addis-Ababa  hence we are using e-mail to receive data.

6.    NMC ENTEBBE – RTH NAIROBI CIRCUIT

This circuit is a Leased Telephone type of circuit using IP  protocol to exchange both alphanumeric data and T4 charts. The circuit has  worked  well since it was implemented.

7.    NMC DAR-ES-SALAAM – RTH NAIROBI CIRCUIT

This circuit is a Leased Telephone type of circuit using IP protocol to exchange both alphanumeric data and T4 charts. The circuit has been working reasonably  well since its implementation.

8.    NMC KIGALI – RTH NAIROBI AND NMC BUJUMBURA – RTH NAIROBI CIRCUITS.

The two centres are currently receiving data from Nairobi RTH through AFMET II HF broadcasts while they are sending their data to Nairobi via AFTN and E-mail  for Kigali.

There are plans to establish a leased circuit using IP protocol between Kigali and  Nairobi soon. The terminal equipment at the two centres have already been procured .The process of  getting a leased circuit from the respective telecommunications authorities has been initiated.