| WORLD METEOROLOGICAL ORGANIZATION _________________________ REGIONAL ASSOCIATION II IMPLEMENTATION - CO-ORDINATION MEETING ON THE GTS IN RA II MOSCOW, 8 - 10 SEPTEMBER 2003 |  | RA II/ICM-GTS 2003/Doc. 2(2) (21.VIII.2003) ____________ ITEM 2.1 -2.3 ENGLISH only |
| --- | --- | --- |

STATUS OF IMPLEMENTATION AT RTH TOKYO

(Submitted by Hiroyuki Ichijo (Japan) )

Summary and purpose of document This document includes the report on the status of implementation of systems, circuits and facilities at RTH Tokyo, and information on SHIP reports collected at RTH Tokyo.

1.  GTS facilities

Main GTS facilities such as Message Switching System (MSS), FAX system started operation in March 1996.  Subsequently, considering TCP/IP strategy and Internet trends, they were reinforced in 1998 and 1999, respectively.  Japan Meteorological Agency (JMA) plans to replace them by new ones in 2005 in consideration of expansion and improvement of information exchange with the current IT trend.

2.  GTS circuits

Table 1  Implementation status of GTS circuits connected with RTH Tokyo (As of 21 August 2003)

| Circuit | Speed | Protocol | Exchange data type |
| --- | --- | --- | --- |
| Washington Tokyo | MTN | FR (IMTN cloud I) CIR: WT ( 32/768kbps ( TK Port: WT=1.5Mbps,TK=1.5Mbps | TCP/IP Socket FTP | Message (A/N, binary, fax) File (Satellite data) |
| Melbourne Tokyo | MTN | FR (IMTN cloud I) CIR: MB ( 16/32kbps ( TK Port: MB=256kbps,TK=1.5Mbps | TCP/IP Socket FTP | Message (A/N, binary, fax) File (Satellite data) |
| Beijing Tokyo | MTN | FR (NNI basis) CIR: BJ (32/32kbps( TK Port: BJ=64kbps,TK=192kbps | TCP/IP Socket | Message (A/N, binary, fax) |
| New Delhi Tokyo | MTN | 64kbps | TCP/IP Socket | Message (A/N, binary) |
| Seoul Tokyo | RMTN | FR (NNI basis) CIR: SL (16/16kbps( TK Port: SL=64kbps,TK=192kbps | TCP/IP Socket | Message (A/N, binary, fax) |
| Khabarovsk Tokyo | RMTN | 14.4kbps | X.25 PVC | Message (A/N, binary, fax) |
| Bangkok Tokyo | RMTN | FR (NNI basis) CIR: BK (16/16kbps( TK Port: BK=64kbps,TK=192kbps | TCP/IP Socket | Message (A/N, binary) |
| Hong Kong Tokyo | RMTN | FR (NNI basis) CIR: HK (16/16kbps( TK Port: HK=64kbps,TK=192kbps | TCP/IP Socket FTP | Message (A/N, binary) File (Satellite data) |
| Manila Tokyo | Inter-regional | 200bps | Asynchronous | Message (A/N) |

CIR :  Committed Information Rate

FR  :  Frame Relay

NNI :  Network-to-Network Interconnection

Table 2  Upgrade plans of GTS circuits connected with RTH Tokyo

| Circuit | Speed | Protocol | Remarks |
| --- | --- | --- | --- |
| Beijing Tokyo | MTN | FR (IMTN cloud II) CIR: BJ (48/48kbps( TK Port: BJ=128kbps,TK=128kbps | TCP/IP Socket | Target : by the end of 2003 |
| New Delhi Tokyo | MTN | FR (IMTN cloud II) CIR: ND (16/16kbps( TK Port: ND=64kbps,TK=128kbps | TCP/IP Socket | Target : 2003/2004 |
| Khabarovsk Tokyo | RMTN | 14.4 - 28.8kbps (V.34) | TCP/IP Socket | Target : by the end of 2003 |

3.  Use of the Internet

3.1  Internet accessing systems and servers

At JMA headquarters the Internet accessing system which was replaced by new one in March 2001 has recently been reinforced for further improvement of reliability and security.  There are two permanent connections to the Internet Service Providers (ISPs) for multi-homed connectivity which provides more reliability than the case of only one ISP.  Each of services has been upgraded in its speed to 10Mbps/2Mbps (outgoing/incoming, asymmetric connection service) and 8Mbps (symmetric) respectively, in order to meet recent requirements in providing data to meteorological users.

All public servers such as JMA-DDB, NEAR-GOOS (North East Asia Regional - Global Ocean Observing System), WDCGG (World Data Centre for Greenhouse Gases) and JMA-Web are placed in DMZ (Demilitarized Zone) for security reasons.  Firewalls are monitored and maintained appropriately with contractual vendor support.

3.2  RSMC Data Serving System

The RSMC Data Serving System (DSS) has been providing NWP products and global observational data mainly to NMCs in the Asian region through the Internet since 1995.  To meet user requirements in expanding data services the DSS was upgraded by the new one in April 2002.  The new DSS is a cluster system consists of three PC servers (see Figure 5) in DMZ.  It is confirmed that the latest PC based server system with clustering architecture has enough reliability and maintainability  to keep continuous operation 24 hours a day, and also cost-effectiveness.

Users are able to access to the DSS by standard ftp commands with authentication procedures.  The DSS identifies accessing from an authenticated user by a user ID, a user password and an IP address of a client host.   Users are requested to change user passwords once a month to ensure security.  E-mails are used for liaison between DSS administrator and users on operational information, notice of new available data and so on.

3.3  Available information of RTH Tokyo

The latest information on GTS matters by RTH Tokyo is available at JMA-DDB and JMA Web site.   The details are:

- History of upgrades of GTS circuits connected with RTH Tokyo

http://www.jma.go.jp/JMA_HP/jma/jma-eng/jma-center/rth/GTS_upgrade.html

- Current status of GTS circuits connected with RTH Tokyo

http://www.jma.go.jp/JMA_HP/jma/jma-eng/jma-center/rth/RTH_current.html

- Routing Catalog of RTH Tokyo

http://ddb.kishou.go.jp/GTS_routeing/RJTD/RJTDROCA.TXT

- Comprehensive Catalog of Meteorological Bulletins in the zone of responsibility of RTH Tokyo

http://ddb.kishou.go.jp/pub/BulletinCatalog/

- List of observing stations in Japan

http://ddb.kishou.go.jp/pub/ObservingStation/OBS_STATION.DAT

4.  Collection of SHIP reports

Although the annual number of SHIP reports has been decreasing since the peak year in 1999, it does not seem that the trend of a sharp drop will continue in the years ahead.    Most of collected reports except for those invalid, garbled and/or duplicated are compiled into RJTD bulletins and put onto the GTS timely.

# Text boxes

INTERNET

ISP

Dummy data tool

Dummy data tool

Socket AP

Socket AP

Test host 2

Simulating FAX

Test host 1

Simulating MSS

Router for Test connections

FAX

FAX

MSS

MSS

Line Switch (for duplicated system)

Packet Switch

Router for GTS connections

NEC IP45/604  (Cisco OEM, Cisco3640)

NAT (Network Address Translation) Router

NEC IP45/621M (Cisco OEM, Cisco4500-M)

Router for IMTN

NEC IP45/651 (Cisco OEM, Cisco7010)

FTP

Server

FTP

Server

Test partners

TCP/IP test environment

via Internet

Figure 1   GTS facilities including TCP/IP test environment via Internet

ISP #2 (C&W)

ISP #1 (IIJ)

Figure 3   Transport level configuration planned in the stage of 2003

64kbps

128kbps

Equant Frame Relay Network

IMTN cloud II    (Seamless Network by a single provider)

New Delhi

Beijing

1.5Mbps

Internet accessing system at JMA headquarters

Internet

Main components of Operational Telecommunication System

at Kiyose operation Office

AS 64520

Pure IP circuits

Asynchronous

circuit

X.25 circuits

Private IP addresses

Official IP addresses

Private IP addresses

Private IP addresses

Official IP addresses

256kbps

1.5Mbps

BT Frame Relay Network

IMTN cloud I    (Seamless Network by a single provider)

Dedicated line connections

200

bps

DNS, Web, FTP,

Mail, News servers

Local

Observatories

Satellite IP network system for information common-use

Real-time file

serving system

Manila

14.4

-28.8

kbps

Khabarovsk

JMA Secure Zone

COSMETS

LAN

JMA Office

Intranet

Packet Shapers

RSMC

Data Serving System

Load Balancer

Public servers

(DDB, NEAR-GOOS…)

Figure 5    RSMC Data Serving System

DMZ

FireWalls

Router Controllers

Proxy Server

8Mbps

Figure 4    Internet accessing systems and servers

CAT

Frame Relay

Network

Figure 2   Transport level configuration of GTS circuits connected with RTH Tokyo

HKT

Frame Relay

Network

DACOM

Frame Relay

Network

Seoul

KDDI

Frame Relay Networks

64kbps

NNI basis Frame Relay connections

64kbps

64kbps

192kbps

1.5Mbps

256kbps

1.5Mbps

BT Frame Relay Network

IMTN cloud I    (Seamless Network by a single provider)

Dedicated line connections

200bps

Manila

64kbps

14.4kbps

Khabarovsk

New Delhi

### Tokyo

CAT

Frame Relay

Network

BTA

Frame Relay

Network

HKT

Frame Relay

Network

DACOM

Frame Relay

Network

Seoul

KDDI

Frame Relay Networks

64kbps

Beijing

NNI basis Frame Relay connections

64kbps

64kbps

64kbps

192kbps

Hong Kong

10Mbps (outgoing)

2Mbps(incoming)

128kbps

### Tokyo

Hong Kong

Bangkok

Melbourne

Washington

Bangkok

Melbourne

Washington

Figure6   Annual amounts of SHIP reports collected at RTH Tokyo