| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Implementation-coordination Team on INFORMATION SYSTEMS & SERVICES geneva, 9-13 september 2002 |  | ICT-ISS 2002/Doc. 6.1(1)ADD. 1 (3.IX.2002) ____________ ITEM 6.1 ENGLISH only |
| --- | --- | --- |

Data representation and codes forms, including procedures for changes

## Modifications to Binary and Alphanumeric Codes

(Submitted by the Secretariat)

________________________________________________________________

Summary and Purpose of Document

The ET/DR&C has recommended supplementary additions to BUFR/CREX Code Tables, proposed.  They are additions to Annex 2 and Annex 3 of Draft Recommendation 6.2/(3) 1.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to consider the proposal of ET/DR&C and recommend it for approval by CBS.

| WORLD METEOROLOGICAL ORGANIZATION _________________ COMMISSION FOR BASIC SYSTEMS EXTRAORDINARY SESSION CAIRNS, AUSTRALIA, 4 TO 12 DECEMBER 2002 |  | CBS-Ext.(02)/Doc. 6.2(3), ADD. 1 (3.IX.2002) _______ ITEM 6.2 Original: ENGLISH |
| --- | --- | --- |

WORLD WEATHER WATCH PROGRAMME, SUPPORT FUNCTIONS AND PUBLIC WEATHER SERVICES, INCLUDING THE REPORTS BY THE CHAIRS OF THE OPEN PROGRAMME AREA GROUPS

INFORMATION SYSTEMS AND SERVICES (ISS)

Data Representation and Codes

## Modifications to Binary and Alphanumeric Codes

(Submitted by the Secretary-General)

Summary and Purpose of Document This document contains supplementary additions to BUFR/CREX Code Tables, proposed by the OPAG/ISS. They are additions to Annex 2 and Annex 3 of Draft Recommendation 6.2/(3) 1.

# ACTION PROPOSED

The Commission is invited to:

- Note the requirements and the additions to the recommendation expressed in this document;

- Adopt these additions to Draft Recommendation 6.2/(3) 1.

__________

Appendices:	A.	Additions to Annex 2 of Draft Recommendation 6.2/(3)

B.	Additions to Annex 3 of Draft Recommendation 6.2/(3)

References:	Report of the ICT on ISS (Geneva, 9-13 September 2002)

CBS-Ext. (02)/Doc. 6.2(3), APPENDIX A

DRAFT TEXT FOR INCLUSION IN THE GENERAL SUMMARY OF CBS-EXT. (02)

6.2	INFORMATION SYSTEMS AND SERVICES (ISS) (Agenda item 6.2)

…………

Data Representation and Codes

…………

MODIFICATIONS TO THE MANUAL ON CODES

…………

6.2.x.5	The Commission further recommended additions to BUFR/CREX tables (See Annex 3 of Draft Recommendation 6.2(3)/1 (CBS-Ext.(02)) for:

…………

- …………

- Coding in BUFR, SIGMET messages

- …………

- Coding certain types of altimeter data

- For representation of ground-based Global Navigation Satellite System (GNSS) data in BUFR format

Modifications or additions to ANNEX 2 of Draft Recommendation 6.2(3)/1 CBS-Ext. (02):

ADDITIONS TO 94-XII BUFR AND FM 95-XII CREX Tables:

Introduce the following new descriptors:

| 0 07 032 | Height of sensor above local ground (or deck of marine platform) | m | 2 | 0 | 16 |
| --- | --- | --- | --- | --- | --- |
| 0 07 033 | Height of sensor above water surface | m | 1 | 0 | 12 |

with notes added under Table B, Class 7, referring to 0 07 032 and 0 07 033:

- Height of sensor above local ground (or deck of marine platform) is the actual height of sensor above ground (or deck of marine platform) at the point where the sensor is located.  This descriptor does not redefine the descriptor either 0 07 030 or 0 07 033.

- Height of sensor above water surface is the height of sensor above water surface of sea or lake.  This descriptor does not redefine the descriptor either 0 07 030 or 0 07 032.

Add descriptors (needed particularly for the Automatic Weather Stations)

| 0 08 010 | Surface qualifier (temperature data) | Code table | 0 | 0 | 4 |
| --- | --- | --- | --- | --- | --- |

0 08 010

Surface qualifier (for temperature data)

| Code figure |  |
| --- | --- |
| 0 | Reserved |
| 1 | Bare soil |
| 2 | Bare rock |
| 3 | Land grass cover |
| 4 | Water (lake, sea) |
| 5 | Flood water underneath |
| 6 | Snow |
| 7 | Ice |
| 8 | Runway or road |
| 9 | Ship or platform deck in steel |
| 10 | Ship or platform deck in wood |
| 11 | Ship or platform deck partly covered with rubber mat |
| 12-30 | Reserved |
| 31 | Missing value |

Modifications or additions to ANNEX 3 to Draft Recommendation 6.2(3)/1 CBS-Ext. (02):

ADDITIONS TO 94-XII BUFR AND FM 95-XII CREX Tables:

PROPOSED ADDITIONS TO BUFR TABLE D FOR AMDAR

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- |
| F | X | Y |  |  |
|  |  |  |  |  |  | (Standard AMDAR reports) |
| 3 | 11 | 005 | 0 | 01 | 008 | Aircraft identifier |
|  |  |  | 0 | 01 | 023 | Sequence number |
|  |  |  | 3 | 01 | 021 | Latitude and longitude |
|  |  |  | 3 | 01 | 011 | Year, month and day |
|  |  |  | 3 | 01 | 013 | Hour, minute and second |
|  |  |  | 0 | 07 | 010 | Flight level |
|  |  |  | 0 | 08 | 009 | Detailed phase of flight |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |
|  |  |  | 0 | 11 | 031 | Degree of turbulence |
|  |  |  | 0 | 11 | 036 | Derived equivalent vertical gust speed |
|  |  |  | 0 | 12 | 101 | Temperature/dry-bulb temperature |
|  |  |  | 0 | 33 | 025 | ACARS interpolated values |

FOR IMPROVING REGULATIONS ON REPLICATION AND COMPRESSION

Add a sub-note (ix) to note 2 of regulation 94.6.3:

(ix)  When delayed replication is present, it is required that the number of replications shall be identical for each data subset if data compression is to be used.  In such cases, sub-note (vii) shall apply when coding the number of replications.

FOR CODING SIGMET

Proposed Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 01 037 | SIGMET sequence number | CCITT IA5 | 0 | 0 | 24 | Character | 0 | 3 |
| 0 01 065 | ICAO region identifier | CCITT IA5 | 0 | 0 | 256 | Character | 0 | 32 |
| 0 08 019 | Qualifier for following centre identifier | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 10 064 | SIGMET cruising level | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 20 028 | Expected change in intensity | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 27 035 | Length of phenomenon | M | -3 | 0 | 13 | m | -3 | 4 |
| 0 28 035 | Width of phenomenon | M | -3 | 0 | 13 | m | -3 | 4 |

Add the following new categories to Table A within BUFR and CREX:

  - Forecasts

  - Warnings

Add the following new code table values for the descriptors to Table B within BUFR:

0 08 011

21		Thunderstorm

22		Tropical Cyclone

23		Mountain Wave

24		Duststorm

25		Sandstorm

0 20 008

15		Obscured (OBSC)

16		Embedded (EMBD)

0 20 024

5		Severe

Code tables for proposed new Table B descriptors:

| Code figure | 0 08 019 Qualifier for following centre identifier |
| --- | --- |
| 0 | Reserved |
| 1 | ATS (Air Traffic Service) unit serving FIR (Flight Information Region) |
| 2 | FIR (Flight Information Region) |
| 3 | UIR (Upper Information Region) |
| 4 | CTA (Control Area) |
| 5 | VAAC (Volcanic Ash Advisory Centre) |
| 6 | MWO (Meteorological Watch Office) issuing SIGMET |
| 7-14 | Reserved |
| 15 | Missing value |

| Code figure | 0 10 064 SIGMET cruising level |
| --- | --- |
| 0 | Subsonic |
| 1 | Transonic |
| 2 | Supersonic |
| 3-6 | Reserved |
| 7 | Missing value |

| Code figure | 0 20 028 Expected change in intensity |
| --- | --- |
| 0 | No change (NC) |
| 1 | Forecast to weaken (WKN) |
| 2 | Forecast to intensify (INTSF) |
| 3-6 | Reserved |
| 7 | Missing value |

New Table D descriptors:

|  |  | (SIGMET header) |
| --- | --- | --- |
| 3 16 020 | 1 02 002 | Replication of 2 descriptors two times (Define validity period) |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 01 037 | SIGMET sequence number |
|  | 0 10 064 | SIGMET cruising level |
|  | 0 08 019 | Qualifier for location identifier, 1=ATS unit serving FIR |
|  | 0 01 062 | Short ICAO location identifier |
|  | 1 02 000 | Replicate two descriptors |
|  | 0 31 001 | Replication count |
|  | 0 08 019 | Qualifier for location identifier, 2=FIR, 3=UIR, 4=CTA |
|  | 0 01 065 | ICAO region identifier |
|  | 0 08 019 | Qualifier for location identifier, 6=MWO |
|  | 0 01 062 | Short ICAO location identifier |
|  | 0 08 019 | Qualifier for location identifier, Missing=Cancel |
|  |  | (Volcanic ash SIGMET, Volcano details) |
| 3 16 021 | 0 08 011 | Meteorological feature, 17=Volcano |
|  | 0 01 022 | Name of feature |
|  | 0 08 007 | Dimensional significance, 0=Point |
|  | 3 01 023 | Location |
|  | 0 08 007 | Dimensional significance, Missing=Cancel |
|  | 0 20 025 | Obscuration, bit 10=Volcanic Ash |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Volcanic ash SIGMET, Obs or Fcst area and motion) |
| 3 16 022 | 0 08 021 | Time Significance, 16=Analysis, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 07 010 | Flight level (base of cloud) |
|  | 0 07 010 | Flight level (top of cloud) |
|  | 0 27 035 | Length of phenomenon |
|  | 0 28 035 | Width of phenomenon |
|  | 0 08 007 | Dimensional significance, 2=Area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 19 005 | Direction of motion |
|  | 0 19 006 | Speed of motion |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 20 090 | Type of cloud, 5=Volcanic Ash/Eruption |
|  | 0 20 028 | Expected change in intensity |
|  | 0 08 021 | Time significance, Missing=cancel |

|  |  | (Volcanic ash SIGMET, Fcst area) |
| --- | --- | --- |
| 3 16 023 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 08 007 | Dimensional significance, 2=Area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 20 090 | Type of cloud, 5=Volcanic Ash/Eruption |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (Volcanic ash SIGMET, Outlook) |
| 3 16 024 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 1 07 000 | Replicate 7 descriptors |
|  | 0 31 001 | Replication count |
|  | 0 07 010 | Flight level (base of cloud) |
|  | 0 07 010 | Flight level (top of cloud) |
|  | 0 08 007 | Dimensional significance, 2=Area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 20 090 | Type of cloud, 5=Volcanic Ash/Eruption |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (SIGMET, Obs or Fcst location and motion) |
| 3 16 025 | 0 08 021 | Time Significance, 16=Analysis, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 07 010 | Flight level (base of cloud) |
|  | 0 07 010 | Flight level (top of cloud) |
|  | 0 27 035 | Length of phenomenon |
|  | 0 28 035 | Width of phenomenon |
|  | 0 08 007 | Dimensional significance, 1=point or 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 19 005 | Direction of motion |
|  | 0 19 006 | Speed of motion |
|  | 0 19 007 | Radius of feature |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 20 028 | Expected change in intensity |
|  | 0 08 021 | Time significance, Missing=cancel |

|  |  | (SIGMET, Fcst position) |
| --- | --- | --- |
| 3 16 026 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 08 007 | Dimensional significance, 1=point or 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 19 007 | Radius of feature |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (SIGMET, Outlook) |
| 3 16 027 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 1 06 000 | Replicate 7 descriptors |
|  | 0 31 001 | Replication count |
|  | 0 07 010 | Flight level (base of cloud) |
|  | 0 07 010 | Flight level (top of cloud) |
|  | 0 08 007 | Dimensional significance, 1=point or 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (Thunderstorm SIGMET) |
| 3 16 028 | 3 16 020 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 21=Thunderstorm |
|  | 0 20 023 | Other weather phenomenon, bit 2=Squalls or all 18 bits = Missing |
|  | 0 20 021 | Type of precipitation, bit 14=Hail or all 30 bits=Missing |
|  | 0 20 008 | Cloud distribution 15=OBSC, 16=EMBD, 12=FRQ, 31=Missing |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Tropical Cyclone SIGMET) |
| 3 16 029 | 3 16 020 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 22=Tropical Cyclone |
|  | 0 01 027 | WMO storm name |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 1 01 000 | Delayed replication |
|  | 0 31 000 | Short replication factor |
|  | 3 16 026 | SIGMET Fcst location |
|  | 1 01 000 | Delayed replication |
|  | 0 31 000 | Short replication factor |
|  | 3 16 027 | SIGMET Outlook |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |

|  |  | (Turbulence SIGMET) |
| --- | --- | --- |
| 3 16 030 | 3 16 020 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 13=Turbulence |
|  | 0 11 031 | Degree of turbulence, 10=Mod, 11=Severe |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Icing SIGMET) |
| 3 16 031 | 3 16 020 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 15=Airframe Icing |
|  | 0 20 041 | Airframe icing, 7=Severe |
|  | 0 20 021 | Type of precip, bit 3=Liquid freezing precip or all 30 bits = Missing |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Mountain Wave SIGMET) |
| 3 16 032 | 3 16 020 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 23=Mountain Wave |
|  | 0 20 024 | Intensity of phenomena, 5=Severe |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Duststorm SIGMET) |
| 3 16 033 | 3 16 020 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 24=Duststorm |
|  | 0 20 024 | Intensity of phenomena, 3=Heavy |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Sandstorm SIGMET) |
| 3 16 034 | 3 16 020 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 25=Sandstorm |
|  | 0 20 024 | Intensity of phenomena, 3=Heavy |
|  | 3 16 025 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (SIGMET cancellation) |
| 3 16 035 | 3 16 020 | SIGMET header |
|  | 1 02 002 | Replication of 2 descriptors two times (Define validity period) |
|  | 3 01 011 | Year, Month, Day of SIGMET to cancel |
|  | 3 01 012 | Hour, Minute of SIGMET to cancel |
|  | 0 01 037 | SIGMET sequence identifier of SIGMET to cancel |
|  | 0 10 064 | SIGMET cruising level of SIGMET to cancel |

FOR CERTAIN TYPES OF ALTIMETER DATA

In existing table Common Table C-5: BUFR 0-01-007 (Satellite Identifier), add new entries:

720 = TOPEX and 721 = GFO

Add new Table B entry:

0-05-044, Cycle number, Numeric, Scale = 0, Reference value = 0, Data width = 11 (BUFR)

4 (CREX)

FOR REPRESENTATION OF GROUND-BASED GNSS DATA IN BUFR FORMAT

Observations at each ground-based station are made at regular intervals, typically 15 minutes, and consist of measurements of several GPS or other GNSS satellites observable from the station at that time.  GNSS means Global Navigation Satellite System, a generic term which includes the U.S. Global Positioning System (GPS) satellites, the corresponding Russian GLONASS satellites and the proposed European GALILEO satellites.

The instruments measure the phase shift of the satellite signal relative to what would have been expected if the entire signal path were a vacuum.  Using the wavelength, this is converted into an atmospheric path delay (typically 2-3 metres).

Data are processed locally to generate estimates of the path delays for a zenith view and for limb views in the main geographic directions.  The processing also generates estimates of errors for these quantities.

New Table D entry for the representation of ground-based GNSS data

The table gives the expansion for the proposed new sequence 3 07 022 for ground-based GNSS data.  New descriptors and code table entries are marked in italics and are fully described in subsequent tables.

| Descriptor | Element name | Units | Notes |
| --- | --- | --- | --- |
| 3 07 022 | (Ground-based GNSS data) |  |  |
| 0 01 015 | Station or site name | CCITT IA5 |  |
| 3 01 011 | Year Month Day | Year Month Day |  |
| 3 01 012 | Hour Minute | Hour Minute |  |
| 3 01 022 | Latitude (high accuracy) Longitude (high accuracy) Height of station | Degrees Degrees Metres |  |
| 0 08 021 | Time significance | Code Table | '23' = 'monitoring period' |
| 0 04 025 | Time period or displacement | Minutes |  |
| 0 10 004 | Pressure | Pa |  |
| 0 12 001 | Temperature | K |  |
| 0 13 003 | Relative humidity | % |  |
| 0 33 038 | Quality flags for ground-based GNSS data | Flag Table | New descriptor |
| 0 08 022 | Total number | Numeric | No. of GNSS satellites used |
| 1 06 025 | Replication |  | 6 descriptors 25 times |
| 0 02 020 | Satellite classification | Code Table | New table entries |
| 0 01 050 | Platform transmitter Id. number | Numeric |  |
| 0 05 021 | Azimuth | Degrees true |  |
| 0 07 021 | Elevation | Degrees |  |
| 0 15 031 | Atmospheric path delay in satellite signal | Metres | New descriptor |
| 0 15 032 | Estimated error in atmospheric path delay | Metres | New descriptor |
| 0 08 060 | Sample scanning mode significance | Code Table | =5 for north/south |
| 0 15 033 | Difference in path delays for limb views at extremes of scan | Metres | New descriptor |
| 0 15 034 | Estimated error in path delay difference | Metres | New descriptor |
| 0 08 060 | Sample scanning mode significance | Code Table | =6 for east/west |
| 0 15 033 | Difference in path delays for limb views at extremes of scan | Metres | New descriptor |
| 0 15 034 | Estimated error in path delay difference | Metres | New descriptor |
| 0 15 035 | Component of zenith path delay due to water vapour | Metres | New descriptor |
| 2 01 131 | Change bit width |  |  |
| 2 02 129 | Change scale |  |  |
| 0 13 016 | Precipitable water | Kg.m-2 |  |
| 2 02 000 | Reset scale |  |  |
| 2 01 000 | Reset bit width |  |  |
| 0 15 011 | Log10 of integrated electron density | Log10(m-2) |  |

New Table B entries:

| Table Reference F XX YYY | Element name | Unit | Scale | Reference value | Data width (bits) |
| --- | --- | --- | --- | --- | --- |
| 0 15 031 | Atmospheric path delay in satellite signal | m | 4 | 10000 | 15 |
| 0 15 032 | Estimated error in atmospheric path delay | m | 4 | 0 | 10 |
| 0 15 033 | Difference in path delays for limb views at extremes of scan | m | 5 | -10000 | 15 |
| 0 15 034 | Estimated error in path delay difference | m | 5 | 0 | 14 |
| 0 15 035 | Component of zenith path delay due to water vapour | m | 4 | 0 | 14 |
| 0 33 038 | Quality flags for ground-based GNSS data | Flag table | 0 | 0 | 10 |

New code figures for Satellite Classification in Code Table 0 02 020

| Code figure | Meaning |
| --- | --- |
| 401 | GPS |
| 402 | GLONASS |
| 403 | GALILEO |

New code figures for Sample Scanning Mode Significance in Code Table 0 08 060

| Code figure | Meaning |
| --- | --- |
| 5 | North/South |
| 6 | East/West |

New Flag Table:  0 33 038

Quality Flags for ground-based GNSS data

| Bit No. | Meaning when set |
| --- | --- |
| 1 | Total Zenith Delay quality is considered poor |
| 2 | GALILEO satellites used |
| 3 | GLONASS satellites used |
| 4 | GPS satellites used |
| 5 | Meteorological data applied |
| 6 | Atmospheric loading correction applied |
| 7 | Ocean tide loading applied |
| 8 | Climate quality data processing |
| 9 | Near-real time data processing |
| All 10 | Missing value |

New entries for Originating/Generating Sub-Centre in 0 01 034 - Common Code Table C-1

| Centre | Sub-centres |
| --- | --- |
| Code figure | Name | Code Figure | Name |
| 74 | UK Meteorological Office, Bracknell (RSMC) | 21 | Agenzia Spaziale Italiana (Italy) |
|  |  | 22 | Centre National de la Recherche Scientifique (France) |
|  |  | 23 | GeoForschungsZentrum (Germany) |
|  |  | 24 | Geodetic Observatory Pecny (Czech Republic) |
|  |  | 25 | Institut d'Estudis Espacials de Catalunya (Spain) |
|  |  | 26 | Swiss Federal Office of Topography |
|  |  | 27 | Nordic Commission of Geodesy |