Commission for Basic Systems

Information Systems and Services – GTS and Data Management

# Technical enquiry on GTS operation  RTH Beijing

  - What is the maximum length of meteorological messages containing data in binary presentation forms that your RTH can currently receive, handle and possibly relay forward to other centres:…………………………………………………………

The maximum length of the binary messages currently received at RTH Beijing is 15KBytes.  But, our current MSS can handle and forward the messages with the maximum length of 500KBytes.

  - At which date is your RTH expected to be able to receive, handle and relay meteorological messages containing data in binary presentation forms up to the maximum length of 500 Koctets:…………………………………………………………

Now.

  - According to your knowledge and experience, what is the status of the NMCs that are associated (connected) to your RTH with respect to the 2 questions above:……………………………………………..

We’re not sure whether NMC Pyongyang can be ready for supporting the extension of the length of binary messages before November, 2007.

- Operational procedures for text of GTS messages/bulletins

The CBS/ Expert Team on Enhanced use of Data Communications Systems (ET-EUDCS) expressed the view that some of the current specifications (originating from teleprinter operation) of operational procedures for the transmission of meteorological messages have become a serious limitation with today's computer-based systems.  A review should be considered, taking into account that most, if not all NMCs, and all RTHs are operating computer-based (e.g. PCs) GTS systems.  The review must consider the implications and requirements of the migration to table driven codes and the impact on small NMCs.

Please indicate your comments on the following elements with respect to your RTH, and, according to your knowledge and experience, as regards the NMCs that are associated (connected) to your RTH:

  - Is the International Telegraph Alphabet No. 2 (5 bits) still needed?

Not needed.

  - Is there still a need to limit the set of characters from the International Alphabet No. 5 (8 bits) used in meteorological messages;  in particular, would it be feasible to allow the use of upper and lower case characters?

Not needed.

RTH Beijing can support the use of upper and lower case characters in messages.

  - Is the antiquated "end of line" marker (CR-CR-LF) still needed?

Not needed.

  - Is the limit of 69 characters per line (teleprinter line) still needed?

Not needed.

  - Additional views:

Some additional information:

1) NMC Ulanbator has a firm plan to upgrade its MSS soon. It seems the two issues in your enquiry will not be a problem;

2) NMC Pyongyang is receiving messages longer than 15000 octets from CMA's satellite channel now. But their MSS may need to be upgraded to handle longer messages