| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Implementation-coordination Team on INFORMATION SYSTEMS & SERVICES geneva, 18 - 22 september 2006 |  | ICT-ISS 2006/Doc. 2.2(2) (14.IX.2006) ____________ ITEM 2.2 ENGLISH only |
| --- | --- | --- |

Status of Implementation of GTS in Region II

(Submitted by the Hiroyuki ICHIJO

(RAII Coordinator of the Subgroup on Regional Aspects of the GTS and Data Management) )

Summary and Purpose of Document This document includes the report on the status on the Regional Meteorological Telecommunication Network (RMTN) in Region II.

Action Proposed :  The meeting is invited to comment on the status on the RMTN in Region II.

Appendix :	A.   Current status of RMTN in RA II as of September 13, 2006

- Current status of multipoint telecommunication system in RA II

[General summary]

Fundamental strategies to Improve the RMTN are:

- Acceleration of TCP/IP migration with a first priority

- Selecting an appropriate network service with a possible framework

- Use of the Internet for a GTS circuit as the very end solution

70 of 82 circuits in RMTN plan are in operation, namely the latest implementation rate is 85 percent.  Problems are that NMCs Baghdad, Kabul, Thimpu and Phnom Penh be isolated from the GTS, and that 33 percent of all circuits be still required to increase their speed.

Generally TCP/IP migration is making satisfactory progress.  About 60 percent are operating on pure TCP/IP.  It is expected that the achievement rate would be over 70 percent by the end of 2006.

Migration to cost-effective connections has been making steady progress since 2000.  Frame Relay service has been introduced in 17 circuits.  IP-VPN (Virtual Private Network) with MPLS (Multi Protocol Label Switching) is a promising network service, though there is currently no MPLS link in the GTS.  Most of the MTN and related circuits will migration from Frame Relay to IP-VPN MPLS within a few years.

There are 9 Internet based RMTN circuits.  In addition, the Internet connection is often used for GTS backup.  Introducing VPN techniques to their Internet circuits is recommended for security reason.

Satellite broadcasting systems are used for complements to the GTS, backup sources and cost-effective alternatives to HF radio broadcasts.  Although RTHs Bangkok, Jeddah, Tehran and Tokyo are still operating HF broadcast, the day is not far distant when HF broadcasts will disappear in Region II.

At its thirteenth session, CBS urged Member countries to develop as soon as possible a national migration plan to Table Driven Code Forms (TDCFs), derived from the international plan, with analysis of impacts, costs, solutions, sources of funding (as necessary), national training, technical planning and schedule.

To know current status of migration to Table Driven Code Forms (TDCFs) by Member countries, a survey was conducted in August 2006.  In addition, some regional templates of BUFR and CREX will be developed for the migration by Members of WMO in RAII.

To promote regional contribution to the development of the WMO Information System (WIS), the VPN Pilot Project in Regions II and V has been making steady progress.  The outcome will be submitted to the third meeting of the Inter-Commission Coordination Group on WIS (ICG-WIS) (Beijing, 5-8 September 2006) and also the CBS Technical Conference on the WIS (Seoul, 6-8 November 2006) preceding CBS-ext.2006..

- Strategy to improve the RMTN

Strategic improvement of the RMTN has been proceeding to meet WWW requirements in the Region since late 1990’s.  Regional Association II endorsed the Improved RMTN concept using modern cost-effective network services at its twelfth session (Seoul, 19-27 September 2000).  Furthermore Internet based techniques were studied and recommended as a GTS standard.   In the circumstances, Implementation Co-ordination Meeting on the GTS in RA II (Moscow, 8-10 September 2003) emphasized importance of introduction of TCP/IP procedures and extrication from expensive leased circuits, and suggested the following strategies:

- Acceleration of TCP/IP migration with a first priority

- Selecting an appropriate network service with a possible framework

- Use of the Internet for a GTS circuit as the very end solution

In line with the strategies, lots of RMTN links have already been upgraded or are planned for their early improvement.

- Status of the improvement of the RMTN  (Refer to Appendix A)

  - Implementation of circuits

According to Resolution 5 at the thirteenth session of Regional Association II (Hong Kong, China, 7-15 December 2004), the following regional circuits are officially included in the RMTN:

- RTH Jeddah – NMC Abu-Dhabi (United Arab Emirates)

- RTH New Delhi – NMC Thimpu (Bhutan)

- RTH Bangkok – RTH New Delhi

- RTH Beijing – RTH New Delhi

and the interregional circuit  RTH Bangkok – NMC Singapore.

Consequently the RMTN configuration plan includes 82 circuits (i.e. 8 MTN, 55 regional, 13 inter-regional and 6 additional circuits).  70 circuits of them are in operation, namely the latest implementation rate is 85 percent.  It is a problem that there are still 12 circuits not in operation.  Especially NMCs Baghdad (ought to have 2 regional circuits), Kabul (3), Thimpu (1) and Phnom Penh (1) are isolated from the GTS.  In spite of difficult situations, efforts to establish the circuits will be continued in cooperation with RTHs concerned.  In fact, NMC Phnom Penh has been practically coordinating establishing a new circuit in cooperation with RTH Bangkok.

Another problem is that quite a few circuits are operating at a low speed.  An appropriate speed more than 9.6kbps at least could be required in consideration of WWW requirements such as dissemination time of observation data within 15 minutes, distribution of processed information of a large volume and handling various data types (e.g. binary, charts and files).   Although improvement in circuit speeds has been progressed in a last few years as shown in Figure 1.  33 percent of all circuits are still required to increase their speed.   In most cases financial conditions, especially lack of recurring cost, prevent improving speeds.

  - Migration to TCP/IP

The migration towards TCP/IP on RMTN circuits has been progressing well.  About 60 percent of all circuits in the Region are operating on pure TCP/IP as of September 2006.  Based on each centre’s report on upgrade plans, it is expected that the achievement rate would be over 70 percent by the end of 2006.

Generally TCP/IP migration is making satisfactory progress.

  - Migration to cost-effective connections

2.3.1  Frame Relay

Migration from leased circuits to Frame Relay circuits has been making steady progress since 2000.   17　Frame Relay circuits are in operation as of September 2006.  There are two types in Frame Relay connection scheme.  One is the NNI (Network-to-Network Interconnection) type which is mutual connection by two network providers.  The other is the seamless connection type by a single provider.   The former is adopted for 7 Regional and Interregional circuits.  The latter is adopted for 7 MTN circuits under the Improved MTN project and 3 related Regional and Interregional circuits.

2.3.2  IP-VPN with MPLS

IP-VPN (Virtual Private Network) with MPLS (Multi Protocol Label Switching) is a fully managed private network different from Internet VPN.  It is secure, flexible, scalable and cost-effective and provides any-to-any connectivity within a VPN group.

Although there is currently no MPLS link in the GTS, it is a promising network service.   According to the latest strategy of the Improved MTN project, most of the MTN and related circuits will migration from Frame Relay to IP-VPN MPLS within a few years.

2.3.3  Internet links

Expansion of the Internet use in recent years brought a possibility of a new type GTS circuit through the Internet.   Currently the number of Internet based circuits is 9.  In addition, there are cases to use the Internet connection for GTS backup.

Introducing VPN techniques such as IPsec is recommended for security reason.  Although the Jeddah-Sana’a circuit is currently a sole Internet VPN link with IPsec in the Region, some centres have been considering to introduce IPsec to their Internet circuits.

2.4.  Satellite broadcasting systems  (Refer to  Appendix B)

Satellite broadcasting systems are used for complements to the GTS, backup sources and cost-effective alternatives to HF radio broadcasts.

- A VSAT-based broadcasting network by China Meteorological Administration has been fully operating since January 1998.  It totally has a 2M broadcasting rate and supports 256 logical channels. The typical channel rate is 64Kbps. It covers China and some neighbouring countries and is integrated into the RMTN as well as METEOSAT-MDD.   CMA-PCVSAT receivers installed in Hanoi, UlaanBaatar Yangon and Pyongyang are used for obtaining GTS data, CMA’s NWP products and CMA’s FY satellite data as complements of the low speed GTS circuits.  The installation in Bangladesh is planned in 2006.

- CMA is developing a new satellite-based broadcasting system, DVB-S system, for replacing the current CMA-PCVSAT system. A pilot system, which includes a hub station and several receiving stations and supports the services of data broadcasting and multimedia program broadcasting, has been put into running since April, 2006. Comparing with the current PCVSAT system, the new system gains the main advantages of higher data rates and lower costs for remote stations due to using standard DVB (Digital Video Broadcasting) technology.

- Russian satellite broadcasting system (TV-Inform-Meteo) had provided fax charts and AN bulletins since 1995.  It was replaced by a new DVB satellite system named “Meteoinform”.  The Meteoinform provides multicast functions for meteorological data based on MITRA (Multi-address Information Transmission) technology.  The broadcasting at high-speed (up to 56 Mbps) is carried out in the C-band through 4 Russian satellites (Expres AM1, Expres AM3, Expres AM11 and Yamal-200) providing the coverage of the whole territory of the Russian Federation and a number of adjacent countries.  In the majority of towns, the subscribers can receive 2 or 3 satellites simultaneously.  More than 100 terminals including terminals in Kazakhstan, Kyrgyz, Tajikistan have already been connected to it. The rates in the channels of various satellites were chosen as required from 64 to 1024 kbps and can be used in the course of operation without changing the H/W and S/W. The programmes over various channels are also different and depend on the users’ requirements in the area of reception.

- RTH New Delhi operates INSAT-MDD which is used for complements to the GTS in NMCs Dhaka, Male and Colombo.

- RTH New Delhi  switched their data serving for users including marine vessels from HF radio broadcasts to a satellite-based DAB (Digital Audio Broadcast) by World Space through Asia Star Satellite in August 2003.  This is a very cost-effective solution.  The approximate cost for distribution of 1 Mbytes through the satellite is US$ 10.  A user receives required data using a commercial radio receiver with a small L band antenna and a PC card adapter, which is manufactured by several companies at an approximate cost of US$150.

- METEOSAT-MDD service has been discontinued as from 14 June 2006.   The MDD data stream itself is now embedded in the EUMETCast dissemination, and the same user-terminal can receive EUMETSAT images as well as MDD data and products.  Oman (C and Ku bands) and  Uzbekistan (Ku) already implemented EUMETCast receivers.

- WAFS (ISCS, SADIS) broadcasting is regularly used for operation in most of RTHs/NMCs.

- Many RTHs already discontinued HF radio broadcasts because of its high recurrent  cost, its obsoleteness and emerging of standard satellite broadcast services.  Although RTHs Bangkok, Jeddah, Tehran and Tokyo are still operating HF broadcast, the day is not far distant when HF broadcasts will disappear in Region II.

- Migration plan to TDCFs

At its thirteenth session, CBS urged Member countries to develop as soon as possible a national migration plan to Table Driven Code Forms (TDCFs), derived from the international plan, with analysis of impacts, costs, solutions, sources of funding (as necessary), national training, technical planning and schedule.

To know current status of migration by Member countries in RA II, a survey was conducted in August 2006.  The result of the survey is reported as Doc.6.2(2).

In addition, some regional templates of BUFR and CREX will be developed for the migration by Members of WMO in RAII.

- WMO Information System

To promote regional contribution to the development of the WMO Information System (WIS), the VPN Pilot Project in Regions II and V has been making steady progress.  Currently the project is entering the advanced phase to evaluate practical usage of VPN techniques.  The outcome was submitted to the third meeting of the Inter-Commission Coordination Group on WIS (ICG-WIS) (Beijing, 5-8 September 2006) and also the CBS Technical Conference on the WIS (Seoul, 6-8 November 2006) preceding CBS-ext.2006.

Appendix A

Appendix B

# Text boxes

Internet

CMA-PCVSAT

Internet

Melbourne

Frame Relay

CIR<8/8K>

Frame Relay

CIR<16/16K>

9.6-26.4K (V.34)

9.6-26.4K (V.34)

64K

1200

Abu-Dhabi

14.4K

Ulaanbaatar

Beijing

100

64K

via Moscow

64K

75

2.4K

64K

Frame Relay

CIR<8/8K>

Figure 6   Growth in GTS circuits through the Internet in RA II

number of circuits

number of circuits

Figure 3   Growth of Frame Relay circuits in RA II

Figure 2   Progress in migration to TCP/IP in RA II

The number

of circuits

16K

32K

48K

768K

Frame Relay

CIR<8/8K>

NI

New Delhi

Thimpu

64K

64K

CMA-PCVSAT

CMA-PCVSAT

CMA-PCVSAT

NNI type by two providers

NMHS

C

NMHS

B

NMHS

A

Figure 4   Frame Relay connection schemes

IMTN-MDCN

Frame Relay

CIR<16/8K>

IMTN-MDCN

Frame Relay

CIR<8/8K>

Seamless connection type by a single provider

### NNI

Frame Relay

Network

##### Y

Frame Relay

Network

##### X

NMHS

B

Telecom. Carrier

Y

NMHS

A

IMTN-MDCN

Frame Relay

CIR<16/16K>

Internet

Telecom. Carrier

X

Frame Relay

CIR<16/16K>

# Frame Relay Network

# by a single provider

14.4-33.6K (V.34)

Figure 5   IP-VPN with MPLS

IMTN-MDCN

Frame Relay

CIR<96/48K>

via Moscow

7.2-28.8K (V.34)

ISDN 128K

Internet

Washington

Internet

64K

64K

64K

Muscat

Internet

Internet

Internet

Jeddah

Internet

IMTN-MDCN

Frame Relay

CIR<48/48K>

Manila

IMTN-MDCN

CIR<16/32K>

IMTN-MDCN
 IR<32/768K>

Frame Relay

CIR<16/16K>

Tokyo

Frame Relay

CIR<32/32K>

NI

Moscow

Hong Kong

200

Sanaa

Tehran

NI         No implementation

Non-IP link

IP link

Internet E-mail transmission

MTN circuit

Regional circuit

Interregional circuit

Additional circuit

Centre in other region

NMC in Region II

RTH in Region II

Singapore

64K

Bishkek

Regional Meteorological Telecommunication Network for Region II (Asia)

Current status as of 13 September 2006

19.2-24K (V.34)

9.6-19.2K (V.34)

19.2-24K(V.34)

NI

NI

Frame Relay

CIR<16/16K>

Washington

Melbourne

Frame Relay

CIR<16/16K>

Frame Relay

CIR<16/16K>

Bangkok

Khabarovsk

Novosibirsk

Tashkent

Kuala Lumpur

Moscow

Algiers

Cairo

Cairo

Offenbach

Offenbach

Melbourne

9.6K

75

100

50

75

1200

75

100

64K

2.4K

200

50

50

50

50

50

64K

64K

7.2-28.8K (V.34)

9.6-26.4K (V.34)

64K

NI

NI

Seoul

NI

NI

NI

NI

Almaty

Dushanbe

64K

Macao

Ashgabad

PyongYang

Phnom Penh

Hanoi

Male

Colombo

Karachi

Kabul

Kathmandu

Yangon

Dhaka

Bahrain

Provider’s PEs and Core Routers based on MPLS have Label Tables and switch IP packets forward according to the Tables.

CE  :  Customer  Edge Router	   VPN : Virtual Private Network

PE  :  Provider Edge Router	   MPLS : Multi Protocol Label Switching

| Destination IP | VPN No. | Output Label | Output port |
| --- | --- | --- | --- |
| . . . | . . . | . . . | . . . |

| Input Label | Input Port | Output Label | Output Port |
| --- | --- | --- | --- |
| . . . | . . . | . . . | . . . |

VPN

group

VPN

group

IP

PE

Core Router

Core Router

Core Router

IP  Label

IP Label

IP

CE

CE

PE

Kuwait

PE

Doha

Closed

# IP network

by a provider

Baghdad

Figure 7   Internet VPN with IPsec

IPsec Product

IP

ESP AH IP

IP

IPsec Product

IPsecVPN products add/remove the ESP for encryption and encapsulation and the AH for authentication to/from an IP packet.

ESP  :  Encapsulation Secure Payload	 AH : Authentication Header

VPN

group

VPN group

ESP AH IP

IPsec Product

Vientiane

Internet

Members equipped with EUMETcast receivers:  Oman (C and Ku bands), Uzbekistan (Ku)

Asia Star broadcast

(DAB)

Meteoinform

(DVB)

Moscow

Members equipped with Meteoinform receivers:  Kazakhstan, Kyrgyz, Tajikistan

INSAT-MDD

(DAB)

Members equipped with INSAT-MDD/VSAT receivers:  Bangladesh, Maldives and Sri Lanka

Members equipped with CMA-PCVSAT receivers:  Democratic People’s Republic of Korea, Mongolia, Myanmar and Vietnam.

EUMETcast

(DVB)

CMA-PCVSAT (Broadcast)

ISBN(Data Collection)

radio broadcast

multipoint system

via satellite

MTSAT DCPs

Fax

Fax

Fax, RTT

Fax, RTT

RTH

Novosibirsk

Tashkent

Tehran

New Delhi

Beijing

Khabarovsk

Tokyo

Jeddah

Bangkok

Multipoint telecommunication systems in Region II

Figure 1   Progress of improvement in circuit speed in RA II  (except for Internet links)

number of circuits