| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Implementation-coordination Team on INFORMATION SYSTEMS & SERVICES geneva, 18 - 22 september 2006 |  | ICT-ISS 2006/Doc. 3.1(1) (15.IX.2006) ____________ ITEM 3.1 ENGLISH only |
| --- | --- | --- |

TCP/IP procedures and applications, including filenaming

File naming convention

(Submitted by the J.-F. Gagnon, co-chair (DCT) of the ET-CTS)

Summary and Purpose of Document CBS-XIII tasked the ET-CTS to finalize the general new file naming convention, in collaboration with the ET-OI. The new file naming convention has been consolidated in coordination with the ET-OI and also with contributions from the IPET-MI, through the follow-up work of an ad-hoc group established by the CBS Expert Team on GTS-WIS Communication Techniques and Structure (ET-CTS) (Tokyo, April 2006).

ACTION PROPOSED

The Implementation Co-ordination Team is invited to review and endorsed the revised section on “General file naming conventions” of the Manual on the GTS, Volume II, Attachment II-15 as given in the Appendix to the document.

Appendix:	Draft amendment to the Manual on the GTS, Volume II, Attachment II-15, “General file naming conventions” section

[The ET-OI agreed with the ET-CTS that the proposed identifier would meet the requirements for file-naming purposes, and it fully endorsed the ET-CTS recommendation.  It noted that the above identifier format may not be adequate as a unique universal identifier, such as for station identifiers, and that another mechanism may need to be developed for that purpose.  The ET-OI was informed that the ET-CTS had established an ad-hoc drafting group for consolidating the proposed text for inclusion in Attachment II-15; it recommended that three ET-IO experts would also join and contribute to the ad-hoc ET-CTS drafting group.]

# General file naming conventions

The following file naming convention should be implemented with a transition period not exceeding 2007.  The implementation date is subject to review by CBS.

The procedure is based on transmission of file pairs, one file being the information file and the other being the associated metadata file. The concept of file pairs allows the communications function to be implemented independently of data management requirements for structure of metadata, yet provides for the carriage of whatever metadata is required. It is not compulsory to always have a .met file, such as when the information file itself is self-specifying or when a single .met file can describe several information files (for example as in the case of same data type for different times).  There is always however a clear relation between the Information File Name and the Metadata File Name, which should only differ from their Extension field and possible wildcards.

File names for new message types (no existing AHL) shall follow the following format.  It should be noted that file names for existing message types (existing AHL) can also follow the following format.

The File Name format is a predetermined combination of fields, delimited by the _ (underscore) character except for the last 2 fields, which are delimited by the . (period) character.

Each field can be of variable length, except for the Date/time stamp field which is predetermined.

The order of the fields is mandatory.

The File Name fields are as follows:

pflag_productidentifier_oflag_originator_yyyyMMddhhmmss[_freeformat].type[.compression]

where the mandatory fields are:

pflag	is a character or combination of characters indicating how to decode the productidentifier field.  At this time, the pflag field has only the following acceptable value:

Table 4.1 Accepted pflag values

| pflag | Meaning |
| --- | --- |
| T | The productidentifier field will be decoded as a standard T1T2A1A2ii data designator (The WMO standard data designators are given in Attachment II-5) |
| A | The productidentifier field will be decoded as a standard Abbreviated Heading, including BBB as appropriate, space characters being discarded, e.g. T1T2A1A2iiCCCCYYGGgg[BBB] |
| W | WMO Product Identifier |
| Z | Originating centre’s local product identifier |

productidentifier  is a variable length field containing information that describes the nature of the data in the file.  The productidentifier field should be decoded according to the pflag.

The WMO Product Identifier to be used with pflag = W shall be decoded as follows:

<location indicator>,<data designator>,<free description>,<International date-time group

>,<BBB modification header>

The WMO Product Identifier is composed of two parts:

the “static part” for description of the product and the "optional part" to define the time stamp and status of the product (correction, amendment).

The WMO Product Identifier is not case sensitive.  These two parts are defined as follows:

Static part: <location indicator>,<data designator>,<free description>

- <location indicator> defines the producer: Country, organization and the production centre; Example: <uk-metoffice-exeter>. Each field shall be separated by “-” symbol.

- <data designator> specifies the type of data with reference to the categories and sub-categories defined in the Common Table C-13 of the Manual on Codes, e.g. <SYNOP>, <TAF>, <MODEL>, <RADAR>, <SATELLITE>, etc.  When the type of data is a composite type, use the sign ”+” for concatenation.

- <free description> is determined by the production centre to characterize the product.

Optional part: [,<International date-time group

>,<BBB modification header>]

- <International date-time group

- > is a YYYYMMDDHHMMSS time stamp of the product, full format without substitution characters (only decimal digits). This field is optional because it can be recovered from the file name field: yyyyMMddhhmmss

- <BBB modification header> is a complementary group with a similar purpose as the current BBB group of AHL

Note: in order to facilitate the identification of each field of the product identifier, the static part, as well as the optional part if used, shall comprise  two symbols “,” separating the fields. Each field shall not contain any symbol “,”. If a field is empty, no character shall be inserted between the relevant field delimiters “_” or “,”.

oflag	is a character or combination of characters indicating how to decode the originator field.  At this time, the oflag field has only the following acceptable value:

Table 4.2 Accepted oflag values

| oflag | Meaning |
| --- | --- |
| C | The originator field will be decoded as a standard CCCC country code |

originator is a variable length field containing information that states where the file originated from.  The originator field should be decoded according to the oflag

yyyyMMddhhmmss is a fixed length date and time stamp field.  The interpretation of this field should be in accordance with the standard rules set for specific data description and types.  Therefore it may have various significance such as date of creation or the file, or date of collection of data. If a particular date and time stamp field is not specified, it should be replaced by a `-` (minus) character.  For example:  ------311500-- represents a stamp that specifies only the day (31st), hours (15) and minutes (00). If there are no rules for a specific data type, this field should represent the date and time of creation of the file by the originator.

Type	is a variable length field that describes the general format type of the file.  Although this information could be considered somewhat redundant to the productidentifier field, it is kept as such for industry accepted standard compatibility.  It should be noted that the delimiter before the type field is a . (period).  This is to help parse the file name for fields, since the freeformat field could make use of further _ (underscore) to delimit subfields.

Table 4.3 Accepted type values

| type | Meaning |
| --- | --- |
| met | The file is a metadata file pair which describes the content and format of the corresponding information file with the same name |
| tif | TIFF file |
| gif | GIF file |
| png | PNG file |
| ps | Postscript file |
| mpg | MPEG file |
| jpg | JPEG file |
| txt | text file |
| htm | HTML file |
| bin | a file containing data encoded in a WMO binary code form such as GRIB or BUFR |
| doc | a Microsoft Word file |
| wpd | a Corel WordPerfect file |

And the non mandatory fields are:

freeformat is a variable length field containing further descriptors as required by a given originator.  This field can be further divided in sub-fields.  Originating countries should strive to make their freeformat descriptions available to others.

compression is a field that specifies if the file uses industry standard compression techniques

Table 4.4 Accepted compression values

| compression | Meaning |
| --- | --- |
| Z | The file has been compressed using the Unix COMPRESS technique |
| zip | The file has been compressed using the PKWare zip technique |
| gz | The file has been compressed using the Unix gzip technique |
| bz2 | The file has been compressed using the Unix bzip2 technique |

Maximum file name length:  Although no maximum length is specified for the entire file name, the mandatory fields shall not exceed 128 characters (including all delimiters) to allow processing by all international systems.

Character set:  The filenames shall be composed of any combination of the standard character set (ITU-T Rec. X.4) with the exceptions noted in Table 4.5.

Table 4.5 Symbols for filenames

| Symbol | Allowed | Meaning |
| --- | --- | --- |
| _ | yes | The underscore symbol is used has a delimiter symbol. To be used only as a delimiter of fields. The underscore is also accepted in the freeformat field, but not in other fields. |
| - | yes | The minus symbol shall be used only as a field delimiter inside the “location indicator” and “free description” fields of the WMO Product Identifier in the productidentifier field. For example, in the case of location indicator: uk-metoffice-exeter. This symbol shall not appear in the "data designator" field. |
| + | yes | The plus symbol shall be used to concatenate several words in a field of the WMO Product Identifier in the productidentifier field. For example, in the “data designator” field: TEMP+MOBIL or CLIMAT+TEMP+SHIP |
| . | yes | The period symbol is used has a delimiter symbol. To be used only before the type and compression fields. |
| / | no | Forward stroke often has special meaning for the full path specification of a filename in some operating systems |
| \ | no | Backward stroke often has special meaning for the full path specification of a filename in some operating systems |
| > | no | Greater than symbol shall not be used since it often represents special file manipulation in some operating systems |
| < | no | Less than symbol shall not be used since it often represents special file manipulation in some operating systems |
| ¦ | no | Vertical bar (pipe) symbol shall not be used since it often represents special file manipulation in some operating systems |
| ? | no | Question mark symbol shall not be used |
| ‘ | no | Single quote shall not be used. |
| “ | no | double quotes shall not be used |
| * | no | The star symbol is often used for wildcard specification in procedures that process filenames. |
| Space | no | The space symbol shall not be used |
| , | yes | The comma symbol shall be used as a field delimiter in the WMO Product Identifier of the productidentifier field. For example, in the static part: <location indicator>,<data designator>,<free description>. The comma symbol can be also used in the freeformat field |
| A-Z a-z 0-9 | yes |  |

The structure of the ‘.met’ file, related to the WMO Metadata standard, is not defined in this guide.

# Examples

# A possible imagery file (Sig Weather Chart) that would have originated from the USA:

T_PGBE07_C_KWBC_20020610180000_D241_SIG_WEATHER_250-600_VT_06Z.tif

# A possible model output file from France:

A_HPWZ89LFPW131200RRA_C_LFPW_20020913160300.bin

# A possible synoptic surface observations file from France:

W_fr-meteofrance-Toulouse,SYNOP,MAIN+HOURS,,RRA_C_LFPW_20060913030000.txt

# A possible model output file from France:

W_ fr-meteofrance-toulouse,GRIB,ARPEGE-75N10N-60W65E_C_LFPW_200610000000.bin

# A possible image from Australia:

Z_IDN60000_C_AMMC_20020617000000.gif

Note that this shows that the date and time stamp is to be interpreted to be 00 hours, 00 minutes and 00 seconds.

# A possible compressed TOVS satellite data file from the United Kingdom:

Z_LWDA_C_EGRR_20020617000000_LWDA16_0000.bin.Z

# A possible image (radar) from Canada:

T_SDCN50_C_CWAO_200204201530--_WKR_ECHOTOP,2-0,100M,AGL,78,N.gif

# A possible single-record GRIB file from Canada:

Z__C_CWAO_2002032812----_CMC_reg_TMP_ISBL_500_ps60km_2002032812_P036.bin

# A possible multiple record batch file from China:

Z_SM_C_BABJ_20020520101502.txt