ETAT DE MISE EN OEUVRE DU CRT D’ALGER

- Introduction.

Les systèmes de commutations automatiques de messages météorologiques (AMS) du Centre Régional de Télécommunications d’Alger (CRT), ont été renouvelés en 2004 (Hard et Soft) par de nouveau systèmes de technologie récente, dotés de toutes les fonctionnalités et protocoles de transmission suivant les recommandations de l’OMM.

L’ Office a également équipé ses centres météorologiques régionaux par des équipements similaires que ceux du CRT d’Alger (reliés au CRT par des liaisons numériques à 64 Kbps TCP/IP) , pour permettre une meilleure circulation de l’information météorologiques et aussi pour servir d’appui au CRT  en cas de problème grave ( panne prolongée, séisme ou autres anomalies).

- Moyens  Mis en Œuvre et Rôle du CRT d’Alger

Le CRT est équipé d’un système de commutation de messages météorologiques doublé, qui fonctionne en mode redondant (HOT/STANDBY) avec 512 Mo de RAM et 72 Go de disque, avec tous les moyens nécessaires à la transmission : périphériques et postes de travail de supervision, de contrôle et des systèmes de  traitement de l’information.

Les équipements  fonctionnent sous le système d’exploitation WINDOWS 2000 Pro et disposent de tous les moyens de sécurité nécessaires.

Le système de commutation automatique assure :

- Echange de données et produits du Centre sur le RPT et SMT avec les CRTs et CMNs associés .

- Collecte et traitement des données en provenance des stations d’observation du  réseau national

- Réception des produits satellites en provenance, de la station satellite  RETIM (visible et infrarouge), de la station satellite SADIS ( produits aéronautiques) et de la station satellite MSG (visibles et MDD).

- Diffusion des données et produits aux centres météorologiques régionaux, aux stations d’observation du réseau, au réseau aéronautique RSFTA et aux différents usagers et utilisateurs de la météorologie.

- Participe au contrôle annuel de fonctionnement de la VMM (AGM) du mois d’Octobre  et les  contrôles spéciaux (SMM) des mois de Janvier- Avril , Juillet et Octobre

- Le système de commutation de messages est doté de toutes les fonctionnalités et protocoles de transmissions :

TCP/IP (ftp, socket), FR, RTC,X25,TGR,

VPN, E-MAIL/Internet) et toute autre type de connectivité.

Le système supporte tout type de données et produits météorologiques de différentes tailles.

- Les Régions météorologiques et stations d’observations du réseau National

Deux (02) régions météorologiques du pays (à l’Est et l’Ouest) sont équipés de systèmes de commutations de messages de même caractéristiques que le CRT d’ALGER et jouent le rôle  d’appui pour la concentration et la diffusion de données des stations d’observations et autres activités d’assistance et de prévision et assurent également le secours du CRT d’Alger. Elles sont reliées au site Central par des liaisons numériques à 64 Kbps TCP/IP et secourues par des liaisons X25 SVC.

Les stations d’observations du réseau National (RBSN et autres) sont toutes équipées de moyens microinformatiques (PCs) pour la transmission de données  et utilisent le support RTC ftp.

- Moyens de réception de données et produits par satellites.

Le  CRT est également  équipé des moyens de réception satellites, qui sont intégrés dans le système de commutations de messages météorologiques et de traitement. Ces moyens sont :

- Une station de réception Satellite SADIS (secouru) : données aéronautiques

- Une Station de réception Satellite (secouru) RETIM : données et produits météorologiques.

- Une station de réception satellite MSG : tous les canaux infra rouge, visibles et vapeurs d’eau + MDD.

Dans le même cadre et pour le renforcement des capacités en secours, il est prévu durant l’année 2006 d’équiper les deux régions météorologiques de ces moyens de réception par satellites.

- Site Internet.

Le site Internet www.meteo.dz du CRT d’Alger est connecté par une liaison numérique haut débit à 2 Mb/s.

# Etat actuel des circuits reliés au RTH Alger et Plan de développement.

| Correspondants | Statut | Type de Circuit | Vitesse de transmission | Protocole | Plan de développement |
| --- | --- | --- | --- | --- | --- |
| Toulouse | RTH | Liaison Numérique | 64 Kbps | TCP/IP ftp | Augmenter le débit à partir de 2007. |
| Le Caire | RTH | Liaison Numérique | 64 Kbps | TCP/IP ftp |  |
| Djeddah | RTH | Internet | -- | ftp | En cours d’installation LS Numérique 64 K, mise en SVC prévue fin 2006 |
| Tunis | NMC | Liaison analogique | 2400 bps | X25 | Remplacement par LS IP à 9.6 Kbps |
| Casablanca | NMC | Liaison Télégraphique | 50 bauds | -- | En projet pour LS numérique à 64 K, 2007 |
| Madrid | NMC | Liaison Analogique | 2400 bps | IP |  |
| Dakar | RTH | Liaisons télégraphiques, à l’arrêt, supports de transmission en dérangement. | En projet de remplacement par des liaisons Vsat à 9.6 Kbps |
| Niamey | RTH |  |  |

Note : Le CRT d’Alger n’est pas connecté au réseau RMDCN, du fait que la liaison avec Toulouse est très fiable et les coûts de location sont beaucoup plus avantageux. Néanmoins le CRT d’Alger a inscrit dans son plan, son adhésion au Réseau RMDCN à partir de 2007.

- Résultats du Contrôle Annuel Global « AGM »

Le CRT d’Alger a participé au contrôle  annuel  global (AGM) de la VMM, qui s’est effectué du 1 au 15 Octobre 2005.

Les commentaires de l’analyse  de ce contrôle se résument comme suit :

- Pour la zone de responsabilité  d’Alger.

Stations RBSN

a)  SYNOP : Algérie : 28 ; Maroc 17 ; Tunisie 10 et  Libye :21

b) TEMP :      Algérie : 04 Maroc : 02 Tunisie : 02   et Libye : ?

Réseau Algérie :

Seul un réseau Surface ( 6/10/2005 à 12 h) sur les 60 prévus n’a pas été pris en compte pour certaines stations RBSN, pour cause technique.

Deux stations RBSN n’ont pas produits :

60690----à l’arrêt.

60506 remplacée par 60507 (voir Volume C1 actualisé).

Pour ce qui concerne les TEMP- CLIMAT ET CLIMAT TEMP : pas de commentaire

Réseau Maroc :

Entre 38 et 60 message selon le fonctionnement des stations d’observations de ce CMN.

Pour ce qui concerne les TEMP- CLIMAT ET CLIMAT TEMP   : pas de commentaire

Réseau Tunisie :

60 messages d’Observation de ce CMN. Correct.

Pour ce qui concerne les TEMP- CLIMAT ET CLIMAT TEMP  : pas de commentaire

Le réseau du CMN de Libye n’est pas pris en charge par le CRT d’Alger, cause résiliation de la liaison par Tripoli.

2.    Un certain nombre de messages  des CMNs du GTS, non reçus au CRT, pour différentes causes : n’arrivent  pas ou ne sont pas programmés dans notre table de routage (vérifications en cours pour résoudre ces anomalies).

##### STATUS OF IMPLEMENTATION - RTH ALGIERS

1.¶	Introduction.¶

The automatic switching systems of meteorologicals messages (AMSS) of RTH  Algiers , were renewed in 2004 (Hardware and Software) by powerful systems with recent technology, equipped with all the functionalities and transmission protocols according to the OMM recommendations .

¶

¶The Office also equipped its regional meteorologicals centers by similar equipment that those of  the CRT Algiers (connected by digital links at  64 Kbps TCP/IP), to allow a better meteorological information flow and also to secure the RTH Algiers in the event of serious problem (prolonged breakdown, seism or other anomalies).¶

2.¶	Means Implemented and Role of the RTH  Algiers. ¶

¶The RTH Algiers is equipped with a Twin Automatic Message switching system, which functions in redundant mode (HOT/STANDBY) with 512 Mo of RAM and 72 Go of disc, with all the means necessary to the transmission that is (i.e): ¶peripherals and supervision/control  workstation  and systems of data processing.¶The equipment functions under the operating system WINDOWS 2000 Pro and has all the necessary means for safety  and protection.

¶

¶The switching system ensures:¶

- Data and products exchange  of the Center on the RPT and SMT with associated RTHs and NMCs.¶

- Collect and process data coming from the observation stations of the national network ¶

- Reception of the satellite products  from receiving station RETIM  (visible and infra-red), and SADIS  ( aeronautical products)) and  MSG (visible and MDD).¶

- Diffusion of the data and products to the regional weather centers, the observation stations of the network, aeronautical network RSFTA and the various users  of meteorology.¶

- Take part in the annual control of operation of the VMM (AGM) of October and special controls (SMM) of January , April , July and October. ¶

The message switching system  is equipped with all the functionalities and protocols of transmissions:

¶

TCP/IP (ftp, socket), FR, RTC, X25, TGR, ¶

VPN, E-MAIL/Internet) and any other type of connectivity.

¶

The system supports any type of data and weather products of various sizes.¶

3.¶	Meteorologicals regions  and observation stations of the National network

¶

Two (02) meteorological regional centers of the country (in the East and the West) are equipped with switching systems  in the same way and characteristic than the RTH of Algiers and play the role of support for the concentration and the data dissemination of the observation stations and other activities of assistance and forecast and also ensure the emergency secure of the RTH.¶They are connected to the Central site by digital links at  64 Kbps TCP/IP and are secured by connections X25 SVC.

¶

¶The observation stations of the National network (RBSN and others) are all equipped with PCs  for the data transmission using support RTC ftp.¶

4.¶	Means of reception of data and products by satellites.¶

The RTH Algiers is also equipped with the satellite means of reception, which are integrated in the AMSS.¶These means are:¶

- A Satellite receiving station SADIS (doubled) for ¶aeronautical data ¶

- A Satellite receiving station RETIM (doubled) for ¶weather data and products.¶

- A satellite receiving station MSG:for ¶channels will infra red, visible and water vapor + MDD.¶

¶Within the same framework and for the reinforcement of the capacities , it is envisaged during this year to equip the two meteorologicals centers with these means of reception by satellites.¶

5.¶	Internet site.¶

The web site www.meteo.dz  of the RTH Algiers is connected by a digital link high flow at 2 Mb/s.¶

# 6.¶   Current State of the circuits connected to the RTH Algiers and Plan of development

| Correspondents | ¶Statut | ¶Type of Circuit | ¶Speed transmission | ¶Protocol | ¶Plan of development ¶ |
| --- | --- | --- | --- | --- | --- |
| Toulouse | ¶RTH | ¶ Digital link | ¶64 Kbps | ¶TCP/IP ftp | ¶Increase the speed, since 2007. ¶ |
| Cairo | ¶RTH | ¶ Digital link | ¶64 Kbps | ¶TCP/IP ftp ¶ |  |
| Djeddah | ¶RTH | ¶Internet | ¶-- | ¶ftp | ¶ digital link 64 kbps, to be installed by the end 2006 ¶ |
| Tunis | ¶NMC | ¶Analog link | ¶2400 bps | ¶X25 | ¶Replacement by LS IP to 9.6 Kbps ¶ |
| Casablanca | ¶NMC | ¶Telegraphic link | ¶50 bauds | ¶-- | ¶In project of Replacement by a numerical LS with 64 Kbps, 2007 ¶ |
| Madrid | ¶NMC | Analog link | ¶2400 bps | ¶IP ¶ |  |
| Dakar | ¶RTH | ¶ Telegraphic link, with the stop supports of transmission in disturbance | ¶In project of replacement by Vsat connections to 9.6 Kbps ¶ |
| Niamey | ¶RTH ¶ |  |  |

NOTE:  The RTH  Algiers is not connected to network RMDCN, owing to the fact that the actual connection with Toulouse is highly reliable and its costs of hiring are much more advantageous.  ¶Nevertheless the RTH Algiers  planned its connection with Network RMDCN from 2007.¶

7.¶	Results of Annual global Monotoring "AGM" ¶

The RTH Algiers took part in the annual  control (AGM) of the VMM, which was carried out from the 1st to 15 of October , 2005.¶

¶The comments of the analysis of this control are summarized as follows:¶

1.¶	For the zone of responsibility for the RTH Algiers.¶

Stations RBSN

¶a) SYNOP:    ¶Algeria:¶28;¶Morocco 17;¶Tunisia 10 and Libya:21

¶b) TEMP:¶       Algeria:¶04 Morocco:¶02 Tunisia:¶02 and Libya:¶?¶

Algeria network :¶

¶Only a network Surface (6/10/2005 to 12 H) out of the 60 envisaged was not taken into account for some stations RBSN, due to technical cause.¶

¶Two stations RBSN did not produce:

¶60690- stopped.¶

¶60506 replaced by 60507 (see updated C1 Volume).

¶

¶Concerning the TEMP CLIMATE AND CLIMATE TEMP: ¶no comments. ¶

Morocco network:¶

¶Between 38 and 60 message according to the operation of the observation stations of this CMN.¶

¶Concerning the TEMP CLIMATE AND CLIMATE TEMP:¶  no comments ¶

¶Tunisia network:¶

¶60 messages of Observation of this Correct CMN. no comments. ¶

¶

¶Concerning the TEMP CLIMATE AND CLIMATE TEMP:¶. no comments ¶

¶The network of the CMN  Tripoli (Libya) is not dealt with  the RTH  Algiers, due to cancellation of the connection by Tripoli.¶

¶2.  Some messages of NMCs in the word, not received in  RTH Algiers, for various causes: do¶ not arrive or are not programmed in our table of routing (checks in progress to solve these anomalies)¶ .¶