| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Joint implementation-coordination meeting on the GTS-WIS MTN and meeting of the CBS Expert Team on GTS-WIS operations and implementation Geneva, 16-19 May 2006 |  | ISS/ICM-MTN & ET-OI 2006/Doc.4.7, CORR. (I.V.2006) Agenda Item 4 ENGLISH only |
| --- | --- | --- |

GTS operational procedures at RTH centres and their associated NMCs

(Submitted by ET-OI Co-chairs Kelvin Wong and Leonid Bezruk)

# Summary and Purpose of the Document

This document presents the results of the survey of GTS operational procedures at RTH centres and their associated NMCs

##### ACTION PROPOSED

The meeting is invited to consider the results of the survey of GTS operational procedures at RTH centres and their associated NMCs and discuss the recommendations for implementation as proposed in paragraphs 5, 6, 7 and 9.

Appendices: 	A.	Extracts from the Manual on the Global Telecommunication System, WMO Publication No. 386, Volume I, Part II Operational Procedures for the Global Telecommunication System, paragraph 2.7

- Questionnaire distributed in the survey of RTH centres and their associated NMCs

- RTHs and NMCs surveyed and responses received

- Summary results of the survey

Status of GTS operational procedures at RTH and their associated NMCs

Background

1.	A survey was conducted in August 2004 in preparation for the meeting of CBS Implementation Co-ordination Team on ISS in Sep/Oct 2004.  The Final Report of the meeting is available at the following URL:

http://www.wmo.int/web/www/TEM/ICT-ISS2004/ICT-ISS2004-report.doc

The report took considerations of the ability of most RTH centres at the time and their plans to upgrade their message switching systems by the year 2007 to handle binary messages up the maximum of 500K octets and accordingly proposed to amend the Manual on the GTS, Volume I, Part II paragraph 2.7.1.  CBS-XIII in 2005 recommended the proposal and the change was implemented.  The amended paragraph 2.7.1 published in the Manual on the GTS is given in Appendix A.

2.	The Co-chairs of ET-OI conducted another survey in April 2006 to assess the status of RTH centres and their associated NMCs to handle binary messages up the maximum of 500K octets, the extent of message segmentation practised at RTH centres and the preferred methods of conversion or delivery mechanisms noting that bulletins shall no longer be segmented for transmission on the GTS on or after 7 November 2007.  A copy of the questionnaire distributed in the survey is given in Appendix B.

Results of the survey

3.	25 RTH centres were requested to complete the questionnaire for their centres and their associated NMCs in their areas of responsibility.  17 RTH centres responded as of 15 April 2006 with varying degrees of success in contacting NMC in their region to complete the questionnaire.  In some cases part of the questionnaire can be assessed based on the returns in the survey conducted in August 2004. The list of the RTH centres surveyed is given in Appendix C and a summary of the results is given in Appendix D.

Alphanumeric bulletins distributed on GTS in segments

4.	The responses to Question 4 to identify alphanumeric and binary bulletins that still require segmentation, i.e. bulletins longer than 15K octets were rather incomplete.  In order to examine the extent of segmentation being used at RTH centres the complete message store archived at RTH Melbourne over a period of time was searched for bulletins which have been segmented for distribution on the GTS, i.e. BBB indicator in the abbreviated header of the bulletins starts with ‘P’.  The bulletins found to be transmitted in segments are given in Table A.

Table A

| TTAAii | CCCC | Data Type |
| --- | --- | --- |
| CNCN01 | CWAO | CLIMAT |
| CSCN13 | CWAO | CLIMAT |
| CSCN18 | CWAO | CLIMAT |
| CSOC01 | AMMC | CLIMAT |
| CUJP01 | RJTA | CLIMAT TEMP |
| CUOC01 | AMMC | CLIMAT |
| FAZA50 | FAPR | ARFOR |
| FCJP30 | RJTD | TAF |
| FPAU02 | AMMC | PUBLIC FORECAST |
| FTAS31 | VABB | TAF |
| FTJP30 | RJTD | TAF |
| FTJP31 | RJTD | TAF |
| FTJP32 | RJTD | TAF |
| SAJP51 | RJTD | METAR |
| SIPH20 | RPMM | SYNOP |
| SMMX01 | MABA | SYNOP |
| SMUK01 | EGRR | SYNOP |
| SMVB11 | RJTD | SYNOP |
| SNCN19 | CWAO | SYNOP |
| SOFX01 | RJTD | BATHY |
| SOVD02 | CWOW | SHIP |
| SOVX01 | RJTD | SHIP |
| SOVX02 | RJTD | SHIP |
| SSVX04 | CWEG | BUOY |
| TWNA01 | KNES | SATOB |
| TWNA03 | KNES | SATOB |
| TWNA04 | KNES | SATOB |
| TWNA06 | KNES | SATOB |
| TWNA07 | KNES | SATOB |
| TWNA09 | KNES | SATOB |
| TWSA01 | KNES | SATOB |
| TWSA03 | KNES | SATOB |
| TWSA04 | KNES | SATOB |
| TWSA06 | KNES | SATOB |
| TWSA07 | KNES | SATOB |
| TWSA09 | KNES | SATOB |
| UDAS01 | RJTD | AMDAR |
| UEJP01 | RJTD | TEMP |
| UEPA01 | RJTD | TEMP |
| UKJP01 | RJTD | TEMP |
| UKPA01 | RJTD | TEMP |
| ULJP01 | RJTD | TEMP |
| USJP01 | RJTD | TEMP |
| USPA01 | RJTD | TEMP |

5.	Only the AMDAR bulletins by JMA (RJTD) and the SATOB bulletins by NESDIS (KNES)) are found to be segmenting their alphanumeric bulletins when they approach the limit of 15K octets.  Korea also reported some national bulletins including the hourly radar precipitation data VEKO40 (RKPM, RKPP, RKNS) and AWS observation data VWKO41 RKSL being segmented.  The rest of the bulletins especially the OPMET bulletins (FA, FC, FT, SA) are segmented well below the limit of 15K octets.  The reasons are likely to be the limit of 1800 characters permitted for messages transmitted on AFTN and the general practice in RTH centres to avoid long bulletins being truncated during transmission.  As meteorological bulletins shall no longer be segmented for transmission on the GTS after 7 November 2007 RTH centres are recommended to split up the long message into parts using RRA, RRB, … as the BBB indicators in the abbreviated header of the bulletins if the partitions do not require re-construction in their original sequence at the destination where the bulletin partitions are received.  Alternatively other mechanisms such as FTP can be used to distribute the long message if the bulletin partitions are likely to be more than 20 to 24 parts as the maximum number of partitions using RRA, RRB, …., RRX is 24 before the same BBB indicator repeats again.

6.	The use RRA, RRB, … to partition bulletins is only one of the options and it may not be the appropriate method as it is using the retarded indicator not in accordance with its intended purpose.  Reference should be made to the instructions for the use of the indicator BBB in Attachment II-12 in the Manual on the GTS.  The meeting is invited to consider other options, e.g. re-defining ‘P’ for partition and use PPA, PPB, PPC, …., PPZ for partitions which do not require re-construction at the destination and the total number of parts is not expected to be more than 24.  Bulletins which require re-construction in exactly the intended sequence should consider other methods of delivery or seek bilateral arrangements with the destination centres to continue using the existing segmentation BBB indictors PAA, PAB, …, PZx where xx = Zx is the last bulletin containing the last segment.

7.	The OPMET bulletins partitioned in two or more parts and transmitted on AFTN using the same abbreviated header without a BBB indicator and eventually returning to GTS is also a potential problem.  It is possible in some centres that the partitioned bulletins will overwrite the original bulletin transmitted earlier on GTS with no segmentation.  The tsunami bulletins issued by PTWC used to have a full bulletin distributed on GTS and followed by part 1 of 2 parts and part 2 of 2 parts partitioned bulletins without using the BBB indicator.  It is important that partitioned bulletins transmitted on AFTN should also use the RRA, RRB, … or PPA, PPB as the BBB indicators in the abbreviated header of the bulletins to avoid returning AFTN bulletins causing potential problems in GTS centres.

Binary bulletins

8.	The survey indicates that there are no binary bulletins being segmented for transmission on GTS.  Bilateral agreements normally exist between GTS centres where both ends are capable of transmitting and receiving binary bulletins e.g. T4 charts more than 15K octets.  The increase in the maximum length from 15K to 500K octets after 7 November 2007 is not expected to impact on existing arrangements among RTH centres that are already transmitting, switching and receiving bulletins more than the current limit of 15K octets imposed on GTS.

Use of International Alphabet No. 5 (8 bits)

9.	Only two RTH centres indicated that they are not able to handle the full character sets of the International Alphabet No. 5 (8 bits); in particular the more flexible use of upper and lower case characters in meteorological messages.  The general consensus obtained in the survey conducted in August 2004 and also this time is that as far as message switching is concerned there is no need to limit the use of IA5.  However there are still concerns in the use of mixed character sets in OPMET data including METAR, SPECI, AIREP, TAF, SIGMET, Tropical Cyclone and Volcanic Ash Advisories.  RTH centres connected to AFTN would have performed an internal translation of lower case to upper case anyway.  It is recommended RTH centres who are not able to handle the full character sets of IA5 proceed to upgrade their systems as soon as possible.  The use of upper and lower case characters in IA5 should be allowed in meteorological messages with the second half of the alphabet (first bit set) reserved for national use.

Appendix A

WMO Publication No. 386
Manual on the Global Telecommunication System

Part II Operational Procedures for the Global Telecommunication System

http://www.wmo.ch/web/www/ois/Operational_Information/WMO386/ManOnGTS.html

2.7 Length of meteorological messages

2.7.1 The length of meteorological bulletins shall be determined according to the following:

2.7.1.1 Prior to 7 November 2007,

- Any meteorological bulletin not segmented for transmission on the GTS should not exceed 15 000 octets;

- Any meteorological bulletin segmented into a series of meteorological bulletins for transmission on the GTS, should not exceed 250 000 octets in its original form or when reassembled.

2.7.1.2 On or after 7 November 2007,

(a) Meteorological bulletins for alphanumeric data representation transmitted on the GTS should not exceed 15 000 octets;

(b) The limit for meteorological bulletins for binary data representation or pictorial form shall be increased from 15 000 to 500 000 octets;

- Meteorological bulletins shall no longer be segmented for transmission on the GTS.

NOTE: Meteorological information may be exchanged using the file transfer technique described in Attachment II-15, particularly when the information exceeds 250 000 octets.

Appendix B

| RTH/NMC |  |
| --- | --- |

| Contact person on RTH/NMC matters |
| --- |
| Title: | Surname: | First name: |
| Tel: | Fax: | E-mail: |

| Item | GTS operational procedures at RTH/NMC |
| --- | --- |
| 1 | What is the current maximum length of bulletins that can be handled at your RTH/NMC. RTH centres please list all the NMCs associated with your centre and the maximum length of bulletins that each NMC can handle. |
| 2 | List all the RTH centres and associated NMCs receiving binary bulletins (T1= H, I, J, O, P, Q and Y) from your centre. |
| 3 | Enabling date to handle binary bulletins from its current limit of 15K to 500K octets for each RTH and NMC. |
| 4 | Identify alphanumeric and binary bulletins that still require segmentation, i.e. bulletins longer than 15K octets. |
| 5 | Date planned to convert segmented alphanumeric bulletins longer than 15K for delivery on GTS and preferred methods of conversion or delivery mechanisms noting that bulletins shall no longer be segmented for transmission on the GTS on or after 7 November 2007. |
| 6 | RTH/NMC plans to produce binary bulletins longer than 15K octets after 7 November 2007 when the limit increases from 15 K to 500K octets. |
| 7 | Any possibility in your RTH/NMC of using International Alphabet No. 5 (8 bits) in order to enable more flexible use of text with upper and lower case characters in meteorological messages | YES | NO |
| 8 | If the answer to Question 7 is ‘NO’ please indicate your plans to implement this feature and the expected date. |

Appendix C – RTHs and NMCs surveyed and responses received

| Survey on GTS operational procedures at RTH centres 26 April 2006 |
| --- |
| RTH | CCCC | Country | Name | E-mail | Bounced | Replied |
| Algiers | DAMM | Algeria | M. Adimi | m.adimi@meteo.dz |  | 9 May |
| Buenos Aires | SABM | Argentina | J.M. Afonso | afonso@meteofa.mil.ar |  |  |
| Brasilia | SBBR | Brazil | J.Mauro de Rezende | jmauro@inmet.gov.br |  | 8 May |
| Sofia | LZSO | Bulgaria | Mariana Grueva | mariana.grueva@meteo.bg |  | 11-May |
| Beijing | BABJ | China | Peiliang Shi | shipl@cma.gov.cn |  | 9 May |
|  |  |  | Xiang LI | lixiang@cma.gov.cn |  | 9 May |
| Prague | OKPR | Czech | Ladislav Keller | keller@chmi.cz |  | 9 May |
| Cairo | HECA | Egypt | Walid Gomaa | walid.gomaa@ema.gov.eg |  |  |
| Toulouse | LFPW | France | Madeleine Ceron | madeleine.ceron@meteo.fr |  | 10 May |
|  |  |  | Jacques Anquetil | jacques.anquetil@meteo.fr |  | 10 May |
| Offenbach | EDZW | Germany | Bernd Richter | Bernd.Richter@dwd.de |  |  |
|  |  | Germany | Wilfried Ruiner | Wilfried.Ruiner@dwd.de |  |  |
| New Delhi | DEMS | India | K. Pangasa | pangasank@imdmail.gov.in |  | 9 May |
|  |  |  | Mahesh Rastogi | rastogi@imdmail.gov.in |  | 9 May |
| Tokyo | RJTD | Japan | Takahiro Saito | t_saito@met.kishou.go.jp |  | 12 May |
|  | VHHH | Hong Kong | Wai-man Ma | wmma@hko.gov.hk |  | 12 May |
|  | VMMC | Macao | Koc Io Chan | kichan@smg.gov.mo |  | 12 May |
|  | RSKL | Korea | Myoung-Hee Lee | mhleekr@kma.go.kr |  | 12 May |
| Nairobi | HKNC | Kenya | G.M. Kibiru | kibiru@meteo.go.ke |  | 10 May |
| Wellington | NZKL | New Zealand | Kevin Alder | kevin.alder@metservice.com |  | 9 May |
| Moscow | RUMS | Russian Federation | Leonid Bezruk | bez@mecom.ru |  | 12 May |
|  | RUHM | Khabarovsk | Anatoly Nagorsky | nag@dvugms.kht.ru |  | 12 May |
|  | RUNW | Novosibirsk | Alexandr Karpenko | Karpenko@meteo.nso.ru |  | 12 May |
|  | UTTW | Tashkent | Nina Yakovleva | rts@meteo.uz |  | 12 May |
| Jeddah | OEJD | Saudi Arabia | Mohammed Ibrahim Al-Shareef | al-shareef@pme.gov.sa |  |  |
|  |  |  | Faiq Mutawal | faiq@me.gov.sa |  | 13 May |
| Dakar | GOOY | Senegal | M. Sonko | meteonat@telecom-plus.sn | 29 April |  |
| Exeter | EGRR | United Kingdom | Chris Little | chris.little@metoffice.gov.uk |  | 10 May |
| Washington | KWBC | USA | Daniel Starosta | daniel.starosta@noaa.gov |  |  |
|  |  | USA | Fred Branski | fred.branski@noaa.gov |  |  |
| Melbourne | AMMC | Australia | Kelvin Wong | K.Wong@bom.gov.au |  | 10 May |
|  | WSSS | Singapore | Guat Mui CHUA | CHUA_Guat_Mui@nea.gov.sg |  | 10 May |
|  | WMKK | Malaysia | Jailan Simon | jailan@kjc.gov.my |  |  |
|  | NFFN | Fiji | Leonard Bale | Leonard.Bale@met.gov.fj |  | 12 May |
|  | WIIX | Indonesia | Endang | endang@bmg.go.id |  |  |
| Norrkoping | ESWI | Seweden | Gunilla Mild | Gunilla.Mild@smhi.se |  | 10 May |
|  | EEMH | Estonia | Margarita Gorohhovastskaja | margarita.gorohhovatskaja@emhi.ee |  | 10 May |
|  | ENMI | Norway | John F. Syer | john.syer@met.no |  | 10 May |
| Vienna | LOWM | Austria | Michael Pichler | michael.pichler@austrocontrol.at |  | 12 May |
| Pretoria | FAPR | South Africa | Christa Ferreira | christa.ferreira@weathersa.co.za |  | 12 May |
| Rome | LIIB | Italy |  | tarantino@meteoam.it |  |  |
| Maracay | SVMR | Venezuela |  | semetfav@telcel.net.ve | 27 April |  |
| Bangkok | VTBB | Thailand |  | Brikshavana@tmdnet.motc.go.th | 29 April |  |

Appendix D – Summary results of the survey

| RTH/NMC | Max Length (K) | Planned | Segmented Bulletins | Upper/Lower Case | Remarks |
| --- | --- | --- | --- | --- | --- |
|  | Alpha | Binary | Binary > 15K | Bulls > 15K | Date Converting |  |  |
| Algiers | > 500 | > 500 | Enabled | Not producing | - | YES | Casablanca does not support 500K |
| Buenos Aires | 65/1000 | Dec 2005 |  |  |  |  | No response but responded in 2004 |
| Brasilia | Unlimited | Unlimited | Enabled | Not producing | - | YES |  |
| Sofia | 15 | Unlimited | Enabled | Not producing | - | YES |  |
| Belgrade | 300 | 300 | End 2006* | Not producing | - | YES | 500K after system upgrade end of 2006 |
| Bucharest | 500 | 500 | - | Not producing | - | YES |  |
| Damascus | - | - | - | Not producing | - | YES | No GTS, no MSS, only RETIM 2000 |
| Skopje | Unlimited* | Unlimited* | - | Not producing | - | YES | No MSS, AFD only |
| Tirana | Unlimited* | Unlimited* | - | Not producing | - | YES | No MSS, AFD only |
| Beijing | 15 | 15 | Jan 2007 * | Sat BUFR | Switch as files | YES | * > 15K on bilateral agreement now |
| Pyongyang |  |  |  |  |  |  | No response |
| Hanoi | 15 | 15 | 2005-2006 |  |  |  | No response but Japan responded in 2004 |
| Prague | 50 | 900* | Any time | Not producing | - | YES | *System configuration changed as required |
| Warsaw | 15 | 250 | No response | No response | No response | YES |  |
| Cairo | > 500 | > 500 |  |  |  |  | No response but Jeddah responded in 2004 |
| Toulouse | 15 | 15 | End 2006* | Not producing | Switched w/o processing | YES | * > 15K on bilateral agreement from Madrid |
| Offenbach |  |  |  |  |  |  | No response in 2004 and 2006 |
| New Delhi | Unlimited | Unlimited | Jun 2007 | Not producing | Jun 2007 | NO | Max length at NMCs 3800 octets |
| Tokyo | 500 | 500 | Enabled | Some TEMP,METAR, and TAF | Under consideration | YES |  |
| Hong Kong | 500 | 500 | 7 Nov 2007 | Not producing | - | YES |  |
| Macao | Unlimited | - | - | Not producing | Not producing | YES |  |
| Korea | 30 | 30* | 1 Jan 2007 | Some national data, see para.5 | 1 Jan 2007 | YES | *Fax up to 250K |
| Nairobi | 15 | 15 | Jul 2006 | Monitoring files | Send by FTP | YES | New MSS installed by Jul 2006 |
| Dar Es Salaam | 15 | - | - | - | - | YES | Tanzania |
| St Dennis | 15 | - | - | - | - | YES | La Reunion |
| Entebbe | 15 | - | - | - | - | YES | Uganda |
| Bujumbura | 3800 octets | - | - | - | - | YES | Burundi |
| Kigali | 3800 octets | - | - | - | - | YES | Rwanda |
| Addis Ababa | 200 groups | - | - | - | - | YES | Ethiopia |
| Mogadishu | 200 groups | - | - | - | - | YES | Somalia |
| Asmara | 200 groups | - | - | - | - | YES | Eritrea |
| Wellington | 15 | 15 | Enabled | Not producing | - | YES | Associated NMCs do not operate MSS |
| Moscow | 15 | 15* | During 2007** | Not producing | - | YES | *15K-500K by ftp only ** After MSS upgrade |
| Yerevan | 15 | 15 | No response | Not producing | - | YES |  |
| Baku | 15 | 15 | No response | Not producing | - | YES |  |
| Minsk | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Tbilisi | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Kishinev | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Kiev | 15 | 15 | After 2007 | Not producing | - | YES |  |
| Khabarovsk | 15 | 15 | During 2007* | Not producing | - | YES | *After MSS upgrade during 2007 |
| Novosibirsk | 15 | 15 | During 2007* | Not producing | - | YES | *After MSS upgrade during 2007 |
| Ulaanbaatar | 15-500 | 15-500 | Enabled | Not producing | - | YES |  |
| Tashkent | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Almaty | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Bishkek | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Dushanbe | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Ashgabad | 15 | 15 | Nov 2007 | Not producing | - | YES |  |
| Jeddah | 1000 | 1000 | 7 Nov 2007 | Not producing | - | YES |  |
| Doha | 15 | 15 | 7 Nov 2007 | Not producing | - | YES |  |
| Kuwait | 15 | 15 | 7 Nov 2007 | Not producing | - | YES |  |
| Bahrain | 15 | 15 | 7 Nov 2007 | Not producing | - | YES |  |
| Emirates | 15 | 15 | 7 Nov 2007 | Not producing | - | YES |  |
| Sanaa | 15 | 15 | 7 Nov 2007 | Not producing | - | YES |  |
| Dakar |  |  |  |  |  |  | No response in 2004 and 2006 |
| Exeter | 1500 | 1500 | Enabled | Not producing | - | YES | T4 charts > 15K switched w/o segmentation |
| Washington |  |  |  |  |  |  | No response in 2004 and 2006 |
| Norrkoping | 250 | 250 | Planned* | Not producing | - | YES | * > 15K on bilateral agreement to Offenbach |
| Tallinn Estonia | 250 | - | Not planned* | Not producing | - | YES | * Technically possible |
| Oslo Norway | Unlimited | Unlimited | Enabled | Not producing | - | YES |  |
| Melbourne | 15 | 500* | Enabled | See Table A | Discussion required | YES | *Not switching if > 15K, bilateral only |
| Singapore | 250 | 250 | Nov 2007 | Not producing | - | YES |  |
| Nadi | 15 | 15 | Upgrade 2007* | Not producing | - | YES | *Subject to upgrade in 2007 |
| Pretoria | Unlimited* | Unlimited* | Enabled | Not producing | - | YES | *Except for gtssoc and ftp (99 MB) |
| Vienna | 600 | 600 | Enabled | Not producing | - | NO* | *Subject to s/w upgrade in 2007 |
| Rome |  | > 500 | Mid 2005 |  |  |  | No response but responded in 2004 |
| Maracay |  |  |  |  |  |  | No response in 2004 and 2006 |
| Bangkok |  | 150 | Upgrade in 2005-2006 |  |  |  | No response but Japan responded in 2004 |