| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on Enhanced Utilization of Data Communication Systems EXPERT TEAM ON THE IMPROVED MAIN TELECOMMUNICATIONS NETWORK AND GTS Beijing, China, 10-14 May 2004 |  | ISS/ET-IMTN 2004/Doc. 2(4) (30.IV.2004) ____________ ITEM 2 ENGLISH only |
| --- | --- | --- |

# Status of Implementation of MTN at RTH Beijing

(Submitted by Peiliang SHI, China)

1. Current status of RTH Beijing GTS circuits

| Circuit | Protocol | Speed | Exchanged data type |
| --- | --- | --- | --- |
| Beijing-Offenbach | TCP/IP (FTP) | FR CIR:48kbps Port: 128Kbps (Beijing side) | Message (A/N,binary,fax) |
| Beijing-Tokyo | TCP/IP (TCP Sockets) | FR CIR:48kbps Port: 128Kbps (Beijing side) | Message (A/N,binary,fax) |
| Beijing-Seoul | TCP/IP (TCP Sockets) | FR CIR:32kbps Port: 128Kbps (Beijing side) | Message (A/N,binary,fax) |
| Beijing-Moscow | X.25 PVC | 9.6Kbps | Message (A/N,binary,fax) |
| Beijing-Bangkok | X.25 PVC | 9.6Kbps | Message (A/N,binary) |
| Beijing-New Delhi | X.25 PVC | 9.6Kbps | Message (A/N,binary) |
| Beijing-Pyongyang | asynchronous | 75 Baud | Message (A/N) |
| Beijing-Ulan Bator | asynchronous | 75 Baud | Message (A/N) |
| Beijing-Hanoi | asynchronous | 75 Baud | Message (A/N) |

2. Daily Traffic on the GTS links at RTH Beijing

3. Satellite-based telecommunication services

Currently, the PCVSAT receiving systems which are remote station of CMA’s VSAT-based broadcasting network have been installed in D.P.R. Korea, Mongolia and Vietnam. Through the receiving systems, they can receive diversified data and products from RTH Beijing.