| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on the Improved Main Telecommunications Network and GTS Expert Team on Enhanced Use of Data Communication Systems Beijing, China, 10-15 May 2004 |  | ISS/ET-IMTN 2004/Doc. x (6 May 2004) ENGLISH only |
| --- | --- | --- |

# Status of MTN at RHT Exeter

(Submitted by Scott Irvine & David Hennings)

Summary and purpose of document This document includes the report on the status of implementation of MTN at RTH Exeter (was Bracknell).

1.	Communication Links

Figure 1	UK Met Office Telecommunication links

Figure 1 shows some of the UK Met Office telecommunications links. The message switches FROST, TROPICS and NETlink  send and receive data arriving over the links while the routers EXERT5 (and EXERT6) provide the connections to the circuits or managed network services.

The TROPICS message switch has mostly been replaced by the new FROST message switch, but currently retains all the X.25 services.

The Regional Meteorological Data Communications Network (RMDCN) is a managed IP network service provided by Equant for the WMO National Meteorological Services (NMSs) in WMO region VI.

The Met Office has Frame Relay links with both British Telecom (Link to Australia BoM, and NOAA-OSO) and Worldcom (Link to NOAA-NESDIS and CMC).

The following sections contain more detailed information on some of the links.

1.1	Links to NOAA

There are two links to NOAA, one to NOAA-NESDIS and a second to the NOAA Office of Systems Operations (NOAA-OSO).

1.2.1	Link to NOAA-OSO

The link to NOAA-OSO is a Frame relay line. There are three separate sockets data streams described in Table 1 for GTS data.

| Protocol | Speed Kbits/sec | NOAA-OSO System | Met Office System | Data |
| --- | --- | --- | --- | --- |
| TCP Sockets | 32 CIR | NOAA-OSO Telecommunications Gateway | FROST | Character |
|  |  |  |  | GRIB |
|  |  |  |  | T4 Fax |

Table 1	Details of the links between METO and NOAA-OSO

(The leased line between Bracknell and Washington has now been replaced with a Frame Relay connection operating from Exeter.)

1.2.2	Links to NOAA-NESDIS

The Frame Relay link to NOAA-NESDIS is used for the transfers of satellite sounding data. Details on the link is shown in Table 2, the utilisation is shown in Appendix A and the daily volumes of data is shown in Table 4.

| Protocol | Speed Kbits/sec | NOAA-NESDIS System | Met Office System | Data |
| --- | --- | --- | --- | --- |
| FTP | 512 Access/ 128 CIR from NESDIS | CEMSCS | NETLINK | Satellite Sounding data and products |
| FTP | 512 Access/32CIR to NESDIS | CEMSCS | NETLINK | ERS-2 Data |

Table 2	Details of the links between Met Office and NOAA-NESDIS

1.2	Link to ECMWF

The 2MBits/Sec link to ECMWF is used to transmit files of data between Met Office and ECMWF using TCP/IP protocols. This data includes GTS Data, numerical modelling products and satellite data. Met Office users can also submit jobs to run on the ECMWF Supercomputer and access data on ECMWF computer systems using their MARS and METVIEW software.

1.3	Links to RMDCN

The link from Met Office to the RMDCN network has an access speed of 512 Kbits/S (ISDN backup 384Kbits/S). Permanent Virtual Circuits (PVCs) are established across RMDCN to other National Meteorological Services (NMSs) in WMO region VI. Two of the key links are:

1.3.1	Link to Météo-France

PVC with a speed of 256Kbits/Sec out (Met Office to Météo-France) with agreed upgrade to 384Kbits/S, and 128Kbits/Sec in (Météo-France to Met Office).

The link is used for:

- Exchange of GTS and Radar data.

- Sending GOES and GMS satellite data to Lannion. This data is then sent from Lannion to METEOSAT for rebroadcast.

- Transmission of Met Office NIMROD products.

- Transmission of NOAA satellite data.

1.3.2	Link to DWD

A PVC with a speed of 64Kbits/Sec in both directions has been established between the Met Office and DWD to exchange GTS products.

1.3.3	Other RMDCN Links

The MET OFFICE has the following PVCs through RMDCN to other NMSs

| National Meteorological Service | Protocol | PVC Speed Kbits/Sec | Status |
| --- | --- | --- | --- |
| Belgium (Brussels) | FTP | 32 Both ways | Operational |
| Denmark | TCP Sockets | 32 Both ways | Operational |
| DWD (Offenbach) | FTP | 64 Both ways | Operational |
| Iceland (Reykjavik) | FTP | 8 Both ways | Operational |
| Ireland (Dublin) | FTP | 64 Both ways | Operational |
| Italy (Rome) | FTP | 16 Both ways | Operational |
| Météo-France (Toulouse) | FTP | 128 in 256 out [384*] | Operational |
| Russian Federation (Moscow) | FTP | 8 in/64 out* | Operational |
| Netherlands (De Bilt) | TCP Sockets | 64 Both ways | Operational |
| Norway (Oslo) | TCP Sockets | 32 Both ways | Operational |
| Portugal (Lisbon) | FTP | 32 Both ways | Operational |
| Spain (Madrid) | TCP Sockets | 32 Both ways | Operational |

Table 3	Details of RMDCN Links to other NMSs in WMO Region VI

We no longer support X.25 services via RMDCN from Exeter as this is now viewed as a legacy protocol. We intend to move the remaining X.25 services to an IP solution and ultimately drop X.25 support entirely.

1.4	Other International Links

In an effort to gain routine, reliable access to global imagery from geostationary satellites, the Met Office has implemented links as described briefly below.

1.4.1	Australian Met. Service

A Frame Relay link has been established between the Met Office and the Australian Bureau of Meteorology (BoM) in Melbourne. The access speed is 256Kbits/Sec at each end and the CIR is 64Kbits/Sec in both directions. The link is being used for the exchange of data in WMO bulletin format using TCP sockets with FROST, files of satellite imagery (METEOSAT from UK and GMS from Australia) and ATOVS (HIRS) level 1D data  with NETLINK.

1.4.2	Canadian Met. Service

A 32 Kbits/Sec Frame Relay link has been established between the Met. Office and the Canadian Met. Service (CMC) in Dorval. It is being used for the exchange of data in WMO bulletin format with FROST and files of satellite data (METEOSAT from UK and GOES from Canada) with NETLINK.

2.	Met. Office Communication Computer Systems

There are two main computer systems at the Met Office that are used to send data to customers. The HP-UNIX-based FROST message switch sends WMO messages using FTP or TCP/IP sockets. FROST is planned to support some X25 services later this year though most remaining X25 customers are encouraged to migrate to FTP or TCP sockets.

The TROPICS system, which is shortly to be retired, handles communications using direct X25 links and X25 over TCP/IP (including GTS traffic to CMC).

The NETLINK system exchanges files using FTP. In general FROST is used for the transfer of low volume data, typically from 100 Bytes to 50 Kbytes, where high speed data switching is important. NETLINK is used for the distribution of higher volume data at slower data switching speeds.

2.1	NETLINK

The NETLINK computer system is responsible for the operational transfer of files of data between computers on the Met. Office Central Data Network (CDN), and computers on external networks. It consists of two identical Compaq Alpha Computers running OpenVMS, the main node is called NETTLE and its backup is called TEAZLE.

Each NETLINK node is a HP Alpha 1200/533 with 256 Mbytes of. Currently the system is switching 44,000 files per day, which is about 28 Gbytes of data.

Planning is in its early stages to replace the functionality of NETLINK with a new platform which integrates better with the new FROST system sometime in 2006.

In the mean time, to handle anticipated loading from Meteosat Second Generation (MSG) and some of the new satellite product sets, the nodes will be replaced by more powerful OpenVMS (HP Alpha) platforms.

2.2	FROST

The new Met Office FROST system is based upon a pair of HP L3000 servers running HP-UX Operating System software configured to run as a main system and a hot standby. There is a separate HP A500 Test & Development server.

A dedicated gigabit Ethernet link between the systems is used for management traffic and data synchronisation.

Application software is based upon the Messir-Comm message switching package for WMO message switching supporting FTP and TCP sockets. This is integrated with Nexor Mailer/Mixer software for general message switching using X.400 and SMTP. Legacy X.25 communications is supported by a pair of CISCO 3640 routers hot-switchable between servers. Operations and management of the system is performed using client software running on standard desktop PCs augmented by integration of the system with existing Met Office Tivoli and OpenView management platforms.

When migrating the Washington link from TROPICS to FROST, protocols were changed to use TCP sockets rather than X25.

The data volumes between Washington and Exeter are shown in Tables 4; 5 & 6 from the Frost Message Switch.

| Date | Washington to Exeter | Exeter to Washington |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| April 1996 | 9.2 | 14256 | 9.1 | 13651 |
| May 1997 | 9.6 | 15535 | 10.4 | 14662 |
| May 1998 | 13.2 | 16524 | 11.0 | 15884 |
| May 1999 | 17.5 | 18036 | 12.4 | 19199 |
| June 2000 | 21.3 | 22123 | 14.2 | 24359 |
| April 2001 | 32.7 | 23011 | 16.4 | 28925 |
| June 2002 | 41 | 31354 | 18 | 32247 |
| April 2003 | 35.6 | 28259 | 37.3 | 29612 |
| May 2004 | 44.6 | 36961 | 17.1 | 29268 |

Table 4 GTS Link Alpha-Numeric Channel

| Date | Washington to Exeter | Exeter to Washington |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| April 1996 | 72.8 | 19455 | 75.9 | 23463 |
| May 1997 | 75.6 | 19220 | 77.3 | 23007 |
| May 1998 | 80.1 | 19932 | 66.5 | 16259 |
| May 1999 | 78.7 | 19876 | 68.7 | 16343 |
| June 2000 | 83.1 | 20389 | 75.3 | 17763 |
| April 2001 | 86.1 | 20740 | 86.6 | 20006 |
| June 2002 | 163 | 36186 | 119 | 24961 |
| April 2003 | 182 | 38834 | 130 | 27687 |
| May 2004 | 181.4 | 40803 | 164.3 | 29302 |

Table 5 GTS Link GRIB Channel

| Date | Washington to Exeter | Exeter to Washington |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| April 2001 | 5.4 | 59 | 5.4 | 60 |
| June 2002 | 3 | 33 | 6 | 68 |
| April 2003 | 3.3 | 33 | 7.5 | 74 |
| May 2004 | 3.4 | 38 | 6.7 | 74 |

Table 6 GTS Link T4 Channel

The data volumes between Toulouse and Exeter are shown in Tables 7; 8 & 9 from the Frost Message Switch.

| Date | Toulouse to Exeter | Exeter to Toulouse |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| May 2004 | 39.6 | 16785 | 71.3 | 47490 |

Table 7 GTS Link Alpha-Numeric Channel

| Date | Toulouse to Exeter | Exeter to Toulouse |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| May 2004 | GRIB received on alpha channel | 98.2 | 27897 |

Table 8 GTS Link GRIB Channel

| Date | Toulouse to Exeter | Toulouse to Toulouse |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| May 2004 | 18 | 1203 | 57.7 | 1476 |

Table 9 GTS Link T4 Channel

The data volumes between Melbourne and Exeter are shown in Tables 10; 11 & 12 from the Frost Message Switch.

| Date | Melbourne to Exeter | Melbourne to Exeter |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| May 2004 | 1.7 | 2680 | 41.4 | 7857 |

Table 10 GTS Link Alpha-Numeric Channel

| Date | Melbourne to Exeter | Melbourne to Exeter |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| May 2004 | 0.1 | 50 | 114.5 | 23953 |

Table 11 GTS Link GRIB Channel

| Date | Melbourne to Exeter | Melbourne to Exeter |
| --- | --- | --- |
|  | Data (Mb) | Msgs | Data (Mb) | Msgs |
| May 2004 | 0.3 | 4 | 6.9 | 84 |

Table 12 GTS Link T4 Channel

3	Met Office Relocation

The Met Office has moved to Exeter in the South West of the UK, around 200 miles from the previous location in Bracknell.

At the new site there are two separate IT Halls. Diversely routed communication ducts to each hall enable highly resilient communication circuits.

Migration of computer systems and circuits is complete with the present building in Bracknell having closed.

The relocation of operational systems began in May 2003 and the last system was moved in January 2004. Throughout this there were few operational issues. There were a few IP routing issues, primarily due to the implementation and configurations on the new Firewall systems which impacted our ability to switch data. These issues were quickly resolved when they occurred.

Appendix A

Utilisation of UK Met. Office Links

Following are utilisation graphs for the following links:

- Washingtom – NOAA OSO

- Melbourne

- RMDCN

- Dorval – CMC

- ECMWF

Note on the graphs which follow:

We are currently in the process of investigating new network monitoring tools, as the previous product has been dropped by the supplier. The following graphs have been captured from a basic OpenView monitoring package and as such are not ideal.

A1	Washington NOAA OSO

A2	Melbourne BoM

A3	RMDCN

A4	Dorval CMC

A5	ECMWF