| WORLD METEOROLOGICAL ORGANIZATION _________________________ COMMISSION FOR BASIC SYSTEMS OPAG ON INFORMATION SYSTEMS & SERVICES Expert Team on the Improved Main Telecommunications Network and GTS Expert Team on Enhanced Use of Data Communication Systems Beijing, China, 10-14 May 2004 |  | ISS/ET-IMTN 2004/Doc. 2(2) ISS/ET-EUDCS 2004/Doc. 2(2) (30.V.2004) ____________ ITEM 2 ENGLISH only |
| --- | --- | --- |

STATUS OF IMPLEMENTATION AT RTH TOKYO

(Submitted by NAKAZONO Akihiko (Japan) )

Summary and purpose of document This document includes the report on the status of implementation of MTN at RTH Tokyo and TCP/IP procedures and applications on the GTS.

1.  GTS facilities

Main GTS facilities such as MSS, FAX system started operation in March 1996.  subsequently, considering TCP/IP strategy and Internet trends, they were reinforced in 1998 and 1999.  Current configuration is a mixture of old-fashioned and trendy facilities.  JMA plans to replace them by new ones in October 2005.

2.  Current status of implementation of the GTS circuits

Table 1   Status of the GTS circuits connected with RTH Tokyo (as of April 2004)

| Circuit | Speed | Procedures Applications | Routing protocol | Exchange data type |
| --- | --- | --- | --- | --- |
| Washington Tokyo | MTN | FR (IMTN cloud I) CIR: WT ( 32/768kbps ( TK Port: WT=1.5Mbps,TK=1.5Mbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary, fax), File (Satellite data) |
| Melbourne Tokyo | MTN | FR (IMTN cloud I) CIR: MB ( 16/32kbps ( TK Port: MB=256kbps,TK=1.5Mbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary, fax), File (Satellite data) |
| Beijing Tokyo | MTN | FR (IMTN cloud II) CIR: BJ (48/48kbps( TK Port: BJ=128kbps,TK=128kbps | TCP Socket | BGP-4 | Message (A/N, binary, fax) |
| New Delhi Tokyo | MTN | 64kbps | TCP Socket | BGP-4 | Message (A/N, binary) |
| Seoul Tokyo | RMTN | FR (NNI basis) CIR: SL (16/16kbps( TK Port: SL=64kbps,TK=192kbps | TCP Socket | BGP-4 | Message (A/N, binary, fax) |
| Khabarovsk Tokyo | RMTN | 14.4kbps (auto fall back V.34 modem ) | TCP Socket | Static | Message (A/N, binary, fax) |
| Bangkok Tokyo | RMTN | FR (NNI basis) CIR: BK (16/16kbps( TK Port: BK=128kbps,TK=192kbps | TCP Socket | BGP-4 | Message (A/N, binary) |
| Hong Kong Tokyo | RMTN | FR (NNI basis) CIR: HK (16/16kbps( TK Port: HK=64kbps,TK=192kbps | TCP Socket Simple FTP | BGP-4 | Message (A/N, binary), File (Satellite data) |
| Manila Tokyo | Inter-regional | 200bps | Asynchronous |  | Message (A/N) |

FR: Frame Relay;     CIR: Committed Information Rate;     NNI: Network-to-Network Interconnection

3.  Upgrades of GTS circuits

3.1  Upgrades achieved after the previous meeting

Table 2   Details of recent upgrades (May 2002 to April 2004)

| Date | Circuit | Before upgrade | After upgrade |
| --- | --- | --- | --- |
|  |  | Circuit type and speed | Protocol | Data type | Circuit type and speed | Protocol | Data type |
| August 2002 | New Delhi Tokyo | Dedicated analogue; 9600bps | X.25 | AN, BIN, FAX | Dedicated digital; 64kbps | TCP/IP (socket) | AN, BIN |
| January 2003 | Washington Tokyo | Dedicated digital; 64kbps | TCP/IP (socket, simple ftp) | AN, BIN, FAX, Satellite data | FR (IMTN cloud I); CIR 32/768 kbps | TCP/IP (socket, simple ftp) | AN, BIN, FAX, Satellite data |
| January 2003 | Melbourne Tokyo | Dedicated digital; 64kbps | TCP/IP (socket, simple ftp) | AN, BIN, FAX, Satellite data | FR (IMTN cloud I); CIR 16/32kbps | TCP/IP (socket, simple ftp) | AN, BIN, FAX, Satellite data |
| September 2003 | Melbourne Tokyo | FR (IMTN cloud I); CIR 16/32 kbps | TCP/IP (socket, simple ftp) | AN, BIN, FAX, Satellite data | FR (IMTN cloud I); CIR 16/32kbps (add CIR 16/16 kbps for the backup PVC via Brisbane) | TCP/IP (socket, simple ftp) | AN, BIN, FAX, Satellite data |
| November 2003 | Khabarovsk Tokyo | Voice (14.4kbps) | X.25 | AN, BIN, FAX | Voice (normally 14.4kbps) | TCP/IP (socket) | AN, BIN, FAX |
| February 2004 | Beijing Tokyo | FR (NNI); CIR 32/32 kbps | TCP/IP (socket) | AN, BIN, FAX | FR (IMTN cloud II); CIR 48/48kbps | TCP/IP (socket) | AN, BIN, FAX |

Changes are shown in bold and italic.

CIR: send/receive at Tokyo

3.2  Upgrade plans

Table 3  Upgrade plans of GTS circuits connected with RTH Tokyo

| Circuit | Speed | Procedures Applications | Routing protocol | Remarks |
| --- | --- | --- | --- | --- |
| New Delhi Tokyo | MTN | FR (IMTN cloud II) CIR: ND (16/16kbps( TK Port: ND=64kbps,TK=128kbps | TCP Socket | BGP-4 | Target : Very soon in 2004 |
| Manila Tokyo | Inter-regional | FR (NNI basis) CIR: MN (16/16kbps( TK Port: MN=64kbps,TK=192kbps | TCP Socket | BGP-4 or static | Target : September 2004 |

4.   Implementation status of TCP/IP protocols and applications

4.1  TCP/IP

TCP/IP protocols are used on all of GTS circuits connected with RTH Tokyo except for Manila-Tokyo where these protocols are planned to introduce in September 2004.  Meteorological messages including T4 charts are currently exchanged through the standard WMO sockets, which would be migrated to FTP of accumulated messages upon necessary arrangements with adjacent centers after renewal of the Message Switching System of RTH Tokyo planned in October 2005.

Simple FTP is also used to receive satellite data from Washington and Melbourne and to relay some part of them to Hong Kong.  The following manners are currently applied.

Data from Washington:	GET by Tokyo

Data from Melbourne:	PUT by Melbourne with renaming

Data to Hong Kong:	PUT by Tokyo with renaming

Satellite data exchange using  simple FTP is being considered to expand to other GTS circuits including Beijing-Tokyo and Seoul-Tokyo.

4.2  Routing protocols

BGP-4 is applied over almost all the TCP/IP circuits connected with Tokyo except Khabarovsk-Tokyo where static routing is applied.  In principal Tokyo advertises all available routing information to BGP neighbours without filtering, while exchange of BGP routes with the Equant router, which interconnects Tokyo and Beijing as well as RA VI-RMDCN, is limited to a minimum that is necessary for establishing IP connectivity among these two centres and Seoul where re-routing is being tested.

With growing IP connectivity among GTS centres, there would be a bypass route(s) through a third centre in addition to the direct one.  For making practical use of this feature, Tokyo, Washington and Melbourne started re-routing via the bypass route in case of a failure of the direct link on a triangle of circuits interconnecting these three centers established within IMTN could I in February 2003.  Besides, Tokyo, Beijing and Seoul have testing re-routing among them, but not all bypasses are working at present due to some routing problem.

5.  Traffic status of IP links

(a) Melbourne-Tokyo

(b) Wahington-Tokyo

(c)  Beijing-Tokyo

(d) New Delhi-Tokyo

(e) Bangkok-Tokyo

(f)  Khabarovsk-Tokyo

(g)  Seoul-Tokyo

(h)  Hong Kong-Tokyo

# Text boxes

INTERNET

ISP

Dummy data tool

Dummy data tool

Socket AP

Socket AP

Test host 2

Simulating FAX

Test host 1

Simulating MSS

Router for Test connections

FAX

FAX

MSS

MSS

Line Switch (for duplex system)

128kbps

Router for GTS connections

IOS Ver.11.3

NEC IP45/604  (Cisco OEM, Cisco3640)

NAT (Network Address Translation) Router

IOS Ver.11.3

NEC IP45/621M (Cisco OEM, Cisco4500-M)

Router for FTP connections

IOS Ver.10.3(8)

NEC IP45/651 (Cisco OEM, Cisco7010)

FTP

Server

FTP

Server

### Tokyo

Test partners

TCP/IP test environment

via Internet

Figure 1   GTS facilities including TCP/IP test environment via Internet

974 Mbytes/day

Frame Relay

Network

64kbps

128kbps

64kbps

128kbps

Equant Frame Relay Network

IMTN cloud II

New Delhi

Beijing

64

kbps

1.5Mbps

256kbps

Internet accessing system at JMA headquarters

Main components of Operational Telecommunication System

at Kiyose operation Office

AS 64520

Pure IP circuits

Asynchronous circuit

Manila

Private IP address

202.245.36.0/24

Private IP address

Private IP address

202.245.39.0/24

1.5Mbps

BT Frame Relay Network

IMTN cloud I

Dedicated line connection

21 Mbytes/day

Figure 3   Configuration plan of GTS circuits connected with RTH Tokyo in 2004

Voice (normally 14.4kbps)

Khabarovsk

New Delhi

24 Mbytes/day

2.6 Mbytes/day

44 Mbytes/day

CAT

Frame Relay

Network

HKT

Frame Relay

Network

DACOM

Frame Relay

Network

Figure 2   Configuration of the GTS circuits connected with RTH Tokyo

80 Mbytes/day

0.4 Mbytes/day

Seoul

128kbps

206 Mbytes/day

KDDI

Frame Relay Networks

128kbps

NNI basis Frame Relay connections

0.6 Mbytes/day

64kbps

64kbps

192kbps

Hong Kong

Bangkok

Melbourne

Equant Frame Relay Network

IMTN cloud II

### Tokyo

Beijing

1.5Mbps

256kbps

1.5Mbps

BT Frame Relay Network

IMTN cloud I

Dedicated line connections

200

bps

Manila

Variable

(normally 14.4kbps)

Khabarovsk

CAT

Frame Relay

Network

HKT

Frame Relay

Network

DACOM

Frame Relay

Network

Seoul

KDDI

Frame Relay Networks

128kbps

NNI basis Frame Relay connections

64kbps

64kbps

192kbps

Hong Kong

Bangkok

Melbourne

121 Mbytes/day

2.2 Mbytes/day

11 Mbytes/day

0.4 Mbytes/day

27 Mbytes/day

0.9 Mbytes/day

30 Mbytes/day

Washington

Washington