Feb. 2002

Table 1  Specifications of Ordinary Weather Radar in JMA

( 1 / 2 )

| Radar Name / Site Name Index number | Sapporo/ Kenasi -yama 47415 | Kusiro/ Kombu -mori 47418 | Hakodate/ Yokotu -dake 47432 | Sendai 47590 | Akita 47582 | Tokyo 47695 | Nagano/ Kuruma -yama 47611 | Shizuoka/ Makino -hara 47659 | Niigata/ Yahiko -yama 47572 | Fukui/ Tojinbo 47705 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Radar Antenna Height (m , S.L.) Frequency (MHz) Peak Power (kW) Pulse Width (μs) Pulse Repetition Freq. (Hz) Antenna Diameter (m) Antenna Gain (dB) Beam Width H. (deg) V. (deg) Antenna Scan Speed (rpm) Noise Figure (dB) Smin (dBm) Effective Range (km) Output Device | JMA-MR 752.50 5310 250 2.50 260 4.0 43.9 1.07 1.10 4 3.1 -110.5 about 300 Coaxial Magnetron | JMA-MR 121.69 5340 250 2.63 260 4.0 44.0 1.00 1.00 4 2.4 -112.8 about 300 Coaxial Magnetron | JMA-MR 1141.70 5300 250 2.70 260 3.0 40.9 1.33 1.43 4 4.1 -113.5 about 300 Coaxial Magnetron | JMA-MR 99.40 5290 250 2.75 260 3.0 42.4 1.32 1.43 4 2.8 -113.0 about 300 Coaxial Magnetron | JMA-MR 56.80 5320 250 2.60 260 3.0 41.6 1.40 1.40 4 8.6 -106.0 about 300 Coaxial Magnetron | JMA-MR 62.06 5320 250 2.68 260 3.0 40.7 1.41 1.45 4 3.7 -108.0 about 300 Coaxial Magnetron | JMA-MR 1937.13 5320 250 2.57 260 4.0 43.6 1.05 1.11 4 1.2 -114.0 about 300 Coaxial Magnetron | JMA-MR 185.99 5300 250 2.60 260 4.0 43.3 1.04 1.12 4 1.3 -113.5 about 300 Coaxial Magnetron | JMA-MR 645.00 5300 250 2.60 260 3.0 41.4 1.42 1.45 4 4.8 -110.0 about 300 Coaxial Magnetron | JMA-MR 107.00 5280 250 2.67 260 4.0 43.5 1.1 1.1 4 7.8 -112 about 300 Coaxial Magnetron |

( 2 / 2 )

| Radar Name / Site Name Index number | Nagoya 47636 | Osaka/ Takayasu -yama 47773 | Matsue/ Misaka -yama 47791 | Hiroshima/ Haiga -mine 47792 | Muroto -misaki 47899 | Fukuoka/ Sefurisan 47806 | Tanega -shima/ Nakatane 47869 | Naze/ Funcha -toge 47909 | Okinawa/ Itokazu 47937 | Ishigaki -jima 47920 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Radar Antenna Height (m , S.L.) Frequency (MHz) Peak Power (kW) Pulse Width (μs) Pulse Repetition Freq. (Hz) Antenna Diameter (m) Antenna Gain (dB) Beam Width H. (deg) V. (deg) Antenna Scan Speed (rpm) Noise Figure (dB) Smin (dBm) Effective Range (km) Output Device | JMA-MR 72.22 5300 250 2.50 260 3.0 41.0 1.5 1.3 4 5.0 -109.3 about 300 Coaxial Magnetron | JMA-MR 497.60 5300 250 2.75 260 4.0 45 0.99 1.03 4 2.1 -113.0 about 300 Coaxial Magnetron | JMA-MR 554.70 5270 250 2.83 260 4.0 45 0.99 1.03 4 2.0 -112.3 about 300 Coaxial Magnetron | JMA-MR 746.90 5300 250 2.80 260 4.0 45 0.99 1.03 4 2.3 -112.5 about 300 Coaxial Magnetron | JMA-MR 200.29 5300 250 2.65 260 3.0 40.9 1.4 1.45 4 2.5 -110.0 about 300 Coaxial Magnetron | JMA-MR 982.70 5300 250 2.56 260 4.0 44.5 1.06 1.01 4 2.6 -111.3 about 300 Coaxial Magnetron | JMA-MR 290.50 5300 250 2.52 260 4.0 44.6 1.06 1.03 4 2.7 -114.0 about 300 Coaxial Magnetron | JMA-MR 315.70 5300 250 2.55 260 4.0 44.7 1.03 1.00 4 2.6 -113.0 about 300 Coaxial Magnetron | JMA-MR 209.69 5300 250 2.65 260 3.0 41.5 1.34 1.42 4 4.7 -113.0 about 300 Coaxial Magnetron | JMA-MR 535.50 5260 250 2.50 260 4.0 43.7 1.2 1.2 4 3.0 -112.7 about 300 Coaxial Magnetron |

Table 2  Specifications of Airport Weather Radar in JMA

| Name of Airport Index number | New Chitose AP. 47487 | New Tokyo AP. 47686 | Tokyo AP. 47671 | Nagoya AP. 47635 | Osaka AP. 47771 | Kansai AP. 47774 | Fukuoka AP. 47808 | Kagoshima AP. 47851 | Naha AP. 47930 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Radar Antenna Height (m , S.L.) Frequency (MHz) Peak Power (kW) Pulse Width (μs) Pulse Repetition Freq. (Hz) Antenna Diameter (m) Antenna Gain (dB) Beam Width H. (deg) V. (deg) Antenna Scan Speed (rpm) Noise Figure (dB) Smin (dBm) Effective Range (km) Output Device | JMA-DRAW (Doppler) 60.70 5280 200 1.0 400～ 2000 7.1 49.2 0.60 0.59 2/4 1.7 -110.7 120/240 Klystron | JMA-DRAW (Doppler) 83.30 5290 200 1.0 400～ 2000 7.1 48.0 0.6 0.6 2/4 1.7 -110 120/240 Klystron | JMA-DRAW (Doppler) 49.20 5280 200 1.0 400～ 2000 7.1 48.4 0.60 0.58 2/4 2.5 -112 120/240 Klystron | JMA-AMR 47.30 5270 150 1.0 1040 2.0 37.2 2.2 2.0 4 8.0 -106.0 100 Coaxial Magnetron | JMA-DRAW (Doppler) 51.40 5270 200 1.0 400～ 2000 7.1 49.7 0.62 0.59 2/4 1.9 -112 120/240 Klystron | JMA-DRAW (Doppler) 47.80 5290 200 1.0 400～ 2000 7.1 48.5 0.61 0.62 2/4 2.0 -112 120/240 Klystron | JMA-AMR 24.40 5280 150 1.0 1040 2.0 38.0 2.2 2.1 4 8.2 -104.0 100 Coaxial Magnetron | JMA-AMR 286.80 5280 150 1.0 1040 2.0 38.0 2.4 2.2 4 6.5 -104.0 100 Coaxial Magnetron | JMA-AMR 38.56 5280 150 1.0 1040 2.0 36.4 2.1 2.1 4 6.5 -105.9 100 Coaxial Magnetron |

Table 3  Specifications of Research Weather Radar in JMA

| Location | Meteorological Research Institute | Meteorological Research Institute (mobile) |  |
| --- | --- | --- | --- |
| Type of Radar Antenna Height (m , S.L.) Frequency (MHz) Peak Power (kW) Pulse Width (μs) Pulse Repetition Freq. (Hz) Antenna Diameter (m) Antenna Gain (dB) Beam Width H. (deg) V. (deg) Antenna Scan Speed (rpm) Noise Figure (dB) Smin (dBm) Effective Range (km) Output Device | (Doppler) 63.44 5260 250 2.0/0.52 ～950 4.0 42.0 1.01 1.01 1～6 4.35 -112.0 about 400 Coaxial Magnetron | (Doppler) 9810 50 1.0 1000/2000 2.0 43.15 1.07 1.07 1～6 3.9 -107.3 about 64 Klystron |  |